## Slide 1: 1. Introduction
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Course opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s introduce Positive Protection!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Define positive protection
Discuss the need for a decision-making process to minimize worker exposure
Discuss Subpart K’s and MAP-21 positive protection language
Discuss positive protection reference guidance
Define engineering judgment & the designer’s role
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module.
Suggested Questions: None
Additional Information: None
Possible Problems: Try to whet their appetite with these objectives. MAP 21 language is going (as of Sept 2012) through rulemaking process. Changes expected by Spring 2013.

## Slide 3: Issues with Worker Exposure
Workers are vulnerable!
Their protection is left to engineering judgment, if at all
Seldom considered on paving and other maintenance projects
Short duration projects may be a problem
Positive protection not always feasible, cost-effective or practical
Notes: Key Message: Discuss Issues with Worker Exposure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Some issues related to worker exposure are on the screen. For example, workers in work zones are vulnerable to vehicle intrusions. Their protection is left to engineering judgment, if at all. Sometimes, the cost associated with Positive Protection devices makes Positive Protection devices cost-prohibitive, leaving workers unprotected. Positive Protection devices are seldom considered on paving and other maintenance projects due to their short duration. Short duration projects may be a problem as far as worker protections. Positive protection is not always feasible, cost-effective or practical. These is why specific guidance and procedures are needed.
Suggested Questions: Can you name some issues with worker exposure? How can we improve on those? What options are there?
Additional Information: None
Possible Problems: None

## Slide 4: What is Positive Protection?
The use of “a device which contains and redirects vehicles in accordance with National Cooperative Highway Research Program (NCHRP) Report 350, preventing their intrusion into the work space.”
72
Image: ATSSA
Notes: Key Message: Define Positive Protection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: By definition, positive protection is “The use of “a device which contains and redirects vehicles in accordance with National Cooperative Highway Research Program (NCHRP) Report 350, preventing their intrusion into the work space.” This is mouthful. Let’s break this definition into its major components to make sure we understand what Positive Protection devices are and what they are not. Often times, channelizing devices are deployed as protection devices and vice versa. Remember, all devices have their function and purpose. Cones, for example, do not provide protection! (next slide)
Suggested Questions: What is redirection? Containment?
Additional Information: Source: (1) Positive Protection - Reducing Risk, Protecting Workers and Motorists. Brochure published by the Federal Highway Administration, 2003. Photo by Juan M. Morales, Route 28, Virginia.
Possible Problems: No need to get into NCHRP 350 here. NCHRP 350 has been rewritten into a manual called MASH (Manual for Assessing Safety Hardware), but it is not mentioned in this definition. May want to mention MASH at this point but it may be too early. MASH is discussed in module 4. See slide 4.

## Slide 5
Are cones positive protection devices?
Image: ATSSA
Notes: Key Message: Illustrate Positive Protection Devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is NOT a Positive Protection device. Do these cones contain or redirect? No!
Suggested Questions: Is this a positive protection device? No. Cones are delineation or channelizing devices.
Additional Information: Photo source ATSSA.
Possible Problems: None

## Slide 6: Are drums protection devices?
Image: ATSSA
Notes: Key Message: Illustrate Positive Protection Devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is NOT a Positive Protection device. Do these drums contain or redirect? No!
Suggested Questions: Is this a positive protection device? No. Drums are delineation or channelizing devices.
Additional Information: None
Possible Problems: Drums, not barrels.

## Slide 7
Is this positive protection?
Image: ATSSA

## Slide 8
Are barriers positive
protection devices?

Image: ATSSA
Notes: Key Message: Illustrate Positive Protection Devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This barrier is a Positive Protection device. Does it contain or redirect? Yes!
Suggested Questions: Is this a positive protection device? Yes!
Additional Information: Worker is on a closed lane.
Possible Problems: Drums, not barrels.

## Slide 9: Questions to Ponder
How do we minimize worker exposure during short duration and other maintenance projects?
When positive protection is not feasible, what “other” strategies exist?
Is there a methodical process to assess the need for positive protection and other strategies?
What guidance exists in this State?
Notes: Key Message: Questions to Ponder
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This discussion brings some questions, such as the ones on the screen. This course will answer these questions!
Suggested Questions: How do we minimize worker exposure during short duration and other maintenance projects? When positive protection is not feasible, what “other” strategies exist? Is there a methodical process to assess the need for positive protection and other strategies? What guidance exist?
Additional Information: None
Possible Problems: No need to answer these questions. They are an intro to the course.

## Slide 10: Work Zone Final Rule
In 2008, FHWA added new Subpart K to 23 CFR 630 to supplement existing regulations that govern work zone safety and mobility in work zones to include conditions for the appropriate use of, and expenditure of funds for:
  Uniformed law enforcement officers
  Positive protective measures
  Installation and maintenance of temporary traffic control (TTC) devices
Notes: Key Message: Work Zone Final Rule
Est. Presentation Time (minutes): 1 minute
Explanation of Cues/Builds: None
Suggested Comments: FHWA added new Subpart K to 23 CFR 630 to supplement existing regulations that govern work zone safety and mobility in work zones to include conditions for the appropriate use of, and expenditure of funds for:
-Uniformed law enforcement officers
Positive protective measures
Installation and maintenance of TTC devices
This course evolved from these requirements.
Suggested Questions: Are you familiar with Subpart K?
Additional Information: None
Possible Problems: None

## Slide 11: The Work Zone Final Rule
Aimed to decrease the likelihood of fatalities and injuries to road users, and to workers who are exposed to motorized traffic while working on Federal-aid highway projects
Notes: Key Message: Why the “New” Regulations?
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Subpart K aims at decreasing the likelihood of fatalities and injuries to road users, and to workers who are exposed to motorized traffic while working on Federal-aid highway projects.
Suggested Questions: Why the “New” Regulations?
Additional Information: The incorporation by reference of certain publications listed in this rule is approved by the Director of the Federal Register as of December 4, 2008.
Possible Problems: Emphasize the safety aspects, and not the regulation.

## Slide 12: Purpose of Subpart K of 23 CFR
To emphasize the need to appropriately consider and manage worker safety as part of the project development process by providing guidance on key factors to consider in reducing worker exposure and risk from motorized traffic
Image: ATSSA
Notes: Key Message: Discuss the Purpose of Subpart K of 23 CFR
Est. Presentation Time (minutes):
Explanation of Cues/Builds: None
Suggested Comments: To emphasize the need to appropriately consider and manage worker safety as part of the project development process by providing guidance on key factors to consider in reducing worker exposure and risk from motorized traffic. Notice the emphasis on worker safety and the reduction of worker exposure.
Suggested Questions: How can we reduce worker exposure?
Additional Information: CFR = Code of Federal Regulations
Possible Problems: None

## Slide 13: MAP-21
Requires Positive Protection measures “as a minimum” where there is “no means of escape”
Requires barriers for “long-duration stationary work zones” if:
  High speed
  Workers within one lane width of a live travel lane
“Unless an analysis determines otherwise”
Notes: Key Message: Summarize MAP-21 Language
Est. Presentation Time (minutes):
Explanation of Cues/Builds: Text boxes appear on click
Suggested Comments: We had looked at the MAP-21 language. Here we have summarized it for you.
Suggested Questions: Remember the MAP-21 language? Why these requirements? What kind of analysis? This is what we will discuss in this course.
Additional Information: None
Possible Problems: Try not to give too much information here. Detailed information to come.

## Slide 14: Requires to Address Worker Safety as Follows:
Avoid or minimize worker exposure to motorized traffic through the application of appropriate positive protective strategies including, but not limited to:
  Full road closures
  Ramp closures
  Crossovers and detours
  Rolling road blocks
Image: ATSSA
Notes: Key Message: Quote Subpart K Language
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: First, by avoiding or minimize worker exposure to motorized traffic through the application of appropriate positive protective strategies including, but not limited to:
-Full road Closures
-Ramp Closures
-Crossovers and Detours
-Rolling Road Blocks
Suggested Questions: How does Subpart K address worker safety?
Additional Information: None
Possible Problems: Avoid reading. Paraphrase. Make interesting. These will be discussed in detail later. Relate to safety.

## Slide 15: Requires to Address Worker Safety as Follows: (cont.):
2. Where exposure cannot be adequately managed through the application of the above strategies, reduce risk to workers from being struck by motorized traffic through the use of appropriate positive protective devices;
Image: ATSSA
Notes: Key Message: Quote Subpart K Language
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Second. Where exposure cannot be adequately managed through the application of the above strategies, reducing risk to workers from being struck by motorized traffic through the use of appropriate positive protective devices;
Suggested Questions: How does Subpart K address worker safety?
Additional Information: None
Possible Problems: Avoid reading. Paraphrase. Make interesting.

## Slide 16: Requires to Address Worker Safety as Follows: (cont.):
3. Where exposure and risk reduction is not adequate, possible, or practical, manage risk through the application of appropriate intrusion countermeasures including, but not limited to, the use of uniformed law enforcement officers
Image: ATSSA
Notes: Key Message: Quote Subpart K Language
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Third, Where exposure and risk reduction is not adequate, possible, or practical, managing risk through the application of appropriate intrusion countermeasures including, but not limited to, the use of uniformed law enforcement officers.
Suggested Questions: What is adequate, possible or practical? {Illustrate that these are based on judgment}
Additional Information: None
Possible Problems: Avoid reading. Paraphrase. Make interesting.

## Slide 17: Requires to Address Worker Safety as Follows: (cont.):
4. Assure that the quality and adequacy of deployed temporary traffic control devices are maintained for the project duration
Notes: Key Message: Quote Subpart K Language
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Fourth, assuring that the quality and adequacy of deployed temporary traffic control devices are maintained for the project duration.
Suggested Questions: How does Subpart K address worker safety?
Additional Information: None
Possible Problems: Avoid reading. Paraphrase. Make interesting.

## Slide 18: How to Minimize Worker Exposure?
Utilizing the entire range of traffic management and control and highway safety strategies and devices used to avoid crashes in work zones that can lead to worker and road user injuries and fatalities, including:
  Positive Protection Devices
  Exposure Control Measures
  Other Traffic Control Measures
Module 3
Module 4
Module 4
Notes: Key Message: How to Minimize Worker Exposure?
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: In other words, we minimize worker exposure by utilizing the entire range of traffic management and control and highway safety strategies and devices used to avoid crashes in work zones that can lead to worker and road user injuries and fatalities, including:
  Positive Protection Devices
  Exposure Control Measures
  Other Traffic Control Measures
Suggested Questions: None
Additional Information: None
Possible Problems: Relate to the modules to come.

## Slide 19
Agency guidelines
Engineering study
Expected operating speed
Proximity of vehicles to workers and pedestrians
Project-specific factors
When to Use Positive
Protection Devices? Based on:
Image: ATSSA
Notes: Key Message: When to Use Positive Protection Devices?
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The determination of when to use positive protection is typically based on either a project-specific engineering study or agency guidelines (which also should be based on an engineering study). Both the project-specific study and agency guidelines typically consider the actual conditions expected to be encountered in the work zone combined with the characteristics of the various devices that may be available.
Suggested Questions: When to Use Positive Protection Devices?
Additional Information: The Roadside Design Guide (RDG) states that “the design and selection of work-zone safety features should be based on expected operating speeds and proximity of vehicles to workers and pedestrians.” Additional factors that may impact the decision are provided in these guidelines.
Possible Problems: None

## Slide 20
Cost
Installation/removal
Work space access
Adverse affects of barrier
Lack of suitable devices
Lack of standardized guidelines
Reliance on judgment
Obstacles to Overcome in the Deployment of Positive Protection Devices
Notes: Key Message: Discuss Obstacles to Overcome
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are some obstacles, such as cost, installation/removal, work space access, adverse affects of barrier, lack of suitable devices, lack of standardized guidelines and reliance on judgment.
Suggested Questions: Can you think of adverse affects of barriers? Limited sight distance, weight, installation/removal issues, etc.
Additional Information: None
Possible Problems: None

## Slide 21
The barrier itself is a hazard!
  If not needed for Positive Protection, eliminate the hazard and consider alternatives
Careful consideration should be given to other alternative strategies to minimize worker exposure
Remember!
Image: Midwest Roadside Safety Facility
Notes: Key Message: Use Barrier with Caution
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Don’t think that the barrier is a magic solution. Remember that the barrier itself is a hazard! If it is possible, eliminate the hazard and consider alternatives. Careful consideration should be given to alternative strategies to minimize worker exposure. Strategies to avoid barrier use should be considered. Barriers are not the only strategy available. This course will discuss some of these strategies.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 22
Several states have developed Positive Protection assessment processes, but most are based on motorists’ protection
An interactive “composite” Positive Protection assessment tool has been developed as part of this course
  Can be customized to your State’s needs!
Will discuss in Module 5!
Are There Positive Protection Assessment Processes?
Notes: Key Message: Introduce the Positive Protection Decision Making (assessment) Process
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Various states have developed processes. We will discuss them later. An interactive “composite” Positive Protection assessment tool has been developed as part of this course.
Suggested Questions: None
Additional Information: None
Possible Problems: Whet their appetite.

## Slide 23: Applicable Standards and Guidance
Manual on Uniform Traffic Control Devices
AASHTO Roadside Design Guide
State’s Positive Protection Guidelines
Manufacturer’s Instructions
Let’s review!
Notes: Key Message: Discuss Applicable Standards and Guidance
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: We can refer to the MUTCD which defines engineering study and engineering judgment. Also the AASHTO Roadside Design Guide and state guidelines. Let’s look at these!
Suggested Questions: Which standards and guidelines apply?
Additional Information: None
Possible Problems: None

## Slide 24: 1. Manual on Uniform Traffic Control Devices (MUTCD)
Temporary traffic barriers
Truck-mounted attenuators (TMA)
Vehicle arresting systems
  Removed from 2009 version (still permitted)
Definitions
  Engineering judgment
  Engineering study
Image: FHWA
Notes: Key Message: Discuss the MUTCD
Est. Presentation Time (minutes):
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The MUTCD discusses Temporary Traffic Barriers and Truck-Mounted Attenuators (TMA). It refers you to the Roadside Design Guide. Vehicle Arresting Systems Removed from 2009 version because they are not “traffic control devices”.
Suggested Questions: None
Additional Information: Subsection (b) refers to the MUTCD and the AASHTO Roadside Design Guide (RDG) as sources of information on work zone safety methods and traffic control strategies
Possible Problems: None

## Slide 25: What is Engineering Judgment?
The evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the:
  Applicability,
  Design,
  Operation, or
  Installation of a traffic control device
MUTCD Page 14, Definition 64
14
Notes: Key Message: Define an Engineering Judgment
Est. Presentation Time (minutes):
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the MUTCD definition: The evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.
Suggested Questions:
Additional Information: MUTCD Page 14, Definition 64
Possible Problems: None

## Slide 26: What is Engineering Judgment? (cont.)
Engineering judgment shall be exercised by an engineer, or by an individual working under the supervision of an engineer, through the application of procedures and criteria established by the engineer
Documentation of engineering judgment is not required
MUTCD Page 14, Definition 64
14
Notes: Key Message: Define an Engineering Judgment
Est. Presentation Time (minutes): 1-2 minutes
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the MUTCD definition: The evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.
Suggested Questions: How come engineering judgment does not need to be documented? We all have different judgments and we, as engineers, don’t have to explain ourselves in writing.
Additional Information: MUTCD Page 14, Definition 64
Possible Problems: May have to discuss the new 2009 MUTCD language stating that standard statements shall not be modified based on engineering judgment. Refer to FHWA’s interpretation available on iBackup and MUTCD webpage, found here: http://mutcd.fhwa.dot.gov/resources/interpretations/1_09_1.htm

## Slide 27: Engineering Study
Final Rule: “The need for longitudinal traffic barrier and other positive protection devices shall be based on an engineering study.”
14
Notes: Key Message: Introduce an Engineering Study
Est. Presentation Time (minutes): None
Explanation of Cues/Builds: None
Suggested Comments: Subpart K states that “The need for longitudinal traffic barrier and other positive protection devices shall be based on an engineering study.”
Suggested Questions: What is an engineering study? What is “shall”?
Additional Information: None
Possible Problems: The MUTCD indicates this is a “should” condition, not a “shall”.

## Slide 28: What is an Engineering Study?
The comprehensive analysis and evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.
MUTCD Page 14, Definition 65
14
Notes: Key Message: Define an Engineering Study
Est. Presentation Time (minutes):
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the MUTCD definition: It is the comprehensive analysis and evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.
Suggested Questions: What is comprehensive?
Additional Information: MUTCD Page 14, Definition 65
Possible Problems: None

## Slide 29: What is an Engineering Study? (cont.)
An engineering study shall be performed by an engineer, or by an individual working under the supervision of an engineer, through the application of procedures and criteria established by the engineer
An engineering study shall be documented
MUTCD Page 14, Definition 65
14
Notes: Key Message: Define an Engineering Study (cont.)
Est. Presentation Time (minutes):
Explanation of Cues/Builds: None
Suggested Comments: An engineering study shall be performed by an engineer, or by an individual working under the supervision of an engineer, through the application of procedures and criteria established by the engineer. An engineering study shall be documented
Suggested Questions: What is documentation?
Additional Information: MUTCD Page 14, Definition 65
Possible Problems: None

## Slide 30: 2. AASHTO Roadside Design Guide (4th Edition 2011)
Barriers
  Flare rates
Clear zones
  Width
Truck-mounted attenuators
Guidance or Regulation?
Image: AASHTO
Notes: Key Message: Introduce the AASHTO Roadside Design Guide
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The RDG provides GUIDANCE on these devices.
Suggested Questions: Is the RDG guidance or regulation? A design GUIDE.
Additional Information: Language in the final rule has been modified to make clear that guidance included in the AASHTO
Roadside Design Guide is not, and should not be construed as a ‘‘regulation.’’
Possible Problems: None

## Slide 31: 3. State’s Positive Protection Guidelines
Have been developed by several states
They vary from state to state
Will govern!
Will discuss in Module 5
Image: ATSSA
Notes: Key Message: State Positive Protection Guidelines
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Several states have developed Positive Protection Guidelines. We will discuss them later.
Suggested Questions: Why are these guidelines state-specific? Every state is different! Also because no national guidance has been available, states recognize its important to be consistent with application of positive protection.
Additional Information: None
Possible Problems: None

## Slide 32: 4. Manufacturer’s Instructions
Should be followed when using proprietary devices
May require separate training
Image: ATSSA
Notes: Key Message: 4. Manufacturer’s Instructions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The MUTCD recommends that proprietary devices are used in accordance with the manufacturer’s instructions and specifications. For instance, the roll ahead distance of a TMA varies by manufacturer. Use of such device may require specific training.
Suggested Questions: Are you specifying any proprietary devices?
Additional Information: None
Possible Problems: None

## Slide 33: Conflicting Goals?
Maximum levels of safety
Minimum worker exposure
Mobility
Cost
Time constraints
Short duration
Notes: Key Message: Discuss conflicting goals
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The more “safety” we provide, the more expensive the project will be. Our job is to achieve the best balance between these two objectives. This is not easy since these are conflicting goals. You should pull more for safety, rather than to cut costs. “Maintain traffic flow” is not mutually exclusive. Many strategies can accommodate both safety and mobility.
Suggested Questions: None.
Additional Information: Maintaining traffic flow and maintaining maximum levels of safety are not necessarily mutually exclusive. Several strategies can do both. Make sure to mention this.
Possible Problems: Turn into a discussion, if possible.

## Slide 34: The Designer’s Dilemma
TTC Plan
Mobility
Safety
Cost
Construct-
ability
Image: ATSSA
Notes: Key Message: Discuss conflicting goals
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The more “safety” we provide, the more expensive the project will be. Our job is to achieve the best balance between these 2. This is not easy since these are conflicting goals. You should pull more for safety, rather than to cut costs.
Suggested Questions: Which is more important? Safety or cost? SAFETY!
Additional Information:
Possible Problems: None.

## Slide 35: The Designer’s Role
To consider ALL project characteristics and factors, the standards and guidelines, and apply engineering judgment to minimize worker exposure through the use of positive protection and/or other strategies
Image: FHWA
Notes: Key Message: Discuss the designer’s role
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Your job as a designer is to take all this information, standards and guidelines and APPLY them to a specific situation utilizing your best engineering judgment and CONSIDERING the needs of ALL users and the safety of the workers.
Suggested Questions: So, what is the role of the designer in all this?
Additional Information: Can you satisfy the needs of ALL users? No, but we should consider the needs of ALL
Possible Problems: None.

## Slide 36
What factors influence a decision to use Positive Protection?
What devices are available to be used as Positive Protection?
What about short-term projects?
Which decision tools are available?
This course answers these questions!
Points to Ponder
Notes: Key Message: Points to Ponder
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Now that we know these things, these questions should come to your mind. This course answers these questions!
Suggested Questions: What factors influence a decision to use Positive Protection? What devices are available to be used as Positive Protection? What about short-term projects? Which decision tools are available?
Additional Information: None
Possible Problems: No need to answer these questions at this point. Whet their appetite.

## Slide 37: Recap
How do we minimize worker exposure?
Name some worker exposure strategies
Are there Positive Protection assessment processes?
What is engineering judgment?
What is the role of the designer?
Notes: Key Message: Recap
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Let’s see what we have learned: [questions]
Suggested Questions: See screen
Additional Information:
Name some issues with worker exposure: Workers are vulnerable, Their protection is left to engineering judgment, if at all, etc.
How do we minimize worker exposure? Positive Protection Devices, Exposure Control Measures, Other Traffic Control Measures
Name some worker exposure strategies: Full road Closures, Ramp Closures, Crossovers and Detours, Rolling Road Blocks
Are there Positive Protection assessment processes? Yes, they vary by State.
What is engineering judgment? The evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device
What is the role of the designer? Consider all the factors and design the best possible TTC plan that balances Safety, Cost, Mobility and Constructability factors.
Possible Problems: None

## Slide 38: Questions