## Slide 1: 2. Characteristics and Factors
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Course opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s introduce Positive Protection!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Discuss the project characteristics and factors that need to be considered when:
  Assessing the need for positive protection
  Selecting positive protection measures and other strategies to minimize worker exposure
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3
Where such devices offer the highest benefits to worker safety, such as situations where workers may be at increased risk of serious injury from exposure to traffic
Remember: Positive Protection Devices are Used…
Image: ATSSA
Notes: Key Message: Discuss when to use Positive Protection devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The determination of when to use positive protection is typically based on either a project-specific engineering study or agency guidelines (which also should be based on an engineering study). Both the project-specific study and agency guidelines typically consider the actual conditions expected to be encountered in the work zone combined with the characteristics of the various devices that may be available.
Suggested Questions: How do you define worker safety? What is risk?
Additional Information: The Roadside Design Guide (RDG) states that “the design and selection of work-zone safety features should be based on expected operating speeds and proximity of vehicles to workers and pedestrians.” Additional factors that may impact the decision are provided in these guidelines.
Possible Problems: None

## Slide 4: DISCUSSION
Which situations (type of work) place workers at increased risk from motorized traffic?
How do you define “risk”?
Definition of risk: exposure to the chance of injury or loss; a hazard or dangerous chance…
Notes: Key Message: Discussion regarding perception of risk
Est. Presentation Time: Depends on participation
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Risk is a human perception, which varies from person to person.
Suggested Questions: Which situations (type of work) place workers at increased risk from motorized traffic? How do you define “risk”?
Additional Information: Definition of risk: exposure to the chance of injury or loss; a hazard or dangerous chance: It's not worth the risk. Risk management is the identification, assessment, and prioritization of risks followed by coordinated and economical application of resources to minimize, monitor, and control the probability and/or impact of unfortunate events or to maximize the realization of opportunities. Risks can come from uncertainty in financial markets, project failures (at any phase in design, development, production, or sustainment life-cycles), legal liabilities, credit risk, accidents, natural causes and disasters as well as deliberate attack from an adversary, or events of uncertain or unpredictable root-cause. Several risk management standards have been developed including the Project Management Institute, the National Institute of Standards and Technology, actuarial societies, and ISO standards. Methods, definitions and goals vary widely according to whether the risk management method is in the context of project management, security, engineering, industrial processes, financial portfolios, actuarial assessments, or public health and safety.
Possible Problems: Try to generate discussion

## Slide 5: Design Considerations for Positive Protection Devices
Shall be considered:
  In work zone situations that place workers at increased risk from motorized traffic, and
  Where positive protection devices offer the highest potential for increased safety for workers and road users
How much risk are you willing to accept as a designer? What is high potential?
Notes: Key Message: Discuss design considerations for positive protection devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click.
Suggested Comments: We all accept different levels of risk. An example would be how much risk we accept with out financial investments. Some are willing to accept more risk than others, based on several factors, such as expected retirement age. In other words, Positive Protection devices shall be considered in work zone situations that place workers at increased risk from motorized traffic, and where positive protection devices offer the highest potential for increased safety for workers and road users, such as: {next slide}
Suggested Questions: What is “increased” risk? Risk that is more than “normal” or accepted.
Additional Information: None
Possible Problems: This is an intro slide for the section to come.

## Slide 6
Project scope and duration
Anticipated traffic speeds through the work zone
Anticipated traffic volume
Vehicle mix
Type of work (as related to worker exposure and crash risks)
What Should be Considered When Assessing Worker Exposure Strategies?
Notes: Key Message: Discuss factors that should be considered when assessing worker exposure strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s start by discussing factors that should be considered when assessing worker exposure strategies. We will discuss 14 of them. Here are the first five.
Suggested Questions: None
Additional Information: None
Possible Problems: No need to discuss these at this time. This is an intro slide.

## Slide 7
Distance between traffic and workers, and extent of worker exposure
Limited escape paths
Time of day
Consequences to road users resulting from roadway departure
Potential hazard to workers and road users presented by the device itself and during device placement and removal
What Should be Considered When Determining the Need for a Positive Protection Device?
Notes: Key Message: Discuss factors that should be considered when assessing worker exposure strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are factors 6-10.
Suggested Questions: None
Additional Information: None
Possible Problems: No need to discuss these at this time. This is an intro slide.

## Slide 8
Geometrics and/or work area restrictions that may increase crash risk
Access to/from work space
Roadway classification
Impacts on project cost and duration
Let’s discuss these factors!
What Should be Considered When Determining the Need for a Positive Protection Device?
Notes: Key Message: Discuss factors that should be considered when assessing worker exposure strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Box appears on click
Suggested Comments: And these are the last four. Let’s discuss them!
Suggested Questions: None
Additional Information: None
Possible Problems: No need to discuss these at this time. This is an intro slide.

## Slide 9
Positive Protection more cost-effective on long term projects
  e.g., More than three days (MUTCD)
1. Project Scope and Duration
A relatively long section of portable concrete barrier may not be feasible for a project duration shorter than the time it takes to install the barrier
115
Notes: Key Message: Discuss project scope and duration
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Box appears on click
Suggested Comments: Positive protection devices such as barriers become more cost effective when used on longer term projects. The Manual on Uniform Traffic Control Devices (MUTCD) defines long term as more than three days, but projects with duration of longer than two weeks may be especially appropriate for positive protection devices requiring substantial effort to install as these projects might otherwise result in substantial worker exposure to motorized traffic. For example, a relatively long section of portable concrete barrier may not be feasible for a project duration shorter than the time it takes to install the barrier.
Suggested Questions: None
Additional Information: See 2009 MUTCD Section 6G.02
Possible Problems: Students may not be familiar with the 5 categories of duration in the MUTCD. Be prepared to address the subject.

## Slide 10: Work Duration
Major factor in determining Positive Protection devices
Defined relative to the length of time a work operation occupies a spot location
The MUTCD defines five categories of duration:
115
Notes: Key Message: Define “duration” as per the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The five MUTCD categories offer guidance and options to the designer of a TCP in how much traffic control is needed; what types of devices might be appropriate for one job but inappropriate for another. These are the first two: Long-term and Intermediate term, along with their MUTCD definitions.
Suggested Questions: What is does “stationary” mean? The work space does not move!
Additional Information: Refer to MUTCD 6G-2.
Possible Problems: These “durations” may vary by state. Students may not be familiar with the 5 categories of duration in the MUTCD. Be prepared to address the subject.

## Slide 11: 1. Long-Term Stationary
  Work that occupies a location more than 3 days
  Subpart K provides example of “two weeks or more
115
The longer the project, the most cost- effective the use of portable barriers will be!
Image: ATSSA
Notes: Key Message: Define “duration” as per the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The five MUTCD categories offer guidance and options to the designer of a TCP in how much traffic control is needed; what types of devices might be appropriate for one job but inappropriate for another. These are the first two: Long-term and Intermediate term, along with their MUTCD definitions.
Suggested Questions: What is does “stationary” mean? The work space does not move!
Additional Information: Refer to MUTCD 6G-2.
Possible Problems: These “durations” may vary by state. Students may not be familiar with the 5 categories of duration in the MUTCD. Be prepared to address the subject.

## Slide 12: MUTCD Guidance Regarding Long-Term Projects:
..there is ample time to install and realize benefits from the full range of TTC procedures and devices that are available for use
Generally, larger channelizing devices, temporary roadways, and temporary traffic barriers are used
115
Image: ATSSA
Notes: Key Message: Discuss long-term projects
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The MUTCD provides guidance for long-term projects. It states that for long-term projects, there is ample time to install and realize benefits from the full range of TTC procedures and devices that are available for use. Generally, larger channelizing devices, temporary roadways, and temporary traffic barriers are used.
Suggested Questions: What is Guidance? Guidance are recommendations, or ‘should” conditions.
Additional Information: MUTCD Section 6G.
Possible Problems: None

## Slide 13
Image: ATSSA
Notes: Key Message: Illustrate a long-term project
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an examples of a long term project. Over 3 days! At long-term stationary TTC zones, there is ample time to install and realize benefits from the full range of TTC procedures and devices that are available for use. On long-term projects, larger channelizing devices, temporary roadways, and temporary traffic barriers are typically feasible (there may be others).
Suggested Questions: Which characteristics do long-term projects have? Day and night!
Additional Information: Photo is I-495 in Virginia.
Possible Problems: Show the photo quickly and move on. No need to discuss it or “pick” at it.

## Slide 14
Image: ATSSA
Notes: Key Message: Illustrate a long-term project
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is another example of a long term project. The duration of a project like this one warrants the use of positive protection.
Suggested Questions: None
Additional Information: Photo is I-495 in Virginia.
Possible Problems: Show the photo quickly and move on. No need to discuss it or “pick” at it.

## Slide 15: 2. Intermediate-Term Stationary
More than one daylight period up to 3 days or nighttime work lasting more than 1 hour
Barriers may not be feasible
The increased time to place and remove these devices in some cases could significantly lengthen the project, thus increasing exposure time
115
Notes: Key Message: Discuss long-term projects
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Subpart K provides example of “two weeks or more”. However, the MUTCD defines long term as “over three days”
Suggested Questions: What do you consider long-term?
Additional Information: Subpart K language: A comment relating to the specificity of the proposed rule noted that the original language ‘‘contains three specific requirements for the use of longitudinal barrier that cause significant concern, as they are restrictive and will have unintended negative consequences if applied unilaterally to all work zones. These requirements include: (1) Stationary work zones lasting two weeks or more;
Possible Problems: MUTCD defines long term as more than 3 days but Subpart K mentions “two week or more”

## Slide 16: 3. Short-Term Stationary
Daytime work that occupies a location for more than 1 hour within a single daylight period
Most maintenance and utility operations
115
Notes: Key Message: Define “duration” as per the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the other three: Short-term, short duration and mobile.
Suggested Questions:
Additional Information: Refer to MUTCD 6G-2.
Possible Problems: Some states use mobile and moving interchangeably. Be prepared to explain the differences: Mobile moves intermittently while moving moves continuously.

## Slide 17
Dangerous on high-speed facilities
Barriers are usually not practical or cost-effective
Maintenance and Utility Work
Notes: Key Message: Illustrate a short-term project
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As compared to stationary operations, mobile and short-duration operations are activities that might involve different treatments. Devices having greater mobility might be necessary such as signs mounted on trucks. Devices that are larger, more imposing, or more visible can be used effectively and economically. The mobility of
the TTC zone is important. Utility and short duration maintenance operation on high-speed facilities are dangerous operations since barriers are usually not practical or cost-effective. Safety in short-duration or mobile operations should not be compromised by using fewer devices simply because the operation will frequently change its location.
Suggested Questions: Which other strategies would you consider? How can we achieve “positive protection”?
Additional Information: Photo source unknown. Meant to show a typical short duration project, in this case, line painting.
Possible Problems: None

## Slide 18: 4. Short Duration
Work that occupies a location up to 1 hour
It often takes longer to set up and remove the TTC zone than to perform the work
“Simplified control procedures” may be warranted
116
Image: ATSSA
Notes: Key Message: Define “duration” as per the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the other three: Short-term, short duration and mobile.
Suggested Questions:
Additional Information: Refer to MUTCD 6G-2.
Possible Problems: Some states use mobile and moving interchangeably. Be prepared to explain the differences: Mobile moves intermittently while moving moves continuously.

## Slide 19: 5. Mobile
Work that moves intermittently or continuously
Safety should not be compromised by using fewer devices simply because the operation will frequently change its location
116
Image: ATSSA
Notes: Key Message: Define “duration” as per the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: You know how long the project is; drivers don’t. Their needs are the same!
Suggested Questions:
Additional Information: Refer to MUTCD 6G-2.
Possible Problems: Some states use mobile and moving interchangeably. Be prepared to explain the differences: Mobile moves intermittently while moving moves continuously.

## Slide 20
Generally 40+ mph or greater is considered a high-speed facility
For design purposes, consider using the anticipated operating speed, not the posted speed
2. Anticipated Traffic Speeds Through the Work Zone
Notes: Key Message: Discuss the anticipated traffic speeds through the work zone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Workers are at increased risk when traffic speeds are higher. Agencies may define high speed versus low speed, but generally 45 mph or greater is considered a high-speed facility. Consideration should be given to the average speed or the 85th percentile speed in addition to the posted speed limit when determining operating speed. For projects with free flow traffic conditions or limited sight distance, positive protection may be used to shield workers from higher speed traffic.
Suggested Questions: None
Additional Information: The MUTCD allows the use of the posted regulatory speed, the 85th percentile or the anticipated operating speed prior to construction. Encourage the use of the actual prevailing speed at the location.
Possible Problems: The definition of high-speed varies by state.

## Slide 21: High Anticipated Operating Speed
Critical, especially when combined with high traffic volumes
The higher the speed, the more severe the crashes will be, and the more unforgiving to exposed workers
Work zone speed management is critical!
Image: ATSSA
Notes: Key Message: Discuss the anticipated traffic speeds through the work zone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Speed is another important factor that deserves serious consideration to warrant Positive Protection devices. The higher the speed, the more severe the crashes will be, and the more unforgiving to exposed workers. Consideration should be made to manage speeds through the work zone in order to minimize the severity of crashes.
Suggested Questions: What do you consider high speed?
Additional Information: Subpart K language: A comment relating to the specificity of the proposed rule noted that the original language ‘‘contains three specific requirements for the use of longitudinal barrier that cause significant concern, as they are restrictive and will have unintended negative consequences if applied unilaterally to all work zones. These requirements include:…. (2) with a design speed of 45 mph or higher;
Possible Problems: None

## Slide 22: Lower the Posted Speed Only if There is a Good Reason!
Road user movement should be inhibited as little as practical, based on the following considerations:
  TTC at work and incident sites should be designed on the assumption that drivers will only reduce their speeds if they clearly perceive a need to do so
45
Image: ATSSA

## Slide 23: Probability of Pedestrian Dying as a Function of the Speed of Impacting Vehicle
https://one.nhtsa.gov/people/injury/research/pub/hs809012.html
Notes: Key Message: Discuss the anticipated traffic speeds through the work zone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Vehicle speed predicts severity of pedestrian injuries. With vehicle speeds below 20 mph the probability of serious or fatal injury is less than 20%; with speeds above 35 mph, most injuries are fatal or incapacitating. Excess and inappropriate speed is widespread and may contribute to around 30% of road traffic crashes and deaths. An average increase in speed of 1 km (0.625 miles)/hour is associated with a 3% higher risk of a crash involving an injury. Pedestrians have a 90% chance of surviving car crashes at 18 mph or below, but less than a 50% chance of surviving impacts at 28 mph or above. Above 25 mph, the chance of surviving drops considerably.
Suggested Questions: What do you consider high speed?
Additional Information: Source: Leaf WA, Preusser DF. 1999. Literature review on vehicle travel speeds and pedestrian injuries. National Highway Traffic Safety Administration. Washington DC. US Department of Transportation. https://one.nhtsa.gov/people/injury/research/pub/hs809012.html
Possible Problems: Chart was converted from metric and rounded to mph. Scale may be off a bit.

## Slide 24
Source: WalkingInfo.org

## Slide 25
In general, volumes greater than a few hundred vehicles per lane per hour are considered high volumes
High volume = lower speeds but more conflicts
High volume with high speeds is possible!
3. Anticipated Traffic Volume
Image: ATSSA
Notes: Key Message: Discuss the anticipated traffic volume
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Workers may be at increased risk when traffic volumes are higher. Volume to capacity ratios may help determine high versus low volume locations. High volume may approach a ratio of 1.0 but not exceed it since congestion will slow traffic naturally, resulting in less volume over time as compared with traffic flow at higher speeds. In general, volumes greater than a few hundred vehicles per lane per hour are considered high volumes. Urban areas may commonly have higher traffic volumes; therefore, consideration of positive protection in such settings is important. As we saw on the previous slide, speed is directly related to the probability of surviving a pedestrian (worker) crash. You would think that lower speeds always lower this risk, but the increased volume increases the possibility of conflict points and the number of crashes.
Suggested Questions: What do you consider high-volume?
Additional Information: Refer to Highway Capacity Manual.
Possible Problems: None

## Slide 26
Projects with a high percentage of truck and heavy vehicle traffic may benefit from positive protection
Crash testing criteria may not consider large vehicles
4. Vehicle Mix
Notes: Key Message: Discuss vehicle mix
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For those projects with a high percentage of trucks, the use of Positive Protection devices maybe easier to justify. The safety potential can be significant since trucks intrusions into the work zone may create serious crashes. As a designer, you should evaluate the vehicle mix and make the necessary adjustments to consider the needs of truck and other “special” vehicles. Trucks are more difficult to control and require longer distances to stop. For example, longer buffer spaces should be considered for trucks. Projects with a high percentage of truck and heavy vehicle traffic may benefit from positive protection due to the greater impact potential of a heavy vehicle intrusion into a work space
Suggested Questions: What do you consider high percentage of trucks?
Additional Information: None
Possible Problems: None

## Slide 27
The closer traffic is to the workers, the greater the benefit of positive protection
Examples:
  Shoulder maintenance
  Bridge slab replacement
  Widening projects
5. Type of Work (as Related to Worker Exposure and Crash Risks)
Image: ATSSA
Notes: Key Message: Discuss the type of work (as related to worker exposure and crash risks)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For operations that place workers close to travel lanes that are open to traffic, positive protection devices provide the greatest value in shielding workers. The value of these devices is enhanced where adequate lateral buffer space does not provide separation between motorists and workers or devices, and a longitudinal buffer is not available to protect workers by giving motorists adequate room to stop upon leaving the traffic space. This may be especially important for bridge projects or confined areas such as tunnels.
Suggested Questions: What do you consider “close”?
Additional Information: Photo is I-495 in Northern Virginia, by J. Morales.
Possible Problems: None

## Slide 28
Consider Positive Protection when buffer spaces (longitudinal and lateral) are not provided
  Especially important for bridge projects or confined areas such as tunnels
6. Distance Between Traffic and Workers, and Extent of Exposure
Image: ATSSA
Notes: Key Message: Discuss the distance between traffic and workers, and extent of worker exposure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The type of construction or maintenance work should also be considered when determining when to use positive protection devices. Work activities that place workers close to moving traffic for extended periods entail the greatest risk to workers and provide the greatest benefit for the use of positive protection. Examples include shoulder maintenance, bridge slab replacement, and widening projects. In addition, shadow vehicles with TMAs and rolling roadblocks can be used to shield workers from traffic during temporary traffic control device installation and removal. Rolling roadblocks that include law enforcement personnel provide time for workers to install and remove devices without direct exposure to traffic.
Suggested Questions: How do you determine the length of the buffer space?
Additional Information: Photo source unknown.
Possible Problems: None

## Slide 29
Image: ATSSA
Notes: Key Message: Illustrate with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here we see a maintenance project on a high-speed facility. Notice the lateral buffer and reliance on flashing lights on vehicles. During short-duration work, it often takes longer to set up and remove the TTC zone than to perform the work. Workers face hazards in setting up and taking down the TTC zone. Also, since the work time is short, delays affecting road users are significantly increased when additional devices are installed and removed. In addition to lateral buffer other possible measures include – closer spacing of devices, larger devices such as drums, and signs.
Suggested Questions: None
Additional Information:.
Possible Problems: None

## Slide 30
Installation and Removal Procedures Usually Expose Workers to Traffic
Consider in your Design!
Image: ATSSA
Notes: Key Message: Illustrate with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Workers are in close proximity to traffic during installation and removal procedures. Don’t neglect that part of your design. Think: Are workers exposed? How can we minimize that exposure?
Suggested Questions: Photo is a screen capture from a TX DOT YouTube video.
Additional Information: None
Possible Problems: None

## Slide 31: Workers Close to Travel Lanes
Proximity of worker to open lanes is a major consideration
2-ft rule may not be enough!
Image: ATSSA
Notes: Key Message: Discuss the 2-foot rule
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There is a rule of thumb in the industry. If the work is within 2 feet of an open lane, that lane should be closed. Even so, 3 feet is very close! Judgment will be involved here. But it is a matter of common sense.
Suggested Questions: How many of you have been in a work zone close to fast-moving traffic?
Additional Information: Photo source: Juan M. Morales (I-66 in near Vienna, Virginia)
Possible Problems: Source for this is unknown. Treat as a recommended practice.

## Slide 32
More difficult for workers to avoid vehicle intrusions
Heavy presence of equipment and materials in a confined area can also benefit from positive protection
7. Limited Escape Paths
Image: ATSSA
Notes: Key Message: Discuss limited escape paths
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Projects with limited or no available escape paths within a work zone restrict workers from avoiding errant vehicles that have entered the work space. Bridge and tunnel projects are examples of locations where positive protection can help protect workers with limited escape paths. Likewise projects with a heavy presence of equipment and materials in a confined area, which restrict workers ability to avoid an errant vehicle, can also benefit from positive protection.
Suggested Questions: None
Additional Information: Photo is the Goethals Bridge EB, NYC, I-278, by Juan M. Morales.
Possible Problems: None

## Slide 33: Limited Escape
Tunnels
Bridges
Images: ATSSA
Notes: Key Message: Discuss limited escape paths
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Tunnels and bridges pose significant problems for TTC due to restricted spaces and lack of escape routes for workers.
Suggested Questions: Why are bridges and tunnels problematic for TTC? Little room for devices and no escape routes. What options are there?
Additional Information: Photos by Juan M. Morales (NYC tunnels)
Possible Problems: Try to generate discussion.

## Slide 34
Tunnels Offer Limited Escape Paths
Image: NYCDOT
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Tunnels offer a lot of TTC challenges due to the confined spaces and reduced visibility. There is little room for signs, and the darkness impacts visibility. How have you dealt with these situations?
Suggested Questions: How can we provide an escape route for a tunnel like this one?
Additional Information: Photo is FDR Drive, in NYC, courtesy of NYC DOT.
Possible Problems: Try to generate discussion.

## Slide 35
Bridges Offer Limited Escape Paths
Image: NYCDOT
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Bridges also offer a lot of TTC challenges due to the confined spaces. There is little room for signs and seldom an escape route.
Suggested Questions: How can we provide an escape route for a bridge like this one?
Additional Information: Photo is Verazzano Narrows Bridge EB, courtesy of NYC DOT.
Possible Problems: Try to generate discussion.

## Slide 36
Lower volumes = higher speeds!
Higher costs
More impaired drivers
Reduced visibility
Illumination requirements
Glare avoidance
8. Time of Day (e.g., Night Work)
125
Image: ATSSA
Notes: Key Message: Discuss time of day and night work
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Performing work during off-peak periods may reduce exposure compared with higher traffic levels during peak periods. Even with reduced exposure to higher traffic, consideration should be given to the time of day and potential impacts on visibility during nighttime work when determining the need for positive protection. Paving projects are often performed at night to minimize impacts to traffic flow.
Some issues with nighttime work that may help warrant use of positive protection include higher speeds, drowsy drivers, and impaired drivers.
Special consideration should be given to the factors that affect night work operations (lighting, visibility, etc.).
Suggested Questions: None
Additional Information: The MUTCD does not address night work specifically, but enhancements to temporary traffic control setup for night work zones can be found in NCHRP 475 – A Procedure for Assessing and Planning Nighttime Highway Construction and Maintenance, NCHRP 476 - Guidelines for Design and Operation of Nighttime Traffic Control for Highway Maintenance and Construction, and NCHRP 498 – Illumination Guidelines for Nighttime Highway Work.
Possible Problems: None

## Slide 37
Proper Illumination, Worker Visibility and Glare Avoidance are Key!
126
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Proper illumination, worker visibility and glare avoidance are key to safe nighttime operations.
Suggested Questions: How do we minimize glare at nighttime?
Additional Information: The MUTCD does not address night work specifically, but enhancements to temporary traffic control setup for night work zones can be found in NCHRP 475 – A Procedure for Assessing and Planning Nighttime Highway Construction and Maintenance, NCHRP 476 - Guidelines for Design and Operation of Nighttime Traffic Control for Highway Maintenance and Construction, and NCHRP 498 – Illumination Guidelines for Nighttime Highway Work.
Possible Problems: None

## Slide 38
To accommodate run-off-the-road incidents, disabled vehicles, or emergency situations, unencumbered roadside recovery areas or clear zones should be provided where practical
9. Consequences to Road Users Resulting from Roadway Departure
46
Notes: Key Message: Discuss the consequences to road users resulting from roadway departure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This situation occurs in areas where motorists are at increased exposure to roadside hazards or are at higher risk of injury from roadway departure, such as where side slopes are greater than 4:1 (horizontal: vertical). Other potential hazards include vertical drop-offs, bridge piers, and construction materials and equipment located in the work space or on the roadside. Agency policy should dictate the magnitude of the drop-off condition that would warrant use of positive protection (the RDG references 3 inches or greater for a drop-off hazard).The RDG should be consulted to determine additional roadway departure hazard considerations.
Suggested Questions: What is the definition of a drop-off?
Additional Information: None
Possible Problems: None

## Slide 39
The total roadside border area, starting at the edge of the traveled way, that is available for an errant driver to stop or regain control of a vehicle
Might consist of a shoulder, a recoverable slope, and/or a non-recoverable, traversable slope with a clear run-out area at its toe
The Clear Zone
12
Notes: Key Message: Discuss the consequences to road users resulting from roadway departure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This situation occurs in areas where motorists are at increased exposure to roadside hazards or are at higher risk of injury from roadway departure, such as where side slopes are greater than 4:1 (horizontal: vertical). Other potential hazards include vertical drop-offs, bridge piers, and construction materials and equipment located in the work space or on the roadside. Agency policy should dictate the magnitude of the drop-off condition that would warrant use of positive protection (the RDG references 3 inches or greater for a drop-off hazard).The RDG should be consulted to determine additional roadway departure hazard considerations.
NOTE: The concept of the clear zone in WZ mostly applies to non-working hours. It is typical for the work to occur inside the work zone. For example, maybe there is a non-recoverable slope while the wz is active, but the slope must be made recoverable when the workers go home e.i., at night.
Suggested Questions: What is the definition of a drop-off?
Additional Information: None
Possible Problems: None

## Slide 40
The Clear Zone
Image: ATSSA
Notes: Key Message: Discuss the consequences to road users resulting from roadway departure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This situation occurs in areas where motorists are at increased exposure to roadside hazards or are at higher risk of injury from roadway departure, such as where side slopes are greater than 4:1 (horizontal: vertical). Other potential hazards include vertical drop-offs, bridge piers, and construction materials and equipment located in the work space or on the roadside. Agency policy should dictate the magnitude of the drop-off condition that would warrant use of positive protection (the RDG references 3 inches or greater for a drop-off hazard).The RDG should be consulted to determine additional roadway departure hazard considerations.
NOTE: The concept of the clear zone in WZ mostly applies to non-working hours. It is typical for the work to occur inside the work zone. For example, maybe there is a non-recoverable slope while the wz is active, but the slope must be made recoverable when the workers go home i.e., at night.
Suggested Questions: What is the definition of a drop-off?
Additional Information: None
Possible Problems: None

## Slide 41
Avoid non-recoverable slopes
  Slopes greater than 4:1
May address:
  Drop-offs
  Above ground hazards
  Bridge piers
  Construction materials and equipment located within the clear zone
Clear Zones
Notes: Key Message: Discuss the consequences to road users resulting from roadway departure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This situation occurs in areas where motorists are at increased exposure to roadside hazards or are at higher risk of injury from roadway departure, such as where side slopes are greater than 4:1 (horizontal: vertical). Other potential hazards include vertical drop-offs, bridge piers, and construction materials and equipment located in the work space or on the roadside. Agency policy should dictate the magnitude of the drop-off condition that would warrant use of positive protection (the RDG references 3 inches or greater for a drop-off hazard).The RDG should be consulted to determine additional roadway departure hazard considerations.
Suggested Questions: What is the definition of a drop-off?
Additional Information: None
Possible Problems: None

## Slide 42
Drop-off Condition
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an example of a drop-off condition. The slope is steeper than 4:1 and within the clear zone. If this is a long-term project, this would be a good candidate for barriers, based on engineering judgment and other factors. Another possibility is to provide a wedge to eliminate the drop-off condition.
Suggested Questions: Are these protection devices? No, they are channelizing devices.
Additional Information: Photo is Route 7 in Vienna, Virginia, by J. Morales.
Possible Problems: Don’t know if this is GOOD or BAD since we don’t know the duration and other factors.

## Slide 43
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an example of a drop-off condition.
Suggested Questions: Are these protection devices? What do you notice about these vests? (Some appear to be ANSI 107 Class 1, which makes them non-compliant)
Additional Information: Photo is Kihei, Hawaii, by SeaRay Beltran.
Possible Problems: None

## Slide 44
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an example of a drop-off condition.
Suggested Questions: Are these protection devices?
Additional Information: Photo is Kihei, Hawaii, by SeaRay Beltran.
Possible Problems: None

## Slide 45
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an example of a drop-off condition.
Suggested Questions: Are these workers protected? Is that cone going to help? What do you notice about these vests? (Some appear to be ANSI 107 Class 1, which makes them non-compliant)
Additional Information: Photo is Atlanta GA, by J. Morales.
Possible Problems: None

## Slide 46: Above-Ground Hazards
More than 4 inches in height
Firm and unyielding
Within the clear zone
During non-working hours (not in use)
Image: ATSSA
Notes: Key Message: Define drop-off and above-ground fixed hazards
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A hazard is any thing that is firm and unyielding, more than 4 inches in height and within the clear zone. Hazards should be removed, shielded or protected. A drop-off is a sudden drop in elevation, within the clear zone, parallel to traffic and steeper than 4:1.
Suggested Questions: What is a hazard? A drop-off? A hazard is any fixed object that is more than 4 inches, firm and unyielding. A drop-off is a sudden (Steeper than 4:1) drop in elevation, parallel to the travel lane, usually deeper than 2.5 inches, located within the clear zone.
Additional Information: See Roadside Design Guide
Possible Problems: These definitions may vary by State. Make sure to specify this is generic guidance from the RDG.

## Slide 47
Rule of thumb: the device should be protecting against the risk of striking something that may result in worse damage than striking the positive protection device itself
Impacts involving temporary barriers are potentially harmful, and may result in serious injuries to vehicle occupants
10. Potential Hazard Presented By The Device Itself & During Device Placement And Removal
Notes: Key Message: Discuss the potential hazard presented by the device itself & during device placement and removal
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Consideration should be given to the exposure created during placement and removal of the positive protection device itself. Additionally, a general rule of thumb is that the device should be protecting against the risk of striking something that may result in worse damage than striking the positive protection device itself (i.e., the damage resulting from driving into a hazard or over a drop-off would be greater than the damage associated with striking the positive protection device). Impacts involving temporary barriers are potentially harmful, and may result in serious injuries to vehicle occupants.
Suggested Questions: What is the definition of a clear zone?
Additional Information: None
Possible Problems: None

## Slide 48
For example:
  Severe curvature
  Narrow lanes
  Restricted sight distance
  Narrow shoulders
Sufficient advance warning should also be provided
11. Geometrics and/or Work Area Restrictions That May Increase Crash Risk
Notes: Key Message: Discuss the geometrics and/or work area restrictions that may increase crash risk
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Work area restrictions and/or geometric characteristics that increase risk to workers or motorists can also benefit from the use of positive protection devices. For example severe curvature, narrow lanes, restricted sight distance, or narrow shoulders could place workers and motorists at increased risk, and warrant consideration of positive protection. Sufficient advance warning should also be provided to ensure maximum levels of traffic safety around the protective devices.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 49
Consider equipment and construction vehicle access points
Positive Protection might cause ingress/egress issues resulting in safety hazards or constructability problems
  Blunt ends
Openings in barrier walls should be planned to ensure that ends are properly protected and that the walls do not create sight problems
12. Access to/from the Work Space
Notes: Key Message: Discuss access to/from the work space
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For longer term work zones such as some pavement rehabilitation projects where work vehicles and equipment cannot readily gain access from the ends of the work space, consideration should be given to equipment and construction vehicle access points throughout the work space. In some cases positive protection might cause ingress/egress issues resulting in safety hazards or constructability problems and therefore should be considered carefully in advance. If positive protection is used, crash cushions may be needed to protect the blunt end of barrier sections that provide construction vehicle access when longitudinal barriers are used.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 50
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an example of an egress situation, protecting the blunt end. The shoulder serves as a temporary acceleration lane.
Suggested Questions: Is this proper? Is the back barrier within the deflection space? Is this good or bad? What about the length of need?
Additional Information: Photo is I-495 in Virginia, by J. Morales.
Possible Problems: None

## Slide 51: Consider Temporary Acceleration Lanes
Hard to merge into fast-moving traffic. Cushion needed.
WORK AREA
TRAFFIC
WORK AREA
TRAFFIC
Easier to merge. No cushion needed!
Barrier
Acc. lane
Image: ATSSA
Notes: Key Message: Discuss temporary acceleration lanes
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text boxes and bottom figure appear upon click
Suggested Comments: How is the equipment getting in and out? Consider temporary acceleration lanes. Notice how the figure on top makes virtually impossible for slow-moving construction vehicles to merge into fast moving traffic. By creating a temporary acceleration lane (bottom figure), we have solved that problem, plus the need for a crash cushion is eliminated. An added bonus is that stalled vehicles may use that pocket during emergencies, without blocking a lane, as an emergency pull-off area.
Additional Information: Not in MUTCD
Possible Problems: None

## Slide 52: VDOT Construction Access Techniques
Image: VDOT
Notes: Key Message: Discuss temporary acceleration lanes
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Flare rate table appears on click
Suggested Comments: This is specific guidance from the Virginia DOT, regarding this technique. Notice the flare rate needed to protect the blunt end (bottom figure). The figure at the top requires an impact attenuator.
Additional Information: Source: VDOT 2011 Work Area Protection Manual, Appendix A.
Possible Problems: VDOT calls the barrier flare the “barrier transition slope ratio”.

## Slide 53
Image: VDOT
Notes: Key Message: Discuss temporary acceleration lanes
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This illustrates the previous point. Notice how the shoulder can be used as a temporary acceleration lane. TTC devices may be used to block the entrance and discourage vehicles from stopping in front of the acceleration lane/exit.
Additional Information: Photo is from Virginia I-495 HOT lanes, taken by Syd Tiffany, Senior Inspector, I-495 HOT Lanes
Possible Problems: None

## Slide 54
Positive Protection may be especially important for higher speed roadways such as freeways
  Example: portable concrete barriers (anchored) should be used to separate opposing traffic flows on a freeway crossover
13. Roadway Classification
Image: ATSSA
Notes: Key Message: Discuss roadway classification
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Positive protection devices should be considered for all roadways when needed, but may be especially important for higher speed, higher mobility roadways such as freeways. For example, portable concrete barriers should be used to separate opposing traffic flows on a freeway crossover and the resulting shared mainline.
Suggested Questions: Is classification related to speed? Yes!
Additional Information: None
Possible Problems: None

## Slide 55
Consider the cost of the positive protection devices relative to the project duration when determining need
Cost is a factor!
14. Impacts on Project Cost and Duration
Image: ATSSA
Notes: Key Message: Discuss the impacts on project cost and duration
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Consideration should be given to the cost of the positive protection devices relative to the project duration when determining need. Additionally, methods to minimize or eliminate exposure for workers and motorists should be considered early on in the planning stages of a project. These methods may include traffic diversion, full roadway closures, or work during off-peak periods such as nights and weekends. Positive protection devices can be selected and included in the project design, but should be preceded by consideration of these alternatives to determine the most appropriate plan that will minimize impacts to the safety of workers and motorists, while considering the impacts on project cost and duration. It is important to consider all options for managing traffic prior to determining the need for positive protection.
Suggested Questions: Is cost an important factor. Yes!
Additional Information: None
Possible Problems: This course does not discuss the specific costs of the various Positive Protection strategies. See module 3.

## Slide 56
How does the cost of positive protection weigh against safety?
What would you consider?
  Example: the added cost of concrete barrier for a short duration project?
Discussion
Notes: Key Message: Discussion
Est. Presentation Time: Depends on participation
Explanation of Cues/Builds: None
Suggested Comments: How does the cost of positive protection weigh against safety? What would you consider? Example: the added cost of concrete barrier for a short duration project? motorists, while considering the impacts on project cost and duration. It is important to consider all options for managing traffic prior to determining the need for positive protection.
Suggested Questions: None
Additional Information: None
Possible Problems: Try to generate discussion

## Slide 57: Module Recap
Name three factors that may determine the need for Positive Protection devices
Name two nighttime work considerations
How does speed affect the decision to use positive protection?
Notes: Key Message: Recap
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Let’s recap what we have learned: [Questions]
Suggested Questions: On screen.
Additional Information:
Name three factors that may determine the need for Positive Protection devices: duration, speed, volume, limited escape paths, etc.
Name two nighttime work considerations: More impaired driver, illumination requirements, etc.
How does speed affect the decision to use positive protection? Increases the likelihood of fatalities.
Any options for tunnel work? Total closures, reduce speeds, etc.
Possible Problems: None

## Slide 58: Questions