## Slide 1: 3. Positive Protection Devices
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Course opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s introduce Positive Protection!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Discuss design considerations of positive protection devices
Discuss the application of various positive protection devices
  Temporary Traffic Barriers
  Truck-Mounted Attenuators
  Vehicle-Arresting Systems
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module. Discuss design considerations of positive protection devices and briefly discuss the application of various positive protection devices:
  Temporary Traffic Barriers
  Truck-Mounted Attenuators
  Vehicle-Arresting Systems
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Remember: Positive Protection Devices Shall be Crashworthy
As per crashworthiness evaluation criteria contained in National Cooperative Highway Research Program (NCHRP) Report 350/Manual for Assessing Safety Hardware (MASH)
Image: AASHTO
Notes: Key Message: Discuss NCHRP 350 Crash Testing Requirements
Est. Presentation Time (minutes): 1-2 minutes
Explanation of Cues/Builds: None
Suggested Comments: Remember that positive protection devices shall be NCHRP 350 ( and MASH) Compliant, as per crashworthiness evaluation criteria contained in National Cooperative Highway Research Program (NCHRP) Report 350/MASH. FHWA policy requires that all roadside appurtenances such as traffic barriers, barrier terminals and crash cushions, bridge railings, sign and light pole supports, and work zone hardware used on the National Highway System meet the crashworthy performance criteria contained in the National Cooperative Highway Research Program (NCHRP) Report 350, “Recommended Procedures for the Safety Performance Evaluation of Highway Features.”.
Suggested Questions: How many of you are familiar with NCHRP 350 and MASH?
Additional Information: “Recommended Procedures for the Safety Performance Evaluation of Highway Features,” (NCHRP Report 350), 1993 Edition (TRB). Crashworthy—a characteristic of a roadside appurtenance that has been successfully crash tested in accordance with a national standard such as the National Cooperative Highway Research Program Report 350, “Recommended Procedures for the Safety Performance Evaluation of Highway Features.” The FHWA website at “http://safety.fhwa.dot.gov/programs/roadside_hardware.htm” identifies all such hardware and includes copies of FHWA acceptance letters for each of them.
Possible Problems: May need to expand based on the audience.

## Slide 4: Manual for Assessing Safety Hardware (MASH)
NCHRP 350 AASHTO rewrite
Adopted with sunset dates
  12/31/19
Test criteria changed slightly
MASH Implementation Agreement between FHWA and AASHTO
Image: AASHTO
Notes: Key Message: Introduce MASH
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: NCHRP 350 has been rewritten (under NCHRP Project 22-14(02)). The rewrite of NCHRP 350 is completed. It was reviewed by the AASHTO Technical Committee on Roadside Safety (TCRS) and is an AASHTO document. It's called The AASHTO Manual for Assessing Safety Hardware (MASH). This rewrite updated the test vehicles, the impact condition criteria, and the evaluation criteria. Temporary work zone devices, including portable barriers, manufactured after December 31, 2019, must have been successfully tested to MASH. Such devices manufactured on or before this date, and successfully tested to NCHRP Report 350 or the 2009 edition of MASH, may continue to be used throughout their normal service lives. There is a MASH Implementation Agreement between FHWA and AASHTO. Crashworthy end terminals should be installed in accordance to the Roadside Design Guide (RDG) and per the terminal’s installer/manufacture’s manual/specs.
Suggested Questions: Any experiences here with MASH. How are you handling the transition.
Additional Information: (will be updated based on final FHWA-AASHTO agreement)
Pickup truck increases from 4,400 lbs. to 5,000 lbs.
Small car increases from 1,800 lbs. to 2,420 lbs.
Small car impact angle changed from 20 to 25 degrees.
Terminal & Crash Cushion impact angle changed from 20 to 25 degrees. TL-4 truck increases from 17,600 lbs. to 22,000 lbs. TL-4 truck speed changed from 80 km/hr to 90 km/hr.
Possible Problems: At the time of this course, the AASHTO/FHWA MASH implementation agreement was in a state of flux. The instructor should review the status of the agreement and provide the most current information possible, Visit: https://safety.fhwa.dot.gov/roadway_dept/countermeasures/reduce_crash_severity/aashto_mash_implementation.cfm

## Slide 5: MASH Test Levels (TL)
Source: Manual for Assessing Safety Hardware
Notes: Key Message: Introduce MASH Test Levels
Est. Presentation Time: 1-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: MASH modified the test levels (speed and impact angle)
Suggested Questions: None
Additional Information: None
Key Points: It is important that the device used has been tested for the conditions present. For example, a TL-2 TMA cannot be used on a freeway!
Possible Problems: This may be beyond the scope of this course. Discuss this if questions come up. Keep brief!

## Slide 6: NCHRP Report 350
FHWA policy that requires all roadside traffic control used on the National Highway System meet the crashworthy performance criteria contained in the National Cooperative Highway Research Program (NCHRP) Report 350
72
Image: Transportation Research Board
Notes: Key Message: Discuss crash testing requirements
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: FHWA policy requires that all roadside appurtenances such as traffic barriers, barrier terminals and crash cushions, bridge railings, sign and light pole supports, and work zone hardware used on the National Highway System meet the crashworthy performance criteria contained in the National Cooperative Highway Research Program (NCHRP) Report 350, “Recommended Procedures for the Safety Performance Evaluation of Highway Features.”
Suggested Questions: What is the NHS? What is NCHRP? What are the requirements and how does that work?
Additional Information: FHWA oversight is limited to projects on the NHS. State transportation agencies may establish different standards for non-NHS projects if desired and may elect to use roadside hardware that has not been successfully tested to NCHRP Report 350 guidelines. Nonetheless, the FHWA strongly recommends the use of crash-worthy devices on all public facilities where run-off-the-road crashes may occur. Visit http://wzsafety.tamu.edu/files/nchrp350.stm
Possible Problems: MASH has replaced NCHRP 350. However, the 09 MUTCD does not mention MASH. After the discussion of 350, there is one slide that introduces MASH in case this question comes up. Various Sections of the MUTCD require certain traffic control devices, their supports, and/or related appurtenances to be crashworthy. Such MUTCD crashworthiness provisions apply to all streets, highways, and private roads open to public travel. Also, State Departments of Transportation and local agencies might have expanded the NCHRP Report 350 crashworthy criteria to apply to certain other roadside appurtenances.

## Slide 7: Positive Protection Devices Can be Grouped as:
Temporary Traffic Barriers
Truck-Mounted Attenuators (TMA)
Vehicle-Arresting Systems
Let’s Discuss Them!
Notes: Key Message: Introduce Positive Protection devices to discuss
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: text box appears on click
Suggested Comments: Let’s provide a list of the available Positive Protection options, along with a discussion of the factors and existing guidelines that should be considered. Positive Protection devices can be grouped as Temporary Traffic Barriers (concrete/mobile/moveable/others), Truck-Mounted Attenuators and Vehicle-Arresting Systems. Let’s discuss their characteristics and features.
Suggested Questions: None
Additional Information: None
Possible Problems: Some devices may be a combination of these.

## Slide 8: A. Temporary Traffic Barrier
Prevent penetration by vehicles while minimizing injuries to vehicle occupants
Provide positive protection to:
      Workers
      Highway users
      Shield:
      Drop-offs
      Roadside hazards
Image: ATSSA
Notes: Key Message: Discuss traffic barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The first device that we will discuss are traffic barriers. Barriers main purpose is protection, not channelization. Channelization is a secondary consideration. Decision to use should be based on protective needs not channelizing needs. If not needed for protection then IT SHALL NOT BE USED. The barrier itself is a hazard!
Suggested Questions: What is the main function of a barrier?
Additional Information: MUTCD 6F.70. Temporary traffic barriers are not TTC devices in themselves; however, when placed in a position identical to a line of channelizing devices (“tangent”) and marked and/or equipped with appropriate channelization features to provide guidance and warning both day and night, they serve as TTC devices .Temporary traffic barriers (see Section 6F.85) shall not be used solely to channelize road users, but also to protect the work space. If used to channelize vehicular traffic, the temporary traffic barrier shall be supplemented with delineation, pavement markings, or channelizing devices for improved daytime and nighttime visibility.
Possible Problems: None

## Slide 9
Image: ATSSA
Notes: Key Message: Discuss temporary traffic barriers
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
  Suggested Comments: This photo gives a good idea at how barriers provide excellent positive protection for workers. Although this is a general practice. It is dangerous for motorist as they may come in contact with stationary or slow moving contractor equipment.
Suggested Questions: what would happen if the barrier is impacted? It may move (deflect) into these workers. How can we keep it from deflecting? By anchoring the barrier?
Additional Information: Photo is from I-66 in Virginia.
Possible Problems: Avoid getting into a discussion about deflection here. The subject is discussed in detail later.

## Slide 10
Because the protective requirements of a TTC situation have priority in determining the need for temporary traffic barriers, their use should be based on an engineering study
113
Subpart K made this a SHALL condition!
Application of Temporary Traffic Barriers
Image: ATSSA
Notes: Key Message: Discuss traffic barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Temporary concrete traffic barrier prevents vehicles from entering the work area or to separate vehicles in temporary two-lane, two-way traffic on normally divided highways. The use of temporary concrete traffic barrier instead of standard temporary traffic control measures is based on engineering judgment. Barriers main purpose is protection, not channelization. Channelization is a secondary consideration. Decision to use should be based on protective needs not channelizing needs. If not needed for protection then IT SHALL NOT BE USED. The channelizing needs are always a secondary consideration. Barriers are used for protection of the work space.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 11
Clear zone
Deflection
Flare rates
Length of need (LON)
Crashworthy end terminal
Speed
Others
Barrier Selection Factors
Image: ATSSA
Notes: Key Message: Barrier selection factors
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
  Suggested Comments: When an errant vehicle leaves the roadway, the probability of an accident occurring depends on the vehicle’s speed, the angle at which it leaves the travel lane, its trajectory, and what lies in its path. If a crash does occur, its severity is dependent upon several factors, including the use of restraint systems, vehicle type, and the nature of the roadside environment. Of these factors, the highway designer has a significant measure of control only over the roadside environment. For a given project, based on field conditions and restrictions, the proper barrier should be selected based on these factors. Let’s discuss them briefly.
Suggested Questions: Can you think of others?
Additional Information: None
Possible Problems: This is an intro side. Next slides provide details. No need to elaborate here.

## Slide 12
“An unobstructed relatively flat area impacted by construction that extends outward from the edge of the traveled way”
  Recovery area (wide enough)
  No above-ground hazards
  4:1 or flatter (“recoverable”)
Source: MUTCD
1. Clear Zone
Notes: Key Message: Discuss the clear zone concept
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: A clear zone is the total roadside border area, starting at the edge of the travel lane, available for safe use by errant vehicles. This area may consist of a shoulder, a recoverable slope, and/or a traversable but non-recoverable slope and a clear runout area. (A “recoverable” fill slope is defined as no steeper than 4:1; a “traversable but nonrecoverable” slope is steeper than 4:1 but no steeper than 3:1 (a “critical” slope is steeper than 3:1 and considered an obstacle); cut slopes as steep as 3:1 are considered
recoverable). The desirable clear zone width, from a roadside safety standpoint, is as wide as cost-effectively possible. However, some practical value needs to be established
for design purposes.
Suggested Questions: None
Additional Information: Above-ground hazard: Fixed object that is firm and unyielding located within the CZ over 4 inches in height.
Possible Problems: None

## Slide 13: The Clear Zone
Requirements vary by State!
Image: ATSSA
Notes: Key Message: Define the clear zone
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: A clear zone is the total roadside border area, starting at the edge of the travel lane, available for safe use by errant vehicles. This area may consist of a shoulder, a recoverable slope, and/or a traversable but non-recoverable slope and a clear runout area. (A “recoverable” fill slope is defined as no steeper than 4:1; a “traversable but non-recoverable” slope is steeper than 4:1 but no steeper than 3:1 (a “critical” slope is steeper than 3:1 and considered an obstacle); cut slopes as steep as 3:1 are considered recoverable). The desirable clear zone width, from a roadside safety standpoint, is as wide as cost effectively possible. However, some practical value needs to be established for design purposes. Design clear zone values have been determined and are dependent upon traffic speeds and the roadside geometry. The CZ is measured from the edge of the traveled way.
Suggested Questions: How wide is the clear zone?
Additional Information: Possible Problems: None
.

## Slide 14: The Clear Zone: Errant Vehicle Lateral Distance Travel on Multi-Lane Highways
Image: NCHRP
Notes: Key Message: Explain the clear zone
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Figure 2 shows the probability of a vehicle accidentally leaving the traveled way of a multi-lane highway reaching a given distance laterally from the travel lanes before being able to stop or regain control. The greater the lateral distance from the traveled lane, the lower the likelihood that an errant vehicle will travel that distance before stopping or regaining control. For example, more than 90 percent of errant vehicles leaving the travel lanes of an Interstate travel out two feet
from the lane before regaining control or stopping. Only about 25 percent travel out more than 30 feet from the travel lanes.
Suggested Questions: Is 30 feet sufficient clear zone all the time?
Additional Information: Source NCHRP 492
Possible Problems: None

## Slide 15
Speed (mph) | Width (ft.)
60 or greater | 30
45-55 | 20
40 | 15
30-40 | 14
Source: 2011 Roadside Design Guide
*Requirements vary by State!
Example of Clear Zone Widths for Work Zones*
Notes: Key Message: Discuss CS width
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Design clear zone values have been determined and are dependent upon traffic speeds and the roadside geometry; they are given in this table. This is a component of the forgiving highway concept.
Suggested Questions: None
Additional Information: Refer to 2011 RDG Page 9-2.
Possible Problems: Some states may have state-specific CZ tables. This is a guideline.

## Slide 16
The distance a barrier will “deflect” when struck
Varies with:
    Type of barrier
    Speed of impact
    Angle of impact
    Mass of impacting vehicle
2. Deflection
Image: Roadside Design Guide
Notes: Key Message: Discuss barrier considerations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second selection is deflection. First they all require solid structural connections, because even 20 foot sections of concrete barrier does not have enough mass to resist overturning by itself. Chapter 9 of the RDG details crash tested connections. A barrier wall very c lose to the travel lane can be very intimating to drivers, so give them as much room as possible. The RDG recommends at least 2 feet. There is a length of need consideration with temporary barriers. It may not be cost effective to provide the full Length of Need (LON), but remember that vehicles can get around the upstream end, so some is needed. Flare rates should be kept as flat as conditions allow. Just as with permanent barriers, slopes in front of temporary barriers should be 1V:10H or flatter. Finally, remember that all temporary barrier systems deflect when struck. The amount of barrier deflection depends on several factors:
• type of barrier,
• barrier length,
• how barrier components are connected,
• if and how barrier is anchor,
• speed of impacting vehicle,
• angle of impact, and
• mass of impacting vehicle.
Suggested Questions: What is barrier deflection?
Additional Information: Refer to AASHTO Roadside Design Guide, Chapter 9, for additional information. Photo source is unknown.
Possible Problems: None

## Slide 17: All Barriers are not Equal
Image: Midwest Roadside Safety Facility
Notes: Key Message: Barrier variability
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
  Suggested Comments: Different barriers behave differently when struck, depending on their weight, connections, wall angles and deflection. This is a NCHRP TL-3 Conventional Barrier Crash Test with ¾ ton pickup impacting temporary F shape concrete barrier at 62.5 mph at 25 degrees. Although this is a pass, it is a very aggressive test, with high occupant risks and stability issues. There is also the potential for secondary crashes. Use the proper barrier for your specific application. These are barrier selection factors.
Suggested Questions: Are all barriers the same
Additional Information: Deflection 4.0 to 6 ft., Trajectory & stability issues
Possible Problems: Video must be in the same folder as the PowerPoint in order to play.

## Slide 18: Typical Lateral Deflection Distances of Work Zone Barriers
Source: FHWA, Use of Work Zone Clear Zones, Buffer Spaces, and Positive Protection Deflection Distances
Notes: Key Message: Typical Lateral Deflection Distances of Work Zone Barriers
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
  Suggested Comments: Here are some typical deflection distances. As discussed, there are several factors that should be considered before settling on a given deflection distance.
  Suggested Questions: None
Additional Information: Source: Use of Work Zone Clear Zones, Buffer Spaces, and Positive Protection Deflection Distances
Possible Problems: These are typical deflections. They also vary by state.

## Slide 19: 3. Flare Rates
Depend on speed
  Typically 17:1 to 20:1 flare for freeways
  5:1 to 6:1 for urban areas
Not in MUTCD but in RDG
Vary by State
1
20
Image: ATSSA
Notes: Key Message: Discuss use of flare for protection of the blunt end
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: Text box appears on click
  Suggested Comments: The third factor is the flare rate. The flare angle depends on speed. Refer to the Roadside Design Guide or consult your local agency for specific information. Typically it is 17:1 to 20:1 (“20 to 1”) flare for freeways. For example, for every foot moved laterally, we move 20 feet longitudinally. This is a precise angle with redirective properties.
Suggested Questions: None
Additional Information: None
Possible Problems: The picture shown is a detail of TA 34, page 701. Indicate that the flare shown in this picture is more like 1:1 (45 degrees) and is very misleading. A 20:1 flare is much more gradual (see next slide). Note: The flare might have a different name depending on the State. For example, in Virginia, it is called the “slope ratio”.

## Slide 20
In order to mitigate the effect of striking the upstream end of a temporary traffic barrier, the end shall be installed in accordance with AASHTO’s “Roadside Design Guide” by:
  Flaring until the end is outside the acceptable clear zone or
  Providing crashworthy end treatments
113
Flares Shield Blunt Ends!
Notes: Key Message: Discuss Shielding of Blunt ends
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The treatment of the end of the barrier in the work zone is also an important consideration. Typically, the barrier may be flared away from traffic and a crash cushion used to protect the end. The effective length of the barrier will vary depending on whether the crash cushion is non-redirective, redirective-gating, or redirective-non-gating. Using a redirective non-gating crash cushion will reduce the amount of barrier needed to protect a hazard because a portion of the crash
cushion can be used as part of the length of need. Engineering analyses should be performed to determine the appropriate crash cushion to use in a particular situation. The blunt end of a barrier may be treated with a crash cushion or with a flare. A flare is a precise angle to redirect errant vehicles.
  Suggested Questions: None
Additional Information: MUTCD: In order to mitigate the effect of striking the upstream end of a temporary traffic barrier, the end shall be installed in
accordance with AASHTO’s “Roadside Design Guide” (see Section 1A.11)
Possible Problems: None

## Slide 21
Design Speed (mph) | Flare Rate
70 | 20:1
60 | 18:1
55 | 16:1
50 | 14:1
45 | 12:1
40 | 10:1
30 | 8:1
*Source: 2011 RDG; Vary by State
Typical Flare Rates*
Notes: Key Message: Discuss typical flare rates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This table shows some typical flare rates for rigid concrete barriers. Remember that these rates may vary by State. These are MAXIMUM flare rates are for RIGID barriers inside the shy line. RDG Page 5-48. Flare rate is the rate at which a barrier moves from a larger offset to a closer offset from the edge of traveled way. Although it is desirable to flare the barrier system as quickly as possible, there are two criteria that must be satisfied for the barrier exposed to approaching traffic. First, in order to keep the angle of impact with the barrier from being too severe, the flare rate is limited to the values shown on the table, which are based on speed and type of the barrier system. Second, a concrete barrier should only be flared if it can be done on 10:1 or flatter For one directional roadways, the downstream flare rate, as the barrier moves away from the traveled way, should not be sharper than 2:1.
Suggested Questions: What does 20 to 1 mean?
Additional Information: None
Possible Problems: May vary by State.

## Slide 22
Lane Closure with Temporary Barrier
197
Image: FHWA
Notes: Key Message: Discuss lane closure with barrier
Est. Presentation Time: 5 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Notice how the taper and buffer are formed with lightweight devices, like drums. The barrier is used for protection and secondarily for delineation of the work space. Notice the buffer space. Also notice that the blunt end of the barrier is protected by a “flare” which will discuss in a moment.
Suggested Questions: Is the taper formed with the barrier? No.
Additional Information: None
Possible Problems: The flare shown is misleading since it shows a 1:1 flare (45 degrees). The right flare in a freeway environment is more like 20:1. Discuss as needed based on audience level.

## Slide 23
The minimum length of effective barrier needed upstream, beginning at the hazard, to adequately shield it
LON
4. Length of Need (LON)
Notes: Key Message: Discuss LON
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The fourth factor is the length of need. If the barrier is a hazard, let’s use the least possible to provide protection! The LON is the length of effective barrier needed upstream, beginning at the hazard, to adequately shield it. As the barrier placement gets closer to the edge of the travel lane, the LON gets progressively longer; this is another reason to locate the barrier as far away as possible.
Suggested Questions: What is the LON?
Additional Information: None
Possible Problems: None

## Slide 24
Vehicles leave the travel way in advance of the hazard, they should either be:
  Safely brought to a stop before impacting the obstacle if the departure is in advance of the barrier and it gets behind the barrier
  Redirected by the barrier along its face (or impact its crashworthy end treatment)
When the LON is provided:
Notes: Key Message: Discuss LON considerations
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: When the LON is provided, vehicles leaving the travel way in advance of an obstacle should either be: 1. safely brought to a stop before impacting the obstacle if the departure is in advance of the barrier and it gets behind the barrier; or 2. redirected by the barrier along its face (or impact its crashworthy end treatment). The LON generally includes some portion of the end treatment. The minimum run of barrier upstream of an obstacle, including LON and the total end treatment, is 75ft. unless otherwise documented.
Also consider the minimum length for a barrier needed to perform at an acceptable level, e.g. NCHRP test level 3. Follow the manufacturer’s product specifications
Suggested Questions: What is the LON?
Additional Information: Source: MD SHA Guide for Traffic Barrier Placement and End Treatment Design
Possible Problems: Discuss based on the audience. Don’t dwell of this.

## Slide 25
15 D
D
Estimating the LON
Image: Maryland SHA
Notes: Key Message: Discuss LON field approximation
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A “field expedient” procedure for approximately determining the LON on high speed roadways is provided for use on field reviews. This procedure will be fairly close to the formula application for obstacles that extend beyond the design clear zone, but will yield somewhat lesser values as the back of the obstacle is less distance from the edge of the pavement; but it is still good for rough application. 15 x D!
Suggested Questions: How can we approximate the LON?
Additional Information: MD SHA Guide for Traffic Barrier Placement and End Treatment Design
Possible Problems: Discuss based on the audience. Don’t dwell on this.

## Slide 26
The end shall be installed in accordance with RDG by:
  Flaring until the end is outside the acceptable clear zone or by
  Providing crashworthy end treatments
113
5. Crashworthy End Terminals
Image: ATSSA
Notes: Key Message: Discuss end terminals
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The blunt end of the barrier is a hazard itself. It must be protected, by either flaring until the end is outside the acceptable clear zone or by providing crashworthy end treatments.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 27: The Blunt End of a Barrier is a Hazard!
Shield with:
  Flare
  Crashworthy end treatment
All blunt ends shall be appropriately flared or protected with properly installed and maintained crashworthy cushions
Image: FHWA
Notes: Key Message: Discuss protection of the blunt end
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The blunt (exposed) end of the barrier is a hazard and must be protected. There are two ways to protect it: providing a flare and/or providing a crash cushion.
Suggested Questions: None
Additional Information: Photo taken during a crash test.
Possible Problems: None

## Slide 28: Crash Cushions Shall be:
Crashworthy
designed for each application to stop or redirect errant vehicles under prescribed conditions
113
Image: ATSSA
Notes: Key Message: Discuss crash cushions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Use the proper device for the conditions at hand. These conditions include speed of vehicles and their weight.
Suggested Questions: None
Additional Information: MUTCD Section 6F.82
Possible Problems: None

## Slide 29: Types of Crash Cushions
Redirective
  Redirects the errant vehicle
Non-Redirective
  Decelerates the errant vehicle
Refer to the Roadside Design Guide
http://www.ssshinc.com/products
https://pss-innovations.com/safety-products/crash-cushions-channelizers-drums/crashgard-sand-barrel-system
Notes: Key Message: Discuss types of crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Each text box appears upon click
  Suggested Comments: Two types of crash cushions: redirective and non-redirective. Redirective crash cushions may no decelerate the impacting vehicle but rather redirect the vehicle back to the highway. Non-redirective one actually decelerate the vehicle to a stop, hence called “inertial”.
Suggested Questions: What’s inside these barrels? Sand! Not water.
Additional Information: AASHTO’s Roadside Design Guide contains additional information on the use of crash cushions. Energite III and Quadguard CZ Sand barrel attenuators are initially low-cost but they need nearly total replacement after a hit. More sophisticated attenuators like the Quadguard CZ are quite expensive, but can be restored quickly and cheaply, sometimes without the need to replace any parts at all.
Possible Problems: None

## Slide 30
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This an example of crash cushion, It protects the blunt end. This is an inertial system, non-redirective.
Suggested Questions: What do the stripes mean? Pass either way!
Additional Information: Photo is I-495 in Virginia, by J. Morales.
Possible Problems: May not be acceptable in some states. Device spacing appears to be too much.

## Slide 31
The work zone design speed will determine the barrier to be used
  E.g., TL- 2 vs. TL-3
  Follow the manufacturer’s recommendations
6. Speed
Image: ATSSA
Notes: Key Message: Discuss how speed affects barrier selection.
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: As we discussed previously, speed is a major factor in determining the need for Positive Protection devices. It is also a factor in determining which barrier to use. Some barriers are suitable for certain speeds only. Usually, the state specifications would tell you the type of barrier that would be required based on speed and a reference to the NCHRP-350 test level (TL).
Suggested Questions: How does speed impact barrier selection?
Additional Information: Photo is Fairfax County Parkway in Fairfax, Virginia, by J. Morales.
Possible Problems: The RDG (see Table 5-5. Selection Criteria for Roadside Barriers) does not explicitly list speed as a selection factor. Speed, however, is considered indirectly through deflection (and clear zone).

## Slide 32
Sight distance restrictions
Visibility problems
Need for local access through the barrier(s)
Worker safety (risk assessment)
Installation and removal considerations
Access and egress
7. Other Temporary Barrier Design Considerations
Notes: Key Message: Temporary barrier design considerations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Here is a checklist of temporary barrier design considerations. Some of these are constructability considerations. {Elaborate as needed}
Suggested Questions: How is visibility affected by a barrier?
Additional Information: None
Possible Problems: Treat as a checklist. Provide examples as needed.

## Slide 33
Barrier product selected
Vehicle type, mass, proximity and speed
Proximity of work to the barrier versus deflection
Ability to ensure correct conditions for operation
Likelihood of attachments including anti-gawking screens striking workers
Risk Exposure Factors
(Work Behind Barriers)
Notes: Key Message: Temporary risk exposure factors
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The risk exposure factors of working behind a barrier are listed here. The risk will depend on barrier product selected, the vehicle type, mass, proximity and speed, proximity of work to the barrier versus barrier deflection, the ability to ensure correct conditions for operation and the likelihood of attachments including anti-gawking screens striking workers
Suggested Questions: What affects the risk of working behind a barrier?
Additional Information: Risk = exposure for all practical purposes
Possible Problems: Treat as a checklist. Provide examples as needed.

## Slide 34
Concrete
Ballast-filled
Anchored
Mobile
Movable
Steel
CHECK WITH YOUR STATE!
Types of Temporary Traffic Barriers
Image: ATSSA
Notes: Key Message: Discuss types of traffic barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
  Suggested Comments: There are several types of barriers that are acceptable in several states. Some are listed here. Let’s look at them and their characteristics.
Suggested Questions: Can you think of any others?
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Photo is from I-495 in Virginia, by J. Morales.
Possible Problems: This is an intro slide. Each barrier type is discussed in the following slides.

## Slide 35
A “Barrier” is a longitudinal device that has met the Report 350/MASH criteria for a redirective barrier at TL-2 or above
A “Barricade” is a channelizing device
  Type 1 and 2
A “Longitudinal Channelizing Device” is a channelizing device
Barrier, Barricade or Longitudinal Channelizing Device?
Notes: Key Message: Define barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Barriers and longitudinal channelizing devices are not the same thing. Ask yourself: Are the devices being used for protection or for delineation? The answer will dictate the devices to use. A longitudinal channelizer is not a barrier because, upon impact by a vehicle, the plastic units rupture and the vehicle penetrates the wall. Some longitudinal channelizers can be converted into crashworthy barriers with the addition of continuous steel rails or by virtue of an internal steel framework.
Suggested Questions: What is the difference between a barrier and a barricade (longitudinal channelizing device)?
Additional Information: Source: NCHRP REPORT 350 DEVICES IN WORK ZONES , Presentation by Nick Artimovich, Feb 2004, http://safety.fhwa.dot.gov.
A "barrier" is a device that safely redirects, slows, or stops an errant vehicle and prevents a more severe crash or prevents vehicles from entering the work area. Barriers include w-beam guardrail, jersey barriers (“K-rail” in California), steel barriers, bridge railings, weak post cable barriers, certain water-ballasted plastic units, and crash cushions. They must be crash tested at 100 km/hr using a small car and a pickup truck to assess occupant risk and barrier integrity. The test vehicle may not penetrate or vault over a barrier. When put in place each unit must be physically connected to the next unit per the state standard or per the manufacturer’s instructions. If the units are merely butted end to end, or if the connection hardware is missing a hazard exists that is dangerous to both the traveling public and the workers. A "barricade" is a lightweight channelizing device that warns motorists of a hazardous situation and offers little or no resistance when hit. For example, a barrier offers "positive protection" to shield workers in a work zone from being hit by an errant motorist while a barricade does not. A “channelizer” is a line of traffic control devices used to delineate the traveled way. Barricades must have orange and white reflectorized striping in accordance with Part 6 of the MUTCD, and include Type I and II "sawhorse" barricades, Type III Road Closure barricades, and some large plastic units that accept water ballast, among others. Barricades must be crash tested at 100 km/hr with a small car to ensure that they do not cause harm to occupants of the impacting vehicle when they are struck.
A hybrid device called a "longitudinal channelizing device" or “longitudinal channelizer” consists of large plastic units linked together, end to end, forming a wall. They are useful for controlling pedestrian traffic, guiding vehicles through confusing work zones, discouraging the use of median crossovers, and providing more delineation when only a line of cones or drums are typically used.
Possible Problems: None

## Slide 36
Include cones, tubular markers, vertical panels, drums, barricades, and longitudinal channelizing devices
NOT POSITIVE PROTECTION DEVICES
100-101
Channelizing Devices
Images: FHWA

## Slide 37
Have not met the crashworthy requirements for temporary traffic barriers
Should not be used to shield obstacles or provide positive protection for pedestrians or workers
Longitudinal Channelizing Devices
105- 106
Notes: Key Message: Discuss LCDs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Even though LCDs look like barriers, they ARE NOT protection devices. They are mainly used for pedestrian accessibility/ listed here. Their use is a State-preference.
Suggested Questions: None
Additional Information: Section 6F-71
Possible Problems: Their use is a State-preference.

## Slide 38
Do NOT redirect a vehicle
Do not prevent vehicle intrusions
NOT A POSITIVE PROTECTION DEVICE!!
Longitudinal Channelizing Devices
105
Notes: Key Message: Discuss LCDs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Even though LCDs look like barriers, they ARE NOT protection devices. They are mainly used for pedestrian accessibility/ listed here. Their use is a State-preference.
Suggested Questions: None
Additional Information: Section 6F-71
Possible Problems: Their use is a State-preference.

## Slide 39
Notes: Key Message: Discuss LCDs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This a sample sticker that ATSSA has developed to make sure these LCDs are not used as protection devices.
Suggested Questions: None
Additional Information: Section 6F-71
Possible Problems: None

## Slide 40
Longitudinal Channelizing Devices (LCD) are not Positive Protection Devices
Image: ATSSA
Notes: Key Message: Discuss LCDs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This a good application for LCDs: to detour pedestrians in compliance with the ADA.
Suggested Questions: None
Additional Information: Photo source unknown.
Possible Problems: None

## Slide 41
Perhaps the most common
Self-standing
Most common types:
  F-Shape**
  Jersey shape
  Single slope
105
1. Portable Concrete Barriers (PCB)
Image: ATSSA
Notes: Key Message: Discuss concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The preferred shape for concrete barriers is the F-shape, which has 9 inches at the top. The generic “Jersey” shape is no longer acceptable in most states. These barriers are held in place by their own weight. The preferred installation method for temporary concrete traffic barrier is freestanding and requires a minimum 2 ft. (0.6 m) clear area behind the barrier to allow for lateral deflection in both work areas and lane separation situations. Unpinned the deflection is 4 to 6 ft for TL3 62mph @ 25 degrees.
Suggested Questions: What is deflection? The distance the barrier would move when struck.
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Clear zone behind barrier has not been routinely considered. Impact tests TL-3 is designed for failure. To determine whether vehicle will vault, penetrate or flip over. Rule of thumb is that for each lane the vehicle can gain 7 degrees (on 3 lane int. 7,14,21 degrees. Extra 4 is for shoulder. That said you would have to start in the fast lane keep your foot on the accelerator and steer into the wall to obtain the result of the test. That is why you don’t see temp. barrier move 4-6 ft very often.
Possible Problems: Tailor to the state

## Slide 42: Jersey Shape vs. F-Shape
Jersey Shape
F-Shape
7”
10”
32”
32”
Images: AASHTO
Notes: Key Message: Discuss concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: These are the two most common concrete safety shapes. An important difference between the NJ and the F shapes is the height of the slope break. The lower break on the F shape (7”) helps minimize the lifting of the impacting side of the vehicle, reducing the tendency to roll small vehicles. The F shape is preferred over the NJ shape and it is required in most states.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Jersey Barriers: Jersey barriers are the original and most widely used safety shape concrete barriers. The only difference between Jersey barriers and F-shape barriers is that the distance from the ground to the slope break point is 13 inches in Jersey barriers, versus 10 inches for F-shape barriers. In high speed impacts, there is a greater likelihood that a small car will be rolled by a Jersey barrier than by an F-shape barrier. F-Shape Barriers: The F-shape barrier was specifically engineered to limit the potential for small cars to rollover upon impact. The F-shape barrier begins with a 3-inch vertical face at the pavement level, then breaks to a sloped face that rises to a height of 10 inches, before changing to a nearly vertical face at the top of the barrier. F-shape barriers are not shaped like the letter "F." They get their name from the research study that analyzed the performance of barrier design parameters, where barrier configurations were labeled A through F, and F was the best-performing design. Refer to: http://www.fhwa.dot.gov/publications/publicroads/00marapr/concrete.cfm
Possible Problems: 42-inch barriers are now common. Refer students to their state’s Specifications and QPL.

## Slide 43
PCB Deflection (Unanchored)
2 ft. up to 45 mph
4 to 6 ft for TL-3 62mph @ 25 degrees
Image: AASHTO
Notes: Key Message: Illustrate barrier deflection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice how an unbolted barrier deflects!
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide, Chapter 9, for additional information. Photo source is unknown.
Possible Problems: None

## Slide 44
Long-term projects
Workers close to high-speed traffic
Either worker exposure to traffic or road user exposure to work space hazards, such as a drop-off condition, are present on a regular basis
Typical Applications:
Image: ATSSA
Notes: Key Message: Discuss the typical uses of concrete barrier
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory
Suggested Questions: What is a long-term project? What is “limited”? What is “regular basis”?
Additional Information: Photo is from I-495 in Virginia, by J. Morales.
Possible Problems: Try to generate discussion.

## Slide 45
Substantial installation and removal costs
Less cost-effective for shorter term projects
Not suited for short duration work or moving operations
Reusable/Low maintenance
Relative Costs and Benefits
Image: ATSSA
Notes: Key Message: Discuss the typical uses of concrete barrier
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Although barriers are relatively low-cost, they do have substantial I/R costs. Equipment to handle the barriers must be utilized and they usually require lane closures for installation. As the duration of the project increases, the cost of barriers drops, making their use on long-term projects more feasible. They require little maintenance and can be reused.
Suggested Questions: What is “substantial”? What alternatives would you consider? How is cost considered in your decision?
Additional Information: Photo is from I-495 in Virginia, by J. Morales.
Possible Problems: Try to generate discussion

## Slide 46
Space is required for heavy equipment to install and remove the barriers
Deflection limited to the space available behind the barrier
Consideration must be given to access and egress points
Exposed barrier ends must be protected
Exposure associated with installation/removal
Other PCB Considerations
Notes: Key Message: Discuss other considerations of concrete barrier
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory
Suggested Questions: How does access affect barrier use?
Additional Information: None
Possible Problems: Treat as a checklist. Don’t dwell!

## Slide 47
Image: ATSSA
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Here you see a barrier being installed. Notice the a lane closure (short term?) is needed. Also notice the worker exposure. Additional lateral buffer lane should be taken to the left of the crane.
Suggested Questions: None
Additional Information: Photo source unknown
Possible Problems: None

## Slide 48
Conventional Concrete
Barrier Deployment
100 ft per flatbed
Front end loader or crane
400 ft to 600 ft. per hour
Must deploy barrier segments from one end to the other
Images: ATSSA
Notes: Key Message: Discuss concrete barrier deployment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: These may vary.
Possible Problems: None

## Slide 49
Plastic container filled with water or sand
Easier to handle
More deflection
    6-22 feet
Follow manufacturer’s instructions
TRITON (Proprietary)
2. Ballast-Filled Barriers
Yodock (Proprietary)
https://www.jtitraffic.com/our-products/temporary-barriers/triton-barrier/
https://ops.fhwa.dot.gov/publications/fhwahop17028/index.htm
Notes: Key Message: Discuss water-filled barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: These are water-filled. The main advantage is that they are lightweight and easy to move. They must be filled with water according to the manufacturer’s instructions. Depending on features, they may be protection devices OR longitudinal channelizing devices. Their features are different.
Suggested Questions: What is ballast? Are these a protection or a delineation device?
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Pictures are from documents and websites.
Possible Problems: Pictures shown are of the TRITON barrier and Yodock barriers, which are proprietary. Do not imply preference or endorsement.

## Slide 50
Where large barrier deflections are less likely
  Low speed and low impact angles
Urban projects requiring pedestrian protection and accommodation
Where space is too limited to allow heavy equipment to place concrete barriers
Where the travel lanes are narrow
Typical Applications
Notes: Key Message: Discuss the typical uses of ballast filled barrier
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory} Remember that depending on their characteristics, these may be protection or channelizing devices, or both.
Suggested Questions: What is a “large” space? [Clear Zone] What is “too limited”? Stress the importance of judgment.
Additional Information: None
Possible Problems: The last two bullets may be controversial since they may not be acceptable for those applications. Better off using a product that meets TL-3.

## Slide 51
Minimal installation and removal cost due to their light weight and easy handling
Keeps workers from inadvertently encroaching into travel lanes
    Slips and falls
Relative Costs and Benefits
Image: https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Notes: Key Message: Discuss the typical uses of ballast-filled barrier
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory
Suggested Questions: What is “Minimal”?
  Additional Information: Notice the steel bracing. This is a barrier installation. Deflection will be larger than space provided. https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Possible Problems: Try to generate discussion

## Slide 52
Worker Encroachment Prevention
Images: ATSSA
Notes: Key Message: Worker Encroachment Prevention
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The photo on the right does not provide protection. They are longitudinal channelizing devices. Notice they are not connected. If a car hits them it would kill everyone standing there. Not any different than the tubular markers on the left. Perhaps they keep workers from encroaching into the lane. Do they keep vehicles form encroaching into the work area?
Suggested Questions: Is this a false sense of security? Room for deflection?
Additional Information: None
Possible Problems: None

## Slide 53
Guardian Safety Barriers
2001M-BM
Sentry Water-Cable Barrier Wall
Triton Barrier TL-3
Let’s Discuss Them!
Water-Filled Barriers Meeting TL-3 Criteria
Notes: Key Message: Discuss water-filled barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Let’s discuss these!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 54
42” high by 72” long
Can acts as its own end treatment
TL-3: Four interlocking steel bars
280 pounds empty
1,750 pounds with water
Estimated Unit Price: $300-700
Guardian Safety Barriers
Image: ATSSA
Notes: Key Message: Discuss Guardian Safety Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
The guardian safety barrier is 42 inch high by 72 inch long water filled low-density polyethylene barrier. The barrier is both NCHRP 350 TL-2 and TL-3 approved and can act as its own end treatment. To meet TL-3 guidelines, each barrier includes four interlocking powder-coated steel bars. Empty
weight is 280 pounds and full weight is 1,750 pounds with water.
Estimated Unit Price: $700 ea. NOTE: Unit price and specifications are based on available 2011/2012 internet and company resources, the prices and specifications are
subject to change after this report has been published.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 55
32” high by 72” long
229 gallons of water or sand filled
For TL-3: two external interlocking cross-connected steel barrier rails
90 lbs empty (900 lbs full)
Estimated Unit Price: $700
2001M-BM
https://startsafety.com/yodock-2001m
Notes: Key Message: Discuss 2001M-BM Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The 2001M-BM is a 32 inch high by 72 inch long with 229 gallons of water or sand filled recycled high-molecular high-density plastic barrier. The barrier is both NCHRP 350 TL-2 and TL-3 approved and can act as its own end treatment. To meet TL-3 guidelines, each barrier includes two external interlocking
cross-connected steel barrier rails. Empty weight is 90 pounds and full weight is 900 pounds with water.
Estimated Unit Price: $700 ea.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 56
https://trinityhighway.com/product/yodock-2001m/
Notes: Key Message: Discuss 2001M-BM Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Yodock® Model 2001M water-filled barricade is a plastic, Longitudinal Channelizing Device (LCD) used for traffic and pedestrian channelization, road or street closures and perimeter fencing for vertical construction. When assembled as an (LCD), the barricades are attached end-to-end using a plastic coupler and may be deployed either empty or full. Additional accessories are available that allow the Yodock® 2001M water-filled barricade to be used for temporary sign supports, perimeter fencing, and TL-2 longitudinal barrier applications.
Estimated Unit Price: $700 ea.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 57
32” high by 72” long
242 gallons of water
For TL-3: four internal 3/8” steel cables connected to a 1 1/8” steel T-pin
200 lbs full
Estimated Unit Price: $685
Sentry Water-Cable Barrier Wall
https://www.traffixdevices.com/products/barriers/sentry
Notes: Key Message: Discuss Sentry Water-Cable Barrier Wall
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Sentry barrier wall is a 42 inch high by 72 inch long with 242 gallon water filled polyethylene barrier. The barrier is both NCHRP 350 TL-2 and TL-3 approved and can act as its own end treatment. To meet TL-3 guidelines, each barrier includes four internal 3/8 inch steel cables connected to a 1 1/8 inch steel T-pin between barriers. Full weight is 2,000 pounds with water. Estimated Unit Price: $685Estimated Unit Price: $700 ea.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 58
Sentry Water-Cable Barrier Wall
http://www.traffixdevices.com/products/barriers/sentry/
Notes: Key Message: Discuss Sentry Water-Cable Barrier Wall
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Sentry Water Cable Barrier is an NCHRP 350 TL-3 certified work zone crash barrier that can be used as an alternative to cumbersome concrete barriers in a construction work zone. The Sentry has been tested and passed all TL-2 and TL-3 light and heavy vehicle impacts at 45 and 62.5 mph (70 and 100 kph). With eleven (11) interlocking knuckles on each end multiple Sentry's can be linked together with a 1 ⅛" (30 mm) diameter galvanized hollow steel T-Pin with a steel keeper pin at the bottom of each T-Pin. Molded into each Sentry are four (4) ⅜" (9.5 mm) diameter stranded steel cables, that are galvanized for excellent corrosion resistance. The cables prevent the impacting vehicle from penetrating the barrier wall and into the work zone or on-coming traffic.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 59
32” high by 78” long
145 gallons of water
For TL-3: endoskeleton structure along with sitting on mechanically strapped pedestals
140 lbs empty (1350 lbs full
Estimated Unit Price: $680 - $720
Triton Barrier TL-3
https://www.jtitraffic.com/our-products/temporary-barriers/triton-barrier/
Notes: Key Message: Discuss Triton Barrier TL-3
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Triton barrier is a 32 inch high by 78 inch long with 145 gallon water-filled polyethylene barrier. The barrier is both NCHRP 350 TL-2 and TL-3 approved and can act as its own end treatment. To meet TL-3 guidelines, each barrier includes an endoskeleton structure along with sitting on mechanically strapped pedestals. Empty weight is 140 pounds and full weight is 1,350 pounds with water.
Estimated Unit Price: $680 - $720
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 60
Antifreeze may be needed
Where to release the water in the barrier
    Pumping may be required
Exterior shell may become brittle due to exposure to cold weather
Follow the manufacturer’s instructions
Other Considerations
Notes: Key Message: Other Considerations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: One advantage to ballast-filled barriers is the empty weight which enables workers to place, move, and tear-down the devices without specialized equipment. Although these devices are becoming more common in urban temporary work zones, a concern that must be considered
is the potential for the water to freeze in the barrier. Many online distributors recommend 12 pounds or 1.5 gallons of calcium chloride is added to each barrier if the temperature falls below freezing (plasticjersey.com 2011). Additionally, many states have implemented environmental protection policies that require water-filled barriers to be emptied and stored off-site.
Suggested Questions: Where will it flow? Will it flood an open lane? Are additional advance warning signs necessary for water over the roadway?
Additional Information: None
Possible Problems: None

## Slide 61
Usually required on bridge railings and where there is no room for deflection
Minimal deflection!
3. Anchored Barriers
Images: ATSSA
Notes: Key Message: Discuss Anchored (pinned down) barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Anchored barriers are bolted or pinned down so their deflection is close to zero. They are used where allowance (room) for that 2-foot deflection is not present, such as separating opposing flows. They may also be required on bridge railings.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Their use is a state preference. May also be called “K wall”, “K barrier” or “K rail”.

## Slide 62
Same as PCB
Where there is no room for deflection
  Bridge railings
  Separating opposing flows
Typical Applications
Image: ATSSA
Notes: Key Message: Typical uses of anchored barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Their features are the same as concrete barriers but their deflection is minimal.
Suggested Questions: Why on bridges? They vibrate so the barrier moves.
Additional Information: None
Possible Problems: None

## Slide 63
Bridge deck
Image: ATSSA
Notes: Key Message: Illustrate through an example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This shows an anchored barrier on a bridge deck.
Suggested Questions: What would happen if not anchored?
Additional Information: None
Possible Problems: None

## Slide 64
Image: ATSSA
Notes: Key Message: Illustrate through an example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This shows an anchored barrier on a bridge deck.
Suggested Questions: What would happen if not anchored? How can you tell? Slots.
Additional Information: None
Possible Problems: May not be anchored (pinned)

## Slide 65
Minimal deflection
Higher installation costs due to anchoring
    Bolted
    Staked
    Pins
    Backfilled
Relative Costs and Benefits
Image: Florida DOT
Notes: Key Message: Relative Costs and Benefits
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: Graphic is from Florida standards.
Possible Problems: None

## Slide 66
Image: Florida DOT
Notes: Key Message: Relative Costs and Benefits
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Notice the nominal deflection is 1.5 inches.
  Suggested Questions: None
Additional Information: Graphic is from Florida standards.
Possible Problems: May vary by State

## Slide 67
Mobile positive protection
Short-term/some mobile operations
Minimizes exposure for workers and motorists
Reduces set-up time
Minimizes foot print and manpower by placing tools and materials on one vehicle
Mobile Barriers (Proprietary)
4. Mobile Barriers
Image: Mobile Barriers
Notes: Key Message: Discuss mobile barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Mobile barriers are designed to provide positive protection for temporary, mobile, or maintenance work zone sites using a standard tractor-trailer configuration. The modified trailer provides a longitudinal barrier that provides a physical and visual wall between passing traffic and work crew personnel. Depending on the barrier type configuration, rear-end crash protection can be provided by attenuator cushions, and work zone lateral protection to divert errant vehicles can be performed by the rigid steel walls of the trailer. This is a vehicle that becomes a barrier. It is ideal for short duration work, providing positive protection. Advantages: Mobile positive protection, minimizes exposure, reduces set-up time, portable power/ lighting, arrow board/ VMS/ Radar, 50 minutes to swap from left to right. MBT-1 provides a physical and visual wall between passing traffic and the maintenance personnel. With integrated crash attenuation at the rear, a semi-tractor at the front, and a rigid wall on the side toward passing traffic, the Trailer provides 100’ of barrier and protected work area. The work area itself will be less cluttered and better lit.
Suggested Questions: None
Additional Information: http://www.mobilebarriers.com. The Mobile Barriers Trailer (MBT-1) is an integrated, rigid wall, trailer that can be used in conjunction with standard semi-tractors to provide mobile, improved, safety and work environments for personnel at applicable maintenance, construction and security sites. In the context of interstate construction, the Trailer is specifically designed to reduce work zone incursions by passing traffic (fore, aft and side protection), to reduce the number of collateral vehicles and equipment needed at and within the work zone, and to improve lighting and ambient conditions thus improving general conditions and alertness on site. Each of these three areas has been shown in applicable research to be significant contributors to on site fatalities and injuries.
Possible Problems: None

## Slide 68: Concrete Patching
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is the view from above. Notice the protection.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 69: Short-Term Operations
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is the view from above. Notice the protection and TMA.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 70: Short-Term Operations
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is the view from above. Notice the protection and TMA.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 71: Short-Term Operations
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is the view from above. Notice the protection and TMA.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 72
Overhead Bridge Inspection/ Repairs
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is an application for a bridge inspection project in Canada.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 73
Concrete Repairs
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Also used for concrete repair work in New Jersey.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 74
Concrete Barrier/Guardrail Repairs
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice on side with barrier no buffer taken. On side without buffer taken. Reduces congestion.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 75: Mobile Barriers
1
2
3
Modular design offers 42 ft to 102 ft of positive protection
Image: Mobile Barriers
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: It is an expandable system. The Trailer can be ordered complete with integrated power, message/arrow board, safety lighting, work lighting, storage and supply areas, and other features intended to reduce the number of collateral vehicles and equipment typically needed on site. MBT-1 is the first fully NCHRP 350/MASH tested and accepted mobile barrier available to the industry.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 76: Reduces “Rubbernecking”
https://www.impactabsorption.com/files/53750052.pdf
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Modular platforms, caboose (movable rear axle assembly) & wall sections. Configurable from 42-102’w/ 0-3 wall sections. Use one or more individually or together. Reconfigurable to the right or left. (tractor & caboose attach at either end) . Tested/FHWA Accepted under NCHRP 350 & MASH for TL-2 and TL-3 use on the National Highway System.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 77: Typical Applications
Concrete deck repairs
Guard Rail / Barrier repairs
Overhead Bridge Repairs
Loop and Junction Box repairs
Pot Holes / light bulb replacement
Crack sealing
Bridge & Pavement Inspection
Accident scene investigations / clean-up
Notes: Key Message: Typical Applications
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: This may be repetitive by now. Treat as a summary.

## Slide 78
Designed by Caltrans
Provides 30 feet of protected space
Balsi Beam
https://dot.ca.gov/programs/maintenance/work-zone-safety
Notes: Key Message: Balsi Beam
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Another example of mobile barriers is the Balsi Beam, developed by Caltrans. A working prototype was built and crash tested in 2003, using a small car and a full size pickup truck. The result of crash test were very good, for both the Balsi Beam and the impacting vehicles. Caltrans currently has a patent pending for this barrier. The protection system is essentially a semi-trailer with two telescoping beams on each side, instead of a bed that would support freight. Each of the beams can be rotated to the other side to stack on the other beam, and provide a double beam barrier on the edge of a live traffic lane. The trailer can be extended to provide a thirty-foot work space between the 3rd and 4th axles, shielded from traffic by the beams. It has its own dedicated tractor truck to transport it to the work site at normal highway speeds without the need for any permits. Once on site, the Balsi Beam can be easily set up by the driver in about 15 minutes. It can be used both in median and shoulder areas by rotating either of the beams to the other side.
Suggested Questions: None
Additional Information: Named after Mark Balsi, a Caltrans District 4 maintenance employee, who was severely injured in January 2001 when a motorist crashed into the work zone where he and others were picking up trash along I-280 in Santa Clara County. As a result of the Balsi accident, the Caltrans Division Chief of Maintenance, Larry Orcutt, ordered a research project be initiated to solve this problem.
Possible Problems: None

## Slide 79
Repositioned laterally using a transfer vehicle that travels along the barrier
Enable short-term closures to be installed and removed on long-term projects
Quickchange Movable Barrier (QMB)
Barrier Systems/Lindsay (Proprietary)
113
5. Movable Barriers
Image: https://ascelibrary.org/doi/abs/10.1061/(ASCE)0733-947X(2006)132%3A12(933)
Notes: Key Message: Discuss movable barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Movable barriers are repositioned laterally using a transfer (“zipper”) vehicle that travels along the barrier. They allow maximum use of the available capacity. Movable barrier technology allows for quick barrier adjustments to create protected work spaces or to reallocate travel lanes in the work zone to match time–of–day traffic flow fluctuations. Unlike traditional barriers, which are difficult and time consuming to reposition, movable barrier sections are interconnected and designed to be picked up and moved as a unit using a conveyer system.
Traditional concrete traffic barriers are used in many work zones to provide separation between work areas and moving traffic as well as between opposing directions of travel. They serve two purposes: 1. To create or expand protected work spaces for highway crews during off-peak traffic periods by positioning the barrier outside of the travel lane during the peak-period, then moving it into the traffic lane for the period of work activity. The barrier is then moved back off of the roadway before the start of the next peak period to allow traffic to use more or all of the travel lanes. 2. To create a median separating two opposing traffic flows where peak-period travel is higher in one direction in the morning and in the opposite direction in the afternoon. In this situation, the movable barrier positioned in the middle of the roadway can be moved to borrow a lane from the off-peak direction and allocate it to the peak direction of traffic flow. When the next peak period arrives, the process is reversed. This allows the space allocated to traffic to be used more efficiently, and allows a larger work space to be created for highway crews
Suggested Questions: None
Additional Information: http://www.barriersystemsinc.com and https://ascelibrary.org/doi/abs/10.1061/(ASCE)0733-947X(2006)132%3A12(933)
Possible Problems: None.

## Slide 80
Lifts the sections off the road and repositions the sections 4 to 18 feet laterally at speeds of 5 mph
Barrier Transfer Machine
https://www.youtube.com/watch?v=UdbDOoS2JX4
Notes: Key Message: Movable barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The machine lifts the sections off the road and repositions the sections 4 to 18 feet laterally at speeds of 5 mph
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 81
Provide a barrier-protected work space for short-term closures
Provide unbalanced flow to accommodate changes in the direction of peak-period traffic flows
113
Movable Barrier Advantages
https://www.youtube.com/watch?v=UdbDOoS2JX4
Notes: Key Message: Movable barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Typical uses are locations where lengthy sections of lanes are opened and closed on a daily or nightly basis or where the work zone is reconfigured daily.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 82
Image: Lindsay Transportation Solutions
Notes: Key Message: Moveable Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Show video}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 83
Images: Lindsay Transportation Solutions
Notes: Key Message: Movable barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Movable barriers are constructed from a series of interconnected sections of barrier hinged together with steel pins to create a movable "chain." The T-shaped top of the barrier is specially designed to allow it to be picked up and moved laterally on a conveyer system by a self-propelled barrier transfer machine (BTM). As the BTM moves along the roadway, rubber wheels run along the underside of the T-shaped top, lift the barrier several inches off of the ground, and move it through an elongated "S" shape until it is repositioned laterally in its desired location. The amount of lateral shift of the barrier can range from 4 to 18 feet. The BTM can move at speeds up to 5 miles per hour (mi/h), allowing protected work spaces to be created in a matter of minutes
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 84
39 inch long by 32 inch high by 24 inch wide concrete barrier sections weighing 1,400 pounds
Segments are connected to each other by steel pins in hinges
Movable Barrier Features
Image: https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Notes: Key Message: Moveable Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory.
Suggested Questions: None
Additional Information: https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Possible Problems: None

## Slide 85
Long-term applications
Reconfiguration: 5 mph
Minimal disruption to traffic flow
Maximizes work productivity
Both workers and motorists are protected during the barrier move
Movable Barrier Benefits
http://www.roadstothefuture.com/Zipper_I95_JRB.html
Notes: Key Message: Relative Costs and Benefits
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: http://www.roadstothefuture.com/Zipper_I95_JRB.html
Possible Problems: None

## Slide 86
Minimizing Work Zone Impacts
with Movable Concrete Barrier
Image: ATSSA
Notes: Key Message: Illustrate protection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 87
May be used in combination with fixed barriers to protect the work space
  The moveable barrier protects opposing traffic flows
Other Considerations
http://www.roadstothefuture.com/Zipper_I95_JRB.html
Notes: Key Message: Relative Costs and Benefits
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 88
Movable Barrier Deployment
100 ft per flatbed
Fork lifts
    Four people can set 400 to 600 ft/ hour
Barrier segments can be placed at either end / middle
Images: Lindsay Transportation
Notes: Key Message: Movable Barrier Deployment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: 100 ft per flatbed, Fork lifts – (4) Persons can set 400 to 600 ft/ hour, Barrier segments can be placed at either end / middle.
Suggested Questions: None
Additional Information: Refer to manufacturer’s recommendations.
Possible Problems:

## Slide 89
PCB vs. Movable Barriers
PCB
Moved or reset w/ cranes or loaders
Front end loader takes days to install 1 mile of barrier
Lane closures required to install
Moveable Barrier
Transferred or reset w/ Transfer Machine (BTM)
At 5 mph, BTM can reset 1 mile of barrier in 12 Minutes (440 ft/min)
No disruption to traffic
Images: Lindsay Transportation
Images: ATSSA
Notes: Key Message: Barrier Transfer / Reset
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is a side by side comparison between conventional barriers and moveable barriers.
Suggested Questions: None
Additional Information: None
Possible Problems: Expand as needed.

## Slide 90
Ingress/Egress
Provides fast coordinated means to address emergencies
Can be opened 3 ways:
*Pry Bar
*Pick Up w/ Pusher Wheel
*Barrier Transfer Machine
Images: Lindsay Transportation
Image: ATSSA
Notes: Key Message: Barrier Ingress/Egress
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
Can be opened fast – 3 ways
Provides fast coordinated means to address emergencies
Suggested Questions: None
Additional Information: None
Possible Problems: Expand as needed.

## Slide 91: Movable Barrier Deflection
4.4 ft deflection
Excellent post impact vehicle behavior
TL-3 (LON 3-11) 62.5 mph
¾ Ton Pick-Up (2,000K) at 25°
Image: Midwest Roadside Safety Facility
Notes: Key Message: Discuss deflection of QMB
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: {Self explanatory}. Movable end treatments are available for this system.
Suggested Questions: None
Additional Information: None
Possible Problems: Deflection may vary based on the length of the run. Deflection may be less for their restrained/stiffened system.

## Slide 92
Image: Midwest Roadside Safety Facility

## Slide 93
An alternative to portable concrete barriers for short-term work zones
6. Steel Barriers
https://www.gproadwaysolutions.com/sales/manufacturer/vulcan-barrier-portable-steel-longitudinal-barrier
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The 6th barrier type to discuss are steel barriers. Hill and Smith, Inc. has developed a durable portable steel traffic barrier, designed to protect highway travelers, as well as road and construction crews. Traditional portable barrier systems are costly, heavy to transport and handle, time-consuming and do not provide the energy-absorbing capabilities of ZoneGuard.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 94
Short-term work zones, such as short activity areas where the barrier must be placed and removed on a daily basis
Typical Applications
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Typical uses are short-term work zones, such as short activity areas where the barrier must be placed and removed on a daily basis.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 95
Developed specifically for the US market
Extensive crash testing
Steel Barriers
Image: Midwest Roadside Safety Facility
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ZoneGuard has been extensively tested to US as well as European crash test standards, and has been accepted by the FHWA as meeting NCHRP 350 and MASH-08 TL-3 and TL-4. More footage per truck means truck entries to and exits from the work zone are reduced by over 80%. Can be used either anchored only at the ends or intermittently to get acceptable deflection
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 96: Steel Barrier Deflection
Standard System (Anchored at ends only):
    5’5”
Minimum Deflection System (Anchored every 33’-4”):
    0”
System can be custom-anchored to meet different requirements
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Standard System - anchored at ends only
Minimum Deflection System – anchored every 33’-4” on both sides
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 97
Deflection in the range of 6 to 8 feet when impacted by a full-size pick-up truck
  Can be anchored down to minimize deflection
Steel Barrier Deflection
Source: https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Notes: Key Message: Deflection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Deflection in the range of 6 to 8 feet when impacted by a full-size pick-up truck but can be anchored down to minimize deflection.
Suggested Questions: None
Additional Information: https://workzonesafety-media.s3.amazonaws.com/workzonesafety/files/documents/training/fhwa_wz_grant/atssa_positive_protection_guidelines.pdf
Possible Problems: None

## Slide 98
ZoneGuard
Vulcan Barrier
ArmorGuard
Let’s Discuss Them!
Steel Barriers Manufactured In The United States

## Slide 99
ZoneGuard
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss ZoneGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The ZoneGuard steel barrier system consists of 50 foot sections that are installed without hand tools using common construction equipment. Unlike other available steel barrier systems, the ZoneGuard does not offer wheels, but does offer rubber padding. The barrier systems can be anchored at the ends, or can be anchored every 33 feet to minimize deflection. The barrier system was tested and approved according to NCHRP-350 at the TL-2 and TL-3 guidelines.
Estimated Unit Price: $0.06 - $0.21 /ft./day rental
Suggested Questions: None
Additional Information: Photo is from brochure.
Possible Problems: None

## Slide 100
ZoneGuard Deflection (Unanchored)
Image: https://hillandsmith.com/products/zoneguard/

## Slide 101
ZoneGuard Deflection (Anchored)
Image: https://hillandsmith.com/products/zoneguard/

## Slide 102: ZoneGuard Features
High performance
      TL-4
Lightweight
        < 61 lb/ft
      750 ft on a truck
Fast and easy installation
Estimated Unit Price: $0.06 - $0.21 /ft./day rental
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ZoneGuard can be easily transported to any job. Each lightweight 50’-0” section weighs just over 3000 lbs.,
enabling 750 feet to be efficiently transported on one truck. ZoneGuard can be easily and quickly placed into position and connected with standard construction equipment. Our
Speed Joint system allows for quick connections with no hand tools.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 103: Cross Section
Height: 2’-8” including 1/2 inch rubber pad
Width at base 2’-3 9/16”
Weight of standard unit: 3,004 lbs.
Standard unit length: 50’-0”
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Steel barriers can be towed behind a vehicle,
moved easily using wheels or a fork lift, and can easily be taken off the roadway if the work zone
has limited operations. The decreased weight of the steel barrier also allows for higher deflection unless the system is
anchored between the ends.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 104: 50-Foot Sections
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Light weight & ease of installation.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 105: Mountable Foot
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here you see the mountable foot which allows for drainage.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 106: Speed Joints
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here you see the speed joints used to connect segments.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 107: Anchoring Pockets
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Anchoring pockets
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 108: Rubber Pads
Increase the coefficient of friction
Add 0.5 inches for drainage
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Rubber pads.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 109: Lifting Points
Image: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Lifting points
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 110: Assembly Sequence
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Typical assembly sequence
Suggested Questions: None
Additional Information: None
Possible Problems: Workers not wearing vests.

## Slide 111: Curves & Flares
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Once the joint is locked together the run of barrier can be lifted and pulled to create a curve or flare. Standard 50’-0 sections can be curved down to xx’ radius. 16’-8 sections can be curved down to xxx’ radius
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 112
Bridge Deck Repairs
Images: https://hillandsmith.com/products/zoneguard/
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This illustrates an application in Indiana
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 113
Stackable barriers are available in 13, 26, or 40-foot sections
Moved by a forklift system or optional caster wheels
Vulcan Barriers
Image: https://s-steel.com/barriergate/
Notes: Key Message: Discuss Vulcan Barriers
Est. Presentation Time: 1-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Similar to the ArmorGuard barrier system, the Vulcan Barrier systems is a steel moveable barrier capable of providing protection for straight tangents and horizontal curves. Stackable barriers are available in 13, 26, or 40 foot sections. The barrier system is moved at the site with either a forklift system or optional caster wheels. The barrier system was tested and approved according to NCHRP-350 TL-3 guidelines.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 114
Portable steel longitudinal barrier
TL-3
Use a vertical steel pivot pin to interlink each module allowing the system to follow curves
Vulcan Barriers
https://www.trinityhighway.com/product/vulcan-barrier/
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: Other types of barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The Vulcan Barrier from Energy Absorption Systems is a portable steel longitudinal barrier that meets NCHRP 350 TL-3 test requirements as a longitudinal redirecting barrier. It is available in effective lengths of four meters, eight meters and twelve meters. Vulcan Barrier uses a vertical steel pivot pin to interlink each module allowing the system to follow curves of up to six degrees per four meter segment. The Vulcan Barrier can be deployed as a free standing system and is designed to be used with a variety of end terminal options, such as the Triton CET System or QuadGuard® CZ System. Optional casters can be installed to simplify deployment and movement. The lightweight and stackable design allows up to 160 meters to be transported on one truck, offering a huge transport savings when compared to traditional concrete barriers. The Vulcan Barrier can also be used as a simple median gate to allow traffic to be diverted for any reason.
Suggested Questions: None
Additional Information: Similar to the ArmorGuard barrier system, the Vulcan Barrier systems is a steel moveable barrier capable of providing protection for straight tangents and horizontal curves. Stackable barriers are available in 13, 26, or 40 foot sections. The barrier system is moved at the site with either a forklift system or optional caster wheels. The barrier system was tested and approved according to NCHRP-350 TL-3 guidelines.
Possible Problems: None

## Slide 115
Create a portable, crashworthy barrier that can be moved and reconfigured as staging progresses
ArmorGuard Barriers
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: Other types of barriers
Est. Presentation Time: Less than 1-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ArmorGuard Steel Barrier is a light-weight towable steel barrier system that makes setting up and tearing down a quick operation. It can also be used for links and gates between portable concrete barriers. Each 28 foot section steel barrier includes a set of wheels and can be deployed at a rate of 200 to 300 feet in 30 minutes. Wheels are lowered and raised using a compressed air or hand crank device. The barrier system was tested and approved according to NCHRP-350 TL-2 and TL-3
guidelines.
Estimated Unit Price: unknown
Suggested Questions: None
Additional Information: Performance:
The ArmorGuardTM Barrier system offers a practical solution for including positive barrier separation in short-term construction work zones and controlled access points on long-term construction projects. Armor- Guard Barrier is ideal for locations where safety and barrier portability are paramount. This freestanding barrier comes in 28 ft. (8.5 meter) sections and can be quickly interlocked to form a 200’ to 300’ portable barrier wall in about 30 minutes. ArmorGuard Steel Barrier is a light-weight towable steel barrier system that makes setting up and tearing down a quick operation. It can also be used for links and gates between portable concrete barriers. Each 28 foot section steel barrier includes a set of wheels and can be deployed at a rate of 200 to 300 feet in 30 minutes. Wheels are lowered and raised using a compressed air or hand crank device. The barrier system was tested and approved according to NCHRP-350 TL-2 and TL-3 guidelines.
• System tested to NCHRP Report 350, TL 2 (70km/h) TL 3 (100 km/h)
• Minimum lengths of 68m (Test Level 3) and 34m (Test Level 2)
• Maximum deflection < 2 m (Test Level 3) and < 1 m (Test Level 2)
• Greater than 68m can be moved longitudinally with a work vehicle.
• Two people can open or close a section in less than 5 minutes, without power.
Possible Problems: None

## Slide 116
ArmorGuard
Personal Photo
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Show photo}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 117
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Show photo}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 118
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Ability to steer and brake using guide wheels. Long arm. Short arm lowers and raises units onto wheels
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 119
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Workers pushed barrier into place in minutes
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 120
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Painting blast truck moves into position
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 121
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Show photo}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 122
Faster relocation than PCB
Lightweight, stackable
Larger deflection
Limited lateral transfer
Easy lateral movement
Steel Barriers: Benefits & Considerations
Image: https://s-steel.com/barriergate/
Notes: Key Message: Other types of barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 123
Deflection for these devices are about 6 feet when impacted by a full-size (TL-3) pick-up truck
May be anchored to minimize deflection
Open sections provide flexibility
Other Considerations
https://www.trinityhighway.com/product/vulcan-barrier/
Notes: Key Message: ArmorGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}. When anchored, the deflection is minimal. The picture shows an opening in an intermediate section for vehicle access.
Suggested Questions: None
Additional Information: None
Possible Problems: Deflection may vary based on anchoring.

## Slide 124: Barrier Summary
Type | Best-Suited | Deflection | Pros | Cons
Concrete | Long term | 2-4 feet | Low maint. Reusable | Lane closure required Access
Ballast-filled | Long term | 6-22 feet | Easy to install Urban areas | Ballast disposal
Anchored | Long term | Minimum | Little deflection | New pavement?
Mobile | Short duration | Negligible | Versatile | Cost
Movable | Long term | Small | Versatile Access | Cost
Steel | Short term | Varies by type | Versatile Access | Cost
Notes: Key Message: Barrier Summary
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: That concludes our discussion of the various barrier types. To summarized, we have prepared this table, to give you an idea (non all inclusive) of the pros and cons of the various barrier types.
Suggested Questions: None
Additional Information: None
Possible Problems: No need to teach this again. Presented as a summary.

## Slide 125: B. Truck-Mounted Attenuators
Energy-absorbing devices attached to the rear of shadow trailers or trucks
115
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Truck-mounted attenuators shall be energy-absorbing devices attached to the rear of shadow trailers or trucks. If used, the shadow vehicle with the attenuator shall be located in advance of the work area, workers, or equipment to reduce the severity of rear-end crashes from errant vehicles. TMA are useful to protect workers during moving/mobile and short term operations.
Suggested Questions: None
Additional Information: MUTCD Support:
06 Trucks or trailers are often used as shadow vehicles to protect workers or work equipment from errant vehicles. These shadow vehicles are normally equipped with flashing arrows, changeable message signs, and/ or high-intensity rotating, flashing, oscillating, or strobe lights located properly in advance of the workers and/or equipment that they are protecting. However, these shadow vehicles might themselves cause injuries to occupants of the errant vehicles if they are not equipped with truck-mounted attenuators.
Possible Problems: Their use is state-specific. May also be trailer-mounted. MUTCD term is “truck-mounted attenuator”. Explain the difference.

## Slide 126: TMAs are a 2-part system:
Truck: protects the crew or hazard from being struck!
Crash cushion: protects anyone that strikes the truck!
Image: Virginia DOT
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: Which arrow board mode is this? Caution mode.
Additional Information: Photo from Virginia DOT, which uses yellow and orange (not black) stripes.
Possible Problems: Their use is state-specific.

## Slide 127: Application of Truck-Mounted Attenuators
Shadow vehicles
Barrier vehicles
Advance warning vehicles
Images: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TMAs have various uses. They are recommended to protect workers when setting devices on the roadway. vehicles. These shadow vehicles are normally equipped with flashing arrows, changeable message signs, and/ or high-intensity rotating, flashing, oscillating, or strobe lights located properly in advance of the workers and/or equipment that they are protecting. However, these shadow vehicles might themselves cause injuries to occupants of the errant vehicles if they are not equipped with truck-mounted attenuators.
Suggested Questions: None
Additional Information:
• Up to 45 M.P.H. or 62 M.P.H. protection • Absorbs collision energy during rear-end impacts • Prevents impacting vehicles from under riding the truck • Reduces expensive equipment damage • Provides a positive barrier between motorist and work crews • Attaches easily to most vehicles (total vehicle weight must be a minimum of 16,000lbs)
Possible Problems: May be required by the state.

## Slide 128: Truck-Mounted Attenuators
Located in advance of the work area, not in the buffer space
Shall be designed for the specific application intended
  Impact speed
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Follow the manufacturer’s instructions!
Suggested Questions: None
Additional Information: None
Possible Problems: May be required by the state.

## Slide 129
Image: Virginia DOT
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TMAs save lives!
Suggested Questions: None
Additional Information: Photo is from Virginia, Dulles Toll Road.
Possible Problems: May be required by the state.

## Slide 130
Long-term, mobile, short duration, and short-term stationary work zones
Where other types of barriers may not be feasible due to:
  The time needed for installation and removal
  The length of the area being protected
For protection of isolated work crews
Typical Applications
Notes: Key Message: TMA Typical Uses
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments:
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 131
Striping
Patching
Paving
Guardrail repair
RPM installation
Crack sealing
Sweeping
Installation/removal
Mobile Operations Where TMA Should be Considered:
Image: ATSSA
Notes: Key Message: Mobile Operations Where TMA Should be Considered
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: May be too basic for an advanced audience. Expand accordingly.

## Slide 132
Source: Humphreys and Sullivan (1991)
Recommendations for the Use of TMAs in Work Zones
Notes: Common guidance on when to use a shadow vehicle and/or a truck mounted attenuator has been found for most state highway agencies. Most require a truck mounted attenuator on shadow vehicles for moving temporary work zones. However, guidance for most other applications is based on AASHTO Roadside Design Guide Table 9.3 which was originally based on research reported by Humphreys and Sullivan (1991). Humphreys and Sullivan (1991) developed preliminary guidance for shadow vehicles and truck mounted attenuators and the results of the study are summarized in this table.
Positive protection using a truck and an attenuator device is highly desirable for many for most work zone applications. However, under many conditions where construction crews are not exposed, it may be justified by an engineer or unique features of the work zone site.
Many state highway agencies have developed guidelines and protocols for the drivers of shadow vehicles in mobile work zones

## Slide 133
Undamaged TMAs can be used on multiple projects
Having a driver may add substantially to project costs
Relative Costs and Benefits
Image: Washington State DOT
Notes: Key Message: TMA Relative Costs and Benefits
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Having a driver may add substantially to project costs compared to benefits, so careful consideration should be given to whether a driver is necessary if the vehicle rarely moves. Attenuators are constantly evolving with new technologies and plastics being produced and they can cost between $15,000 and $20,000 each.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 134: Truck-Mounted Attenuators
114
If used, the TMA should be used in accordance with the manufacturer’s specifications
  Intended application
  Roll-ahead distance
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. These recommendations vary by manufacturer.
Suggested Questions: What is the roll-ahead distance? See next slide.
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 135: Positioning of TMAs
“The shadow truck should be positioned a sufficient distance in advance of the workers or equipment being protected….but not so much that the errant vehicle will travel around….”
“Roll-ahead distance”
RAD
114
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested. Comments: The shadow truck should be positioned a sufficient distance in advance of the workers or equipment being protected so that there will be sufficient distance, but not so much so that errant vehicles will travel around the shadow truck and strike the protected workers and/or equipment The position of the TMA is critical to its effectiveness. It should allow for the “Roll-Ahead Distance”. This the distance a TMA would push forward when struck. If this distance is too short, the TMS would be pushed into the workers. If it is too large, a vehicle may go around the TMA. It is specific to the TMA being used.
Suggested Questions: What would happen if a TMA is struck? What do you thing the typical TMA is? 10 feet, 200 feet? See next slide.
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 136
Source: Washington State DOT

## Slide 137: Sample Roll-Ahead Distances by Prevailing Speed (Stationary)
Source: Humphreys and Sullivan, “Guidelines for the Use of TMA’s”
*Mid-size auto = 2,250 lbs
Full-size auto = 3,500 lbs
Loaded cargo truck = 10,000 lbs
Notes: Key Message: Discuss RAD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The RAD varies between 25’ and 175’, according to this study.
Suggested Questions: Why would the RAD be more for a moving operation? It had a running start!
Additional Information: Refer to the source study for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms. Don’t spend too much time here. Just say the RAD varies from 25’ top 175’ depending on the factors discussed. Some states say 100’ as a constant for the RAD.

## Slide 138: Sample Roll-Ahead Distances by Prevailing Speed (Moving)
Source: Humphreys and Sullivan, “Guidelines for the Use of TMA’s”
*Mid-size auto = 2,250 lbs
Full-size auto = 3,500 lbs
Loaded cargo truck = 10,000 lbs
Notes: Key Message: Discuss RAD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The RAD varies between 25’ and 175’, according to this study.
Suggested Questions: Why would the RAD be more for a moving operation? It had a running start!
Additional Information: Refer to the source study for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms. Don’t spend too much time here. Just say the RAD varies from 25’ top 175’ depending on the factors discussed. Some states say 100’ as a constant for the RAD.

## Slide 139
Not in 2009 MUTCD
Section 6F-83 of 2003 MUTCD
Still permitted
C. Vehicle-Arresting Systems (VAS)
https://www.impactabsorption.com/dragnet-vehicle-arresting-barrier--vab-.html
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The last category of Positive Protection devices are vehicle-arresting systems. A relatively new type of positive protection device is vehicle arresting systems for work zones applications. This system is designed to complement such positive protection devices as portable concrete barriers to prevent vehicle penetration into activity areas such as a closed ramp, runaway truck lanes, or temporary roads where there is a chance of a head-on crash (AASHTO, 2011).
Suggested Questions: None
Additional Information: Removed because “it is not a traffic control device”
Possible Problems: None

## Slide 140
Vehicle-arresting systems are designed to prevent penetration into activity areas while providing for smooth, reasonably safe deceleration for the errant vehicles
They can consist of portable netting, cables, and energy absorbing anchors
2003 MUTCD Section 6F-83: SUPPORT:
Image: FHWA
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The 2003 MUTCD had a
brief description of an arresting system in Section 6F.83. This system is designed to deflect and/or significantly slow a vehicle to a stop with limited damage or injury to the occupants. Dragnet is the only known product at the time of the report that met NCHRP 350 TL-3 guidelines for head-on impact crashes, and approved by the FHWA. Vehicle-arresting systems are designed to prevent penetration into activity areas while providing for smooth, reasonably safe deceleration for the errant vehicles. They can consist of portable netting, cables, and energy absorbing anchors.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 141
When used, a vehicle-arresting system should be used in accordance with the manufacturer’s specifications and should be located so that vehicles are not likely to penetrate the location that the system is designed to protect
2003 MUTCD Section 6F-83: GUIDANCE
Image: FHWA
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: When used, a vehicle-arresting system should be used in accordance with the manufacturer’s specifications and should be located so that vehicles are not likely to penetrate the location that the system is designed to protect.
Suggested Questions: None
Additional Information: MUTCD shown is 2003 Edition.
Possible Problems: None

## Slide 142
To prevent access into a closed section of highway during periods when work is active
Where a section of highway is closed and reopened daily over an extended period of time
Typical Applications of VAS
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Typical uses: To prevent access into a closed section of highway during periods when work is active. Where a section of highway is closed and reopened daily over an extended period of time.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 143: Vehicle Arresting Net
Vehicle
Slowing
Initial Position of Net
Vehicle
Stopped
Energy
Absorber
Energy
Absorber
Image: ATSSA
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: It works like a rubber band to slowly stop a vehicle. The Dragnet system is a net-type attenuator. It provides a safe, controlled stop with minimum damage to the impacting vehicle, regardless of speed or vehicle size. The Dragnet system, with its ability to span any road width, is ideal for use in work zones, truck emergency run-off ramps, median openings, "T" intersections and other road closures. It provides positive protection allowing the establishment of a secure and yet forgiving perimeter.
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 146: Dragnet
Uses a “metal Bender” to absorb energy
Allows for stopping varying weights & speed
A metal tape is pulled through a series of offset pins
Few moving parts- When impacted replacing the metal tapes is normally all that is required
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The AASHTO Roadside Design Guide describes one proprietary vehicle arresting system used for work zone applications called DragnetThe Dragnet Vehicle Arresting Barrier is a simple, yet versatile, non-lethal product that was derived from The Entwistle Company's long history in the design and manufacture of aircraft arresting gear systems for shipboard installations. The system offers a practical solution for highway safety, security, and force protection applications. Dragnet has been extensively tested by independent transportation research organizations. The system has satisfied the Structural Adequacy, Occupant Risk and Vehicle Trajectory evaluation criteria per the National Cooperative Highway Research Program Report 350 (NCHRP 350), TL-3 Head-On Impact. Dragnet systems are currently designed and tested for highway safety applications such as:
Median barriers
Work zone protection
Truck escape ramps
High Occupancy Vehicle (HOV) lane closures
Railroad crossings
The Dragnet also offers a solution to the need for security and force protection by denying access to highly sensitive areas such as military bases, government buildings, or industrial facilities.
Suggested Questions: None
Additional Information: The cost of a the Dragnet vehicle arresting system ranges from a rental price of $4,000 to $5,000 with a replacement net after being stuck costing between $3,000 to $4,000. Generally, very limited research and technical information is available for vehicle arresting systems in temporary work zone settings.
Possible Problems: None.

## Slide 147: Dragnet Median Barrier and Work Zone Net System
Image: ATSSA
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Dragnet Median Barrier and Work Zone Net System is comprised of a chain link net assembly with single energy absorbers attached to each end. The energy absorbers are supported by anchors, which can be mounted into their own concrete foundation or directly to a concrete median divider. The variables involved with determining the stopping distance and "g" load response of a system are vehicle weight, vehicle speed, and net width. A 1,800 pound vehicle impacting a 30-foot wide net at a speed of 62 mph will stop in approximately 39 feet with an average deceleration of approximately 3.3 g's. A 4,500 pound vehicle impacting a 30-foot wide net at a speed of 62 mph will stop in approximately 83 feet with an average deceleration of approximately 1.6 g's.
Suggested Questions: None
Additional Information: http://www.entwistleco.com/defense/danville/medianBarrier.htm
Possible Problems: Picture not clear (Can’t see the net)

## Slide 148
Fixed end anchors may require substantial effort to install, providing minimal return for very short-term use
Temporary anchors are available for short-term applications
Relative Costs and Benefits of VAS
https://www.impactabsorption.com/files/53747097.pdf
Notes: Key Message: Relative Costs and Benefits of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Fixed end anchors may require substantial effort to install, providing minimal return for very short-term use. Temporary anchors are available for short-term applications.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 149
May require a work vehicle entrance that bypasses the arrestor net, with a watchman or police officer to prevent unauthorized entrances to work space
Past history of unauthorized or unintentional entry may warrant its use
Requires a buffer space behind the arrestor net that equates to 120 ft for a 60 mph approach speed
Other VAS Considerations
Notes: Key Message: Other Considerations for Using VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 150: Module Recap
Name the three categories of Positive Protection devices
Name 2-3 barrier selection factors
Name three types of temporary traffic barriers
Are vehicle arresting systems still permitted?
Notes: Key Message: Recap slide
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Try to gauge understanding by asking these questions and others.
Suggested Questions: Shown.
Additional Information: None
Possible Problems: None

## Slide 151: Questions