## Slide 1: 4. Other Exposure & Traffic Control Measures
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s proceed with Module 4, Other Exposure and Traffic Control Measures
Suggested Questions: None
Additional Information: None
Possible Problems: This modules may be taught quite fast depending on the level of knowledge of the participants. Avoid getting into details and present these measure as a menu of alternatives that are available.

## Slide 2: Module Objectives
Discuss “other” work zone safety management measures and strategies:
  Exposure Control Measures
  Other Traffic Control Measures
  Uniformed Law Enforcement Officers
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module. We will look at “other” safety management measures and strategies, including:
  Exposure Control Measures
  Other Traffic Control Measures
  Uniformed Law Enforcement Officers
Suggested Questions: None
Additional Information: The term ‘‘Work Zone Safety Management’’ was added as an ‘‘umbrella’’ encompassing all actions taken by an agency to ensure the protection of workers and road users in work zones, including the development of policies, procedures, and guidelines for individual projects or programs.
Possible Problems: None

## Slide 3: Why “Other” Safety Management Measures And Strategies?
Positive protection devices may not be feasible
Barriers are hazards themselves
Other alternatives that should be considered
More cost-effective
Perhaps a combination of strategies works better
Strong reference to other exposure control measures in Subpart K
Notes: Key Message: Discuss the need for “other” safety management measures and strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As we have discussed, PP is not always feasible or practical. There are several reasons for that, cost and duration, for example. Consideration of
exposure control and other traffic control measures that would avoid or minimize worker exposure to motorized traffic may decrease the overall need for positive protection devices.
Suggested Questions: Why do we need to consider “other” safety management strategies?
Additional Information: None
Possible Problems: Downplay Subpart K. Emphasize safety!

## Slide 4: A. Exposure Control Measures
Try to improve safety by
  Eliminating or reducing traffic through the work zone, or
  Diverting traffic away from the work space
Notes: Key Message: Exposure Control Measures
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments:. Exposure Control Measures should be considered where appropriate to avoid or minimize worker exposure to motorized traffic and exposure of road users to work activities, while also providing adequate consideration to the potential impacts on mobility.
Suggested Questions: How can we eliminate or reduce traffic through the work zone?
Additional Information: Source: 23 CFR 630, Subpart K-Temporary Traffic Control Devices. Photo is from Los Angeles.
Possible Problems: None

## Slide 5: “Exposure Control Measures”
Aimed not solely at preventing vehicles from entering the work space, but to reduce worker exposure!
Image: Texas DOT
Notes: Key Message: Exposure control measures
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: The term “Exposure control measures” reflects the fact that strategies were not aimed solely at preventing vehicles from entering the work space, but to reduce worker exposure through a variety of strategies.
Suggested Questions: None
Additional Information: This term was added in place of ‘‘Positive Protective Strategies’’ to reflect this fact. Photo is from a TXDOT video clip.
Possible Problems: None

## Slide 6: Worker Exposure
Image: ATSSA
Notes: Key Message: Illustrate worker exposure
Est. Presentation Time (minutes): Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: In this photo we can see that workers are expose to a roadway departure crash. The work occurs within the clear zone, so an errant driver would not have sufficient time and distance to stop before impacting a worker.
Suggested Questions: How can we minimize exposure for this type of maintenance operation? TMAs? Shadow vehicles?
Additional Information: None
Possible Problems: Try to generate discussion

## Slide 7: Exposure Control Measures
Should be considered where appropriate
Avoid or minimize exposure of:
  Workers to motorized traffic
  Users to work activities
Consider Internal Traffic Control Plans (ITCP)
Image: Texas DOT
Notes: Key Message: Discuss when to consider exposure control measures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: According to Subpart K, exposure control measures should be considered where appropriate to avoid or minimize worker exposure to motorized traffic and exposure of road users to work activities, while also providing adequate consideration to the potential impacts on mobility.
Suggested Questions: Where are they appropriate? Engineering judgment? What is adequate consideration to the potential impacts on mobility? Balancing safety and mobility!
Additional Information: Photo is a screen capture from a TXDOT video
Possible Problems: None

## Slide 8: Internal Traffic Control Plans (ITCP)
Focus on keeping workers on foot from being struck by construction equipment and large trucks within the activity area of a work zone
Guidance has been developed
Image: ATSSA
Notes: Key Message: Internal Traffic Control Plans
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Internal Traffic Control Plans focus on keeping workers on foot from being struck by construction equipment and large trucks within the activity area of a work zone. For instance, ITCP provide rules for workers to move within the work space, utilizes back-up alarms, MUTCD signs to control the movement of work vehicles, etc.
Suggested Questions: None
Additional Information: Guidance document is available at : https://www.workzonesafety.org/publication/guidance-developing-internal-traffic-control-plans-itcps-for-work-zones/
Possible Problems: None

## Slide 9: Exposure Control Measures
Full road closures
Ramp closures
Median crossovers
Full or partial detours or diversions
Protection of work zone setup and removal operations using rolling road blocks
Night work
Accelerated construction techniques
Notes: Key Message: Introduce exposure control measures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s briefly look at these seven exposure control measures.
Suggested Questions: None
Additional Information: None
Possible Problems: This is an into slide. Don’t discuss them here.

## Slide 10: 1. Full Road Closures
Temporarily closing a facility for rehabilitation or maintenance
Eliminate exposure!
Traffic is detoured
May be used for:
  An extended period of time, weekends or nights, or directional control
Image: https://ops.fhwa.dot.gov/wz/resources/publications/FullClosure/CrossCutting/FullClosureX-CuttingRpt.pdf
Notes: Key Message: Full road closures are becoming a popular work zone safety management strategy
Estimated Presentation Time: Less than 1 minute
Explanation of Cues/Builds: None
Suggested Comments: The first one is full closures. Obviously, if the road is closed, workers’ exposure to traffic is eliminated. It is the perfect positive protection! The problem is that closures are not always possible. Alternate routes may not be available, or closures may not be politically acceptable. But closures are strategy to consider and keep in mind as we look at ways to minimize exposure.
Suggested Questions: Would you consider a total closure? Any experiences with total closures in the room?
Additional Information: Full road closure: a construction work zone mitigation strategy wherein traffic operations are removed or suspended in either one or two directions on a segment of roadway or ramp. When roadway traffic is completely eliminated, construction efficiency and the resultant quality of permanent features (i.e., bridge and pavements) are maximized, while the time required for completion is minimized. When work under traffic first became necessary, it was common to close the road and complete work in the closed roadway section. However as traffic volumes increased and work under traffic became necessary on the Interstate system, closing the road was rarely used. Lane closures on high speed roadways put the workers and moving traffic very close. Working in one or two lanes at a time also slows the progress of work. Recently in an attempt to shorten the duration of work zones, agencies have closed major urban routes and done work on a full-time basis while the road was closed. Experience with full road closures has been very good and has reduced the time a road is affected by reconstruction. Total closures involve detours.
Possible Problems: None

## Slide 11: Potential Benefits of Full Closures
Reduced project duration
Increased worker productivity
Worker safety
Improved product quality
Positive public sentiment
Cost savings
Image: FHWA
Notes: Key Message: Discuss benefits of total closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The benefits of full closures are clear. It is a solution to consider as we look at the array of exposure control strategies.
Suggested Questions: What are the benefits of full closures?
Additional Information: Full road closure is an approach designed to eliminate the exposure of motorists to work zones and workers to traffic by temporarily closing a facility for rehabilitation or maintenance. During full road closure, traffic is detoured, allowing full access to roadway facilities. It is not suitable for all construction situations. In applicable situations, use of full road closure can result in positive public sentiment, increased productivity, reduced project duration, increased safety and/or a shortened risk period, and in some cases cost savings. A full closure approach may be used for an extended period of time, on weekends or nights, or directionally on a segment of roadway. Full closures help in three ways: 1) safer working conditions, 2) faster completion and 3) lower cost!
Possible Problems: None

## Slide 12: Drawbacks of Full Closures
Availability and suitability of alternate routes
Increased complaints if public outreach is weak
Slower emergency response times?
Increased delays?
Image: FHWA
Notes: Key Message: Discuss drawbacks of total closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Alternate routes need to be suited for the additional volume, including extra truck weight and widths. If public outreach is not properly done, the number of public complaints may increase. It is ESSENTIAL to the project to have a well-organized public information campaign. Also, closed roads may affect emergency response times. It is important to notify those that may be affected.
Suggested Questions: None
Additional Information: Question marks used to try to generate discussion.
Possible Problems: Discuss depending on the audience.

## Slide 13: 2. Ramp Closures
Same potential benefits as full closures
Consider the availability of alternate routes
Public information is key
Notes: Key Message: Discuss ramp closures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Ramp closures offer the same advantages of full closures. They need to be planned carefully. Public information is key.
Suggested Questions: None
Additional Information: None
Possible Problems: Similar to full closures so may keep brief.

## Slide 14: When Closing Ramps, Ask:
Which geographic areas benefit the most?
Which have the most impacts?
Who gets the most from the strategy?
Who may be negatively affected?
Ramp closures can have extreme impacts, so other strategies should be examined before this strategy is selected
Notes: Key Message: Discuss ramp closures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Ramp closures can have extreme impacts, so other strategies should be examined before this strategy is selected. The public involvement activities need to be adapted to the characteristics of the particular stakeholder community. For example, to encourage more local participation and increase attendance, community meetings with hand-delivered notices and a local venue are sometimes needed. Although the disruption may only be temporary, it still has the potential to have severe impacts for users of the ramp. Ramp closures that occur only at times of low traffic demand like night-time hours will have less impact on travelers and may have less severe impacts overall, so the outreach effort will not need to be as extensive as for closures that affect peak traffic hours. Construction impacts in work zones are also a design consideration for temporary closures.
Suggested Questions: See slide
Additional Information: http://ops.fhwa.dot.gov/publications/ramp_mgmt_handbook/manual/manual/10_1.htm
Possible Problems: None

## Slide 15: 3. Median Crossovers
Images: ATSSA
Notes: Key Message: Discuss crossovers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Crossovers involve routing the traffic from one direction onto a portion of the median and roadway of the opposing traffic. On higher speed roadways, a portable or temporary barrier is used to separate the two directions of traffic. They also eliminate exposure particularly if buffers are used.
Suggested Questions: What types of tapers are these? What is the separation between these two tapers? This is a merging taper followed by a shifting taper (bottom figure). For what length of project are these suited?
Additional Information: None
Possible Problems: Participants may not be familiar with multiple tapers. Be prepared to explain. Avoid spending too much time here.

## Slide 16: Median Crossovers
Advantages | Disadvantages
Separates construction from traffic Maintains continuous flow | Costly if barriers Temporary roadway needed Reduces shoulders Long duration May reduce capacity if lane closed
Notes: Key Message: Discuss crossovers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief. Also vehicles are in close proximity to each other. Long duration refers to the fact that this strategy in only suitable for long term projects.
Suggested Questions: None
Additional Information: By definition, long term is more than 3 days.
Possible Problems: None

## Slide 17: Median Crossovers Separate Workers From Traffic!
Image: Massachusetts DOT
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Median crossovers separate workers from traffic
Suggested Questions: None
Additional Information: Massachusetts 93 Fast Project
Possible Problems: None

## Slide 18: 4. Full or Partial Detours or Diversions
Image: ATSSA
Notes: Key Message: Discuss detours
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A detour is a temporary rerouting of road users onto an existing highway in order to avoid a TTC zone. diversion is a temporary rerouting of road users onto a temporary highway or alignment placed around the work area. Detours take users on an alternate route. Desirable when there is unused capacity on roads running parallel to the closed roadway. Full closures involve detours
Suggested Questions: What’s the difference between a detour and a diversion? What is the public acceptance of detours? Any considerations?
Additional Information: Section 6C.09 Detours and Diversions. Detour: a construction work zone mitigation strategy wherein traffic in one or both directions is rerouted onto an existing highway to avoid a construction work zone. Detoured vehicles may travel on permanent roads only or on a combination of permanent and temporary roads. This strategy compensates for the removal of permanent travel lanes from service. Generally, a detour is applicable to all approaching traffic, but some detours reroute a portion of the traffic from the affected facility and accommodate all other traffic through the work zone.
Possible Problems: None

## Slide 19: Detours
Advantages | Disadvantages
No traffic in construction area No roadside disruption Low cost Low impact Maintains number of lanes | Potential damage to detour route (trucks) Disruption to businesses and local traffic Local access Cost to motorists due to longer trips
Notes: Key Message: Discuss detours
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Detours have low impact on traffic flow, although his is not always the case. Detouring traffic imposes additional capacity and load demands on an alternative route and may result in congestion and infrastructure deterioration on the detour (i.e., alternate route). Detours should be carefully evaluated to ensure that they are capable of accommodating the volume and types (configuration, size, and weight) of detoured vehicles. Mitigation may include temporary changes to traffic control (e.g., signal timing and signs) and remedial pavement and bridge work. When detours are being considered, the access normally provided to various land uses (e.g., residents and businesses) by the closed facility should also be considered. The added length of trips using the detour is a cost to motorists and should be evaluated. Detours may cause the length and travel time of the trip to increase.
Suggested Questions: None
Additional Information: Ownership or owner agreement is usually needed to use a facility as a detour. If the agency detouring traffic from a facility does not own the roadway onto which traffic is detoured, coordination with the other agency is needed. In some jurisdictions, interagency agreements are needed and may provide for improvements to the detour route in preparation for the detour or as redress for damage induced by the detour traffic.
Possible Problems: Provide examples as needed

## Slide 20: Diversions
Advantages | Disadvantages
No detour needed Local traffic not affected | Workers may be in close proximity to traffic
Notes: Key Message: Discuss diversions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 21: 5. Rolling Road Blocks
Traffic is temporarily slowed rather than completely stopped
Traffic is paced at a safe speed
  Desirably not less than 20 mph on the Interstate
Law enforcement personnel works best
Less expensive and more convenient than building detours
Notes: Key Message: Rolling road blocks
Est. Presentation Time: 1-3 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Rolling road blocks help minimize exposure particularly during installation and removal phases of a project.
Suggested Questions: What are your experiences with rolling road blocks?
Additional Information: This method is used when roadway construction activities (e.g., placing bridge beams, overhead sign structures, etc.) are taking place in or above all lanes of the roadway, thus requiring traffic to be temporarily slowed rather than completely stopped. Traffic is paced at a safe speed (desirably not less than 20 mph on the Interstate) to provide a gap in traffic and allow the work activities to be performed. The pacing of traffic is controlled by pilot vehicles (i.e., law enforcement vehicles with blue lights flashing) driven by uniformed law enforcement personnel. Any on−ramps between the beginning point of the pacing area and the work area are blocked until the pilot vehicle has passed. Two−way radio provides constant communication to pilot vehicles, contractor's workers, flaggers stationed at on−ramps, and the project engineer. Advance signing warning motorists of the traffic pacing area is also provided. To increase safety and reduce the number of crashes caused by roadway construction activities by allowing traffic to continue moving at a reduced speed rather than coming to a complete stop. This method is much less expensive and more convenient than building detours.
Possible Problems: None

## Slide 22: Rolling Road Blocks Create Traffic Gaps so Workers are Safe!
Image: Massachusetts DOT
Notes: Key Message: Illustrate previous point with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A rolling road block provides the gaps in traffic necessary for safe installation and removal of devices. Workers are isolated from traffic so they can work not only in a safer environment but also faster and presumably at a lower cost.
Suggested Questions: None
Additional Information: Massachusetts 93 Fast Project
Possible Problems: None

## Slide 23: 6. Night Work
Takes advantage of lower volumes at night
Direct costs tend to be higher
More impaired drivers
Image: ATSSA
Notes: Key Message: Discuss Night Work
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Night work is another measure to consider.
Suggested Questions: Is night work a strategy to minimize exposure? What your experiences with night work and worker safety?
Additional Information: Night traffic volumes are generally lower than daylight volumes. Consequently, agency interest in night work as a means of reducing impacts is growing. Generally, there are no or few legal and contracting limits on an agency’s authority to specify day and time restrictions. There are many costs involved in highway construction, including those related to safety, user delay, and possible economic disruption. These direct costs tend to be higher for night construction because of additional devices, wage differential, and producer costs. Additionally, agencies and personnel experienced in administering night construction often refer to elevated risk factors (e.g., higher speeds, impaired drivers, and reduced visibility). However, a careful evaluation of potential ramifications should be conducted before selecting this alternative.
Possible Problems: Some may think (perhaps correctly) that night work is less safe for workers due to reduce visibility, higher speeds and more impaired drivers. Try to generate discussion. Safety, user delay, and economic disruption are not considered direct costs.

## Slide 24: Advantages/Disadvantages of Nighttime Work
Advantages | Disadvantages
Lower traffic volumes | Higher agency cost
Lower traffic impacts | Higher speeds; more impaired drivers
Lower impact to commercial activity | Crew social patterns disrupted
Fewer people affected | Noise and possible compromise of quality
 | Reduced worker visibility (and safety?)
Notes: Key Message: Introduce NWZ
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In addition to safety, nighttime projects must try to minimize adverse impact to the community and improve daytime mobility.
Suggested Questions: Why work at night? What are the advantages? Disadvantages? Lower volumes = higher speeds. Is that safer for workers?
Additional Information: None
Possible Problems: Try to generate discussion. Often freight is shipped and delivered at night so the commercial activity may still be impacted at night.

## Slide 25: 7. Accelerated Construction Techniques
The faster the job is completed, the less worker exposure
Consider:
  Contracting techniques to expedite the work
Images: ATSSA
Notes: Key Message: Accelerated construction techniques
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We should also consider accelerated construction techniques. The faster the job is completed, the less worker exposure. For example, using precast modules or fast-curing concrete. Also optimizing the construction sequence (Critical path method) can help cut time.
Suggested Questions: Any experiences with accelerated construction techniques? Contracting techniques?
Additional Information: None
Possible Problems: None

## Slide 26: B. Other Traffic Control Measures
Should be given appropriate consideration for use in work zones to reduce work zone crashes and risks and consequences of motorized traffic intrusion into the work space
Not mutually exclusive
Should be considered in combination as appropriate
Notes: Key Message: Other Traffic Control Measures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second group of work zone safety management measures and strategies to discuss in “other” traffic control measures. be given appropriate consideration for use in work zones to reduce work zone crashes and risks and consequences of motorized traffic intrusion into the work space. These measures are not mutually exclusive and should be considered in combination as appropriate.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 27: Other Traffic Control Measures
All strategies and temporary traffic controls other than Positive Protection Devices and Exposure Control Measures, but including uniformed law enforcement officers, used to reduce the risk of work zone crashes involving motorized traffic
Source: Subpart K
Image: ATSSA
Notes: Key Message: Discuss the need for “other” traffic control measures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Other Traffic Control Measures means all strategies and temporary traffic controls other than Positive Protection Devices and Exposure Control Measures, but including uniformed law enforcement officers, used to reduce the risk of work zone crashes involving motorized traffic.
Suggested Questions: What are “other” traffic control measures?
Additional Information: Source: Subpart K
Possible Problems: None

## Slide 28: To Which Extent?
Each of these strategies should be used to the extent that they are possible, practical, and adequate to manage work zone exposure and reduce the risks of crashes resulting in fatalities or injuries to workers and road users
Based on Engineering Judgment?
Notes: Key Message: Discuss the extent of the considerations
Est. Presentation Time (minutes): Depends on discussion
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Each of these strategies that we are about to discuss should be used to the extent that they are possible, practical, and adequate to manage work zone exposure and reduce the risks of crashes resulting in fatalities or injuries to workers and road users
Suggested Questions: How would you determine the extent?
Additional Information: Source: Subpart K
Possible Problems: Try to generate discussion

## Slide 29: Other Traffic Control Measures
Wide range:
Let’s list them!
Notes: Key Message: Other Traffic Control Measures
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These measures include a wide range of other traffic control measures such as the ones we are about to discuss. Let’s look at them.
Additional Information: None
Possible Problems: The following slides can be summarized on a list. They are not meant for detailed explanation but rather a reminder of how these measures can impact safety.

## Slide 30: 1. Effective, Credible Signing
Ineffective signing leads to driver disregard
Quality of signs is important
Implement strict inspection procedures
Images: ATSSA
Notes: Key Message: 1. Effective, Credible Signing
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Better signage generates more respect from drivers, it also eliminates uncertainty, which leads to fewer erratic maneuvers.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 31: 2. Portable Changeable Message Signs
Information must be credible and reliable
Supplemental devices
Effective when used properly
Is the message worth it?
Notes: Key Message: 2. Changeable Portable Message Signs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: PCMS can provide supplemental information to users. Consider them. Do remember that these devices are hazards themselves and require installation and removal, so workers are exposed. Ask: Is the message worth displaying? They can also help divert traffic away from the work zone.
Suggested Questions: None
Additional Information: Photo is from CA, 405 closure.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 32: 3. Arrow Boards
Required for ALL freeway lane closures
Considered a hazard when off
Proper location is critical
Image: ATSSA
Notes: Key Message: 3. Arrow Boards
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: ABs provide a visual queue that the lane is about to end. If they are not required, consider AB for all high-speed closures and shoulder work.
Suggested Questions: None
Additional Information: The 2009 MUTCD requires ABs for ALL freeway lane closures. They used to be optional. “Arrow Panels” were renamed “Arrow Boards” in the 2009 MUTCD
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 33: 4. Warning Flags and Lights on Signs
Draw attention to warning signs
Type B (high-intensity flashing) lights
Orange flags
Allowed in MUTCD
Images: ATSSA
Notes: Key Message: 4. Warning Flags and Lights on Signs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: How do flags and lights draw attention to sign?
Additional Information: These may be required in certain states (i.e., Florida)
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 34: 5. Longitudinal and Lateral Buffer Spaces
Very effective/inexpensive way to minimize worker exposure
Issues:
  Optional in MUTCD
  Shadow vehicle frequently in the buffer space
  Wrong speed is used
Image: ATSSA
Notes: Key Message: 5. Longitudinal and Lateral Buffer Spaces
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The buffer space is a lateral and/or longitudinal area that separates road user flow from the work space or an unsafe area, and might provide some recovery space for an errant vehicle. Buffer spaces separate workers from traffic. Neither work activity nor storage of equipment, vehicles, or material should occur within a buffer space. Yet they are optional in the MUTCD. You should strongly consider providing buffer spaces if you can. They protect both workers and motorists. Just because something is options doesn’t mean you don’t do it!
Suggested Questions: None
Additional Information: According to the MUTCD Section 6C.06 Activity Area, buffer spaces “may” be used. They are highly recommended though, particularly if there is room available.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 35
Source: MUTCD
Image: ATSSA
Notes: Key Message: Illustrate how buffer spaces reduce exposure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Remember that buffer spaces “buffer” or separate workers from traffic. They provide an empty space for errant vehicles to recover.
Suggested Questions: How long is the longitudinal buffer space? It is a function of stopping distance. The MUTCD has a table (two slides later). If errant vehicles can recover, does that reduce worker exposure? What is a “forgiving design”?
Additional Information: Source: MUTCD
Possible Problems: This slide emphasizes the longitudinal buffer space. There is also a lateral buffer space.

## Slide 36: Longitudinal Buffer Space
May be placed in advance of a work space
If one is used, Table 6C-2 may be used to determine the length of the longitudinal buffer space
Provide a buffer space unless you have a documented reason not to
Source: MUTCD
Notes: Key Message: Expand on the longitudinal buffer space
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: This is the MUTCD language regarding buffer space. Remember, buffer spaces should be used unless you have a documented reason not to do so.
Suggested Questions: What about a truck-mounted attenuator? Can it be in the buffer space? No, it should be in the work area.
Additional Information: None
Possible Problems: None

## Slide 37: Table 6C-2. Stopping-Sight Distance as a Function of Speed*
Speed (mph) | Buffer (ft.)
20 | 115
25 | 155
30 | 200
35 | 250
40 | 305
45 | 360
Speed (mph) | Buffer (ft.)
50 | 425
55 | 495
60 | 570
65 | 645
70 | 730
75 | 820
*May use for longitudinal buffer spaces
Source: MUTCD
Notes: Key Message: Quantify the length of the longitudinal buffer space
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are minimum distances. If warranted, longer distances may be used.
Suggested Questions: Which speed do we use to go into this table? The posted speed? You may use the posted speed as a minimum, but traffic usually travels faster. We will discuss other speeds that may be used later. How long is a buffer for 40 miles per hour? 305 feet or about the length of a football field!
Additional Information: Source: 2009 MUTCD, Table 6C-2. Stopping Sight Distance as a Function of Speed.
Possible Problems: Avoid spending too much time on this, unless there are questions. Participants should be familiar with this.

## Slide 38: Lateral Buffer Space
May be used
The width of a lateral buffer space should be determined by engineering judgment
Lateral buffer space
Source: MUTCD
Image: ATSSA
Notes: Key Message: Explain the lateral buffer space
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The buffer space is a lateral and/or longitudinal area that separates road user flow from the work space or an unsafe area, and might provide some recovery space for an errant vehicle. Buffer spaces are highly recommended. There are no tables for lateral buffer spaces.
Suggested Questions: None
Additional Information: Lateral means to the side
Possible Problems: None

## Slide 39
Lateral buffer space
Image: ATSSA
Notes: Key Message: Illustrate the lateral buffer space with a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This photo shows the space between the work space and the traffic space. This is the lateral buffer space.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 40: 6. Trained Flaggers and Spotters
Flaggers are exposed to traffic
Perhaps the most exposed worker!
Several states do not require flagger training or certification
Image: ATSSA
Notes: Key Message: 6. Trained Flaggers and Spotters
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Trained workers are safer workers! Flaggers are no exception. They have a dramatic impact on safety and motorists respect. Make sure that your flaggers are trained!
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 41: 7. Enhanced Flagger Station Setups
Improper training leads to improper setups
Illumination of flagger station is required (except in emergencies)
Large 24” paddle
Image: ATSSA
Notes: Key Message: 7. Enhanced Flagger Station Setups
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Using larger paddles, ANSI Class 2 apparel, and even a cone next to the flagger can improve his/her visibility.
Suggested Questions: How can we make the flagger more visible?
Additional Information: MUTCD requires 18” min. paddles.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 42: Safety Circles (Proprietary)
Enhance flagger’s visibility
Image: ATSSA
Notes: Key Message: Safety Circles (Proprietary)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Here is an example of a device that can help improve the flagger’s visibility. The Safety Circle is a high-visibility yellow rubberized mat that increases the visibility of flaggers and reduces fatigue and injuries from standing for extended periods on hot, hard road surfaces.
Suggested Questions: What’s wrong with this picture? Flagger in the middle of the road!
Additional Information: None
Possible Problems: None

## Slide 43: 8. Intrusion Alarms
Alarm goes off if vehicle intrudes into the protected area
Could be an air horn!
http://commons.wikimedia.org/wiki/File:Work_Zone_Intrusion_Alarm.JPG
Image: Transpo Industries
Notes: Key Message: 8. Intrusion Alarms
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Intrusion alarms are designed to protect workers from injury caused by errant vehicles that breach the work zone. Intrusion alarms detect vehicles entering the buffer zone between work crews in the work zone and vehicles driving past the work zone, and sound an alarm to warn workers in the proximate area. The warning allows workers to react to avoid the intruding vehicle. Various technologies are used to detect an intruding vehicle, including infrared, microwave, laser, pneumatic, and direct impact. These alarms also serve to alert drivers that they are breaching the work zone. The driver can respond by braking or steering out of the work zone, or both actions. A key benefit of all intrusion alarms is their rapid deployment compared to most other work zone protection systems.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 44: If They Only Knew It Was Coming!
https://slideplayer.com/slide/1677625/
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a situation that we encounter too often. I'm not here today to tell you how we can change the attitudes or mindset of these workers, but what instruments we have available to help give us a warning. Intrusion devices do not take the place of a physical barrier, but they will give the worker or inspector a number of seconds to clear the area should a vehicle enter the work zone.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 45: Transpo SonoBlaster (Proprietary)
Image: FHWA
Notes: Key Message: Transpo SonoBlaster
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: One example is the SonoBlaster. The SonoBlaster!® Work Zone Intrusion Alarm is an impact- or tilt-activated safety device that is mounted on work zone barriers such as traffic cones, drums, and delineators. When activated by direct impact of an errant vehicle, the device emits an alarm that warns roadway workers and the driver of an errant vehicle that the buffer zone has been violated.
Suggested Questions: None
Additional Information: FHWA has accepted the SonoBlaster!® as a National Cooperative Highway Research Program (NCHRP) 350/MASH Category II Safety Device, acceptable for use when attached to the base of conventional traffic cones, plastic drums, or large base road tubes or delineators. Requires No Electrical Power - Powered by safe, reliable CO2 cartridges, the SonoBlaster has an 'infinite' shelf life & won't 'go-dead' or loose power while waiting to do its job. Notifies Both Workers and Drivers - The ability of the SonoBlaster to alert both errant vehicle drivers and highway workers at the same time creates a new level of protection for preventing crashes and injuries in a wide variety of work zones. Identifies the Source of Danger - The source of the alarm sound is always the source of danger. Intrusion alarms that place audible receiver alarms in the work zone, which may be behind some workers, can direct worker's attention the wrong direction. With the SonoBlaster, the source of the alarm sound, which moves as an errant vehicle hits successive cones, moves along with the danger. The source of the SonoBlaster alarm sound pinpoints the source of danger allowing proper response by workers who find themselves in harms way. Provides Multiple Warnings - Each SonoBlaster cone struck by an errant vehicle sounds an independent 125+ dB alarm providing a continuous warning for both workers and drivers.
Possible Problems: This is not an endorsement of this product. For educational use only.

## Slide 46
Image: Transpo Industries
Notes: Key Message: Close-Up of SonoBlaster!® Work Zone Intrusion Alarm
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Cones equipped with the device are readily stackable, facilitating storage and transport to the work site. Portability, however, is compromised by the potential for misfiring.
Suggested Questions: None
Additional Information: Source: Kuta, Work Zone Intrusion Alarm Demonstration Interim Report, July 2009.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 47: Safety Line (Proprietary)
LED Alignment
https://slideplayer.com/slide/1677625/
Notes: Key Message: Safety Line Sl-d12 Lightweight
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The purpose of the Safety Line™ is to give workers the earliest possible warning that a vehicle has entered a "safety zone" such as a taper, that is closed off by cones, drums, or other channelizing devices (TCD). It works similar to a garage door. The Safety Line™ consists of a Transmitter and Receiver. The Transmitter is placed at the start of a taper just inside of the channelizing devices. The receiver can be placed up to 1000 feet away, closest to the workers. The transmitter projects a dual Inferred beam to the receiver. Should a vehicle intrudes into the buffer area, the dual transmitted beams would be obstructed thus causing the receiver to activate the 147 db air horn, alerting the workers.
Suggested Questions: None
Additional Information: The Safety Line™ is extremely easy to use. It is rugged, lightweight, portable and completely self contained. It can be aligned in less than a minute using the alignment LED’s. Here’s a close-up of the transmitter and receiver. The transmitter has the solar charger option and the receiver has the solar charger and strobe light option. Switches are recessed to prevent accidental activation. Battery access doors are at the bottom with a detailed set of instructions on the inside.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 48: 9. Rumble Strips
Alert road users that they are leaving the travel lanes
Two types
  Longitudinal
  Transverse
http://mutcd.fhwa.dot.gov/htm/2009/images/fig3j_01.gif
Image: ATSSA
Notes: Key Message: 9. Rumble Strips
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Rumble strips can alert road users that they are leaving the travel lanes. They are particularly useful to alert distracted or impaired drivers. They alert drivers to unusual vehicular traffic conditions. Through noise and vibration they attract the driver’s attention to such features as unexpected changes in alignment and to conditions requiring a stop. They could be longitudinal or transverse
Suggested Questions: None
Additional Information: Section 6F.87 Rumble Strips. Rumble Strip—a series of intermittent, narrow, transverse areas of rough-textured, slightly raised, or depressed road surface that extend across the travel lane to alert road users to unusual traffic conditions or are located along the shoulder, along the roadway center line, or within islands formed by pavement markings to alert road users that they are leaving the travel lanes.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 49: Portable Rumble Strips
Image: FHWA
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are portable rumble strips:
•Enhance work zone awareness through audible and “Feel”
•Mobile yet stable
•Road form fitting yet not intrusive
•Durable; withstanding traffic impacts and weathering elements
•Quick, manual installation and removal
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 50: 10. Pace or Pilot Vehicles
Used to guide a queue of vehicles through the TTC zone or detour
Name of the contractor or contracting authority prominently displayed
The PILOT CAR FOLLOW ME (G20-4) sign shall be mounted on the rear of the pilot vehicle
Image: ATSSA
Notes: Key Message: 10. Pace or Pilot Vehicles
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These vehicles are used to guide a queue of vehicles through a complex TTC zone or detour.
Suggested Questions: None
Additional Information: Section 6C.13 Pilot Car Method of One-Lane, Two-Way Traffic Control
Possible Problems: These may not be very common in some states. Keep brief!

## Slide 51: 11. Quality Pavement Markings
Particularly for nighttime lane closures
Long-term projects
Obliterate conflicting markings
Notes: Key Message: 11. Quality Pavement Markings
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Quality pavement markings can help provide positive guidance to motorists.
Suggested Questions: None
Additional Information: Lack of pavement markings is commonly cited in work zone litigation cases.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 52: 12. Channelizing Device Spacing Reduction
1X and 2X the posted speed in feet may not be adequate
A denser pattern is more restrictive and may create the impression of danger
Image: ATSSA
Notes: Key Message: 12. Channelizing Device Spacing Reduction
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Remember the MUTCD requires a MAX spacing, in feet, equal to the posted speed for tapers and 2 times on tangents. This large spacing may be too much (not restrictive enough) for certain conditions. This not THE spacing but rather a MAX. Consider reducing the spacing to create a denser, more restrictive pattern.
Suggested Questions: None
Additional Information: MUTCD: The maximum distance in feet between devices in a taper should not exceed 1.0 times the speed limit in mph.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 53
Image: ATSSA
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice how this dense pattern gives a visual cue that the lane is closed. It also guarantees that a device would get hit, alerting both the intruder and the workers (perhaps).
Suggested Questions: None
Additional Information: Photo is from Louisiana. Source: Tom Ervin
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 54
Image: ATSSA
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice how this relaxed spacing on this tangent may give the impression that the lane has been reopened. The prohibition symbol refers to the fact that these devices on a tangent are too far apart. The MUTCD allows a maximum device spacing on a tangent to be twice the posted speed in feet. Assuming these skip lines follow a 10-30 pattern, these devices appear to be too far apart. Reducing the device spacing would give the impression to drivers that there is little danger and may leave workers more exposed.
Suggested Questions: None
Additional Information: Photo is from Louisiana. Source; Tom Ervin
Possible Problems: None

## Slide 55: 13. Longitudinal Channelizing Devices
Not protection devices!
Provide detectable edging for visually disabled pedestrians as per American with Disabilities Act (ADA)
Previously discussed
Notes: Key Message: 13. Longitudinal Channelizing Barricades
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click.
Suggested Comments: Longitudinal channelizing devices are lightweight, deformable devices that are highly visible, have good target value, and can be connected together. Longitudinal channelizing devices have not met the crashworthy requirements for temporary traffic barriers and should not be used to shield obstacles or provide positive protection for pedestrians or workers. These devices may be problematic since some assume that they are protection devices. THEY ARE NOT! They are channelizing devices, which may be used to channelize pedestrians (in compliance with the American with Disabilities Act (ADA); continuous edging) but not for positive protection. They also have significant deflection.
Suggested Questions: None
Additional Information: Some manufacturers provide stiffener members which allow these devices to provide some protection. Check with the manufacturer. MUTCD: longitudinal channelizing devices may be used to discourage pedestrians from unauthorized movements into the work space. Section 6F.71 Longitudinal Channelizing Devices: If used for pedestrian traffic control, longitudinal channelizing devices shall be interlocked to delineate or channelize flow. The interlocking devices shall not have gaps that allow pedestrians to stray from the channelizing path.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly. Discussed previously.

## Slide 56: 14. Work Zone Speed Management
Consider changes to the regulatory speed limit (if warranted) and/or variable speed limits
Regulatory not advisory speeds
Requires authorization
Radar speed display trailer
Images: ATSSA
Notes: Key Message: 14. Work Zone Speed Management
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Managing regulatory speeds is another way to reduce exposure. It is easier to control a vehicle and recover at lower speeds. Changing the posted speed requires permission and usually a speed study. Check with your jurisdiction.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 57: Enforce Work Zones Like School Zones!
Image: ATSSA
Notes: Key Message: 14. Work Zone Speed Management
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: WZ speed limits should be enforced like at schools zones. Here, a VMS is being used to reinforce the point.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 58: 15. Law Enforcement Officers
Functions:
  Presence
  Enforcement
  Traffic control
Do not assume officers are trained
Officers are also “workers”
Images: Virginia DOT
Notes: Key Message: 15. Law Enforcement Officers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The use of traffic law enforcement at a highway work zone is recognized as one of the most effective means available for reducing speeding, speed variability, and undesirable driving behaviors such as tailgating and unsafe lane changes, thereby improving traffic and worker safety in the work zone. The presence of work zone enforcement is also believed to raise driver awareness and level of alertness, reducing perception-reaction times in response to unexpected hazards encountered. Specific reasons should exist for providing enforcement at a work zone. Enforcement costs are not insignificant, and represent an additional burden on enforcement agency manpower and equipment resources in a region, even when highway agency funds are being used to pay for such efforts. If enforcement is to be used, it should be to address specific hazards, and the strategy used should be capable of minimizing those hazards. IT IS NOT A MAGIC SOLUTION!
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid discussion too much here. This topic will be presented in more detail later.

## Slide 59: 16. Automated Speed Enforcement
Where permitted by State/local laws
  Cameras
  Detectors
  Others
Image: ATSSA
Notes: Key Message: 16. Automated Speed Enforcement
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Automated Speed Enforcement (ASE) systems can be an effective tool for managing speed and reducing speed related crashes when used correctly and in the appropriate circumstances. Through an ASE program involving public education and visible enforcement, agencies seeks to change behavior and urge drivers to do what they already should be doing: driving responsibly, staying alert, and obeying the posted speed limit. ASE is a supplement to, not a replacement for, traditional enforcement operations .
Suggested Questions: None
Additional Information: An automated speed enforcement (ASE) system is an enforcement technique with one or more motor vehicle sensors producing recorded images of motor vehicles traveling at speeds above a defined threshold. Images captured by the ASE system are processed and reviewed in an office environment and violation notices are mailed to the registered owner of the identified vehicle. Often, these systems are referred to as speed cameras. The ASE system measures the speed of each passing vehicle. A series of photographs and video will be recorded to document vehicles traveling at or above a determined speed threshold. The date, time, and location of the violation, as well as the speed and license plate of the violator’s vehicle will be recorded. Following the proper identification of the registered owner of the vehicle, using the license plate number, the registered owner will be mailed a citation, which will include the violation photos and the vehicle speed. Bottom photo is from Washington DC.
Possible Problems: Laws may vary by state.

## Slide 60: 17. Drone Radar
Emits radio signals that activate radar detectors used by the general public
Vehicles equipped with radar detectors perceive the transmitted radar signals from the drone as the presence of police enforcement in the area
Image: ATSSA
Notes: Key Message: 17. Drone Radar
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Drone radar can be used to alleviate some of the speeding problems in work zones. Radar drones are intended to slow those vehicles equipped with radar detectors (it is assumed that drivers with radar detectors typically drive faster than the mean). Drone radar is very effective in reducing the number of vehicles traveling at excessive speeds (i.e., 10 mph or more over the speed limit). The proportion of excessive speeders is reduced by 6 to 33 percent. DISADVANTAGES: Radar transmissions do not present a speed reducing stimulus to each driver approaching a work zone. Drone radar only targets motorists with radar detectors. Traffic speeds are reduced near the location of the drone radar, but about one mile after exposure the traffic speeds return to normal. Drone radar alone does not reduce traffic speeds to the desired level.
Suggested Questions: None
Additional Information: Drone Radar units range in price from $400.00 to $600.00.
Possible Problems: None

## Slide 61: 18. Worker and Work Vehicle/ Equipment Visibility
ANSI 107 Class 2 required
ANSI 107 Class 3 recommended at night
Proper illumination
Conspicuity tape on vehicles
Notes: Key Message: 18. Worker and Work Vehicle/Equipment Visibility
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Obviously, the more visible workers and equipment are, the less the chances of getting hit. Visibility is key. Make sure workers were ANSI 107 Class 2 apparel and mark vehicles and devices such as ABs with conspicuity tape (red and white). Also, proper illumination will help make things more visible.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 62: 19. Worker Training
Critical to worker safety
Encourage certification in your State
Lack of training remains problem
Protects from litigation
Image: Virginia DOT
Notes: Key Message: 19. Worker Training
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Worker training is critical. The more workers know about standards, guidelines and their options the safer they will be. Encourage workers to be certified.
Suggested Questions: None
Additional Information: Photo is from i_495 in Virginia.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 63
Image: Virginia DOT
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Was this worker trained is safe installation and removal practices?
Additional Information: Photo is from I-495 in Virginia
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 64: 20. Public Information and Traveler Information
Commuter alternatives
  Alternate routes
  Alternate modes
Provision of information on changing conditions on the project during implementation
Lower demand
Notes: Key Message: 20. Public Information and Traveler Information
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The more information highway users have, the better. They can forgo the trip, go on different hours or choose an alternate route. There are several ways to provide this information. Remember that significant projects have to have a TMP with a public information component. Real-time information is best. Even PCMS can be used for this purpose.
Suggested Questions: None
Additional Information: MUTCD: Portable changeable message signs have a wide variety of applications in TTC zones including: roadway, lane, or ramp closures; incident management; width restriction information; speed control or reductions; advisories on work scheduling; road user management and diversion; warning of adverse conditions or special events; and other operational control.
Possible Problems: Participants may not be aware of TMPs and their requirements. Be prepared to explain.

## Slide 65: Examples
Source: FHWA, Full Road Closure for Work Zone Operations
Notes: Key Message: Example of PI
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here are two examples of outreach. Think outside the box. How can we get information to our users? Limited capacity closure projects require a significant amount of public information and outreach. Media outlets were used to disseminate details on the project, and information about alternate routes was available. As part of the Fix Detroit 6 program the I-75 project details were provided in a flyer included in the Detroit Free PressSunday paper. The flyer related information on six projects. More than 850,000 Fix Detroit 6 flyers were included in the paper at a cost of over $80,000.
Suggested Questions: How can we get information to our users?
Additional Information: Source: FHWA, Full Road Closure for Work Zone Operations
Possible Problems: None

## Slide 66: Carmaggedon Not!
Image: Caltrans
Notes: Key Message: Illustrate previous point through an example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: On July 2011, the 405 in LA was completely shut down in both directions between the 101 and 10 freeways -- an insanely busy 10-mile stretch -- beginning the night of Friday, July 15 and ending 5 a.m. the following Monday morning. The PI and scare tactic was so successful that the construction took place without a hitch. They called it Carmaggedon! Drivers stayed home and there were no significant traffic issues.
Suggested Questions: None
Additional Information: None
Possible Problems: This message may not satisfy the message content criteria of the CA MUTCD. Treat as a question if needed.

## Slide 67
https://www.cbsnews.com/news/carmaggedon-las-405-becomes-ghost-freeway/
Notes: Key Message: Illustrate previous point through an example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is an example of the public information campaign that took place.
Suggested Questions: None
Additional Information: https://www.cbsnews.com/news/carmaggedon-las-405-becomes-ghost-freeway/
Possible Problems: None

## Slide 68: 21. Temporary Traffic Signals
Eliminate the need for flaggers: No exposure!
Automated Flagger Assistance Devices (AFAD)
Image: ATSSA
Notes: Key Message: 21. Temporary Traffic Signals
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Temporary traffic signals and AFAD keep workers out of the way. They also eliminate worker exposure.
Suggested Questions: None
Additional Information: Photo on right is from Hawaii.
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 69
Notes: Key Message: AFAD video
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at a quick video of a PCMS
Suggested Questions: None
Additional Information: None
Possible Problems: Proprietary Device

## Slide 70
No flagger = No exposure!
Image: ATSSA
Notes: Key Message: Illustrate previous point through a photo
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid spending time on this topic unless questions are asked. Treat as a quick list and keep moving accordingly.

## Slide 71: C. Uniformed Law Enforcement Officers
Can:
  Affect driver behavior, helping to maintain appropriate speeds and
  Improve driver alertness
May provide:
    Presence
    Enforcement
They also need to be trained and protected!
Image: ATSSA
Notes: Key Message: C. Uniformed Law Enforcement Officers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The third group of strategies involves uniformed law enforcement officers. They may provide presence, to help deter speeding, and/or enforcement. They can be very effective but these officers should be trained themselves to be effective.
Suggested Questions: None
Additional Information: MUTCD: Consideration should be given to stationing uniformed law enforcement officers and lighted patrol cars at night work locations where there is a concern that high speeds or impaired drivers might result in undue risks for workers or other drivers.
Possible Problems: None

## Slide 72: Law Enforcement Officers
Greatest benefits:
  Projects with high traffic speeds and volumes
  Work zones expected to result in substantial disruption to or changes in normal traffic flow patterns
Image: ATSSA
Notes: Key Message: Law enforcement officers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The use of police enforcement in work zones is a common practice among state DOTs. Some states use off-duty state police officers who volunteer for assignment in work zones, for monetary gain. In some states, they are a pay item, in others, they are paid by the state. They may perform the functions of presence, to deter speeding, and enforcement. They should be on the shoulder within the advance warning area and never blocking a lane.
Suggested Questions: None
Additional Information: None
Possible Problems: Previously discussed. Keep brief.

## Slide 73: Consider When:
Worker presence adjacent to high-speed traffic
Risky installation and removal
Complex or very short term changes may create confusion
Image: ATSSA
Notes: Key Message: Discuss when to consider law enforcement officers in work zones
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Their criteria for use is either ADT and/or nighttime work. Other considerations are listed on the screen. Engineering judgment is needed.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss as needed

## Slide 74: Consider When (Cont.):
Night work
High crash locations
High volumes
Operations require brief stoppage of all traffic in one or both directions
Rolling road blocks
Image: Massachusetts DOT
Notes: Key Message: Discuss when to consider law enforcement officers in work zones
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Additional considerations are listed on the screen.
Suggested Questions: None
Additional Information: Photo is from MassDOT video clip.
Possible Problems: Discuss as needed

## Slide 75: Consider When (Cont.):
Queuing is anticipated on high-speed roadways
Traffic presents a high risk for workers and road users
Image: FHWA
Notes: Key Message: Discuss when to consider law enforcement officers in work zones
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Additional considerations are listed on the screen.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss as needed

## Slide 76: Law Enforcement Officers are not Immune to Crashes!
Nor are they a substitute for proper temporary traffic control and positive protection
The trooper’s vehicle should not be used to block a lane: It is not a TMA!
Image: Virginia DOT
Notes: Key Message: Discuss potential patrol vehicle position during stationary work zones.
Est. Presentation Time: Less than 1 minute
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Law enforcement officers are not immune to crashes, nor are they a substitute for proper temporary traffic control and positive protection. They are vulnerable human beings. Don’t use a patrol vehicle to block a lane! That is not their function. They are not a TMA!
Suggested Questions: None
Additional Information: Photo is from Virginia, by D. Rush.
Possible Problems: None

## Slide 77: Position of the trooper’s vehicle should be addressed in the TTC Plan!
Image: ATSSA
Notes: Key Message: Discuss patrol vehicle positioning
Est. Presentation Time: Based on discussion
Explanation of Cues/Builds: None
Suggested Comments: Let’s open the floor for discussion. Based on what you have learned so far, where would you position your patrol vehicle if working on a lane closure?
Suggested Questions: Should it be in the buffer space? In the taper? In the termination area? Where can you be safe and at the same time effective? (Answers on next slide)
Additional Information: None
Possible Problems: Little discussion may be possible. Other publications developed under the grant refer position and orientation to local preference or policy. The FHWA had not previously seen data sufficient to recommend facing 1 direction over another.

## Slide 78
BEFORE the transition
  NOT IN BUFFER
On the SHOULDER or MEDIAN
Between the 2nd & 3rd sign
  Where we need the motorists to pay most attention to what they need to do ahead.
Consider facing traffic
Headlights OFF, emergency lights ON
TROOPER SHOULD BE HERE!
Image: ATSSA
Notes: Key Message: Suggest patrol vehicle positioning.
Est. Presentation Time: 3-4 minutes
Explanation of Cues/Builds: Bullets appear on subsequent clicks.
Suggested Comments: This is what we recommend. Remember each case is different and that judgment is involved. Use common sense! We recommend what’s on the slide: FACING TRAFFIC before the 2nd and 3rd sign. This is when motorists are about to make their maneuvers.
Suggested Questions: Why facing traffic? Advantages? Disadvantage? See following slide.
Additional Information: There is little information on this. This is what one state (Louisiana) is doing. This is not required by the MUTCD or any standard that we are aware of.
Possible Problems: This may be controversial. Be prepared to defend your suggestion. Do not argue. This is a suggestion only.

## Slide 79: Reasons for Ineffective Use of Law Enforcement Officers in Work Zones
Officer leaves the work zone for enforcement and is not visible
Traffic is very heavy
Officer is parked within the work zone and not back with the end of the queue
Officer does not issue any citations
Not enough officers
Officer is not positioned in the correct location
Notes: Key Message: Discuss patrol vehicle positioning
Est. Presentation Time: Based on discussion
Explanation of Cues/Builds: None
Suggested Comments: Several conditions causing police use to be ineffective include:
• Officer leaves the work zone for enforcement and is not visible.
• Traffic is very heavy.
• Officer is parked within the work zone and not back with the end of the queue.
• Officer does not issue any citations.
• There are not enough officers; at least two are needed for most work zones.
• Officer is not positioned in the correct location.
Suggested Questions: What leads to this? Untrained officers or officers not attending the preconstruction conference.
Additional Information: None
Possible Problems: Little discussion may be possible

## Slide 80: Module Recap
When should “other” safety management measures and strategies be considered?
Name three “other” exposure control measures
Name the advantages and disadvantages of nighttime work
Name some considerations of using law enforcement officers in work zones
Notes: Key Message: Recap slide
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Try to gauge understanding by asking these questions and others.
Suggested Questions: Shown
Additional Information: None
Possible Problems: None

## Slide 81: Questions