## Slide 1: 5. Making Decisions
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Open module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s move on now to Module 5, Making Decisions.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Discuss the basis for available decision and assessment tools
Discuss some existing assessment processes
  Including this State’s
Apply a positive protection assessment (decision-making) process
Discuss/Apply an interactive Excel-based Positive Protection assessment tool
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module. We will look at the basis for available decision and assessment tools, discuss existing processes from two states and introduce an interactive Excel-based tool to help you with this process.
Suggested Questions: None
Additional Information: None
Possible Problems: No need to read the objectives. Paraphrase them in general terms and move on.

## Slide 3: Remember the basis for available PP decision and assessment tools?
  From 23 CFR Part 630 Subpart K:
      The use of positive protection shall be based on an engineering study
      Encourages states to consider techniques intended to reduce the likelihood of vehicle intrusions
Image: ATSSA
Notes: Key Message: Tie this module to the requirements of Subpart K
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s review the basis for available Positive Protection decision and assessment tools. As we discussed, it emanates from Subpart K and the requirement to assess the need for Positive Protection based on an engineering study and a methodical process. In this module we will look at some of these processes. Remember that this subpart is applicable to all Federal-aid highway projects, and its application is encouraged on other highway projects as well.
Suggested Questions: Remember the basis for available Positive Protection decision and assessment tools? Remember the requirement for an engineering study?
Additional Information: The Rule provided guidance on what factors to consider as part of an engineering study. At a minimum, the rule states that positive protection shall be considered where work zone conditions place workers at increased risk from motorized traffic (e.g., tunnels and bridges that limit worker escape routes, long duration projects on high-speed facilities that place workers in close proximity to motorized traffic, etc.) and where positive protection devices can significantly improve safety (such as to protect a pavement edge drop-off that will be in place overnight or longer). However, the rule does not provide specific requirements or thresholds on positive protection usage. Rather, states are responsible for developing general policies or project-specific decision frameworks for determining situations, locations and types of positive protection to use (e.g., traditional portable concrete barrier or some of the newer barrier technologies). FHWA also encourages states to consider techniques intended to reduce the likelihood that a vehicle intrusion into the work zone will occur at all.
Possible Problems: This was discussed in the introduction module. You are not teaching this again, just giving them a reminder.

## Slide 4: Questions to Ponder…
How are the states addressing Subpart K requirements?
Which processes/tools are available to assess positive protection devices?
How are states defining an “engineering study”?
Notes: Key Message: Generate discussion
Est. Presentation Time: May vary depending on participation
Explanation of Cues/Builds:
Suggested Comments: The main emphasis of Subpart K is to encourage and require certain process considerations to increase the safety of work zones for workers and motorists alike. For example, states are required to consider positive protection measures, including the use of barriers and other exposure control methods, where workers are at greater risk from traffic and where these measures offer the highest potential for increased safety. Let’s ponder a few questions: How are the states addressing Subpart K requirements? Which processes/tools are available to assess positive protection devices? What constitutes an “engineering study”? The next few slides answer these questions and indicate .
Suggested Questions: What is your State doing? Are you aware of any procedures in place?
Additional Information: None
Possible Problems: Try to generate discussion. If no one participates, have some pre-prepared answers.

## Slide 5: Positive Protection Guidelines: What are the States Doing?
Several have formulated policies/ guidelines similar to the requirements stated in the federal regulations, almost verbatim
Judgment call as to whether the safety risks outweigh the additional costs/issues of requiring barriers
Images: ATSSA
Notes: Key Message: Discuss how several states are addressing the Subpart K requirement
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds:
Suggested Comments: A review of state DOT policies and guidelines pertaining to positive protection use in work zones finds that many are formulated very similarly to the requirements stated in the federal regulations. The policy often indicates that positive barrier will be “considered” for a variety of situations and then lists the same factors found in the subpart K requirements almost verbatim. It should be noted that many states include some guidance pertaining to the protection of large (greater than 2”) drop-offs near the travel lanes. However, positive protection guidelines beyond that particular condition are fairly limited. Not just cost alone. There are also risks associated with placing and removing the barriers. Other measures may be options as well.
Suggested Questions: What is you state doing? Do you know? What is a judgment call?
Additional Information: None
Possible Problems: None

## Slide 6: Positive Protection Guidelines: What are the States Doing?
Several require barriers to protect drop-off conditions or fixed hazards
  Positive Protection guidelines beyond that particular condition are fairly limited
Image: ATSSA
Notes: Key Message: Discuss how several states are addressing the Subpart K requirement
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As we said earlier, several states require barriers to protect drop-off conditions or fixed hazards Positive Protection guidelines beyond that particular condition are fairly limited. Engineering analysis of the need for Positive Protection should consider the disruption to traffic, and potential crashes, caused by deploying temporary barriers. For a longer term project this should be only a minor consideration, but it could sway the decision in a project of medium duration. Let’s look at some examples:
Suggested Questions: Who remembers the definition of a drop-off? It varies by State but in general terms, it is a sudden (4:1 or steeper) drop in vertical elevation parallel to traffic, usually 2.5 inches or deeper.
Additional Information: 2011 Roadside Design Guide. The specifics may vary by State.
Possible Problems: None

## Slide 7: Work Zone Positive Protection Guidelines
TTI Report 0-6163-1
Project Title: Improved Positive Protection Guidance for Work Zones
http://d2dtl5nnlpfr0r.cloudfront.net/tti.tamu.edu/documents/0-6163-1.pdf
Notes: Key Message: Introduce TTI Report on WZ Positive Protection Guidelines
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There is an excellent report developed by TTI in 2011. Some of the information in this module was obtained from this report. We encourage you to review this report. The goal of TTI’s project was to develop implementation guidance that the Texas Department of Transportation (TxDOT) can use to make better decisions regarding when and where to use positive protection in work zones, and when to consider exposure control and other traffic control measures that could improve work zone safety. The specific objectives of the project were:
• Analyze the benefits and costs of using portable concrete barrier for positive protection in work zones.
• Analyze the benefits and costs associated with the use of moveable and portable barrier technologies that can be more quickly deployed and removed at work sites than traditional PCB.
• Analyze the benefits and costs of non-positive protection devices that can be used to improve safety and reduce work zone intrusion events in work zones.
• Develop implementation guidelines for these various technologies.
Suggested Questions: None
Additional Information: TTI = Texas Transportation Institute. Report available here: http://tti.tamu.edu/documents/0-6163-1.pdf
Possible Problems: None

## Slide 8
Notes: Key Message: Summarize the typical criteria for Positive Protection consideration
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This table gives you an idea of the typical criteria for Positive Protection consideration used by several states. As shown in the list, the most common reasons or factors cited for using positive protection were the presence of a pavement or edge drop-off that met or exceeded the current drop-off depth and lateral proximity criteria. Also, the combination of high speeds and high traffic volumes makes it easier for work zone designers to justify in their minds the use of positive protection.
Suggested Questions: None
Additional Information: Source: WORK ZONE POSITIVE PROTECTION GUIDELINES, FHWA/TX-11/0-6163-1, May 2011. http://d2dtl5nnlpfr0r.cloudfront.net/tti.tamu.edu/documents/0-6163-1.pdf
Possible Problems: Table may not be legible based on lighting conditions. Be prepared to summarize it. There is no need to go State by State, you are just showing that most states mostly consider the presence of a drop-off as a decision-making criteria. Also, do not criticize states. This a common acceptable practice. The point to make is that drop-offs are not the ONLY criteria.

## Slide 9: Is This a Problem?
Some states apply a drop-off or fixed hazard criteria without considering other factors such as worker exposure!
Much is left to the designer’s engineering judgment!
Limited assessment processes
Notes: Key Message: Illustrate the existing problem (perhaps)
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Some states apply a drop-off or fixed hazard criteria without considering other factors such as worker exposure. These criteria leave a lot of room for engineering judgment, resulting in lack of uniformity nation wide. The drop-off in itself is not a problem. Drop-offs are a hazard for motorists, so treatment for that condition does not need consideration of worker exposure. A given device may protect motorists but not workers. We need to protect both!
Suggested Questions: Is this a really a problem? If so, Why? What happens if all we use to assess the need for Positive Protection is the presence of a drop-off condition? Who should we be protecting: the motorists? Or the workers? BOTH!
Additional Information: None
Possible Problems: Notice the question mark on the title. This is meant to generate discussion. You are not saying that this is a problem. You are asking.

## Slide 10: States Surveyed: Positive Protection Requirements Based on:
Chart: 
| Duration | Small separation bet. Opposing Traffic | Exposed Structures (Hazard) | Close Horizontal Offset to Hazard | Traffic Speed | Workers/Motorist Safety | Presence/Height of Drop-off
 | 4 | 6 | 15 | 17 | 17 | 19 | 40
http://d2dtl5nnlpfr0r.cloudfront.net/tti.tamu.edu/documents/0-6163-1.pdf
Notes: Key Message: Discuss other factors considered
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In addition to drop-offs, a survey (from this source) found the breakdown of factors considered was:
• Pavement edge drop-off presence and height (40 percent).
• Worker and motorist safety (19 percent).
• Close horizontal offsets to hazards (e.g., work area or edge drop-off) (17 percent).
• High traffic speed (17 percent of projects).
• Exposed structures (e.g., bridge abutments) (15 percent).
• Small separation between traffic in opposing directions (6 percent).
• Project duration (4 percent).
Suggested Questions: None
Additional Information: Source: WORK ZONE POSITIVE PROTECTION GUIDELINES, FHWA/TX-11/0-6163-1, May 2011. http://d2dtl5nnlpfr0r.cloudfront.net/tti.tamu.edu/documents/0-6163-1.pdf
Possible Problems: None

## Slide 11: Several States have developed Positive Protection Assessment Processes, including:
Colorado
Maryland
Michigan
New York
North Carolina
Oregon
Texas
Virginia
Utah
Others
Notes: Key Message: Present a partial list of states with Positive Protection assessment processes in place
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: During the development of this course, we conducted an informal survey of states that have Positive Protection assessment processes in place (that go beyond the drop-off criteria). Here is a partial list. This is a PARTIAL list, not all inclusive. Let’s look at the common elements we found (click):
Suggested Questions: Are you aware of any others?
Additional Information: States are listed alphabetically to avoid favoritism
Possible Problems: Someone may get defensive because their state is not listed. This is a PARTIAL list, not all inclusive.

## Slide 12: Example 1: Colorado DOT Positive Protection Guidelines:
“An Engineering Study is a process which will integrate data, analysis, judgment, and creativity to determine the best construction strategy for a given scenario.”
“An Engineering Study does not take the place of good engineering judgment, but should be used in conjunction with engineering judgment to guide the decision-making process.”
Notes: Key Message: Look at one definition, from Colorado.
Est. Presentation Time: 2 minutes
Explanation of Cues/Builds:
Suggested Comments: For example, let’s look at how Colorado defines an engineering study. Here is their definition. Look at the factors they consider: Data, analysis, judgment and creativity.
Suggested Questions: What do you think about these definitions? How would you use “creativity”?
Additional Information: None
Possible Problems: Try to generate discussion. Do not be critical of this definition. It is just one state’s definition. There are others. This definition seems to or trying to set the stage for making decisions based on engineering judgment rather than on the engineering study required in Subpart K.

## Slide 13: Example 2: North Carolina DOT Positive Protection Guidelines:
“The Engineering Study performed to determine the need for positive protection shall take into
consideration clear zone distances, roadway geometry, anticipated construction year traffic
volumes, traffic speeds, roadside geometry, workers safety, pedestrian safety, etc.
Notes: Key Message: Look at North Carolina’s definition
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Here is North Carolina’s definition. Notice that there are different factors that need to be considered, such as clear zone distances, roadway geometry, anticipated construction year traffic volumes, traffic speeds, roadside geometry, workers safety, pedestrian safety, etc.
Suggested Questions: How do these definitions compare? What do you think the “etcetera” means? How can that be used?
Additional Information: None
Possible Problems: Try to generate discussion. Do not be critical of this definition. It is just one state’s definition. There are others

## Slide 14: Example 3: VDOT’s Clear Zone & Drop-Off Chart
Image: Virginia DOT
Notes: Key Message: Show VDOT’s Clear Zone & Drop-Off Chart
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a portion of the VDOT chart, which shows the width of the clear zone and the criteria for drop-offs.
Suggested Questions: None
Additional Information: None
Possible Problems: Chart may not be legible. No need to discuss the table, just show it to illustrate the format of the chart. This a partial chart.

## Slide 15: Example: 3 VDOT’s Clear Zone & Drop-Off Chart
Image: Virginia DOT

## Slide 16: Example 6: Utah DOT Positive Protection Decision Tree
Image: Utah DOT

## Slide 17: UT: Key Decision Point
Image: Utah DOT

## Slide 18: Utah DOT Positive Protection Decision Tree
Image: Utah DOT

## Slide 19: Utah Scoring Factors
Factor 1: Duration of specific work elements
Factor 2: Exposure
Factor 3: Posted speed (prior to construction)
Factor 4: Location of work

## Slide 20: Utah Scoring: If TOTAL:
> 31 points - Positive protection device(s) are required in addition to standard traffic control and any other mitigation efforts
20-30: Positive protection device(s) or other mitigation efforts and standard traffic control required to minimize worker exposure.
<20: Use of standard traffic control is required

## Slide 21: Common Elements of The Positive Protection Selection Decision/Assessment Process
Determine variables & other factors (Mod. 2)
Apply Assessment Tool
Evaluate hazards & exposure
Consider “other”
strategies (Mod. 4)
Design positive protection
Apply engineering judgment
Notes: Key Message: Discuss common elements of existing Positive Protection selection decision processes
Est. Presentation Time: 3-4 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Let’s look at the common elements we found: This slide shows an informal flow chart that illustrates the common elements we identified in the states we evaluated. First, states determine the variables and other factors that are applicable. Factors such as speed, type of highway, duration and the others we have discussed. Second, they evaluate the hazards (such as drop-offs) and the exposure of the workers (such as proximity to traffic, probability of intrusions and lack of an escape route.) Then comes the key step, SIMULTANEOUSLY consider (and design) positive protection using the assessment tool AND/OR the other strategies we have discussed. Finally, engineering judgment is applied to confirm or modify the final decision. Notice the AND/OR. It is not necessarily one or the other. It could be both.
Suggested Questions: Would you consider this process an “engineering study”? Why or why not? Is this a “process”? This process may be considered an engineering study since it may be considered the “the comprehensive analysis and evaluation of available pertinent information, and the application of appropriate principles, provisions, and practices as contained in the MUTCD and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.”
Additional Information: Refer to definition of an engineering study as per the MUTCD, already discussed. Yes, this is a process.
Possible Problems: This is an informal finding and not an official research project. These “boxes” were already discussed in previous modules.

## Slide 22: Remember:
Apply solid engineering judgment
No black box syndrome!
Notes: Key Message: Discuss the engineering judgment element
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In any process, there must be room for engineering judgment. This judgment should be documented to protect against litigation in case of a lawsuit. Ask: Can I justify my decision? For example, engineering judgment is normally required to determine which work zones most need enforcement support. These strategies (positive protection and/or “other”) also have implications in terms of traveler mobility as well as work productivity and quality. Therefore, engineering judgment must be used to determine whether some or all of these are appropriate for a given project. Remember that the definition for engineering judgment in the MUTCD indicates that documentation of engineering is not required although is advisable to have in the case of litigation.
Suggested Questions: None
Additional Information: Judgment has to be part of the entire process and not only at the end. Make sure this emphasized.
Possible Problems: Treat this as a reminder. This is a point that has to be reinforced. Clarify that engineering judgment should be exercised throughout the entire process, not necessarily at the end.

## Slide 23: What About Your State?
Overview of this state’s Positive Protection process
Positive Protection Decision-Making Process

## Slide 24: Cost Factors
Cost of barrier vs. crash cost reductions
Benefit/cost ratio
  Is added safety a benefit?
  How to determine?
Is accelerated construction = less exposure?
Notes: Key Message: Discuss cost factors
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Designers typically consider factors discussed in a more qualitative manner and try to make a judgment call as to whether the safety risks outweigh the additional costs of requiring barriers. The goal is to reduce the severity of crashes with those objects by protecting them with barrier. The assumption is that impacts with the barrier will be less severe and so less costly than impacts with the other objects. Because of engineering judgment and other subjective factors, evaluation of the benefit-cost analysis may suggest highly different results.
Suggested Questions: Is accelerated construction equal to less exposure? Yes! So the additional costs involved with accelerated construction techniques may be offset by the safety benefits.
Additional Information: It appears that the minimum duration thresholds for Maryland and Michigan reflect the practicalities of moving PCB into and out of a work zone, rather than any type of benefit-cost analysis. The fact that neither discusses traffic demand nor expected crash frequency provides further evidence supporting this hypothesis.
Possible Problems: Try to generate discussion.

## Slide 25: For one-year, one-half mile work zone on a 70-mph divided highway with the actual work area located two feet beyond the edge of the travel lane
Source: WORK ZONE POSITIVE PROTECTION GUIDELINES,
FHWA/TX-11/0-6163-1, May 2011
Notes: Key Message: Discuss cost factors
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For analysis purposes, this figure illustrates a one-year, one-half mile work zone on a 70-mph divided highway with the actual work area located two feet beyond the edge of the travel lane (the buffer distance corresponding to either PCB or channelizing devices placed next to the travel lane). Under this scenario, intrusion crash costs savings alone can justify PCB protection once the roadway ADT approaches 40,000 vpd, as long as there are constant hazards in the work area. Furthermore, this value can simply be extrapolated to look at other work zone durations (i.e., this is equivalent to a 6-month work zone with an ADT of 80,000 vpd, a 2-year work zone on a 20,000 vpd facility, etc.).
Suggested Questions: At which ADT do the crash cost reductions match the costs to install and remove the PCB? At 40,000.
Additional Information: Source: WORK ZONE POSITIVE PROTECTION GUIDELINES, FHWA/TX-11/0-6163-1, May 2011. The encroachment-based hazard protection benefit-cost analysis approach outlined in the AASHTO Roadside Design Guide (2002) was viewed as the most logical methodology for calculations of crash cost benefits associated with portable concrete barrier use for positive protection in work zones. Researchers used the Roadside Safety Analysis Program (RSAP) to perform the analysis. RSAP was developed with the intent of evaluating permanent roadside hazard situations and so suffers from a number of limitations relative to its use for work zone analyses.
Possible Problems: This is one example. This graph may not be applicable to other projects.
(Note: The Texas report was published prior to the release of the 2011 RDG)

## Slide 26: Decision Making Assessment Tool
http://alamoheightsunitedmethodistchurch.blogspot.ca/2013_06_01_archive.html
Notes: (Transition slide. This slide is the transition to discussion of the assessment tool. No narrative required)

## Slide 27: Positive Protection Assessment Tool – Development
Evaluated existing Positive Protection assessment procedures
Combined their best features
Developed an interactive Excel-based Positive Protection Assessment Tool
Notes: Key Message: Discuss the composite Positive Protection assessment tool
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: The range and depth of assessment processes for deciding if positive protection should be used or not is extremely diverse throughout the US. These vary from basic to complex in nature. The assessment tool presented in this course is a composite of many states’ procedures. States whose assessment processes were used in developing the course assessment tool include NY, VA, CO, NC, MD, OR, MI, TX. The best features of these checklists and assessment elements were combined to provide an objective and comprehensive set of project and roadway conditions and factors representing the majority of work zones states and local agencies would be constructing.
Suggested Questions: How many here are aware of a positive protection checklist or set of assessment questions for your own state? At what stage in the project design process is the positive protection decision made? Are any here with local road authorities? If so, is there a process in place with your agency to assess the need for positive protection use?
Additional Information: None
Possible Problems: None

## Slide 28: Positive Protection Assessment Tool - Description
Composite of several state processes
Applies weights for various specific Roadway and Project factors assigned by user
Aggregates values yielding recommended action based on total score
Objective, but not “black box” – needs engineering judgment for final decision
Notes: Key Message: Describe Positive Protection assessment tool
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: Now that we have looked at a couple state examples, let’s move toward what those and other state processes have taught us about making decisions and look at an assessment tool developed as a composite of several states’ practices. Because of the ability for detailed selection of factors and conditions represented by this tool, there is a great deal of objectivity built in. Specificity in factor and condition selection yields scores that are aggregated for a final tally, which, in turn, yields a recommendation based on that score. These recommendations need independent engineering validation by professionals familiar with the project.
Additional Information: None
Possible Problems: Emphasize that other traffic control measures may be considered if the tool scoring does not reach the level of recommending use of positive protection.

## Slide 29: Preliminary Assessment Tool Use Filter
Will other exposure control measures accomplish the goal?
Y
Assessment tool not recommended
N
Is the project mobile or short duration?
Y
Assessment tool not recommended
N
Continue to assessment tool
Notes: Key Message: Consideration of other factors prior to use of the Assessment Tool
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: There may be other exposure control methods such as detours, alternate work schedules, law enforcement presence, full road closures, intensive public information campaigns, etc., that may be more effective or more economical than the use of concrete or other types of temporary, portable barriers. If, following an engineering study, one of these strategies or several in combination with one another may effectively take the place of barrier use, the assessment tool would not be used. If other strategies are deemed to be not as effective, then the question should be asked, “Is the project mobile or short duration?” Usually, temporary, portable barriers are not considered effective – cost or worker installation removal exposure-wise – for short-term or mobile operations.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 30: Getting Familiar with the Assessment Tool
Get in groups
Use this time to read and familiarize yourself with the:
  User Guide (Tab 1)
  Screening Tab (Tab 2)
  Assessment Tool layout (Tab 3)
  Wording of the Conclusions and Recommendations (Tab 4)
Notes: Key Message: Explain that this is a time to allow students to become familiar with the Assessment Tool, so when the instructor goes over various elements of the Tool, there is cursory knowledge on the part of the student.
Est. Presentation Time: 15 minutes
Explanation of Cues/Builds: Have the students get into groups of appropriate size – gathering around those who have brought a laptop.
Suggested Comments: Explain that students should move through the various tabs in the Excel workbook, familiarizing themselves first with how the Tool works (Tab 1 – User Guide) and with the various additional elements of the Tool (Tabs 2,3, 4). Explain that the last tab contains macros used by the Tool itself and need not be reviewed.
Suggested Questions: Are there any basic questions on how the Tool is organized?
Possible Problems: Participants may want to delve too deeply at this point into the workings of the Tool. Express the need to wait for additional slides and explanation. Likely this future discussion will answer most initial familiarity questions.

## Slide 31: Assessment Tool Overview – How It Works
Three main categories of input yield the score – project duration and characteristics; roadway characteristics
    Decision weight of the various factors
    Various conditions within factors
    Value of those conditions
The value of the factor is based on weight and condition selected, leading to an Assessment score for that factor
Notes: Key Message: The assessment tool seeks to take into consideration the variety of project and roadway factors and conditions that might exist on a project and, based on the selection of these various conditions, provide a primarily objective basis for a decision on the use of positive protection.
Est. Presentation Time: 10 minutes
Explanation of Cues/Builds: Distribute the Tool sample sheet and the User Guide and refer to them as you discuss the Tool. Slides 65 through 86 assume good instructor familiarization with the workings of the Assessment Tool. Read the “Positive Protection Assessment Tool development narrative” for a background on the development of the Tool.
Suggested Comments:
If, after consideration of other protective measures, positive protection is thought to be valuable to consider, this assessment tool can be used in the decision process. The word “assessment” is purposely used as this tool is not intended to yield a decision – only to lend objective information and a tentative recommendation to the decision process. As we will mention frequently, this tool is supplementary to an engineering study and engineering judgment as to whether the use of positive protection is the best decision for the project.
  Roadway and project factors; cost/benefit – The three main categories that feed into assessment of whether or not to use positive protection are Project duration; Road characteristics and Project characteristics. Selection of various conditions under these three main elements drives the totals that are eventually aggregated to deliver a recommendation for consideration. The Cost/Benefit analysis is separate from the other elements as is has the potential to cancel consideration of positive protection due to economic considerations.
  Decision weight of the various factors – The project and roadway characteristics listed in the assessment tool represent as many of the potential situations that may occur on a project. How important these are on any given project will vary by roadway, agency and significance of the project. For this reason, the weights given to factors in the tool are able to be customized to the needs of the individual agency.
  Various conditions within factors – Within each of the gray dropdown boxes in the “Condition Selection” column there are several options to select from in order to most accurately describe the specific condition related to the project or roadway factor in question. These choices were developed from a composite of indicators included in the various states’ checklists and processes reviewed. An attempt was made to be as inclusive as possible, but it is recognized that not every condition will or can be covered with these selections. In some cases conflicting suggestions were received from our practitioner group. In such cases, a judgment call was made on how to best represent that condition.
  Values assigned to conditions – the value placed on the individual conditions was, similar to the factor weights, done with application of knowledge and experience of the developer. In general, the more exposure or risk the condition adds to the mix, the higher the value. Higher condition values when multiplied by higher factor weights yield higher end scores
  The value of that factor based on weight and condition selected – The tool calculates a value for the condition selected based on the relative importance given to that condition and the weight assigned to that factor.
  Assessment score for that factor – Values are aggregated at the bottom of the “Score” column and a recommendation is generated based on the score. It should be noted that the final score is generated in terms of a “% of Total Possible” due to the fact that the individual factor weights can be customized. The calculations for determining 100 percent and for doing the math to yield the final percentage score are hidden in the worksheet.
Suggested Questions: Are there any questions about the workings of the assessment tool?
Additional Information: In all cases, regardless of the strength of recommendation to use or to avoid use of positive protection on the project, a qualified engineer should evaluate the weight factors and conditions selected and independently validate the recommendations of the assessment tool. This instrument is to be used as an objective supplement to engineering judgment and should not be used without independent professional validation.
Possible Problems: Participants may want to suggest significant changes to the tool during the class. There is always room for improvement in this process, but the instructor should take notes on the suggestions and indicate that these will be reviewed for possible inclusion. It is probably best for class productivity to avoid lengthy discussion on the validity of the tool itself during class time.

## Slide 32: Assessment Tool Overview – How It Works (cont.)
Weight factor determination
Benefit/cost evaluation
Scoring and recommendations
Role of engineering judgment
Notes: Key Message: Explanation of the assessment tool framework and development
Est. Presentation Time: 7 minutes
Explanation of Cues/Builds: None
Suggested Comments:
Weight factor determination – These were determined initially from developer knowledge and experience and modified based on practitioner input. All factor weights are able to be customized to provide a value that is commensurate with the experience of the individual agency doing the assessment and the individual project being assessed.
Scoring and recommendations – As mentioned earlier, the percentage scored in the upper portion of the assessment tool will yield one of three recommendations on use of positive protection. All of these recommendations are subject to the caveat that the final decision rests with the judgment of an experienced professional.
Role of engineering judgment – The tool is designed to be an objective base as support for a final decision on the use of positive protection on the project. The outcome of use of the tool becomes part of the “engineering study” required by the Final Rule.
Benefit/cost evaluation – There may be economic factors which preclude the use of positive protection. The Cost/Benefit dropdown box provides an N/A option plus four escalating percentages of positive protection cost, i.e., purchase, placement, movement and removal costs versus total project cost. The potential exists that, given a strong, objective recommendation for positive protection use based on the percentage of total points possible, cost factors would make the investment unfeasible. However, there may be specific agency policies which do not limit the cost of including positive protection in a project, favoring safety at any cost.
Suggested Questions: How does your agency strike the balance between various forms of information gathering and a final engineering decision on the use of positive protection?
Additional Information: None
Possible Problems: Their may be strong opposition to putting a limit on the value of safety. These objections are understood and should be validated with a nod toward the reality of cost versus benefit in actual project scenarios.

## Slide 33: Assessment Tool Overview – Roadway Factors
Access limitations, if any
Speed
Traffic volume and vehicle mix
Roadway geometry and sight distance issues
Notes: Key Message: Explaining data needs and condition assessments for the roadway element of the project
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments:
  Access limitations, if any – The judgment is made that limited (or controlled) access roadways are higher speed facilities and, therefore, have a greater risk associated with them for motorists and workers. Although the “Speed” factor is similar, this is a way to augment the score where speed is concerned. Limited access roadways with higher posted speeds will score significantly higher toward the use of positive protection than unlimited access and higher speeds.
  Posted speed limit – Much discussion ensued over the proper terminology here. The terms “construction speed”, posted speed” and “design speed” were considered. The term “construction posted speed (B/W)” was eventually selected as it is an enforceable speed and represents engineering judgment for those conditions.
  Traffic volume and vehicle mix – A fairly broad set of conditions was settled on for this factor, given that projects will be constructed on a variety of functional classifications. More volume with a greater percentage of commercial vehicles was considered to be the most likely to benefit from positive protection.
  Roadway geometry and sight distance issues – The assumptions is made that the greater the departure from level and straight, the greater the risk and greater the need for positive protection.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 34: Assessment Tool Overview – Project Factors
Project duration
Edge drop-off, if applicable
Work period(s)
Clear distance to hazard
Distance between traffic and workers
Device placement considerations
Escape path considerations
Subpart K
Image: ATSSA
Notes: Key Message: Discussion of various data elements related to the project.
Est. Presentation Time: 7 minutes
Explanation of Cues/Builds: None
Suggested Comments:
  Project duration – the condition selections for this item were a composite of many field staff suggestions. They do not meet the definitions in the MUTCD, but have been accepted by field practitioners.
  Edge drop-off, if applicable – the assumption is made that the deeper or steeper the drop-off, the higher the value, building from 1” to greater than 12”
  Work period(s) – three conditions were selected to cover day-only, night-only and a combination of both. The assumption is that a continuous day-night operation provides the greatest risk and, therefore, the highest value for that condition.
  Clear distance to hazard – the greater the distance – the less the risk to the worker.
  Distance between traffic and workers – Again, the greater the distance, the less the risk
  Device placement considerations – this is the only condition with potential to subtract points toward recommendation for positive protection. There are two elements considered here: 1) The economics of placement and removal – is that investment higher than the potential safety benefit; and 2) is the placement, removal and fixed object hazard, i.e., worker and motorist exposure, greater than the potential benefit that positive protection would provide.
  Escape path consideration – the fewer the options for worker escape, the greater the risk and the greater the value of positive protection.
Suggested Questions: Can you give me some situations in your experience related to the last four conditions – clear distance, distance of traffic to worker, device placement considerations and escape paths?
Additional Information: None
Possible Problems: None

## Slide 35: Assessment Tool User Guide
Used in conjunction with the Excel-based Assessment Tool
Contains guidance on use and definitions of elements of the Tool
Explains how values and recommendations are arrived at
Re-emphasizes importance of a final review of the Tool outcomes by a competent professional
Notes: Key Message: Pointing out the purpose and content of the Assessment Tool User Guide
Est. Presentation Time: 7-10 minute(s)
Explanation of Cues/Builds: A discussion will follow the class review of the User Guide
Suggested Comments: The tool is comprised of three tabs in an Excel spreadsheet. Tab 1 is the Assessment Tool itself; Tab 2 is Conclusions and Recommendations along with some possible decision justification language; Tab 3 is hidden and links to the contents of the Condition Selection drop down boxes. The Guide explains how the tool is to be used as well as its flexibility and limitations. The various elements of the Tool are explained and how values are entered and a score and recommendations are presented. The point is emphasized again that the Tool is an objective means of supporting a decision whether or not to use positive protection devices on a particular project and that a final decision must be made after a review by a competent professional.
Let’s take a look at the guide. It’s broken down into five major headings – introductory notes; general instructions for use; general definitions; roadway and project factor definitions; and output and recommendations. Take 5 minutes and review this guide and then we’ll discuss it before we actually take a look at the tool itself.
Suggested Questions: (After the 5-minute class review of the user guide) Do you have any specific questions on the user guide?
Additional Information: None
Possible Problems: None

## Slide 36: General Instructions for Use
Determine if there are any of the Factor Weights that you may want to customize for more local applicability
Click on the Condition Selection box across from the Roadway and project factor you are considering
Select the condition that is most appropriate to your project for all applicable factors, including the B/C options. This will yield a score and recommendation
Notes: Key Message: Become familiar with the first three general instructions for using the tool
Est. Presentation Time: 10 minutes
Explanation of Cues/Builds: Topics appear on click
Suggested Comments:
1) Decide if there are any of the Factor Weights that you care to customize to more local applicability – Because conditions vary by functional classification of the roadway and significance of the project, Users may want to review the default weights given to the Roadway and Project Factors. The User simply need enter a different value from 1-5 in the box to the right of that Factor. The remainder of the worksheet is locked and no other values may be adjusted.
2) Click on the Condition Selection box across from the Roadway and Project Factor you are considering – These Conditions are representative of a majority of cases and were vetted with a broad-ranging practitioner group. If the User does not find a Condition representative of their current project, the tool may be set aside, or a close proximity selected. The spreadsheet is programmed to zoom the Condition Selection Box to 140% to facilitate viewing. It is also designed to return to 80% when you click elsewhere on the worksheet. If this function does not activate, the version of Excel you use may not support the macro embedded and you may need to increase and decrease your zoom percentage manually.
3) Select the condition that is most suitable to your project – Condition values were assigned from 0-5, generally increasing in value as the potential hazard represented by the Condition increases. Once a Condition has been selected for each Condition dropdown box, the Assessment Tool will automatically calculate values for each and aggregate the scores to yield of “% of Total Possible”. Since the Weight Factors are customizable, a background calculation sums the total possible based on the User’s choices and yields a “% of Total Possible” based on the customized weights, keeping the final percentage in direct relation to the choices made.
Suggested Questions: Given the default weights in the Assessment Tool, are there any that you, personally, would adjust?
Additional Information: None
Possible Problems: None

## Slide 37: General Instructions for Use (cont.)
Review the score and recommendation for reasonableness based on the conditions selected.
Make a final decision on use of positive protection based on review of the Tool outcomes through professional engineering judgment
Notes: Key Message: Become familiar with the last three instructions for tool use
Est. Presentation Time: 10 minutes
Explanation of Cues/Builds: Topics appear on click
Suggested Comments:
4) Review the score and recommendation for reasonableness – The Assessment Tool is designed to provide an objective aggregation of values for conditions you select. However, “standing back” and making sure the outcome meets the “reasonableness” factor is the first step in the engineering judgment part of the process.
– There are four ranges and “N/A” to select from. The condition selected here may yield a recommendation that, regardless of the value of the use of positive protection indicated by the recommendation to the right of the “% of Total Possible”, that economic factors may make its use untenable.
5) Make a final decision on positive protection use based on engineering judgment - The point must be stressed that this assessment tool is an objective supplement to an engineering study and the final decision must be made through engineering judgment.
Suggested Questions: When we use the term “engineering study” and ‘engineering judgment”, what comes to mind?
Additional Information: Now that we have an idea of the background, let’s take a look at the Tool itself.
Possible Problems: Demonstrate the Excel tool live on the screen. This slide is for information only. Hide if not needed.

## Slide 38: Data Entry and Customization of Weight Factors
Image: FHWA
Notes: Key Message: Explanation of data entry process and customization of the weight factors
Est. Presentation Time: 2 minutes
Explanation of Cues/Builds: The instructor brings up the assessment tool as a separate file and walks participants through its use. Review the layout of the tool, including headings, project and roadway factors, function of the dropdown boxes, values, scores, percent of total possible, recommendations and B/C outcome. Adjust a Factor Weight to demonstrate this option. Select various Conditions from the drop down boxes to demonstrate how the final score and recommendation changes. Following the explanation of the workings of the tool, the instructor should go through each Condition Selection dropdown box to show participants what Conditions have been loaded into the Tool. Following this review, the instructor should ask participants to suggest changes to the Factor Weights to illustrate how the values change with the different factors. At least once during the discussion, make sure to select factors and conditions that change the “% of Total Possible “ to the three ranges: <50%; 50% - 75%; 76 – 100%
Suggested Comments: The Conditions in the dropdown boxes paired with the Weight Factor determine the Condition Values. The higher the Weight Factor and the more potentially hazardous the Condition, the higher the Condition Value and the more the value contributes to a higher “% of Total Possible” and recommendation of positive protection use.
Suggested Questions (choose two Roadway or Project Factors to use as examples): What situations would contribute to adjustment of (discuss the two selected factors you chose)
Additional Information: Refer to Module 3.
Possible Problems: Demonstrate the Excel tool live on the screen using the separate Excel Tool file. This slide is for information only. Hide if not needed, i.e., discussion is conducted using the Excel Tool itself. Going through all of the dropdown box conditions and changing several of the Weight Factors could be very time consuming. The instructor may want to abbreviate the explanation or have pre-prepared example

## Slide 39: Results and Recommendations
Image: FHWA
Notes: Key Message: Discuss outcomes of scoring
Est. Presentation Time: 1-2 minutes
Explanation of Cues/Builds: Explain that the recommendations for both the “% of Total Possible” and “B/C Considerations” outcomes have their source in the Conclusions and Recommendations tab (3rd tab), which will be discussed in the next two slides.
Suggested Comments: The recommendations for both the “% of Total Possible” and the “B/C Considerations” are based on the scores and conditions selected as demonstrated in the previous slide. The Conclusions and Recommendations tab is the source for those recommendations. As discussed in the last slide, the guidance moves progressively toward more solid recommendation of positive protection use as the “% of Total Possible” increases. The outcome for the “B/C Consideration” is considered separately due to the fact that, although conditions may lean toward positive protection use, the cost of purchase, placement and removal may be economically prohibitive.
Suggested Questions: Have you ever faced the situation where cost of positive protection stopped its consideration for use on a project even though conditions may have warranted its use?
Additional Information: As stated previously, the tool is intended as an objective supplement to the decision based on an engineering study and judgment.
Possible Problems: Demonstrate the Excel tool live on the screen. Use this slide as an instructor reference as the actual Excel Tool file is being viewed.

## Slide 40: Assessment Review and Conclusions Related to Base Score
Image: FHWA
Notes: Key Message: Discuss possible outcomes of scoring for the “% of Total Possible”
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: The instructor should close the tool Excel file and work again from the course PowerPoint. This portion of the Conclusions and Recommendations tab (3rd tab) shows the source of the “% of Total Possible” recommendation based on the percentage in the cell.
Suggested Comments: As demonstrated in our discussion of the assessment tool, the recommendations for both the “% of Total Possible” and the “B/C Considerations” are based on the scores and conditions selected. The Conclusions and Recommendations tab is the source for those recommendations. Notice that each of these recommendations stops short of a definitive decision. Each intentionally leaves the door open to engineering judgment. Again, the value listed in the “% of Total Possible” pulls one of these recommendations as an objective outcome.
Suggested Questions: None
Additional Information: None
Possible Problems: Demonstrate the Excel tool live on the screen. This slide is for information only. Hide if not needed. Participants may differ on the language used in the recommendations, notes or additional justification. The instructor should thank the participant for their input and note suggestions for future consideration when a course update is undertaken.

## Slide 41: Assessment Review and Conclusions Related to B/C Considerations
Image: FHWA
Notes: Key Message: Discuss outcomes of “B/C Considerations”
Est. Presentation Time: 2 minutes
Explanation of Cues/Builds:
Suggested Comments: The recommendations for the “B/C Considerations” are based on the estimated percent the purchase, placement, adjustment and removal of the positive protection cost is of the estimated total project cost. Again, the language here leaves plenty of room for engineering judgment if certain circumstances call for a decision other than what is recommended from the tool. Also included in Tab 3 is guidance for documentation of the decision made with suggestions on additional justification of positive protection use and suggested documentation for deciding against its use when the assessment tool indicates it may be recommended.
Suggested Questions: None
Additional Information: B/C = benefit/cost
Possible Problems: Demonstrate the Excel tool live on the screen. This slide is for information only. Hide if not needed. Participants may differ on the language used in the recommendations, notes or additional justification. The instructor should thank the participant for their input and note suggestions for future consideration when a course update is undertaken.

## Slide 42: Positive Protection Assessment Tool
Assessment Tool

## Slide 43: Applying the Tool to Real-World Examples – Scenario 1
Project description: Overlay project on freeway
  ROADWAY CHARACTERISTICS: Duration-13 days; Limited access; posted 65 mph; 75,000 vpd; 5% trucks; straight; no sight distance issues
  PROJECT CHARACTERISTICS : Day only; 2-3” drop-off (uneven lanes) for 200’; 4’ workers to traffic; device placement cost/benefit = install time vs. benefit too high; no escape path issues
Notes: Key Message: Apply assessment tool to a real-world example No. 1
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The project type is: Overlay project on freeway. The project-specific data is shown. Enter this information in the tool and apply weight factors
Suggested Questions: None
Additional Information: None
Possible Problems: Three scenarios are provided. Adjust depending on available time and participants’ interests. Instructor may do this him/herself or have students do it in groups, which may be more time consuming. Consider doing the first one and let the students do the other(s).

## Slide 44
Image: Washington State DOT
Notes: Key Message: Illustrate the example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This photo gives you an idea of the project in question.
Suggested Questions: What do you observe from this picture? How can Positive Protection help? Other strategies?
Additional Information: Photo from Washington State Webpage.
Possible Problems: None

## Slide 45: Scenario 1 Decision/Discussion
Use the assessment tool to aid in the decision whether to use or not use barrier as positive protection
Would other exposure reduction measures be more cost-effective and beneficial?
Notes: Key Message: Discussion of scenario
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: Use the assessment tool to aid in the decision whether to use or not use barrier as positive protection. Apply weight factors based on your assumptions and judgment.
Suggested Questions: Other positive protection measures that would be more cost-effective and beneficial? Which strategies would you recommend and why?
Additional Information: Allow students to apply the tool as they wish. Break into groups and encourage interaction. If there is time have a person summarize their decision-making process and discuss as a group.
Possible Problems: Students may have different answers based on assumptions and weight factors. That is okay and helpful with the discussion. A “solution” is not given. There is not a single answer since we all have different judgment. That is part of the learning process. Avoid taking sides. Facilitate until a reasonable level of consensus is reached.

## Slide 46: Assessment Tool Discussion
What are your thoughts about this tool?
Do you think it is viable?
Which changes would you make?
Is it practical? Useful?
Is it realistic? Simplistic?
Does it leave room for engineering judgment?
Notes: Key Message: Discussion of Assessment Tool
Est. Presentation Time: 5 minutes
Explanation of Cues/Builds: None
Suggested Comments: Now that you have used the tool, let’s discuss it. Let’s consider the questions on the screen.
Suggested Questions: Can you suggest improvements? What are your thoughts?
Additional Information: None
Possible Problems: Allow students time to think. Have some questions prepared to generate discussion. Keep a list.

## Slide 47: Module Recap
Name two states that have developed Positive Protection use assessment tools
What are some common elements to assessment procedures?
Describe the decision-making process of the proposed Excel-based tool
Are the recommendations of the tool final and absolute?
Notes: Key Message: Module Recap
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s see what we have learned. {Address the questions on the screen}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 48: Questions