## Slide 1: 6. Decision-Making Scenarios
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s move on to Module 6, where we look at various scenarios and a Positive Protection matrix.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Apply the Positive Protection flow chart and assessment tool to various scenarios
Present a Positive Protection matrix for various scenarios
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module. We will look at applying the Positive Protection flow chart and assessment tool to various scenarios and present a Positive Protection matrix.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Key Decision Points
Moving?
Roll-ahead distance?
Station-ary?
Short duration?
Intermediate-term?
Long-term?
Short-term?
TMAs
Steel barrier
Mobile barrier
Barriers
Vehicle-arresting systems
Notes: Key Message: Discuss key decision points
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: Text boxes on right appear on clicks
Suggested Comments: In assessing the need for Positive Protection, and based on the processes we evaluated, the first key decisions we need to make is whether the project is a moving or a stationary operation. If it is moving, we need to check if there is sufficient RAD. For moving operations, the options are, other than law enforcement officers, [click] the ones you see here. TMAs are common and usually required for multilane highways with speeds higher than 45 mph. Some of the barriers we discussed are applicable to moving operations. For stationary operations, we need to assess the duration. The duration would be a main factor. For those projects [click], these devices, among others may be best suited.
Suggested Questions: How does the RAD affect this decision? (next slide). Duration?
Additional Information: None
Possible Problems: We are simplifying a very complex decision. Emphasize this is not a black box and that these are examples (not all inclusive). Engineering judgment is required, and every project is different. TMAs may be required in some states.

## Slide 4: Moving Operations: Adequate Roll-Ahead Distance?
YES
Shadow vehicles w/TMAs
Steel Barrier
NO
Steel Barrier
Mobile barrier
Notes: Key Message: Discuss key decision points
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: Text boxes on right appear on clicks
Suggested Comments: If the RAD is adequate, then we can use shadow vehicles with TMAs or steel barriers. If there is no RAD, then we should consider steel or mobile barriers.
Suggested Questions: How does the RAD affect this decision?
Additional Information: None
Possible Problems: Mobile barriers are proprietary and may require rental for several projects. Treat as a summary. These devices have been discussed earlier.

## Slide 5: Stationary Operations: Duration of Operation
Long
term
Barriers
“Other” Positive Protection Measures
Short
term
TMAs
Vehicle-Arresting Systems
“Other” Positive Protection Measures
Notes: Key Message: Discuss key decision points
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: Text boxes on right appear on clicks
Suggested Comments: For stationary operations, as an example, duration is a major factor. These are some of the Positive Protection devices and “other” strategies that may be considered.
Suggested Questions: By definition, how long are “long term” projects? More than 3 days.
Additional Information: Treat as an EXAMPLE.
Possible Problems: This is an EXAMPLE of the decision making process based on DURATION. As previously discussed, there are several other factors to consider

## Slide 6: “Strategies” Matrix Ingredients
Positive Protection assessment tool
Existing guidance
  Positive Protection flowchart
Input from Positive Protection Task Force
A touch of engineering judgment
REMEMBER: This matrix provides GUIDANCE. It is not a warrant nor is it a substitute for engineering judgment!
Notes: Key Message: Discuss basis for decision matrix
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Using similar decision points, we have developed a Positive Protection assessment matrix, to provide guidance and support for your decisions. We looked at the Positive Protection assessment tool, the existing guidance we found, input from our Positive Protection Task Force and added to our judgment, we compiled a Positive Protection “guidance” decision matrix. This matrix is the result of the items listed on the screen. All these items are considered the “ingredients” that resulted in the matrix. Let’s look at it.
Suggested Questions: None
Additional Information: Existing guidance refers to some of the Positive Protection decision processes in place.
Possible Problems: This matrix provides GUIDANCE. It is not a warrant nor is it a substitute for engineering judgment!

## Slide 7: Positive Protection Selection Matrix
Work Type or Location /Work Duration | LT | IT | ST | SD | M
Paving | 2 | 2 | 2 | C/D | C
Grind inlay/overlay |  | 2 | 2 | C/D | C
Bridge construction | 1 |  |  | C/D | 
Bridge rail replacement | 2 | 2 | 3 | C/D | 
Roadway realignment | 2 |  |  | C/D | 
Pavement widening | 3 |  |  | C/D | C
Culvert/pipe installation | 3 | 3 | 3 | C/D | 
Shoulder work | 3 | 3 |  | A | A
Open excavation | 1 | 2 | 3, B |  | 
Pothole patching |  |  |  | A/D | A/D
Sweeping |  |  |  |  | C
Guardrail/Barrier repair |  |  | B | D | B
Crack sealing |  |  | B | C | C
Ramp closure | 1 | 2 | 3 |  | 
Lane closure | 1 | 2 | 3 |  | A
Pavement marking |  |  |  |  | A
Bridge inspection |  |  |  |  | C
Overhead Sign Repair/Replacement | 2 | 2 | 3 | C/D | 
1 = Barrier strongly recommended
2 = Barrier should be considered
3 = Barrier optional
A = TMA strongly recommended
B = TMA should be considered
C = TMA
D=Mobile barrier/arrestor
LT = Long-Term IT = Intermediate- Term ST = Short-Term SD = Short Duration M = Mobile
Image: FHWA
Notes: Key Message: Positive protection selection matrix
Est. Presentation Time: Several minutes
Explanation of Cues/Builds: None
Suggested Comments: Here is the matrix. Remember that this is Guidance ONLY. You may adjust based on all the factors we have discussed, including your own engineering judgment and other factors. First let’s look at the legend on the right hand side. [explain the colors]. The column headings refer to the project duration as indicated on the legend on the lower right. We have listed several work types. Of course, this list is not all-inclusive, but it gives you an idea (“supports your decision-making”) when evaluating the need for Positive Protection devices. [Provide examples as needed]
Suggested Questions: None
Additional Information: This matrix excludes law enforcement
Possible Problems: Colors and numbers indicate the same. Colors are used to facilitate at-a-glance viewing. TMA may be required in some states. Shoulder work and Ramp/Lane Closure are not types of work. Clarify. Re: Bridge Inspection: “Mobile” in this instance refers to work that mover intermittently (as opposed to continuously). Bridge inspection is usually a mobile operation, depending on whether there is lane. May not be legible due to point size.

## Slide 8: Sample Scenarios
For the following sample scenarios, let’s use the tool/flow chart to suggest Positive Protection and/or other strategies
Justify your decision
Image: FHWA
Notes: Key Message: Introduce sample scenarios
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For the following three sample scenarios, let’s use the tool/flow chart to suggest Positive Protection and/or other strategies. Remember that this is guidance only.
Suggested Questions: None
Additional Information: None
Possible Problems: Matrix here is for decoration.

## Slide 9: Sample Scenario 1
Long-term right-lane closure on Interstate freeway
2 weeks
8-inch drop-off
Workers within 3 feet of moving traffic
Notes: Key Message: Sample scenario 1
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [Describe the scenario on the screen as needed].
Suggested Questions: None
Additional Information: None
Possible Problems: Try to generate discussion BEFORE showing the next slide. Photo is used to illustrate the type of highway.

## Slide 10: Sample Scenario 1
Image: FHWA
Notes: Key Message: Illustrate the use of the matrix
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [demonstrate the use of the matrix for the scenario conditions given]. For these conditions, the matrix suggests a barrier for worker protection.
Suggested Questions: What assumptions are we making, if any? That this is high speed. Any others?
Additional Information: None
Possible Problems: Some may disagree. That is fine. This is just guidance based on assumptions and engineering judgment.

## Slide 11
Image: FHWA
Notes: Key Message: Present the same scenario with the flow chart
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [demonstrate the use of the flow chart]. Notice that we arrive at the same conclusion: Barriers should be considered for this project.
Suggested Questions: None
Additional Information: None
Possible Problems: Flow chart may not be legible. Refer students to handout. Make sure you indicate the content of the boxes.

## Slide 12: Sample Scenario 1 Discussion
Process recommends a barrier
  Drop-off condition will require it!
  Worker exposure considerations?
Notes: Key Message: Discuss sample scenario 1
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: What led to this recommendation? Duration? Worker safety considerations?
Suggested Questions: Do you agree with this recommendation?
Additional Information: None
Possible Problems: Try to generate discussion. Best if there are disagreements. Do not take sides but facilitate the discussion.

## Slide 13: Sample Scenario 2
Nighttime paving project on 4-lane divided suburban arterial
Paving one mile per hour
Uneven lanes
Workers on foot
Image: ATSSA
Notes: Key Message: Sample scenario 2
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [Describe the scenario on the screen as needed].
Suggested Questions: None
Additional Information: None
Possible Problems: Try to generate discussion BEFORE showing the next slide. Photos are used to illustrate the type of highway.

## Slide 14: Sample Scenario 2
Notes: Key Message: Illustrate the use of the matrix
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Arrows and circle appear on click.
Suggested Comments: [demonstrate the use of the matrix for the scenario conditions given]. For these conditions, the matrix suggests a TMA for worker protection.
Suggested Questions: What assumptions are we making, if any?
Additional Information: None
Possible Problems: Some may disagree. That is fine. This is just guidance based on assumptions and engineering judgment.

## Slide 15
Image: FHWA
Notes: Key Message: Present the same scenario with the flow chart
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [demonstrate the use of the flow chart]. Notice that we arrive at the same conclusion: TMAs should be considered for this project.
Suggested Questions: None
Additional Information: None
Possible Problems: Flow chart may not be legible. Refer students to handout. Make sure you indicate the content of the boxes. TMA may be required in some states.

## Slide 16: Sample Scenario 2 Discussion
Process recommends shadow vehicles with TMAs
  High speed requires the TMA
  Worker exposure considerations?
Notes: Key Message: Discuss sample scenario 2
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: What led to this recommendation? Duration? Worker safety considerations?
Suggested Questions: Do you agree with this recommendation?
Additional Information: None
Possible Problems: Try to generate discussion. Best if there are disagreements. Do not take sides but facilitate the discussion.

## Slide 17: Sample Scenario 3
Guardrail repair on two-lane road
Speed: 45 mph
Duration: 6 hours
No shoulder
Notes: Key Message: Sample scenario 2
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [Describe the scenario on the screen as needed].
Suggested Questions: None
Additional Information: None
Possible Problems: Try to generate discussion BEFORE showing the next slide. Photos are used to illustrate the type of highway. Photo is not a two-lane road.

## Slide 18: Sample Scenario 3
Notes: Key Message: Illustrate the use of the matrix
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Arrows and circle appear on click.
Suggested Comments: [demonstrate the use of the matrix for the scenario conditions given]. For these conditions, the matrix suggests a barrier for worker protection.
Suggested Questions: What assumptions are we making? Are TMAs common on two-lane roads? We are assuming the TMA would fit in these conditions.
Additional Information: None
Possible Problems: Some may disagree. That is fine. This is just guidance based on assumptions and engineering judgment.

## Slide 19
Image: FHWA
Notes: Key Message: Present the same scenario with the flow chart
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [demonstrate the use of the flow chart]. Notice that we arrive at the same conclusion: TMAs should be considered for this project.
Suggested Questions: None
Additional Information: None
Possible Problems: Flow chart may not be legible. Refer students to handout. Make sure you indicate the content of the boxes. TMA may be required in some states.

## Slide 20: Sample Scenario 3 Discussion
Process recommends shadow vehicles with TMAs
  High speed requires the TMA
  Worker exposure considerations?
Notes: Key Message: Discuss sample scenario 3
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: What led to this recommendation? Duration? Worker safety considerations?
Suggested Questions: Do you agree with this recommendation?
Additional Information: None
Possible Problems: Try to generate discussion. Best if there are disagreements. Do not take sides but facilitate the discussion.

## Slide 21: Positive Protection Selection Matrix
Attempts to simplify a very complex decision affected by very many factors
There is no substitute for engineering judgment
Provides support to your decision process
Provides a framework for decision-making
Notes: Key Message: Summarize the scenarios and seek input
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We have presented a matrix (and flow chart and tool) that attempts to simplify a very complex decision affected by very many factors. There is no substitute for engineering judgment. This process provides support to your decision process and provides a framework for decision-making.
Suggested Questions: None
Additional Information: None
Possible Problems: May want to keep this short based on the level of discussion achieved during the scenario discussions.

## Slide 22: Module Recap
Name some considerations about the matrix presented
Name some conditions for its use
What are the key decision points?
Is it a substitute for engineering judgment?
Notes: Key Message: Recap slide
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Try to gauge understanding by asking these questions and others.
Suggested Questions: Shown.
Additional Information: None
Possible Problems: None

## Slide 23: Questions