## Slide 1: 7. Workshop
Minimizing Worker Exposure Through the Use of Positive Protection and Other Strategies
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s move on to Module 7. Let’s do a workshop, so we can apply the some of the concepts we have learned.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Apply the concepts learned to real-world scenarios
Present recommendations to class
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module. We will look at applying the Positive Protection flow chart and assessment tool to various scenarios and present a Positive Protection matrix.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Workshop Scenarios
Working as a group, for the three scenarios given, assess the need for positive protection devices and/or other exposure control measures
Make a group recommendation for each
Assign a group leader to present your recommendation to the class
Notes: Key Message: Introduce workshop
Est. Presentation Time: Less than 3-4 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For the workshop, we will look at the same facility and work zone (size) and consider three separate scenarios, with varying types of work, work duration and other factors. Please refer to the handout provided for details. Please discuss and brainstorm the following, assign a group leader and present your group recommendations to the rest of the class. Please discuss, for each of the three scenarios, the following:
Temporary traffic control
The need for positive protection
- Positive Protection devices used
- Other strategies deployed
Constructability considerations
- Other factors that may influence your decision (be specific)
- How would you document/justify your decision?
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 4: Highway Facility
Rural six-lane interstate freeway
EB right lane closure
65 mph
12-ft wide lanes
Ramps must remain open
Light volume
Image: ATSSA
Notes: Key Message: Introduce workshop
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This the highway facility where the three scenarios will take place. [describe as needed]
Suggested Questions: None
Additional Information: None
Possible Problems: May say that 65 mph is the anticipated prevailing speed. North is up. Traffic moves Eastbound.

## Slide 5: Three Scenarios
 | 1 | 2 | 3
Type | Full Depth Patching | Milling and Resurfacing | Bridge Inspection
Duration | 2 weeks | 6 hours (nighttime) | 1 hour (up to 3)
Drop-off | 8 inches | 3 inches | None
Workers | 2 feet from traffic | 2 feet from traffic | On shoulder
Notes: Key Message: Introduce workshop
Est. Presentation Time: Allow 30-45 minutes for discussion and 10 minutes per group for presentations. Adjust as needed.
Explanation of Cues/Builds: None
Suggested Comments: Here is a summary of the three scenarios. Please refer to the handout for additional information. Let’s read the scenarios together!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 6: Snooper Truck (Scenario 3)
Image: Virginia DOT

## Slide 7: For Each Scenario, Document the Following:
Decision process for use or non-use of Positive Protection
Type of Positive Protection used, if any – in some cases, multiple types may be utilized
Reasons for type(s) utilized and reasons why others were not used or no Positive Protection was used
Any agency policies/standards on Positive Protection re: duration, drop-off, speed, etc.
Other recommended Exposure Control Measures
Notes: Key Message: Introduce workshop
Est. Presentation Time: Allow 30-45 minutes for discussion and 10 minutes per group for presentations. Adjust as needed.
Explanation of Cues/Builds: None
Suggested Comments: For the three scenarios given, document whether you would deploy Positive Protection devices and the type chosen, along with the reasons to utilize/not utilize Positive Protection. Discuss whether workers are “safe” and how worker safety is achieved. Document all your assumptions.
Suggested Questions: None
Additional Information: Have the students refer to the written scenarios.
Possible Problems: None

## Slide 8: Group Presentations
Image: ATSSA
Notes: Key Message: Group presentations
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This the highway facility where the three scenarios will take place. [describe as needed]
Suggested Questions: None
Additional Information: Use this slide to have group leaders explain their recommendations. Make sure you have a laser pointer. Projecting on a white board allows students to draw their recommendations. If the group is small, may project on the clipboard.
Possible Problems: May say that 65 mph is the anticipated prevailing speed. North is up. Traffic moves Eastbound.

## Slide 9: Group Presentations (Detail)
Image: ATSSA
Notes: Key Message: Discuss workshop
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: [Zoomed area for presentations, if needed]
Suggested Questions: None
Additional Information: Use this slide to have group leaders explain their recommendations, if needed. Make sure you have a laser pointer. Projecting on a white board allows students to draw their recommendations. If the group is small, may project on the clipboard.
Possible Problems: None

## Slide 10: Positive Protection Selection Matrix
Work Type and Location/Work Duration | LT | IT | ST | SD | M
Paving |  | 2 | 2 | C/D | C
Grind inlay/overlay |  | 2 | 2 | C/D | C
Bridge construction | 1 |  |  | C/D | 
Bridge rail replacement | 2 | 2 | 3 | C/D | 
Roadway realignment | 2 |  |  | C/D | 
Pavement widening | 3 |  |  | C/D | C
Culvert/pipe installation | 3 | 3 | 3 | C/D | 
Shoulder work | 3 | 3 |  | A | A
Open excavation | 1 | 2 | 3, B |  | 
Pothole patching |  |  |  | A/D | A/D
Sweeping |  |  |  |  | C
Guardrail/Barrier repair |  |  | B | D | B
Crack sealing |  |  | B | C | C
Ramp closure | 1 | 2 | 3 |  | 
Lane closure | 1 | 2 | 3 |  | A
Pavement marking |  |  |  |  | A
Bridge inspection |  |  |  |  | C
Overhead Sign Repair/Replacement | 2 | 2 | 3 | C/D | 
1 = Barrier recommended
2 = Barrier should be considered
3 = Barrier optional
A = TMA recommended
B = TMA should be considered
C = TMA
D=Mobile barrier/arrestor
LT = Long-Term IT = Intermediate- Term ST = Short-Term SD = Short Duration M = Mobile
Image: FHWA
Notes: Key Message: Positive protection selection matrix
Est. Presentation Time: N/A
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: Provided here for student use during presentations, if needed.
Possible Problems: None

## Slide 11
Image: FHWA
Notes: Key Message: Positive protection flow chart
Est. Presentation Time: N/A
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: Provided here for student use during presentations, if needed
Possible Problems: None

## Slide 12: Module Recap
Which factors influence your decision to use Positive Protection devices and strategies?
Do these recommendations minimize worker exposure?
Did you get a feel for the assignment of weights?
How can we justify our decisions?
Notes: Key Message: Recap slide
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Try to gauge understanding by asking these questions and others.
Suggested Questions: Shown.
Additional Information: None
Possible Problems: None

## Slide 13: Questions