## Slide 1: 3. Examples of ITS Applications
Smarter Work Zones
Image: Utah DOT
Notes: Key Message: Title slide
Background Information: As time permits on day 1 cover as many examples as possible. Note: the purpose of the examples is to illustrate potential uses of ITS in the work zone area.
Interaction: None
Notes: This module will provide examples of Smarter Work Zones that have used Technology applications on roadway construction projects to reduce work zone conflicts. This module is the third of six modules.

## Slide 2: Module Objectives
Provide examples of Smarter Work Zones that have used ITS applications on roadway construction projects to reduce work zone conflicts
Notes: Key Message: Module Objectives
Background Information: We will provide examples of Smarter Work Zones that have used ITS applications on roadway construction projects to reduce work zone conflicts
Interaction: N/A
Notes: None

## Slide 3: Smarter Work Zones Examples
Variable Speed Limits
Dynamic Merge
Queue Warning
Portable Changeable Message Signs (PCMS)
Image: Utah DOT
Image: Minnesota DOT
Image: FHWA
Notes: Key Message: This module will describe example applications of Smarter Work Zones. It will provide information regarding technology that have been used by various states regarding applications for:
Variable Speed Limits
Dynamic Merge
Queue Warning
Portable Changeable Message Signs (PCMS)
Background Information: Briefly introduce what will be discussed during this module.
Interaction: N/A
Notes: None

## Slide 4: Example #1: Utah Variable Speed Limits in Work Zones
Implementation Goal: Improve safety for construction personnel and the traveling public within construction work zones through significant reductions in traveler speed within the boundaries of active work zones
Image: Utah DOT
Notes: Key Message: Introduce the first example in Utah
Background Information: The first example is Utah’s use of variable speed limits in work zones. The goal of the implementation was to Improve safety for construction personnel and the traveling public within construction work zones through significant reductions in traveler speed within the boundaries of active work zones. Utah has a lot of 80mph roads, but speed limits on these roads are typically reduced down to 45 or 50 miles an hour for work zones. While the MUTCD recommends no more than 10 mph reduction, a speed of 70 mph still makes for a fast-moving semi when you only have a drum between you and it!
In an active work zone it's the public’s understanding that you are reducing the speed for a reason. In a construction zone, it’s different. When the public drives through a 10-mile long project and only sees one crew working at mile nine, but the speed limit has been reduced from 80 to 50 for the entire 10-mile distance, they lose confidence in the transportation agency. Drivers need to see the reason why they should slowdown, and that the speed limit is actually reduced for a reason. That is why the words “significant” and “active” are critical in our goal.
Interaction: None
Notes: None

## Slide 5: Concerns
Traffic Queueing
  Preliminary traffic modeling predicted no queueing
  1,800 vehicle/hour/lane with small variance
Speed Harmonization
  Little concern until deviation greater than 15 mph from median speed
Enforcement
  System logs time that speed changed
  Document location of device
Notes: Key Message: Talk about the concerns with this project.
Background Information: We will first talk about static variable speed limit signs and then we will be discussing dynamic variable speed limit signs.
One of the work zone issues we have looked at is queuing. In regard to variable speed limits, we are looking primarily at projects where queuing is not a risk. If you have roughly 1800 vehicles per hour, per lane and no significant grades, you have a low risk of queuing.
We have analyzed speed harmonization, so you know that we want all the vehicles going plus or minus 15 miles per hour from the 85th percentile speed. Research shows that speed variations plus and minus 15 mph is reasonably safe.
But if we are changing the regulatory speed, then the speed needs to be enforceable. That means we need to know:
Where the sign is located,
What the sign is displaying at any given time, and
When changes to the speed limit become are made.
These are the three big concerns with portable variable speed limits because this information must be collected and maintained for court challenges.
Interaction: None
Notes: None

## Slide 6: Success Stories: Beaver Ridge Climbing Lane, Beaver, Utah
I-15 posted speed limit:
  80 mph originally
  Dropped to 65 mph at work zone
        85th percentile: 70 mph
  45 mph allowed during structure work
        85th percentile: 51 mph
  Speed harmonization +/- 12 mph
Image: Utah DOT
Notes: Key Message: Talk about the successes and reduction in speed
Background Information: This has been done successfully using static assembly on five different projects, primarily in southern Utah. On the Beaver Ridge project, where workers were working on a structure without positive protection. Speeds were reduced from 80 mph to 65 at the front of the work zone with a resulting drop to 70 mph. The speed was then dropped to 45 mph with an 85th percentile speed of 51 mph. These were good reductions with speed harmonization also.
Interaction: None
Notes: I-15 / Start Milepost: 98 - End Milepost: 102.93
Structure work refers to structural work on the climbing lane.

## Slide 7: Dynamic Variable Speed Limit (VSL):
Project objectives
  Develop a portable and dynamic system
  Test on two projects in 2016
  Evaluate results and revise requirements
  Test on two projects in 2017
  Bid into future projects
Image: Utah DOT
Notes: Key Message: Introduce concept of dynamic variable speed limit
Background Information: Consultant Developed from an FHWA Grant. The results have talked about have been with a static sign system. Now the focus is on developing a dynamic speed sign system. A consultant was used with funding from an FHWA Grant to study dynamic variable speed limits. The project objectives were:
  Develop a portable and dynamic system
  Test on two projects in 2016
  Evaluate results and revise requirements
  Test on two projects in 2017
  Bid into future projects
Interaction: None
Notes: None

## Slide 8: Goals, Objectives, and Performance Measures (1 of 2)
Source: Utah DOT
Notes: Key Message: Talk about the end goal
Background Information: These are the goals and performance measures set up for the variable dynamic speed system for field or worker personnel. The overriding goal is Zero Fatalities for the work zone, which includes the worker and the public.
The goals in the Field are safety for field personnel, and the secondary measure would be ease of deployment and operation.
For this study implementation, one of the performance measures would be whether the VSL can be adjusted without exposing workers but still work properly. It also must provide the correct speed in the work area, and there must be speed compliance when workers are present. The workers also need to see satisfactory results.
The performance measures for ease of deployment and operation would include the time it takes to set up, adjust, or shift the system in a work zone; the time it takes to learn how to operate the Portable VSL; and the cost of the system.
Interaction: None
Notes: Go through the goals, objectives, and performance measures on the slide.

## Slide 9: Goals, Objectives, and Performance Measures (cont.)
Source: Utah DOT
Notes: Key Message: Review page two of goals and objectives.
Background Information: These are the goals and performance measures set up for the variable dynamic speed system for the motoring public. Again, safety is the overall goal and objective. The speeds should reflect the complexity of the project (type and extent of work), and the system should be easy for the public to understand. Again there are performance measures that will determine whether the system is satisfying the goal, which includes reduced crashes, better speed compliance, and fewer delays.
Interaction: None
Notes: Go through the goals and objectives and performance measures on the slide.

## Slide 10: Implementing a Portable VSL System: Goal
Adjust speed limits based on detected speeds/queue
Provide real-time detection for traffic speed and occupancy (queue):
  Through ACTIVE work space
  In advance of the work space
Provide advanced notification to drivers about variable speed limits
Provide travel time or traffic delay through the work zone
Notes: Key Message: Review needs and wants in the VSL system
Background Information: (Broken into 2 slides) The goals of the portable VSL system are to adjust the speed limits based on detected speeds and/or queue. The system will provide real-time detection of traffic speed through the work space and advance notification to drivers about the VSL. The system will provide monitoring of the work zone and real-time weather detection.
Interaction: None
Notes: Go through the needs and wants on the slide, explain how the goals and objectives were identified and intended to be applied to a VSL system.

## Slide 11: Implementing a Portable VSL System: Objective
Provide surveillance/monitoring capability at the work zone
Provide real-time weather detection
Source: UDOT
Notes: Key Message: Review needs and wants in the VSL system
Background Information: The goals of the portable VSL system are to adjust the speed limits based on detected speeds and/or queue. The system will provide real-time detection of traffic speed through the work space and advance notification to drivers about the VSL. The system will provide monitoring of the work zone and real-time weather detection.
Interaction: None
Notes: Go through the needs and wants on the slide, explain how the goals and objectives were identified and intended to be applied to a VSL system.

## Slide 12: Parameters and Limits: Speeds
Increments
Frequency of posted speed changes
Set work zone speed limit based on prevailing conditions
Source: UDOT
Notes: Key Message: Discuss parameters and limits
Background Information: (Broken into 2 slides) Things to be considered in using VSL are the increments at which you would reduce the speed in using VSL ― typically 5 – 10 mph increments are used, and the frequency of the posted speed changes.
Consider the following speed characteristics: increments, frequency of posted speed changes, and set work zone speed limit based on prevailing conditions. Consider the following spacing characteristics: Between VSL signs and advanced warning signs, variable message signs (VMS) communications, and Maximum distance away from active work zone to display travel time?
Interaction: Question: What would you use to set the work zone speed limit? Answer: motorist speed or speeds based on the work zone conditions. Other considerations include distance between VSL signs and advance warning signs, changeable message sign communications for motorists, and also the location of travel time signing.
Notes: None

## Slide 13: Parameters and Limits: Spacing
Between VSL signs and advance warning signs
Variable message signs (VMS) communications
Maximum distance away from active work zone to display the real-time speed limit
Notes: Key Message: Discuss parameters and limits
Background Information: (Broken into 2 slides) Things to be considered in using VSL are the increments at which you would reduce the speed in using VSL ― typically 5 – 10 mph increments are used, and the frequency of the posted speed changes.
Consider the following speed characteristics: increments, frequency of posted speed changes, and set work zone speed limit based on prevailing conditions. Consider the following spacing characteristics: Between VSL signs and advanced warning signs, variable message signs (VMS) communications, and Maximum distance away from active work zone to display travel time?
Interaction: Question: What would you use to set the work zone speed limit? Answer: motorist speed or speeds based on the work zone conditions. Other considerations include distance between VSL signs and advance warning signs, changeable message sign communications for motorists, and also the location of travel time signing.
Notes: VMS = permanent CMS

## Slide 14: Special Provisions for VSL (1 of 2)
Source: UDOT
Notes: Key Message: Review special provisions
Background Information: This is a standard detail sheet that has been developed and used for the VSL.
Interaction: None
Notes: Need printout of this sheet to add into the materials for participants to review. Have student see sheets in the appendix.

## Slide 15: Special Provisions for VSL (2 of 2)
Source: UDOT
Notes: Key Message: Review special provisions
Background Information: This is a supplemental detail for a shorter term work zone.
Interaction: None.
Notes: Need printout of this sheet to add into the materials for participants to review. Have student see sheets in the appendix.

## Slide 16: Portable VSL Primary Candidate Projects
Multilane divided or undivided highway
  Single or dual lane closure
High speed (> 50 mph)
Simple geometry
Example
  Roadway resurfacing
  Slab replacement
  Patching
Notes: Key Message: Characteristics of good candidate projects for this type of solution.
Background Information: Criteria for candidate projects for using a portable VSL system were established which included:
  Lane divided or three or four lane undivided roads
    -Single or dual lane closure
  High speed (50 mph +)
  Project with simple geometries
  Example
    -Roadway resurfacing
    -Slab replacement
    -Patching
Interaction: Do you all have any similar situation where you could use this solution?
Notes: Go through the slide.

## Slide 17: Future Portable VSL Considerations
Anticipate broadening the circumstances where the system will be deployed
  Only doing the pilot on these “parameters” for now
Parameters not in 1st deployment:
  Higher-volume roadways
  Higher-profile roadways (political attention)
  Variable characteristics
    Curvature, sight distance,
    Proximity to signals, access
    Others
Notes: Key Message: discuss the future portability of VSL and the considerations associated with VSL
Background Information: VSL considerations for future deployments would include broadening the circumstances where the system would be deployed, but for now would only use the previously listed type of projects. Future considerations would include higher volume roadways and higher profile roadways -- those which could draw political attention. Roadways with more geometric characteristics could also be considered.
Interaction: None
Notes: None.

## Slide 18: Component Parts
Portable VSL (PVSL) signs
Portable Changeable Message Sign (PCMS)
Mainline detection by lane
Wireless communication
Road weather information system (RWIS) and closed-circuit TV (CCTV) - not included
Notes: Key Message: discuss the component parts that go into the system
Background Information: VSL systems use the listed technologies:
Portable VSL (PSVL) Signs
Portable Changeable Message Sign (PCMS) = PVMS for variable
Mainline detection by lane
Wireless communication
RWIS and CCTV –not included
For this test project we are going to rely on cellular communication through an off-site computer.
Interaction: None
Notes: None

## Slide 19: System Architecture Diagram
Source: UDOT
Notes: Key Message: Describe the system architecture
Background Information: This is a schematic of the site control system to be used. As a test project it goes through a human operator considered as a safety net. In the future, with proven success in using the system, it would do everything for you.
Interaction: None
Notes: None

## Slide 20: Typical VSL Signing
Source: UDOT
Notes: Key Message: Introduce the typical signage associated with VSL
Background Information: This is the schematic of the signs we would place. There may be a VSL sign upstream. If you're anticipating queuing within your project, you would repeat that regulatory sign and another sign upstream.
Interaction: None
Notes: Provide handout and review handout.

## Slide 21: Typical VSL Downstream Set Up
Source: UDOT
Notes: Key Message: review typical setup
Background Information: This is a downstream setup with a longer work zone. Speed is reduced at the end of the taper.
Interaction: None
Notes: Provide handout and review handout

## Slide 22: Example #2: Maryland Dynamic Lane Merge (DLM)
Source: workzonesafety.org
Notes: Key Message: Introduce Example from Maryland
Background Information: The Maryland Lane merge example is set up to be a dynamic system that alternates between the early merge and the late merge system. (The zipper merge is primarily a late merge example.)
Interaction: None
Notes: None

## Slide 23: Maryland DLM Test Deployment
Maryland SHA and University of Maryland partnership
Test section on I-83 north of Baltimore
  Four-lane divided freeway
  Average Daily Traffic (ADT) of 61,140 vpd (2014)
  Southbound only work zone
  Right lane closure
Notes: Key Message: describe case study
Background Information: The test section for this project was a segment of I-83, which is a north-south freeway out of Baltimore, Maryland. It is heavily traveled with solid traffic volume. It is a four-lane divided freeway. The traffic is very peaky in this area and as such warrants a dynamic system that was designed to handle both conditions.
Interaction: None
Notes: SHA = Maryland State Highway Administration, ADT = Average daily traffic

## Slide 24: System Configuration
Source: MDSHA
Notes: Key Message: talk about system configuration
Background Information: This system was laid out to combine the standard signing required for a lane closure in a work zone that directs the driver to merge. The sign is designed to display a selected message depending on whether people are to merge early or merge late. This example is showing basically an extension of the late merge.
Interaction: None
Notes: None. May need to have printout.

## Slide 25: Operation – Low Volume
“All On - All Off” algorithm
If all occupancies are below 5%, all PCMS are deactivated
Source: MDSHA
Notes: Key Message: Illustration of low volume operations.
Background Information: PCMS boards should not conflict with the road signage but rather provide supplementary guidance. The system is designed to work with a series of different algorithms. It can be an “all on” or “all off” type of situation: using both lanes all the way up to the merge point, or encouraging an early merge. It can also be set to a dynamic reading telling people to use both lanes up to a certain point, and then encouraging a merge based on the volume. It could be set to be time based, so that at a certain time of day it switches from one mode of operation to another. It could also switch from an early merge to a late merge, as in the example.
The same pattern could be carried back as far as you need it, depending on the anticipated length of queue. The evaluation that Maryland did for this particular implementation uses both a manual data collection component and a simulated data component.
Interaction: None
Notes: If occupancy is between 5% and 15%, are the sensors on or off?

## Slide 26: Operation – High Volume
If any occupancy among the sensors is over 15 percent, all PCMS are activated
Source: MDSHA
Notes: Key Message: Illustration of high volume operations.
Background Information: This shows how all the PCMS are activated when there is a high volume of traffic and the late merge is being used.
Interaction: None
Notes: None

## Slide 27: Evaluation - Methodology
Manual data collection
  Work zone throughputs, lane volume distributions, and queues
  Obtained for no-control baseline and during DLM operation
Simulation calibrated to no-control baseline conditions
Simulated no-control throughput & queues based on upstream volumes measures during DLM operation
Notes: Key Message: Discuss the methodology for evaluating the performance of the Maryland DLM test deployment.
Background Information: The evaluation that Maryland performed for this particular implementation incorporated both a manual data collection component and a simulated data component. The reason for this is that the agency was able to collect manual data for a no dynamic merge condition as a
baseline. Once the dynamic merge system was in place, Maryland wanted to be able to compare the observed conditions using the dynamic merge to the condition without dynamic merge. They set up a simulation model based on the baseline conditions that incorporated manually collected data. The simulation could then be used to model what would have happened given the initial inputs of how much traffic was coming into the work zone.
Interaction: None
Notes: None

## Slide 28: Evaluation - Results
Throughput
Source: MDSHA
Notes: Key Message: discuss increased throughput
Background Information: These results are fairly promising. Throughput increased significantly, from 9% to 34% depending on the day the system was used. These are based on the manual traffic count for the DLM throughput as compared to the simulated throughput based on the no control scenario.
Interaction: None
Notes: None

## Slide 29: Evaluation - Results
Maximum Queue Lengths
Source: MDSHA
Notes: Key Message: talk about reduction in queue length
Background Information: The maximum queue lengths show a similar promise. There is a significant reduction of the queue length. The typical cues without a dynamic merge run from 1.5 to 2 miles. These are reduce by 15% to 20% with the dynamic lane merge.
Interaction: None
Notes: None

## Slide 30: Evaluation - Results
Lane Volume Distribution
Source: MDSHA
Notes: Key Message: review the lane distribution of two scenarios
Background Information: The other important element is the uniformity of traffic conditions between the two lanes. It's the question of speed differential, if you have a lot of traffic traveling in one lane at a low speed, and another lane traveling at a high speed there are a lot of safety concerns. The dynamic Lane merge showed a significant improvement in uniform Lane distribution relative to the situation without the dynamic Lane merge. That was another positive finding of this experiment.
Interaction: None
Notes: None

## Slide 31: Example #3: Queue Warning Systems
Used to alert drivers to traffic conditions (e.g., stopped traffic, slowing traffic) ahead
Reduce the number and severity of rear-end crashes
Avoid drivers being surprised by stopped or slowing traffic
Image: FHWA
Notes: Key Message: Innovative approaches to reducing crashes and congestion can include tools such as queue wrning systems.
Background Information: Queue warning systems (QWS) are one of the tools in the technology applications toolkit. QWS are geared towards alerting drivers about downstream reductions in speed when there is a work zone with a capacity constraint. In the worst case, you have a queue of traffic forming that can go beyond the initial warning signs. When that happens you have a dangerous condition where cars are traveling at freeway speed and all of a sudden they encounter a stopped or slowed queue of traffic with no warning. It's obviously a dangerous situation, particularly when large trucks are in the mix because truck take longer to come to a stop. The last thing you want is a car traveling at freeway speed or a truck traveling at freeway speed running into the back of a stopped queue. It is one of the more significant work zone safety issues that agencies face and try to mitigate.
Interaction: None
Notes: None

## Slide 32: Queue Warning System Components
Sensors
Portable changeable message signs (PCMS)
Cameras
Rumble strips
Images: FHWA
Images: FHWA
Notes: Key Message: A number of system components make up a QWS.
Background Information: QWS components consist of:
Sensors
Portable changeable message signs (PCMS)
Cameras
Rumble Strips
Interaction: None
Notes: None

## Slide 33: I-35 Construction Corridor, Central Texas
$2.1 billion effort
17 sections
96 miles
Multiple projects active at one time
ADT: 70K – 110K vpd
~ 66% through traffic
> 75% trucks at night
Notes: Key Message: Provide an overview of example in Texas.
Background Information:
An overview of the QWS planning, design, implementation and effectiveness on the I-35 project in central Texas.
Commitment to rebuild any remaining section of I-35 that is not at least three lanes in each direction around the Waco district.
Fairly rural part of the state, contains a lot of through traffic with large trucks.
Interaction: None
Notes: None

## Slide 34: I-35 Construction Traveler Information System Components
Real-time queue warning
Lane and road closure information
Current travel time information
Expected construction delay information
Volume and spot speed data
Traffic cameras at high incident locations
Dynamic message signs
Notes: Key Message: Summarize the traveler information system components of the Texas QWS.
Background Information: The I-35 project used numerous traveler information system components which include:
Real-time queue warning
Lane and road closure information
Current travel time information
Expected construction delay information
Volume and spot speed data
Traffic cameras at high incident locations
Dynamic message signs
Interaction: None
Notes: None

## Slide 35: User Needs Analysis: Travelers
Many long-distance travelers
Normally uncongested, especially at night
Nighttime lane closures would create queues in some cases
Queues would be unexpected
Notes: Key Message: Summarize findings of the user needs analysis.
Background Information: (broken into 2 slides)
When assessing road users’ needs and expectations:
The first step is to understand the makeup of the traffic: there would be a lot of long-distance travelers traveling at high speeds.
Any lane closures would have to occur at night to mitigate the potential for significant delays, but there would still be some level of queuing, which the travelers would not expect. In some locations, the queuing would be more significant, lasting several hours and extending several miles.
The needs of the contractors and DOT include:
Meeting an aggressive contract schedule with work going on simultaneously throughout the project limits, including in the median and between frontage roads.
Being able to move equipment into and out of the work zone, which could be impacted by traffic and could be difficult at times.
Being able to vary lane closures based on time, location, and duration due to the work schedule. Lane closures could occur at one location nightly for a week and then be at another location for a few days. Predicting which lane closures would create queues would be difficult.
Interaction: None
Notes: None

## Slide 36: User Needs Analysis: TxDOT and Contractors
Aggressive construction schedule
Equipment in right-of-way (ROW) would adversely affect progress
Lane closures infrequent at any one location
Not all lane closures will create queues
Notes: Key Message: Summarize findings of the user needs analysis.
Background Information: (broken into 2 slides)
When assessing road users’ needs and expectations:
The first step is to understand the makeup of the traffic: there would be a lot of long-distance travelers traveling at high speeds.
Any lane closures would have to occur at night to mitigate the potential for significant delays, but there would still be some level of queuing, which the travelers would not expect. In some locations, the queuing would be more significant, lasting several hours and extending several miles.
The needs of the contractors and DOT include:
Meeting an aggressive contract schedule with work going on simultaneously throughout the project limits, including in the median and between frontage roads.
Being able to move equipment into and out of the work zone, which could be impacted by traffic and could be difficult at times.
Being able to vary lane closures based on time, location, and duration due to the work schedule. Lane closures could occur at one location nightly for a week and then be at another location for a few days. Predicting which lane closures would create queues would be difficult.
Interaction: None
Notes: None

## Slide 37: Concept of Operations
A highly-portable end-of-queue warning system
  Deploy at each lane closure where queue is expected, remove devices when the need for the lane closure ends
  Scale deployment to queue expectations
Source: TxDOT
Notes: Key Message: introduce how system works
There would be quite a few lane closures distributed up and down the corridor.
As a result, placing a lot of ITS equipment to try to capture all of that in a stationary environment was not going to be feasible. The concept of operations was to try to deploy something very portable.
Background Information:
A couple vendors had some equipment that could be deployed quickly and picked up equally quickly.
The queue warning system would provide a fairly accurate detection of queues and subsequent notification of the presence of the queue upstream.
DOT and contractor agreed to use a system that could be put out where and when it was needed and picked up when not in use.
Interaction: None
Notes: None

## Slide 38: System Design Needs
Method of identifying when and where lane closures will occur
Method for quickly assessing queue potential and expected maximum length
Determine optimum queue detection and warning configuration
Method for increasing likelihood of motorist receiving queue warning information
Notes: Key Message: Discuss the four key system design needs identified.
Background Information: There are four key items that had to be addressed:
Needed to be able to determine when and where lane closures would occur given that there were multiple contractors working in multiple locations in the corridor. Needed a way to keep track of lane closures, a mechanism for notification, and information about when and where they're going to be.
Based on this information, needed to determine whether the planned closures would be locations where there might a chance that a queue would form.
Needed to determine a configuration for the actual system itself. How far back was system needed? What are the thresholds for activating?
Needed recognizing that people are very set in their driving mode and probably not paying attention. Need to make sure motorist see the messages and know that there is a queue ahead.
Interaction: None
Notes: None

## Slide 39: Identifying When and Where Lane Closures will Occur
Source: TxDOT
Notes: Key Message: introduce tool for how project identifies the need for a system
Background Information: As far as notifying or identifying when a where laying closures occur, a notification system was established.
Some of the coding was borrowed from the Houston district TxDOT operations had a module for keeping track of incidents and lane closures as part of their day-to-day traffic management capabilities. It was modified a little bit and used for the I-35 corridor as a way to track and identify precisely when, where, and in what direction the lane closures would occur.
Interaction: None
Notes: None

## Slide 40: Assessing Potential for Queues (1 of 2)
Simple input-output analysis used
  Real-time volume data at some locations
  Assumed hourly distributions of Average Annual Daily Traffic (AADT) values
  Estimates of work zone capacity
    Highway Capacity Manual (HCM)
    Sample counts
Process automated to occur whenever a lane closure was entered or modified
Notes: Key Message: introduce the analysis for a potential of a queue
Background Information:
As far as the assessment, the corridor does not have a lot of feasible alternative routes. Ramp spacing is far apart. The corridor operates almost like a pipeline. A very simple input-output analysis was used to decide whether or not a queue would form.
This process was integrated into the notification subsystem so that it could generate an estimate of whether a queue would occur and how far back.
Interaction: None
Notes: None

## Slide 41: Assessing Potential for Queues (2 of 2)
Source: TxDOT
Notes: Key Message: review output of tool
Background Information:
In addition to a best estimate, the analysis recognized that volumes fluctuate from night to night and factored in increased demand to create a greater cushion as a way of improving safety. This gave everyone a little bit more comfort level with being ready to deal with variations.
Interaction: None
Notes: None

## Slide 42: Queue Warning System Configuration (1 of 3)
Simulation analyses performed to evaluate:
  Sensor spacing
  Sensor location
  System update frequency
  Logic thresholds for queue detection
Notes: Key Message: introduce system configuration
Background Information:
Simulation analyses were performed to determine sensor spacing, sensor location, system frequency update and queue detection logic thresholds.
Interaction: None
Notes: None

## Slide 43: Queue Warning System Configuration (2 of 3)
Source: TxDOT
Notes: Key Message: This slide summarizes the details on sensor spacing, etc.
Background Information:
The configuration is like you see here, putting a sensor right at the lane closure bottleneck location. The beginning of the merge is very critical because that is where we expect a queue to start. Even for a very brief queue there would be a high probability of detecting it. Another sensor was needed to verify and check the potential for congestion.
Once a queue got beyond that sensor, increasing the spacing to about a mile apart was deemed satisfactory for performance purposes. You probably can't read the table, but the table shows the spacing of sensors and what the appropriate traffic message would be on the warning message upstream.
One way to get people to wake up and see the warning message if it was active was the use of some rumble strips. One set of rumbles was upstream of the sign, and the other was positioned where it was expected that the farthest end of queue would occur, so that there would be auditory and vibratory alert to drivers in addition to the warning message displayed there.
Interaction: None
Notes: None

## Slide 44: Queue Warning System Configuration (3 of 3)
Source: TxDOT
Notes: Key Message: system configuration
Background Information:
Ultimately went with a simple plan and then a more extensive plan in case the queues extended longer than anticipated.
This is often referred to as a plan one. It is basically something that will protect up to 3 ½ miles of queuing, but the idea is to keep it within 2 ½ miles.
If the maximum queue went beyond the 3 ½ miles, there would be a second message board with additional sensors, and this would be something that would provide queue warning all the way up to a queue that may grow to 7 ½ miles. Theoretically you could extend this in an incremental fashion even if you thought it would be a 13 mile queue by replicating and moving backwards.
Interaction: None
Notes: None

## Slide 45: Procurement
Indirect purchase through construction contracts
Original plan: bid on a per-deployment basis
Switched to mobilization plus a per-night deployment bid
First systems change ordered into existing contracts, included in latter projects as bid items
Notes: Key Message: how the system was procured
Background Information:
As far as a procurement, it was tied directly to contractor decisions on when and where they wanted to close lanes; i.e., they were deployed as an indirect procurement by the contractor through the construction contracts themselves.
The initial plan was to have the bids on a per night or per deployment basis, but when the agency found that the contractors were not comfortable and had not used the technology enough to be able to provide comparative bids, they went with the deployment or bid mechanism of a mobilization price for the equipment itself and then an each-per-deployment price for the additional time for taking out and bringing back. The original deployments had to be change ordered because a couple of contracts were already in place.
They were included as regular bid items in the latter projects that were left.
Interaction: None
Notes: None

## Slide 46: Deployment
Began use in 2013 (300+ deployments to date)
Systems shared between contractors
  Several used same TTC subcontractor
Notes: Key Message: provide information on the deployment of this system
Background Information:
The same subcontractor was used on many projects. Each contractor would bid their deployment night costs and then depending on whether they asked for a system or not they would provide the mobilization costs. They put out more than 300 lane closure nights to date.
Interaction: None
Notes: None

## Slide 47: Effectiveness of System
Across approximately 200 deployment nights:
  Total crashes reduced by 18 to 45%
  Crash cost reduced between $6,600 and $10,000 per night
Source: TxDOT
Notes: Key Message: discuss effectiveness of systems
Background Information:
The results have been positive across 200 deployment nights, with less than one year’s worth of exposure.
Crash reductions from what was expected if a system was not deployed: total crashes reduced 18% to 45%.
The crashes that did occur were less severe. Also, fewer of them ended up being the rear-end crash type.
It does show that the systems are affecting driver behavior at least with the data so far and have had a positive effect.
Amortized the benefits show $6,600 to $10,000 in crash cost reductions per night.
Interaction: None
Notes: What are these percentages of in the chart? 58% of what? Answer, Normal work zone measures in place without a End of Queue (EOQ) warning system.

## Slide 48: Example 3 a: Queue Warning Systems- Illinois DOT
Background information:
Source: The Southern
Notes: Key Message: introduce example 3 in Illinois
Background Information: In July 2010, a seven-vehicle, multiple-fatality crash occurred in a very rural section of Illinois on I-57. This accident occurred in the queue of an Illinois DOT research project and involved four tractor trailers.
Interaction: None
Notes: None

## Slide 49: Illinois DOT - I-55 (I-70 to IL 140)
Madison County, IL
30 miles of bi-directional mainline interstate on I-55
Rubblizing, resurfacing, and bridge work
Nov. 2010 – Jun. 2012
Source: IDOT
Notes: Key Message: provide background of Illinois project
Background Information: At that same time the DOT was preparing plans for a rehabilitation project along a busy corridor of two lanes of I-55 between St. Louis and Chicago. It involved maintaining one lane of traffic and, due to the anticipated delays, it required the contractor to work 24/7. The agency also had two ongoing projects that involved significant lane closures along that same corridor.
Interaction: None
Notes: Rubblization is a construction and engineering technique that involves saving time and transportation costs by reducing existing concrete into rubble at its current location rather than hauling it to another location.

## Slide 50: Two Directives For This Project After End-of-Queue Crash
Reduce risk of similar crashes
Better inform traveling public about delays and help with options to minimize delays
Notes: Key Message: goal and reason for system
Background Information:
Regional engineer provided design group with two directives:
Reduce risk of accident like on I-57.
Better inform traveling public about delays and help with options to minimize delays.
Interaction: None
Notes: None

## Slide 51: Smart Traffic Monitoring Special Provision Requirements
Collect real-time traffic data
Analyze data via control software
Alert drivers of:
  Magnitude of delay
  Stopped traffic conditions and
  Alternate route options
Source: IDOT
Notes: Key Message: review objectives of system
Background Information: For this project a smart traffic monitoring special provision was developed that:
Collected real-time vehicle data
Analyzed data via control software
Alerted drivers of delay times, stopped traffic conditions, and alternate route options
Interaction: None
Notes: None

## Slide 52: Equipment Procurement
Researched and interviewed several ITS Smart Work Zone companies
Developed a Contract Special Provision and Plan Sheet Addendum
Allowed at least 2 bidders to meet the specification
Notes: Key Message: introduce how system was procured
Background Information: The system included coverage of the contract project limits but also included smart zone coverage over all the projects shown on the earlier slide. To procure the equipment, the agency identified and interviewed several ITS Smart Work Zone companies. A contract Special Provision and Plan Sheet Addendum were developed for the projects, and at least two bidders were allowed to bid to meet the specifications.
Interaction: None
Notes: None

## Slide 53: Deployment
73 PCMS (One per mile each direction and at crossroads)
56 Doppler speed sensors
6-mile lead in each direction
Source: IDOT
Notes: Key Message: talk about system deployment
Background Information: The system covered over 30 miles of interstate utilizing portable changeable message signs, one every mile in each direction, with several at every traffic decision point, (interchanges). This included 73 PCMS at 1 per mile in each direction and at cross roads, with 56 Doppler speed sensors with a 6 mile lead in each direction.
Interaction: None
Notes: None

## Slide 54: System Operation
Drivers alerted 1 and 2 miles upstream of any detected queue
If below 40 mph, alternating
  “STOPPED TRAFFIC AHEAD” and
  “BE PREPARED TO STOP”
Provided anticipated magnitude of delay at the approach to each work zone and every traffic decision point
Notes: Key Message: system operation
Background Information: For the system operation, drivers were alerted 1 to 2 miles upstream of any detected queue with alternating “stopped Traffic Ahead” and “Be Prepared to Stop” messages being displayed when traffic slowed below 40 mph. Anticipated delay times were provided at the approach and at every decision point.
Interaction: None
Notes: None

## Slide 55: 2010 and 2011 Construction Seasons
Source: IDOT
Notes: Key Message: when and where system was deployed
Background Information: This map shows the various projects. Note that the 2010 season did not have a smart work zone in place. During the 2011 season, a smart work zone was in place and operational during the entire construction season.
Interaction: None
Notes: None

## Slide 56: 2010 Construction Season
Source: IDOT
Notes: Key Message: where the system was used in 2010
Background Information: Another map showing on only the 2010 construction season, when no smart work zone technology was used.
Interaction: None
Notes: None

## Slide 57: 2011 Construction Season
Source: IDOT
Notes: Key Message: where the system was deployed in 2011
Background Information: The 2011 construction season with smart work zones used on all projects.
Interaction: None
Notes: None

## Slide 58: System Evaluation
Compared 2010 and 2011 construction years for 5 projects along I-55
Only looked at rear-end accidents because that is what system was setup to reduce
Notes: Key Message: review system evaluation
Background Information: (Broken into 2 slides) This shows the difference in the accidents between the two years. If you notice there were 185 more lane closure days in 2011 (with increased vehicle exposure) than in 2010. There were decreases in various accident types ranging from 11% to 15% for the year smart work zone technology was used.
Interaction: None
Notes: None

## Slide 59: System Evaluation
Source: IDOT
Notes: Key Message: review system evaluation
Background Information: This shows the difference in the accidents between the two years. If you notice there were 185 more lane closure days in 2011 (with increased vehicle exposure) than in 2010. There were decreases in various accident types ranging from 11% to 15% for the year smart work zone technology was used.
Interaction: None
Notes: None

## Slide 60: Lessons Learned
Develop statewide tiered special provisions that will allow for competition between all SWZ systems
Establish guidelines for utilization of tiered SWZ systems
Recognize that no system is perfect at this point
SWZ costs average 2.5% of our contract costs
SWZ can reduce queuing type crashes
Notes: Key Message: review lessons learned from these deployments
Background Information: Lessons learned on this contract are:
Develop statewide tiered special provisions that will allow for competition between all SWZ systems
Establish guidelines for utilization of tiered SWZ systems
Recognize that no system is perfect at this point
Smart Work Zone costs average 2.5% of our contract costs
Smart Work Zones can reduce queuing type accidents
Interaction: None
Notes: None

## Slide 61: For Further Information
To look at other SWZ technology that has been used by other states, go the National Work Zone Clearinghouse at:
https://www.workzonesafety.org/swz
https://www.workzonesafety.org/swz/webinars/

## Slide 62: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: If no questions, you may ask a few yourself.