## Slide 1: 2. Technology Applications and Work Zone ITS Implementation Guide
Smarter Work Zones
Image: ATSSA
Notes: Key Message: We will begin by looking at Technology applications and the work zone ITS Implementation
Guide.
Background Information: This module is scheduled to last a few hours and there will be intermittent breaks during this module.
Interaction: None
Notes: This module walks participants through the Work Zone Intelligent Transportation Systems Implementation Guide, FHWA 2014 on how to select and maintain ITS solutions in work zones.

## Slide 2: Module Objectives
Define Smarter Work Zones
Discuss the technologies used for work zone ITS
List the six steps within the ITS Implementation Guide
Notes: Key Message: Review the FHWA SWZ Initiatives
Background Information: In 2015, FHWA selected Smarter Work Zones as a topic for the Every Day Counts Initiative. Through this initiative, two strategies were identified with the first being project coordination. Project coordination is defined as coordination within a single project and among multiple projects within a corridor, network or region to minimize the collective impact of work zone congestion. This coordination could cross agency jurisdictions. This will be discussed in future modules.
The second strategy is technology application, specifically, the use of Intelligent Transportation Systems (ITS) to enable dynamic management of work zone traffic impacts, such as queue and speed management.
Interaction: N/A
Notes: We will now discuss the Technology Application initiative goals and strategies.

## Slide 3: Every Day Counts Initiative Identified Two Smarter Work Zone Initiatives:
Project Coordination
Technology Application (focus of this module)
Image: FHWA
Notes: Key Message: Review the FHWA SWZ Initiatives
Background Information: (Intro slide broken into the following two slides) In 2015, FHWA selected Smarter Work Zones as a topic for the Every Day Counts Initiative. Through this initiative, two strategies were identified with the first being project coordination. Project coordination and technology application. Let’s look at them.
Interaction: N/A
Notes: We will now discuss the Technology Application initiative goals and strategies.

## Slide 4: Project Coordination
Coordination within a single project and among multiple projects within:
  A corridor
  A network, or
  A region and
  Possibly across agency jurisdictions
Image: ATSSA
Notes: Key Message: Review the FHWA SWZ Initiatives
Background Information: Project coordination is defined as coordination within a single project and among multiple projects within a corridor, network or region to minimize the collective impact of work zone congestion. This coordination could cross agency jurisdictions. This will be discussed in future modules.
Interaction: N/A
Notes: We will now discuss the Technology Application initiative goals and strategies.

## Slide 5: Technology Application (focus of this module)
Deployment of ITS for dynamic management of work zone traffic impacts, such as:
  Queue and
  Speed management to provide actionable information to drivers and traffic managers
Notes: Key Message: Review the FHWA SWZ Initiatives
Background Information: The second strategy is technology application, specifically, the use of Intelligent Transportation Systems (ITS) to enable dynamic management of work zone traffic impacts, such as queue and speed management.
Interaction: N/A
Notes: We will now discuss the Technology Application initiative goals and strategies.

## Slide 6: What is Work Zone ITS?
Using technology to support effective work zone management and operations
Use of communications-based information and electronics technologies for work zones
  With portable and temporary components that may be combined with permanent ITS
Image: FHWA
Notes: Key Message: Define Work Zone ITS
Background Information: (broken onto two slides) What are ITS technology applications? Lets expand on what we mean by that. Everybody is familiar with ITS and we have all used ITS to some degree on works on projects. But, for the smarter work zone initiative, we are thinking of ITS as moving beyond dragging out a PCMS to a work zone and flashing “roadwork ahead” out there. The idea is to use data from the field to generate actionable information that can actually guide driver behavior so they can react better to work zone-related congestion. This also gives traffic managers a tool to help them better understand what is happening in the field and what they can do to better manage the work zone or measure the performance of the work zone as a lesson for future deployments. The concept of technology application is more of a data- focused strategy for managing work zones and congestion.
Interaction: Ask the audience what types of ITS they have used. Dig in and ask why did they use ITS, did it work, would they use it in the future.
Notes: None

## Slide 7: What is Work Zone ITS? (cont.)
Using real-time data for traffic managers and drivers regarding work zone traffic conditions
Software that processes and analyzes data to be used by other components and users
Image: FHWA
Notes: Key Message: Define Work Zone ITS
Background Information: (broken onto two slides) What are ITS technology applications? Lets expand on what we mean by that. Everybody is familiar with ITS and we have all used ITS to some degree on works on projects. But, for the smarter work zone initiative, we are thinking of ITS as moving beyond dragging out a PCMS to a work zone and flashing “roadwork ahead” out there. The idea is to use data from the field to generate actionable information that can actually guide driver behavior so they can react better to work zone-related congestion. This also gives traffic managers a tool to help them better understand what is happening in the field and what they can do to better manage the work zone or measure the performance of the work zone as a lesson for future deployments. The concept of technology application is more of a data- focused strategy for managing work zones and congestion. Example of other components and users include for instance queue detection software.
Interaction: Ask the audience what types of ITS they have used. Dig in and ask why did they use ITS, did it work, would they use it in the future.
Notes: None

## Slide 8: Work Zone ITS Has Evolved
Historically
  Handful of companies
  Many were first time deployments and prototypes
Today
  Mature industry
  More reliable ITS components and ability to leverage permanent ITS
  More successful deployments with documented results
Notes: Key Message: Review were we have come from
Background Information: Historically there have been a handful of companies could supply a “system” to do something. Typically, the systems were not very flexible and solution driven. Throughout the years, there were many prototypes. Each deployment was an adventure that led to unsatisfactory results, which may have created a bad impression to management. In the end, ITS may not have provided a big bang for the buck.
Today, determine what you want the system to do and it can basically do it. The industry overall has matured and learned from their mistakes. The components are more reliable and flexible depending the application, which can also link to existing infrastructure and permanent ITS. Greater system capability leading to more successful deployments which have been Tested, refined, and proven systems with documented benefits exist that show positive results.
Interaction: Has your state had any work zone ITS that didn’t work as anticipated?
Notes: Briefly, go over the history and where the industry stands now

## Slide 9: Work Zone Challenges
Congestion and delay
Safety
  Speed management
  Crashes
  Ingress and egress of construction vehicles
  Incident detection and response including secondary incidents
Customer dissatisfaction
Contractor performance
Notes: Key Message: List the work zone challenges
Background Information:
Congestion and delay: excess capacity is disappearing as more volumes are on the roadway and as the work zone takes away lanes the overall capacity of the roadway is reduced, but the demand is typically the same. Lane closures and lane restrictions reduce the overall capacity which recreates congestion and delay. This congestion creates queues that have to be estimated to ensure adequate warning is provided to oncoming traffic.
  Safety: Safety is a concern for both the worker and the motorists. The safety challenge encompasses the overall safe speed of motorist and determining the appropriate speed limit, incorporating elements within your work zone to manage the overall speeds of motorists, incident detection and response as well as secondary crashes and notifying motorists of slow moving construction vehicles entering and existing the work space.
  Customer Dissatisfaction: unhappy motorist because of lengthy queues, unexpected detours, and unreliable travel times due to lane closures, other construction-related delays.
  Contractor performance: agencies may impose penalties to contractors for creating excessive delays or queues during a project, but may not have the personnel available to monitor work zone activities continuously to verify compliance.
Interaction: none.
Notes: Go over each point.

## Slide 10: Capabilities of Work Zone ITS Applications
Improve driver awareness
Dynamic and actionable guidance to drivers
Tools for on-site traffic management
  Speed monitoring
  Automated speed enforcement
  Queue formation
Image: ATSSA
Notes: Key Message: Provide an overview of some of the capabilities of work zone ITS applications
Background Information:
Improve driver awareness during complex situations including changing traffic patterns, downstream congestion, construction vehicle ingress/egress, and expected delay and possibly travel times
Provide real time dynamic and actionable guidance to drivers, for example “Road work ahead” vs “Traffic Stopped 1 mile ahead” or “Road work – expect delays” vs. “Road Work I-95 past Exit 52”
Utilizing tools that are available to enhance information to DOT staff to make informed decisions based on data
Interaction: None
Notes: None

## Slide 11: Benefits of Using Work Zone ITS
A study of successful deployments showed that:
  50% to 85% of drivers surveyed said they changed their route in response to the info provided by the work zone ITS
  Queue length reductions up to 50% are possible
  There have been up to 45% fewer crashes than expected at work zones with nighttime lane closures where queues were expected
Source: workzonesafety.org
Notes: Key Message: Introduce some potential benefits of work zone ITS
Background Information:
Benefits from ITS implementation guide on page 4:
The use of an incident management system in New Mexico work zone reduced average incident clearance time by 20 minutes and is believed to have reduced frequency of secondary crashes
Real-time traveler information induced up to 19% diversion away from a route with a work zone in California
Work zone ITS can be deployed to monitor and archive traffic conditions continuously, and the resulting data can assist agencies in imposing penalties on contractors for creating excessive delays or queues during a project.
In Little Rock Arkansas, 82% of drivers surveyed agreed that an Automated Work Zone Information System improved their ability to react to slow or stopped traffic.
Interaction: None
Notes: Source for crash reduction statistic: https://www.workzonesafety.org/files/documents/training/courses_programs/rsa_program/RSP_Guidance_Documents_Download/RSP_EndOfQueueWarning_Guidance_Download.pdf

## Slide 12: Benefits of Technology Applications
Empowers drivers to be proactive
Streamlines traffic management functions through partial automation
Information increases customer satisfaction
Notes: Key Message: Continue covering benefits of ITS
Background Information:
Empowers drivers to be proactive in responding to work zones by providing awareness to motorists of downstream hazards and facilitates real-time decision-making and trip planning to allow drivers to divert from their original path and save time.
Streamlines traffic management functions through partial automation of speed enforcement, data collection, and performance measurement
Information increases customer satisfaction by allowing them to make their own informed decisions.
Interaction: None
Notes: None

## Slide 13: ITS Applications in Work Zones
Traffic monitoring and management
Traveler information
Queue detection and warning
Incident detection and management
Speed management and enforcement
Worker safety
Performance monitoring
Notes: Key Message: ITS Applications in work zones
Background Information: ITS is being used in work zones for these applications.
Interaction: Ask audience which types of ITS they have used.
Notes: None

## Slide 14: Work Zone ITS Components
Sensors for real-time data collection
Communications equipment
Software to process and analyze data
Equipment that uses data to:
  Provide real time information to road users
  Implement work zone management decisions
Notes: Key Message: Cover the typical components to an ITS system
Background Information:
Work Zone ITS components perform the following functions: Collect data such as vehicle speeds and vehicle presence, Verify the accuracy of data, Transmit the data to other system components, Store and manage data for other contract performance requirements, Analyze the data to provide the proper instructions or information to give road users, and Provide real-time video of the work zone to aid decision making regarding lane closures or incident management response
These systems generally include:
• Detection components used to collect roadway data, which may include Acoustic, Global Position Systems (GPS), Infrared, Magnetic, Microwave, Piezo-electric, Pneumatic road tubes, Radar, Ultrasonic, and or Video.
Data exchange between components may be transmitted using: Cellular telephone, Hard wired cable, Optical, radio frequencies, satellite, and or wireless access points.
• Software that processes and analyzes the data, converting it to information that can be used by other components and various users of the information
• Electronic equipment to disseminate the processed information to end users of the information, such as motorists and transportation agencies
Interaction: None
Notes: None

## Slide 15: ITS Application Examples
Dynamic Lane Merge
Queue Warning Systems
Variable Speed Limits (VSL)
Traffic Management/Route Choice
Automated Speed Enforcement
Performance Monitoring/Management
Let’s discuss…
Notes: Key Message: Introduce students to some of the applications
Background Information: Mention each one and ask which ones have the audience used to better gauge how much to dive into each topic. Do not cover each one here, wait for each slide to further expand on these topics.
Interaction: Ask audience which ones they have used.
Notes: Introduction to types of applications. Table 1 on page 3 in the guide goes through each one.

## Slide 16: 1. Dynamic Lane Merge
Signs that encourage drivers to merge at a point based on current conditions
Regulates merging (early or late) based on traffic data
Source: workzonesafety.org
Notes: Key Message: Provide background information on the dynamic lane merge concept
Background Information: (Broken into two slides) Dynamic Lane merge is a strategy to smooth down the interaction of traffic on the approach to capacity constraint conditions, it encourages traffic to either merge early or merge late. In a low-volume high-speed situation if you have capacity constraint, then traffic needs to move into a single lane upstream of a work zone, and you want to encourage those merges to happen early. If you have the high-speed traffic coming right up to the merge point, they have to make a high-speed, last-minute lane change without any time to react.
The traditional merging lane closure method is well understood by road users. This operation normally works well during most of the day when traffic demand is less than the capacity of the open lane. How­ever, when the demand exceeds the capacity, congestion develops and road rage intensifies. Aggressive drivers remain in the closed lane up to the actual merge point. In response, sign-abiding drivers do not let the aggressive drivers merge. The resulting traffic backup continues to grow and typically will extend upstream beyond the advance lane closure signs. When this happens, drivers unfamiliar with the lane closure approach the end of the queue at high speed. This increases the likelihood of rear-end crashes.
There are two new work zone techniques that use Work Zone ITS technology to address these problems. The first is the early merge, which is intended to encourage the aggressive drivers to merge into the open lane sooner than they would with the traditional merging lane closure. The second method is the late merge, which encourages all drivers to remain in their lanes until they reach the merge point. Dynamic merge control systems aim to improve driver behavior by providing a clear way to understand the traffic control method. This concept ensures that some vehicles are not waiting for a long time while others, fa­miliar with the lane closure, find a way to get in front to reduce their delay. The “fairness” of the systems has been found to reduce road rage or other aggressive driving actions.
Interaction: Show video and asks questions about video If access to internet, consider showing a couple of YouTube videos from MnDOT
https://www.youtube.com/watch?v=vLVMW8KnfBE; https://www.youtube.com/watch?v=FCLF2tyW0TU.
Another video from Kansas DOT: https://www.youtube.com/watch?v=8wgSjstvsPc
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 17: Dynamic Lane Merge (cont.)
Leads to “smooth” merging and improves safety
Encourages early merge during free flow conditions and late merge during congestion
Provides lane use instructions to motorists
  USE BOTH LANES or
  TAKE YOUR TURN-MERGE HERE
Notes: Key Message: Provide background information on the dynamic lane merge concept
Background Information: Dynamic Lane merge is a tactic to smooth down the interaction of traffic on the approach to capacity constraint conditions, it encourages traffic to either merge early or merge late. In a low-volume high-speed situation if you have capacity constraint, then traffic needs to move into a single lane upstream of a work zone, and you want to encourage those merges to happen early. If you have the high-speed traffic coming right up to the merge point, they have to make a high-speed, last-minute lane change without any time to react.
The traditional merging lane closure method is well understood by road users. This operation normally works well during most of the day when traffic demand is less than the capacity of the open lane. How­ever, when the demand exceeds the capacity, congestion develops and road rage intensifies. Aggressive drivers remain in the closed lane up to the actual merge point. In response, sign-abiding drivers do not let the aggressive drivers merge. The resulting traffic backup continues to grow and typically will extend upstream beyond the advance lane closure signs. When this happens, drivers unfamiliar with the lane closure approach the end of the queue at high speed. This increases the likelihood of rear-end crashes.
There are two new work zone techniques that use Work Zone ITS technology to address these problems. The first is the early merge, which is intended to encourage the aggressive drivers to merge into the open lane sooner than they would with the traditional merging lane closure. The second method is the late merge, which encourages all drivers to remain in their lanes until they reach the merge point. Dynamic merge control systems aim to improve driver behavior by providing a clear way to understand the traffic control method. This concept ensures that some vehicles are not waiting for a long time while others, fa­miliar with the lane closure, find a way to get in front to reduce their delay. The “fairness” of the systems has been found to reduce road rage or other aggressive driving actions.
Interaction: Show video and asks questions about video If access to internet, consider showing a couple of YouTube videos from MnDOT
https://www.youtube.com/watch?v=vLVMW8KnfBE; https://www.youtube.com/watch?v=FCLF2tyW0TU.
Another video from Kansas DOT: https://www.youtube.com/watch?v=8wgSjstvsPc
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 18: Early Lane Merge
Advises drivers to move out of the closed lane well before the forced merge point
Works best when there is a low traffic volume combined with high average speeds
Image: FHWA
Notes: Key Message: Discuss early merge and benefits
Background Information: (Broken into two slides) The objective of the early merge is to move vehicles out of the closed lane upstream as soon as possible. The dynamic early merge system uses ITS sensors to monitor traffic in the open lane on the approach to a work area. As vehicles begin to slow down and queues start to develop, advance warning signs with the message “Do Not Pass When Flashing” are activated. These signs are installed adjacent to the closed lane at ¼ to ½ mile intervals in advance of the lane closure. When slow or stopped vehicles are detected in the open lane next to the sign, a wireless signal is transmitted to activate the next sign upstream.
Benefits:
• Matches the length of the Early Merge System application to the upstream roadway demand.
• Reduces aggressive driving and unsafe merge maneuvers.
• Provides significant advanced warning so drivers have adequate distance to merge.
• Gives drivers guidance on lane usage and merging points, which helps reduce road rage and misunderstandings between drivers.
• Compliance to lane assignment may be enforceable by law enforcement.
Interaction: None
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 19: Early Lane Merge Benefits
Reduces aggressive driving and unsafe merge maneuvers
Provides significant advanced warning to allow drivers adequate distance to merge
Gives positive guidance on lane usage
Image: FHWA
Notes: Key Message: Discuss early merge and benefits
Background Information: The objective of the early merge is to move vehicles out of the closed lane upstream as soon as possible. The dynamic early merge system uses ITS sensors to monitor traffic in the open lane on the approach to a work area. As vehicles begin to slow down and queues start to develop, advance warning signs with the message “Do Not Pass When Flashing” are activated. These signs are installed adjacent to the closed lane at ¼ to ½ mile intervals in advance of the lane closure. When slow or stopped vehicles are detected in the open lane next to the sign, a wireless signal is transmitted to activate the next sign upstream.
Benefits:
• Matches the length of the Early Merge System application to the upstream roadway demand.
• Reduces aggressive driving and unsafe merge maneuvers.
• Provides significant advanced warning so drivers have adequate distance to merge.
• Gives drivers positive guidance on lane usage and merging points, which helps reduce road rage and misunderstandings between drivers.
• Compliance to lane assignment may be enforceable by law enforcement.
Interaction: None
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 20: Late Lane Merge
Advises drivers to use both lanes up to the merge point
Works better for high traffic volumes
Image: FHWA
Notes: Key Message: Discuss Late Merge and benefits
Background Information: The dynamic late merge is the opposite of the early merge. It is intended to encourage drivers to use all available lanes until they reach the beginning of the merging taper. When congestion forms, changeable message signs are activated to provide the following lane use instruction:
• Located upstream of the taper beyond the estimated maximum queue length: “Stopped Traffic Ahead” alternating with “Use Both Lanes”.
• Located upstream of the taper at the estimated queue length when the dynamic late merge will be activated: “Merge Ahead” alternating with “Use Both Lanes”.
• Located at the desired point of merge: “Take Turns” alternating with “Merge Here”.
Using ITS technology, the safest and most efficient merging operation can be implemented by switch­ing between the conventional merge and the late merge when congestion is detected.
Benefits include:
• Alerts drivers that they are approaching slow or stopped traffic.
• Allows queue to “stack” in multiple lanes, which reduces the overall queue length by approximately half.
• Reduces the differential in speed between lanes, providing for safer lane changes.
• Gives drivers positive guidance on lane usage and merging points, which helps reduce road rage and misunderstandings between drivers.
Interaction: None
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 21: Late Lane Merge Benefits
Maximize available storage upstream of work zone
Reduces confusion between drivers who think they should merge early vs. drivers that use open lanes as far as possible
Clarifies right-of-way at merge point (“alternate merge”)
Image: FHWA
Notes: Key Message: Discuss Late Merge and benefits
Background Information: The dynamic late merge is the opposite of the early merge. It is intended to encourage drivers to use all available lanes until they reach the beginning of the merging taper. When congestion forms, changeable message signs are activated to provide the following lane use instruction:
• Located upstream of the taper beyond the estimated maximum queue length: “Stopped Traffic Ahead” alternating with “Use Both Lanes”.
• Located upstream of the taper at the estimated queue length when the dynamic late merge will be activated: “Merge Ahead” alternating with “Use Both Lanes”.
• Located at the desired point of merge: “Take Turns” alternating with “Merge Here”.
Using ITS technology, the safest and most efficient merging operation can be implemented by switch­ing between the conventional merge and the late merge when congestion is detected.
Benefits include:
• Alerts drivers that they are approaching slow or stopped traffic.
• Allows queue to “stack” in multiple lanes, which reduces the overall queue length by approximately half.
• Reduces the differential in speed between lanes, providing for safer lane changes.
• Gives drivers positive guidance on lane usage and merging points, which helps reduce road rage and misunderstandings between drivers.
Interaction: None
Notes: Consider reviewing ATSSA’s ITS Safety and Mobility Solutions, 2008, ATSSA

## Slide 22: Dynamic Lane Merge Components
Sensors
Portable Changeable Message Signs (PCMS) in advance of a lane closure
Source:
workzonesafety.org
Notes: Key Message: Briefly describe the component parts of the system
Background Information: Non-intrusive vehicle presence detectors, which could include Microwave signals to identify traffic volume; video analysis to track traffic volume, lane occupancy, and queue; Doppler radar to determine average speed; Pneumatic tubes to calculate traffic volume; or computer simulations to optimize dynamic merging algorithms. Using this data, the information would then be fed by data exchange between components may be transmitted using cellular telephone, hard wired cable, or optical to the portable changeable message signs to determine which sign message to display.
Interaction: None
Notes: None

## Slide 23: 2. Queue Warning System (QWS)
Used to alert drivers to traffic conditions ahead:
  Stopped traffic
  Slowing traffic
  Others
Image: FHWA
Notes: Key Message: Describe the queue warning system
Background Information: Queue Warning Systems are one of the tools in the technology applications toolkit. They are geared toward alerting drivers about stopped traffic or reductions in speed downstream. Typically, if you have a work zone with a capacity constraint, there will be some kind of backup. In the worst case, what you can see is a queue that gets so long it goes back past the initial warning signs. When that happens, you have a dangerous condition where cars are traveling at freeway speed then suddenly encounter the stopped traffic or slowed queue of traffic with no warning. This is an even more dangerous situation when large trucks are in the mix due to the distance they must brake before coming to a stop. The last thing you want is a car or a truck traveling at freeway speed running into the back of a stopped queue. It is one of the more significant work zone safety issues that agencies face, but queue warning systems can help to mitigate it.
Interaction: None
Notes: None

## Slide 24: Queue Warning System Benefits
Reduces the number and severity of rear-end crashes
Helps prevent drivers from being surprised by stopped or suddenly slowed traffic
Image: ATSSA
Notes: Key Message: Describe the queue warning system
Background Information: Queue Warning Systems are one of the tools in the technology applications toolkit. They are geared toward alerting drivers about stopped traffic or reductions in speed downstream. Typically, if you have a work zone with a capacity constraint, there will be some kind of backup. In the worst case, what you can see is a queue that gets so long it goes back past the initial warning signs. When that happens, you have a dangerous condition where cars are traveling at freeway speed then suddenly encounter the stopped traffic or slowed queue of traffic with no warning. This is an even more dangerous situation when large trucks are in the mix due to the distance they must brake before coming to a stop. The last thing you want is a car or a truck traveling at freeway speed running into the back of a stopped queue. It is one of the more significant work zone safety issues that agencies face, but queue warning systems can help to mitigate it.
Interaction: None
Notes: None

## Slide 25: Concept of Operations
A highly-portable end-of-queue warning system
  Deploy at each lane closure where queue is expected, pick up when lane is no longer closed
  Scale deployment to queue expectations
Image: FHWA
Notes: Key Message: Review how end of queue system works
Background Information: Work Zone ITS queue detection tools monitor the speed of vehicles within and upstream of the work zone. When reduction in travel speed is detected, changeable message signs or other warning systems are activated to warn approaching drivers that they should be prepared to stop.
The upstream effects of slowed or stopped traffic vary day to day and hour by hour. However, Work Zone ITS tools allow real-time collection of data, resulting in current messages being displayed
to drivers.
Benefits:
• Alerts drivers of slowing or stopped traffic so they can safely stop.
• Reduces rear-end and secondary crashes.
• Helps reduce driver anxiety by giving advanced warning of stopped or slowed traffic, reducing the need to apply the brakes.
Example: Scale deployment to queue expectations (Modify location of advance warning signs)
Interaction: None
Notes: None

## Slide 26: Queue Warning System Components
Sensors
Portable Changeable Message Boards (PCMS)
Cameras (optional)
Rumble strips (optional)
Source:
workzonesafety.org
Notes: Key Message: Review types of components for this system
Background Information: The components of a Queue Warning Systems:
Sensors to measure the speed of traffic on the approach to the work zone. You may have several sensor devices spaced starting back at the capacity constraint where the lane merges for example extending back to the limits of where anticipated cues will be. So the system can pick up not only that there's a slowdown in traffic occurring but where that slowdown is happening. It can relay that information back upstream where it is important for a driver to know the traffic is slowing down 3 miles ahead or if it's slowing down over the next hill. The more sensors you have out there, the more detail and better accuracy in conveying that information to drivers.
That information is typically conveyed by portable changeable message signs. To aid in speed detection and traffic management, an agency might place cameras in the field out there to make sure that the placement of the sensors is picking up the limits of the queue. Rumble strips have also been used upstream of the work zone as a means of improving driver awareness. They are typically placed in the same location as the PCMS.
Interaction: None
Notes: None

## Slide 27: 3. Variable Speed Limits (VSL)
Multiple speed trailers in and on the approach to a work zone
Each unit
  Monitors prevailing speed
  Relays information to upstream units
Posted speed limit is dynamically adjusted to reduce the downstream speed differential
Image: FHWA
Notes: Key Message: Review variable speed limit concept
Background Information: Selecting the appropriate work zone speed limit for a work zone is a challenge. For driver compli­ance, the posted speed limit needs to be reasonable, and if drivers do not see a need to reduce their speed, they will not. This is especially true for long-term work zones with commuter drivers.
When activities require workers to be near open lanes of traffic and unprotected by a barrier, when lane closures are required, or when geometric conditions of the open roadway change, reductions in work zone speed should be considered.
The Work Zone ITS system allows the posted speed limit value to be changed to an appropriate, en­forceable “work zone speed limit” during the work activity. When the activity stops, the speed limit is changed back to the normal posted speed for the roadway. During a 24-hour period, the speed limit may change several times.
Before implementing changeable speed limits, check state and/or municipal speed limit administra­tive procedures.
The typical application of a variable speed limit is time-based. We use the systems both to measure the speeds that of downstream traffic and to relay that information upstream to warn drivers to adjust their speed either with a VSL sign like this one, or with a PCMS.
Interaction: None
Notes: None

## Slide 28: Variable Speed Limits Benefits
Reduction of potential crashes as drivers approach back of queue
Reduction of congestion and ease traffic through work zone depending on current conditions
Reduction in travel time through speed harmonization
Image: FHWA
Notes: Key Message: Review variable speed limit concept
Background Information:
Benefits
• Allows speed limits to be changed quickly using wireless technology to match the requirements of the work activity
• Are portable and can be moved to new areas were speed management is needed.
• Are often recognized better by drivers than static regulatory speed limit signs due to the use of modern electronic displays. Drivers must see the speed limit in order to comply.
• Encourages compliance of the speed limit. This reduces variations in speeds, which increases roadway capacity and may reduce crashes within the work zone.
Interaction: None
Notes: For more information see ATSSA ITS Safety and Mobility Solutions. Photograph from ATSSA ITS Safety and Mobility Solutions.

## Slide 29: Variable Speed Limits Considerations
Advisory versus Enforceable
  Legislative policy (allowing enforceable VSLs)
  Law Enforcement involvement
    Enforcement
    Presence
Pre-determined, fixed time VSL versus fully automated VSL
  During active work zone (workers present)
  Changing congestion conditions
Notes: Key Message: Considerations when deploying VSL
Background Information: There are two different kinds of VSL’s you can have. Advisory versus enforceable. Which you use depends on the local regulations and whether a state has provisions in its legislation for enforcement of variable speed limits. What you use and what is appropriate might just depend on the law in your area.
There are both dynamic VSLs, which vary based on the information collected in the field, and those that are set on a fixed time base.
Some of the benefits of variable speed limits include crash reductions. One of the biggest contribution to crashes is speed differential, so if you can target what is causing differences in speed and encourage the harmonization of speeds from a higher speed condition to a lower speed condition, you will reduce those local speed differentials and thereby improve safety.
We are trying to anticipate where the congestion is going to be downstream and to provide guidance and enforceable speed limits to drivers. That is the basic concept behind variable speed limits.
Consider for Use
When the project is long term in duration, requiring multiple phases, with each having variable affects on the travel way.
• When closed lanes are reopened at the end of the work day with no lasting effects on the travel way.
• When the location of the day’s work activities do not always require a reduction in speed.
• When manually covering or removing speed limit signs is unsafe.
Interaction: None
Notes: None

## Slide 30: 4. Traffic Management/Route Choice
Provides additional information to motorist
  Trip planning information
  Travel times along route
  Speeds along route
Image: FHWA
Notes: Key Message: Describe Traffic Management/Route Choice system to students
Background Information: (broken into two slides) Drivers are provided information about current travel conditions and that information can be used by the driver to encourage diversion.
Work Zone ITS systems that monitor delay through a work zone can provide valuable trip planning information on a regional basis.
Good communication along a particular roadway corridor can help drivers make informed deci­sions about their travel plans. To do this, the cities and transportation districts inform each other when lane closures are planned, and then share this information with roadway users by way of internet web sites, 511 traveler informational systems, public media announcements, highway advi­sory radio (HAR), and permanent ITS systems.
It is common that a work zone, using traditional work zone applications, on a major roadway link­ing two major destinations, can result in lengthy delays upwards of one or two hours. Queue build­ups can result in rear-end and secondary crashes, which can cripple the roadway corridor. Wasted fuel, excessive emissions, and unproductive driver time add to this inefficient equation.
A Work Zone ITS system’s software can monitor queue length and process speed detection data along the roadway corridor. Various types of communication technology can be used to distribute real-time information that can be displayed on permanent ITS message boards or portable change­able message boards. The information can also be broadcast on HAR along the route. This traveler information can be included on many GPS systems, including those used by interstate trucking companies. Messages may include the location of the expected delay, anticipated delay time, and/or possible alternate routes.
Benefits
• Provides real-time information so road users can better plan their routes and travel times.
• Advises drivers to seek alternate routes.
• Reroutes traffic in order to:
• Reduce work zone traffic congestion, which decreases fuel consumption and emissions.
• Reduce traffic demands on roadway sections under construction.
• Allow for more efficient material delivery, which expedites work progress.
• Reduce the potential for work zone crashes.
• Helps relieve driver anxiety by providing increased knowledge of the situation.
Consider for Use
• When roadway accommodates long-distance, regional travelers who desire an alternate route that provides the lowest travel time to the next major populated area or major roadway interchange.
• When a viable alternate route exist that can help absorb travel demand through the work zone.
Interaction: None
Notes: For more information see ATSSA ITS Safety and Mobility Solutions

## Slide 31: 4. Traffic Management/Route Choice Benefits
Provides real-time information
Enables drivers to make informed route choices
Potentially diverts motorists
Image: FHWA
Notes: Key Message: Describe Traffic Management/Route Choice system to students
Background Information: Drivers are provided information about current travel conditions and that information can be used by the driver to encourage diversion.
Work Zone ITS systems that monitor delay through a work zone can provide valuable trip planning information on a regional basis.
Good communication along a particular roadway corridor can help drivers make informed deci­sions about their travel plans. To do this, the cities and transportation districts inform each other when lane closures are planned, and then share this information with roadway users by way of internet web sites, 511 traveler informational systems, public media announcements, highway advi­sory radio (HAR), and permanent ITS systems.
It is common that a work zone, using traditional work zone applications, on a major roadway link­ing two major destinations, can result in lengthy delays upwards of one or two hours. Queue build­ups can result in rear-end and secondary crashes, which can cripple the roadway corridor. Wasted fuel, excessive emissions, and unproductive driver time add to this inefficient equation.
A Work Zone ITS system’s software can monitor queue length and process speed detection data along the roadway corridor. Various types of communication technology can be used to distribute real-time information that can be displayed on permanent ITS message boards or portable change­able message boards. The information can also be broadcast on HAR along the route. This traveler information can be included on many GPS systems, including those used by interstate trucking companies. Messages may include the location of the expected delay, anticipated delay time, and/or possible alternate routes.
Benefits
• Provides real-time information so road users can better plan their routes and travel times.
• Advises drivers to seek alternate routes.
• Reroutes traffic in order to:
• Reduce work zone traffic congestion, which decreases fuel consumption and emissions.
• Reduce traffic demands on roadway sections under construction.
• Allow for more efficient material delivery, which expedites work progress.
• Reduce the potential for work zone crashes.
• Helps relieve driver anxiety by providing increased knowledge of the situation.
Consider for Use
• When roadway accommodates long-distance, regional travelers who desire an alternate route that provides the lowest travel time to the next major populated area or major roadway interchange.
• When a viable alternate route exist that can help absorb travel demand through the work zone.
Interaction: None
Notes: For more information see ATSSA ITS Safety and Mobility Solutions

## Slide 32: 5. Automated Speed Enforcement
Illinois
Maryland
Oregon
Washington State
Pennsylvania
California
Images: FHWA
Notes: Key Message: Introduce Automate Enforcement application
Background Information: Excessive speed through roadway work zones continues to be a safety concern for workers, trans­portation agencies, and law enforcement agencies. Over the last decade, in an attempt to increase awareness of speed limits within roadway construction projects, many states have enacted “Double Fines in Work Zones” laws. Yet, without enforcement, these laws did little good. Enforcement that is evident to the driver allows them to realize that speed limit signs are important and must be obeyed.
While traditional speed enforcement can be effective, it can be dangerous to both road users and law enforcement officers. Work zone environments may restrict the ability of officers to set up radar. Violators may have difficulty finding a safe place to pull over, since work zone environments sometimes have limited shoulder space. Additionally, speed enforcement may create traffic conges­tion and increase the potential for work zone crashes.
Automated speed enforcement using ITS technology is one tool that can be used to reduce work zone speeds and crashes. These systems combine radar and image-capturing technologies to de­tect speeding vehicles and collect digital photographic evidence. The owner of the vehicle is then mailed a citation including a photo of the vehicle, vehicle license plate, and the detected vehicle speed. The process is similar to systems that catch road users running red lights. ITS automated speed enforcement systems are being used in several states. Prior to installing any automated en­forcement system, be sure to check local statutes to see if they are allowed.
Some states utilize speed-radar photo enforcement in work zones, including Illinois, which uses van with retrofitted equipment to reduce speeds through work zones and work zone fatalities.
Interaction: None
Notes: None

## Slide 33: Automated Speed Enforcement Legal and Deployment Issues
May require legislative approval
Coordination required with
  Law enforcement
  Court systems
Locations of deployments as not to interfere with the work zone
Notes: Key Message: Talk about deployment issues with Automated Enforcement
Background Information: In order to use automated enforcement the issues listed have to be considered and overcome depending on the state.
May require legislative approval
    Minimum speeds for which it would be issued
Advance signing required for the system to be used for a work zone
    Use of revenues and fines assessed
Coordination required with law enforcement officers and court systems
Locations of deployments as not to interfere with the work zone
Benefits
• Increases driver awareness of the work zone.
• May increase 24-hour compliance to work zone speed limits without law enforcement officers present.
• Allows law enforcement officers to focus on other job duties.
• Eliminates officer’s exposure to hazardous roadside traffic stops.
Consider for Use
• On roadways where the temporary traffic control zone has narrowed shoulders and limited roadway exit points for speed violators and law enforcement to safely exit the travel way.
• When 24-hour speed enforcement is desired.
• On projects where law enforcement availability is limited.
Interaction: None
Notes: None

## Slide 34: 6. Performance Monitoring/Management
Evaluates effectiveness of each strategy
  Queue detection
  Lane rental
  Night work
Image: FHWA
Notes: Key Message: Introduce performance monitoring/management.
Background Information: (Broken into two slides) Monitor and archive traffic conditions data to support real-time traveler information, modify operations, and support evaluation. Both Ohio and Indiana DOT have established policies on acceptable work zone queue length and duration. Work zone ITS can monitor and archive traffic data that can be used to evaluate performance measures, including those used in performance-based contracting.
Interaction: None
Notes: None

## Slide 35: 6. Performance Monitoring/Management
Expands to other forms of work zones
  Travel times
  Sensors
  Countdown timers
Provides information by project type
  Data collection to make informed decisions
Image: FHWA
Notes: Key Message: Introduce performance monitoring/management.
Background Information: Monitor and archive traffic conditions data to support real-time traveler information, modify operations, and support evaluation. Both Ohio and Indiana DOT have established policies on acceptable work zone queue length and duration. Work zone ITS can monitor and archive traffic data that can be used to evaluate performance measures, including those used in performance-based contracting.
Interaction: None
Notes: None

## Slide 36: Work Zone ITS Implementation Guide
Provides guidance
Designed to assist:
  Public agencies,
  Design and construction firms, and
  Industry stakeholders
Provides a six-step systems engineering approach to work zone ITS implementation
Available online
Image: FHWA
Notes: Key Message: Begin presenting the Work Zone Intelligent Transportation Systems Implementation Guide.
Background Information: The guide is intended to provide users, state DOTs and agencies, contractors, and other industry stakeholders a basic map for how to go about implementing smarter work zones. It was developed around a six step process that uses a systems engineering approach, which is basically engineering a solution to a problem.
Interaction: None
Notes: Available at:
http://ops.fhwa.gov/plulications/fhwahop14008/index.htm

## Slide 37: Six-step Systems Engineering Approach to WZ ITS Implementation
--Assessment of Needs
--Concept Development & Feasibility
--Detailed System Planning & Design
--Procurement
--System Deployment
--System Operation, Maintenance, and Evaluation
Notes: Key Message: Briefly introduce them to 6 step process
Background Information:
The engineering approach to ITS implementation is a fairly straightforward process that consist of six basic steps. The level of effort required in each of these steps is going to depend on each agency’s needs and deployment processes. For smaller applications, some steps might be fairly simple and straightforward. In other cases, a more complex regional, customized design might require more effort in one or more of these steps.
Interaction: None
Notes: None

## Slide 38: Step 1 – Assessment of Needs
Source: FHWA
Image: FHWA
Notes: Key Message: Step 1- assessment of Needs.
Background Information: The first thing to do is to look at what the needs are for a particular project. This actually should be done as part of the overall transportation management planning process. You should not be just now identifying X product, smart work zone product A, just because it is a cool product. Step back and look at what's really going to be the expected impact of using the ITS you’ve identified. Look at the when, where, and how the situation is going to develop. Ask yourself, what kinds of things are going to be going on in my work zones that will lead to safety and mobility concerns that I need or want to address in some part. Also at this point, you are looking what are other special regulatory requirements or restrictions you can or can't do as an agency or contractor. Look at the physical limitations of the project itself. Ask yourself, am I going to have space to work, or is this going to be a project where I have limited right-of-way and my contractor's equipment is going to be constantly in and out, moving around? From a user needs standpoint, is there working space available?
Interaction: None
Notes: None

## Slide 39: Step 1 – Assessment of Needs
1.1 What are the user needs?
1.2 What are the systems goals and objectives?
1.3 Who are the stakeholders?
1.4 Who should be on the project team?
1.5 What, if any, existing ITS resources are available?
Notes: Key Message: Step 1 has 5 sub steps, each step will be discussed in detail. Read the list of sub steps for the class.
Background Information: There are five key things to keep in mind when looking at needs assessment or user needs. Let’s look at each one of these.
1.5 Finally, one of the key things in the early steps is recognizing and identifying what do I have already within the area, maybe not within my project but possibly adjacent to it, from an existing ITS resource standpoint. Many urban transportation centers operating in covering a significant portion of the transportation network. A project might be not on one of the routes under surveillance, but adjacent to it and it would be an opportunity to leverage what kind of capabilities that system has in terms of operating stuff and such things that leaking those, or considering that in the ultimate design, might be a good idea.
Interaction: None
Notes: None

## Slide 40: Step 1 – Assessment of Needs
Think as News Reporters…
WHO needs to know?
WHAT do they need to know?
WHEN will these issues occur?
WHERE will they occur?
WHY will they occur?
HOW often will they occur?
Notes: Key Message: Talk in broad terms what the needs are for the work zone
Background Information:
WHO will be affected by these issues?
WHAT real-time work zone-induced traffic issues or problems will exist?
WHEN will these issues occur?
WHERE will they occur?
WHY will they occur?
HOW often will they occur?
Interaction: None
Notes: None

## Slide 41: 1.1 What are the user needs?
Who are the users of a Work Zone ITS system?
Motorists
Public
Contractor
DOT
Law enforcement
Localities
Images: FHWA
Notes: Key Message: Identify the users of the system
Background Information:
Examples of work zone-induced traffic issues or problems:
New or worsened peak-period congestion due to long-term road capacity loss
Creation of unexpected queues when lanes are temporarily closed
Creation of queues and/or increased congestion when a vehicle stalls or a crash occurs
Development of bottlenecks at entrance ramps just upstream of lane closures
Need for truck deliveries in and out of a median work space
Need to dynamically adjust the posted speed limit when workers are out next to traffic
Altered traffic patterns at multiple signalized intersections in corridor due to temporary closure of cross-streets in work zone
The first step in identifying user needs is identifying the users. “Drivers” is the most obvious one, but who are the others?
Public – people who might be planning a trip, wondering how long congestion in their area will last
DOT – could be a TMC, could be a District Construction division, many possible “users”
Police – can use the output for enforcement purposes, but also need to be involved in messaging delivered to the public
Researchers
Localities
Interaction: None
Notes: None

## Slide 42
Be SMART…
  Specific
  Measurable
  Attainable
  Relevant
  Time-bound
1.2 What are the Systems Goals and Objectives?
Notes: Key Message: Introduce system goals and objectives
Background Information: Next is to try and define, again technology independent, what would I want to do from a goals and objective standpoint to address those user needs. For example, I would like to reduce the frequency of crashes because I think I am going to see a spike in, or I would like to get some drivers to change when and where they are going to travel, move away from my project limits. Or, if it is simply I want to make motorist more aware, or aware of upcoming slowdowns and delays so they can decide whether they want to stop for gas or a break prior to entering my work zone. All those things come in to there.
The goals and objectives should then address the user needs, and be aligned with the overall Transportation Management Plan (TMP) development and execution effort. System goals and objectives should follow SMART criteria, meaning that they are Specific, Measurable, Attainable, Relevant, and Time-bound. It is critical at this point to set realistic objectives for the system and avoid the creation of unrealistic expectations that result in diminished
credibility in the system’s outputs
Interaction: None
Notes: None

## Slide 43: 1.2 Systems Goals and Objectives
Image: FHWA
Notes: Key Message: Talk about goals and objectives as this is a critical step.
Background Information: The system should be adequately robust to consider the full impact of the work zone.
The area of ITS influence due to a work zone may include adjacent routes. It is likely that at least some drivers will divert, regardless of whether messages encourage taking an alternate route. This additional traffic may cause congestion on those adjacent routes and should be considered when planning for the ITS. If diversion is expected, ITS devices may be required on alternate routes as well as the mainline. These alternate routes will need to be monitored and managed in order for benefits to be achieved.
Goals:
“Minimize work zone delay”
“Enhance safety”
“Maintain positive public outlook on project”
Objectives:
“Maintain average peak hour travel time of 5 min from Exit 75 to Exit 80”
“No queues longer than 500 ft. at ramp terminal”
“Maintain minimum public feedback score of 3 out of 5”
A goal is a broad statement that describes a desired end state. It is the "what" an agency is trying to achieve. Goals can address different aspects of the work zone: delay, crash reduction, speed management, etc.
An objective is more specific and measurable and is defined as "what" needs to be done in order to achieve the goals you’ve established. Although developing these aims is usually discussed together with goals (e.g., "developing goals and objectives"), it’s important to understand the distinction between goals and objectives within the systems engineering approach. While goals relate to the "big picture" or desired end-result, objectives should be specific and measurable and support the achievement of a goal. For example, “Limit delay in the work zone area to a maximum of 15 minutes.”
A strategy is defined as a capability put in place to achieve an objective. This is where you have the opportunity to be innovative, and also identify strategies that are achievable and sustained within your agency’s existing level of capability. For example, “Develop an outreach and communication strategy to maximize the traveler information available to users.”
A tactic is the specific method to implement a strategy. It is an action taken (activities) or tool used to help implement the strategies in order to achieve objectives and attain goals. For example, in response to the objective of limiting delay, one tactic may be to implement a variable speed limit in the work zone. Another tactic may be to utilize local media, the internet, and the 511 system to advise travelers of the active work zone and when lane closures are planned to occur.
Strategies and Tactics are then used to satisfy the Goal and Objectives.
Interaction: None
Notes: None

## Slide 44: 1.3 Who are the Stakeholders?
Those actively involved in planning and implementing work zone ITS solutions
Notes: Key Message: Go to page 11 of the guide and look at their list.
Background Information: Another key group that should be considered during system planning is stakeholders. Stakeholders include any person or organization that may be affected by construction, and all agencies that are directly involved with motorist assistance, law enforcement, and providing traveler information. Stakeholders are a broader group than users, and include those who are not intended to be primary users of an ITS deployment. Stakeholders must be involved early on for a successful ITS implementation.
Interaction: Can you think of any stakeholders?
Notes: None

## Slide 45: Stakeholders: Owners / Operators
Toll Authorities
FHWA Division Office
Construction contractors
Departments of Transportation
Metropolitan Planning Organizations
Notes: Key Message: Go to page 11 of the guide and look at their list.
Background Information: Another key group that should be considered during system planning is stakeholders. Stakeholders include any person or organization that may be affected by construction, and all agencies that are directly involved with motorist assistance, law enforcement, and providing traveler information. Stakeholders are a broader group than users, and include those who are not intended to be primary users of an ITS deployment. Stakeholders must be involved early on for a successful ITS implementation.
Interaction: Can you think of any others?
Notes: None

## Slide 46: Stakeholders: First Responders
Fire departments
Emergency medical services
State and local police departments
Notes: Key Message: Go to page 11 of the guide and look at their list.
Background Information: Another key group that should be considered during system planning is stakeholders. Stakeholders include any person or organization that may be affected by construction, and all agencies that are directly involved with motorist assistance, law enforcement, and providing traveler information. Stakeholders are a broader group than users, and include those who are not intended to be primary users of an ITS deployment. Stakeholders must be involved early on for a successful ITS implementation.
Interaction: Can you think of any others?
Notes: None

## Slide 47: 1.3 Who are the Stakeholders?
Shopping centers and other major traffic generators
Major commercial trucking companies
Motorists
Media
Local residents
Public officials
Local businesses
Stakeholders: The Public
Notes: Key Message: Go to page 11 of the guide and look at their list.
Background Information: Another key group that should be considered during system planning is stakeholders. Stakeholders include any person or organization that may be affected by construction, and all agencies that are directly involved with motorist assistance, law enforcement, and providing traveler information. Stakeholders are a broader group than users, and include those who are not intended to be primary users of an ITS deployment. Stakeholders must be involved early on for a successful ITS implementation.
Interaction: Can you think of any others?
Notes: None

## Slide 48: 1.4 Who should be on the Project Team?
Owners / Opera-tors
First Responders
Public
Notes: Key Message: Describe who could be on project team
Background Information: You might want to start to make decisions about who would be on your project team to help make decisions and assess options.
The project team is the actual working group whose members are drawn from the stakeholder organizations identified in the previous step. It is recommended that the number of people on this team be small because this team will be conceptualizing and planning the project.
Interaction: Can you think of any others?
Notes: None

## Slide 49: 1.5 What, if any, existing ITS resources are available?
What potential equipment do you have in your state or locality that could be leveraged for use with Smart Work Zones?
Can temporary equipment be tied into permanent ITS systems for further monitoring by managers?
Notes: Key Message: Identify and utilize existing resource
Background Information:
Finally, one of the key things in the early steps is recognizing and identifying what you have already within the area, maybe not within my project but possibly adjacent to it, from an existing ITS resource standpoint. Many urban transportation centers may cover a significant portion of the transportation network. A project might be not be on one of the routes under surveillance but there could be surveillance on an adjacent route, and this could provide an opportunity to leverage that system’s capabilities in terms of operations during the active work zone period or even after work is complete, during normal roadway operations.
Taking an inventory of existing ITS resources in the corridor or region that can be applied to help manage the work zone can help to control system acquisition and deployment costs. For example, there may be a permanent traffic detector within or adjacent to the work zone that can provide archived or real-time data to help predict and/or monitor traffic conditions leading up to and throughout the work zone. There may be permanent CMS upstream of the work zone that can display warnings of stopped or slow traffic ahead or encourage diversion to alternate routes.
Can temporary equipment be tied into permanent systems to provide additional information to traffic managers?
Interaction: None
Notes: None

## Slide 50: 1.5 Existing ITS Resources (Equipment)
Permanent CMS
Traffic cameras
Permanently installed count stations / speed sensors
Telecom infrastructure
Adaptive signal systems
Notes: Key Message: Show example of an available set of resources that potentially could be used for a work zone
Background Information: See the picture on the right shows lots of resources that potentially could be tied into the work zone ITS system
Interaction: None
Notes: None

## Slide 51: Step 1 - Overview
Who are the users?
What are the objectives?
Who are the stakeholders?
Who should be on the project team?
What existing ITS assets can be utilized?
Notes: Key Message: Review step 1, this is a critical step in getting started correctly
Background Information: In summary, step one should not be thought of as the end of the project so much as the end of where you want to get with respect to your transportation management solution to address the mobility and safety impacts of the work zone. It is the process for creating a kind of a vision of what we want to accomplish. At this point you should also start to have some thoughts and expectations about your how you’re going to move toward a more coordinated approach that is connected to the overall transportation management planning process for the project or set of projects you are looking at.
Interaction: None
Notes: None

## Slide 52: Step 2 - Concept Development & Feasibility
Source: FHWA
Image: FHWA
Notes: Key Message: Review step 2
Background Information: Step two is the concept development and feasibility assessment
This step essentially answers the question, “How does the agency envision that the system will operate within WZ?”
• May include multiple sub-systems
• Solution considerations
Is the system permitted in the current laws and regulations?
• What is the potential increased liability for placing ITS equipment in the work zone?
• What are possible liability issues regarding how warnings and messages are given?
Interaction: have students turn in the guide to the correct page.
Notes: Starting on page 15 in guide

## Slide 53: Work Zone ITS Options
Traffic monitoring/management
Traveler information
Queue detection/warning
Incident detection/management
Worker safety/protection
Speed management/enforcement
Performance monitoring
Assessing/setting work hours
Tracking contract incentives/disincentives
Notes: Key Message: Briefly review the options of work zone ITS
Background Information: At this point, you start to look at what solutions are available. There are a number of standalone, commercial off-the-shelf products―what I call the communication system engineering aspects of a particular solution. They are pretty much a product that you set up, configure a little bit, and they start to do what they are intended to do. There are also customized software solutions that involve developing a concept of operation. We’re also starting to see more and more in terms of third-party services, either for data or for the development and implementation of a system, that are available on an on-demand basis.
You start to look at the feasibility of an ITS solution at this point. You need to ask if the expected benefit you might be able to achieve by using an ITS system is great enough to offset the cost. You also need to look at the legal and policy issues that are involved or potentially involved by your solution. Look at the choices you have for various ITS products. Some of them are fairly similar in terms of the types of issues being addressed. But if they are applied in different ways, you can see that there is evidence in most cases of a work zone solution having real, measurable effects on motoring traffic or other aspects of a benefit analysis.
Key takeaways under step two, this is the point where you have reached the point of yes, we need a work zone ITS solution here. At this point one of the key things is recognition that it may be good to make sure that your ITS staff is involved in your work zone ITS planning, because of the potential leveraging of permanent infrastructure you have as well as awareness and knowledge of current data in terms of technologies and systems already in place.
Interaction: None
Notes: None

## Slide 54: Step 2 - Concept Development & Feasibility Assessment
Is ITS Feasible? When should ITS be Used?
  Does it fulfill the overall objectives?
  Is general cost reasonable for benefits?
  Is ITS the best Transportation Management Plan (TMP) strategy?
  Was a scoring criteria developed
  Is there a general ITS application guide
Notes: Key Message: Talk about the feasibility of using ITS
Background Information: The overall feasibility of the original approach should be revisited to determine if it meets the overall objectives for the system. Another key consideration in assessing project feasibility is whether ITS is the best TMP strategy to deploy to address the identified needs, or if other non-ITS options may be better for the given situation.
Interaction: None
Notes: None

## Slide 55: Example Set of Scoring Criteria to Establish Feasibility of Work Zone ITS
  Page 25 of the guide
Factor 1 – Duration of work zone
Factor 2 – Impact
Factor 3 – Queuing and Delay
Factor 4 – Temporal Aspects
Factor 5 – Specific Issues Expected
Total Score
Notes: Key Message: Review guide page 25 and walk students through assessment
Background Information: A general set of scoring criteria was developed that agencies can tailor as desired for their use as one possible way to assess the feasibility for ITS (see Table 6, page 25 of the guide). The intent for these criteria was to assist decision makers by providing a structured approach to considering the need for work zone ITS on specific projects. For each result, other mitigation treatments should be considered, as applicable, in addition to work zone ITS since ITS is only one possible solution for stakeholders to use to address a given issue in a work zone and may not be the best alternative.
Interaction: None
Notes: Have students turn to page 25 of the guide.

## Slide 56: Possible Work Zone ITS Applications To Consider For Various Critical Project Characteristics.
Page 26 of the guide
Source: FHWA
Image: FHWA
Notes: Key Message: Review guide page 25 and walk students through assessment
Background Information: Table 7 from page 26 of the guide presents another possible way to consider when to use work zone ITS. It can be used as a general application guide to assess the characteristics and conditions existing or anticipated in a given work zone that would help justify implementation of one or more of the systems.
Interaction: None
Notes: Have students turn to page 26 of the guide.

## Slide 57: Step 3 - Detailed System Planning and Design
Source: FHWA
Image: FHWA
Notes: Key Message:
Background Information:
Interaction:
Notes:

## Slide 58: Step 3 - Detailed System Planning and Design
3.1 Determining system requirements and specifications
3.2 Developing the system design
3.3 Developing a testing strategy
3.4 Planning for operations and maintenance
Notes: Key Message: Introduce Step 3
Background Information: (Broken into two slides) Step three is where it gets into actual nuts and bolts. Again depending on the system solution. A lot of this may be done in large case for you. As you can see here, this step includes defining system requirements and specifications, what specifically does the system need to do and how precisely, how accurately you require it to do that. Those kinds of things. Testing strategies. How are you going to ensure whether your system requirements and specs are going to be met by a solution and verifying, figuring out how to verify if the solution you have selected is meeting your requirements. At this step you start thinking about what it is going to take for it the operation and maintenance over the life of the project and start planning for that. Staffing, ability to move it to another project. Of those things start to be thought about here. Training, if there is going to be out right -- outreach or a public relations standpoint consideration or recognition of system security and those things planning for evaluation is very important as well as getting more finite testaments of both the benefits and costs you anticipate from the specific design being considered at this point.
Interaction: None
Notes: None

## Slide 59: Step 3 - Detailed System Planning and Design (cont.)
3.5 Determining staff training needs for those using and operating the work zone ITS
3.6 Planning for public outreach
3.7 Investigating system security
3.8 Planning for evaluation
3.9 Estimating system benefits and costs
Notes: Key Message: Introduce Step 3
Background Information: (Broken into two slides) Step three is where it gets into actual nuts and bolts. Again depending on the system solution. A lot of this may be done in large case for you. As you can see here, this step includes defining system requirements and specifications, what specifically does the system need to do and how precisely, how accurately you require it to do that. Those kinds of things. Testing strategies. How are you going to ensure whether your system requirements and specs are going to be met by a solution and verifying, figuring out how to verify if the solution you have selected is meeting your requirements. At this step you start thinking about what it is going to take for it the operation and maintenance over the life of the project and start planning for that. Staffing, ability to move it to another project. Of those things start to be thought about here. Training, if there is going to be out right -- outreach or a public relations standpoint consideration or recognition of system security and those things planning for evaluation is very important as well as getting more finite testaments of both the benefits and costs you anticipate from the specific design being considered at this point.
Interaction: None
Notes: None

## Slide 60: 3.1 Determining System Requirements and Specifications
Concept of operations- describe how it work
  Design system to assure it will accomplish goals
Performance specifications (Function requirements)
Physical requirements (self-contained trailer, etc.)
System requirements
  Data – type, availability, etc.
  Website
Notes: Key Message: System Requirements and Specs
Background Information: How are you going to ensure whether your system requirements and specs are going to be met by a solution? How will you verify if the solution you have selected is meeting your requirements?
Effective requirements define performance requirements and targets rather than design features
Requirements should link to a user need
Requirements should be verifiable and monitored for compliance
By conducting a thorough and well-focused requirements generation process, agency staff will better manage stakeholder expectations, ensure that the key needs identified earlier are addressed, and gain consistent understanding of and buy-in for the system, and will be able to develop a more realistic estimate of the project deployment schedule and cost.
Interaction: None
Notes: None

## Slide 61: 3.2 Developing the System Design
Define what the system will do
  Know the limitations of the components
  Understand the site conditions
    Terrain
    Other obstacles that could affect placement of devices
  Understand the communications systems
Notes: Key Message: System Design
Background Information: This step includes defining system requirements and specifications, what specifically does the system need to do and how precisely, how accurately you require it to do that. Make sure the system design meets the requirements needed and will actually work for the site conditions in the field.
Interaction: None
Notes: None

## Slide 62: 3.3 Developing a Testing Strategy
Develop a strategy to validate system operations
Schedule in advance of “going live” to enable any issues to be resolved prior to the critical date
Document testing results
Notes: Key Message: Testing Strategy
Background Information: (Broken into two slides) Testing strategies. How are you going to ensure whether your system requirements and specs are going to be met by a solution and verifying, figuring out how to verify if the solution you have selected is meeting your requirements. At this step you start thinking about what it is going to take for it the operation and maintenance over the life of the project and start planning for that.
Interaction: None
Notes: Step two is the concept, development and feasibility assessment

## Slide 63: A Strategy Should Include:
Functional testing
Performance testing
Storage testing (data)
Failure testing
Notes: Key Message: Testing Strategy
Background Information: Testing strategies. How are you going to ensure whether your system requirements and specs are going to be met by a solution and verifying, figuring out how to verify if the solution you have selected is meeting your requirements. At this step you start thinking about what it is going to take for it the operation and maintenance over the life of the project and start planning for that.
Interaction: None
Notes: Step two is the concept, development and feasibility assessment

## Slide 64: 3.4 Planning for Operations and Maintenance
Timeliness of maintenance/repair of work zone ITS is critical for system credibility
  Who is responsible for various aspects of system?
  Contractor or agency (and who within each)
Notes: Key Message: Planning
Background Information: (Broken into two slides) We bring a planning early in step three here, because it's one of the aspects of a deployment that typically unfortunately gets overlooked. One wants to think, know how their system performed and what benefits they have got out of the system, lessons they learn so they can turn around and learn and do a better job next time. Lets you start thinking about it early in the process and figure out what you will be -- what you will evaluate how you will integrate lessons once you are finished, the efforts to get something out and working you get to the end of the project and realize you have not got what you wanted in terms of information and your ability to translate the information to the next -- essentially learned from your experience is hampered.
Criteria, an example here when looking at evaluation plans or planning for evaluation, basically what is your objective for the evaluation you want to do, generating a hypothesis for that objective, identifying what measure of effectiveness would be useful to test your hypothesis and figuring out if I want this measure of effectiveness, what data do I need to have to test that hypothesis or hypotheses.
Interaction: None
Notes: None

## Slide 65: 3.4 Planning for Operations and Maintenance
It is critical to identify needs beyond end of contract if components will be incorporated into the permanent system
Determine staffing needs to operate system
  Trained on system
  Understand goal of system (problem being addressed)
Notes: Key Message: Planning
Background Information: (Broken into two slides) We bring a planning early in step three here, because it's one of the aspects of a deployment that typically unfortunately gets overlooked. One wants to think, know how their system performed and what benefits they have got out of the system, lessons they learn so they can turn around and learn and do a better job next time. Lets you start thinking about it early in the process and figure out what you will be -- what you will evaluate how you will integrate lessons once you are finished, the efforts to get something out and working you get to the end of the project and realize you have not got what you wanted in terms of information and your ability to translate the information to the next -- essentially learned from your experience is hampered.
Criteria, an example here when looking at evaluation plans or planning for evaluation, basically what is your objective for the evaluation you want to do, generating a hypothesis for that objective, identifying what measure of effectiveness would be useful to test your hypothesis and figuring out if I want this measure of effectiveness, what data do I need to have to test that hypothesis or hypotheses.
Interaction: None
Notes: None

## Slide 66: 3.5 Determining Staff Training Needs
In-depth training required to operate and maintain the system
Training required of:
  In-house staff by
    Vendor
    Contractor
Notes: Key Message: Staffing
Background Information: Staffing, ability to move it to another project. Training, if there is going to be out right -- outreach or a public relations standpoint consideration or recognition of system security and those things planning for evaluation is very important as well as getting more finite testaments of both the benefits and costs you anticipate from the specific design being considered at this point.
The amount of training needed will be determined by the approach that will be taken to procure, operate, and maintain the system. If the system will be leased, operated, and maintained by the vendor or a contractor, training of agency staff will focus primarily on operational aspects of the system.
Interaction: None
Notes: None

## Slide 67: 3.6 Planning for Public Outreach
Determine the level of public outreach and types
  Web-based
  Press releases
  Media
Notes: Key Message: Public Outreach
Background Information: An important step in the planning process is to determine the amount and type of public outreach that the agency wants to pursue to alert local residents and businesses to the system and its capabilities, including web-based information. For example, how useful would it be to display real-time traffic information on a website if nobody knew that the website existed or how to access it? Carefully prepared press releases and involvement in community meetings are some of the strategies employed with success by state agencies.
Interaction: None
Notes: None

## Slide 68: 3.7 Investigating System Security
Image: FHWA
Notes: Key Message: Example of a PCMS being hacked
Background Information: Show an example of someone hacking into system.
Interaction: None
Notes: None

## Slide 69: 3.7 Investigating System Security (cont.)
Password security
Vulnerability of components
  Remote locations
    Easy vandalism targets
  Physical security of equipment
Notes: Key Message: Security
Background Information: Agency staff need to take system security into consideration to ensure that access to the ITS application is protected from unauthorized intrusion. System security is especially critical for systems
providing traveler information.
Interaction: None
Notes: None

## Slide 70: 3.8 Planning for Evaluation
The primary purpose:
  Identify changes needed to optimize operation and improve performance
  Understand and quantify benefits of the system
  Document lessons learned
    Issues identified may not be easily fixed for the existing deployment, but,
    Could improve a future deployment
Notes: Key Message: Evaluation
Background Information: Criteria, an example here when looking at evaluation plans or planning for evaluation, basically what is your objective for the evaluation you want to do, generating a hypothesis for that objective, identifying what measure of effectiveness would be useful to test your hypothesis and figuring out if I want this measure of effectiveness, what data do I need to have to test that hypothesis or hypotheses. Key takeaways. A good set of documents in respect to what you are going to do for system testing, how this will operate, what the design looks like, what kind of public outreach if anything is going to be accomplished and so on. The effective system plans that are most effective occur when the goals and objectives are measured and stated explicitly early on and what was used to drive the system design itself.
See page 38 of the guide. A six step process for evaluating ITS projects is shown. The ITS Evaluation Resource Guide contains a more detailed explanation of this six-step process, as well as a discussion of evaluation measures that correspond to overall ITS goal areas – safety, mobility, efficiency, productivity, environmental impacts, and customer satisfaction. Sample evaluation strategies, evaluation plans, test plans, and final reports are also available for downloading from the website.
Page 39 of the guide. Table 8 presents some example criteria that might be used for a work zone ITS evaluation.
Interaction: None
Notes: None

## Slide 71: 3.9 Estimating System Benefits and Costs
Benefits include
  Improved safety
  Improved mobility
  Reduced cost and duration of work zone activities
Notes: Key Message: Benefits and Costs
Background Information: A key part of system planning is estimating system benefits and costs. In estimating the benefits that the system will have on traffic, mobility and safety are both key factors to consider. Estimation of these impacts will become easier as results become available from more ITS in work zone deployments. At present, traffic modeling and traffic flow theory can be used to estimate impacts on delay through factors such as diversion of traffic around the work zone. The level of effort spent to evaluate potential system impacts should be proportional to the size, duration, and complexity of the work zone.
When refining cost estimates, agencies should be sure to consider ancillary costs such as
required training, agency labor, outreach activities, and system maintenance. It is also recommended that agencies include a reserve or contingency fund to pay for unexpected items, such as fixing system integration and communications problems (e.g., costs for cellular modems and pagers, etc.).
System costs will vary widely depending on whether the system is purchased or leased, and whether labor associated with operating and maintaining the system is provided internally by agency staff or by an outside contractor.
Interaction: None
Notes: None

## Slide 72: 3.9 Estimating System Benefits and Costs (cont.)
Costs include
  Training
  Agency labor
  Outreach activities
  System maintenance
  Materials
  Installation
Notes: Key Message: Benefits and Costs
Background Information: A key part of system planning is estimating system benefits and costs. In estimating the benefits that the system will have on traffic, mobility and safety are both key factors to consider. Estimation of these impacts will become easier as results become available from more ITS in work zone deployments. At present, traffic modeling and traffic flow theory can be used to estimate impacts on delay through factors such as diversion of traffic around the work zone. The level of effort spent to evaluate potential system impacts should be proportional to the size, duration, and complexity of the work zone.
When refining cost estimates, agencies should be sure to consider ancillary costs such as
required training, agency labor, outreach activities, and system maintenance. It is also recommended that agencies include a reserve or contingency fund to pay for unexpected items, such as fixing system integration and communications problems (e.g., costs for cellular modems and pagers, etc.).
System costs will vary widely depending on whether the system is purchased or leased, and whether labor associated with operating and maintaining the system is provided internally by agency staff or by an outside contractor.
Interaction: None
Notes: None

## Slide 73: Step 3: Key Takeaway No. 1
Documentation should include plans for:
  System testing
  Operation
  Staffing
  Public Outreach
  Security, and
  Evaluation throughout the duration of the system’s life
Notes: Key Message: Key takeaways for step 3
Background Information: (broken into 3 slides) The main products of Step 3 are detailed system plans that build on the concept of operations from Step 2. The concept of operations describes the objectives of the system and how it would operate to achieve the objectives. Step 3 develops the system requirements and specifications that define what the system will do and ideally include performance targets.
Documentation should include plans for system testing, operating the deployed system, the staffing approach, any necessary public outreach, system security considerations, and evaluation throughout and at the conclusion of the project. It is important to plan for each of these aspects to avoid issues later with system deployment and to ensure that data will be available for system evaluation.
The most effective evaluations occur when the goals and objectives for a work zone ITS are explicitly stated, measurable, and agreed to by all stakeholders. Then it is much easier to pick appropriate performance measures for evaluation and to know what data to collect to best determine system success and value.
Interaction: None
Notes: None

## Slide 74: Step 3: Key Takeaway No. 2
Must plan for each of these aspects to avoid issues with system deployment and ensure data will be available for system evaluation
Notes: Key Message: Key takeaways for step 3
Background Information: (broken into 3 slides) The main products of Step 3 are detailed system plans that build on the concept of operations from Step 2. The concept of operations describes the objectives of the system and how it would operate to achieve the objectives. Step 3 develops the system requirements and specifications that define what the system will do and ideally include performance targets.
Documentation should include plans for system testing, operating the deployed system, the staffing approach, any necessary public outreach, system security considerations, and evaluation throughout and at the conclusion of the project. It is important to plan for each of these aspects to avoid issues later with system deployment and to ensure that data will be available for system evaluation.
The most effective evaluations occur when the goals and objectives for a work zone ITS are explicitly stated, measurable, and agreed to by all stakeholders. Then it is much easier to pick appropriate performance measures for evaluation and to know what data to collect to best determine system success and value.
Interaction: None
Notes: None

## Slide 75: Step 3: Key Takeaway No. 3
Most effective evaluations occur when the goals and objectives are:
  Explicitly stated
  Measurable, and
  Agreed to by all stakeholders
Notes: Key Message: Key takeaways for step 3
Background Information: (broken into 3 slides) The main products of Step 3 are detailed system plans that build on the concept of operations from Step 2. The concept of operations describes the objectives of the system and how it would operate to achieve the objectives. Step 3 develops the system requirements and specifications that define what the system will do and ideally include performance targets.
Documentation should include plans for system testing, operating the deployed system, the staffing approach, any necessary public outreach, system security considerations, and evaluation throughout and at the conclusion of the project. It is important to plan for each of these aspects to avoid issues later with system deployment and to ensure that data will be available for system evaluation.
The most effective evaluations occur when the goals and objectives for a work zone ITS are explicitly stated, measurable, and agreed to by all stakeholders. Then it is much easier to pick appropriate performance measures for evaluation and to know what data to collect to best determine system success and value.
Interaction: None
Notes: None

## Slide 76: Step 4 - Procurement
Source: FHWA
Image: FHWA
Notes: Key Message: Introduce Procurement
Background Information: You can see the basic steps in this -- particular sub steps, assessing what your options are based on your particular situation. Figuring out the type of procurement, mechanism and so on. Basically, the procurement approach is possible. Interaction: None
Notes: None

## Slide 77: Step 4 - Procurement
4.1 Assessing procurement options
4.2 Deciding direct or indirect procurement
4.3 Determining the procurement award mechanism
4.4 Issuing a request for proposals
4.5 Selecting the preferred vendor, consultant, or contractor
Notes: Key Message:
Background Information:
Interaction:
Notes:

## Slide 78: Procurement Overview (Page 42)
Source: FHWA
Notes: Key Message: There are multiple options available – See page 42 of the guide.
Background Information: The key here is that there are a lot of options available for agencies to consider, and some may work better than others depending on the contracting mechanisms and funding available.
Procurement options depend on the characteristics of the ITS
Traditionally, WZ ITS procurement has primarily been for customized ITS solutions
The Potential now exists for agencies and contractors to purchase data collected by private-sector data providers for similar purposes
Interaction: None
Notes: Procure the work zone ITS by first considering a number of options, based on the type of deployment being procured.
Steps include:
•Assessing procurement options
•Deciding direct or indirect procurement
•Determining the procurement award mechanism
•Issuing a request for proposals
•Selecting the preferred vendor, consultant, or contractor
One of the key factors in selecting a procurement approach is the type of ITS you are looking at deploying. If the system is a commercial off-the-shelf product, and you have written a good set of functional requirements and specifications, and plans are in place that are pretty solid, a low-bid mechanism might work well. Then there are more customized solutions where the goals and objectives may be well-defined, but the system components and how they are going to work and how they are going to interface may be a little tougher to realize strictly on a low bid approach. But again, it depends on each agency and the laws and regulations that govern the agency’s contracting mechanisms.
You typically see two general types of procurement methods in place: one that I would call “direct,” which where the agency itself either owns the equipment or leases it. It can be a method where they are paying someone else to put the equipment out there as part of a construction contract and the contractor either installs it or gets a subcontractor to do the work. You can also have an on-call arrangement where the consultant has the equipment and gets paid to use it on an on-call basis at locations that the agency identifies.

## Slide 79: Contracting Options
Traditional sub-contract to main project
Stand alone for a single construction project
Stand alone for multiple construction projects
Notes: Key Message: Contracting Options
Background Information:
Really you can blend, in a number of different ways, one of the key factors is the type of work on ITS if you are looking at deploying. If it is a commercial off-the-shelf product, and you have written a good set of functional requirements and specifications, and plans are in place that are pretty solid, a low bid mechanism might work well. You get into more customized solutions where the goals and objectives may be well-defined, but the system components and how they are going to work and how they are going to interface may be a little tougher to realize strictly on a low bid situation but again it depends on each agency, the laws and regulations that govern each agency in a contracting mechanisms there. You typically see two general types of procurement methods in place. What I would call direct which is one where the agency itself either owns equipment, buys it or release it and they own it, if you will or in a method where they are paying someone else to put the equipment out there whether as part of a construction contract and the contractor either does it itself or gets a subcontractor or perhaps an on-call arrangement where the consultant has equipment and obtained equipment and gets paid to address, on an on-call basis, the locations and work zone situations that the agency calls for.
Interaction: None
Notes: None

## Slide 80: Method 1: Include in Main Construction Contract
  Fits normal low-bid contracting process
  Typically lump sum
  Contractor responsible for product
Notes: Key Message: Discussing four methods for purchasing ITS.
Background Information: An agency can directly procure ITS equipment, services,
and/or data for its own use and dissemination as part of work zone safety and mobility management efforts.
Method 1- Include in Main Construction Contract: It’s Easy, It’s what we do, and Contract people like this method. This is typically lump sum bid item. Some of the characteristics include:
Agency not required to maintain expertise on staff for set up, troubleshooting, maintaining, and updating equipment
Maintenance and removal by vendor allows them to ensure proper operation, quality control over equipment used, and up-to-date equipment
A preferred method by vendors and agencies for commercial off the shelf (COTS) deployments
Direct engagement with vendor keeps high focus on work zone ITS
Interaction: None
Notes: None

## Slide 81: Issues
Low priority to prime contractor
Timing startup is even more important with existing system integration
Lack of communications about traffic switches
Lack of appropriate expertise
Cost
Notes: Key Message: Discuss potential issues with this method
Background Information: ITS is a low priority for the prime because of the cost.
Timing is problematic at best.
Need systems online at start of lane restrictions; integration takes time.
Deductions can’t give drivers back the time they lost.
Very inflexible, and allows limited control.
Interaction: None
Notes: None

## Slide 82: Method 2: Stand-Alone per Project
Allows ITS focus
More control for contractor
More direct oversight by DOT
Better timeline
Notes: Key Message: Method 2
Background Information: Prime Contractor is focused on ITS
Better control for both Contractor and DOT
Leads to better timeline, lets you get started early, which helps integration
Characteristics include:
Contractor has responsibility for determining and selecting a vendor (agency does not make vendor selection)
Contractor determines whether to purchase or lease the system
Agency can retain ability to negotiate with the contractor regarding pricing and other aspects of the ITS deployment
Agency does not have direct link to vendor to provide input on set-up and adjustments during operation
Interaction: None
Notes: None

## Slide 83: Issues with Method 2
Still cannot address rapidly changing construction staging
Susceptible to multiple integration needs
Adds contract management challenges
Cost
Notes: Key Message: Issues with Method 2
Background Information: Lead time is sometimes more than the project
i.e. canned project on the shelf moved up
Interaction: None
Notes: None

## Slide 84: Method 3: Stand-Alone for Multiple Projects
All the benefits of stand alone ITS project
Offers increased flexibility
Not time and resources intensive
Notes: Key Message: Review method 3
Background Information: All the benefits of stand alone ITS project that has increased flexibility and reduced management costs and configuration and integration time.
Interaction: None
Notes: None

## Slide 85: Method 4: On-Call Annual Contract
Annual contract
Offers the most flexibility
Provides options for smaller maintenance projects
Provide options for rapidly changing construction program
Notes: Key Message: Method 4, on-call annual contract
Background Information: Have an annual contract with a specific vendor, which has the most flexibility and provides options for smaller maintenance projects as well as rapidly changing construction program. Bid system components only to be installed and operated via work order – Agency determines need. Bid for consultant services/supplier. Determine need and install and maintain system via work order
Interaction: None
Notes: None

## Slide 86: Purchase of Third-Party Data
Obtain data for performance monitoring
Evaluation of operations
Possibly use for decisions on work zone ITS components
  INDOT working on using INRIX HD data
Notes: Key Message: Purchase 3rd party data
Background Information:
We are seeing increased examples where agencies and contractors are actually able to purchase data from a third party, private-sector data provider for what they are trying to accomplish and use that for works and purposes as well.
Interaction: None
Notes: None

## Slide 87: Key Tips and Takeaways
Work zone ITS does not need to follow the traditional procurement approach
  Hybrid approaches are possible
Agency personnel experiences and capabilities with work zone ITS should be consulted before selecting a procurement method
Notes: Key Message: Review key takeaways
Background Information: (Broken into 2 slides) In this step, the procurement type and mechanism is determined, an RFP is issued, and a proposal is selected.
In procuring work zone ITS, there are three different perspectives: the contracting agency that desires work zone ITS, the contractor responsible for the overall construction project, and the vendor who supplies work zone ITS. Lessons learned from each of these perspectives were gathered from five FHWA-sponsored case studies that examined deployments of ITS in work zones in Effingham, Illinois; Mount Vernon, Illinois; Salt Lake City, Utah; Orem/Provo, Utah; and Las Vegas, Nevada in 2012; interviews with agency officials from five States that are active in work zone ITS; and interviews with four experienced work zone ITS vendors.
Agencies need to consider the necessary personnel experience for operating and maintaining work zone ITS before deciding
whether to purchase or lease work zone ITS, so that the procured system can be effectively operated and maintained.
Regardless of whether ITS is procured directly by an agency or indirectly through a construction contract, it is important
that there be expertise available locally (either on agency, contractor, or vendor staff) who are tasked with day-to-day
responsibility for operations and maintenance of the system to enable quick response and resolution of issues.
Interaction: None
Notes: None

## Slide 88: Key Tips and Takeaways
Including ITS procurement as part of the initial contracting process is usually preferable to change-order additions
Procuring private-sector mobility data may be the simplest approach in certain cases, but
  The type of data procured should match overall system goals and objectives
Notes: Key Message: Review key takeaways
Background Information: (Broken into 2 slides) In this step, the procurement type and mechanism is determined, an RFP is issued, and a proposal is selected.
In procuring work zone ITS, there are three different perspectives: the contracting agency that desires work zone ITS, the contractor responsible for the overall construction project, and the vendor who supplies work zone ITS. Lessons learned from each of these perspectives were gathered from five FHWA-sponsored case studies that examined deployments of ITS in work zones in Effingham, Illinois; Mount Vernon, Illinois; Salt Lake City, Utah; Orem/Provo, Utah; and Las Vegas, Nevada in 2012; interviews with agency officials from five States that are active in work zone ITS; and interviews with four experienced work zone ITS vendors.
Agencies need to consider the necessary personnel experience for operating and maintaining work zone ITS before deciding
whether to purchase or lease work zone ITS, so that the procured system can be effectively operated and maintained.
Regardless of whether ITS is procured directly by an agency or indirectly through a construction contract, it is important
that there be expertise available locally (either on agency, contractor, or vendor staff) who are tasked with day-to-day
responsibility for operations and maintenance of the system to enable quick response and resolution of issues.
Interaction: None
Notes: None

## Slide 89: Step 5 - System Deployment
Source: FHWA
Image: FHWA
Notes: Key Message: Introduce Step 5
Background Information: Quickly introduce this step and review four sub steps
Interaction: None
Notes: None

## Slide 90: Step 5 - System Deployment
5.1 Implementing the system
5.2 Scheduling decisions
5.3 Systems acceptance testing
5.4 Handling major deployment issues
Image: FHWA
Notes: Key Message: Step 5- System Deployment
Background Information:
5.1 Implementing the system
5.2 Scheduling decisions
5.3 Systems acceptance testing
5.4 Handling major deployment issues
Interaction:
Notes:

## Slide 91: Implementing System Plans
Small projects
  Track system deployment, monitoring, and system validation
Large project
  Requires significant staff time for testing, troubleshooting, validating, monitoring, and system maintenance
Staff needs expertise with ITS deployment
Notes: Key Message: Implementing system plans
Background Information: For small, COTS systems that are intended to operate independently, agency involvement during deployment may consist of the project engineer and inspectors keeping track of the system and monitoring and validating the information being collected and
disseminated. For larger and/or more novel or complex deployments and deployments that involve integration with existing ITS components, the level of agency involvement may span across several offices and divisions, and require significant staff time to test, troubleshoot, validate, monitor, and maintain the system.
Interaction: None
Notes: None

## Slide 92: Scheduling
Schedule lead time to deploy system
Incorporate calibration time into schedule
Plan for the unexpected
  i.e., weather
Notes: Key Message: Scheduling
Background Information:
Some agencies that are incorporating work zone ITS deployments into their construction contracts require that the system be operating before actual construction work starts. Contractors need to allow sufficient time for this requirement in their overall project scheduling. Agencies or their consultants who are deploying work zone ITS themselves to support a particular project need to plan sufficient lead time as well.
Systems that provide real-time travel time and delay information to motorists typically require some level of calibration to fine tune the values presented. Normally, this will need to occur after work and its associated congestion have begun. Efforts should be taken to ensure the availability of staff to assist during the calibration process very early in the project. Continued display of inaccurate travel times or delays will significantly erode credibility of the system with drivers, and make it more difficult to get drivers to react to the real-time information.
It can be difficult to predict in advance the traffic impacts that a work zone might generate, and thus the amount of coverage needed for a work zone ITS deployment. It can be beneficial for agencies to have contingency plans, or at least have options available to them, with regards to modifying the system slightly. For example, an agency can designate that the contractor obtain an initial work zone COTS system meeting a set of specifications and equipment requirements as part of the original bid process. However, if additional equipment or functionalities are later found to be required, the potential implications for using a change order process to obtain that additional equipment or functionality should be thought through.
Interaction: None
Notes: None

## Slide 93: Contract Coordination
Could be critical, depending on procurement method
  System required prior to work beginning?
  Allow time for validation testing and system calibration
  Will system components have to be relocated during construction?
Notes: Key Message: Discuss contract coordination as this relates to system deployment
Background Information: At this point efforts have been focused on procurement of the system based on the planning and system design. We will now look at deployment efforts. The deployment could be pretty straightforward, depending on the project and the system used. The contracting agency may be doing some oversight and most of the deployment occurs within the contracting consultant or vendor area of responsibility. If it is a more customized solution, the contracting agency might be much more heavily involved in the implementation.
One of the key factors to successful deployment is scheduling the equipment and system. In most cases you need to make sure that you've got adequate time first to test the system and make sure it is performing in the desired way and also to calibrate and make adjustments. As projects move, along there are field changes that can influence a work zone ITS deployment. Adjustment may need to be made in terms of scheduling due to changing needs as the project moves forward.
Interaction: None
Notes: None

## Slide 94: Key Tips and Takeaways
Allow for adequate start-up and calibration time
Significant resources may be required to remain on schedule
  Consider the potential for the unexpected to occur
New technologies may require longer testing times to achieve acceptable performance levels
Notes: Key Message: review tip and takeaways
Background Information: Coordinating the deployment of the work zone ITS needs to occur in conjunction with other aspects of the project, including phasing and any other TMP strategies being implemented for the project.
There should be a solid plan, but recognize that ITS integration is a process and should include the ability to be flexible, depending on what other changes have occurred between the time when the planning process started and when deployment actually occurs. Planning is everything, but plans themselves are often less valuable because of the fact you have always got to be flexible and constantly adjusting.
Problems will arise—such as the operation of sensors, communications (wireless or wired), calibration, or software—and will take time to address. These “bugs” require time to locate and address. Failure to allow for sufficient start-up time can lead to less than optimal performance of the system during the initial days of the project. Unfortunately, this is often the time at which the system is most needed, as drivers are encountering unexpected conditions due to the capacity and operational constraints imposed by the MOT plan, are surprised, and need and would benefit significantly from having improved information and guidance in how to best accommodate the work zone.
Although it is desirable to begin the process for considering, planning, designing, and deploying a work zone ITS early in the overall project development process, circumstances sometimes dictate that an accelerated timeline be followed. It is important to recognize when such circumstances arise and to dedicate enough resources to be successful in meeting that timeline.
Interaction: None
Notes: None

## Slide 95: Step 6 - System Operation, Maintenance, and Evaluation
Image: FHWA
Notes: Key Message:
Background Information: The last step is system operation, maintenance, and evaluation. Hopefully by this time the ITS system had been set up and tested, calibrated, doing what it is intended to do, having the positive impacts that all the stakeholders had anticipated. At this point monitoring and dealing with changing conditions with continued monitoring of the system is required. There are a lot of cases where systems go in and it works great initially but then not enough attention is given to monitor the functioning of the system, and then components start to fail or need to be recalibrated due to changing conditions. Suddenly without warning, system performance is decreases or fails and the level of accuracy or system benefits are not being achieved.
Interaction: None
Notes: Read each step included here.

## Slide 96: Step 6 - System Operation, Maintenance, and Evaluation
6.1 Dealing with changing work zone conditions
6.2 Using and sharing ITS information
6.3 Maintaining adequate staffing
6.4 Leveraging public support
6.5 Conducting system monitoring and evaluation
Notes: Key Message:
Background Information:
Interaction:
Notes:

## Slide 97: Flexibility is Key Under Changing Conditions
Changing work zone conditions during various times of the day, or staging changes
Field conditions may differ from what was expected
Notes: Key Message: Changing conditions
Background Information: Flexible and proven work zone ITS that can be dynamic or react in real-time is important for meeting real-time conditions. Not surprisingly, most agencies select highly portable systems built around proven technologies and wireless communications. Some systems have capabilities to communicate via cellular network or satellite depending on whether or not cellular communication is available in an area. Sometimes conditions in the field may differ from what was expected during systems planning and design, and adjustments may be needed. For example, queues may be longer or shorter than what was estimated before construction actually started. Personnel should monitor conditions in the field such that if queues regularly extend beyond the system signs (or detectors), the agency/contractor can consider adjusting the placement of the system components to make the most effective use of the system or adding additional devices to extend coverage.
Interaction: None
Notes: None

## Slide 98: Information From The Work Zone ITS Should Be Used and Shared
Traffic management
Work zone hours
Lane closure schedules
Alternate routes
Diversions messages or
Public outreach
Notes: Key Message: Sharing ITS information
Background Information:
Information gathered from the work zone ITS might be used internally for traffic management purposes and to inform the use of other TMP strategies. Information about the work zone may provide insights about adjusting work zone hours, the lane closure schedule, the procedure to identify incidents, or fine tuning of alternate routes, diversion messages, or public outreach efforts. Information gathered from the work zone ITS might be used internally for traffic management purposes and to inform the use of other TMP strategies. Information about the work zone may provide insights about adjusting work zone hours, the lane closure schedule, the procedure to identify incidents, or fine tuning of alternate routes, diversion messages, or public outreach efforts. It is important to assess and update expectations based on true experiences of the deployment in the work zone. The deployment may have greater or lesser impacts than originally anticipated, and it is important for stakeholders to understand why that is the case. One of the most valuable products of ITS work zone applications is the development of real-time information
that can be disseminated to a wide variety of users. ITS work zone systems collect data from several different types of roadside systems, process the data, and – with minimal human interaction – translate those data into valuable information for facility operators, emergency responders, and the traveling public.
Interaction: None
Notes: None

## Slide 99: Staffing and Public Support
6.3 Maintaining adequate staffing
  Contractor
  In-house
6.4 Leveraging public support
  Keep public informed regarding ITS usage
  Information on intended benefits, temper expectations
  Update on actual benefits
Notes: Key Message: Staffing and Public Support
Background Information: If operations and maintenance are contracted out, it is the contractor’s responsibility to ensure that adequate, trained staff is available. However, if in-house staff are engaged, the agency must take steps to ensure that it has multiple staff members trained in system operations, maintenance, and troubleshooting. It is in the agency’s best interest to select a set of project personnel who are expected to be available for the duration of the project.
Publicizing the advanced features of the work zone system and the type of information that will be available to the public is the first stage in developing public support for these systems. In this early stage, while it is important to share potential system benefits with the public, it is likewise important to temper expectations of the system, in case any of the benefits do not ultimately develop. Support from the public and elected officials combined with quantified benefits will help to ensure long-term funding availability for appropriate applications of ITS in future work zones.
Interaction: None
Notes: None

## Slide 100: System Monitoring
Based on the evaluation plan from Step 3
Collected data and field observations should be analyzed
Monitor over multiple phases of the project
Notes: Key Message: Monitoring and Evaluation
Background Information: (Broken into 3 slides) It is important to monitor the work zone ITS during its operation to ensure that it is working correctly and meeting the needs of its users, and that the vendor is meeting contract obligations. The data collected and analyzed over the course of the project can then be used as part of a more comprehensive evaluation at the conclusion of the project. In some instances, it may be necessary to modify the deployment to improve operations based on the results from system monitoring. System monitoring and evaluation will be conducted based on the evaluation plan from Step 3. Data should be collected throughout the course of the ITS deployment according to the plan. Various data elements can be analyzed periodically throughout the course of the project to assess the system performance. Data alone will not be able to address all aspects of the ITS deployment that need to be monitored. Agency staff also need to make observations in the field, which can be logged as qualitative data. Together, the quantitative data and qualitative observations will help ensure that the system is working correctly or identify any changes that may need to be made.
Interaction: None
Notes: None

## Slide 101: System Modifications
Identify modifications for improvement
Modifications may require change orders
Image: ATSSA
Notes: Key Message: Monitoring and Evaluation
Background Information: (Broken into 3 slides) It is important to monitor the work zone ITS during its operation to ensure that it is working correctly and meeting the needs of its users, and that the vendor is meeting contract obligations. The data collected and analyzed over the course of the project can then be used as part of a more comprehensive evaluation at the conclusion of the project. In some instances, it may be necessary to modify the deployment to improve operations based on the results from system monitoring. System monitoring and evaluation will be conducted based on the evaluation plan from Step 3. Data should be collected throughout the course of the ITS deployment according to the plan. Various data elements can be analyzed periodically throughout the course of the project to assess the system performance. Data alone will not be able to address all aspects of the ITS deployment that need to be monitored. Agency staff also need to make observations in the field, which can be logged as qualitative data. Together, the quantitative data and qualitative observations will help ensure that the system is working correctly or identify any changes that may need to be made.
Interaction: None
Notes: None

## Slide 102: System Evaluation
Document
  Lessons learned
  Benefits
Image: FHWA
Notes: Key Message: Monitoring and Evaluation
Background Information: (Broken into 3 slides) It is important to monitor the work zone ITS during its operation to ensure that it is working correctly and meeting the needs of its users, and that the vendor is meeting contract obligations. The data collected and analyzed over the course of the project can then be used as part of a more comprehensive evaluation at the conclusion of the project. In some instances, it may be necessary to modify the deployment to improve operations based on the results from system monitoring. System monitoring and evaluation will be conducted based on the evaluation plan from Step 3. Data should be collected throughout the course of the ITS deployment according to the plan. Various data elements can be analyzed periodically throughout the course of the project to assess the system performance. Data alone will not be able to address all aspects of the ITS deployment that need to be monitored. Agency staff also need to make observations in the field, which can be logged as qualitative data. Together, the quantitative data and qualitative observations will help ensure that the system is working correctly or identify any changes that may need to be made.
Interaction: None
Notes: None

## Slide 103: Evaluation
The rational assessment of how well project goals and objectives are being achieved
Source: FHWA
Images: FHWA
Notes: Key Message: Evaluation
Background Information: A major objective of the final evaluation is to document lessons learned and benefits of the ITS deployment. This might include the collection of some final qualitative data from stakeholders, e.g., surveys or interviews. Analysis of all collected quantitative and qualitative data that has been collected over the course of the project should be conducted as described by the evaluation plan. The results, conclusions, and recommendations of the evaluation should be documented in a final report. These results can be used not only by the project partners for continual refinement of similar systems at other locations, but also by others wanting to implement similar systems in the future.
Interaction: None
Notes: None

## Slide 104: Key Tips and Takeaways
Flexibility is important
Field conditions may differ significantly from what was expected in system planning and design
Managing expectations for the system continues to be important
Notes: Key Message: Review tips and takeaways
Background Information: Flexibility is important; field conditions may differ significantly from what was expected in system planning and design
Managing expectations for the system continues to be important
Verification of information being disseminated to the public is critical
A final evaluation that identifies and documents key findings, lessons learned, etc. is a valuable learning tool for future efforts
Interaction: None
Notes: None

## Slide 105: Key Tips and Takeaways (cont.)
Verification of information being disseminated to the public is critical
A final evaluation is a valuable learning tool for future efforts, to identify and document:
  Key findings
  Lessons learned
Notes: Key Message: Review tips and takeaways
Background Information: Flexibility is important; field conditions may differ significantly from what was expected in system planning and design
Managing expectations for the system continues to be important
Verification of information being disseminated to the public is critical
A final evaluation that identifies and documents key findings, lessons learned, etc. is a valuable learning tool for future efforts
Interaction: None
Notes: None

## Slide 106: Knowledge Check
What are the two strategies for managing Smarter Work Zones?
List some potential ITS technologies to mitigate work zone impacts?
What are the six steps within the ITS Implementation Guide?
Notes: Key Message: Review module objectives
Background Information:
What are the two strategies for managing Smarter Work Zones? Project Coordination and Technology Applications
List some potential ITS technologies to mitigate work zone impacts? Traffic monitoring and management, Traveler information, Queue detection and warning, Incident detection and management, Dynamic Lane Merge, Queue Warning Systems, Variable Speed Limits (VSL), Traffic Management/Route Choice, Automated Speed Enforcement, and Performance Monitoring/Management
List the six step within the ITS Implementation Guide?
Assessment of Needs
Concept Development and Feasibility
Detailed System Planning and Design
Procurement
System Deployment
System, Operation, Maintenance, and Evaluation
Interaction: Ask students questions and allow them time to respond. Do not answer the questions for the students
Notes: None

## Slide 107: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: If no questions, you may ask a few yourself.