## Slide 1: 1. Introduction
Work Zone Strategies
https://patch.com/pennsylvania/northwhitehall/coplay-creek-road-closed-for-repairs_345b7cce
Notes: Key Message: Module Opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s move to the next module. In this module {name}, we will.. {next slide}
Suggested Questions: None
Possible Problems: None

## Slide 2: Module Objectives
Define work zone strategies
Discuss the need for work zone strategies
Discuss Transportation Management Plans (TMP)
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Work Zone “Strategies”
An approach for mitigating the impacts of work zones, while ensuring constructability
Must be evaluated when there are two or more competing interests or alternatives
Strategy: an approach, method, or series of maneuvers for obtaining a specific goal or result
Notes: Key Message: Define Work Zone “Strategies”
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A strategy is an approach to mitigate the impacts of construction projects, while ensuring constructability. Work zone impacts management strategies are intended to minimize traffic delays, maintain or improve motorist and worker safety, and maintain access for businesses and residents.
Suggested Questions: What is a strategy?
Additional Information: Strategy: an approach, method, or series of maneuvers for obtaining a specific goal or result
Possible Problems: None

## Slide 4: Work Zone “Strategies”
Once selected, they are used to develop:
  Contract requirements
  Transportation Management Plans (TMP)
    A Temporary Traffic Control Plan (TTC) Plan
All designed to OPTIMIZE the cost and effectiveness of construction, traffic management, safety, mobility & social needs
Notes: Key Message: Discuss strategy considerations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Once selected, strategies are turned into a Traffic Control Plan (TCP) and contract requirements. Both are designed to OPTIMIZE the cost and effectiveness of construction, traffic management, safety, mobility and social needs.
Suggested Questions: None
Additional Information: Both are designed to OPTIMIZE the cost and effectiveness of construction, traffic management, safety, mobility and social needs.
Possible Problems: Keep this simple. More on this topic later.

## Slide 5: Work Zone “Strategies”
Become more important as the job complexity increases:
  Size
  Type of work
  Work duration
May present conflicting objectives
May minimize construction costs AND user costs
Notes: Key Message: How do we optimize safety and mobility in work zones?
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The “Strategies” become more important as the job complexity increases. The application of sound WZ strategies can reduce cost, for example, by accelerating the construction schedule.
Suggested Questions: Which factors impact the selection of a strategy?
Additional Information: More on this point later on during the course.
Possible Problems: None

## Slide 6: Why do we Need Work Zone Strategies? And Now?
Work zone fatalities remain high
Work zone congestion is worsening
Customer dissatisfaction is high
The Work Zone Safety and Mobility Rule requires a Transportation Management Plan (TMP) for all Federal-aid highway projects
Notes: Key Message: How do we optimize safety and mobility in work zones?
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Section 630.1012 of the Work Zone Safety and Mobility Rule states that in all Federal-Aid highway projects the State shall develop a TMP that consists of a Temporary Traffic Control (TTC) plan and addresses both Transportation Operations (TO) and Public Information (PI) components. The required components of a TMP vary based on whether the project is “significant”.
Suggested Questions: Which factors impact the selection of a strategy?
Additional Information: More on this point later on during the course. 835 WZ fatalities in 2007.
Possible Problems: None

## Slide 7: Traffic Safety: Is There a Problem?
891 work zone fatalities in 2022
94 worker fatalities
Source: www.workzonesafety.org
Notes: Key Message: Quantify the safety problem in the USA and in the state
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Traffic safety is a serious problem in the US and around the world.
Suggested Questions: Before showing the slide, may ask: How many people die in US work zones every year? After saying approximately 38,000, may say that 58,000 US soldiers were lost at the Vietnam War, or that 40,000 attend an NFL game every week. Try to relate the number to a group of people they can visualize or relate to.
Additional Information: Worker fatalities are included in the “pedestrian” category. For specific state statistics, go to https://workzonesafety.org/work-zone-data/work-zone-traffic-crash-trends-and-statistics/
Other information to be used at the discretion of the instructor.
Possible Problems: This slide reflect the LATEST known data. This is usually 1 or 2 years behind. As new data are released, we will update this slide.
State 2017 Data:
Alabama 948 948
Alaska 79 79
Arizona 1000 1,000
Arkansas 493 493
California 3602 3,602
Colorado 648 648
Connecticut 278 278
Delaware 119 119
District of Columbia 31 31
Florida 3112 3,112
Georgia 1540 1,540
Hawaii 107 107
Idaho 244 244
Illinois 1097 1,097
Indiana 914 914
Iowa 330 330
Kansas 461 461
Kentucky 782 782
Louisiana 760 760
Maine 172 172
Maryland 550 550
Massachusetts 350 350
Michigan 1030 1,030
Minnesota 357 357
Mississippi 690 690
Missouri 930 930
Montana 186 186
Nebraska 228 228
Nevada 309 309
New Hampshire 102 102
New Jersey 624 624
New Mexico 379 379
New York 999 999
North Carolina 1412 1,412
North Dakota 115 115
Ohio 1179 1,179
Oklahoma 655 655
Oregon 437 437
Pennsylvania 1137 1,137
Rhode Island 83 83
South Carolina 988 988
South Dakota 129 129
Tennessee 1040 1,040
Texas 3722 3,722
Utah 273 273
Vermont 69 69
Virginia 839 839
Washington 565 565
West Virginia 303 303
Wisconsin 613 613
Wyoming 123 123
Total 37,133 37,133

## Slide 8: USA Work Zone Fatalities: 2013-2022
USA Work Zone Fatalities: 2007-2018
Source: National Work Zone Safety Information Clearinghouse
Notes: Key Message: Quantify WZ fatalities in the USA
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We reached an all-time high in work zones fatalities in 2002. Since then, the numbers have declined but they are on the upswing again! We can still do better!
Suggested Questions: Do you see any trends?
Additional Information: These figures include both workers, motorists and pedestrians. http://www.workzonesafety.org/crash_data/
2017 STATE DATA: Format 3 numbers):
FATALITIES IN MOTOR VEHICLE TRAFFIC CRASHES IN WORK ZONE BY STATE AND YEAR
FATALITY ANALYSIS REPORTING SYSTEM (FARS) 2016 FINAL AND 2017
(State, 2016 fatalities, 2017 fatalities, 2016+2017)
Alabama 13 24 37
Alaska 2 0 2
Arizona 9 15 24
Arkansas 14 21 35
California 75 48 123
Colorado 7 17 24
Connecticut 5 6 11
Delaware 2 3 5
Dist of Columbia 0 1 1
Florida 80 76 156
Georgia 41 60 101
Hawaii 3 3 6
Idaho 0 7 7
Illinois 44 27 71
Indiana 18 28 46
Iowa 11 10 21
Kansas 6 12 18
Kentucky 11 15 26
Louisiana 12 11 23
Maine 1 5 6
Maryland 5 14 19
Massachusetts 6 2 8
Michigan 18 25 43
Minnesota 12 10 22
Mississippi 7 4 11
Missouri 8 15 23
Montana 1 1 2
Nebraska 13 8 21
Nevada 14 14 28
New Hampshire 3 0 3
New Jersey 7 6 13
New Mexico 8 4 12
New York 8 3 11
North Carolina 13 11 24
North Dakota 6 0 6
Ohio 27 25 52
Oklahoma 17 12 29
Oregon 7 3 10
Pennsylvania 16 20 36
Rhode Island 1 1 2
South Carolina 4 20 24
South Dakota 1 1 2
Tennessee 13 10 23
Texas 172 165 337
Utah 5 5 10
Vermont 1 0 1
Virginia 12 11 23
Washington 7 4 11
West Virginia 1 2 3
Wisconsin 11 9 20
Wyoming 3 5 8
National 781 799 1,580
Puerto Rico 1 0 1

## Slide 9: National Work Zone Safety Information Clearinghouse
Internet work zone resource
www.workzonesafety.org
Notes: Key Message: Introduce the WZSC
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Work Zone Safety Clearinghouse is a good resource for everything related to work zones. It contains links to the various states’ TTC standards, a video vault, the states’ approved product lists and more. It is run by Texas A&M University and funded by the Federal Highway Administration. It is an excellent resource. You can reach it at workzonesafety.org.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 10: Factors for Work Zone Crashes
Highway maintenance & improvement projects
More vehicle-miles driven
Unfamiliar conditions
Hazards & workers present
Image: ATSSA
Notes: Key Message: Why Crashes in Work Zones?
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: What does “normal” mean? Familiar? Ideal?
Additional Information: Self explanatory
Possible Problems: None

## Slide 11: Factors for Work Zone Crashes
Users unfamiliar with work zones
Distracted drivers
Aggressive drivers
Speeding
Improper temporary traffic control
Image: ATSSA
Notes: Key Message: Why Crashes in Work Zones?
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Do you think improper (substandard) designs contribute to crashes? Try to turn into a discussion.
Additional Information: Try to turn the last bullet into a discussion. Do improper design contribute to crashes in WZ?
Possible Problems: None

## Slide 12: Negative Consequences of Work Zones
Responsible for 24% of non-recurring freeway delay
2nd leading cause of public dissatisfaction with transportation (behind poor traffic flow)
Image: FHWA
Notes: Key Message: Work zones can bring negative consequences
Est. Presentation Time: One minute.
Explanation of Cues/Builds: None.
Suggested Comments: The instructor should summarize the following details, which expand the three bulleted items on the slide:
A 2002 study by the Dept of Energy indicates that WZs are responsible for almost a quarter of all non-recurring delay.
Looking at this from a customer service perspective, WZs are the second leading cause of dissatisfaction - - 32% of survey respondents indicating they were not satisfied.
Suggested Questions: None.
Additional Information: Information in first bullet point obtained from U.S. Department of Transportation, Federal Highway Administration, A Snapshot of Peak Summer Work Zone Activity Reported on State Road Closure and Construction Websites. Washington, D.C., August 2002. Information in second bullet point obtained from U.S. Department of Energy, Temporary Losses of Highway Capacity and Impacts on Performance, Oak Ridge National Laboratory (ORNL/TM-2002/3). May 2002. Information in third bullet point obtained U.S. Department of Transportation, Federal Highway Administration, Moving Ahead: The American Public Speaks on Roadways and Transportation Communities. FHWA-OP-01-017. Washington, D.C., 2001.
Possible Problems: No need to mention the source of the information.

## Slide 13: Work Zone Risk Factors
Confusing information sources
Distractions
Roadside hazards
Lack of positive guidance
Lack of traveler information
Inattentive driving
Aggressive driving/speeding
Improper TTC
Drivers
Design
Image: ATSSA
Notes: Key Message: Discuss risk factors
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None.
Suggested Comments: The risk factors that apply to all roadways are often amplified in work zones. Some risk factors are associated with drivers and we’ve already identified improvement actions in that area. Many risk factors are within the influence of the design process:
Confusing Information Sources – driving is an information processing task. Work zones inherently involve additional information processing. If information sources are confusing or even conflicting, it will degrade from driver performance.
Distractions – Distractions can be thought of as irrelevant but compelling information. Construction operations are interesting to observe but divert mental energy from driving.
Roadside Hazards – Many work zones introduce additional roadside hazards (pavement drop offs, large equipment) with limited separation. These features are sometimes necessary for construction but run contrary to roadside design principles.
Lack of Positive Guidance – As the complexity of the driving environment increases, drivers need additional assistance to perform successfully. Positive guidance is the approach to providing that assistance. If we don’t provide the guidance the probability for negative outcomes increases.
Suggested Questions: None.
Additional Information: None.
Possible Problems: None.

## Slide 14: The Positive Side of Work Zones
Better infrastructure
Safer roads
Added capacity
Improved mobility
Work zones resulted in the highways we have today!
Image: ATSSA
Notes: Key Message: Discuss the positive side of WZ
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: WZ are a necessity! They also have a positive side. They are a “necessary evil”!
Suggested Questions: None
Additional Information: Try to turn the last bullet into a discussion.
Possible Problems: None

## Slide 15: Conflicting interests?
Maximum levels
of safety
Maintain traffic flow
Keep costs down
TTC impact on traffic flow is important,
but not at the expense of safety!
Notes: Key Message: Discuss conflicting goals
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The more “safety” we provide, the more expensive the project will likely be. Our job is to achieve the best balance between these 2. This is not easy since these are conflicting goals. You should pull more for safety, rather than to cut costs. “Maintain traffic flow” is not mutually exclusive. Some strategies can accommodate both safety and mobility.
Suggested Questions: None.
Additional Information: Maintaining traffic flow and maintaining maximum levels of safety are not necessarily mutually exclusive. Some strategies can do both. Make sure to mention this.
Possible Problems: Turn into a discussion, if possible.

## Slide 16: The Designer’s Dilemma
Safety vs. Mobility vs. Cost
Notes: Key Message: Discuss conflicting goals
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None
Suggested Comments: So this is the designer’s dilemma. What do you think is more important?
Suggested Questions: Which is more important? Safety or cost? SAFETY!
Additional Information: Try to generate discussion
Possible Problems: None.

## Slide 17: Work Zone Costs
Direct costs
  Labor and materials
Indirect costs
  Crashes, injuries, fatalities
  Property damage
  Delays
  Vehicle costs
  Fuel consumption
  Quality of life
Notes: Key Message: Discuss work zone costs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Provide examples as needed.
Suggested Questions: What are the costs of highway work zones?
Additional Information: Indirect costs are “societal”; costs to society.
Possible Problems: None.

## Slide 18: The Designer’s Role
Critical to work zone safety
Assess and consider ALL factors that may impact the safety and mobility of all people within the work zone
  Motorists
  Pedestrians
  Cyclists
  Workers
Notes: Key Message: Discuss the designer’s role
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The designer has then a critical role: to assess the needs of the work zone users and optimize their safety and mobility. Sounds easy!
Suggested Questions: Can you satisfy the needs of ALL users? No, but we should consider the needs of ALL!
Additional Information: None
Possible Problems: None.

## Slide 19: The Designer’s Role
To consider ALL factors and ALL users involved, the standards and guidelines, and apply engineering judgment to develop the BEST possible strategy
Notes: Key Message: Discuss the designer’s role
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Your job as a designer is to take all this information, standards and guidelines and APPLY them to a specific situation utilizing your best engineering judgment and CONSIDERING the needs of ALL users.
Suggested Questions: So, what is the role of the designer in all this? What is engineering judgment? (next slide)
Additional Information: None
Possible Problems: None.

## Slide 20: Engineering Judgment
An engineer’s evaluation of available pertinent information, and the application of appropriate principles, standards, guidance, and practices for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device.
MUTCD Definition 64, Page 14
Notes: Key Message: Define Engineering Judgment
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click.
Suggested Comments: Engineering judgment is an engineer’s evaluation of available pertinent information, and the application of appropriate principles, standards, guidance, and practices for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device. Notice that engineering judgment DOES NOT have to be documented. In other words, you don’t have to explain your reasoning. For example, say you need to extend the buffer space because of a downhill. I would extend it by 10% but you might extended by 20%. They are both right because we have different judgment!
Additional Information: MUTCD Definition 64, page 14
Possible Problems: None.

## Slide 21: How do we optimize safety and mobility in work zones?
Analyzing multiple strategies
  Advantages and disadvantages
Considering the needs of all the stakeholders
Image: ATSSA
Notes: Key Message: How do we optimize safety and mobility in work zones?
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are multiple strategies to consider, each one with advantages and disadvantages. As a designer we must carefully study these and select the best one?
Suggested Questions: How do you define the “best one”? Performance? Objectives?
Additional Information: None
Possible Problems: None

## Slide 22: Project-Level Work Zone Strategies
All projects require a strategy, an approach!
These strategies are outlined in Transportation Management Plans (TMPs)
TMP
Notes: Key Message: Discuss Project-Level Work Zone Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: All projects require a strategy or set of strategies that will accommodate needed construction operations while maintaining acceptable transportation service. These strategies are outlined in Transportation Management Plans (TMPs)
Suggested Questions: Where do you “present” the strategies to implement?
Additional Information: None
Possible Problems: None

## Slide 23
TMP
PI&O
TTC Plan
TO
The “strategies” presented are organized around this concept!
Umbrella image: https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A TMP is basically an umbrella term for three components (next slide). Although a full TMP document is not developed until design, conducting some TMP analyses during systems planning and preliminary engineering will help ensure that the TMP development and implementation costs are included in the project budget. At this early stage, more alternatives for addressing work zone impacts are available, so a broader range of strategies can be chosen. Early TMP development will also help with scheduling and coordinating projects to minimize the cumulative work zone impacts of multiple projects along a corridor or in a region. This includes examining the adequacy of detour or alternate routes and coordinating with the agencies responsible for those routes. Another strategy available in the earlier stages of project development is to consider work zone impacts in the evaluation and selection of design alternatives. For some projects it may be possible to choose a design alternative that alleviates many work zone impacts. These broader strategies cross various disciplines and highlight the need for a multidisciplinary approach. For the TMP, work zone impact management strategies should be identified for both the mainline and detour routes for the selected construction phasing/staging approach(es).
Suggested Questions: What is a TMP?
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here.

## Slide 24: What is a TMP?
A set of coordinated transportation management strategies
Describes how they will be used to manage the work zone impacts of a road project
The TTC Plan is just one part
TMP
https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A TMP lays out a set of strategies for managing the work zone impacts of a project. Because work zone objectives, needs, and issues vary from project to project, the scope, content, and degree of detail in a TMP will also vary from project to project. It is ultimately up to the agency to establish and implement TMPs that best serve the mobility and safety needs of the motoring public, construction workers, businesses, and community. Many States have already recognized the benefits of developing and implementing TMPs, or similar plans.
Suggested Questions: What is a TMP?
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here.

## Slide 25: TMPs Require
Temporary Traffic Control Plan (TTC Plan)
If “significant project”:
  Public information and outreach (PI&O) plan
  Transportation operation (TO) plan
https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Work Zone Safety and Mobility Rule states that for significant projects the State shall develop a TMP that consists of a Temporary Traffic Control (TTC) plan and addresses both Transportation Operations (TO) and Public Information (PI) components. For individual projects or classes of projects that the State determines to have less than significant work zone impacts, the TMP may consist only of a TTC plan. However, states are encouraged to also consider TO and PI issues for these projects. Most agencies have temporary traffic control (TTC) plan policies and report procedures in place for basic TMPs, in the form of traffic control plans (TCPs) or maintenance of traffic (MOT) plans.
Where appropriate, the management strategies should be documented on plan sheets. Agencies may elect to develop separate sections or plans specific to the PI and/or TO strategies to distinguish them from the TTC strategies.
Suggested Questions: What are the components of a TMP?
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here.

## Slide 26: What is a “Significant Project”?
Projects that alone or in combination with other concurrent projects nearby, are anticipated to cause sustained work zone impacts that are greater than what is considered tolerable based on State policy and/or engineering judgment
Image: FHWA
Notes: Key Message: FHWA criteria for a significant project
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: A significant project is a project that alone or in combination with other concurrent projects nearby, are anticipated to cause sustained work zone impacts that are greater than what is considered tolerable based on State policy and/or engineering judgment.
A TMP must be prepared for all federal-aid projects . Non significant projects require only a TTC plan but the PI and TO are encouraged.
Suggested Questions: Do you feel this is an acceptable definition of significant project?
Additional Information: Significant Projects: As defined in Section 630.1010 of the Rule, a significant project is one that, alone or in combination with other concurrent projects nearby is anticipated to cause sustained work zone impacts that are greater than what is considered tolerable based on State policy and/or engineering judgment.
Possible Problems: None

## Slide 27: What is a “Significant Project”?
All Interstate system projects
Within the boundaries of a designated Transportation Management Area (TMA)
  > 200,000 population
That occupy a location for more than three days with either intermittent or continuous lane closures shall be considered as significant projects
T
M
A
Notes: Key Message: FHWA criteria for a significant project.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: All Interstate projects that are within the boundaries of a designated Transportation Management Area (TMA) that occupy a location for more than three days with either intermittent or continuous lane closures shall be considered significant. States may request an exception to these provisions if they feel a project of this type does not have significant sustained impacts. Various agencies will have different judgments about what is a tolerable impact.
Suggested Questions: Do you feel this is an acceptable definition of significant project?
Additional Information: A Transportation Management Area (TMA) is an area designated by the Secretary of Transportation, having an urbanized area population of over 200,000, or upon special request from the Governor and the MPO designated for the area.
Possible Problems: This definition varies by State.

## Slide 28: What if the Project is Not “Significant”?
The TMP may consist only of a TTC Plan
Agencies are encouraged to consider TO and PI&O issues for these projects as well
Not significant does not mean “insignificant”!
https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: FHWA criteria for a significant project.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: TMPs are required for ALL projects on Federal-Aid highways. What varies is the level of detail and the components of the TCP. If the project is not significant, then only a TCP is required, however agencies are encouraged (not required) to consider the TO and PI components as well.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 29: Temporary Traffic Control Plan (TTC Plan) Component (Module 2)
A set of drawings and other information detailing how the work will be accomplished
A plan for maintenance and control of traffic during work
Temporary traffic control measures to be used for facilitating road users through a work zone safely
Based on applicable TTC standards and guidelines
Notes: Key Message: Define TCP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A TCP is simply a plan for maintenance and control of traffic during work. It may be part of a larger umbrella term called a TMP.
Suggested Questions: What is the TCP component?
Additional Information: See MUTCD Section 6C-1. A temporary traffic control plan describes temporary traffic control measures to be used for facilitating road users through a work zone. Temporary traffic control plans play a vital role in providing continuity of safe and efficient road user flow when a work zone, incident, or other event temporarily disrupts normal road user flow. Important auxiliary provisions that cannot conveniently be specified on project plans can easily be incorporated into Special Provisions within the temporary traffic control plan. Temporary traffic control plans range in scope from being very detailed to simply referencing typical drawings contained in this Manual, standard approved highway agency drawings and manuals, or specific drawings contained in the contract documents. The degree of detail in the temporary traffic control plan depends entirely on the complexity of the situation.
Possible Problems: AVOID GETTING INTO DETAILS HERE. THERE IS AN ENTIRE MODULE DEDICATED TO THESE.

## Slide 30: Public Information and Outreach (PI&O) Component (Module 3)
Addresses communication with the public and concerned stakeholders
Seeks to inform affected users of the work zone and its conditions
Notes: Key Message: Discuss the PI component
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: The public information (PI) component addresses communication with the public and concerned stakeholders, both before and during the project, about the project, what to expect in and around the work zone, and available travel alternatives. Examples of PI strategies include using brochures, web sites, radio, and/or variable message signs to disseminate this information both pre-trip and in-route.
Suggested Questions: What are the results of the PI component? Turn into discussion.
Additional Information:
Possible Problems: AVOID GETTING INTO DETAILS HERE. THERE IS AN ENTIRE MODULE DEDICATED TO THESE.

## Slide 31: Transportation Operations (TO) Component (Module 4)
Addresses sustained operations and management strategies of the work zone impact area, such as:
  Demand Management
  Corridor/network Management
  Enforcement
  Traffic Management
  Signal timing
Notes: Key Message: These are the areas that must be considered in the traffic operations plan.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: TO strategies really refer to the traffic management goals we discussed above. Demand management would include shifting trips to other modes, routes or other times. Trip reductions of 20 to 25% of normal traffic have been achieved in some cases. Corridor/ network management may mean speeding up or delaying projects on alternate routes. Safety of road users on alternate routes must be assessed as well as the safety of workers and road users traversing the work zone.
Suggested Questions:
Additional Information:
Possible Problems: AVOID GETTING INTO DETAILS HERE. THERE IS AN ENTIRE MODULE DEDICATED TO THESE.

## Slide 32: How Much Detail?
  The scope, content, and level of detail of a TMP may vary based on the State or local transportation agency's work zone policy and the anticipated work zone impacts of the project
  Required for ALL Federal Aid projects
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The level of detail will vary by State and by project. The scope, content, and level of detail of a TMP will vary based on the agency's work zone policy, the anticipated work zone impacts of the project, and whether the project is determined to be a significant project.
Suggested Questions: How much detail?
Additional Information: http://ops.fhwa.dot.gov/wz/rule_guide/appc.htm
Possible Problems: Avoid getting too specific here.

## Slide 33: The Benefits of a TMP
Promotes more efficient and effective work zones
Reduces costs
Improves work zone safety
Increases public satisfaction and project acceptance
Image: ATSSA
Notes: Key Message: Discuss benefits of TMPs
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: So in summary, TMPs have significant benefits. Some of them we have discussed and can be summarized here. TMP’s can:
-Promote more efficient and effective construction staging, duration, and costs.
-Improve work zone safety for construction workers and the traveling public.
Suggested Questions: Do you feel TMP’s would improve work zone safety? How?
Additional Information:
Possible Problems: Keep brief. Treat the following three slides as a wrap up or summary of the points discussed in this module. Avoid repeating information or stating the obvious. Convert to questions.

## Slide 34: The Benefits of a TMP (cont.)
Minimizes work zone impacts
Improves public awareness
Improves intra & interagency coordination
Image: ATSSA
Notes: Key Message: Discuss benefits of TMPs
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: So in summary, TMPs have significant benefits. Some of them we have discussed and can be summarized here. TMP’s can:
-Minimize traffic and mobility impacts.
-Improve public awareness.
-Minimize impacts to local communities and businesses.
-Improve intra and interagency coordination.
-They also help address the broader safety and mobility impacts of work zones at the corridor and network levels.
Suggested Questions: Do you feel TMP’s would improve work zone safety? How?
Additional Information:
Possible Problems: Keep brief. Treat the following three slides as a wrap up or summary of the points discussed in this module. Avoid repeating information or stating the obvious. Convert to questions.

## Slide 35: Knowledge Check
How many people die in traffic crashes in the USA every year? In work zones?
When are TMPs required?
What are the 3 components of a TMP?
When are all 3 components required?
What are the benefits of TMPs?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.

## Slide 36: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at your questions.
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: None