## Slide 1: 2. Temporary Traffic Control (TTC) Strategies
Work Zone Strategies
https://patch.com/pennsylvania/northwhitehall/coplay-creek-road-closed-for-repairs_345b7cce
Notes: Key Message: Module Opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s move to the next module. In this module {name}, we will.. {next slide}
Suggested Questions: None
Possible Problems: None

## Slide 2: Module Objectives
Review sources of Federal TTC standards and guidelines
Discuss common TTC strategies
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: IMPORTANT: Assess the level of knowledge of your audience during introductions. Although this material may appear to be basic to some, there are many misconceptions and common mistakes (like using the posted speed for determining taper lengths). Cover the material at the pace needed for your audience.

## Slide 3
TMP
TTC Plan
https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: Introduce the TTC Plan component
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the TTC Plan component of the TMP and the strategies associated with TTC.
Suggested Questions: None
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here.

## Slide 4: TTC Zone Definition
The entire section of roadway between
  The first advance warning sign (or device)
  Through the last traffic control device, where traffic returns to its normal path
TTC Zone
Images: FHWA
Notes: Key Message: Define a TTC zone
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Quote the definition. Interpretation of this definition has led to a “spin off.”
Suggested Questions: A question might be, “Is there any obligation of the TTC person (AGENCY) for traffic incidents that may occur outside this area of traffic control?” The answer to that could be, “Yes, there could be.” If the operation and/or consequence of the activity adversely affects nearby traffic flow, I.e., on a cross street or access ramp, then there might be some associated liability. Notice the keyword here is MIGHT. Each case must be evaluated on it’s own merits.
Additional Information: None
Possible Problems: None

## Slide 5: TTC Strategies are detailed in a TTC Plan
Consistent with the standards and guidelines of the:
  MUTCD
  Roadside Design Guide, and
  Other applicable documents
Images: FHWA/AASHTO
Notes: Key Message: Review what a TCP is
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: None
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: A TTC Plan may be called a TCP or an MOT.

## Slide 6: TCPs Shall Comply with the MUTCD
Code of Federal Regulations (CFR) Title 23:
“The US Department of Transportation shall promulgate a manual of traffic control standards.”
Image: FHWA
Notes: Key Message: Introduce the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: States are required to adopt a manual in substantial conformance with the MUTCD issued by FHWA. In some states the manual is entirely rewritten, in other states, just some things are changed.
Suggested Questions: Where does the MUTCD apply?
Additional Information: http://mutcd.fhwa.dot.gov
Possible Problems: Some may ask if the MUTCD applies in private areas, like shopping center parking lots. Unless there is an ordinance, the answer is no, since there is no way to enforce it.

## Slide 7: The MUTCD
MINIMUM standards and guidelines
  States and local agencies can go beyond them
Applies to ALL streets & highways open to the public
Image: FHWA
Notes: Key Message: Introduce the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The “MUTCD” contains MINIMUM standard and guidelines applicable EVERYWHERE in the USA and its territories (Puerto Rico, Virgin Islands and Guam)
Suggested Questions: Where does the MUTCD apply? What is a “minimum” standard?
Additional Information: http://mutcd.fhwa.dot.gov
Possible Problems: Some may ask if the MUTCD applies in private areas, like shopping center parking lots. Unless there is an ordinance, the answer is no, since there is no way to enforce it.

## Slide 8: The MUTCD
Current Edition: 2009
Published by US Department of Transportation, Federal Highway Administration (FHWA)
Image: FHWA
Notes: Key Message: Introduce the MUTCD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The current edition (200) replaced the “2003” edition. It will become effective on January 15, 2012
Suggested Questions: Who publishes the MUTCD?
Additional Information: http://mutcd.fhwa.dot.gov
Possible Problems: Some may ask if the MUTCD applies in private areas, like shopping center parking lots. Unless there is an ordinance, the answer is no, since there is no way to enforce it.

## Slide 9: State Options
States and territories had to adopt one of the following, by Jan 15, 2012:
  The 2009 MUTCD
  A State MUTCD
  A State supplement to the 2009 MUTCD
Image: FHWA
Notes: Key Message: Explain state options
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: States may choose 1 of 3 options within 2 years of release of a new MUTCD.
Suggested Questions: None
Additional Information: These are the options chosen on the 03 MUTCD. States may choose a different option in the future:
States (24) which have adopted the National MUTCD, 2003 Edition, and have no State Supplement: Alabama, Iowa, Mississippi, North Dakota, South Carolina , Arkansas , Kansas , Missouri , Nevada , South Dakota , Florida , Kentucky , Montana , Oklahoma , Vermont , Georgia , Louisiana , New Hampshire , Puerto Rico , Wyoming , Hawaii , Maine , New Jersey , Rhode Island States (21) which have adopted the National MUTCD, 2003 Edition, and have a State Supplement: Alaska , Idaho , Nebraska , Tennessee , Wisconsin , Arizona , Illinois , New Mexico , Utah , Colorado , Maryland , North Carolina , Virginia , Connecticut , Massachusetts , Oregon , Washington, Delaware , Michigan , Pennsylvania , West Virginia States (4) which have a State MUTCD in conformance with the National MUTCD, 2003 Edition: California , Minnesota , Ohio , Texas States (3) which have not yet identified adoption of the National MUTCD, 2003 Edition: (As of July 2007) District of Columbia , Indiana (w/Supplement)
Possible Problems: Keep brief.

## Slide 10: State and Local Standards
Must meet or exceed the MUTCD
All States are required to have a manual which substantially conforms with the MUTCD
MUTCD (Min.)
State
City/
County
Notes: Key Message: Indicate that the State may have a higher standard
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Clipart indicates the state/city/county standards must be a “higher” standard.
Suggested Comments: State may choose to have a more restrictive standard, but must follow the MUTCD as a minimum.
Suggested Questions: What about a city or a county, may they have their own standards? Yes, even higher!
Additional Information: None
Possible Problems: Some states, like Maryland and Florida, allow the cities and counties to drop down the minimum levels of the MUTCD.

## Slide 11: MUTCD Levels of Compliance
Standard
“SHALL”
Guidance
“SHOULD”
Option
“MAY”
Additional
Information
Support
Notes: Key Message: Explain MUTCD’s levels of compliance
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Each level appears upon click
Suggested Comments: The MUTCD is formatted so we can separate the standards from the guidelines from the options. The levels of compliance tell you whether an MUTCD statement shall, should or may be done. These have legal implications.
Suggested Questions: What’s the difference between a standard and a guideline?
Additional Information: This reformat was first done with the “Millennium” edition.
Possible Problems: Avoid getting into much detail here since individual slides follow.

## Slide 12: MUTCD vs. State: Which One Governs?
Use State standards first
Use MUTCD second
State governs!
Notes: Key Message: Indicate the hierarchy of standards
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The local standards govern over the MUTCD.
Suggested Questions: If we find a difference between the MUTCD and the State standards, which one will govern?
Additional Information: None
Possible Problems: This may be a point of contention due to misconceptions.

## Slide 13: Example
MUTCD = 28” Min.
Some States = 36” Min.
Images: ATSSA
Notes: Key Message: Illustrate previous point with an example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Cone to the right and caption appear upon click
Suggested Comments: The MUTCD requires that for a cone to be used on a freeway it shall be at least 28 inches in height. Several states, like Florida and Virginia, require cones to be 36 inches.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 14: Other Possible Sources of TTC Standards and Guidelines
State/local manuals
Recommended practices, procedures and guidelines
Manufacturers’ instructions
Occupational Safety and Health Administration (OSHA)
Roadside Design Guide
Notes: Key Message: Introduce other publications published separately that contain TTC standards, guidelines and practices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Other organizations have input into how we do things in the traffic industry. Their publications are referenced in the MUTCD and are considered to be part of it. Various documents may contain information related to traffic control. Always check with your local agency.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 15: OSHA Requirements
Occupational Safety and Health Administration (OSHA) may enforce worker safety requirements in the MUTCD
OSHA is part
of the
US Department of Labor
Image: USDOL
Notes: Key Message: Introduce OSHA requirements
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: OSHA adopts and enforces the MUTCD by reference. This varies by State.
OSHA adopts the MUTCD by reference but “usually” does not have any involvement with traffic control. This varies by State.
Suggested Questions: OSHA is part of which Federal department?
Additional Information: OSHA has adopted the Millennium Edition of the MUTCD, but not the 2003 Edition (as of 2007).
Possible Problems: Some states have a local branch of OSHA, not the Federal agency, overseeing work zones.

## Slide 16: OSHA’s Jurisdiction
  Limited to worker safety
  “Usually” not traffic control
    Varies by State
  May:
    Perform inspections
    Issue fines
    Shut down projects
Image: USDOL
Notes: Key Message: Introduce OSHA requirements
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: OSHA may impose fines for violations.
Suggested Questions: What is “usually” not traffic control? Taper length? Missing buffer? If in OSHA’s judgment the safety of the worker is in jeopardy, they may take action. OSHA may impose fines for violations.
Additional Information: None
Possible Problems: Some states have a local branch of OSHA, not the Federal agency, overseeing work zones. Be specific to the state, if possible.

## Slide 17: OSHA Requirements
Possible requirements:
  High-visibility safety apparel
  Hardhats
  Safety shoes
  Gloves
Anything that
impacts worker
safety!
Image: ATSSA
Notes: Key Message: Introduce OSHA requirements
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: OSHA’s primary area of interest is in the worker safety area of: clothing, eye, ear, breathing protection, gloves, etc. Anything that impacts worker safety!
Suggested Questions: What is “usually” not traffic control? Taper length? Missing buffer? If in OSHA’s judgment the safety of the worker is in jeopardy, they may take action.
Additional Information: None
Possible Problems: Some states have a local branch of OSHA, not the Federal agency, overseeing work zones. Be specific to the state, if possible.

## Slide 18: Roadside Design Guide
Published by the American Association of State Highway and Transportation Officials (AASHTO)
Referenced in the MUTCD
2011 Edition
Image: AASHTO
Notes: Key Message: Introduce other publications published separately that contain TTC standards, guidelines and practices
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The American Association of State Highway and Transportation Officials, or AASHTO, publishes the Roadside Design Guide, which includes specific information on the use of impact attenuators and portable barriers. It is referenced in the MUTCD (Page 6F-42, for example)
Suggested Questions: None
Additional Information: AASHTO is an association of state DOTs.
Possible Problems: Spell out. Do not assume/use acronyms.

## Slide 19: Manufacturer Instructions and Recommendations
Specify the application of the devices they manufacture
  Instructions
Image: ATSSA
Notes: Key Message: Introduce other publications published separately that contain TTC standards, guidelines and practices
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Manufacturer instructions and recommendations are also considered recommendations. It a device is used, it should be used in accordance to these. A device, such as a truck-mounted attenuator, will not be effective if used improperly. It is important to follow manufacturer recommendations to be sure the device is being used correctly.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 20: Other Applicable Publications
State Traffic Engineering Manuals
State’s “Standard Specifications for Road and Bridge Construction”
Image: ATSSA
Notes: Key Message: Indicate where additional standards and guidelines may be found
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Depending on the State, TTC standards and guidelines may also be found in other documents, such as the State’s “Standard Specifications for Road and Bridge Construction”. Make sure that you are aware of all your State’s requirements. Various documents may contain information related to traffic control. Always check with your local agency.
Suggested Questions: How can you tell if you are in compliance with all standards and guidelines? Ask the agency!
Additional Information: None
Possible Problems: None

## Slide 21: Standard Specifications for Road and Bridge Construction
Construction details
Published by the individual States
Image: ATSSA
Notes: Key Message: Indicate where additional standards and guidelines may be found
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Note that the State’s “Standard Specifications for Road and Bridge Construction” are truly “specifications” and not standards. Specifications are very detailed and are normally stated in measurable units. The Federal Highway Administration, Construction Division, publishes, usually annually, the Federal Road and Bridge Specifications. Each State then adjusts the federal specifications to meet their local conditions.
Suggested Questions: How can you tell if you are in compliance with all standards and guidelines? Ask the agency!
Additional Information: None
Possible Problems: Be specific to this state, if possible.

## Slide 22: Project-Specific Plans & Special Provisions
Site-specific
Contain the most specific requirements for that particular project
These requirements will govern
Image: ATSSA
Notes: Key Message: Discuss project-specific plans & special provisions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For each construction and maintenance project there is normally a contract which includes P,S, and Es; this means Plans, Specifications, and Estimates. These plans include very site specific details showing street names, adjacent land use, type of use, and often street “hardware.” Included in the plans is usually a TCP, or Traffic Control Plan. This plan as well will be detailed. Because they are so specific, special provisions will govern over the MUTCD. These are your contract documents.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 23: Project Specific Plans & Special Provisions
  Prosecution and progress
  Device spacing
  Allowable lane widths
  Pavement marking requirements
  Allowable work hours/restrictions
  Allowable control methods
  Specific devices to be used
  Other requirements
Notes: Key Message: Discuss project-specific plans & special provisions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are some of the more specific things in the plans and special provisions. Need to look at more than just the plan sheets. The special provisions may have some peculiar details about times a road can be closed, or lane width requirements.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 24: Common TTC Strategies
This section identifies common work zone strategies and factors that should be considered in the selection process
Image: FHWA
Notes: Key Message: Discuss feasible methods to handle traffic
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self-explanatory.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 25: TTC Strategies Can be Divided Into:
Temporary traffic control (TTC)
Traffic control devices
Contracting & innovative construction strategies
3
Notes: Key Message: Introduce how the TTC strategies are organized
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds:
Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 26: A. TTC Strategies
Lane constriction
Lane closure
Shared right-of-way
Temporary bypass
Intermittent closure
Crossover
Shoulder use
Median use
Detour
Lane separation
Full road closure
Night work
Notes: Key Message: Discuss feasible methods to handle traffic
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s discuss the various methods to control, or handle traffic.(This is an intro slide. Avoid discussing these bullets here). The following strategies have been widely and successfully employed for construction work zones on high-speed highways. These strategies are not necessarily separate, individual choices. In fact, several of them do not provide a complete and workable solution. Use of a full road closure requires one or more additional strategies (e.g., detour or diversion). Some of
the strategies are identified as mitigation strategies, meaning that they can be used to offset negative consequences (e.g., reduced capacity and access limitations) for one or more other strategies.
Suggested Questions: None
Additional Information: These are work zones that take place WITHIN the travel lane (exception is total closure)
Possible Problems: None

## Slide 27: A1. Lane Constriction
Reducing the width of one or more lanes
Image: ATSSA
Notes: Key Message: Discuss lane constriction
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The first one is lane constriction: Reducing the width of the travel lane. Detour: Traffic is routed off a roadway onto another existing street. Diversion: Traffic is directed to use another part of the roadway within the same right-of-way. EMPHASIZE: Traffic disruption is MINIMAL. This work zone strategy is employed when maintaining traffic with less-than-desirable travel lane widths is preferable to other candidate alternatives. At some level of expenditure and impact, constricted lanes can almost always be avoided. The decision to use this strategy is made in consideration of the magnitude of the constriction (i.e., actual traveled way width), the service conditions (e.g., duration, length, and traffic), and the cost associated with avoiding the constriction. In making these decisions, agencies often draw on their considerable accumulated experience.
Suggested Questions: What is the minimum lane width we can have? Usually 11 feet for freeways and 10 feet for other facilities. It does vary by State.
Additional Information: Lane constriction: a construction work zone mitigation strategy wherein the width of one or more travel lanes is reduced. The number of travel lanes may be retained (possibly through median or shoulder use) or reduced.
Possible Problems: This work zone strategy can directly impact the ability of the facility to accommodate large vehicles. In some cases, agency coordination involving permits for oversized vehicles is needed.

## Slide 28: A1. Lane Constriction
Advantages | Disadvantages
Number of lanes and alignment are retained Minimal disruption to traffic | May be problematic for large vehicles Little/no room for bicycles May reduce speeds
Image: FHWA
Notes: Key Message: Discuss lane constriction
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: Why a problem for large vehicles? This work zone strategy can directly impact the ability of the facility to accommodate large vehicles. In some cases, agency coordination involving permits for oversized vehicles is needed.
Additional Information: None
Possible Problems: None

## Slide 29: A2. Lane Closure
Uses merging tapers to close one or more lane
Capacity analysis is needed
Image: ATSSA
Notes: Key Message: Discuss lane closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Lane closure is another type of TTC activity.
Suggested Questions: What type of taper is this? Merging taper! Why? Can you think of any disadvantages?
Additional Information: None
Possible Problems: None

## Slide 30: A2. Lane Closures
Advantages | Disadvantages
Maintains flow Minimal roadside impact Familiarity Low cost if no barriers | Reduces capacity May create queues Workers close to traffic Interference with access points Costly if barriers
Image: FHWA
Notes: Key Message: Discuss lane closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 31
1. Advance
Warning Area
2. Transition Area
3. Activity
Area
4. Termination Area
Longitudinal Buffer Space
Work Space
Traffic Space
Component Parts of a TTC Zone
NOT TO SCALE
49
Image: ATSSA
Notes: Key Message: Define component parts of the TTC
Est. Presentation Time: 10 minute(s)
Explanation of Cues/Builds: Each part appears upon click
Suggested Comments: Most TTC zones are divided into four areas: the advance warning area, the transition area, the activity area,
and the termination area. This illustrates these four areas:
The advance warning area is the section of highway where road users are informed about the upcoming work zone or incident area.
The transition area is that section of highway where road users are redirected out of their normal path. Transition areas usually involve strategic use of tapers, which because of their importance are discussed later.
The activity area is the section of the highway where the work activity takes place. It is comprised of the work space, the traffic space, and the buffer space.:
The traffic space is the portion of the highway in which road users are routed through the activity area.
The buffer space is a lateral and/or longitudinal area that separates road user flow from the work space or an unsafe area, and might provide some recovery space for an errant vehicle. Buffer spaces are highly recommended. A longitudinal buffer space may be placed in advance of a work space. Neither work activity nor storage of equipment, vehicles, or material should occur within a buffer space.
The work space is where the work takes place. Workers, materials and equipment are located in the work space.
The termination area shall be used to return road users to their normal path. The termination area shall extend from the downstream end of the work area to the last TTC device such as END ROAD WORK signs, if posted.
Suggested Questions: What do you see in the buffer space? Nothing!
Additional Information: Refer to Section 6C.03 of MUTCD. L stands her for LONGITUDINAL (explained later)
Possible Problems: Don’t get into details here. Use the following slides for that. The objective of this slide is to explain the terminology, not to give details. There is no ACTIVITY in the buffer space so this may be a bit misleading. Make sure to explain that.

## Slide 32: Recommended Advance Warning Sign Minimum Spacing
Road Type | A | B | C
Urban (low speed)* | 100’ | 100’ | 100’
Urban (high speed)* | 350’ | 350’ | 350’
Rural | 500’ | 500’ | 500’
Freeways and Expressways | 1,000’ | 1,500’ | 2,640’
*Speed category to be determined by highway agency.
50
Notes: Key Message: Discuss sign spacing
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s discuss sign spacing. The A, B, and C refer to the suggested distance between signs (next slide). Notice that this is a suggested spacing.
Suggested Questions: What is high speed? What is low speed? Notice that that is to be determined by the highway agency with jurisdiction. If in doubt, go larger!
Additional Information: Refer to Table 6C-1, MUTCD. Where highway conditions permit, warning signs should be placed in advance of the TTC zone at varying distances depending on roadway type, condition, and posted speed. Table 6C-1 contains information regarding the spacing of advance warning signs. Where a series of two or more advance warning signs is used, the closest sign to the TTC zone should be placed approximately 100 ft for low-speed urban streets to 1,000 ft) or more for freeways and expressways. Various conditions, such as limited sight distance or obstructions that might require a driver to reduce speed or stop, might require additional advance warning signs. As an alternative to a specific distance on advance warning signs, the word AHEAD may be used (this is a state preference) At TTC zones on lightly-traveled roads, all of the advance warning signs prescribed for major construction might not be needed. Utility work, maintenance, or minor construction can occur within the TTC zone limits of a major construction project, and additional warning signs may be needed. Utility, maintenance, and minor construction signing and TTC should be coordinated with appropriate authorities so that Sign spacing may vary by state. Also, the 2003road users are not confused or misled by the additional TTC devices.
Possible Problems: Manual said “Suggested”, not “recommended”.

## Slide 33: Min. Length (L) of a MERGING Taper
L = WS (45 mph or more)
L = (WS2)/60 (40 mph or less)
Where:
  L = length of the MERGING taper in feet
  W = width of offset in feet
  S = Speed in mph
53
Notes: Key Message: Introduce formulas for L
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The letter L is used to indicate the minimum length of a MERGING taper. Other taper lengths are a fraction of L. A merging taper requires the longest distance because drivers are required to merge into common road space.
Suggested Questions: What is W? What is S?
Additional Information: Refer to MUTCD. The appropriate taper length (L) should be determined using the criteria shown in Tables 6C-3 and 6C-4.
Possible Problems: Someone may ask why two formulas. At low speeds, there is more time to make decisions, so a second formula is needed. Emphasize that S is not necessarily the posted speed. See next slide.

## Slide 34: S = Which Speed?
The posted speed minimum
Off-peak 85th percentile speed prior to work starting
Anticipated operating speed
    “Prevailing speed”
53
Notes: Key Message: Define S
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Is S always the posted speed? No. Use the “prevailing” speed.
Additional Information: Refer to MUTCD. “S = posted speed limit, or off-peak 85th-percentile speed prior to work starting, or the
anticipated operating speed mph.
Possible Problems: Emphasize that S is not necessarily the posted speed. This is a common misconception. Avoid discussing the definition of 85th percentile. Not within the scope of this course. Call it “prevailing” speed, or the speed at which the majority of the traffic is traveling.

## Slide 35: The 85th Percentile Speed
The speed at which at least 85 percent of the traffic is traveling, or below
Can be computed graphically
Typically 8-10 mph above the posted speed
Notes: Key Message: Define the 85th percentile speed
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Is S always the posted speed? No. It is the speed at which the “majority” of the traffic is traveling. A good representation of that speed is the 85th percentile speed, defined as he speed at which at least 85 percent of the traffic is traveling, or below. The 85th percentile speed may be used to design the TTCZ.
Additional Information: Refer to MUTCD Page 6C-8 for the definition of S. The 85th percentile speed is the speed at or below which 85 percent of the motorists drive on a given road unaffected by slower traffic or poor weather. This speed indicates the speed that most motorists on the road consider safe and reasonable under ideal conditions. It is a good guideline for the appropriate speed limit for that road.
Possible Problems: Emphasize that S is not necessarily the width of the lane. That is ONLY true on lane closures. On lane shifts, W is the lateral distance of the shift. May only be a few feet. This is a common misconception. The term “offset” may be confusing. May want to say “distance moved laterally”.

## Slide 36: W = Which Width?
Width of offset
  The width of the lane on lane closures (merging tapers)
  The distance shifted laterally on lane shifts (shifting tapers)
Notes: Key Message: Define W
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Is W always the width of the lane? No. The distance move laterally.
Additional Information: Refer to MUTCD. “W = width of “offset” feet
Possible Problems: Emphasize that W is not necessarily the width of the lane. That is ONLY true on lane closures. On lane shifts, W is the lateral distance of the shift. May only be a few feet. This is a common misconception. The term “offset” may be confusing. May want to say “distance moved laterally”.

## Slide 37
MPH | 9’ | 10’ | 11’ | 12’
25 | 95 | 105 | 115 | 125
30 | 135 | 150 | 165 | 180
35 | 185 | 205 | 225 | 245
40 | 240 | 270 | 295 | 320
45 | 405 | 450 | 495 | 540
50 | 450 | 500 | 550 | 600
55 | 495 | 550 | 605 | 660
60 | 540 | 600 | 660 | 720
65 | 585 | 650 | 715 | 780
70 | 630 | 700 | 770 | 840
75 | 675 | 750 | 825 | 900
80 | 720 | 800 | 880 | 960
Table to determine the minimum MERGING taper length (L) in feet
Notes: Key Message: Discuss table for L
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give several examples.
Suggested Questions: How long is the min. merging taper for, say, 55 mph, 12 foot lanes? 660 feet min.!
Additional Information: None
Possible Problems: If W is something other than 9-12, may need to use the formulas, or (tip!) take a fraction of these numbers. For example, for S = 50 mph and W = 3 feet, L would be ¼ (12/4 = 3) of the number shown on the “12’” column, or 150 feet.

## Slide 38
MPH | 9’ | 10’ | 11’ | 12’
< 25 | 95 | 105 | 115 | 125
30 | 135 | 150 | 165 | 180
35 | 185 | 205 | 225 | 245
40 | 240 | 270 | 295 | 320
45 | 405 | 450 | 495 | 540
50 | 450 | 500 | 550 | 600
55 | 495 | 550 | 605 | 660
60 | 540 | 600 | 660 | 720
65 | 585 | 650 | 715 | 780
70 | 630 | 700 | 770 | 840
75 | 675 | 750 | 825 | 900
80 | 720 | 800 | 880 | 960
MERGING TAPER
EXAMPLE:
S = 60 mph
W = 12 ft
L = 720 ft MIN!
Notes: Key Message: Discuss table for L
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give several examples.
Suggested Questions: How long is the min. merging taper for, say, 55 mph, 12 foot lanes? 660 feet min.!
Additional Information: None
Possible Problems: If W is something other than 9-12, may need to use the formulas, or (tip!) take a fraction of these numbers. For example, for S = 50 mph and W = 3 feet, L would be ¼ (12/4 = 3) of the number shown on the “12’” column, or 150 feet.

## Slide 39
Recovery area for errant vehicles
Protects BOTH workers & motorists
COMPLETELY empty
  No vehicles (including law enforcement vehicles), equipment, materials
  Provide a buffer space unless you have a documented reason not to
Table 6C-2
Based on stopping sight distances
Longitudinal Buffer Space
51
Notes: Key Message: Expand on the longitudinal buffer space
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: Remember, buffer spaces should be used unless you have a documented reason not to do so.
Suggested Questions: What about a truck-mounted attenuator? Can it be in the buffer space? No, it should be in the work area.
Additional Information: None
Possible Problems: Emphasize the use of buffer spaces even though they are not required.

## Slide 40
Buffer Space
Work Space
Activity
Area
Image: ATSSA
Notes: Key Message: Illustrate the longitudinal buffer space
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This illustrates the longitudinal buffer space.
Suggested Questions: None
Additional Information: The buffer space is a lateral and/or longitudinal area that separates road user flow from the work space or an unsafe area, and might provide some recovery space for an errant vehicle. Buffer spaces are highly recommended. A longitudinal buffer space may be placed in advance of a work space. Neither work activity nor storage of equipment, vehicles, or material should occur within a buffer space.
Possible Problems: None

## Slide 41
Speed (mph) | L. Buffer (ft.)
20 | 115
25 | 155
30 | 200
35 | 250
40 | 305
45 | 360
Speed (mph) | L. Buffer (ft.)
50 | 425
55 | 495
60 | 570
65 | 645
70 | 730
75 | 820
(May use for Longitudinal Buffer Spaces)
Table 6C-2. Stopping-Sight Distance as a Function of Speed
51
Notes: Key Message: Quantify the length of the longitudinal buffer space
Est. Presentation Time: 3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are minimum distances. If warranted, longer distances may be used.
Suggested Questions: Which speed do we use to go into this table? The posted speed? You may use the posted speed as a minimum, but traffic usually travels faster. We will discuss other speeds that may be used later. How long is a buffer for 40 miles per hour? 305 feet or about the length of a football field!
Additional Information: Source: 2009 MUTCD, Table 6C-2. Stopping Sight Distance as a Function of Speed. Page 51
Possible Problems: None

## Slide 42: Longitudinal Buffer Space
Buffer Space
Image: ATSSA
Notes: I-95 SB, near Woodbridge, VA by J. Morales

## Slide 43
S | L | ½ L | 1/3 L | Buffer
25 | 125 | 63 | 42 | 155
30 | 180 | 90 | 60 | 200
35 | 245 | 123 | 82 | 250
40 | 320 | 160 | 107 | 305
45 | 540 | 270 | 180 | 360
50 | 600 | 300 | 200 | 425
55 | 660 | 330 | 220 | 495
60 | 720 | 360 | 240 | 570
65 | 780 | 390 | 260 | 645
70 | 840 | 420 | 280 | 730
75 | 900 | 450 | 300 | 820
Combo table for W = 12 ft.
Notes: Key Message: Present the “combo” table
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is the table for L that we saw earlier, but we have added the buffer space so we have both in the same table.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 44: Multiple Tapers
“Back to back” tapers
Must be separated by a tangent section: “transition between tapers”
Image: ATSSA
Notes: Key Message: Discuss multiple tapers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: When consecutive tapers are needed, they shall be separated by a tangent transition section, to allow motorists to adjust to one condition before moving to another. There is no name for this tangent section. It can be called “transition between tapers”.
Suggested Questions: What is a tangent? Straight!
Additional Information: None
Possible Problems: None

## Slide 45: Multiple Tapers: Two Cases:
Merging taper followed by another merging taper
Merging taper followed by a shifting taper
Notes: Key Message: Discuss multiple tapers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are two cases of back-to-back tapers. They are listed here. Let’s look at each one.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 46: Merging Taper followed by a Merging Taper
Separated by a minimum of 2L, where L is the merging taper
203
Image: FHWA
Notes: Key Message: Discuss merging taper followed by a merging taper Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In the case of a merge, followed by another merge, a much longer time is required to make the adjustments, BEFORE another movement is required; the shift. Thus, the longer distance. Since it is desirable to have the motorist make all their adjustments before they are told to do another action a long distance of 2L is required.
Suggested Questions: None
Additional Information: MUTCD Page 203
Possible Problems: None

## Slide 47: Example
W= 12’
S= 55 mph
L = 660’ Min.
2L = 1320’ Min.
Buffer
TMA
Not to scale
Image: FHWA
Notes: Key Message: Discuss merging taper followed by a merging taper Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Example. Self explanatory.
Suggested Questions: None
Additional Information: MUTCD Page 203
Possible Problems: This may vary by state.

## Slide 48: Merging Taper followed by Shifting Taper
Separated by a minimum distance of 1/2 L, where L is the merging taper
½ L
L
½ L
L
193
Image: FHWA
Notes: Key Message: Discuss merging taper followed by shifting taper Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A ½ L distance required when a merge is followed by a shift. Here, a shorter separation distance is needed because the driver can still make his adjustments while going through the shift.
Suggested Questions: None
Additional Information: MUTCD Page 6H-79
Possible Problems: This may vary by state. Also, notice that this drawing is NOT TO SCALE and that the ½ L for the separation and the ½ L for the shifting tapers are not equal. They should be. Also notice that this picture does not show a buffer space since it is optional in the MUTCD. It may be required in your state.

## Slide 49: Example
W = 12’
S = 55 mph
L = 660’ Min.
½ L = 330’ Min.
330’
330’
660’
Not to scale
Image: FHWA
Notes: Key Message: Discuss merging taper followed by shifting taper Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Example. Self explanatory.
Suggested Questions: None
Additional Information: MUTCD Page 6H-79
Possible Problems: This may vary by state. Also, notice that this drawing is not to scale and that the ½ L for the separation and the ½ L for the shifting tapers are not equal. They should be. Also notice that this picture does not show a buffer space since it is optional in the MUTCD. It may be required in your state.

## Slide 50: A3. Shared Right-of-Way
Uses flaggers or temporary signals
Signing alone may be sufficient for short, very low volume work zones
Image: ATSSA
Notes: Key Message: Discuss shared ROW
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Shared Row is another possibility, where traffic is alternated. Alternating one-way operation: a construction work zone
mitigation strategy used on two-way roadways wherein opposing directions of travel take turns using a single travel lane. Flaggers, with or without pilot vehicles; STOP signs; or signals are normally used to coordinate the two directions of traffic. This strategy compensates for the removal of permanent travel lanes from service and is sometimes referred to as one-lane, two-way operation. There are several variations of this strategy related to the type of control employed (e.g., STOP sign, temporary signal control,
or pilot car), as outlined in the MUTCD. Design and TTC provisions are also required to facilitate transition from high-speed approaches to stop conditions for the spectrum of operational conditions (e.g., day-night and weather). The agency cost and non transportation impacts of this strategy are generally low.
Suggested Questions: What else would be needed here? Flaggers!
Additional Information: None
Possible Problems: None

## Slide 51: A3. Shared Right-of-Way
Involves using one lane for both directions of traffic
Flagging operation used to alternate the right-of-way to approaching vehicles
  Flaggers
  Temporary traffic signals or
  Automated Flagger Assistance Devices (AFAD) “One-lane, two-way” tapers are required
Notes: Key Message: Discuss shared ROW
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 52
50-100’ MAX
On two-lane roads
Flaggers required
  “Flagging taper”
One-Lane, Two-Way Taper
149
Images: ATSSA
Notes: Key Message: Discuss one-lane two-way tapers
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The one-lane, two-way taper is used in advance of an activity area that occupies part of a two-way roadway in such a way that a portion of the road is used alternately by traffic in each direction. Traffic should be controlled by a flagger or temporary traffic control signal (if sight distance is limited), or a STOP or YIELD sign. A short taper having a maximum length of 30 m (100 ft) with channelizing devices at approximately 10-20 ft. spacing should be used to guide traffic into the one-way section. We call these roads a “special case” since the taper has a fixed length.
Suggested Questions: Which devices are never used on two-lane roads? Arrow boards (displaying arrows). Why would these tapers have a maximum length? Short tapers encourage drivers to slow down!
Additional Information: None
Possible Problems: The length of the flagging taper may vary by State.

## Slide 53
Use with flaggers, portable signals or AFADs
One-Lane, Two-Way Taper = 50’-100’ Max.
Image: ATSSA
Notes: Key Message: Discuss tapers on two-lane roads
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: How long are tapers on 2-lane roads? 50-100 ft max. Notice the buffer space.
Suggested Questions: Which device is never used on these roads? Arrow board (displaying arrows).
Additional Information: The one-lane, two-way taper is used in advance of an activity area that occupies part of a two-way roadway in such a way that a portion of the road is used alternately by traffic in each direction. Traffic should be controlled by a flagger or temporary traffic control signal (if sight distance is limited), or a STOP or YIELD sign. A short taper having a maximum length of 100 ft with channelizing devices at approximately 20 ft spacing should be used to guide traffic into the one-way section. An example of a one-lane, two-way traffic taper is shown in MUTCD Figure 6C-3.
Possible Problems: Note that both flaggers are on the shoulder! Flagger symbol appears to be on the road.

## Slide 54: Automated Flagger Assistance Devices (AFADs)
Remotely operated
Two types permitted in MUTCD
  Check with your state for acceptability
Follow manufacturer’s instructions
Usually require a separate certification to operate
63
Image: ATSSA

## Slide 55: A3. Shared Right-of-Way
Advantages | Disadvantages
Closed lane may enhance worker safety Maintains two-way traffic | Flaggers in close proximity to traffic May created delays if volumes are high Illegal U-turns Queues
Image: FHWA
Notes: Key Message: Discuss shared right-of-way
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 56: A4. Temporary Bypass (Diversion)
Total closure with traffic diverted to temporary roadway
Shifting tapers
Image: ATSSA
Notes: Key Message: Discuss temporary bypass
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Temporary bypass is another type. Here a portion of the shoulder is used as a travel lane. Traffic is routed to a temporary bypass constructed within the highway’s right-of-way. It involves total closure of one or both directions of travel on the roadway. This involves the use of shifting tapers.
Suggested Questions: What type of taper is this? Shifting taper!
Additional Information: None
Possible Problems: None

## Slide 57: Shifting Taper = 1/2 L Min.
53
Image: ATSSA
Notes: Key Message: Show shifting taper example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give more examples. Notice the TMA in the work area, not the buffer space.
Suggested Questions: What is W here? The width of the lane since this is a full lane shift.
Additional Information: None
Possible Problems: Notice that the taper past the work space is a shifting taper, not a downstream taper.

## Slide 58
MPH | 9’ | 10’ | 11’ | 12’
< 25 | 95 | 105 | 115 | 125
30 | 135 | 150 | 165 | 180
35 | 185 | 205 | 225 | 245
40 | 240 | 270 | 295 | 320
45 | 405 | 450 | 495 | 540
50 | 450 | 500 | 550 | 600
55 | 495 | 550 | 605 | 660
60 | 540 | 600 | 660 | 720
65 | 585 | 650 | 715 | 780
70 | 630 | 700 | 770 | 840
75 | 675 | 750 | 825 | 900
80 | 720 | 800 | 880 | 960
SHIFTING TAPER EXAMPLE:
W= 12 ft.
S= 55 mph
Shifting taper:
= (1/2 L)
= 660/2
= 330’ MIN.
Notes: Key Message: Give shifting taper examples
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give several examples.
Suggested Questions: None
Additional Information: None
Possible Problems: If W is something other than 9-12, may need to use the formulas, or (tip!) take a fraction of these numbers. For example, for S = 50 mph and W = 3 feet, L would be ¼ (12/4 = 3) of the number shown on the “12’” column, or 150 feet.

## Slide 59: A4. Temporary Bypass (Diversion)
A temporary rerouting of road users onto a temporary highway or alignment placed around the work area
New surface is constructed to divert traffic around the work space
Image: FHWA
Notes: Key Message: Discuss temporary bypass
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 60: Road Closure With Diversion
63
Image: FHWA

## Slide 61: A4. Temporary Bypass (Diversion)
Advantages | Disadvantages
Maintains number of lanes Capacity is maintained Possible faster completion Improved worker safety Separates traffic from workers | Alignment must be changed Costly Larger footprint May need additional ROW
Notes: Key Message: Discuss temporary bypass
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 62: A5. Intermittent Closure
Stopping all traffic in both directions for a short period of time
Applicable only on very low volume roads
Image: ATSSA
Notes: Key Message: Discuss intermittent closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Intermittent closures involve stopping all traffic in both directions for a relatively short time to allow the work to proceed. After certain amount of time, driven by the traffic volume or completion of the work activity, the roadway is reopened.
Suggested Questions: Are these common? Can you think of any conditions that would have to be met?
Additional Information: Intermittent closure: a construction work zone mitigation strategy wherein all traffic in one or both directions is
stopped for a relatively short period to allow for construction operations. This work zone strategy alone is generally not adequate for an entire construction project. It is often employed during specific operations (e.g., setting bridge beams, conducting blast detonation, and moving equipment) for which project personnel can select the beginning point and reasonably predict the duration. In nonemergency cases, intermittent closure should be used only if the duration of closure and period of traffic impact will be short (less than 20 minutes).
Possible Problems: None

## Slide 63: A5. Intermittent Closure
Advantages | Disadvantages
Very low cost No detour No roadside impacts Safer environment for workers | Delays may be possible Queues Equipment movement and access
Notes: Key Message: Discuss intermittent closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 64: A6. Crossover
Images: ATSSA
Notes: Key Message: Discuss crossovers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Crossovers involve routing the traffic from one direction onto a portion of the median and roadway of the opposing traffic. On higher speed roadways, a portable or temporary barrier is used to separate the two directions of traffic.
Suggested Questions: What types of tapers are these? What is the separation between these two tapers? This is a merging taper followed by a shifting taper (bottom figure)
Additional Information: None
Possible Problems: None

## Slide 65: A6. Crossover
Routes the traffic from one direction onto a portion of the median and roadway of the opposing traffic
On higher speed roadways, a portable or temporary barrier is used to separate the two directions of traffic
Pavement markings are essential
Notes: Key Message: Discuss crossovers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Crossovers involve routing the traffic from one direction onto a portion of the median and roadway of the opposing traffic. On higher speed roadways, a portable or temporary barrier is used to separate the two directions of traffic.
Suggested Questions: What types of tapers are these? What is the separation between these two tapers? This is a merging taper followed by a shifting taper (bottom figure)
Additional Information: None
Possible Problems: None

## Slide 66: A6. Crossover
Advantages | Disadvantages
Separates construction from traffic Maintains continuous flow | Costly if barriers Temporary roadway needed Reduces shoulders Long duration May reduce capacity if lane closed
Notes: Key Message: Discuss crossovers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.. Also vehicles are in close proximity to each other. Long duration refers to the fact that this strategy in only suitable for long term projects. By definition, long term is 3 days or more.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 67: A7. Shoulder Use
Use of the shoulder as a temporary traffic lane
Shoulder should support extra loads
Image: ATSSA
Notes: Key Message: Discuss shoulder use
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Use of shoulder: a construction work zone mitigation strategy involving the use of a right-side or median shoulder as all or part
of a temporary traffic lane. This strategy compensates for the removal of permanent travel lanes from service. Employing this strategy may require constructing or upgrading shoulder pavement structures to adequately support traffic loads. The traffic lanes are routed onto the shoulder. The structural capacity of the shoulder must first be analyzed to determine its ability to carry the proposed traffic.
Suggested Questions: What types of tapers are these? Shifting tapers? Why? The number of lanes stay the same!
Additional Information: None
Possible Problems: None

## Slide 68: Work in the Center of a Road with Low Traffic Volumes
159
Image: FHWA

## Slide 69: A7. Shoulder Use
Advantages | Disadvantages
Lanes are maintained Minimal roadside impact Low cost | Workers close to traffic May be costly if barriers
Notes: Key Message: Discuss shoulder use
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 70: Shoulder Taper = 1/3 L Min.
53
Image: ATSSA
Notes: Key Message: Show shoulder taper example
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give more examples. Notice the TMA in the work area, not the buffer space.
Suggested Questions: What is the yellow area? The buffer space. How can you tell this is a merging taper? It is a lane closure.
Additional Information: When computing a shoulder taper, W is the width of the shoulder.
Possible Problems: Shoulder tapers are required in several states (Virginia, for example)

## Slide 71
MPH | 9’ | 10’ | 11’ | 12’
25 | 95 | 105 | 115 | 125
30 | 135 | 150 | 165 | 180
35 | 185 | 205 | 225 | 245
40 | 240 | 270 | 295 | 320
45 | 405 | 450 | 495 | 540
50 | 450 | 500 | 550 | 600
55 | 495 | 550 | 605 | 660
60 | 540 | 600 | 660 | 720
65 | 585 | 650 | 715 | 780
70 | 630 | 700 | 770 | 840
75 | 675 | 750 | 825 | 900
80 | 720 | 800 | 880 | 960
SHOULDER TAPER EXAMPLE:
S = 60 mph
W = 10 ft
Shoulder taper:
= (1/3 L)
= 600/3
= 200’ Min.
Notes: Key Message: Give shoulder taper examples
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Give several examples.
Suggested Questions: None
Additional Information: This example is for a 10-ft shoulder.
Possible Problems: None

## Slide 72: A8. Median Use
Similar to shoulder use
Median should support extra loads
Requires shifting tapers
Image: ATSSA
Notes: Key Message: Discuss median use
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The traffic lanes are routed onto the median. The structural capacity of the median must first be analyzed to determine its ability to carry the proposed traffic.
Suggested Questions: What types of tapers are these? Shifting tapers? Why? The number of lanes stay the same!
Additional Information: None
Possible Problems: None

## Slide 73: A8. Median Use
Advantages | Disadvantages
Separates construction from traffic Maintains continuous flow | Costly if barriers Temporary roadway needed Reduces shoulders Long duration
Notes: Key Message: Discuss median use
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize key points and keep brief. Also vehicles are in close proximity to each other. Long duration refers to the fact that this strategy in only suitable for long term projects. By definition, long term is 3 days or more.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 74: A9. Detour
Image: ATSSA
Notes: Key Message: Discuss detours
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize that detours take users on an alternate route. Desirable when there is unused capacity on roads running parallel to the closed roadway.
Suggested Questions: None
Additional Information: Detour: a construction work zone mitigation strategy wherein traffic in one or both directions is rerouted onto an existing highway to avoid a construction work zone. Detoured vehicles may travel on permanent roads only or on a combination of permanent and temporary roads. This strategy compensates for the removal of permanent travel lanes from service. Generally, a detour is applicable to all approaching traffic, but some detours reroute a portion of the traffic from the affected facility and accommodate all other traffic through the work zone.
Possible Problems: None

## Slide 75: A9. Detour
Advantages | Disadvantages
No traffic in construction area No roadside disruption Low cost Low impact Maintains number of lanes | Potential damage to detour route (trucks) Disruption to businesses and local traffic Local access Cost to motorists
Notes: Key Message: Discuss detours
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Emphasize that detours have low impact on traffic flow, although his is not always the case. Detouring traffic imposes additional capacity and load demands on an alternative route and may result in congestion and infrastructure deterioration on the detour (i.e., alternate route). Detours should be carefully evaluated to ensure that they are capable of accommodating the volume and types (configuration, size, and weight) of detoured vehicles. Mitigation may include temporary changes to traffic control (e.g., signal timing and signs) and remedial pavement and bridge work. When detours are being considered, the access normally provided to various land uses (e.g., residents and businesses) by the closed facility should also be considered. The added length of trips using the detour is a cost to motorists and should be evaluated. Ownership or owner agreement is usually needed to use a facility as a detour. If the agency detouring traffic from a facility does not own the roadway onto which traffic is detoured, coordination with the other agency is needed. In some jurisdictions, interagency agreements are needed and may provide for improvements to the detour route in preparation for the detour or as redress for damage induced by the detour traffic.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 76: A10. Multiple Lane Separation
Image: ATSSA
Notes: Key Message: Discuss multiple lane separation
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The traffic lanes in one direction are separated to allow construction activities within one of the lanes. On higher speed roadways, temporary barriers are provided to prevent errant vehicles from entering the work area.
Suggested Questions: What types of tapers are these? Shifting tapers? Why? The number of lanes stay the same!
Additional Information: This is a last resort, based on volumes.
Possible Problems: None

## Slide 77: A10. Multiple Lane Separation
Advantages | Disadvantages
Maintains number of lanes Low impact Maintains capacity | May require use of shoulders or medians Access to work area is difficult Workers may be exposed
Notes: Key Message: Discuss multiple lane separation
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Access to work area is difficult since it is surrounded by traffic.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 78: A11. Full Road Closures
For rehabilitation or maintenance
Eliminate exposure
Traffic is detoured
May be used for:
  Extended periods
  Weekends or nights
  Directional control
Image: ATSSA
Notes: Key Message: Full road closures are becoming a popular transportation management strategy.
Estimated Presentation Time:
Explanation of Cues/Builds:
Suggested Comments: When work under traffic first became necessary, it was common to close the road and complete work in the closed roadway section. However as traffic volumes increased and work under traffic became necessary on the Interstate system, closing the road was rarely used. Lane closures on high speed roadways put the workers and moving traffic very close. Working in one or two lanes at a time also slows the progress of work. Recently in an attempt to shorten the duration of work zones, agencies have closed major urban routes and done work on a full-time basis while the road was closed. Experience with full road closures has been very good and has reduced the time a road is affected by reconstruction. Total closures involve detours.
Suggested Questions: Would you consider a total closure? Any experiences with total closures in the room?
Additional Information: Full road closure: a construction work zone mitigation strategy wherein traffic operations are removed or suspended in either one or two directions on a segment of roadway or ramp. When roadway traffic is completely eliminated, construction efficiency and the resultant quality of permanent features (i.e., bridge and pavements) are maximized, while the time required for completion is minimized. Contract provisions (i.e., liquidated damages) should reflect the degree of disruption that this strategy involves.
Full road closure is designed to eliminate the exposure of motorists to work zones and workers to traffic by temporarily closing a facility for rehabilitation or maintenance. During full road closure, traffic is detoured, allowing workers full access to roadway facilities. It is not suitable for all construction situations. In applicable situations, use of full road closure can result in positive public sentiment, increased productivity, reduced project duration, increased safety and/or a shortened risk period, and in some cases cost savings. A full closure approach may be used for an extended period of time, on weekends or nights, or directionally on a segment of roadway.
Possible Problems: None

## Slide 79: A11. Full Road Closures
Several case studies
  I-95, Wilmington, DE
  M-10, Lodge Freeway, Detroit, MI
  I-84, Portland, OR
  http://www.ops.fhwa.dot.gov/wz
Image: FHWA
Notes: Key Message: Full road closures are becoming a popular transportation management strategy.
Estimated Presentation Time:
Explanation of Cues/Builds:
Suggested Comments: There are several successful stories. Here are just 3. For more information, refer to this website.
Suggested Questions: Would you consider a total closure? Any experiences with total closures in the room?
  Additional Information: Refer to report: http://www.ops.fhwa.dot.gov/wz/construction/full_rd_closures.htm
Possible Problems: None

## Slide 80: Potential Benefits of Full Closures
Reduced project duration
Increased worker productivity
Improved safety
Improved product quality
Positive public sentiment
Cost savings
Can be directional as long as traffic is diverted off the facility
Image: FHWA
Notes: Key Message: Discuss benefits of total closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Full road closure is an approach designed to eliminate the exposure of motorists to work zones and workers to traffic by temporarily closing a facility for rehabilitation or maintenance. During full road closure, traffic is detoured, allowing full access to roadway facilities. It is not suitable for all construction situations. In applicable situations, use of full road closure can result in positive public sentiment, increased productivity, reduced project duration, increased safety and/or a shortened risk period, and in some cases cost savings. A full closure approach may be used for an extended period of time, on weekends or nights, or directionally on a segment of roadway. Full closures help in three ways: 1) safer working conditions, 2) faster completion and 3) lower cost!
Suggested Questions: What are the benefits of full closures?
Additional Information: None
Possible Problems: None

## Slide 81: Disadvantages of Full Closures
Availability and suitability of alternate routes
Increased complaints if public outreach is weak
Increased delays?
Image: FHWA
Notes: Key Message: Discuss drawbacks of total closures
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Alternate routes need to be suited for the additional volume, including extra truck weight and widths. If public outreach is not properly done, the number of public complaints may increase. It is ESSENTIAL to the project to have a well-organized public information campaign.
Suggested Questions: What are the benefits of full closures?
Additional Information: None
Possible Problems: None

## Slide 82
Columbus, OH
Full Closure Strategies
Image: FHWA
Notes: Key Message: Permanent guide signs may need to be altered during a full road closure.
Estimated Presentation Time:
Explanation of Cues/Builds:
Suggested Comments: This picture shows some of the advanced guide signing and how it was altered for an extended full road closure in Columbus, Ohio.
Suggested Questions:
Additional Information:
Possible Problems:

## Slide 83: Full Closure Strategies
Portland, OR
Image: FHWA
Notes: Key Message: Full road closures may be safer for workers also.
Estimated Presentation Time:
Explanation of Cues/Builds:
Suggested Comments: This picture shows the closure of one direction of traffic on I-84 in Portland. Crews are able to pave without working in traffic.
Suggested Questions:
Additional Information:
Possible Problems:

## Slide 84: Full Closure Strategies
Columbus, OH
Image: FHWA
Notes: Key Message: Road closures also allow easier access for construction traffic.
Estimated Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: Here in Columbus, Ohio the entire roadway was closed and construction traffic was not delayed in getting to the work site.
Suggested Questions:
Additional Information:
Possible Problems:

## Slide 85: Considerations Associated with Full Road Closures
Construction logistics
Contractor logistics
Project schedule & completion
Impacts to businesses & residents
Capacity of alternate routes
Image: FHWA
Notes: Key Message: Considerations Associated with Full Road Closure
Estimated Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments:
• City/county agencies and personnel often need to be convinced of the feasibility of implementing a full closure strategy and the potential benefits that can be realized, compared to traditional means of performing rehabilitation under traffic.
• Full closure projects are typically done on an accelerated schedule. Contractor and supplier ability to provide adequate amounts of resources (materials, equipment, crew, asphalt production facilities) to maintain an accelerated pace should be assessed prior to letting a project as a full closure.
• Meeting the project completion deadline is particularly important when using full closure since this is often highly publicized as the date when the road will re-open. Therefore full closure projects may carry additional deadline pressure for those involved. This can accelerate decisions and limit the time for researching options when issues arise.
• Impacts to business or entertainment venues can be a factor. Many of the project sites planned closures around events and considered impacts to businesses during the planning process. Full closure projects are often scheduled on a 24-hour work basis, so there is potential for impacts to local residents, including noise and light pollution.
• Increases to traffic densities on alternate routes must be assessed, planned for, and managed. Depending on available alternate routes, there is a potential need for capacity improvements and operational enhancements that may require additional funding and coordination during the planning and programming phases.
Suggested Questions:
Additional Information: Source: Full Road Closure for Work Zone Operations
Possible Problems: None

## Slide 86: Alternative Closure Strategies
Limited capacity closures
Nighttime/ off-peak closures
Ramp closures
Intermittent closures
Image: FHWA
Notes: Key Message: Introduce alternative “closure” strategies
Estimated Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments:
A limited capacity closure refers to removal or suspension of a portion of traffic operations directionally from a segment of roadway for the purpose of reconstruction and/or maintenance activities. Traffic can be suspended based on vehicle type (e.g., removing automobiles, allowing trucks to continue) and/or destination (e.g., removing through traffic while maintaining local traffic).
-Many projects have utilized nighttime or off-peak closures to facilitate construction or maintenance operations. As defined in this report, a nighttime or off-peak closure is removal or suspension of traffic from a segment of roadway during the night or off-peak traffic periods for the purpose of reconstruction and/or maintenance activities. Often the work performed under nighttime closures requires complete access to the road such as bridge work or utilities repair.
-Ramp closure, as defined in this report, requires the removal or suspension of traffic from a ramp or series of ramps for the purpose of rehabilitation or construction. Closing a ramp can eliminate the need for complex traffic control that addresses both traffic entering the facility and traffic already on the facility.
-Intermittent closures are the removal or suspension of traffic from a segment of roadway for specified time increments, typically 5 to 30 minutes, while roadwork takes place. Examples of project types conducive to intermittent closures include utility work or bridge girder placement.
Suggested Questions:
Additional Information: Source: Full Road Closure for Work Zone Operations
Possible Problems: None

## Slide 87: A12. Night Work
Takes advantage of lower volumes at night
Direct costs tend to be higher
Image: ATSSA
Notes: Key Message: Discuss Night Work
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Night traffic volumes are generally lower than daylight volumes. Consequently, agency interest in night work as a means of reducing impacts is growing. Generally, there are no or few legal and contracting limits on an agency’s authority to specify day and time restrictions. There are many costs involved in highway construction, including those related to safety, user delay, and possible economic disruption. These direct costs tend to be higher for night construction because of additional devices, wage differential, and producer costs. Additionally, agencies and personnel experienced in administering night construction often refer to elevated risk factors (e.g., higher speeds, impaired drivers, and reduced visibility). However, a careful evaluation of potential ramifications should be conducted before selecting this alternative.
Additional Information: None
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 88: Nighttime Work Zones
More common due to:
  Daytime congestion
  Reduced business impact
  Reduced community impact
125
Image: FHWA
Notes: Key Message: Introduce NWZ
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Nighttime work zones are becoming more common due to these factors. As a TCS, you may be involved with nighttime projects.
Suggested Questions: How many of you have worked at night? Which problems or issues did you run into?
Additional Information: None
Possible Problems: None

## Slide 89: Advantages/Disadvantages of Nighttime Work
Advantages | Disadvantages
Lower traffic volumes Lower traffic impacts Lower impact to commercial activity Less overall impact | Higher agency cost Higher speeds More impaired drivers Crew social patterns disrupted Reduced visibility Noise Possible compromise of quality
Notes: Key Message: Introduce NWZ
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In addition to safety, nighttime projects must try to minimize adverse impact to the community and improve daytime mobility.
Suggested Questions: Why work at night? What are the advantages?
Additional Information: None
Possible Problems: None

## Slide 90: Conditions for Nighttime Work
Reduced traffic volumes
Easy setup and removal of the traffic control on a nightly basis
Image: ATSSA
Notes: Key Message: Introduce NWZ
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The decision to work at night is made during the planning and design stages. Generally, there are no or few legal and contracting limits on an agency’s authority to specify day and time restrictions. However, schedule restrictions (i.e., days, dates, or times when activities are not permitted) or requirements (i.e., days, dates, or times when activities must be performed) carry many potential consequences.
Suggested Questions: Which conditions are required to consider NWZ?
Additional Information: None
Possible Problems: None

## Slide 91: Other Factors That Impact the Suitability of Nighttime Work
Traffic
Construction
Social
Economic
Environmental
Health/alertness
Other
Image: ATSSA
Notes: Key Message: Introduce NWZ
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The decision to work at night is a difficult one. Many factors must be considered. These direct costs tend to be higher for night construction because of additional devices, wage differential, and producer costs. Additionally, agencies and personnel experienced
in administering night construction often refer to elevated risk factors (e.g., higher speeds, impaired drivers, and reduced visibility). Prevailing commercial, personal, family, and social patterns are the very reasons that traffic volumes are reduced at night; therefore, working at night may be very disruptive to a person’s quality of life. This may affect the ability of the transportation agency and contractor to attract qualified personnel. Also, construction often creates sound, and the noise levels that may be tolerable and conform to ordinances during day hours may not be at night. Also, nearly all construction operations (e.g., materials placement and compaction) are vision dependent. Although lighting systems can mitigate for the absence of sunlight, there remains a concern that some work is compromised by limited visibility.
Suggested Questions: Which factors should be considered? Is cost a factor? Noise?
Additional Information: None
Possible Problems: None

## Slide 92: Technological Advancements to Improve Nighttime Safety
Better sign retroreflectivity
Better channelizing devices
Crashworthiness of devices
Better lighting equipment
Better impact attenuators
Better worker visibility
Intrusion alarms
Driver information systems
Image: ATSSA
Notes: Key Message: Discuss how technological advancements make nighttime traffic control safer.
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: What is an intrusion alarm? An intruder?
Additional Information: Photo shows an intrusion system. If the cone is moved, an alarm goes off.
Possible Problems: None

## Slide 93: Key to Nighttime Work
Analyze the component parts of the work zone and make the necessary adjustments for nighttime conditions
Guidance is available
Image: NCHRP
Notes: Key Message: Introduce NWZ
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Adjustments will vary from case to case.
Suggested Questions: So which enhancements are we talking about?
Additional Information: None
Possible Problems: None

## Slide 94: NCHRP Report 476
Guidelines for Design and Operation of Nighttime Traffic Control for Highway Maintenance and Construction
Image: NCHRP
Notes: Key Message: Discuss NCHRP Report 476
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: NCHRP Report 476 includes some Typical Applications already enhanced for nighttime operations. Refer to NCHRP Report 476, Guidelines for Design and Operation of Nighttime Traffic Control for Highway Maintenance and Construction, for the specifics of the following seven TAs, including corresponding notes.
Suggested Questions: None
Additional Information: http://onlinepubs.trb.org/onlinepubs/nchrp/nchrp_rpt_476.pdf
Possible Problems: Spell out NCHRP = National Cooperative Highway Research Program

## Slide 95: Potential Nighttime Adjustments
Longer buffers and tapers
Type B lights on signs
PCMS
Better retroreflective materials
Elimination of hazards
Equipment and worker visibility
Proper illumination
Class 3 apparel for workers
Image: ATSSA
Notes: Key Message: Introduce NWZ
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Adjustments will vary from case to case. Here are a few to consider (give examples of each)
Suggested Questions: Why longer tapers and buffers? Lower volumes at night means higher speeds? Also, there is reduced visibility.
Additional Information: None
Possible Problems: None

## Slide 96: Illuminance Levels
Depend on:
  Level of accuracy
  The type of work
  The location of work
Three levels are defined:
  Level 1
  Level 2
  Level 3
Measured in foot-candles (fc)
Image: FHWA
Notes: Key Message: Discuss illumination requirements
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are three levels of illumination, based on the level of accuracy of the task on hand.
Suggested Questions: What requires more light? Threading a needle or walking around?
Additional Information: None
Possible Problems: None

## Slide 97: Recommended Min. Illuminance Levels & Categories for Nighttime WZ
LEV. | Min. Illuminance Level, fc | Area of Illumination | Examples of Activities
1 | 5 | Throughout spaces | Excavation, sweeping & cleanup, movement area in work zone, movement between two tasks, flagger stations
2 | 10 | Of tasks and around equipment | Paving, milling, concrete work, around paver or miller
3 | 20 | Illuminance on task | Crack filling, pot filling, tasks requiring extreme accuracy and attention
Notes: Key Message: Discuss illumination requirements
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This table shows you the three levels of illumination and the typical activities that can be conducted with that amount of light. Notice that Level III illumination is needed for tasks that require a lot of accuracy.
Suggested Questions: None
Additional Information: None
Possible Problems: The next three slides get into more details. Avoid discussing in detail here.

## Slide 98: B. Traffic Control Devices
Temporary signs
Arrow boards
Channelizing devices
Warning lights
Positive protection
Others
72
Image: ATSSA
Notes: Key Message: Introduce traffic control devices
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Most of you are familiar with these traffic control devices, but let’s spend some time discussing some key aspects.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 99: B1. Temporary Signs
Regulatory (R)
Warning (W)
Guide (G)
72
Images: FHWA
Notes: Key Message: Introduce categories (or types) of signs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are three types of signs: Regulatory, Warning and Guide. The letters R, W and G are used to designate these types. Let’s look at each type.
Suggested Questions: What shape are warning signs? Diamond.
Additional Information:
Possible Problems: This is an intro slide. Specific slides follow.

## Slide 100: Regulatory Signs
Indicate traffic laws and regulations
Shall be authorized by the governing authority
Design standards (EVEN IF TEMPORARY)
  Rectangular/Octagonal
  Black and white, red
79
Images: FHWA
Notes: Key Message: Discuss regulatory signs
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Regulatory signs indicate traffic laws and regulations. Their use is not trivial since they indicate traffic laws. Because of that, they must be authorized by proper authority. They are rectangular in shape (except for the STOP and YIELD signs) and white.
Suggested Questions: What if you had a temporary SPEED LIMIT sign in your work zone, what color would it be? WHITE. Orange speed limit signs do not exist.
Additional Information: Refer to MUTCD Section 6F.05. Regulatory signs such as those shown in Figure 6F-3 inform road users of traffic laws or regulations and indicate the applicability of legal requirements that would not otherwise be apparent. Regulatory signs shall be authorized by the public agency or official having jurisdiction and shall conform with Chapter 2B. TTC regulatory signs shall conform to the Standards for regulatory signs presented in Part 2 and in the FHWA’s “Standard Highway Signs” book (see Section 1A.11). Regulatory signs are generally rectangular with a black legend and border on a white background. Exceptions include the STOP, YIELD, DO NOT ENTER, WRONG WAY, and ONE WAY signs. The ONE WAY sign may be either a horizontal or vertical rectangular sign. If a TTC zone requires regulatory measures different from those existing, the existing permanent regulatory devices shall be removed or covered and superseded by the appropriate temporary regulatory signs. This change shall be made in conformance with applicable ordinances or statutes of the jurisdiction.
Possible Problems: Students may think that the SPEED LIMIT sign may be orange. This is not the case. Be prepared to defend this point. If the sign is orange, it would not be regulatory. Must discuss this since a question on the test refers to this.

## Slide 101
None of these signs should ever be orange!
Regulatory Signs in TTC Zones
Images: FHWA
Notes: Key Message: Show samples of regulatory signs
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: Here are some regulatory signs. None of these signs should ever be orange. Notice the W designation. Also notice that every time there’s a prohibition, the color red is used.
Suggested Questions: None
Additional Information: This is Figure 6F-3 in the MUTCD. The sign designation (number) may vary by state.
Possible Problems: None

## Slide 102: Warning Signs
Design standards
  Diamond shape
  Black on yellow (if permanent)
  Black on orange (if temporary)
PERMANENT
TEMPORARY
83
Images: FHWA
Notes: Key Message: Introduce warning signs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Warning signs are diamond shape and black on yellow (if permanent and black on orange (if temporary)
Suggested Questions: What does yellow mean? Warning!
Additional Information: TTC warning signs shall conform to the Standards for warning signs presented in Part 2 and in FHWA’s “Standard Highway Signs” book (see Section 1A.11). Except as noted in the Option below, TTC warning signs shall be diamond-shaped with a black legend and border on an orange background, except for the W10-1 sign which shall have a black legend and border on a yellow background, and except for signs that are permitted in Parts 2 or 7 to have fluorescent yellow-green backgrounds.
Possible Problems: None

## Slide 103
Sample Warning Signs in TTC Zones
Images: FHWA
Notes: Key Message: Show examples of warning signs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TTC warning signs are diamond shape and black on orange.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 104: Guide Signs
Provide guidance information to help users in the most simple, direct manner possible
Example:
  Route markers
  Detour signs
Images: FHWA
Notes: Key Message: Introduce guide signs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The third category of signs are guide sings. These signs are used to “guide” users from point A to point B.
Suggested Questions: What color are guide signs? Depends on their use (next slide)
Additional Information: Refer to MUTCD Section 6F.50 Guide Signs. Guide signs along highways provide road users with information to help them along their way through the TTC zone. The design of guide signs is presented in Part 2.GuidaThe following guide signs should be used in TTC zones as needed: A. Standard route markings, where temporary route changes are necessary; B. Directional signs and street name signs; and C. Special guide signs relating to the condition or work being done.
Possible Problems: None

## Slide 105: Guide Signs
Design standards
  Rectangular
  Color depends on use
    White on green
    Black on orange
    White on brown
    White on blue
93
Images: FHWA
Notes: Key Message: Introduce guide signs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The third category of signs are guide sings. These signs are used to “guide” users from point A to point B.
Suggested Questions: What color are guide signs? Depends on their use (next slide)
Additional Information: Refer to MUTCD Section 6F.50 Guide Signs. Guide signs along highways provide road users with information to help them along their way through the TTC zone. The design of guide signs is presented in Part 2.GuidaThe following guide signs should be used in TTC zones as needed: A. Standard route markings, where temporary route changes are necessary; B. Directional signs and street name signs; and C. Special guide signs relating to the condition or work being done.
Possible Problems: None

## Slide 106: B2. Arrow Boards
A supplemental device
  Should be used in addition to appropriate signs, barricades, or other traffic control devices
97
Image: ATSSA
Notes: Key Message: Introduction to arrow boards
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a very effective device if used properly, but it can be lethal if used improperly. As you can see, arrow boards are made of a matrix of elements capable of either flashing or sequential displays. AP are A supplemental devices, used in addition to appropriate signs, barricades, or other traffic control devices. They do not replace signs, they supplement them. We still need advance warning signs!
Suggested Questions: What does “supplemental” mean?
Additional Information: Refer to MUTCD Section 6F.61. “This sign shall provide additional warning and directional information to assist in merging and controlling road users through or around a TTC zone.”
Possible Problems: None

## Slide 107: Arrow Board Types
Type | Min. Size (in.) | Min. Legibility Distance | Min. No. of Elements | Application
A | 48 x 24 | ½ mi | 12 | Low-speed urban streets
B | 60 x 30 | ¾ mi | 13 | Intermediate speed, Mobile ops.
C | 96 x 48 | 1 mi | 15 | High-speed
D | None | ½ mi | 12 | Vehicle-mounted
98
Source: FHWA
Notes: Key Message: Discuss arrow board types
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Arrow boards shall meet the minimum size, legibility distance, number of elements, and other specifications shown on this figure (table). Type A arrow boards are appropriate for use on low-speed urban streets. Type B arrow boards are appropriate for intermediate-speed facilities and for maintenance or mobile operations on high-speed roadways. Type C arrow boards are intended to be used on high-speed, high-volume motor vehicle traffic control projects. Type D arrow boards are intended for use on authorized vehicles.
Suggested Questions: Which type should be used on freeways? Type C, which is legible (visible) for 1 mile.
Additional Information: Refer to MUTCD Section 6F.61.(Figure 6F-6.). Type A, B, and C arrow boards shall have solid rectangular appearances. A Type D arrow board shall conform to the shape of the arrow.
Possible Problems: May have to define high-speed versus low-speed again.

## Slide 108: Arrow Boards at Night
Shall be dimmed
  50% dimming from full-rated lamp voltage
Image: ATSSA
Notes: Key Message: Discuss arrow board dimming
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Arrow board elements shall be capable of at least a 50 percent dimming from full brilliance. The dimmed mode shall be used for nighttime operation of arrow boards. Full brilliance should be used for daytime operation of arrow boards.
Suggested Questions: Why do we dim arrow boards at night? They would blind drivers!
Additional Information: Refer to MUTCD Section 6F.61.
Possible Problems: None

## Slide 109: Arrow Board Modes
Flashing arrows (or chevrons) for lane closures
Caution mode for shoulder work
Use arrows ONLY when a lane is closed!
Images: FHWA
Notes: Key Message: Discuss arrow board applications
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Arrows or chevrons are used to warn of a lane closure, caution mode is used for shoulder work.
Suggested Questions: When you work on the shoulder, how many lanes are closed? None!
Additional Information: Refer to MUTCD Section 6F.61.
Possible Problems: Some states prefer arrows (Virginia, Florida, Maryland) , others chevrons (New Mexico). Several states do not allow the flashing bar caution mode. Tailor to the state. 2009 MUTCD allows the “dancing diamonds” as a third caution mode.

## Slide 110: Preferred Arrow Board Location
For a stationary lane closures should be located on the shoulder at the beginning of the taper
OUT OF THE TRAVEL LANE,
IF POSSIBLE
Image: FHWA
Notes: Key Message: Discuss arrow board location
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: Arrow boards are not crashworthy. Ideally they should be located off the travel lane. For a stationary lane closures should be located on the shoulder at the beginning of the taper. For a stationary lane closure, the arrow board should be located on the shoulder at the beginning of the merging taper. Where the shoulder is narrow, the arrow board should be located in the closed lane. An arrow board should be placed on the shoulder of the roadway or, if practical, further from the traveled lane. It should be delineated with retroreflective TTC devices. When an arrow board is not being used, it should be removed; if not removed, it should be shielded; or if the previous two options are not feasible, it should be delineated with retroreflective TTC devices.
Suggested Questions: Where should the arrow board be located?
Additional Information: Refer to MUTCD Section 6F.61.
Possible Problems: Some of the “should” conditions above may be “shall” conditions.

## Slide 111
Proper Location?
Image: ATSSA
Notes: Key Message: Illustrate previous point through an example.
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This shows the arrow board at the beginning of the buffer space.
Suggested Questions: is this the best location? Is there room on the shoulder?
Additional Information: Photo taken in Washington, DC, by Juan Morales
Possible Problems: None

## Slide 112: Arrow Boards Shall Not Be Used…
On lane shifts
On two-lane roads
Image: ATSSA
Notes: Key Message: Discuss when NOT TO use APs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are two conditions under which arrow boards shall not be used: On to laterally shift traffic and on two lane roads. Let’s discuss why.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 113: B3. Channelizing Devices
Cones
Tubular markers
Vertical panels
Drums
Barricades
100
Images: ATSSA
Notes: Key Message: Start discussion on channelizing devices
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second TCD to be discussed are channelizing devices. These are the one to discuss.
Suggested Questions: None
Additional Information: Channelizing devices include cones, tubular markers, vertical boards, drums, barricades, and temporary raised islands.
Possible Problems: None

## Slide 114: Functions of Channelizing Devices
Secondary
function
PROTECTION
Main
function
CHANNELIZATION
Notes: Key Message: Discuss the function of channelizing devices
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The main function of channelizing devices is channelization or delineation. Although they may provide some level of protection, this is not their function. If we need protection, we must use protection devices, such as barriers.
Suggested Questions: Do they provide “protection”? Some, but this is not their main function. Would these devices keep your car from falling in a hole? No.
Additional Information:
Possible Problems: None

## Slide 115: B4. Warning Lights
Included in MUTCD
  Only a few states use them
Types
  A - Low-intensity flashing
  B - High-intensity flashing
  C - Low-intensity steady-burn
  D – 360-degree
110
Image: ATSSA
Notes: Key Message: Discuss types of warning lights.
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Type A, Type B, Type C, and Type D 360-degree warning lights are portable, powered, yellow, lens-directed, enclosed lights.
Suggested Questions: None
Additional Information: Refer to MUTCD Section 6F.78. When warning lights are used, they shall be mounted on signs or channelizing devices in a manner that, if hit by an errant vehicle, they will not be likely to penetrate the windshield.
Possible Problems: None

## Slide 116: Type A Warning Lights
Alternating
Low intensity flashing
To mark
  Hazards
  Obstructions adjacent to the roadway
Image: ATSSA
Notes: Key Message: Discuss Type A warning lights.
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Type A Low-Intensity Flashing warning lights shall be maintained so as to be capable of being visible on a clear night from a distance of 3,000 ft. Type A Low-Intensity Flashing warning lights are used to warn road users during nighttime hours that they are approaching or proceeding in a potentially hazardous area. Type A warning lights may be mounted on channelizing devices.
Suggested Questions: None
Additional Information: Refer to MUTCD Section 6F.78.
Possible Problems: None

## Slide 117: Type B Warning Lights
Bright
High intensity flashing
Visible from 1,000’ without sun behind
Mounted on advanced warning signs
Type B!
Image: ATSSA
Notes: Key Message: Discuss Type B warning lights.
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Type B High-Intensity Flashing warning lights shall be maintained so as to be capable of being visible on a sunny day when viewed without the sun directly on or behind the device from a distance of 1,000 ft.
Suggested Questions: None
Additional Information: Refer to MUTCD Section 6F.78.
Possible Problems: None

## Slide 118: Type C (and D) Warning Lights
Constant = Steady-burn
Visible from 3,000’ on a clear night
Used in a series
  For delineation
Not for warning
Images: ATSSA
Notes: Key Message: Discuss Type C and D warning lights
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Type C Steady-Burn warning lights and Type D 360-degree Steady-Burn warning lights may be used during nighttime hours to delineate the edge of the traveled way. When used to delineate a curve, Type C and Type D 360-degree warning lights should only be used on devices on the outside of the curve, and not on the inside of the curve.
Suggested Questions: None
Additional Information: Refer to MUTCD Section 6F.78.
Possible Problems: Required by several states.

## Slide 119: B5. Positive Protection Devices
Crashworthy (crash-tested) devices that contain and/or redirect vehicles to prevent vehicular penetration into a work zone
  i.e., barriers
112
Image: FHWA
Notes: Key Message: Discuss the definition of positive protection devices
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Positive protection is also used to prevent vehicles from striking objects that may be hazardous. Such devices must meet NCHRP Report 350 requirements for crashworthiness, or the newer Manual for Assessing Safety Hardware (MASH). Temporary traffic barriers are devices designed to help prevent penetration by vehicles while minimizing injuries to vehicle occupants, and are designed to protect workers, bicyclists, and pedestrians.
Suggested Questions: What is your current policy for when to use positive protection?
Additional Information: All crashworthy devices should have an FHWA Office of Safety acceptance letter. Devices already approved may continue to be used, but new devices must be tested and approved based on the MASH requirements as MASH supersedes NCHRP Report 350.
Possible Problems: None

## Slide 120: Positive Protection Devices: Portable Barriers
Speed
Traffic volume/ composition
Road classification
Deflection space
Roadway alignment
Sight distance
Other factors
Image: ATSSA
Notes: Key Message: Discuss types of traffic barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: There are several types of barriers that are acceptable in several states. Some are listed here. Let’s look at them.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Photo is from the Great Wall of China, the mother of all barriers.
Possible Problems: Instructors may have a tendency to go into too much detail on this slide. Each barrier type is discussed in the following slides.

## Slide 121: FHWA’s Temporary Traffic Control Devices Rule States That…
“At a minimum, positive protection SHALL be considered where workers are at increased risk from motorized traffic…”
“devices should be used to the extent they are possible, practical, and adequate to reduce worker exposure…”
Notes: 121
Key Message: Describe the FHWA Work Zone Rule
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: 23 CFR 630 Subpart K is the Temporary Traffic Control Devices Rule. It requires consideration, but it doesn’t always require use of positive protection. Use is not always required due to factors such as project duration (do we have adequate time to install the devices), cost (will it be expensive relative to the project cost), and type of work (are workers exposed to traffic), to name a few. Exposure control measures and other traffic control measures discussed in Subpart K should be considered when barriers are not appropriate.
From FHWA Q/A Document (http://ops.fhwa.dot.gov/wz/resources/temptraf_qa.pdf):
Positive Protection Devices – use shall be based on an engineering study.
An engineering study may be used to develop positive protection guidelines
Use of positive protection shall be considered in work zone situations that place workers at increased risk from motorized traffic and where positive protection devices offer the highest potential for increased safety for workers and road users. Specific situations include work zones that provide workers no means of escape; long duration work zones (e.g., two weeks or more) resulting in substantial worker exposure; projects with high anticipated operating speeds (e.g., 45 mph or greater) and high traffic volumes; work operations that place workers close to travel lanes open to traffic; and roadside hazards, such as drop offs or unfinished bridge decks.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 122: Use of Positive Protection Devices
Shall be based on an engineering study
Decision to use can be based on consideration of the factors listed in this module
Image: AASHTO
Notes: Key Message: Discuss positive protection devices such as portable concrete barrier
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Positive protection devices such as portable concrete barrier (shown) prevent vehicles from entering the work area or separate vehicles in temporary two-lane, two-way traffic on normally divided highways. Subpart K requires that the need for positive protection shall be based on an engineering study. Additionally, subpart K states that an engineering study may also be used to develop positive protection guidelines for the agency.
Suggested Questions: None
Additional Information: The diagram is from the Roadside Design Guide showing a typical portable concrete barrier cross section.
Possible Problems: None

## Slide 123: Functions of PP Devices
Main
function
PROTECTION
Secondary
function
CHANNELIZATION
Notes: Key Message: Discuss the functions of traffic barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The main purpose of using these devices is protection, not channelization. Channelization is a secondary consideration. The decision to use positive protection should be based on protective needs not channelizing needs. If not needed for protection then IT SHALL NOT BE USED. The channelizing needs are always a secondary consideration. Devices are used for protection of the work space.
Suggested Questions: Can portable concrete barriers ever be used to form tapers? Yes, but typically in low speed urban settings. For higher speed facilities, other devices form the taper and the barrier is behind these devices. See MUTCD TA-24 on page 6H-73.
Additional Information: None
Possible Problems: None

## Slide 124: Temporary Barriers
Design must be in accordance with AASHTO Roadside Design Guide
May be:
  Concrete
  Metal
  Plastic, or
  Any approved material
Image: AASHTO
Notes: Key Message: Discuss types of traffic barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Several different types of barriers exist and their use is based on factors such as deflection. Devices must be crashworthy based on NCHRP Report 350 and the newer Manual for Assessing Safety Hardware (MASH) standards. Also see ANSI A10.47 for factors that influence the decision to use positive protection.
Suggested Questions: Do barriers have to be made of concrete? No.
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Participants may expect to see information tailored to their state. Performing research into types of barriers and state and local standards ahead of time can improve the course.

## Slide 125: Types of Temporary Traffic Barriers
C:\Users\JMM Toshiba\Dropbox\Barriers VA 2\IMG_0887.JPG
Concrete
Water-filled
Anchored
Movable
Mobile
Steel
Barrier selection is based on its application and its deflection! CHECK WITH YOUR STATE!
Image: ATSSA
Notes: Key Message: Discuss types of traffic barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
  Suggested Comments: There are several types of barriers that are acceptable in several states. Some are listed here. Let’s look at them.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Photo is from Fairfax County Parkway, Fairlakes, VA, by J. Morales.
Possible Problems: This is an intro slide. Each barrier types is discussed in the following slides

## Slide 126: 1. Portable Concrete Barriers (PCB)
Perhaps the most common
Self-standing
Various shapes
  F-Shape: Preferred
Deflection = 2 ft. up to 45 mph
Images: FHWA
Notes: Key Message: Discuss concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The preferred shape for concrete barriers is the F-shape, which has 9 inches at the top. The generic “Jersey” shape is no longer acceptable in most states. These barriers are held in place by their own weight. The preferred installation method for temporary concrete traffic barrier is freestanding and requires a minimum 2 ft. (0.6 m) clear area behind the barrier to allow for lateral deflection in both work areas and lane separation situations.
Suggested Questions: What is deflection? The distance the barrier would move when struck.
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Tailor to the state

## Slide 127: Jersey Shape vs. F-Shape
Jersey Shape
F-Shape
7”
10”
32”
32”
Image: AASHTO
Notes: Key Message: Discuss concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the two most common concrete safety shapes. An important difference between the NJ and the F shapes is the height of the slope break. The lower break on the F shape (7”) helps minimize the lifting of the impacting side of the vehicle, reducing the tendency to roll small vehicles. The F shape is preferred over the NJ shape and it is required in most states. The F-Shape design was specifically engineered to limit the potential roll over and the 9.1-degree constant slope reasonably mimics that performance. Another consideration may be the nature of the traffic using the facility or future overlays. The Jersey- and F-shape barriers are both “safety-shape” barriers that begin with a 3 inch vertical face at the pavement level. Then they break to a sloped face that goes up to 13 inches above the pavement on the Jersey barrier, but only up to a height of 10 inches in the case of the F-Shape. Both then transition to a nearly vertical face to the top of the barrier.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Jersey Barriers: Jersey barriers were the original and most widely used safety shape concrete barriers. The only difference between Jersey barriers and F-shape barriers is that the distance from the ground to the slope break point is 13 inches in Jersey barriers, versus 10 inches for F-shape barriers. In high speed impacts, there is a greater likelihood that a small car will be rolled by a Jersey barrier than by an F-shape barrier. F-Shape Barriers: The F-shape barrier was specifically engineered to limit the potential for small cars to rollover upon impact. The F-shape barrier begins with a 3-inch vertical face at the pavement level, then breaks to a sloped face that rises to a height of 10 inches, before changing to a nearly vertical face at the top of the barrier. F-shape barriers are not shaped like the letter "F." They get their name from the research study that analyzed the performance of barrier design parameters, where barrier configurations were labeled A through F, and F was the best-performing design. Refer to: http://www.fhwa.dot.gov/publications/publicroads/00marapr/concrete.cfm. Because the Jersey-shape design requires very little modification to become an F-shape design, asphalt resurfacing can convert the Jersey-shape barrier into a more F-shape-like barrier that is safer for lighter cars. However, these increased layers of asphalt also reduce the working height of the barrier which reduces its effectiveness for heavier vehicles.
Possible Problems: No need to elaborate or discuss these angles.

## Slide 128: Advantages of Portable Concrete Barriers
Less expensive for long-term projects
Easy to maintain
Reusable
Low deflection
Image: ATSSA
Notes: Key Message: Discuss advantages of concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: Photo is from Fairfax County Parkway, Fairlakes, VA, by J. Morales.
Possible Problems: None

## Slide 129: Disadvantages of Portable Concrete Barriers
Heavy equipment and lane closure are needed for installation/ removal
Not suited for short-term projects or moving operations
Image: ATSSA
Notes: Key Message: Discuss disadvantages of concrete barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: Photo is from Fairfax County Parkway, Fairlakes, VA, by J. Morales.
Possible Problems: None

## Slide 130
Easier to handle
Follow manufacturer’s instructions
Various types available
2. Water-Filled Barriers
Proprietary
https://tf13.stagemydomain.com/
Notes: Key Message: Discuss water-filled barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: These are water-filled. The main advantage is that they are lightweight and easy to move. They must be filled with water according to the manufacturer’s instructions.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Pictures are from brochures.
Possible Problems: None

## Slide 131
Triton Barriers
(Proprietary)
Images: Valtir
Notes: Key Message: Discuss Triton Barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The Triton barrier is an example. May have to be interconnected with cables to be considered PP devices. Check manufacturer’s instructions.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Pictures are from brochures. Triton Barrier Design Features:
﻿• Positive, crashworthy protection up to 45 M.P.H. (70 km/h) - does not allow penetration into work area • Absorbs collision energy and safely redirects errant vehicles • Fast and easy deployment - 600 feet per hour with just three workers • Modular design allows use in varied lengths for both straight and curved applications • No cranes or heavy equipment needed for deployment • Certified as its own end treatment • Transition hardware available for attachment to guardrail or concrete barrier • Internal steel frame — no additional assembly required • Positively connected with a 2” steel pin • Built on steel tension cable, connects from barrier to barrier to form a single continuous barrier. • No external rails required for NCHRP 350 Certification.
Possible Problems: Proprietary or Energy Absorption Systems. Do not imply preference or endorsement.

## Slide 132
Roadguard Barriers
(Proprietary)
Images: Trident Devices
Notes: Key Message: Discuss Roadguard Barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: For water filled units to actually perform as a barrier, you must have a steel framework, internal or external.
Suggested Questions: None
Additional Information: Brochure: Using new blow-mold technology, the ROADGUARD/2 is a double-chambered, 85 lb. barrier that is stronger and lighter than all competitive Jersey-style barriers. The two chambers are structurally interlocked and brass-bolted together with four strong structural foam-molded polyolefin lugs. The double chamber provides two vertical walls in the center of the barrier, delivering added strength and stability. Easy to handle, quick to install, 6-feet long, 3.5-feet high, 2-feet wide at base. Weighs ONLY 85 lbs. empty, and a secure 1,600 lbs. when filled with water. Patented locking design keeps barriers firmly connected. Locks with all ROADGUARD/2, ROADGUARD and OTW MB 350 barriers. Two (2) fill caps, four (4) drain plugs. Fork lift slots, hand grips, and positions for lights and screens. Barriers curve up to 15 degrees in each direction at each connection. Manufactured with UV inhibitors. Available in orange, white, and mixed orange/white colors. Approved as a Longitudinal Channelizing Device
Possible Problems: Trident Security Devices, Inc. Do not imply preference or endorsement.

## Slide 133
(Proprietary)
Yodock Barriers
Images: Yodock Wall Co.
Notes: Key Message: Discuss water-filled barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: These are water-filled. The main advantage is that they are lightweight and easy to move. They must be filled with water according to the manufacturer’s instructions.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Pictures are from brochures. Yodock Wall – Yodock units have been crash tested in three ways: as stand alone barricade units, as longitudinal channelizers, as shown here, and with the addition of a steel box beam rail, as barriers. When deployed like this, water filled units are a good substitute for a line of drums. They are not redirective vehicle barriers, as the vehicle may penetrate a longitudinal channelizing barricade. Forces on the vehicle occupants must be below the limits acceptable for a barrier impact.
Possible Problems: Pictures shown are of the YODOCK barrier, which is proprietary or Yodock. Do not imply preference or endorsement.

## Slide 134
Portable
Water-filled
Guardian Barriers (Armorcast)
(Proprietary)
Images: Armorcast
Notes: Key Message: Discuss Guardian Safety Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
The guardian safety barrier is 42 inch high by 72 inch long water filled low-density polyethylene barrier. The barrier is both NCHRP 350 TL-2 and TL-3 approved and can act as its own end treatment. To meet TL-3 guidelines, each barrier includes four interlocking powder-coated steel bars. Empty
weight is 280 pounds and full weight is 1,750 pounds with water.
Estimated Unit Price: $700 ea. NOTE: Unit price and specifications are based on available 2011/2012 internet and company resources, the prices and specifications are
subject to change after this report has been published.
Suggested Questions: None
Additional Information: Armorcast is the manufacturers. Guardian is the name of the barrier.
Possible Problems: None

## Slide 135: 3. Anchored Barriers
Various types
  Type K, for instance
May be required for bridge railings
Minimal deflection!
Images: ATSSA
Notes: Key Message: Discuss Anchored barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Anchored barriers are bolted down so their deflection is zero. They are used where allowance (room) for that 2-foot deflection is not present. They may also be required on bridge railings.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information. Bridge railings differ from other longitudinal roadside barriers because they are physically connected to the bridge structure, and are not usually designed to deflect when struck by a vehicle. Bridge railings are very important components of roadway safety systems and play an important role in preventing and mitigating crashes. Since the primary purpose of a bridge railing is to prevent penetration, it must be strong enough to redirect an impacting vehicle. Various types of anchoring exist: Anchor bolts, drift pins or brackets. Check with your State DOT.
Possible Problems: Their use is a state preference. May also be called “Type K”, “K wall” or “K rail”. California’s current standard for concrete temporary barrier is K-rail. This barrier, when properly installed, may also be used in semi-permanent applications. The K-rail that has become the standard within California consists of 6.1-m (20-ft) long sections with pin and loop connections, each weighing approximately 3630 kg (8000 lbs). Eventually, details were developed which also allowed K-rail to be used as a semi-permanent barrier (2-5 years). The configuration of semi-permanent barrier required pin and loop connections between the K-rail segments as well as stakes at each of the four stake holes located in the K-rail. The configuration passed NCHRP Report 350 criteria, but removing the stakes from a paved surface led to expensive repairs and increased worker exposure. An effort is being made to discover the minimum number of stakes and distance that a K-rail barrier can be placed adjacent to an excavation and as a median barrier before it is no longer compliant with NCHRP Report 350. Minimizing the number of stakes needed in order to achieve a NCHRP Report 350-compliant barrier will save money and worker exposure time.

## Slide 136
Why anchor the barrier on bridge railings?
Image: ATSSA
Notes: Key Message: Discuss anchored barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Temporary barriers on bridges should be structurally connected to the deck. The Type K wall, described in Chapter 9 of the RDG is an appropriate system to use in this case.
Suggested Questions: What would have happened is this barrier is not attached to the bridge deck?
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Their use is a state preference.

## Slide 137
Anchor Barriers if No
Deflection Space Behind the Barrier
Image: ATSSA
Notes: Key Message: Discuss anchored barriers if there is no room for deflection
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: When there is no space for deflection behind the barrier, portable concrete barriers should be anchored.
Suggested Questions: What would have happened is this barrier is not attached to the pavement?
Additional Information: Photo on I-495, Virginia, by J. Morales. Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Their use is a state preference.

## Slide 138
Anchor Barriers on Bridge Decks
Image: ATSSA
Notes: Key Message: Discuss anchored barriers on bridge decks
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: On bridge decks, barriers should be anchored. Bridges vibrate, plus we don’t want to risk the barrier moving and falling down.
Suggested Questions: How can you tell these are anchored? The slots on the side.
Additional Information: Photo on I-495, Virginia, by J. Morales. Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: Their use is a state preference.

## Slide 139
Bolted
Staked/Pinned
Free standing
Backfilled
The pins and bolts should not protrude beyond the face of the barrier
Anchoring Portable Concrete
Barriers to the Traveled Way
Refer to your State’s Construction Specifications
Notes: Key Message: Discuss anchoring
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: There are various ways to achieve the anchoring. Some are listed here. Refer to RDG and your State’s Construction Specifications for details
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: None

## Slide 140: 4. Movable Barriers
Repositioned laterally using a transfer vehicle that travels along the barrier
Enable short-term closures to be installed and removed on long-term projects
(Proprietary)
Image: Illinois DOT
Notes: Key Message: Discuss movable barriers
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Movable barriers are capable of being repositioned laterally using a transfer vehicle that travels along the barrier. Movable barriers enable short-term closures to be installed and removed on long-term projects. Providing a barrier-protected work space for short-term closures and providing unbalanced flow to accommodate changes in the direction of peak-period traffic flows are two of the advantages of using movable barriers.
Suggested Questions: What is the main advantage of these barriers? Flexibility and speed!
Additional Information: None
Possible Problems: Their use is a state preference.

## Slide 141
Image: Maryland DOT
Notes: Key Message: Discuss movable barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice that the barrier is not dragged along the pavement but rather lifted off using a unique T-shape cross section
Suggested Questions: None
Additional Information: Photo is from MD SHA.
Possible Problems: Their use is a state preference.

## Slide 142
Image: Barrier Systems
Notes: Key Message: Show movable barrier movie clip
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This video clip shows movable barriers
Suggested Questions: None
Additional Information: Source: Barrier Systems. Video lasts 40 seconds. No need to show the entire video. Show as much as needed and move on.
Possible Problems: Video plays automatically. If it doesn’t, hit ESC and browse to the folder that has the video clip and play it directly from there.

## Slide 143: 5. Mobile Barriers
Short-term/ some mobile operations
Minimizes worker exposure
Reduces set-up time
(Proprietary)
Image: Mobile Barriers, Inc.
Notes: Key Message: Discuss mobile barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a vehicle that becomes a barrier. It is ideal for short duration work, providing positive protection. Advantages: Mobile positive protection, minimizes exposure, reduces set-up time, portable power/ lighting, arrow board/ VMS/ Radar, 50 minutes to swap from left to right. MBT-1 provides a physical and visual wall between passing traffic and the maintenance personnel. With integrated crash attenuation at the rear, a semi-tractor at the front, and a rigid wall on the side toward passing traffic, the Trailer provides 100’ of barrier and protected work area. The work area itself will be less cluttered and better lit.
Suggested Questions: None
Additional Information: http://www.mobilebarriers.com. The Mobile Barriers Trailer (MBT-1) is an integrated, rigid wall, trailer that can be used in conjunction with standard semi-tractors to provide mobile, improved, safety and work environments for personnel at applicable maintenance, construction and security sites. In the context of interstate construction, the Trailer is specifically designed to reduce work zone incursions by passing traffic (fore, aft and side protection), to reduce the number of collateral vehicles and equipment needed at and within the work zone, and to improve lighting and ambient conditions thus improving general conditions and alertness on site. Each of these three areas has been shown in applicable research to be significant contributors to on site fatalities and injuries.
Possible Problems: None

## Slide 144: Reduces “Rubbernecking”
Image: Mobile Barriers, Inc.
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Modular platforms, caboose (movable rear axle assembly) & wall sections. Configurable from 42-102’w/ 0-3 wall sections. Use one or more individually or together. Reconfigurable to the right or left. (tractor & caboose attach at either end) . Tested/FHWA Accepted under NCHRP 350 & MASH for TL-2 and TL-3 use on the National Highway System.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 145
Image: Mobile Barriers, Inc.
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is the view from above. Notice the protection.
Suggested Questions: None
Additional Information: Source: Art Korfin
Possible Problems: None

## Slide 146
Concrete Barrier Repairs
Image: Mobile Barriers, Inc.
Notes: Key Message: Mobile Barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Notice on side with barrier no buffer taken. On side without buffer taken. Reduces congestion.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 147: 6. Steel Barriers
May be used for temporary or permanent applications
(Proprietary)
Image: Hill and Smith
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The 6th barrier type to discuss are steel barriers. Hill and Smith, Inc. has developed a durable portable steel traffic barrier, designed to protect
highway travelers, as well as road and construction crews. Traditional portable barrier systems are costly, heavy to transport and handle, time-consuming and do not provide the energy-absorbing capabilities of Zoneguard.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 148: Typical Uses
Short-term work zones, such as short activity areas where the barrier must be placed and removed on a daily basis
Image: Hill and Smith
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Typical uses are short-term work zones, such as short activity areas where the barrier must be placed and removed on a daily basis.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 149
Examples:
  BarrierGuard 800
  Vulcan
  ZoneGuard
Steel Barriers
Image: Hill and Smith
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The next barrier type to discuss are steel barriers. Hill and Smith, Inc. has developed a durable portable steel traffic barrier, designed to protect highway travelers, as well as road and construction crews. Traditional portable barrier systems are costly, heavy to transport and handle, time-consuming and do not provide the energy-absorbing capabilities of Zoneguard.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 150
BarrierGuard 800
(Proprietary)
Image: Thomas Barriers
Notes: Key Message: Discuss steel barriers
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
BarrierGuard 800 portable steel barrier is the latest in road barrier technology, designed to protect both motorists and construction workers. Rigorously tested to meet the highest demands throughout the world, BarrierGuard has achieved the HIGHEST PERFORMANCE levels of any portable steel barrier for both US testing (NCHRP 350) and European testing (EN1317) – achieving TL-3, TL-4, N2 and H2 criteria. Its unique stepped profile has proven to reduce damage to both vehicle and barrier during impact, minimizing the need for repair or replacement. During impact, BarrierGuard provides an extremely shallow exit angle for the vehicle, minimizing the risk of secondary accidents. BarrierGuard 800’s galvanized steel structure offers an expected LIFE CYCLE OF 25 YEARS and with its exceptional durability, the requirement for replacement through handling or impact damage, unlike similar portable barriers, is greatly reduced
Suggested Questions: None
Additional Information: None
Possible Problems: None
.

## Slide 151
Vulcan Steel Barriers
(Proprietary)
Image: Valtir
Notes: Key Message: Discuss Vulcan Barriers
Est. Presentation Time: 1-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Similar to the ArmorGuard barrier system, the Vulcan Barrier systems is a steel moveable barrier capable of providing protection for straight tangents and horizontal curves. Stackable barriers are available in 13, 26, or 40 foot sections. The barrier system is moved at the site with either a forklift system or optional caster wheels. The barrier system was tested and approved according to NCHRP-350 TL-3 guidelines.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 152
ZoneGuard
(Proprietary)
Image: Hill and Smith
Notes: Key Message: Discuss ZoneGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here you see a photo of the system. Zoneguard has been extensively tested to US as well as European crash test standards, and has been accepted by the FHWA as meeting NCHRP 350 and MASH-08 TL-3 and TL-4. More footage per truck means truck entries to and exits from the work zone are reduced by over 80%. Can be used either anchored only at the ends or intermittently to get acceptable deflection
Suggested Questions: None
Additional Information: Photo is from brochure.
Possible Problems: None

## Slide 153
ZoneGuard
(Proprietary)
Image: Hill and Smith
Notes: Key Message: Discuss ZoneGuard
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Zoneguard steel barrier system consists of 50 foot sections that are installed without hand tools using common construction equipment. Unlike other available steel barrier systems, the ZoneGuard does not offer wheels, but does offer rubber padding. The barrier systems can be anchored at the ends, or can be anchored every 33 feet to minimize deflection. The barrier system was tested and approved according to NCHRP-350 at the TL-2 and TL-3 guidelines.
Estimated Unit Price: $0.06 - $0.21 /ft./day rental
Suggested Questions: None
Additional Information: Photo is from brochure.
Possible Problems: None

## Slide 154: Temporary Traffic Barrier as Channelizing Devices
Should not be used for a merging taper except in low-speed urban areas
Image: ATSSA
Notes: Key Message: Discuss where not to use barriers
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Do not use barriers to form tapers, unless the speed is low. Use flexible, lightweight devices instead to form a taper and a buffer.
Suggested Questions: Would that be a forgiving design? No.
Additional Information: Photo is from Columbia, SC by J Morales
Possible Problems: None

## Slide 155: Delineation of Temporary Traffic Barriers
If used for channelization, they shall delineated
  Spacing shall match device spacing
  Color shall match the applicable pavement marking color
    Right = White
    Left = Yellow
Image: ATSSA
Notes: Key Message: Discuss barrier delineation
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
  Suggested Comments: Remember that channelization is a secondary consideration. When serving that purpose, delineation devices are required. These vary by State. They may be Type C warning lights or reflectors.
Suggested Questions: Why? To make it visible!
Additional Information: None
Possible Problems: None

## Slide 156
Examples of Barrier Delineation
Image: ATSSA
Notes: Key Message: Illustrate barrier delineation
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This illustrates the use of delineators to delineate a tangent section of a barrier wall.
Suggested Questions: What is the distance
Additional Information: Photo taken at Dulles Toll Road, Virginia, by J. Morales. The distance from the edgeline the barrier is called the “shy distance”. The shy distance is the distance from the edge of the traveled way, on the right hand side, within which a roadside object will be perceived as an immediate hazard by the typical driver to the extent that the driver will change the vehicle’s placement or speed.
Possible Problems: State preference.

## Slide 157: Examples of Barrier Delineation
Varies by State
Image: Maryland DOT
Notes: Key Message: Discuss barrier delineation
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
  Suggested Comments: When the barrier serves its secondary function of channelization, it shall be delineated with either reflectors (delineators) or Type C warning lights. This is a state preference.
Suggested Questions: What’ the disadvantage of using Type C lights? Someone has to get out there to replace batteries
Additional Information: Source: Maryland standards.
Possible Problems: The 96-ft spacing (top left) applies in Maryland. May vary in other states.

## Slide 158
Lane Closure with Temporary Traffic Barrier
197
Image: FHWA
Notes: Key Message: Discuss lane closure with barrier
Est. Presentation Time: 5 minute(s)
Explanation of Cues/Builds: Text box appear upon click
  Suggested Comments: Notice how the taper and buffer are formed with lightweight devices, like drums. The barrier is used for protection and secondarily for delineation of the work space. Notice the buffer space. Also notice that the blunt end of the barrier is protected by a “flare” which will discuss in a moment. The angle of that flare has to be precise so it has redirective properties. Notice the forgiving design that allows an errant drive to run through the taper and recover before being redirected by the barrier.
Suggested Questions: Is the taper formed with the barrier? No.
Additional Information: None
Possible Problems: The flare shown is misleading since it shows a 1:1 flare (45 degrees). The right flare in a freeway environment is more like 20:1

## Slide 159
Do Not Form Tapers with Barriers!
Impacts!
Image: ATSSA
Notes: US 50 WB, near Chantilly, VA by J. Morales

## Slide 160
Should be parallel to traffic
Image: ATSSA
Notes: Key Message: Illustrate protection of the blunt end
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
  Suggested Comments: This photo illustrates the concepts we just learned.
Suggested Questions: What’s wrong with this? The impact attenuator should be parallel to the travel lane.
Additional Information: Photo taken in Woodbridge, VA, by J. Morales
Possible Problems: None

## Slide 161
Example of Proper Flare and
Blunt End Shielding
Image: ATSSA
Notes: I-95 North, near Quantico, VA, by J Morales

## Slide 162: The Blunt End of a Barrier is a Hazard!
Shield with:
  Flare and/or
  Crash cushion
  Bury into the cut slope
“All upstream leading ends that are present shall be appropriately flared or protected with properly installed and maintained crashworthy cushions.”
Image: FHWA
Notes: Key Message: Discuss protection of the blunt end
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The blunt (exposed) end of the barrier is a hazard and must be protected. There are two ways to protect it: providing a flare and/or providing a crash cushion.
Suggested Questions: None
Additional Information: Photo taken during a crash test.
Possible Problems: None

## Slide 163: The Blunt End of a Barrier is a Hazard!
Blunt end!
Image: ATSSA
Notes: Key Message: Discuss protection of the blunt end
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Notice how the blunt (exposed) end of the barrier is exposed. This is a hazard within the clear zone.
Suggested Questions: None
Additional Information: Photo is from Vienna, Virginia, ramp to Dulles Toll Road, by J. Morales.
Possible Problems: Technically, this is a low speed situation, so depending on the state, this blunt end may actually be outside the clear zone. No need to discuss this but someone may bring it up. Be prepared to discuss.

## Slide 164: Barrier Flare Ratio
Not parallel to the edge of the traveled way
  Angled
Depends on speed
  Typically 16:1 to 20:1 flare for freeways
1
20
“Break point”
(“flare-tangent” point) is considered a hazard
Image: FHWA
Notes: Key Message: Discuss use of flare for protection of the blunt end
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: Text box appears on click
  Suggested Comments: The flare angle depends on speed. Refer to the Roadside Design Guide or consult your local agency for specific information. Typically it is 16:1 to 20:1 (“20 to 1”) flare for freeways. For example, for every foot moved laterally, we move 30 feet longitudinally. This is a precise angle with redirective properties.
Suggested Questions: What does 20 to 1 mean?
Additional Information: None
Possible Problems: The picture shown is a detail of TA 34, page 701. Indicate that the flare shown in this picture is more like 1:1 (45 degrees) and is very misleading. A 20:1 flare is much more gradual (see next slide). Note: The flare might have a different name depending on the State. For example, in Virginia, it is called the “slope ratio”.

## Slide 165
Design Speed (mph) | Flare Rate
70 | 20:1
60 | 18:1
55 | 16:1
50 | 14:1
45 | 12:1
40 | 10:1
30 | 8:1
Source: 2011 Roadside Design Guide
Typical Flare Rates (May vary by State)
Notes: Key Message: Discuss typical flare rates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This table shows some typical flare rates for rigid concrete barriers. Remember that these rates may vary by State.
Suggested Questions: What does 20 to 1 mean?
Additional Information: These are MAXIMUM flare rates for RIGID barriers inside the shy line. RDG Page 5-48. Flare rate is the rate at which a barrier moves from a larger offset to a closer offset from the edge of traveled way. Although it is desirable to flare the barrier system as quickly as possible, there are two criteria that must be satisfied for the barrier exposed to approaching traffic. First, in order to keep the angle of impact with the barrier from being too severe, the flare rate is limited to the values shown on the table, which are based on speed and type of the barrier system. Second, a concrete barrier should only be flared if it can be done on 10:1 or flatter For one directional roadways, the downstream flare rate, as the barrier moves away from the traveled way, should not be sharper than 2:1.
Possible Problems: May vary by State.

## Slide 166: What does 20:1 mean?
A “ratio”
  For every foot moved laterally, 20 feet longitudinally
Quite “shallow” to provide redirection
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Image: ATSSA
Notes: Key Message: Discuss use of flare for protection of the blunt end
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Black line appears on click
  Suggested Comments: Self explanatory
Suggested Questions: What does 20 to 1 mean?
Additional Information: Photo is from Virginia, by J. Morales.
Possible Problems: None

## Slide 167: How long is the flare?
Extend the flare until the exposed end is outside of the clear zone
If the end is still within the clear zone, an end treatment shall be provided
30’
Remember: No hazards in the clear zone!
Image: FHWA
Notes: Key Message: Discuss use of flare for protection of the blunt end
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: For an impact attenuator not to be required, the end of the barrier must be outside the clear zone, which typically is 30 feet measured from the edge of the travel lane.
Suggested Questions: Where is the edge of the travel lane? The white line!
Additional Information: None
Possible Problems: Clear zone widths and flare rates are state-specific. In some states, like Virginia, the flare may be called something else, like “slope” or “offset”.

## Slide 168: The Clear Zone
An unobstructed relatively flat area
Impacted by construction
Extends outward from the edge of the traveled way
Allows a driver to recover
A “FORGIVING DESIGN”
Image: ATSSA
Notes: Key Message: Define the clear zone
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: A clear zone is an unobstructed, traversable roadside area designed to enable a driver to stop safely or regain control of a vehicle that has accidentally left the roadway. Clear zones are an effective strategy for prevention and mitigation of roadway departure crashes. The clear zone provides recovery: a forgiving design.
Suggested Questions: How wide is the clear zone? What is relatively flat? No “non-recoverable” slopes, defined as steeper than 4H:1V.
Additional Information: Photo source unknown: See Definition 33, Page 12: Clear Zone—the total roadside border area, starting at the edge of the traveled way, that is available for an errant driver to stop or regain control of a vehicle. This area might consist of a shoulder, a recoverable slope, and/or a non-recoverable, traversable slope with a clear run-out area at its toe. The AASHTO Roadside Design Guide defines a clear zone as the total roadside border area, starting at the edge of the traveled way, available for safe use by errant vehicles. This area may consist of a shoulder, a recoverable slope, a non-recoverable slope, and/or a clear run-out area. A recoverable slope is a slope on which a motorist may, to a greater or lesser extent, retain or regain control of a vehicle by slowing or stopping. Slopes flatter than 1V:4H are generally recoverable. A non recoverable slope is a traversable slope on which an errant vehicle will continue to the bottom. Embankment slopes between 1V:3H and 1V:4H may be considered traversable but non-recoverable if they are smooth and free of fixed objects. A clear run-out area is the area at the toe of a non-recoverable slope available for safe use by errant vehicles. Slopes steeper than 1V:3H are not considered traversable and are not considered part of the clear zone.
Possible Problems: None
.

## Slide 169: The Clear Zone
Requirements vary by State!
Image: ATSSA
Notes: Key Message: Define the clear zone
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The CZ is measured from the edge of the traveled way.
Suggested Questions: How wide is the clear zone?
Additional Information: A clear zone is the total roadside border area, starting at the edge of the travel lane, available for safe use by errant vehicles. This area may consist of a shoulder, a recoverable slope, and/or a traversable but non-recoverable slope and a clear runout area. (A “recoverable” fill slope is defined as no steeper than 4:1; a “traversable but non-recoverable” slope is steeper than 4:1 but no steeper than 3:1 (a “critical” slope is steeper than 3:1 and considered an obstacle); cut slopes as steep as 3:1 are considered
recoverable). The desirable clear zone width, from a roadside safety standpoint, is as wide as cost effectively possible. However, some practical value needs to be established for design purposes. Design clear zone values have been determined and are dependent upon traffic speeds and the roadside geometry.
Possible Problems: None
.

## Slide 170
10-170
The Clear Zone
Edge of traveled way
No hazards in CZ
(non-working hours)
Crashworthy TCDs may be in the CZ
CZ
Image: ATSSA
Notes: Key Message: Illustrate the clear zone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: text bubbles appear on clicks
  Suggested Comments: This photo shows a good clear zone. Of course, if the work zone is active, equipment can be inside the CZ. The concept of the clear zone applies mostly to non-active work zones.
Suggested Questions: Where is the edge of the traveled way? The edgeline!
Additional Information: Photo: I-4, Florida, by J. Morales
Possible Problems: None

## Slide 171: Example of Clear Zone Widths for Work Zones
Speed (mph) | Width (ft.)
60 or greater | 30
45-55 | 20
40 | 15
30-40 | 14
Source: 2011 Roadside Design Guide
Requirements vary by State!
Notes: Key Message: Discuss clear zone width
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This table shows examples of CZ widths. Notice that the higher the speed, the wider the CZ. Remember that the CZ width may vary by State.
Suggested Questions: How wide is the clear zone?
Additional Information: The 2011 AASHTO Roadside Design Guide (page 9-2) provides guidance to help highway agencies develop consistent design approaches for determining the widths of clear zones along roadways based on speed, traffic volume, roadside slope and curvature. This publication recommends clear zone ranges based on a width of 30 to 32 feet for flat, level terrain adjacent to a straight section of a 60 mph highway with an average daily traffic of 6,000 vehicles. For steeper slopes on a 70 mph roadway the clear zone range increases to 38 to 46 feet, and on a low speed, low volume roadway the clear zone range drops to 7 to 10 feet. For horizontal curves the clear zone can be increased by up to 50 percent from these figures. Another AASHTO publication, A Policy on Geometric Design of Highways and Streets (Green Book), recommends a 10-foot minimum clear zone on collectors without curbs, low-speed rural collectors, and rural local roads. For local roads and streets, a minimum clear zone of 7 to 10 feet is considered desirable on sections without curb.
Possible Problems: These numbers are examples, specific to one State. Check you local standards. These specific numbers are from Florida. NOTE: RDG indicates that the presence of a curb does not affect the clear zone width.

## Slide 172: No hazards in the clear zone?
Image: ATSSA
Notes: Key Message: Illustrate the clear zone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This photo illustrates a hazard within the clear zone. This is an unacceptable practice!
Suggested Questions: Is this a hazard in the clear zone? Yes!
Additional Information: Photo believed to be Florida.
Possible Problems: None

## Slide 173: Barriers Connections
Barriers segments shall be connected
Connection types*
  Channel connections
  Others
*Preferred connections vary by State!
Image: AASHTO
Notes: Key Message: Discuss barrier connections
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Barriers should be connected to be effective. There are different types of connections.
Suggested Questions: Are all connections the same? What makes a good connection? What would happen if the barriers are not connected. We would have multiple exposed ends!
Additional Information: Short intermittent segments of temporary traffic barrier shall not be used because they nullify the containment and redirective capabilities of the temporary traffic barrier, increase the potential for serious injury both to vehicle occupants and pedestrians, and encourage the presence of blunt, leading ends.
The typical pin and loop design that has been in use for years needs to be beefed up in order to meet current crash test criteria. Failures of pin and loop designs have been caused by thin pins pulling out of the loops, loops breaking, or concrete fracturing due to lack of reinforcement. There are nearly a dozen successfully crash tested designs of portable concrete barriers, and they are posted on FHWA’s web site. As of October 1, 2002, all temporary barriers must have a connection that transfers tension and moment.
Possible Problems: None.

## Slide 174
Shall not be used because they
  Nullify the containment and redirective capabilities
  Increase the potential for serious injury
  Result in more blunt ends
Short Intermittent Segments Of Temporary Traffic Barriers
http://atdetroit.net/forum/messages/107211/116609.jpg
Notes: Key Message: Discuss barrier connections
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Barriers should be connected to be effective. There are different types of connections.
Suggested Questions: Are all connections the same? What makes a good connection? What would happen if the barriers are not connected. We would have multiple exposed ends!
Additional Information: Short intermittent segments of temporary traffic barrier shall not be used because they nullify the containment and redirective capabilities of the temporary traffic barrier, increase the potential for serious injury both to vehicle occupants and pedestrians, and encourage the presence of blunt, leading ends.
Possible Problems: None.

## Slide 175
Image: ATSSA
Notes: Key Message: Illustrate barrier connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Barriers should be connected to be effective. Notice that these barriers are not connected.
Suggested Questions: What would happen if the barriers are not connected? We would have multiple exposed ends!
Additional Information: None.
Possible Problems: None.

## Slide 176
Image: ATSSA
Notes: Key Message: Illustrate barrier connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is another example of an improper use of barriers.
Suggested Questions: Which device is more appropriate here? Type 3 barricades!
Additional Information: Photo source: John Mceahern
Possible Problems: None.

## Slide 177
Image: Utah DOT
Notes: Key Message: Illustrate barrier connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is another example of an improper use of barriers.
Suggested Questions: Which device is more appropriate here? Perhaps drums since there is no hazard.
Additional Information: Photo from Utah DOT
Possible Problems: None.

## Slide 178: Pin and Loop Connection
Allows for flaring
Some may not be crashworthy
Check the state’s approved product list
Image: ATSSA
Notes: Key Message: Illustrate pin/loop barrier connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The pin and loop is an effective barrier connection mechanism. The pin, however may fly off when the barrier is struck. This connection did not pass the crash test and may be phased out. Failures of pin and loop designs have been caused by thin pins pulling out of the loops, loops breaking, or concrete fracturing due to lack of reinforcement. There are nearly a dozen successfully crash tested designs of portable concrete barriers, and they are posted on the FHWA web site.
Suggested Questions: What would happen if the barrier is impacted? The pin may fly off becoming a projectile.
Additional Information: Info from FHWA Nich Artimovich: The simple pin-and-loop (two loops at either end of the barrier segment) did not pass crash testing under NCHRP Report 350 – the pin deforms too much, allowing the barrier to separate and deflect so much that the test vehicle rolls over. We have, however, allowed barriers of this common design to remain in use until the end of their service life. The generic solution so the pin-and-loop is to use two loops at the top and one at the bottom of the barrier, with the opposite arrangement on the other end of the segment – in each case the single loop goes between the pair of loops on the other barrier. This spreads the forces out on the pin so that it does not deform nearly as much, and the barrier resists deformation much better.
Nicholas Artimovich, II, Highway Engineer, Office of Safety Design. Federal Highway Administration HSSD, email: nick.artimovich@dot.gov, phone: 202-366-1331. web: http://safety.fhwa.dot.gov
FHWA web page: The typical pin and loop design that has been in use for years needs to be beefed up in order to meet current crash test criteria. Failures of pin and loop designs have been caused by thin pins pulling out of the loops, loops breaking, or concrete fracturing due to lack of reinforcement. There are nearly a dozen successfully crash tested designs of portable concrete barriers,
Possible Problems: This refers to NCHRP Report 350 requirements.

## Slide 179: Channel Connections
No moving parts
Various (proprietary) types:
  J-J Hook
  T-Lok
  Others
http://www.jjhooks.com/
Notes: Key Message: Discuss channel connections
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is a better connection, a channel connection (J-J hook, which is a proprietary name). There are no projectiles to fly off. It also allows for the flare. This design passed the crash test. It allow no loss of structural integrity due to bent or missing hardware. State and Federal transportation officials require “positive connection barriers” for increased safety.
Suggested Questions: None
Additional Information: Photo from www.jjhooks.com.
Possible Problems: J-J Hook is a proprietary term. NCHRP 350 Level 3 compliant. The Federal Highway Administration memorandum regarding guidelines for application of the Roadside Design Guide requires states to use only crash tested barriers that have been tested and classified as operational on Federal-aid projects.

## Slide 180: J-J Hook
J-J Hook
(Proprietary)
http://www.jjhooks.com/
Notes: Key Message: Discuss channel connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the J-J hook.. There are no projectiles to fly off. It also allows for the flare. This design passed the crash test. It allow no loss of structural integrity due to bent or missing hardware.
Suggested Questions: None
Additional Information: Please go to FHWA’s web site http://safety.fhwa.dot.gov/roadway_dept/policy_guide/road_hardware/barriers
and use the Search by Keyword feature, highlighting “Temporary Concrete Barriers/Steel Barriers” and you will find all portable barrier systems that are acceptable for use.
Possible Problems: J-J Hook is a proprietary term. NCHRP 350 Level 3 compliant. The Federal Highway Administration memorandum regarding guidelines for application of the Roadside Design Guide requires states to use only crash tested barriers that have been tested and classified as operational on Federal-aid projects.

## Slide 181
Two identical steel J-shaped hooks
Cast into the barrier
Create a continuous steel connection
J-J Hook
(Proprietary)
http://www.jjhooks.com/
Notes: Key Message: Discuss J-J Hook connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The J-J Hooks connection consists of two identical steel J-shaped hooks, which are cast into the barrier, creating a continuous steel connection. To attach the barrier ends, one barrier is lowered vertically next to an adjacent barrier. With minimal guidance, the self aligning connection automatically “hooks” into place. Workers don’t need to endanger their hands by having them in between barriers during the connection process. Lost or stolen hardware issues are eliminated because of the integrated barrier connection. J-J Hooks barrier provide a continuous positive shear connection throughout the barrier system. As the J-J Hooks are identical, there are no left or right pieces, simplifying the installation process. Due to vertical lift, one barrier can be removed without disturbing adjacent barriers.
Suggested Questions: None
Additional Information: Please go to FHWA’s web site http://safety.fhwa.dot.gov/roadway_dept/policy_guide/road_hardware/barriers
and use the Search by Keyword feature, highlighting “Temporary Concrete Barriers/Steel Barriers” and you will find all portable barrier systems that are acceptable for use. Source: http://www.jjhooks.com/connection.shtml
Possible Problems: J-J Hook is a proprietary term. NCHRP 350 Level 3 compliant. The Federal Highway Administration memorandum regarding guidelines for application of the Roadside Design Guide requires states to use only crash tested barriers that have been tested and classified as operational on Federal-aid projects.

## Slide 182
Positive connection
T-Lok
(Proprietary)
https://www.t-lok.com/
Notes: Key Message: Discuss T-Lok connection
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: T-Lok™ Barriers, with their patented locking ends, are on construction sites throughout the mid-Atlantic region. In addition, they are being used as security barriers at the U.S. Capitol Building in Washington, DC. FHWA Approved. The T-Lok Barrier has been crash tested to NCHRP 350 as a Test Level 3 62 mph] redirective longitudinal barrier.
Suggested Questions: None
Additional Information: It is also approved for use on state projects in: Maryland, Virginia, West Virginia, District of Columbia. The minimum length of a T-Lok Barrier installation
should be 48m. The ends of each section are constructed with unique T & C Connection design that interlocks all segments together. The sections can swivel up to seven degrees at the connection for easy positioning around work areas or following road contours. T-Lok™Barrier Sizes: 12-foot length, 5,400 pounds; 18-foot length, 8,100 pounds
Possible Problems: None

## Slide 183: Other Positive Protection Devices:
Crash cushions
Shadow vehicles (w/TMA)
Vehicle arresting systems
Image: Washington State DOT
Image: Impact Absorption
Notes: 183
Key Message: Discuss types of positive protection devices
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: Here are two additional types of positive protection features that are acceptable for use. We group the devices mentioned on the previous slide together as they are all types of barriers.
Suggested Questions: None
Additional Information: Refer to AASHTO Roadside Design Guide for additional information.
Possible Problems: None

## Slide 184: Crash Cushions
Also called “impact attenuators”
Absorb the energy of the impact
To attenuate = to weaken or reduce in force, intensity, effect,…
Image: ATSSA
Notes: Key Message: Discuss crash cushions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
  Suggested Comments: They are designed to absorb the energy of an impact.
Suggested Questions: What does attenuate mean?
Additional Information: None
Possible Problems: Crash cushions is the term used in the MUTCD, section 6F.82.

## Slide 185: Crash Cushions
Protect motorists from:
  Blunt ends of barriers
  Fixed objects
  Shadow vehicles
  Dropoffs
  Other hazards
Images: FHWA
Notes: Key Message: Discuss crash cushions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Crash cushions can be effective in preventing fatalities. These her some of their uses.
Suggested Questions: What is a “shadow vehicle”? A vehicle that follows the workers for their protection. What is a dropoff? A sudden drop in elevation parallel to traffic.
Additional Information: None
Possible Problems: Crash cushions is the term used in the MUTCD, section 6F.82.

## Slide 186: Crash Cushions Shall be:
Crashworthy
Designed for the specific application intended
Periodically inspected
Promptly repaired or replaced
Image: ATSSA
Notes: Key Message: Discuss crash cushions
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Use the proper device for the conditions at hand. These conditions include speed of vehicles and their weight. Verify that the device has been crash tested and approved for the application.
Suggested Questions: None
Additional Information: MUTCD Section 6F.82. Photo courtesy of Mack Braxton
Possible Problems: None

## Slide 187: Types of Crash Cushions
Redirective
  Redirects the errant vehicle
Non-Redirective
  Decelerates the errant vehicle
Images: ATSSA
Notes: Key Message: Discuss types of crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Each text box appears upon click
  Suggested Comments: Two types of crash cushions: redirective and non-redirective. Redirective crash cushions may no decelerate the impacting vehicle but rather redirect the vehicle back to the highway. Non-redirective one actually decelerate the vehicle to a stop, hence called “inertial”.
Suggested Questions: What’s inside these barrels? Sand! Not water.
Additional Information: AASHTO’s Roadside Design Guide contains additional information on the use of crash cushions. Energite III and Quadguard CZ Sand barrel attenuators are initially low-cost but they need nearly total replacement after a hit. More sophisticated attenuators like the Quadguard CZ are quite expensive, but can be restored quickly and cheaply, sometimes without the need to replace any parts at all.
Possible Problems: None

## Slide 188
TAU-II
(Proprietary)
Image: ATSSA
Notes: Key Message: Discuss redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This an example of a redirective crash cushion. They mostly look like guardrails, with similar redirective properties. Redirective cushions, like the TAU-II, “redirect” the impacting vehicle, similar to a guardrail. Notice the crushable modules. They are more expensive that inertial systems but can be reused. Some examples follow:
Suggested Questions: None
Additional Information: Photo in Kissimmee, FL, by J. Morales. The Universal TAU-II Family of Crash Cushions are a full line of re-directive crash cushions that meet both TL-2 and TL-3 NCHRP 350 requirements.
A fully re-directive system, the TAU-II Crash cushions are ideally suited for ends of rigid barriers, toll booths, utility polls, high speed roads with narrow medians, and many other roadway hazards. The TAU-II system's open architecture reduces build-up coming from roadside debris. This helps keep the system clear of litter and ensure top performance and easy access for maintenance workers.
Low Life Cycle Cost and minimum number of anchors
Low Profile 6" foundation ideal for bridge deck
Can be used for 27.5" or 36" backups
One parts kit repairs or builds any size unit
Easily lengthened or shortened
Standard transitions and reusable nose standard
70mph system available
The marker on the nose is a Type I object marker, aka a “9-button” marker”.
Possible Problems: Someone may say that if they are redirective and no not decelerate, then they are not “cushions”. This is a great point that comes up frequently. Attenuators may be a better term.

## Slide 189: React 350
(Proprietary)
http://www.tapconet.com/
Image: ATSSA
Image: ATSSA
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the REACT 350. The REACT 350 self-restores up to 100% of its attenuation capacity after a typical design impact and remains in service protecting a hazard. During head-on impacts, the REACT 350 crushes the reusable cylinders to absorb the energy of impact
Suggested Questions: None
Additional Information: Proprietary to Energy Absorption Systems. The system meets NCHRP 350 TL 2 or 3 and is 90% self-restoring after design impacts, keeping the hazard protected even after an impact occurs. It helps reduce liability in the event of secondary impacts.
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 190: QuadGuard
(Proprietary)
Images: Energy Absorption Systems
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the QuadGuard. When impacted from the side, the QuadGuard® System redirects the errant vehicle back toward its original travel path without allowing gating.
Suggested Questions: None
Additional Information: Proprietary to Energy Absorption Systems. The QuadGuard CZ is an innovative, new portable crash cushion for work zones. It consists of crushable, energy-absorbing cartridges surrounded by a framework of Energy Absorption’s exclusive steel Quad-Beam™ boards. The QuadGuard CZ meets all of today’s strict crash cushion performance requirements as mandated by NCHRP 350, Test Level 3, and provides the same lifesaving efficiency and features of the permanent QuadGuard System, in a compact, portable unit.
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 191: Advance Dynamic Impact Extension Module (ADIEM)
Lightweight crushable concrete modules
(Proprietary)
Images: Valtir
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the ADIEM. Looks very imposing since it appears to be made of concrete. The Advanced Dynamic Impact Extension Module (ADIEM™) utilizes lightweight crushable concrete modules which provide an affordable energy-absorbing system, which crush upon impact. Composed of three component groups; reinforced concrete base, engineered lightweight concrete modules, and anchor brackets.
Suggested Questions: None
Additional Information: Proprietary of Trinity Highway Products. The ADIEM II system is composed of two main parts: a wedge-shaped base and ten crushable concrete modules (see Figure 2.3). The base, fabricated using a conventional concrete mix design, is held in-place by twelve 25 mm x 60 mm steel pins which are driven though the base into the asphalt or gravel. A side pipe rail is cast on the base at automobile wheel-hub height to help redirect side impacts. Features: No site-specific foundation pad needed. Can be placed on existing surfaces such as concrete, asphalt or compacted soil/base material. Composed of three component groups; reinforced concrete base, engineered lightweight concrete modules, and anchor brackets. Re-directive capability. (Beginning Length of Need at 15’ (4.6 m) from nose.) NCHRP Report 350 Test Level 3 compliant. Installation and Repair Advantages: Pinned anchorage allows unit to be moved and relocated quickly. All ten lightweight modules are common in design and composition, requiring no sequence priority when attaching or replacing damaged modules. Impact damage to the product is typically confined to the modules making repair a simple process. Contains no torque-sensitive bolts. No concrete to pour.
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 192: ADIEM
Image: ATSSA
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the ADIEM. It was developed by the Texas Transportation Institute as a low cost option. It utilizes lightly reinforced, ultra-low-strength Perlite concrete modules on an inclined concrete base, locked together to act as a unit. Because the Perlite concrete is susceptible to moisture, the blocks are coated with a protective covering. The modules are designed to crush upon impact, absorbing kinetic energy so the vehicle can make a controlled stop. If damaged, the modules can be slid out and replaced with new ones.
Suggested Questions: None
Additional Information: Photo taken at the Dulles Toll Road, in Reston, VA, by Juan Morales. The cable seen on the bottom right is not part of the system. It is from a cable barrier system nearby.
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 193: ADIEM
Images: ATSSA
Notes: Key Message: Show ADIEM
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the ADIEM. These modules are covered with plastic.
Suggested Questions: None
Additional Information: Photos taken at Fairfax County Parkway, VA, by J. Morales.
Possible Problems: Shown for educational purposes only.

## Slide 194
Image: Virginia DOT
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: Here you see an impact on an ADIEM terminal.
Suggested Questions: None
Additional Information: Photo is from Virginia (donated by student)
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 195: Trinity Attenuating Crash Cushion (TRACC)
(Proprietary)
Images: Valtir
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: This is the TRACC (Trinity Attenuating Crash Cushion). The Trinity Attenuating Crash Cushions™ (TRACC™ Family) feature a complete line of fully re-directive, non-gating crash cushions that are available in a variety of lengths for a variety of highway speeds. No cartridges or black boxes.
Suggested Questions: None
Additional Information: Photos are from manufacturer’s webpage
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 196: Non-redirective Energy Absorbing Terminal (NEAT) System
(Proprietary)
Images: Valtir
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Also, non-redirective:
NEAT = Non-redirective Energy Absorbing Terminal
The N.E.A.T. is a NCHRP 350, Test Level 2 (45 M.P.H.) attenuator designed specifically to be attached to portable concrete barriers. The N.E.A.T. Systems cartridge is lightweight, weighing less than 300 lbs. It is compact, as well, measuring less than 10 feet in length. The system can be installed quickly, in about 15 minutes, without the use of any special tools or heavy equipment.
Suggested Questions: None
Additional Information: Photos are from manufacturer’s webpage
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 197
Water-filled
Non-redirective
Gating
ABSORB 350
(Proprietary)
Images: Lindsay
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Absorb 350 Crash Cushion is a non-redirective crash cushion that is NCHRP 350 approved for TL-2 and TL-3 applications.
Suggested Questions: None
Additional Information: Product Features:
Narrow Footprint
Fast deployment and repair
No foundation anchors required
Construction or Permanent Applications
Speed Rating Flexibility
Optional wheel lifting device available for movement to new lane position or side of the road
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 198
Gating vs. Non-Gating
Non-Gating | Gating
Vehicle is redirected | Vehicle passes through (gates)
Images: Lindsay
Notes: So what is non-gating and gating? Gating is term used to describe an attenuator that is designed to allow an errant vehicle to enter a clear zone where it can safely decelerate before coming into contact with a hazard. NCHRP Test 33 and 32 above are gating tests.
When the vehicle comes in contact with the attenuator, the attenuator folds away (or gates) to allow the vehicle to safely pass. Gating attenuators are more economical than non-gating so if there is enough clear zone you should be using attenuators of the gating variety.
Non-gating attenuators as you can imagine, do not allow the vehicle to pass though when impacted at the front to of the system. True or false, a clear zone is not needed when a Non-Gating crash cushion is installed. FALSE. A clear zone is still needed, It is just smaller. Your high school physics teacher will be able to tell you that when a vehicle comes into contact with an attenuator at 15 degrees at a high speed the vehicle will most likely pass behind the system. A non-gating crash cushion can’t stop this from happening, but it can slow the vehicle. Non-gating attenuators are normally used in medians and on the side of the road when a full clear zone can not be achieved

## Slide 199
ABSORB 350
(Proprietary)
Images: Lindsay
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Absorb 350 can be attached to the end of portable or permanent concrete barriers and steel barriers without the need to anchor the system to the roadway. This provides for easy and fast installation and repair . The system is 24 inches wide, making it the ideal option for narrower roads where workspace and road space are limited.
It is designed for use on narrow hazards, exits, wide medians, edge of road locations.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 200
Redirective, non-gating, bidirectional
Smart Cushion
(Proprietary)
Image: Hill and Smith
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The SCI100GM is a fully redirective, non-gating, bidirectional Impact Attenuator. It was designed for safety and reusability. All required NCHRP 350 tests were performed with the same unit with no required replacement parts. Safety comes first with the SCI100GM as it provides lower average ridedown G forces due to the fact that it is a speed dependent system instead of fixed force. It requires minimal spare parts inventories due to the new side panel design which minimizes damage and snag potential on side impacts. During our testing, it produced very low angles of exit which reduces the potential of the vehicle rebounding back into traffic. Quick resetting due to minimal damage reduces worker exposure, repair part costs and repair labor costs.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 201
Smart Cushion
(Proprietary)
Image: ATSSA
Notes: Key Message: Show examples of redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The SMART CUSHION ® impact attenuators are manufactured by SCI Products, Inc./Work Area Protection Corp. They are NCHRP Report 350, Test Levels 2 and 3 (TL2 and TL3) compliant (Models SCI 70 GM and SCI 100 GM, respectively) and are fully redirective, non-gating, and bi-directional. SMART CUSHION ® impact attenuators are used to help protect motorists from hazards in both permanent and work zone locations. They can be attached to most types of median and roadside barriers.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 202: Non- Redirective Crash Cushions
Sand-Filled Barrels = “Inertial”
Image: TrafFix
Notes: Key Message: Show examples of non-redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This system consists of a group of freestanding plastic barrels configured in increasing weights from the impact point toward the object. Such an array transfers the vehicle’s momentum to the increasing masses of sand in the barrels and provides a gradual deceleration. Each barrel is designed with a specific weight of sand to absorb the energy of an errant vehicle. Non-redirective crash cushions are called “inertial” since they decelerate rather than redirect vehicles. System array breaks up during impact and momentum transfer slows the vehicle. Non-redirective cushions completely absorb the energy of the impact, without redirecting the impacting vehicle. They require more precision in terms of the array, amount of sand and location of the sand within the barrel. They are not reusable. Damaged parts need to be replaced after impact.
Suggested Questions: None
Additional Information: Some meet the criteria for non-redirective crash cushions when placed in appropriately designed arrays. Example: Each module in the array consists of a one piece barrel, a lid and, in some modules, a cone insert. The cone insert is used to adjust the sand height or center of mass and the overall weight of the barrel. The barrel’s weight requirement is determined by its place in the array. Some inertial systems meet NCHRP 350, Test Level 3 criteria for non-redirective crash cushions when placed in appropriately designed arrays. Inertial systems are non-redirective, easy to install crash cushion consisting of a number of sand-filled, polyethylene plastic modules that are installed in a specific geometric array in front of a hazard. These are the same barrels used by State D.O.T.s in permanent applications on many State roadways. These barrels are completely modular and can be configured for any speed limit. Because Barrels can be easily relocated on the job site during different phases of work. Barrels can be rented with or without sand.
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 203
Big-Sandy
(Proprietary)
Images: TrafFix
Notes: Key Message: Show examples of non-redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The TrafFix Devices "Big Sandy" is an Impact Attenuator Sand Barrel that is easy to move and provides external verification of the barrels correct weight of sand. This Impact Attenuator/Crash Cushion Sand Barrel has been tested and certified to meet the crash worthy requirements of NCHRP 350. "Big Sandy" Sand Barrels go above and beyond these requirement to provide the best in highway safety. Different barrel configurations are used to create all of the weights used in current standard array geometries (200, 400, 700, 1400, and 2100 lbs). Reinforced lip prevents barrels from deforming when filled and provides a quick and secure fit of blow molded lid. All three barrels shoulder allows for easy moving, lifting and emptying with TrafFix optional lifting ring
Suggested Questions: None
Additional Information:
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 204
Example of Barrel Array
Image: Florida DOT
Notes: Key Message: Show examples of non-redirective crash cushions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The configuration of barrels is critical to their effectiveness and performance. Follow the manufacturer’s instructions. The number you see refer to the weight of sand in each barrel (This picture is form the Florida Design Standards).
Suggested Questions: What are these numbers?
Additional Information: Some meet the criteria for non-redirective crash cushions when placed in appropriately designed arrays.
Possible Problems: Their use is state-specific. Shown for educational purposes only. Discuss in general terms.

## Slide 205
Examples of
Barrel Arrays
Images: New Mexico DOT
Notes: Key Message: Show examples of barrel array
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This shows an example of a barrel array. Various arrays are
Suggested Questions: None
Additional Information: Some meet the criteria for non-redirective crash cushions when placed in appropriately designed arrays.
Possible Problems: Their use is state-specific. Source: New Mexico DOT.

## Slide 206: Example of Sand Placement
= sand
= spacer
YES
NO
Image: ATSSA
Notes: Key Message: Show importance of sand placement
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: “NO” arrow appears upon click. Bottom figure appear upon click.
Suggested Comments: This shows the proper placement of the sand. Always follow the manufacture’s instructions. The sand goes toward the center so it works telescopically. We use spacers for that.
Suggested Questions: What would happen if we place the sand at the bottom of the barrel (top figure). We would create a ramp!
Additional Information: None
Possible Problems: Their use is state-specific.

## Slide 207: Inspecting Sand-Filled Barrels
Overlap the fixed object on the traffic side by a minimum of 30 inches
Traffic
30”
Images: ATSSA
Notes: Key Message: Discuss barrel overlap
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. A minimum overlap of 30 inches is required to properly protect hazards.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific.

## Slide 208: C. Truck-Mounted Attenuators (TMAs)
Energy-absorbing devices attached to the rear of shadow trailers or trucks
The insides of a TMA
Image: Virginia DOT
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Truck-mounted attenuators shall be energy-absorbing devices attached to the rear of shadow trailers or trucks. If used, the shadow vehicle with the attenuator shall be located in advance of the work area, workers, or equipment to reduce the severity of rear-end crashes from errant vehicles. TMA are useful to protect workers during moving operations. Notice the crushable modules inside to reduce the severity of the crash.
Suggested Questions: None
Additional Information: None.
Possible Problems: Their use is state-specific.

## Slide 209
Image: Virginia DOT
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TMAs save lives!
Suggested Questions: None
Additional Information: Photo is from Virginia, Dulles Toll Road.
Possible Problems: May be required by the state.

## Slide 210: Truck-Mounted Attenuators
Weight of the truck: protects the crew or hazard from being struck!
Crash cushion: protects anyone that strikes the truck!
Image: Virginia DOT
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: Which arrow board mode is this? Caution mode.
Additional Information: Photo from Virginia DOT, which uses black and orange (not yellow) stripes.
Possible Problems: Their use is state-specific.

## Slide 211
(Proprietary)
  Truck-Mounted (TMA)
Categories of Truck-Mounted Attenuators
  Trailer-Mounted (TTMA)
Images: ATSSA
Notes: Key Message: Provide examples of TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are various types available, each with unique properties.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 212
(Proprietary)
Image: TrafFix
Notes: Key Message: Provide examples of TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are various types available, each with unique properties. This is the Scorpion. The Scorpion consists of strut and cartridge sections that are linked together on a support frame. The curved side rails are made from corrosion resistant aluminum tubes, which offer full width impact protection along the entire length of the unit. The side rails were designed to re-direct errant vehicles away from the rear of the truck (coffin corner). Other manufacturers Crash Attenuator models have little or no side-angle impact protection.
Suggested Questions: None
Additional Information: None
Possible Problems: Their use is state-specific. Shown for educational purposes only.

## Slide 213: Application of Truck-Mounted Attenuators
Barrier vehicles
Shadow vehicles
Advance warning vehicles
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TMAs have various uses. They are recommended to protect workers when setting devices on the roadway. vehicles. These shadow vehicles are normally equipped with flashing arrows, changeable message signs, and/ or high-intensity rotating, flashing, oscillating, or strobe lights located properly in advance of the workers and/or equipment that they are protecting. However, these shadow vehicles might themselves cause injuries to occupants of the errant vehicles if they are not equipped with truck-mounted attenuators.
Suggested Questions: Who remembers what a shadow vehicle is?
Additional Information: Photo is from I-95 in Virginia, by J. Morales.
• Up to 45 M.P.H. or 62 M.P.H. protection • Absorbs collision energy during rear-end impacts • Prevents impacting vehicles from under riding the truck • Reduces expensive equipment damage • Provides a positive barrier between motorist and work crews • Attaches easily to most vehicles (total vehicle weight must be a minimum of 16,000lbs)
Possible Problems: May be required by the state.

## Slide 214: Truck-Mounted Attenuators
Located in advance of the work area
  Past the buffer!
Shall be designed for the specific application intended
  Impact speed
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Follow the manufacturer’s instructions!
Suggested Questions: None
Additional Information: None
Possible Problems: May be required by the state.

## Slide 215
Advance
Warning Area
Transition Area
Activity
Area
Termination Area
Longitudinal Buffer Space
Work Space
TMA goes here!
Image: ATSSA
Notes: Key Message: Discuss Position of TMA within a lane closure
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Remember the TMA DOES NOT belong in the buffer space. Let errant vehicles recover before impacting a TMA. The buffer space must be empty
Suggested Questions: Where does the TMA go?
Additional Information: This picture shows the four component parts of a TTC zone:
Advance Warning Area
Transition Area
Work Area
Termination Area
Possible Problems: Discuss options if the buffer space is not available.

## Slide 216
BUFFER SPACE
TMA
Image: ATSSA
Notes: Key Message: Discuss Position of TMA within a lane closure
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Buffer space appears on click.
Suggested Comments: Notice that the TMA is located AFTER the buffer space
Suggested Questions: None
Additional Information: Taken in Reston, VA, by J. Morales
Possible Problems: Virginia requires stripes to be orange and black. They have to be yellow and black in other states.

## Slide 217: Truck-Mounted Attenuators
Work as a system
Follow manufacturer’s recommendations & local agency specifications
10,000 pounds or more on host vehicle
  Pickups unacceptable on TTMAs
http://epg.modot.org/files/thumb/4/47/612_Impact_Attenuators.jpg/325px-612_Impact_Attenuators.jpg
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Follow the manufacturer’s instructions!
Suggested Questions: None
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: Each TMA is different. Discuss this in general terms.

## Slide 218: Truck-Mounted Attenuators
Usually equipped with
  Arrows boards
  Rotating/strobe lights
  Changeable message signs
Their application is state-specific
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Pay attention to the visibility of the TMA!
Suggested Questions: None
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 219: Truck-Mounted Attenuators
Typically (if stationary):
  Parking brake set
  Transmission in gear
  Wheels straight ahead
  Allow for roll-ahead distance
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. These recommendations vary by manufacturer.
Suggested Questions: What is the roll-ahead distance? See next slide.
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 220: TMA Roll-Ahead Distance
Sufficient distance in advance of the workers or equipment being protected but
Not so much that the errant vehicle will travel around
“Roll-ahead distance”
RAD
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested. Comments: The shadow truck should be positioned a sufficient distance in advance of the workers or equipment being protected so that there will be sufficient distance, but not so much so that errant vehicles will travel around the shadow truck and strike the protected workers and/or equipment The position of the TMA is critical to its effectiveness. It should allow for the “Roll-Ahead Distance”. This the distance a TMA would push forward when struck. If this distance is too short, the TMS would be pushed into the workers. If it is too large, a vehicle may go around the TMA. It is specific to the TMA being used.
Suggested Questions: What would happen if a TMA is struck? What do you thing the typical TMA is? 10 feet, 200 feet? See next slide.
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 221: Roll-Ahead Distance
The distance a TMA will displace when impacted
It depends on
  Weight of TMA
  Speed of impact
  Weight of impacting vehicle
Check with the manufacturer!
RAD
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The “Roll-Ahead Distance” is the distance a TMA would push forward when struck. If this distance is too short, the TMS would be pushed into the workers. If it is too large, a vehicle may go around the TMA. It is specific to the TMA being used.
Suggested Questions: What would happen if a TMA is struck? What do you thing the typical TMA is? 10 feet, 200 feet?
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 222: Roll-Ahead Distance
Image: ATSSA
Notes: Key Message: Discuss TMAs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: This photo illustrates the RAD
Suggested Questions: None
Additional Information: Refer to AASHTO’s Roadside Design Guide for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms.

## Slide 223: Sample TMA “Roll-Ahead Distances” for 55 mph Impact
Weight of TMA (lbs) | Weight of Impacting Vehicle (lbs)* |  | 
 | 4,500 | 10,000 | 15,000
10,000 (moving) | 100’ | 150’ | 175’
15,000 (moving) | 75’ | 125’ | 150’
10,000 (stationary) | 25’ | 75’ | 100’
15,000 (stationary | 25’ | 50’ | 75’
Source: Humphreys and Sullivan, “Guidelines for the Use of TMAs”
*Mid-size auto = 2,250 lbs
Full-size auto = 3,500 lbs
Loaded cargo truck = 10,000 lbs
Notes: Key Message: Discuss RAD
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: The RAD varies between 25’ and 175’, according to this study.
Suggested Questions: Why would the RAD be more for a moving operation? It had a running start!
Additional Information: Refer to the source study for additional information.
Possible Problems: : Each TMA is different. Discuss this in general terms. Don’t spend too much time here. Just say the RAD varies from 25’ top 175’ depending on the factors discussed. Some states say 100’ as a constant for the RAD.

## Slide 224
To close off an area
Prevent errant vehicle entry
For long term work zones
Consideration must be given for work vehicle access to the area
Vehicle Arresting Systems (VAS)
Image: Impact Absorption
Notes: 224
Key Message: Discuss vehicle arresting systems (arrestor nets)
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These devices are more appropriate for work zones where the installation can remain in place over an extended period of time. They require adequate buffer space behind the arrestor net that equates to 120 ft for a 60 mph approach speed.
The fixed end anchors require substantial effort to install, providing minimal return for very short term use. Temporary anchors are available for short-term applications.
These systems may require a work vehicle entrance that bypasses the arrestor net, with a watchman or police officer to prevent unauthorized entrances to the work space.
Past history of unauthorized or unintentional entry into the work space on a closed highway section may indicate that this system is worthwhile for similar projects. It may also deter motorists by providing physical separation between traffic and the closed area via the device.
Suggested Questions: Have you seen these before?
Additional Information: None
Possible Problems: The picture shown is of a proprietary system and is not meant to imply preference or endorsement.

## Slide 225
Not in 2009 MUTCD
Section 6F-83 of 2003 MUTCD
Vehicle Arresting Systems (VAS)
Image: Impact Absorption
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: The last category of PP devices are vehicle-arresting systems.
Suggested Questions: None
Additional Information: Removed because “it is not a traffic control device”
Possible Problems: None

## Slide 226
Vehicle-arresting systems are designed to prevent penetration into activity areas while providing for smooth, reasonably safe deceleration for the errant vehicles
They can consist of portable netting, cables, and energy absorbing anchors
2003 MUTCD Section 6F-83: SUPPORT:
Image: FHWA
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Vehicle-arresting systems are designed to prevent penetration into activity areas while providing for smooth, reasonably safe deceleration for the errant vehicles
They can consist of portable netting, cables, and energy absorbing anchors.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 227
Should be used in accordance with the manufacturer’s specifications
Should be located so that vehicles are not likely to penetrate the location that the system is designed to protect
2003 MUTCD Section 6F-83: GUIDANCE
Image: FHWA
Notes: Key Message: Vehicle-Arresting Systems (VAS)
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: When used, a vehicle-arresting system should be used in accordance with the manufacturer’s specifications and should be located so that vehicles are not likely to penetrate the location that the system is designed to protect.
Suggested Questions: None
Additional Information: MUTCD shown is 2003 Edition.
Possible Problems: None

## Slide 228
To prevent access into a closed section of highway during periods when work is active
Where a section of highway is closed and reopened daily over an extended period of time
Typical Applications of VAS
Image: FHWA
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Typical uses: To prevent access into a closed section of highway during periods when work is active. Where a section of highway is closed and reopened daily over an extended period of time.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 229: Dragnet
Uses a “metal Bender” to absorb energy
Allows for stopping varying weights & speed
A metal tape is pulled through a series of offset pins
Few moving parts- When impacted replacing the metal tapes is normally all that is required
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Dragnet Vehicle Arresting Barrier is a simple, yet versatile, non-lethal product that was derived from The Entwistle Company's long history in the design and manufacture of aircraft arresting gear systems for shipboard installations. The system offers a practical solution for highway safety, security, and force protection applications.
Dragnet has been extensively tested by independent transportation research organizations. The system has satisfied the Structural Adequacy, Occupant Risk and Vehicle Trajectory evaluation criteria per the National Cooperative Highway Research Program Report 350 (NCHRP 350), TL-3 Head-On Impact.
Dragnet systems are currently designed and tested for highway safety applications such as:
Median barriers
Work zone protection
Truck escape ramps
High Occupancy Vehicle (HOV) lane closures
Railroad crossings
The Dragnet also offers a solution to the need for security and force protection by denying access to highly sensitive areas such as military bases, government buildings, or industrial facilities.
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 230
Image: Impact Absorption
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: {Show photo}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 231
Image: Impact Absorption
Notes: Key Message: Typical Uses of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: {Show photo}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 232
Fixed end anchors may require substantial effort to install, providing minimal return for very short-term use
Temporary anchors are available for short-term applications
Relative Costs and Benefits of VAS
Image: FHWA
Notes: Key Message: Relative Costs and Benefits of VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Fixed end anchors may require substantial effort to install, providing minimal return for very short-term use. Temporary anchors are available for short-term applications.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 233
May require a work vehicle entrance that bypasses the arrestor net, with a watchman or police officer to prevent unauthorized entrances to work space
Past history of unauthorized or unintentional entry may warrant its use
Requires a buffer space behind the arrestor net that equates to 120 ft for a 60 mph approach speed
Other Considerations for Using VAS
Notes: Key Message: Other Considerations for Using VAS
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
  Suggested Comments: {Self explanatory}
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 234: B6. Other
Temporary pavement markings
Temporary rumble strips
Use in accordance with the MUTCD and/or State standards and guidelines
Image: FHWA
Notes: Key Message: Discuss other TCDs
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are many other devices applicable to work zones. Of course all should be used in accordance with applicable standards and guidelines.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss as needed. Students may not be familiar with the use of these devices, particularly barriers. Be prepared to expand.

## Slide 235: Temporary Rumble Strips
Should be considered to supplement other TTC devices to alert drivers of unusual conditions
Remove prior to removing signs
Image: FHWA

## Slide 236: Removable Polymer Rumble Strip
Image: Florida DOT
Notes: Source FDOT standards

## Slide 237: Removable Polymer Rumble Strip
Image: FHWA
Notes: Source FDOT standards

## Slide 238: Molded Engineered Polymer Rumble Strip
Image: Florida DOT
Notes: Source FDOT standards

## Slide 239: Molded Engineered Polymer Rumble Strip
Image: ATSSA

## Slide 240: Typical Placement of Temporary Raised Rumble Strips
Image: Florida DOT
Notes: Source FDOT standards

## Slide 241: C. Contracting Strategies
Conventional contract model
Alternative contracting techniques
Evaluation of contractor designs
Notes: Key Message: Introduce contracting strategies
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The AASHTO Highway Subcommittee on Construction has developed a catalog of contracting methods and procedures (Primer on Contracting 2000 1998). Among the specific techniques identified are several pertinent to minimizing lane occupancy. These include:
• Lane rental,
• Cost-plus-time bidding,
• Incentives/disincentives, and
• Flexible notice-to-proceed dates (or flexible start dates).
Additional Information: None
Possible Problems: None

## Slide 242: C1. The Conventional Contract Model
Remains the dominant approach to contracting
Alternative contracting strategies are being deployed
Notes: Key Message: Discuss contracting strategies and considerations
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Innovative contracting methods could complement the TCP. Contract methods such as lane rental, cost-plus-time bidding, and the use of incentives and disincentives, may reduce contractor time in work zones. Many transportation agencies are employing a variety of alternate contracting methods to accelerate construction and reduce the time contractors occupy work zones.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 243: C1. Conventional Contract Model
Agency prepares a set of contract documents
Bids are solicited
A contract is awarded to the responsible bidder submitting the lowest responsive bid
“Low bid”
Images: ATSSA
Notes: Key Message: Discuss the conventional contract model
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The traditional competitive bidding system has served the public well. The foundation of this system is the principle of competitive sealed bids, with the award going to the lowest responsive bidder. The selection of the contract winner is based strictly on cost. The low bid system, however, does not always optimize construction duration.
Suggested Questions: Do you use this model?
Additional Information: None
Possible Problems: None

## Slide 244: C2. Alternative Contracting Strategies
Contracting strategies where the winning bid is based on criteria other than cost (alone)
Cost is not the
only factor!
Image: FHWA
Notes: Key Message: Discuss the conventional contract model
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: In recent years, DOTs have been under increasing pressure to reduce construction time and minimize the impact of construction on the traveling public and local businesses. In response to these pressures, several innovative or “alternative” modifications to the low bid system have been used. Bids that can be accepted based on reduced time, improved quality, centralized accountability, and reduced delays to motorists. Let’s discuss a couple of them.
Suggested Questions: Have you used alternative procurement techniques? Which ones?
Additional Information: None
Possible Problems: None

## Slide 245: Other Possible Criteria for Selecting the Winning Bid
Reduced project delivery time
Reduced delays
Centralized accountability (in one organization rather than several
Improved quality
Notes: Key Message: Discuss other possible criteria for selecting the winning bid
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are some of the possible criteria that we can use to select the winning bid. We could use reduced project delivery time, reduced motorists’ delays, whether the contractor has centralized accountability (in one organization rather than several) and improved quality of the work.
Additional Information: If cost is not the criteria, what other criteria can we use? Can you think of any others?
Possible Problems: None

## Slide 246: C2. Alternative Contracting Strategies Used in WZ
A+B bidding
Design-build contracting
Incentive- disincentive provisions
Lane rental
Flexible notice to proceed
Notes: Key Message: Discuss alternative contracting strategies used in WZs
Est. Presentation Time: 2 minutes
Explanation of Cues/Builds:
Suggested Comments: Several “project specific” innovative contracting techniques are currently being used and evaluated by a number of State highway agencies. These include the ones listed on the screen. Let’s discuss them in detail.
Suggested Questions: None
Additional Information: These contracting techniques are not work zone strategies, per se, but are sometimes regarded as a means to reduce work zone impacts. In general, the transportation agency uses competitive market-based incentives to attain its objectives. Each of these techniques and night work will be discussed separately. Contracts are legal documents. Agencies are governed by a body of law, including procurement statutes. Therefore, project personnel should be aware of potential limitations and requirements as contracts are awarded and administered.
Some agencies have combined two strategies in a single contract. For example, lane rental could be combined with A+B bidding or incentive-disincentive provisions. The strategies should be consistent with each other and with agency goals. For example, a lane rental fee structure designed to discourage peak-hour traffic interference may not have its intended effect if the contract also includes an early completion incentive provision that is large enough to economically justify occupying lanes during peak-hour periods. The role and responsibilities of contractors varies substantially with contracting type. This variation is intended. Contracting strategies and some of the associated opportunities and implications are described next.
Possible Problems: Discuss this in general terms since the following slides get into details. T

## Slide 247: A + B Bidding
Also known as cost-plus-time
“Bid” is computed using the equation Bid=A+Bx, where
  A = Dollar amount to perform all work
  B = number of calendar days required to complete the project
  x = Road user cost per day
Notes: Key Message: Define A + B Bidding
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Cost-plus-time (A+B) contract bidding generally reduces the total time of construction, but may not substantially reduce lane occupancy during the construction period. To implement this method, many contractors work off-peak hours, nights, and weekends to complete construction within the time bid. This reduces the impact on the traveling public, a basic goal of reducing lane occupancy. The equation is used to determine the lowest bid. Contractor payments are based on the schedule of bid items (A portion of bid). Additionally, for each day in excess of B used by the contractor to actually complete the work, an assessment is made for road user costs. Frequently, there is a reciprocal incentive provision when the actual number of days to complete construction is less than the number of days bid (B). Typically, the agency’s cost-plus-time contract documents include a work zone design in the same or similar manner as if the contract were a conventional one. Contractors, as bidders and in contract performance, have a strong business incentive to minimize the number of days needed to complete the specified work. Therefore, the contract documents must clearly indicate contractor duties and limitations with regard to traffic control and work zone design. This strategy is generally applied to projects with a high potential for mobility and/or safety impacts, generally on high-volume facilities that do not have reasonable detour routes.
Additional Information: http://ops.fhwa.dot.gov/wz/workshops/accessible/Kent_MWZWB.htm
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 248: Design-Build Contracting
An agency-owner procures a single contract providing for both design and construction
Benefits:
  Time savings
  Contractor innovation
  Administration efficiencies
Notes: Key Message: Define Design-Build Contracting
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Under this contracting method, an agency-owner procures a single contract providing for both design and construction. This avoids questions of responsibility and coordination between a contract designer and contract constructor. It has been employed on a wide variety of project scales, including the reconstruction of I-15 in Salt Lake City, Utah. Benefits attributed to design-build contracting include time savings, contractor innovation, and administration efficiencies. Design-build practices are emerging and varied due to the merging of these traditionally separate functions. In many jurisdictions, design service and construction contract procurements are governed by distinct laws and traditions. Federal and state laws may be relevant to contracts that include both categories of service. The development of the entire TMP may be assigned to the design-build contractor. The agency should always specify its high-level requirements and acceptable criteria and processes.
Additional Information: State transportation agencies have shown an increasing interest in design-build contracting as an alternate contracting technique. Under the design-build approach, the contracting agency identifies the end result parameters and establishes the design criteria for a project. The design- build contractor is responsible for both design and construction of the facility and develops a design proposal in agreement with agency requirements, which optimizes the contractor's construction abilities. Design-build contracting is particularly suited for projects that fit the design- build process, such as complex
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 249: Incentive-Disincentive Provisions
Financial consequences to contractors
Based on actual completion of work relative to scheduled completion
Notes: Key Message: Define Incentive-Disincentive Provisions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Incentive-disincentive contract provisions provide for specified financial consequences to contractors based on actual completion of identified work (considered critical by the agency owner) relative to scheduled completion. The schedule (calendar days or completion date) for critical work items is established by the owner agency and identified in the bid documents. A daily incentive-disincentive amount is also established by the owner agency in the procurement documents. Additional contractor payment (i.e., incentive payment) is made for each day that the identified critical work is completed ahead of schedule, and contractor payment is reduced for each day that the contractor overruns the scheduled completion. Incentive-disincentive provisions are intended primarily to minimize work zone impacts on critical projects. The determination of incentive-disincentive daily amounts includes consideration of traffic safety, road user delay, and maintenance of traffic costs.
Additional Information: None
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 250: Lane Rental
Contractor pays a pre-established fee to occupy (“rent”) a travel lane
Fees based on:
  Rental rates
  Actual times that the contractor occupies lanes
Image: ATSSA
Notes: Key Message: Define Lane Rental Provisions
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Lane rental involves assessing the contractor a pre-established fee to occupy a travel lane or shoulder as part of the contract. Rental rates are established by the agency in the procurement documents and are typically stated in dollars per travel lane or shoulder per time period (e.g., day, hour, or faction of hour), with peak periods carrying higher rates. The anticipated times or durations of occupation are not stated in the agency procurement or bid. The contract is awarded to the low bidder on the basis of pay items. During execution of the contract, rental fees are computed by the agency based on the agency’s rental rates and actual times that the contractor occupies travel lanes and shoulders. The rental fees reduce the net amount paid to the contractor and provide a financial incentive to minimize the duration of contractor occupations and hasten return of the facility to service. The lane rental approach allows some flexibility in the distribution of work zone design assignments between agency and contractor. The conventional approach of providing a work zone design with the contract documents is workable and common. When a TTC and/or construction phasing plan are provided, the competitive and innovative forces are focused on minimizing the time that travel lanes are occupied while completing the identified work. Alternatively, an agency may identify the high level requirements and lane rental fee schedule. This more open approach allows the contractor greater flexibility and more areas of potential innovation. This approach has been used for several freeway paving projects.
Additional Information: None
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 251: Flexible Notice to Proceed
Contractor has the option of selecting when construction can begin
Scheduling problems that may delay contract completion are avoided
Public exposure to adverse construction conditions is reduced
Notes: Key Message: Define Flexible Notice to Proceed
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Flexible notice-to-proceed dates (variable start dates) is an approach that gives the contractor the option of selecting, within a specified period, when construction can begin. Although the number of calendar days of construction time is specified, and the contractor may be required to bid time, a flexible start date is still allowed. Normally, the contractor begins work shortly after the "Notice to Proceed." With flexible starting provisions, the contractor is allowed to extend this period of time (usually up to 100 days) before starting construction (Alternate Contracting Users Guide 1997 and Primer on Contracting 2000 1998). FLDOT uses flexible start dates for two reasons. First, this technique reduces the length of time the public is exposed to construction conditions. Second, the probability of completing construction within the authorized contract time is increased. This technique provides the contractor with more time to plan and schedule the use of equipment and manpower prior to the start of construction. Scheduling problems that may delay contract completion are avoided and public exposure to adverse construction conditions is reduced.
Additional Information: None
Possible Problems: Introduce this as a concept. Avoid details to stay on schedule.

## Slide 252: C3. Evaluation of TTC Designs Proposed by Contractors
There should be a basis for the review and approval
Certification programs for designers are available and recommended
Notes: Key Message: Discuss Evaluation of WZ Designs Proposed by Contractors
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are situations under which contractors develop work zone designs and submit them for agency approval or concurrence. There should be a basis for the review. Requiring a PE stamp is not enough!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 253: Knowledge Check
Which lights are used for delineation?
Name two advantages of nighttime work zones?
Name three positive protection devices
Name 2 alternative contracting strategies?
What is lane rental?
Name two advantages of full closures
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.

## Slide 254: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at your questions.
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: None