## Slide 1: 4. Transportation Operation (TO) Strategies
Work Zone Strategies
https://patch.com/pennsylvania/northwhitehall/coplay-creek-road-closed-for-repairs_345b7cce
Notes: Key Message: Module Opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s move to the next module. In this module {name}, we will.. {next slide}
Suggested Questions: None
Possible Problems: None

## Slide 2: Module Objectives
  Discuss TO strategies and their application to work zones
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3
TMP
TO
Umbrella image: https://www.pinterest.com/pin/452471093788604008/
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the TO component of the TMP and the strategies associated with TTC.
Suggested Questions: None
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here. This slide is to remind them that to is one of the components of the TMP.

## Slide 4: Considerations of Work Zone Impact Analysis
Mobility and safety impacts of the project at the…
  Project,
  Corridor, and
  Network levels
The combined impacts of concurrent projects that are located…
  Near each other or
  On the alternate route for another project
Notes: Key Message: Why Analyze the Impacts of the Work Zone?
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Analyzing and understanding the anticipated type, severity, and extent of work zone impacts associated with various project alternatives enables practitioners to include appropriate mitigation strategies during project programming, design, and in the development of effective transportation management plans (TMPs). Analysis of the work zone may include consideration of items such as:
Mobility and safety impacts of the project at the project, corridor, and network levels.
The combined impacts of concurrent projects that are located near each other or on the alternate route for another project
Impacts on nearby intersections and interchanges, railroad crossings, and public transit and other junctions in the network.
Impacts on evacuation routes and affected public property.
Impacts on affected businesses and residences.
Questions: None
Additional Information: None
Possible Problems: Avoid getting too specific here.

## Slide 5: Considerations of Work Zone Impact Analysis (cont.)
Impacts on:
  Nearby intersections and interchanges
  Railroad crossings, and
  Public transit and other junctions in the network.
Impacts on evacuation routes and affected public property
Impacts on affected businesses and residences
Notes: Key Message: Why Analyze the Impacts of the Work Zone?
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Analyzing and understanding the anticipated type, severity, and extent of work zone impacts associated with various project alternatives enables practitioners to include appropriate mitigation strategies during project programming, design, and in the development of effective transportation management plans (TMPs). Analysis of the work zone may include consideration of items such as:
Mobility and safety impacts of the project at the project, corridor, and network levels.
The combined impacts of concurrent projects that are located near each other or on the alternate route for another project
Impacts on nearby intersections and interchanges, railroad crossings, and public transit and other junctions in the network.
Impacts on evacuation routes and affected public property.
Impacts on affected businesses and residences.
Questions: None
Additional Information: None
Possible Problems: Avoid getting too specific here.

## Slide 6: Transportation Operation Strategies
Intelligent Transportation Systems (ITS)
Demand management strategies
Corridor/network management strategies
Incident management and enforcement strategies
Safety management strategies
Back-of-Queue strategies
Notes: Key Message: Introduce the TO Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We can divide TO strategies into these five groups.
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid getting too specific here.

## Slide 7: A. Intelligent Transportation Systems (ITS) Strategies
Allow the use of technology as strategy to improve mobility and safety in work zones
Improve incident
  Detection
  Response, and
  Clearance in work zones
Image: FHWA
Notes: Key Message: Discuss Intelligent Transportation Systems Strategies
Est. Presentation Time: Less than 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: By easing congestion and improving traffic flow, ITS technologies can reduce construction time and costs. ITS technologies also improve incident detection, response, and clearance in work zones; this is particularly important because traffic capacity often is reduced in work zones, and incidents in these areas cause even greater congestion and increase the potential for secondary crashes.
ITS in work zones is one of the tools in our work zone management toolbox, and the benefits information in the report, as well as the tips and lessons learned, can help other transportation practitioners use this tool effectively.
Suggested Questions: None
Additional Information: Forward-looking transportation agencies across the country are using ITS in their major work zones to make travel through and around the work zones safer and more efficient. ITS involves the use of electronics, computers, and communications equipment to collect information, process it, and take appropriate actions. ITS technology can be applied in work zones for: Traffic monitoring and management, providing traveler information, incident management, enhancing safety of both the road user and worker, increasing capacity, enforcement, tracking and evaluation of contract incentives/disincentives (performance-based contracting) and work zone planning.
Possible Problems: None

## Slide 8: ITS Work Zone Strategies
Being used to anticipate and mitigate congestion caused by highway work zones
Should be considered
Examples follow:
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ITS technologies are increasingly being used to anticipate and mitigate congestion caused by highway work zones. ITS can help secure the safety of workers and travelers in a work zone by facilitating traffic flow through and around the work zone. ITS in work zones include the temporary implementation of traffic management or incident management capabilities. These temporary systems can be stand-alone implementations, or they may supplement existing systems in the area during construction ITS applications for managing work zones include measures to control vehicle speeds and notify travelers of changes in lane configurations or travel times and delays through the work zones. ITS technologies also improve incident detection, response, and clearance in work zones; this is particularly important because traffic capacity often is reduced in work zones, and incidents in these areas cause even greater congestion and increase the potential for secondary crashes.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 9: Portable Traffic Management Systems
Real-time traveler information
Congestion & incident management applications
Sensors to monitor real-time traffic conditions
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In 2002, the North Carolina Department of Transportation (NCDOT) deployed its first smart work zone during roadwork on I-95 just north of
Fayetteville. Sensors collected traffic data and analyzed the data to estimate delay. When delay surpassed a pre-set threshold, the system automatically displayed alternate route information on electronic signs. Traffic condition information was also displayed on a Web site. Before the system was installed, whenever there were lane closures queues approaching the work zone were often several miles long and sometimes exceeded five miles. After the system began operating, the queues decreased to generally two miles or less. NCDOT noted that there were no fatalities associated with this work zone and fewer crashes as compared to previous I-95 road projects without ITS.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 10
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is an example of portable traffic management system that incorporates video, sensors, wireless communications, and dynamic message signs integrated throughout the work zone. Smart Zone gives TMC operators the ability to monitor changing traffic patterns and weather conditions.
Suggested Questions: None
Additional Information: None
Possible Problems: Location does not allow for deflection of guardrail (no need to mention).

## Slide 11: Traveler Information
Info automatically displayed on CMS and website
  Map
  CMS messages
Info can also be distributed via Highway Advisory Radio (HAR)
Cameras to gather additional condition info
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Automated Work Zone Information Systems (AWIS) provide real-time travel information to road users and encouraged diversion to less congested alternate routes during periods of heavy congestion in the work zone. A central computer system collects speed data from roadside detectors, estimates current travel times, and posts work zone travel information on PCMS and a project website.
Suggested Questions: None
Additional Information: A 2004 AWIS deployed by Caltrans in Devore, CA, provided updated travel time information every 10 minutes and displayed one of six different messages depending on the level of congestion detected in the work zone. When congestion was categorized as severe, and travel time estimates exceeded 50 minutes, the central computer system automatically crosschecked traffic conditions on alternate routes to determine if a detour recommendation was warranted. If the alternate route was experiencing free flow conditions, the detour recommendation was displayed in a flashing sequence with the work zone travel time information (e.g., “TRAVEL TIME 50 MIN FROM I-15/I-210 TO SR-138” and “DETOUR TO I-10 EAST”). In MN, a freeway work zone travel time system provides travel time information in real time for a freeway route that contains work-zones by automatically integrating normal loop data on non-work zone area with temporary work-zone detector data. The system has been operating at the I-494 Wakota bridge work zone since June 2005. It was also applied at the I-94 Crow River work zone area during the bridge rehabilitation period in July 2005. Speed measurements from the temporary work zone detection system are uploaded to an internet site every 30 seconds. The travel time calculation module, developed by Mn/DOT, accesses the work zone speed data and combines them with the data from the normal loop detectors on the non-work-zone sections. Travel times for different destinations can be calculated every 30 seconds in a given corridor and downloaded back to the variable message signs in the field through the internet.
Possible Problems: HAR = Highway Advisory Radio

## Slide 12: Variable Speed Limit (VSL) Systems
Establish and display a condition-responsive speed limit on signs based on pre-programmed criteria
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Variable speed limit (VSL) systems detect occupancy, speed, and weather; the data are analyzed by a virtual traffic management center or field unit that uses the information to establish and display a condition-responsive speed limit on signs based on preprogrammed criteria. The data also helps provide real-time information to motorists through changeable message signs, Web sites, and traveler advisory radio alerts. Eliminate the need to cover/remove non-applicable static speed limit signs.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 13: Variable Speed Limit (VSL) Systems
Already being used in several States and internationally
Potentially reduce driver error and speeds
Image: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: VSL systems are already being used in several states and could be implemented in appropriate areas across the United States to help potentially reduce driver error and speeds, and to enhance the safety of our roadways through the use of innovative technology.
AZ, CO, MI, MN, NE, NJ, NM, OR, WA
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 14: VSL Evaluation
Evaluate the effectiveness based on:
  Speed limit compliance
  Credibility of speed limits
  Improved safety
  Improved traffic flow
Image: FHWA
Notes: Key Message: Variable Speed Limits in Work Zones
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Once the VSL system is implemented, it will be necessary to evaluate its effectiveness. The following measures of effectiveness can be used: 1) speed limit compliance: is traffic complying with the VSL? A speed study may be necessary. 2) How credible are the speed limits? This is related to compliance. If the VSL is not credible, compliance will be low. 3) Improved safety: Arguably, better compliance will lead to better flow and improved safety. 4) Improved traffic flow: Compliance will affect flow positively, reducing the variance between high speeds and low speeds. These four measures are tightly related.
Suggested Questions: None
Additional Information: Available at http://www.ops.fhwa.dot.gov/wz/its/index.htm
Possible Problems: None

## Slide 15: Speed Management Strategies
Speed is a determining factor for selection of strategies
Crash severity increases with speed - substantially so for speeds exceeding 60 mph
Which speed should we use as
our work zone design speed?
Notes: Key Message: Discuss Speed Management Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There is a widely held perception that speed is one of the most significant factors in road crashes. This perception is especially strong with regard to work zones. Speed reduction measures are a prominent topic in work zone practice and published research. Perceived speed-safety linkages stem, in part, from the relationship between vehicle speed and operator capability. Crash severity is related to the change in speed upon impact. Crash severity increases with speed and substantially so for speeds exceeding 100 km/h [60 mph]. The relationship of vehicle speed to crash probability is less clear. For permanent roadways, there is evidence indicating that crash probability is related to speed deviation above and below the mean speed. Crash rates are lowest for vehicles traveling near the mean speed.
Many factors can influence the speed at which a motorist drives, including driver age, gender, attitude, and perceived risks of law enforcement or crash. Therefore, different drivers will choose different speeds for the same conditions. Speed choice is also influenced by factors such as weather, road and vehicle characteristics, speed zoning, speed adaptation, and impairment.
Suggested Questions: Is lowering the posted speed a good idea? Turn into a discussion.
Additional Information: Available at http://www.ops.fhwa.dot.gov/wz/its/index.htm
Possible Problems: None

## Slide 16: Establish Reasonable Target Speeds
Work zone design speed
Posted speed
85th percentile
Anticipated operating speed
  “prevailing speed”
Notes: Key Message: Discuss Speed Management Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Target speed is the desirable free-flow operating speed. No single value can represent all vehicle speeds, since different drivers will choose to operate at different speeds under the same conditions. The 85th-percentile speed is commonly used to characterize operating speed at a location or segment. In this guidance, target speed is the desirable 85th-percentile free-flow speed within a construction work zone. The work zone design speed is defined as “a selected speed used to determine specific work zone geometric design features.” A value equal to or slightly greater than the target speed is appropriate. Specific candidate speed management measures include automated enforcement(if applicable), dedicated enforcement patrols, drone radar, portable changeable message signs, rumble strips, speed trailers, warning devices, and variable speed limits. The selection of speed management measures should also consider the magnitude of speed reduction, exposure (i.e., traffic volume and duration of condition), and experience with comparable situations. Work zone speed management and control strategies are the subject of ongoing development and evaluation. Current information is available through a variety of websites, including the National Work Zone Safety Information Clearinghouse and sites hosted by organizations such as AASHTO and the FHWA.
Suggested Questions: Is lowering the posted speed a good idea? Turn into a discussion.
Additional Information: Available at http://www.ops.fhwa.dot.gov/wz/its/index.htm
Possible Problems: None
T

## Slide 17: MUTCD
TTC plans “be designed so that vehicles can reasonably safely travel through the TTC zone with a speed limit reduction of no more than 10 mph.”
Image: FHWA
Notes: Key Message: Discuss MUTCD re: Speed
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The general characteristics of certain highways and drivers’ previous experience with specific facilities create expectations, including those related to appropriate speed. Target speeds that meet or nearly meet experience-based expectations are desirable. The MUTCD suggests that TTC plans “be designed so that vehicles can reasonably safely travel through the TTC zone with a speed limit reduction of no more than 10 mph.” For a variety of reasons, experience-based speed expectancies are not always reasonable targets speeds. Operating speeds at particular locations must sometimes be reduced substantially below approach speeds. On high-speed facilities, this is undesirable yet unavoidable. Work zone design features are a potential cause of speed reduction and may preclude a target speed directly related to experience-based speed expectancies. The Green Book and many other design policies employ a design speed approach for the design of permanent roads. With this convention, criteria for some design elements (e.g., sight distance, minimum radii, maximum grade, some cross sectional dimensions, and superelevation) are directly related to design speed, whereas criteria for other roadway design elements (e.g., some cross-sectional elements and vertical clearance) are not related to design speed. Many, but not all, state transportation agencies use a speed parameter to guide some work zone design decisions. Agencies may use a speed parameter primarily for selected features (e.g., horizontal curvature) and/or for selected work zones types (e.g., median crossover).
Suggested Questions: Is lowering the posted speed a good idea? Turn into a discussion.
Additional Information: Page 47, 12
Possible Problems: None

## Slide 18: MUTCD
“Traffic control in temporary traffic control zones should be designed on the assumption that road users will only reduce their speeds if they clearly perceive a need to do so, and then only in small increments of speed”
Image: FHWA
Notes: Key Message: Discuss MUTCD re: Speed
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The general characteristics of certain highways and drivers’ previous experience with specific facilities create expectations, including those related to appropriate speed. Target speeds that meet or nearly meet experience-based expectations are desirable. The MUTCD suggests that TTC plans “be designed so that vehicles can reasonably safely travel through the TTC zone with a speed limit reduction of no more than 10 mph.” For a variety of reasons, experience-based speed expectancies are not always reasonable targets speeds. Operating speeds at particular locations must sometimes be reduced substantially below approach speeds. On high-speed facilities, this is undesirable yet unavoidable. Work zone design features are a potential cause of speed reduction and may preclude a target speed directly related to experience-based speed expectancies. The Green Book and many other design policies employ a design speed approach for the design of permanent roads. With this convention, criteria for some design elements (e.g., sight distance, minimum radii, maximum grade, some cross sectional dimensions, and superelevation) are directly related to design speed, whereas criteria for other roadway design elements (e.g., some cross-sectional elements and vertical clearance) are not related to design speed. Many, but not all, state transportation agencies use a speed parameter to guide some work zone design decisions. Agencies may use a speed parameter primarily for selected features (e.g., horizontal curvature) and/or for selected work zones types (e.g., median crossover).
Suggested Questions: Is lowering the posted speed a good idea? Turn into a discussion.
Additional Information: Page 47, 12
Possible Problems: None

## Slide 19: Criteria for Work Zone Posted Speed Reduction
Varies by state
Typically based on:
  Work duration
  Length of project
  Barriers used
  Lane width
  Presence of workers
  Uneven lanes
Image: FHWA
Notes: Key Message: Criteria for WZ Posted Speed Reduction
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general term and refer students to state standards.

## Slide 20: Dynamic Lane Merge Systems
Facilitate efficient & safe traffic merging on work zone lane closures
Use dynamic electronic signs & other special devices to control merging
Images: Minnesota DOT
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Dynamic lane merge systems facilitate efficient and safe traffic merging as vehicles approach work zone lane closures.
These systems use dynamic electronic signs and other special devices to control vehicle merging at the approach to lane closures.
Suggested Questions: None
Additional Information: http://www.dot.state.mn.us/trafficeng/workzone/2004DLMS-Evaluation.pdf
Possible Problems: Avoid explicitly endorsing the product. Discuss in general terms.

## Slide 21: Work Zone Speed Advisory Systems
Detect and display the speed of approaching vehicles to encourage drivers to slow down
Images: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The WZSAS is comprised of three primary components: (1) a video detection system, (2) two portable CMSs, and (3) a control system. The video detection system was used to measure the speeds of traffic at two selected points in advance of the work zone. Average speeds measured at the two points were displayed on the two portable CMSs which were placed upstream of diversion points in advance of the work zone. The control system, installed on a computer at the NDOR District 2 office, coordinated communications between the video detection system and the portable CMSs necessary to display the appropriate speed messages. NDOR personnel were alerted when speeds dropped below the selected threshold of 15 miles per hour, which enabled them to display incident-related messages when necessary.
Suggested Questions: None
Additional Information: http://www.itsdocs.fhwa.dot.gov/JPODOCS/REPTS_TE/14057.htm. Picture on right WZSAS Camera Mounted Above Roadway
Possible Problems: None

## Slide 22: Advanced Speed Info. Systems Using Microwave Sensors
Microwave traffic sensors and PCMSs to alert motorists of upcoming traffic conditions
Information can also be displayed on the Internet or sent to a pager/cell phone/PDA
Images: FHWA
Notes: Key Message: Discuss ITS Work Zone Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: An advanced speed information system is an ITS system that utilizes microwave traffic sensors and PCMSs to alert motorists of upcoming traffic conditions. This information can also be displayed on the Internet or sent to a pager/cell phone/PDA.
A downstream traffic sensor detects vehicle speeds as the vehicles pass the sensor and provides this information to an upstream PCMS. The speed ahead information is then displayed to the motorist. All of the traffic data can be sent to the base station in the project field office to be placed on the Internet. If the downstream speeds are free flow conditions then the signs can display a message reminding motorists of the speed limit. As speeds reduce, the signs can display the downstream speeds in five (5) MPH increments. If the downstream speeds are very slow, the signs can display a message alerting motorists of congested or stopped traffic ahead. This system was deployed along Eastbound I-70 between MD 32 and I-695 in Howard and Baltimore Counties.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 23: Benefits of Using ITS in Work Zones
Quantifiable assessment of 5 sites
Summary report
FHWA Website
Image: FHWA
Notes: Key Message: Introduce ITS in Work Zones Report
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
The report shares the results of a research project that involved doing some quantifiable assessment of the effectiveness of intelligent transportation systems (ITS) in work zones. The intent of the study was to find and document some benefits and helpful information that we could share with other States and practitioners looking to effectively deploy these systems. Five sites participated in the study: I-40 outside Winston-Salem in North Carolina; I-30 between Benton and Little Rock in Arkansas; US-131 in Kalamazoo, Michigan; I-35 in Hillsboro, Texas; and DC-295 in Washington, DC.
Suggested Questions: None
Additional Information: Available at http://www.ops.fhwa.dot.gov/wz/its/index.htm
Possible Problems: None

## Slide 24: B. Demand Management Strategies
Strategies to reduce traffic volumes through the work zone
Likely to be more effective when used in combination with PI&O strategies
Image: ATSSA
Notes: Key Message: Discuss Demand Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second area group of TO strategies involves demand management, or how to reduce the volume of traffic through the work zone.
Suggested Questions: Why are TDM strategies likely to be more effective when used in combination with PI strategies?
Additional Information: None

## Slide 25: B. Demand Management Strategies: Examples
Transit service improvements
Transit incentives
Shuttle services
Incentives
Park-and-ride promotion
HOV lanes
Toll/congestion pricing
Notes: Key Message: Discuss Demand Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These slides lists some of these strategies: Transit service improvements. Where appropriate, transit service improvements may include the modification of transit schedules and/or routes, increases in frequency, or the establishment of transit service in the corridor. Transit incentives. Transit incentives include employer and/or traveler transit subsidies and guaranteed ride home programs. Shuttle services. Shuttles and charter buses can reduce traffic volumes through a work zone if a sufficient number of users along the corridor are anticipated to use the service. Ridesharing/carpooling incentives. This strategy involves the use of rideshare/carpool incentives to reduce the number of vehicles traveling through a work zone. Incentives may include preferential parking for carpools, the addition of mainline HOV lanes or bypass lanes on ramps, provision of vanpool vehicles, etc. Park-and-ride promotion. This involves the creation, expansion, and/or promotion (advertising) of park-and-ride lots to encourage ridesharing or transit use, thus reducing the number of vehicles traveling through the work zone. High-occupancy vehicle (HOV) lanes. HOV lanes, also known as carpool lanes, require two or more persons per vehicle for use (exceptions may include motorcycles and/or low emission vehicles). HOV lanes are intended to provide an incentive for carpooling. Toll/congestion pricing. Tolls involve fees paid by motorists to drive on a particular roadway. Congestion pricing, or value pricing, is intended to reduce peak-period vehicle trips through the use of higher tolls during congested conditions.
Suggested Questions: None
Additional Information:

## Slide 26: B. Demand Management Strategies: Examples
Ramp metering
Parking supply management
Variable work hours
Telecommuting
Image: ATSSA
Notes: Key Message: Discuss Demand Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These slides lists some of these strategies: Ramp metering. Ramp meters are traffic signals located on on-ramps or freeway connectors to maintain safe and smooth freeway operations by controlling the entry of vehicles onto the roadway. This strategy serves both to decrease demand on a facility by controlling the entrance of vehicles, and to improve flow by matching entering vehicles to gaps in the traffic stream.
Parking supply management. This strategy involves reducing traffic demand by managing the parking supply typically through cost strategies.
Variable work hours. This strategy involves encouraging motorists who typically travel through the work zone during periods of high demand to work variable hours (off-peak) in order to reduce travel demand during peak periods.
Telecommuting. Telecommuting means working at home, or at a telecommuting center near home, either full or part time. Motorists who normally travel through the work zone would be encouraged to telecommute for the duration of the project to reduce the demand
Suggested Questions: None
Additional Information:
.

## Slide 27: C. Corridor/Network Management Strategies
Strategies to optimize traffic flow through the work zone corridor and adjacent roadways using various traffic operations techniques and technologies
Notes: Key Message: Discuss Corridor/Network Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This THIRD category includes strategies to optimize traffic flow through the work zone corridor and adjacent roadways using various traffic operations techniques and technologies.
Suggested Questions: When do you feel these strategies would be most effective? Perhaps when a work zone affects a large area and options (alternate routes) are available.
Additional Information:
Possible Problems: None

## Slide 28: C. Corridor/Network Management Strategies
Signal timing/coordination improvements
Temporary traffic signals
Street/intersection improvements
Bus turnouts
Turn restrictions
Parking restrictions
Image: FHWA
Notes: Key Message: Discuss Corridor/Network Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Some examples of these strategies are on the screen: Signal timing/coordination improvements. This involves retiming traffic signals to increase throughput of the roadway(s), improve traffic flow, and optimize intersection capacity in and around the work zone. Temporary traffic signals. The installation of temporary traffic signals can be used to improve traffic flow through and near the work zone. At a corridor or network level, using temporary traffic signals is more effective than stop signs or flaggers for providing mobility through the work zone area. These temporary traffic signals may also be coordinated with existing signals. Street/intersection improvements. Improvements on streets and intersections for the roadway and/or alternate routes may be necessary to provide increased capacity to handle the traffic through the work zone or within the adjacent corridor. This may include improvements to the mainline and intersections, including roadway and/or shoulder widening and additional through and/or turn lanes. Bus turnouts. This involves the construction of bus stop areas that are recessed from the travel lanes. This strategy may be helpful in work zones or on detour routes with a high occurrence of bus traffic and stops. Turn restrictions. This involves restricting turn movements for driveways and/or intersections to increase roadway capacity, reduce potential congestion and delays, and improve safety. Restrictions may be applied during peak periods or all day. Parking restrictions. This strategy involves the elimination of parking in all or part of the work zone and/or alternate routes, or parking restrictions during work hours or peak traffic periods. Parking restrictions can be used to increase capacity by converting the parking lane to an additional travel lane, reduce traffic conflicts, or provide improved access to the work area.
Suggested Questions: None
Additional Information:
Possible Problems: None

## Slide 29: C. Corridor/Network Management Strategies
Truck/heavy vehicle restrictions
Separate truck lanes
Reversible lanes
Dynamic lane closure system
Ramp metering
Temporary suspension of ramp metering
Image: FHWA
Notes: Key Message: Discuss Corridor/Network Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Other examples include: Truck/heavy vehicle restrictions. This strategy, which imposes restrictions on truck travel through the work zone either during specific periods or at all times, can increase passenger vehicle capacity of the roadway when a facility normally has a high truck volume. When using this strategy, the requirements of 23 CFR Part 658.11 (d) (1) and (g) must be followed.
Separate truck lanes. This strategy involves the provision of a separate truck lane through the restricted use of an existing lane, use of the shoulder or median, or construction of a new lane.
Reversible lanes. This strategy, also known as variable lanes or contra-flow lanes, involves sharing lane(s) of travel to accommodate peak period traffic flow. The direction of travel in the shared lane varies by time of day or day of the week.
Dynamic lane closure system. Also called dynamic lane merge system. This system uses dynamic electronic signs and other special devices to control vehicle merging at the approach to lane closures.
Ramp metering. Ramp meters are traffic signals located on on-ramps or freeway connectors to maintain safe and smooth freeway operations by controlling the entry of vehicles onto the roadway. This strategy serves both to decrease demand on a facility by controlling the entrance of vehicles, and to improve flow by matching entering vehicles to gaps in the traffic stream. Various strategies for ramp metering include pre-set timing, traffic actuated (metering changes based on mainline traffic), or centrally controlled. Ramp metering may be used during peak periods or all day.
Temporary suspension of ramp metering. This strategy involves turning existing ramp meters off during specific time periods or for the duration of the project.
Suggested Questions: None
Additional Information:
Possible Problems: None

## Slide 30: C. Corridor/Network Management Strategies
Ramp closures
Railroad crossings controls
Coordination with adjacent construction site(s)
Total closures
Image: FHWA
Notes: Key Message: Discuss Demand Management Strategies
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are several strategies available to optimize traffic flow through the work zone corridor and adjacent roadways using various traffic operations techniques and technologies, including the ones on the screen.
Suggested Questions: None
Additional Information:
Ramp closures. Ramp closure involves closing one or more ramps in or around the work zone. The ramp closure may be necessary to provide work access within the work space or can be used to improve traffic flow on the mainline.
Railroad crossings controls. When a rail crossing is located within a work zone and/or on a detour or diversion route, traffic control improvements at the crossing may become necessary for safety purposes, especially if work zone delays and congestion have the potential to force vehicles to stop on the tracks or between the crossing gates. Improvements may include advanced warning signs, railroad crossing signs, pavement markings, flashing lights, gate arms, flaggers or police officers, and possibly closure of the crossing to traffic during work periods.
Coordination with adjacent construction site(s). This involves combining or coordinating projects within a specific corridor to minimize the combined impacts on the motoring public and community. Coordination typically involves scheduling projects within a corridor to ensure that adequate capacity remains available to accommodate the anticipated travel demand within the corridor by not implementing work zones on adjacent or parallel highways at the same time. This may entail communicating about the timing of lane closures and occurrence of incidents, and coordinating diversion routes. It may also involve the completion of needed capacity and safety improvements on a highway prior to its use to carry traffic diverted or detoured from another project.
Possible Problems: None

## Slide 31: D. Incident Management and Enforcement Strategies
ITS for traffic monitoring/management
Transportation management center (TMC)
Surveillance
  Closed-Circuit Television (CCTV)
  Loop detectors
  Probe vehicles
Helicopter for aerial surveillance
Traffic screens
Quick-Clearance
Notes: Key Message: Discuss Incident Management and Enforcement Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This fourth category includes various strategies to manage work zone traffic operations. Work zone traffic management strategies involve monitoring traffic conditions and making adjustments to traffic operations based on changing conditions. Some of those changing conditions involve traffic incidents, so this category also looks at management strategies that have specific applicability to traffic incidents. These strategies involve improved detection, verification, response, and clearance of crashes, mechanical failures, and other incidents in work zones and on detour routes. This category also includes strategies to provide adequate enforcement of traffic regulations in work zones. Strategies in this area include the ones on the screen.
Suggested Questions: None
Additional Information: ITS for traffic monitoring/management. ITS can be used in work zones to identify areas where traffic flow is impeded so that traveler information can be provided and/or adjustments to the work zone can be made. A work zone ITS deployment uses sensors to detect traffic conditions and can automatically feed this information to motorist information outlets such as CMS and websites, or to a TMC. Monitoring traffic cameras can help detect places where drivers are having difficulty negotiating a work zone and then the layout can be adjusted. Transportation management center (TMC). This strategy involves the use of a TMC for coordinating and managing traffic and incident management activities in and around the work zone. Often an existing TMC for the region is used and may be staffed by either contract staff and/or agency personnel. If the project is large and of long duration, a project specific TMC may be established and operated to help manage incidents and maintain traffic flow. Surveillance [Closed-Circuit Television (CCTV), loop detectors, lasers, probe vehicles]. This strategy involves the use of surveillance equipment, such as detector stations or cameras, to help identify traffic problems and to detect, verify, and respond to incidents in the work zone. Helicopter for aerial surveillance. This involves the use of aerial surveillance to identify and verify traffic problems and incidents. Traffic screens. Traffic screens help prevent driver distractions in work zones, which can help to keep traffic moving and enhance safety. Screens may be mounted on the top of temporary traffic barriers to discourage gawking and reduce headlight glare.
Possible Problems:

## Slide 32: D. Incident Management and Enforcement Strategies
511 services
Mile-post markers
Service patrol
Photogrammetry
Coordination w/media
Local detour routes
Contract support for incident management
Image: ATSSA
Notes: Key Message: Discuss Incident Management and Enforcement Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This category includes various strategies to manage work zone traffic operations. Work zone traffic management strategies involve monitoring traffic conditions and making adjustments to traffic operations based on changing conditions. Some of those changing conditions involve traffic incidents, so this category also looks at management strategies that have specific applicability to traffic incidents. These strategies involve improved detection, verification, response, and clearance of crashes, mechanical failures, and other incidents in work zones and on detour routes. This category also includes strategies to provide adequate enforcement of traffic regulations in work zones. Strategies in this area include the ones on the screen.
Suggested Questions: None
Additional Information: Call boxes. Temporary or permanent call boxes may be installed through the work zone to provide motorists with a means to contact incident response personnel, thus expediting the response and clearance times for crashes and breakdowns.
Mile-post markers. Mile-post markers consist of a sign located in the median or shoulder, which lists location information (direction, route, mile, and tenths of a mile). Some areas may refer to these as location reference markers, since they can be used to mark direction; route, bridge or overpass names; intersection names; etc. in addition to mileage information.
Tow/freeway service patrol. This strategy involves the use of dedicated or on-site (or near site) towing services to reduce the time required to remove vehicles involved in an incident (breakdown or crash). Towing service is almost always contracted, while freeway service patrols might be contracted but are more likely to be publicly operated.
Total station units. This involves the use of survey equipment for documenting/mapping major incidents (e.g., fatal crashes, HAZMAT conditions, etc.) in order to reduce the clearance time. In some locations, total station units are being replaced by laser measuring units.
Photogrammetry. Photogrammetry involves the use of photos taken in the field and computer software for documenting and measuring incident-related data (e.g., skid marks, vehicle location, etc.) which may reduce incident clearance times.
Coordination with media. This strategy involves working with local news media to publicize traffic delays, incidents, and incident management. Working with media contacts in advance to establish procedures to be followed in the event of a major delay or incident can facilitate the dissemination of specific information upon the occurrence of a major delay or incident.
Local detour routes. Advance identification and approval/authorization of local detour routes is an especially useful strategy to address major traffic delays and incidents, particularly for high volume and incident prone work zones.
Contract support for incident management. This strategy provides additional contract support for incident management and response beyond that available from the construction contractor or within the agency. Contracts may include entities such as police agencies, towing/recovery providers, engineering consultants, or others, depending on the support needed for a project.
Possible Problems: None

## Slide 33: D. Incident Management and Enforcement Strategies
Incident management coordinator
Incident response plan
Dedicated (paid) police enforcement
Cooperative police enforcement
Automated enforcement
Increased penalties for work zone violations
Image: FHWA
Notes: Key Message: Discuss Incident Management and Enforcement Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This category includes various strategies to manage work zone traffic operations. Work zone traffic management strategies involve monitoring traffic conditions and making adjustments to traffic operations based on changing conditions. Some of those changing conditions involve traffic incidents, so this category also looks at management strategies that have specific applicability to traffic incidents. These strategies involve improved detection, verification, response, and clearance of crashes, mechanical failures, and other incidents in work zones and on detour routes. This category also includes strategies to provide adequate enforcement of traffic regulations in work zones. Strategies in this area include the ones on the screen.
Suggested Questions: None
Additional Information:
Incident/emergency management coordinator. This strategy provides a designated individual with overall responsibility for incident and emergency management on a project. Responsibilities may include developing incident and/or emergency response plans, overseeing implementation and monitoring of the work zone management strategies, and overall management of incidents or emergencies.
Incident/emergency response plan. This involves the development of a plan with information needed to respond to an incident. This information typically includes roles and responsibilities, response agencies, processes/procedures, actions to take for various incident types and levels, contact information, alternate routes, personnel and equipment information, staging area locations, and other information as appropriate to the individual project.
Dedicated (paid) police enforcement. This strategy provides police patrols in the work zone under a contractual arrangement with the agency or contractor.
Cooperative police enforcement. Cooperative enforcement is similar to dedicated enforcement, except it is implemented through a cooperative agreement between the police and agency.
Automated enforcement. Automated enforcement involves the use of various technologies such as radar, cameras, video, and sensors to detect and record vehicle speed or traffic signal violations. When a vehicle speed exceeds a specified threshold or a red signal violation occurs, the vehicle's license plate and/or driver are photographed. The citation with the photo(s) is then mailed to the registered owner of the vehicle.
Increased penalties for work zone violations. This strategy involves the imposition of increased penalties for speeding or other violations in work zones. Such penalties include increased fines, increased points, license suspension, and even mandatory prison terms for serious violations.

## Slide 34: E. Safety Management Strategies
Described in Part 6 of the MUTCD
Used to enhance safety and mobility in highway work zones
Image: FHWA
Notes: Key Message: Introduce Safety Management Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A fifth category includes safety management strategies. A wide range of other safety devices are described in Part 6 of the MUTCD and are widely used to enhance safety and mobility in highway work zones. These devices, such as temporary traffic barriers and crash cushions, are included in the Work Zone Safety Management Strategies category.
Suggested Questions: None
Additional Information: Refer to http://ops.fhwa.dot.gov/wz/rule_guide/sec6.htm
Possible Problems: None

## Slide 35: E. Safety Management Strategies
Temporary traffic signals
Temporary traffic barriers
Movable traffic barriers
Crash cushions
Rumble strips
Road safety audits
Others
Already
discussed…
Notes: Key Message: Introduce Safety Management Strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Some safety managements strategies are listed on the screen: 1) Temporary traffic signals may be used to avoid the need for flaggers, 2) Temporary traffic barriers may provide positive protection, 3) Movable traffic barriers may also improve the capacity of the roadway, 4) Crash cushions may be used to protect hazards, 5) Rumble strips may help reduce speeds in the vicinity of the work zone, 6) Road safety audits may detect problems before the crashes occur.
Suggested Questions: Can you think of any others? Any experiences with road safety audits?
Additional Information: Refer to http://ops.fhwa.dot.gov/wz/rule_guide/sec6.htm
Possible Problems: Discuss these as needed based on your audience. Be prepared to expand.

## Slide 36: F. Back-of-Queue Strategies
Image: ATSSA
Notes: 36
Key Message: Define the term queue
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A queue by definition is a line of people or vehicles waiting their turn. In the case of vehicles, each is waiting to get through a capacity restriction in a work zone. Queues can extend for miles upstream of the capacity restriction. Prior to a queue, flow can be very unstable. As queues dissipate, the flow is relatively stable.
Suggested Questions: What is the greatest safety risk from a queue? Speed variability, which creates greater rear-end crash risk.
Additional Information: None
Possible Problems: None

## Slide 37: Where are Queues Likely to Occur?
In the advance warning area
Upstream of the advance warning area (more dangerous)
In the traffic space near the work area itself
Image: FHWA
Notes: 37
Key Message: Describe some common issues associated with queues
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: These areas can commonly experience queuing. The advance warning area provides information to motorists and can experience queues due to the downstream taper, for example. Queues may also extend upstream of the advance warning area, and the back-of-queue may extend past the first advance warning sign. Queues may also form adjacent to the work space as equipment moves in and out, causing temporary queuing.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 38: Back-of-Queue Issues
Increased crash risk, particularly rear-end crashes
Potentially large variability in speeds between approaching traffic and queued traffic
Impacts on driver expectations
  May be accustomed to unencumbered travel and
  May have a slower perception-reaction time
Image: FHWA
Notes: 38
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: It is widely recognized that when congestion develops and queues form at the approach to a work zone, the risk of crashes increases, especially on highways where speeds are high and drivers are accustomed to unencumbered travel. These types of conditions may make queuing situations even more difficult for drivers to navigate safely. Queuing can lead to increased rear-end crash risk due to the higher speed of traffic approaching the back-of-queue. The higher the variability in speed, the higher the crash risk. Also, the crash may be more severe with injuries and possibly fatalities due to the high speed variability. According to a study conducted by the Liberty Mutual Research Center for Safety and Health, rear-end collisions account for 31% of crashes that occur at highway construction sites. The same study noted that 26% of crashes involved a stopped or slowing vehicle in the work zone.
Suggested Questions: None
Additional Information: Statistics source – “Motor vehicle crashes in roadway construction work zones”. Accident Analysis and Prevention, Volume 28, Issue 1, January 1996.
Possible Problems: None

## Slide 39: Back-of-Queue Issues
Geometry of roadway
  Limited sight distance to the back-of-queue due to curvature
Impacts from recurring congestion
Multiple public access points
Impacts near work vehicle access/egress points
Image: ATSSA
Notes: 39
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: End-of-queue risks can be compounded by other site-specific conditions, such as limited sight distance and roadway curvature. Recurring congestion may also compound the problem. Roadway geometry may make it difficult for drivers to see a queue in enough time to be able to slow and stop. Access points near a traffic queue may make merge and diverge conditions less safe, and areas near work vehicle access points may also experience greater queue impacts.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 40: Why Should We Analyze Queues?
Analysis can provide valuable insights into the anticipated:
  Length of queue
  Time when queues may occur
  Location of queue
  Variability in traffic speeds
Analysis helps determine potential treatments for the problem
Notes: 40
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Analysis of work zone impacts can help identify when and where queues are likely to occur. This helps to identify when mitigation strategies are needed and which strategies would be appropriate. We will discuss some treatments later. The more knowledge we have about the potential problems and issues, the better we can design treatments for the specific issues.
Suggested Questions: None
Additional Information: None
Possible Problems: We will hold off on discussing treatments until the analysis techniques have been described.

## Slide 41: Analyzing Potential Queues
When the volume to capacity ratio (V/C) exceeds one, a queue forms
Notes: Key Message: Discuss demand as it relates to capacity
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Queues build as traffic demand increases above the capacity of the facility. A volume to capacity (v/c) ratio compares demand to capacity. A v/c ratio is less than one for undersaturated conditions, equal to one for saturated conditions, and greater than one for oversaturated conditions. Demand accurately represents the volume crossing a point on the roadway plus queued vehicles, while volume is simply a traffic count for a given time period. Queues can build rapidly once oversaturated conditions are present.
Suggested Questions: How can you have a v/c ratio greater than 1? It’s because of the stored vehicles in the queue that aren’t processed immediately, making the demand higher than the capacity. If you use traffic counts, do you typically get volume or demand? Typically volume, as the counts for a spot location do not represent the vehicles stored in the queue at the end of the count period. Additional methods or equipment would be needed to measure true demand that includes queued vehicles.
Additional Information: None
Possible Problems: None

## Slide 42: Example: V/C Estimate
This is a rough estimate of the potential for queuing if no other data are available
Notes: 42
Key Message: Discuss how to calculate (roughly) a V/C ratio given planning level data
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a high level analysis meant to illustrate how to calculate a rough estimate of a V/C ratio given only AADT. Begin with AADT, assume a directional split (60% for one direction is used in this example), use the factor 0.10 (commonly 10% of the total daily traffic occurs during the peak hour), estimate a capacity, and then calculate a V/C ratio. One can perform a sensitivity analysis to determine where the V/C break point lies (in this simplistic example, an AADT of 25,000 would reach capacity during the peak hour).
Suggested Questions: What might be an issue with the volumes used in a tool such as this? They may be counts and may not represent true demand. How would you measure demand? Count the vehicles in the queue at the end of the count period and add them to the volume.
Additional Information: None
Possible Problems: None

## Slide 43: Measured Average Work Zone Capacities for Freeways
Normal | Open | vph | vphpl
3 | 1 | 1,170 | 1,170
2 | 1 | 1,340 | 1,340
5 | 2 | 2,740 | 1,370
4 | 2 | 2,960 | 1,480
3 | 2 | 2,980 | 1,490
4 | 3 | 4,560 | 1,520
Source: Highway Capacity Manual
Number of Lanes
Avg. Capacity
Notes: Key Message: Provide example of rough estimates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This table provides example capacities for lane closure scenarios. The columns on the left show how many lanes are open (“open”) from a given original number of lanes per direction (“normal”). The columns on the right show the average capacity for all lanes open (vph) and for each lane (vphpl).
Suggested Questions: How do we account for trucks? Convert them to passenger cars using passenger car equivalents (pce). Generally, a truck is equal to 2 passenger car equivalents. What is a truck (semi, delivery truck, etc.)? Anything with more than four tires touching the pavement (would include a six tire pick-up truck and count it the same in terms of impact as a an eighteen wheel semi!)
Additional Information: This report is from 1985 but the data is still applicable. Some newer values are shown with an asterisk from the 2000 HCM.
Possible Problems: Some may be familiar with numbers such as approximately 2,400 vphpl as capacity. The 2,400 number is an ideal capacity (no trucks, level terrain, shoulder, etc.). The numbers on this table are MEASURED capacities, so these numbers are more accurate (however some are based on limited observations). TRB Special Report 209 is the Highway Capacity Manual.
43

## Slide 44: Ohio-DOT Permitted Lane Closure Spreadsheet (PLCS)
Image: Ohio DOT
Notes: Key Message: Discuss, as an example, the Ohio Department of Transportation Permitted Lane Closure Spreadsheet (PLCS) Tool
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Some agencies have developed lane closure policies, lane closure analysis tools, or permitted lane closure maps that guide lane closure decisions.
This tool allows ODOT to determine if queues exceed their threshold. Unless the queue can be completely eliminated, they can estimate where it will end and determine the appropriate mitigation strategies. It is one example of how demand can be compared to capacity to determine whether or not queuing may occur. The capacity per lane is 1490 vphpl (a “spot” location) for this particular example. When the table shows a demand higher than 1490 vphpl and queues are expected to exceed the tolerance level, lane closures are not permitted during those time periods.
Suggested Questions: What might be an issue with the volumes used in a tool such as this? They may be counts and may not represent true demand. What would a queue estimate allow us to do differently than without it? It would let us place signs further upstream or add signs to the traffic control plan as an example of one specific treatment.
Additional Information: http://plcm.dot.state.oh.us//plcm/plcm_web.jsp.
Possible Problems: None

## Slide 45: Traffic Analysis Considerations
Seasonal variation
Demand fluctuation
Fluctuation within the peak hours or peak periods
Data accuracy
Image: FHWA
Notes: Key Message: Discuss considerations when performing an analysis
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Assess data as part of the planning process to determine the type of analysis that is feasible given the adequacy and coverage of the data. The analysis is only as good as the data used to predict impacts from lane closures, for example. Analysis using good data will help determine the extent of the impacts (such as whether or not queuing may exist for long periods of time). Additionally, understanding the limitations of the data can help determine the best analysis technique to use. Students may realize that data from congested time periods will underestimate demand and skew the analysis.
Suggested Questions: What might cause fluctuation during a peak hour? An example would be a plant shift letting out and flooding the network for a short time period. We account for this using the peak hour factor.
Additional Information: None
Possible Problems: None

## Slide 46: A Process-Oriented Approach
Comparison
of Alternatives
Design
Detailed
Analysis
Notes: 46
Key Message: Discuss the process for determining the best design
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Analysis of data will help understand potential issues for the project. The analysis produces specific metrics and measures for each alternative that can then feed into detailed design, staging, other requirements, and traffic control plan development.
Suggested Questions: Why is this a cycle? Due to the fact that there may be more than one alternative requiring more refined analysis at the design stage.
Additional Information: None
Possible Problems: None

## Slide 47: Choosing Mitigation Strategies
Once potential impacts are understood, appropriate strategies can be evaluated
Analyzing impacts can help determine the need for strategies
Design solutions that are tailored to solve a specific problem
Image: ATSSA
Notes: Key Message: Introduce mitigation strategies
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Several different mitigation strategies can be considered to lessen impacts from road work. Planning-level analysis can help eliminate alternatives that would cause impacts above a tolerance threshold. Once impacts are known and quantified, mitigation techniques can be designed into the project. This occurs when the best alternative still has some potential issues that are unavoidable but can be treated.
Suggested Questions: Are there techniques used in your state to mitigate impacts?
Additional Information: None
Possible Problems: None

## Slide 48: Types of Strategies
Reducing/eliminating the end of queue
Strategies to treat the end of the queue
Communications techniques to improve awareness of impacts for enhanced trip planning
Image: FHWA
Notes: 48
Key Message: Discuss types of strategies to mitigate back-of-queue issues
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Ideally we eliminate the queue to the degree we can through good design, time of day restrictions, etc. For remaining queues, we provide treatment and motorist awareness to mitigate the impacts. We will go into these strategies more on the next slides.
Suggested Questions: What types of strategies have you used? How did they work?
Additional Information: None
Possible Problems: None

## Slide 49: Queue Reduction/Elimination - Nighttime Construction
May reduce or eliminate a queue that would normally occur during the day
Image: FHWA
Notes: 49
Key Message: Discuss the use of nighttime construction (may also be referred to as “off peak” work)
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Performing construction during nighttime hours, when traffic demand is lower, can reduce the frequency of queuing as compared with daytime work, when traffic demand is higher, and the potential for queuing is greater. It is becoming more and more common especially in urban areas. Analysis can help determine when nighttime work may alleviate back-of-queue issues that might occur if work were performed during daytime hours. Agencies may also reduce or eliminate queues by maintaining the same number of lanes during construction as prior to construction (by reducing lane widths, for example) or by increasing the length of taper or changing the location of the beginning of the taper.
Suggested Questions: What are some trade-offs to working at night compared with daytime? Noise issues, visibility, drowsy drivers, impaired drivers, limited work durations, and others. These considerations should be part of the decision-making process.
Additional Information: None
Possible Problems: None

## Slide 50: End of Queue Treatment – TTC Setup
Important for alerting motorists of any potential hazards
Evaluate warning sign spacing
  Extend if warranted
Possibly law enforcement personnel
Image: ATSSA
Notes: 50
Key Message: Discuss the importance of proper setup of temporary traffic control devices
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Proper design and installation of devices is important. For example, sign spacing guidelines from the MUTCD may be exceeded to account for long queues. Drivers approaching the queue have the appropriate advanced warning of the potential hazard downstream. By analyzing impacts, designers can exceed the MUTCD sign spacing requirements and locate the advance warning signs upstream of the back-of-queue.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 51
In Advance Warning Area
  NOT IN BUFFER
On the shoulder
Between the 2nd & 3rd sign
  Where we need the motorists to pay most attention to what they need to do ahead
Consider facing traffic
  Headlights OFF
  Emergency lights ON
TROOPER SHOULD BE HERE!
Use of Law Enforcement
Image: ATSSA
Notes: Key Message: Discuss the use of law enforcement personnel
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: Law enforcement vehicle appears on click.
Suggested Comments: Law enforcement personnel may provide presence as opposed to active enforcement. We focus on presence / visibility as a mitigation technique. For positioning, one state has a policy to have the officer between the 2nd and 3rd sign, on the shoulder, facing traffic, headlights off, emergency lights flashing. This is when motorists are about to make their maneuvers. If safe, the officer will move upstream with the queue as it builds to provide visibility in advance of the back-of-queue. Obviously this is situation specific and local agency policy should guide such a practice. We are emphasizing that this is one example, and not a requirement.
Suggested Questions: What is your policy? What do you think about this example?
Additional Information: There is little information on this. This is what one state (Louisiana) is doing. This is not required by the MUTCD or any standard that we are aware of.
For incidents, the MUTCD defines “Safe-Positioned” as the positioning of emergency vehicles at an incident in a manner that attempts to protect both the responders performing their duties and road users traveling through the incident scene, while minimizing, to the extent practical, disruption of the adjacent traffic flow. Possible Problems: This is a suggestion only and varies by location.
Suggested Comments: This is what we recommend. Remember each case is different and that judgment is involved. Use common sense! We recommend what’s on the slide: FACING TRAFFIC before the 2nd and 3rd sign. This is when motorists are about to make their maneuvers.
Suggested Questions: Why facing traffic? Advantages? Disadvantage? See following slide.
Additional Information: There is little information on this. This what one state (Louisiana) is doing. This is not required by the MUTCD or any standard that we are aware of.
Possible Problems: This may be controversial. Be prepared to defend your suggestion (see next slide). Do not argue. This is a suggestion only.

## Slide 52: Why Face Traffic?
May relocate up the shoulder to prevent back of queue crash
Larger field of view
Engine and air bag provide protection
  Not the gas tank!
Escape route
More effective
Image: ATSSA
Notes: Key Message: Discuss why we suggest to face traffic.
Est. Presentation Time: 2 minutes
Explanation of Cues/Builds: Text box appears on click.
Suggested Comments: These are the advantages of facing traffic. The disadvantages would be opposite.
Suggested Questions: None
Additional Information: Pay attention to traffic!
Possible Problems: This may be against their practices. Make your point as a recommendation and be prepared to defend it.

## Slide 53: End of Queue Treatment – Intelligent Transportation Systems
Image: FHWA
Notes: 53
Key Message: Discuss the use of Intelligent Transportation Systems in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ITS can be used for mobile traffic monitoring and management. Some systems are active (physically control traffic such as the dynamic lane merge system) while others are passive (provide general information). Advance warning of slow or stopped traffic ahead may alleviate back-of-queue issues. Queues can be monitored by ITS technologies (sensors, cameras, etc.) that provide enhanced information to practitioners for decisions about the appropriate treatments to implement.
Suggested Questions: None
Additional Information: Examples include the CB Wizard system that alerts truck drivers to work zone issues, Dynamic Early Merge systems that create an enforceable “Do Not Pass When Flashing” zone, Late Merge systems that use both lanes but guide motorists to take turns at the merge point, real-time information systems that provide motorists with work zone congestion and delay information, and variable speed limit systems that can flatten the speed variability approaching the work zone by changing the posted speed in real-time.
Possible Problems: Researching some examples and spending a few minutes discussing issues and potential ITS solutions may be warranted.

## Slide 54: End of Queue Treatment – Dynamic Lane Merge System
Image: ATSSA
Notes: 54
Key Message: Discuss the use of Dynamic Lane Merge Systems in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Dynamic Lane Merge Systems actively control traffic in advance of the taper. They have benefits such as reduced aggressive maneuvers at the merge point and supplemental advance warning information. Traffic is lined up into one lane so that smoother traffic flow occurs prior to the lane closure. It may also help draw extra attention to an area where queuing potential may occur.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 55: End of Queue Treatment – An Example From South Carolina
Some projects require truck-mounted PCMS to display queue warnings
  TMA with operator shall be placed on the shoulder
  PCMS shall be 2,000 feet in advance of queue
Notes: 55
Key Message: Discuss truck mounted PCMS to display queue warnings in South Carolina
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: South Carolina DOT has a policy on use of truck mounted PCMS to display queue warnings. An excerpt from the policy is shown below:
1. The contractor shall provide a truck mounted changeable message sign for each lane closure when development of a traffic queue is evident. The contractor shall utilize the sign to provide advance notice to motorists that the motorists are approaching a traffic queue and should be prepared to stop.
2. The contractor shall place a truck mounted changeable message sign manned with an operator at all times on the shoulder of the roadway immediately upon the development of a traffic queue. The truck mounted changeable message sign shall remain no less than 2,000 feet in advance of the traffic queue at all times. Placement of the truck on the shoulder of the roadway without an operator is prohibited.
3. The contractor shall include a truck mounted attenuator only on vehicles over 5,000 lbs GVW.
4. The department requires the contractor to be prepared to stop work immediately and remove the lane closure if a TMA is unable to be provided in advance of a queue.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 56: End of Queue Monitoring – Portable or Permanent Cameras
Images: ASTI
Notes: 56
Key Message: Discuss the use of closed circuit television cameras in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Closed Circuit Television (CCTV) cameras can be used to monitor queues in and around work zones. As the queue grows, temporary traffic control personnel can monitor the camera images and implement strategies such as adjusting sign locations and spacing. Such CCTV devices can be portable or be part of a permanent ITS deployment. The ones shown here are portable, with a solar platform. Video, weather, and traffic sensors can also be combined on the same platform with wireless communications.
Suggested Questions: None
Additional Information: The pictures shown here are courtesy of Noah Jenkin of ASTI (an ITS vendor). The CCTV cameras are not required for the portable ITS system in operation in the location where these photos were taken, but they are an enhancement to the ITS deployment that allows for queue monitoring and manual adjustments to traffic control.
Possible Problems: None

## Slide 57: Public Information and Outreach
Project flyers
Websites
Marketing materials
Signs
Alternate route information
Traveler information
Traffic reports
Notes: 57
Key Message: Discuss types of public information and outreach strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Many agencies provide advance information to motorists in the form of brochures, websites, and via other marketing materials. Agencies also use the media to provide information to motorists on upcoming construction projects and alternate routing, especially those with lane closures. Some additional information will likely have more of an effect on queue issues compared with general information sources such as brochures and flyers. Information may include travel times, delay, general messages on work zone conditions, and may warn motorists of potential hazards ahead. It may also include information on alternate routes or alternate means of transportation during the construction period. Sections 6I.02 and 6I.03 of the MUTCD recommend warning signs in advance of the end of queue for incidents.
Suggested Questions: What types of strategies have you used? How did they work?
Additional Information: None
Possible Problems: None

## Slide 58: Work Zone Inspection – An Example from Maryland SHA
Includes multiple aspects of TTC operations
  Devices
  Queuing
Checklist that include:
  Work zone impacts
  ITS
  TO strategies
  Etc.
Notes: 58
Key Message: Discuss the role of inspection in queue identification and mitigation
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Queues may occur that were not anticipated prior to construction, or the queue may be longer than anticipated. Inspection plays an important role in queue verification and response. Inspectors can use a checklist, similar to the one described for Maryland, to note information about the queues and relay the information to the appropriate people for potential field modifications of temporary traffic control or other treatments and strategies.
The Maryland SHA (MdSHA) Work Zone Analysis Guide provides guidance to designers and other staff on work zone traffic analysis methods. The guide has two sections: one focuses on arterials and the other focuses on freeways. Each section presents guidance and information on mobility thresholds, traffic analysis tools, determining the study network, data collection, traffic modeling, and the recommended analysis procedure. The analysis procedure MdSHA uses for both arterials and freeways is similar, beginning with determining the objective of the analysis, then collecting all necessary data, modeling existing conditions and alternatives, determining if the alternative meets mobility thresholds, and recommending an alternative.
To help with the analysis, MdSHA developed several tools, including MD-QuickZone (a modified version of FHWA's QuickZone tool) and the Lane Closure Analysis Program (LCAP). After evaluating all feasible alternatives for work zone configurations and potential mitigation measures, MdSHA recommends that the results of the impacts analysis be summarized in a report, along with the justification for the alternative selected. The guide includes a template for the impacts analysis report, examples of analysis reports for several different types of projects, and a checklist to help ensure that the analysis is complete and has considered all necessary factors. The MdSHA Work Zone Safety and Mobility Web Site provides additional resources for implementing the Rule.
Suggested Questions: None
Additional Information: Temporary Traffic Control Inspection Form (MD SHA): http://www.sha.maryland.gov/OOTS/14AppETTCInspectionFormmastercopyRev2.pdf
Possible Problems: None

## Slide 59: Knowledge Check
Name two ITS strategies applicable to work zones
Name 2 demand management strategies
Name 2 incident management strategies
How can we minimize back-of-queue crashes?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.

## Slide 60: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at your questions.
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: None