## Slide 1: 5. Identifying and Evaluating Alternative Work Zone Strategies
Work Zone Strategies
https://patch.com/pennsylvania/northwhitehall/coplay-creek-road-closed-for-repairs_345b7cce
Notes: Key Message: Module Opening
Est. Presentation Time: As needed
Explanation of Cues/Builds: None
Suggested Comments: Let’s move to the next module. In this module {name}, we will.. {next slide}
Suggested Questions: None
Possible Problems: None

## Slide 2: Module Objectives
  Discuss work zone impacts assessment
  Discuss factors for identifying and evaluating WZ strategies
  Discuss strategies used in developing an effective TMP
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are the objectives of this module.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Work Zone Impacts Assessments
A comprehensive, integrated and proactive work zone management and design effort
Notes: Key Message: Discuss work zone impacts assessments
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A WZ Impact Assessment is comprehensive, integrated and proactive work zone management and design effort
Suggested Questions: When is this assessment needed? Turn into a discussion.
Additional Information: None
Possible Problems: None.

## Slide 4: What is Work Zone Impacts Assessment?
The process of understanding the safety and mobility impacts of a road construction/ maintenance/ rehabilitation project
Notes: Key Message: Discuss Work Zone Impacts Assessment
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Factors that will influence the level of impacts caused by a work zone include traffic conditions and characteristics, project characteristics, geographic/physical features, and aspects of the surrounding area (e.g., alternate routes, nearby businesses). The assessment process may involve a high-level, qualitative review of these factors for some projects, and a detailed quantitative analysis using modeling and/or simulation tools for other projects.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 5: Work Zone Impacts Assessment
An Approach to Assess and Manage Work Zone Safety and Mobility Impacts of Road Projects
Developed by FHWA to provide guidance
Image: FHWA
Notes: Key Message: Introduce Work Zone Impacts Assessment Report
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The purpose of this document is to provide guidance to practitioners on developing and/or updating procedures to assess and manage the work zone impacts of their road projects. This document presents a general approach for conducting work zone impacts assessment and management. This approach is not the only way to perform work zone impacts assessment, and is not intended to advocate a “one-size-fits-all” approach.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Note: Only the impacts assessment portion of the TO section is based on this report.
Possible Problems: None

## Slide 6: Work Zone Impacts Assessment Constitutes:
Assessing the likely work zone impacts
Developing appropriate TMPs
Monitoring the actual impacts
Making adjustments to the TMP
Conducting performance assessments
Identifying trends towards overall improvement of work zone:
  Policies
  Procedures and practices
Notes: Key Message: Discuss Work Zone Impacts Assessment
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Assessing the likely work zone impacts and developing appropriate work zone transportation management plans (TMPs) during project development and delivery.
• Monitoring the actual impacts of the project and making adjustments to the TMP (if necessary) during project implementation.
• Conducting performance assessment to track performance, document lessons learned, and identify trends towards overall improvement of work zone policies, procedures, and practices.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 7: Work Zone Impact Assessment Process
Policy level
System planning
Preliminary engineering
Design
Construction/Implementation
Performance assessment
Maintenance & operation
Let’s discuss..
Notes: Key Message: Discuss the Components of WZ Impact Assessment Process
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: WZ impacts can be assessed during all phases of the project. Let’s discuss these components.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 8: 1. Addressing Work Zone Impacts at the Policy-Level
To facilitate streamlined decision-making and consistency
To help standardize work zone practices that are known to work
To serve as a guide for planning, designing, and constructing road projects
To gain management support buy-in
Notes: Key Message: Addressing WZ Impacts at the Policy-Level
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None.

## Slide 9: 2. Work Zone Impacts Assessment During Systems Planning
To identify transportation systems needs and deficiencies
To develop and evaluate alternative improvement solutions
To compile plans and programs for implementing the solutions
Notes: Key Message: WZ Impacts Assessment During Systems Planning
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Systems planning is the stage of program delivery where planning for the future is carried out by identifying transportation systems needs and deficiencies, developing and evaluating alternative improvement solutions, and compiling plans and programs for implementing the solutions. Systems planning is conducted at several levels including Statewide, regional, metropolitan, county, local, and corridor. The process is both interactive and iterative, with participation and feedback from concerned public and private organizations, other interested parties, and the general public.
Suggested Questions: None
Additional Information: Quantitative analysis of work zone impacts may not be possible during systems planning due to inadequate project detail and lack of data. In such
cases, the particular issue under investigation may be noted so that the staff that conduct assessments in subsequent phases are made aware of the issue.
Possible Problems: None.

## Slide 10: Analyze Potential Impacts with Analytical Tools
Suitable tools are available
A quantitative analysis may:
  Be performed at the WZ, corridor, and/or network levels
  Be combined with an ongoing project
  Not be possible during systems planning stage
Notes: Key Message: Introduce WZ Analysis Tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Suitable tools are available & are applicable to the project. Quantitative analysis of work zone impacts may not be possible during systems planning due to inadequate project detail and lack of data. In such cases, the particular issue under investigation may be noted so that the staff that conduct assessments in subsequent phases are made aware of the issue.
Suggested Questions: None
Additional Information: Refer students to the Work Zone Analysis Tools course.
Possible Problems: None

## Slide 11: When to Consider Analytical Tools
The project is definitely a “significant project”
It may be “significant”
To help choose between multiple TMP approaches
To justify additional funds
Notes: Key Message: Introduce WZ Analysis Tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Suitable tools are available & are applicable to the project. You should consider using these tools to analyze the impacts of the work zone.
Suggested Questions: None
Additional Information: Refer students to the Work Zone Analysis Tools course.
Possible Problems: None

## Slide 12: Work Zone Analysis Tools
Traffic simulation
Deterministic
Estimation
Notes: Key Message: List various work zone impact analysis tools.
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are tools available to help us assess the impact on the work zone on traffic. Concurrent with selecting study objectives, the appropriate analysis tools should be selected. There are many tools available to address work zones, as discussed further in the next sections of
this Guide. The available tools range from simple to complex. Simpler tools include Highway Capacity Manual techniques and sketch planning while more complex tools include macro, meso and microscopic simulation tools. Choosing a tool is generally a tradeoff between desired
functionality, results, time, training and cost. They can be grouped in these 3 categories. Let’s discuss them!
Suggested Questions: None
Additional Information: None
Possible Problems: This is an intro slide. The 3 categories are discussed in detail in the new few slides.

## Slide 13: Traffic Simulation
A great tool to assess the impact of the work zone on traffic flow BEFORE construction begins
Enables adjustments to design
Stochastic, microscopic
Great for public hearings!
Image: FHWA
Notes: Key Message: List various work zone impact analysis tools.
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Traffic simulation is a viable tool. There are various packages available. One of them is CORSIM, which is part of TSIS (Traffic Software Integrated System (TSIS) and developed by FHWA. CORSIM is available from McTrans. It requires lots of data so it may be overkill for some projects.
Suggested Questions: None
Additional Information: http://mctrans.ce.ufl.edu/featured/tsis/version5/corsim.htm. The Traffic Software Integrated System (TSIS) is a collection of software tools for use by traffic engineers and researchers. Originally built as a simple shell around CORSIM, TSIS has evolved into a sophisticated toolkit. Though used by the FHWA for conducting research, these tools are sold to the public. CORSIM is a comprehensive microscopic traffic simulation, applicable to surface streets, freeways, and integrated networks with a complete selection of control devices (i.e., stop/yield sign, traffic signals, and ramp metering). It simulates traffic and traffic control systems using commonly accepted vehicle and driver behavior models. CORSIM combines two of the most widely used traffic simulation models, NETSIM for surface streets, and FRESIM for freeways. CORSIM has been applied by thousands of practitioners and researchers worldwide over the past 30 years and embodies a wealth of experience and maturity.
Possible Problems: Try to familiarize yourself with these tools before the course. Keep this brief.

## Slide 14: Available Simulation Tools
CORSIM
VISSIM
PARAMICS
Syncho/ SimTraffic
Others
Image: PTV Group
Notes: Key Message: Available Simulation Tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As with any type of traffic analysis, there are several models that could be used to evaluate traffic conditions under work zone operations, such as Critical Lane Volume (CLV) analysis, simulation models such as CORSIM, VISSIM, PARAMICS or SimTraffic, and Highway Capacity Manual (HCM) based tools such as HCS or Synchro. The Synchro / SimTraffic software package is the recommended traffic analysis tool. work zone applications on arterials since many of Maryland’s arterials have already been coded using Synchro and Synchro can calculate LOS, control delays and travel times directly, based on user inputs. Also, simulation analysis can be easily performed with SimTraffic.
Suggested Questions: None
Additional Information: For a complete presentation of traffic analysis tools, see the Federal Highway Administration’s Traffic Analysis Toolbox, available online at http://ops.fhwa.dot.gov/trafficanalysistools/toolbox.htm.
Possible Problems: This is an intro slide. The 3 categories are discussed in detail in the new few slides.

## Slide 15: CORSIM Screen
Closed lane
“Rubbernecking”
Image: FHWA
Notes: Key Message: Show sample CORSIM screen
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a CORSIM screen shot. It shows a closed lane (left) and a right lane being affected by rubbernecking, or a drop in capacity. CORSIM cannot simulate a taper, however. For the condition being simulated, CORSIM will generate a series of PMs (Measures of Effectiveness) such as average speed, delays, and others.
Suggested Questions: None
Additional Information: http://mctrans.ce.ufl.edu/featured/tsis/version5/corsim.htm. NOTE: CORSIM can only simulate closures on freeways.
Possible Problems: Try to familiarize yourself with these tools before the course.

## Slide 16: Deterministic (e.g., QuickZone)
Same results for same data
Quantifies work zone delays and delay impacts of alternative plans
http://ops.fhwa.dot.gov/wz/traffic_analysis/wzta.htm
Image: FHWA
Notes: Key Message: Discuss QuickZone
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second category of tools are deterministic tools. These analytical tools are always give the same result for a given set of input data. One example of a deterministic tool is QuickZone, developed by FHWA and available through McTrans. Its data requirements are not as intense as CORSIM’s but it gives you a quick (hence the name) analysis of the work zone. Refer to the website shown for additional information.
Suggested Questions: What is deterministic? For the same input always gives the same result. “Stochastic” models are random: for the same input they may generate different results (like in real life).
Additional Information: http://ops.fhwa.dot.gov/wz/traffic_analysis/wzta.htm
Possible Problems: When the tool is “quick”, someone may say we are compromising accuracy. This is a fair statement but this is the compromise that we need to make in order to work faster (and cheaper!). The user must be aware of this compromise and should not demand a high degree of accuracy.

## Slide 17: QuickZone
“Quickly” compares work zone mitigation strategies
Estimates:
  Costs
  Queues
  Delays
  Potential backups
Image: FHWA
Notes: Key Message: Introduce QuickZone
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: QuickZone compares the traffic impacts for work zone mitigation strategies and estimates the costs, traffic delays, and potential backups associated with these impacts. For example, if a highway agency planned to widen a shoulder, QuickZone could estimate the costs of doing work at night instead of during the day or diverting the traffic to one road versus another road during different phases of construction. The costs, traffic delays, and potential backups can be estimated for both an average day of work and for the whole life cycle of construction.
The primary functions of QuickZone are:
-Quantification of corridor delay resulting from capacity decreases in work zones.
-Identification of delay impacts of alternative project phasing plans.
-Supporting tradeoff analyses between construction costs and delay costs.
-Examination of impacts of construction staging, by: - location along mainline - time-of-day (peak vs. off-peak) - season (summer vs. winter)
-Assessment of travel demand measures and other delay mitigation strategies.
-Allowing the establishment of work completion incentives.
Suggested Questions: None
Additional Information: Refer students to the Work Zone Analysis Tools course.
Possible Problems: None

## Slide 18
Sample QuickZone Output
Source: FHWA
Notes: Key Message: QuickZone results are easy to interpret.
Est. Presentation Time: One minute.
Explanation of Cues/Builds: None.
Suggested Comments: This is a sample QuickZone output. The graph plots delay against time of day for different phases, which are designated by different colors. The total delay, in vehicle-hours, and maximum queue length, in number of vehicles, are tabulated for each phase on the right hand side.
Suggested Questions: None.
Additional Information: None.
Possible Problems: None.

## Slide 19
Supports the integrated analysis of project alternatives for:
  Different pavement design
  Construction logistics
  Traffic operations options
CA4PRS (Construction Analysis for Pavement Rehab. Strategies)
Image: Caltrans
Notes: Key Message: Discuss CA4PRS
Est. Presentation Time: Less than 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: CA4PRS is a schedule and traffic analysis tool that helps planners and designers select effective, economical rehabilitation strategies. Funded through an FHWA (Federal Highway Administration) pooled-fund, multistate consortium (California, Minnesota, Texas, and Washington), CA4PRS was developed by the University of California Pavement Research Center (UCPRC) through the UC Berkeley Institute of Transportation Studies. FHWA formally endorsed CA4PRS as a “Priority, Market-Ready Technologies and Innovations” product in 2008 for national wide deployment. Caltrans IT recently added CA4PRS into the standard software list for its statewide implementation.
Suggested Questions: None
Additional Information: http://www.dot.ca.gov/research/roadway/ca4prs/index.htm
Possible Problems: Try to familiarize yourself with these tools before the course.

## Slide 20
A dynamic traffic assignment analysis tool that can be used to support decision making for regional work zone management
Dynasmart-P
Image: FHWA
Notes: Key Message: Discuss Dynasmart-P
Est. Presentation Time: Less than 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Another available tool is DYNASMART-P, a state-of-the-art planning tool that engineers can use to address complex transportation planning and operations issues simultaneously. Researchers at the University of Maryland developed the software under the Federal Highway Administration's (FHWA) Dynamic Traffic Assignment research project. Version 1.0 of DYNASMART-P is available from the Center for Microcomputers in Transportation (McTransTM) at http://mctrans.ce.ufl.edu/featured/dynasmart/index.htm. In addition, FHWA recently completed testing of an updated version of the software, which is available from McTrans. The new version reduces the computer memory required for using the software and includes new features, such as a pricing element that enables planners to specify a toll that depends on the time of day.
Suggested Questions: None
Additional Information: http://www.tfhrc.gov/trnsptr/jun06/index.htm#opera
Possible Problems: Try to familiarize yourself with these tools before the course

## Slide 21: Estimation: e.g., Time of Day Fluctuations
0
200
400
600
800
1000
Cap.=1,000 vph
Cap.=500 vph
Congestion periods!
Congestion periods!
Time of Day
Source: FHWA
Notes: Key Message: Discuss WZ Impact Analysis
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears upon click
Suggested Comments: Another way to determine the impact of the WZ is through estimation. In this example, capacity of the roadway was 1,000 vehicles per hour was before a closure, resulting in no congestion. With the closure, the capacity DECREASED to 500 vph, resulting in two congestion periods during the shown time of day.
Suggested Questions: None
Additional Information: None
Possible Problems: “cap” is “capacity”, or how many vehicles go through a point over a period of time, in this case in vehicles per hour.

## Slide 22: Methodology for Selecting a Traffic Analysis Tool
FHWA has developed detailed guidance/tools for selecting a traffic analysis tool
Traffic Analysis Toolbox is a great resource!
Image: FHWA
Notes: Key Message: Discuss the methodology for selecting traffic analysis tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The selection of any traffic analysis tool should align the purpose and objective of the analysis with the capabilities and limitation of the tool. From a project administrative perspective, there are several technical, time requirements and budget factors which come into play, as does the availability of the associated data. Volume II: Decision Support Methodology for Selecting Traffic Analysis Tools is a good resource. This volume identifies key criteria and circumstances to consider when selecting the most appropriate type of traffic analysis tool for the analysis at hand. The audience for this volume are project managers and project engineers. Volume VIII is intended to provide the local decision-maker with a broad, fundamental understanding of how analytical tools can be used to support work zone decision making throughout an entire project life cycle. The guidance is rooted in an overall philosophy that "one size does NOT fit all" with respect to the best analytical approach, that is, no single tool or analytical approach is the right answer for all work zone analyses. Work zones are associated with a vast range of road work activities, ranging from multi-billion dollar mega-projects to emergency pothole repair. Further, mobility impacts can be an issue for projects on almost any type of facility ranging from low-volume rural roadways to highly congested urban freeway interchanges. Volume IX provides specific guidance to the analyst, researcher, or manager in charge of conducting a specific work zone analysis project or who has been charged with developing an overall work zone modeling program or approach. This volume includes numerous case study examples, discussion and analysis designed to provide the prospective work zone analyst with information pertaining to the selection of a transportation modeling approach (including the identification of opportunities for use, managing technical risk and examples) as well as specific project applications (including constructability, scheduling and transportation management plan design and evaluation).
Additional Information: http://ops.fhwa.dot.gov/trafficanalysistools/index.htm. An introduction to the role of traffic analysis tools and tool categories is provided. A set of criteria for selecting the appropriate type of traffic analysis tool is described in detail and each tool category is scored as to its relevance to the criteria. The criteria include the analysis context, study area, facility type, travel mode, management strategy, traveler response, performance measures, and cost-effectiveness. A process and worksheets for an analyst to rate a tool category for a particular transportation analysis task are presented based on the criteria and the analyst's weighting of the criteria. Some challenges and limitations of the use of traffic analysis tools are provided.
Possible Problems: None

## Slide 23: 3. Work Zone Impacts Assessment During Preliminary Engineering
Early project-level planning
Develop an overall design concept
Identify ways to implement the project
Develop design concepts
Notes: Key Message: Discuss WZ Impacts Assessment During Preliminary Engineering
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Preliminary engineering is the first stage in project development. This is the stage when designers and project planners conduct early project-level planning and develop an overall design concept of what the new facility would look like. At this stage, projects that are identified in systems planning are handed over to the respective project planners and designers to further develop the project. The main objective is to identify ways to implement the project, and develop appropriate plans and design concepts. Therefore, during preliminary engineering more project-specific information is collected and synthesized.
Suggested Questions: None
Additional Information: Preliminary engineering is also referred to as the first stage of design.
Possible Problems: None

## Slide 24: A4. Work Zone Impacts Assessment During Design
Plans, documents, specifications, & cost estimates
How the project will be built, implemented and managed
Notes: Key Message: Discuss WZ Impacts Assessment During Design
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Design represents the stage in program delivery where the final design is conducted for the project and appropriate plan documents, specifications, and cost estimates are developed. These documents lay out exactly how the project will be built, what the issues are, and how the work zone will be implemented and managed. WZ impacts assessment can be done during the design stages of a project. When we consider the traffic impact of the work zone, it may lead to an entirely different way to manage traffic, considering other alternatives.
Suggested Questions: None
Additional Information: Preliminary engineering and the subsequent design stages are generally performed by similar staff, i.e., project planners and designers belonging to the design/engineering departments of transportation agencies, either at the central office or the region/district level.
Possible Problems: None

## Slide 25: 5. Work Zone Impacts Assessment During Construction
The project is actually built in the field
Decisions made during:
  The planning
  Preliminary engineering, and
  Design stages are implemented
Image: ATSSA
Notes: Key Message: Discuss WZ Impacts Assessment During Construction
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: During construction, agencies focus on implementing the TCP, managing the construction project, facilitating safety for motorists and workers, and maintaining traffic through the work zone. Recordkeeping of day-to-day project activities and tracking of project progress is performed using field diaries and project logs.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 26: 6. Performance Assessment
Evaluation of work zone:
  Policies
  Processes
  Procedures, and
  Work zone impacts aids
Feedback to make program improvements
Evaluation of the effectiveness of work zone management strategies
Notes: Key Message: Discuss Performance Assessment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are four key measures of work zone performance:
• Safety.
• Mobility.
• Construction efficiency and effectiveness.
• Public perception and satisfaction.
Where feasible and appropriate, these performance measures should be evaluated quantitatively. In the absence of funding and/or data availability, measures of performance may be evaluated qualitatively.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 27: Project Assessment Steps
Collect project information
Collect public perceptions/stakeholder inputs
Assess project-level performance
Synthesize & analyze data for program-level assessment
Evaluate/revise WZ impacts assessment
Management process & practices
Notes: Key Message: Discuss Project Assessment Steps
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Most of the data needed for the project-level assessment should be available from each project’s monitoring efforts including field observations, crash data, and operational data. It is important that traffic and safety monitoring data collected during construction be documented and maintained in a consistent manner for each project.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 28: Work Zone Performance Measures (PMs)
What makes one work zone strategy better than another one?
  Less delay?
  Shorter duration?
  Shorter queues?
  Safety?
  Shorter duration?
These are performance measures!
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: What makes one work zone strategy better than another one
-Less delay?
-Shorter duration?
-Shorter queues?
Suggested Questions: How can you assess which is the best strategy? What are your objectives?
Additional Information: None
Possible Problems: None

## Slide 29: Possible WZ Performance Measures (PMs)
What are the PMs that are important to you and your objectives?
Important to set acceptable levels
  Example: Certain LOS requires night work
Let’s look at typical work zone PMs
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: What are the PMs that are important to you and your objectives?
Important to set acceptable level. Example: Certain LOS requires night work. Let’s look at typical WZ PMs
Suggested Questions: How can assess which is the best strategy? What are your objectives?
Additional Information: None
Possible Problems: None

## Slide 30: Level of Service (LOS):
The conditions within a traffic stream, based on service measures such as speed and travel time, freedom to maneuver, traffic interruptions, comfort, and convenience.
Ranges from LOS A (best) to LOS F (worst)
A B C D E F
Image: ATSSA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: LOS refers to the conditions within a traffic stream, based on service measures such as speed and travel time, freedom to maneuver, traffic interruptions, comfort, and convenience. Ranges from LOS A (best) to LOS F (worst). E is capacity (next slide). The Highway Capacity Manual and AASHTO -Geometric Design of Highways and Streets ("Green Book") list the following levels of service: A= Free flow B=Reasonably free flow C=Stable flow D=Approaching unstable flow E=Unstable flow F=Forced or breakdown flow
Suggested Questions: None
Additional Information: Note: LOS is a HCM concept which may not be referenced in traffic models.
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 31: LOS E = V/C = 1 = Capacity
Maximum hourly rate at which vehicles or persons can reasonably be expected to traverse a point on a lane during a given period of time under prevailing roadway, traffic and control conditions
A B C D E F
Image: ATSSA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Capacity is defined as the maximum hourly rate at which vehicles or persons can reasonably be expected to traverse a point on a lane during a given period of time under prevailing roadway, traffic and control conditions
Suggested Questions: None
Additional Information: Note: LOS is a HCM concept
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 32: Speed Flow Relationships
Image: TRB
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These curves depend on the prevailing traffic and roadway conditions on the segment under study and on its length in determining density. The curves illustrate several significant points:
A zero flow rate occurs under two different conditions: One is when there are no vehicles on the facility—density is zero, and flow rate is zero. And the second is when density becomes so high that all vehicles must stop—the speed is zero, and the flow rate is zero. The density at which all movement stops is called jam density, denoted by Dj in the diagrams.
As flow increases from zero, density also increases, since more vehicles are on the roadway. When this happens, speed declines because of the interaction of vehicles. This decline is negligible at low and medium densities and flow rates.
As density increases, these generalized curves suggest that speed decreases significantly before capacity is achieved. Capacity is reached when the product of density and speed results in the maximum flow rate. This condition is shown as optimum speed So (often called critical speed), optimum density Do (sometimes referred to as critical density), and maximum flow vm.
The slope of any ray line drawn from the origin of the speed-flow curve to any point on the curve represents density.
Any flow rate other than capacity can occur under two different conditions, one with a high speed and low density and the other with high density and low speed (oversaturated flow).
LOS A though E are defined on the low-density, high-speed side of the curves, with the maximum-flow boundary of LOS E placed at capacity; by contrast, LOS F, which describes oversaturated and queue discharge traffic, is represented by the high-density, low-speed part of the functions.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 33: Speed
Average travel speed
Mean speed
Free-flow speed
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Other speed parameters used in HCM 2000 include:
Average running speed—A traffic stream measure based on the observation of vehicle travel times traversing a section of highway of known length. It is the length of the segment divided by the average running time of vehicles to traverse the segment. Running time includes only time that vehicles are in motion.
Space mean speed—A statistical term denoting an average speed based on the average travel time of vehicles to traverse a segment of roadway. It is called a space mean speed because the average travel time weights the average to the time each vehicle spends in the defined roadway segment or space.
Time mean speed—The arithmetic average of speeds of vehicles observed passing a point on a highway; also referred to as the average spot speed. The individual speeds of vehicles passing a point are recorded and averaged arithmetically.
Free-flow speed—The average speed of vehicles on a given facility, measured under low-volume conditions, when drivers tend to drive at their desired speed and are not constrained by control delay.
Note: For most of the procedures using speed as a measure of effectiveness in this manual, average travel speed is the defining parameter. For uninterrupted-flow facilities not operating at level of service (LOS) F, the average travel speed is equal to the average running speed.
Suggested Questions: Q1:What do we mean by “Average Travel Speed”? A traffic stream measure based on travel time observed on a known length of highway. It is the length of the segment divided by the average travel time of vehicles traversing the segment, including all stopped delay times. It is also a space mean speed.
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 34: Free-Flow Speed
Usually an input, not an output
Not an observed speed
Not an MOE
Equivalent to LOS A or B speed
Image: ATSSA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Free-flow speed is the term used to describe the average speed that a motorist would travel if there were no congestion or other adverse conditions (such as bad weather). The "highest" (ideal) type of basic freeway section is one in which the free-flow speed is 70 mph or higher. Flow rate is defined as the rate at which traffic traverses a freeway segment, in vehicles per hour or passenger cars per hour. Free-flow speed is the speed on unimpeded vehicles. A common mistake is to enter observed speeds as the free-flow speed.
Suggested Questions: What is the free-flow speed?
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 35: Flow Rate
The equivalent hourly rate at which vehicles pass over a given point or section of a lane or roadway during a given time interval of less than 1 hour, usually 15 min
Image: FHWA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Flow rate represents the number of vehicles passing a point during a time interval less than 1 h, but expressed as an equivalent hourly rate. A flow rate is the number of vehicles observed in a sub hourly period, divided by the time (in hours) of the observation.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 36: Travel Time
Average time spent traveling from point A to B, including delay and stops, in seconds or minutes per vehicle
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Travel time is the average time spent traveling from point A to be, including delay and stops, in seconds or minutes per vehicle.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 37: Volume
Number of vehicles (or pedestrians) passing a point on a roadway during some time interval (expressed in vehicles, bicycles, or persons per hour)
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Volume and flow are variables that quantify demand, that is, the number of vehicle occupants or drivers (usually expressed as the number of vehicles) who desire to use a given facility during a specific time period. The distinction between volume and flow rate is important.
Volume is the number of vehicles observed or predicted to pass a point during a time interval.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 38: Volume-to-Capacity (V/C) Ratio
Ratio of flow rate to capacity for a transportation facility
Pay attention to the C!
Image: FHWA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Several analysis methods use the volume to capacity ratio as an MOE. The volume-to-capacity (V/C) ratio may offer a better measure of exposure than traffic volume per se. It is important to think about the C! For example using 2,000-2,200 veh/hr per lane is a common mistake. That is an IDEAL capacity, not measured.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 39: Density
Number of vehicles on a roadway segment averaged over space (usually expressed in vehicles per mile or vehicles per mile per lane)
Image: FHWA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Direct measurement of density in the field is difficult, requiring a vantage point for photographing, videotaping, or observing significant lengths of highway. Density can be computed, however, from the average travel speed and flow rate, which are measured more easily.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 40: Delay
Additional travel time experienced by travelers at speeds less than the free flow (posted) speed (expressed in seconds or minutes)
Image: FHWA
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Delay is defined as the additional travel time experienced by travelers at speeds less than the free flow (posted) speed (expressed in seconds or minutes). Some agencies have established thresholds of acceptable delay, or LOS. (Delay and speed are related)
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 41: Queue Length
Length of queued vehicles waiting to be served by the system (expressed in distance or number of vehicles)
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Queue length is the length of queued vehicles waiting to be served by the system (expressed in distance or number of vehicles).
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 42: Work Zone Safety Performance Measures
Work Zone Safety Performance Measures Guidance Booklet
Available at atssa.com
Image: FHWA
Notes: Key Message: Introduce WZ Safety Performance Measures Guidance Booklet
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The purpose of this guidance booklet is to introduce the concept of performance measures and performance data collection for work zone safety.
Suggested Questions: None
Additional Information: None
Possible Problems: None
42

## Slide 43: Example of Safety Performance Measures
Performance Measures
Performance Goal – “Pass” ¦ |  |  |  |  |  | 
5 - Excellent | 4 - Good | 3 - Fair | 2 – Poor |  | 1 – Very Poor | 
Work zone crash rate 20% less than pre-construction crash rate | Work zone crash rate equal to pre-construction crash rate | Work zone crash rate 20% higher than pre-construction crash rate | Work zone crash rate 30% higher than pre-construction crash rate |  | Work zone crash rate more than 30% higher than pre-construction crash rate | 
Levels of Performance
Source: Work Zone Safety Performance Measures Guidebook
Notes: Key Message: Provides an example of a multi-level performance measure for work zone safety
Est. Presentation Time: 1-2 minutes
Explanation of Cues/Builds: None
Suggested Comments: Using work zone crash rate as a measure of effectiveness, an example of a 5-level performance measure is shown. In this example, Level 4 (Good) is defined as the performance goal or the “passing” level. The full set of levels of performance here, including the designated goal, make up the performance measure. Another example of a multi-level performance measure is traffic level of service.
If you are using pass-fail performance measures then you would only have the performance goal, you would not have the additional levels of performance listed in the chart.
Suggested Questions: None
Additional Information:
This particular measure likely would apply to a long-term work zone; however, performance measures are not solely for long-term work zones. Even short-term temporary work zones can have major safety and traffic implications, and performance measures (such as maximum allowable queue length) can be generated and used to define acceptable performance.
The actual values for the various levels of performance need to be tailored to suit the locality and the specific project.
Possible Problems: None

## Slide 44: Additional Examples of Safety Performance Goals
Pass/fail – Incident Rate (IR) for worker injuries is less than 4.0
Subjective – Drivers feel safe traveling through work zones
Surrogate/Congestion – No stopped queues in the work zone longer than ¼ mile
Policy – Respond to all customer complaints within 24 hours
State/Agency Level – No construction-related fatalities in work zones State-wide in the year
Notes: Key Message: Discuss examples of different types and levels of performance goals
Est. Presentation Time: 1-2 minutes
Explanation of Cues/Builds: None
Suggested Comments: An example of an objective, multi-level measures for a project was provided on the previous slide. These are examples of other types of performance goals. Some goals will result in quantitative results, while others may be more qualitative.
Surrogate and safety-related congestion measures can play an important role when the work zone is short in duration or when crash data may not be readily available. A number of congestion measures have a strong relation to safety. For example, the presence of stopped queues creates traffic shock-waves that can contribute to crashes when sight distance is limited.
The Incident Rate refers to the OSHA worker injury rate.
The subjective measure could be examined using driver intercept surveys or web surveys.
Suggested Questions: What are some other examples of safety-related performance goals that you can think of? Can you name another congestion-related goal that may affect safety?
Additional Information: None
Possible Problems: None

## Slide 45: Others
Number of stops
Emissions
Noise level
Others?
ASK:
Which PMs are critical to me?
Does this assessment give me these PMs?
Notes: Key Message: Discuss WZ PMs
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: And there are other PMs. The important thing is to ask yourself, what is important to you? What are the objectives of your project? This information will help you choose strategies.
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 46: 7. Maintenance & Operation
Trained workers
Inspection requirements
Documentation
Modification guidelines
Adjustments
Image: ATSSA
Notes: Key Message: 7. Maintenance & Operation
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Making sure the TTC Plan is maintained and its is working as intended, through:
Trained workers
Inspection requirements
Documentation
Modification guidelines
Adjustments
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms depending on the level of your audience.

## Slide 47: Identifying Work Zone Strategies
Based on:
  Experience
  Guidance
  Judgment
  Cost?
NCHRP 581 has guidance
Image: NCHRP
Notes: Key Message: Introduce the concept of identifying strategies to consider
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The identification of candidate strategies begins after the project scope is defined and other preliminary information (e.g., typical sections, traffic volumes, right-of-way, and context) is available. Based on experience and guidance, a set of preliminary alternatives is identified.
Depending on the type of TMP required, the information required for the selected alternative may range from a list referring to the MUTCD or agency standards, to comprehensive plan sheets and special provisions. The level of detail should be determined on a project-by-project basis. Where appropriate, the construction approach/phasing/staging strategy should be provided on detailed plan sheets with plans for accommodating traffic at each stage. The work zone transportation management strategies should be documented on the plan sheets where possible (e.g., geometric improvements, control devices, etc.). If not, the strategies should be listed with text describing any restrictions, usage (duration, stage/phase, etc.), or other considerations. The type, number, location, and timing for traffic control devices should be listed for directing traffic through the work zone. Any work schedule restrictions should be documented for each stage (e.g., night work, peak hour restrictions, etc.).
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 48: Framework for Comparative Evaluation
Factors
  Road user factors
  Agency factors
Notes: Key Message: Introduce a Framework for Comparative Evaluation
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 49: 1. Road User Factors
Safety
Mobility
Access
Non-motorized traffic
Special (modal connections, trucks, etc.)
Notes: Key Message: Discuss Road User Factors
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: Some of this may be repetitive. Treat as a review.

## Slide 50: 2. Agency Factors
Worker safety
Emergency service implications
Community impacts
Contract administration
Inspection
Project coordination
Quality of work & cost
Image: FHWA
Notes: Key Message: Discuss Agency Factors
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: Some of this may be repetitive. Treat as a review.

## Slide 51: Strategy Selection
Requires project-specific information
Once identified, the preliminary alternatives are evaluated at two levels:
  “Fatal flaw”
  “Comparative analysis”
Notes: Key Message: Discuss Strategy Selection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Once identified, the preliminary alternatives are evaluated at two levels. The first is to determine if an alternative has a “fatal flaw.” . If none, then a comparative analysis is done.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 52: Fatal Flaw
Renders the alternative categorically infeasible
If found, the alternative is dismissed from further consideration
Notes: Key Message: Discuss Strategy Selection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A “fatal flaw,” is some factor that renders the alternative categorically infeasible. If a fatal flaw is found, the alternative is dismissed from further consideration. The remaining alternatives are retained for the second level of consideration, which is comparative analysis. At this level, each alternative is rated against a set of criteria. The fatal flaw and comparative analysis typically use most of the same evaluation factors. The purpose of the first-level analysis is to eliminate any alternative that does not meet predetermined threshold criteria.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 53: Comparative Analysis Should Consider:
Access
Basic traffic functionality & operation
Capacity and queues
Constructability
Cost
Human environment & other modes
Notes: Key Message: Discuss Strategy Selection
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The remaining alternatives are retained for the second level of consideration, which is comparative analysis. At this level, each alternative is rated against a set of criteria. The fatal flaw and comparative analysis typically use most of the same evaluation factors. The purpose of the first-level analysis is to eliminate any alternative that does not meet predetermined threshold criteria. The strategy that is most responsive to the evaluation factors, on an overall basis, is selected. Only rarely is the same strategy optimal for all factors. Usually, the various strategies will exhibit offsetting considerations (e.g., cost or disruption of commerce) that cannot easily be converted to a common measure. In such cases, agency policy, preferences, and discretion prevail. At the conclusion of the identification and evaluation phase, a work zone strategy and supporting strategies should be selected. The level of information assembled and the evaluation process should be sufficiently detailed to ensure feasibility of the selected strategies.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 54: 1. Access
Should be maintained
Should be inventoried and well understood
To both the work zone and:
  Commercial
  Industrial
  Recreational, and
  Residential property
Image: ATSSA
Notes: Key Message: Discuss Access
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Potential work zone impacts are directly related to the functionality of a highway in its permanent state (i.e., prior to construction work zone). Temporary denial or impedance of access to commercial, industrial, recreational, and residential property can be very disruptive. Additionally, freeway interchanges are sometimes closed or substantially altered during construction. In designing the work zone, the access function should be inventoried and well understood.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 55: Access Mechanisms
Abutting land use (i.e., driveways & private roads),
At-grade intersections,
Interchange ramps
Temporary occupancy
Temporary acceleration lanes
Image: ATSSA
Notes: Key Message: Discuss Access Mechanisms
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Each of these mechanisms is a work zone design variable, meaning that the design process can affect the status quo. However, designers rarely exercise unconstrained flexibility on any aspect. Although excluding all other access to a highway work zone may result in the greatest construction efficiency, that option is rarely available (and is generally used in the interest of rapid completion). Normally, existing access mechanisms are sustained as part of work zone design, but often at a diminished level.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 56: 2. Basic Traffic Functionality & Operation
Constructability
Construction necessarily alters the pre-project roadway configuration
It is important to tabulate the probable effects on basic traffic and highway operations
Image: ATSSA
Notes: Key Message: Discuss Basic Traffic Functionality & Operation
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Construction necessarily alters the pre-project roadway configuration. The ramifications of the alterations are sometimes overlooked until project implementation. Physical alteration and occupation by construction operations can affect traffic operations in many ways. Example impacts include increasing the response time of emergency services and rendering facilities unsuitable for oversized vehicles. The identification of undesirable features may be used to mitigate the condition or, if the condition is unmitigated, to serve as an evaluation factor. Tabulating the following information for each alternative will show the probable effects on basic traffic and highway operations:
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 57: Probable Effects On Basic Traffic & Highway Operations
Bridge deck width available compared with approach road
Freeway entrance ramps closed
Freeway entrance ramp acceleration lane length reductions
Freeway exit ramps closed
Freeway exit ramp deceleration lane length reductions
Notes: Key Message: Discuss Probable Effects On Basic Traffic & Highway Operations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory (provide examples as needed)
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 58: Probable Effects On Basic Traffic & Highway Operations
Horizontal clearance to bridge piers, above-ground lighting
Hardware, signs, and other roadside appurtenances
Impact on existing drainage systems
Location and control of affected intersections
Notes: Key Message: Discuss Probable Effects On Basic Traffic & Highway Operations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory (provide examples as needed)
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 59: Probable Effects On Basic Traffic & Highway Operations
Number of lanes per direction
Railroad crossings affected
Roadway lighting affected
Travel lane widths
Vertical clearance
Image: ATSSA
Notes: Key Message: Discuss Probable Effects On Basic Traffic & Highway Operations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory (provide examples as needed). One example: Bridge clearances may have an effect on detours since trucks may be affected by these clearances.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 60: 3. Capacity and Queues
Reduced lanes and/or speed will reduce capacity
Other factors can influence capacity:
  Access
  Lane width
  Shy distance
  Lateral clearances
  Rubbernecking
Notes: Key Message: Discuss Capacity and Queues
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Construction work zones often reduce the capacity of a facility below its pre-project capacity level and below the capacity level of the approach roadways. Capacity is related to the number of travel lanes and free-flow speeds; thus, construction-related factors that reduce either will reduce capacity. Although the number of travel lanes is a substantive control on capacity, many additional factors can also influence traffic flow and capacity, including access, lane width, lateral clearance, and activities that result in speed reduction (i.e., enforcement and construction-related activities).
Possible Problems: None
Additional Information: NCHRP Report 581 includes some guidance.

## Slide 61: Limited Queue Length
Policies limiting the projected queue length have been developed
QuickZone can estimate queue lengths
Notes: Key Message: Discuss Capacity and Queues
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Some agencies have developed policies limiting the projected queue length for work zone strategies involving a reduction in the number of travel lanes. Various techniques have been employed to estimate work zone capacity and traffic impacts. Some agencies have conducted analyses of their highway networks and predetermined facility segments for which work zone capacity reductions are prohibited or permitted within defined time frames (i.e., time and day).
Possible Problems: May be repetitious. Treat as a review.
Additional Information: NCHRP Report 581 includes some guidance.

## Slide 62: 4. Constructability
Ability to “bid and build”
A fundamental necessity of every project
A growing number of State DOTs routinely conduct constructability reviews
Notes: Key Message: Discuss Constructability
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The ability to “bid and build” proposed work is a fundamental necessity of every project. When the feasibility of constructing as-designed work comes into question, then delays, disruption, and additional costs often follow. To prevent this situation and in consideration of increasing project complexity, a growing number of state DOTs routinely conduct constructability reviews. In some cases, the reviews are conducted entirely with internal agency staff; however, more often external people or organizations are engaged. A body of guidance based on research and experience is available to guide these reviews. AASHTO’s Constructability Review Best Practices Guide outlines processes and procedures used by several state DOTs, including consideration of work zones (e.g., maintenance and protection of traffic and detours), for conducting these reviews.
Possible Problems: May be repetitious. Treat as a review.
Additional Information: NCHRP Report 581 includes some guidance.

## Slide 63: Constructability Evaluation Factors
Traffic movement through the work zone
Separation of through traffic from construction operations, workers, and construction traffic
Access to storage areas and all operations
Image: ATSSA
Notes: Key Message: Discuss Constructability Evaluation Factors
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Whether a documented constructability review or a less structured constructability review is conducted, design plans and work zone strategies should be reviewed by personnel experienced in construction operations to evaluate the feasibility and possible cost implications of the design. Rudimentary evaluation factors include the following:
-Traffic movement through the work zone during all construction phases and the geometric constraints of temporary construction features (e.g. shoring and bracing);
-Separation of through (i.e., non construction) traffic from construction operations, workers, and construction traffic (equipment and vehicles) and stationary construction roadside hazards; and
-Access by construction forces to storage areas (equipment and materials) and to all necessary operations.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: May be repetitious. Treat as a review.

## Slide 64: 5. Cost
Both agency & user costs
Explicitly associated with maintenance and protection of traffic
Actual agency cost of a work zone type can be considerably different from the cost of TTC
Notes: Key Message: Discuss Cost Factors
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Work zone strategies have both agency and user cost consequences. Agency costs associated with maintenance and protection of traffic are always estimated for the selected strategy. Typically, the costs of TTC items are explicitly associated with maintenance and protection of traffic. Bidders submit prices as an element of their cost proposal, and this bid history is typically used to estimate the cost. However, the actual agency cost of a work zone type can be considerably different from the cost of TTC. Work zone strategies often influence the general method and efficiency of construction operations and the bid prices for major cost items (e.g., earthwork, pavement, and structures). Such differences may not be recognized by design teams. This point emphasizes the benefit of a multidisciplinary approach to work zone strategy evaluation and selection. The safety risk specifically associated with queue formation has not been quantified, but is widely considered to exist. As a result, many agencies endeavor to prevent or mitigate for queue formation. Quantitative estimates of user cost associated with delay are possible. Time distributed traffic demand (i.e., volume by time of day and day of week) is needed. The values that an agency uses for delay in its life cycle cost analysis policy may be appropriate for a user cost estimate.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 65: 6. Human Environment and Other Modes
Disruption of pedestrian/ social patterns
Noise
Displacements
Effects on:
  The disabled
  Transit/non motorized users
  Intermodal connections
Notes: Key Message: Discuss Human Environment and Other Modes
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The category of “human environment and other modes” covers a myriad of factors that may arise at the intersection of construction operations and transportation facilities and that may not be specifically identified under another category. Disruption of pedestrian and social patterns, noise, natural resource impacts, and displacements are matters of public concern, and the impacts often vary with work zone strategy. The potential effects of work zones on disabled populations, transit users, intermodal connections, and non-motorized travel should be evaluated.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 66: The Bottom Line
Various strategies will exhibit offsetting considerations
Agency policy, preferences, and judgment will prevail
Mistakes are possible
Be willing to adjust
Notes: Key Message: Discuss the Bottom Line
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The strategy that is most responsive to the evaluation factors, on an overall basis, is selected. Only rarely is the same strategy optimal for all factors. Usually, the various strategies will exhibit offsetting considerations (e.g., cost or disruption of commerce) that cannot easily be converted to a common measure. In such cases, agency policy, preferences, and discretion prevail. At the conclusion of the identification and evaluation phase, a work zone strategy and supporting strategies should be selected. The level of information assembled and the evaluation process should be sufficiently detailed to ensure feasibility of the selected strategies.
Additional Information: NCHRP Report 581 includes some guidance.
Possible Problems: None

## Slide 67: Knowledge Check
What is a work zone impact assessment?
Name two road user factors to consider in the evaluation of TTC strategies
Name two factors that affect capacity
Notes: Key Message: Recap slide
Est. Presentation Time: 2-3 minutes
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Try to gauge understanding by asking these questions and others.
Suggested Questions: Shown.
Additional Information: None
Possible Problems: None

## Slide 68: Questions
Notes: Key Message: Questions
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at your questions.
Suggested Questions: Any questions before we move on?
Additional Information: None
Possible Problems: None