## Slide 1: -MODULE 1- Background
Work Zone Traffic Impact Analysis
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None. Module 1 discusses the background of WZ traffic impact analysis.
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 2: Module Objectives
Discuss why and when to consider work zone traffic impact analysis
Discuss issues and challenges associated with highway work zones
Discuss the Transportation Management Plan (TMP) requirements
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In this module, we will discuss the reasons for performing work zone analysis and when it takes place during the project timeline, quantify the work zone safety problem in the United States, and discuss requirements for development of transportation management plans as specified in the work zone final rule.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: WZ Issues and Challenges
Safety (users and workers)
Mobility
  Improper designs
Public relations
Others?
Work zone traffic impact analysis can systematically help improve these!
Image: FHWA
Notes: Key Message: Introduce WZ issues and challenges
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Self explanatory. In order to meet safety and mobility needs during highway maintenance and construction, and to meet the expectations of the traveling public, it is important to systematically assess the work zone impacts of projects and take appropriate action to manage these impacts.
Suggested Questions: What are some of the issues and challenges associated with work zones? Any others?
Additional Information: None
Possible Problems: None

## Slide 4: Traffic Safety: Is There a Problem?
891 work zone fatalities in 2022
94 worker fatalities
Source: www.workzonesafety.org
Notes: Key Message: Quantify the safety problem in the USA and in the state
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Traffic safety is a serious problem in the US and around the world.
Suggested Questions: Before showing the slide, may ask: How many people die in US work zones every year? After saying approximately 38,000, may say that 58,000 US soldiers were lost at the Vietnam War, or that 40,000 attend an NFL game every week. Try to relate the number to a group of people they can visualize or relate to.
Additional Information: Worker fatalities are included in the “pedestrian” category. For specific state statistics, go to http://www.workzonesafety.org/crash_data/
Other information to be used at the discretion of the instructor.
Possible Problems: This slide reflect the LATEST known data. This is usually 1 or 2 years behind. As new data are released, we will update this slide.
Image Credit: https://krcrtv.com/north-coast-news/eureka-local-news/chp-2-people-die-in-hwy-101-crash-in-humboldt-county-south-of-salmon-creek-road
Overall fatalities source: https://www.nhtsa.gov/press-releases/2020-traffic-crash-data-fatalities

## Slide 5: USA Work Zone Fatalities: 2000-2013
Source: www.workzonesafety.org
Notes: Key Message: Quantify WZ fatalities in the USA
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We reached an all-time high in work zones fatalities in 2002. Since then, the numbers have been declining! That is great news, but a single fatality is too many. We can still do better!
Suggested Questions: Do you see any trends?
Additional Information: These figures include both workers, motorists and pedestrians. http://www.workzonesafety.org/crash_data/
2013 STATE DATA: Format 3 numbers):
Fatalities in Motor Vehicle Traffic Crashes by State and Work Zone
State Not in WZ In WZ Total
Alabama 840 12 852
Alaska 49 2 51
Arizona 840 9 849
Arkansas 469 14 483
California 2,949 51 3,000
Colorado 467 14 481
Connecticut 273 3 276
Delaware 98 1 99
DC 20 0 20
Florida 2,338 69 2,407
Georgia 1,156 23 1,179
Hawaii 101 1 102
Idaho 212 2 214
Illinois 961 30 991
Indiana 774 9 783
Iowa 315 2 317
Kansas 343 7 350
Kentucky 632 6 638
Louisiana 695 8 703
Maine 144 1 145
Maryland 455 10 465
Mass 324 2 326
Michigan 939 8 947
Minnesota 378 9 387
Mississippi 607 6 613
Missouri 755 2 757
Montana 228 1 229
Nebraska 204 7 211
Nevada 256 6 262
NH 134 1 135
New Jersey 536 6 542
New Mexico 305 5 310
NY 1,189 10 1,199
NC 1,281 8 1,289
North Dakota 145 3 148
Ohio 969 20 989
Oklahoma 659 19 678
Oregon 307 6 313
Pennsylvania 1,192 16 1,208
Rhode Island 64 1 65
SC 762 5 767
South Dakota 129 6 135
Tennessee 981 14 995
Texas 3,278 104 3,382
Utah 215 5 220
Vermont 69 0 69
Virginia 723 17 740
Washington 435 1 436
West Virginia 330 2 332
Wisconsin 533 10 543
Wyoming 82 5 87
Total 32,140 579 32,719
Puerto Rico 344 0 344
Possible Problems: None

## Slide 6: National Work Zone Safety Information Clearinghouse
Internet work zone resource
www.workzonesafety.org
Image: workzonesafety.org
Notes: Key Message: Introduce the WZSC
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Work Zone Safety Clearinghouse is a good resource for everything related to work zones. It contains links to the various states’ TTC standards, a video vault, the states’ approved product lists and more. It is run by Texas A&M University and funded by the Federal Highway Administration. It is an excellent resource. You can reach it at workzonesafety.org.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 7: Mobility Challenges
Work zones may increase user delay due to reduced capacity
Work zones may have sustained impacts on traffic
Image: FHWA
Notes: Key Message: Relate safety and mobility
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: How can increased mobility improve safety?
Additional Information: Work Zone Clearinghouse (www.workzone safety.org) and FARS are possible sources for work zone related data.
Possible Problems: None

## Slide 8: Safety and Mobility are Related
Most WZ crashes are rear-end crashes
Congestion and stop-and-go can increase crashes
Smooth traffic flow can reduce primary & secondary crashes
Image: FHWA
Notes: Key Message: Relate safety and mobility
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None
Suggested Comments: Safety and mobility are related. Minimizing the impacts of the work zone may yield significant safety improvements. Both are important.
Suggested Questions: How can increased mobility improve safety?
Additional Information: Work Zone Clearinghouse (www.workzone safety.org) and FARS are possible sources for work zone related data.
Possible Problems: None
Image Credit: https://www.fhwa.dot.gov/publications/focus/08may/01.cfm

## Slide 9: Public Relations Challenges
Travelers are frustrated with the delays and unexpected road conditions caused by work zones
Is congestion = poor public relations?
Notes: Key Message: Discuss public relations challenges
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory.
Suggested Questions: Is congestion bad for public relations?
Additional Information: MUTCD Chapter 6B: Good public relations should be maintained by applying the following principles:
A. The needs of all road users should be assessed such that appropriate advance notice is given and clearly defined alternative paths are provided.
B. The cooperation of the various news media should be sought in publicizing the existence of and reasons for TTC zones because news releases can assist in keeping the road users well informed.
C. The needs of abutting property owners, residents, and businesses should be assessed and appropriate accommodations made.
D. The needs of emergency service providers (law enforcement, fire, and medical) should be assessed and appropriate coordination and accommodations made.
E. The needs of railroads and transit should be assessed and appropriate coordination and accommodations made.
F. The needs of operators of commercial vehicles such as buses and large trucks should be assessed and
appropriate accommodations made.
Possible Problems: None
Image Credit: https://cronolder.wordpress.com/2012/12/19/the-rabbling-rover-part-deux/angry-crowd/

## Slide 10: Analyze Potential WZ Impacts with Analytical Tools
Suitable tools are available & are applicable to the project
The analysis may be performed at the work zone, corridor and/or network levels
The analysis may be combined with an ongoing project study such as a corridor/subarea
Notes: Key Message:
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Quantitative analysis may be needed only for longer-duration projects that are expected to have major impacts (corridor, network, or regional levels), and may represent a small percentage (e.g., 5%) of all projects that an agency is involved in. FHWA does not require the use of analytical tools on all projects, however an impacts assessment shall be done for all Federal-Aid projects. Minor or shorter duration projects may only warrant qualitative assessment. Major or longer duration project will require more extensive impacts assessment, likely including quantitative analysis through the use of sophisticated tools.
Suggested Questions: None
Additional Information: Design/construction personnel can provide valuable input regarding the influence of design and construction issues in analyzing the work zone impacts of a project. For example, how much room is needed to store materials and maneuver? EIS = Environmental impact Statement
Possible Problems: None.

## Slide 11: Application of WZ Impact Analysis Tools
To compare multiple TTC strategies
  Example: Day versus Night work
To quantify and minimize the WZ impacts
Notes: Key Message: When to consider analytical tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: To help the agency choose between multiple traffic control and management approaches. Examples include night work vs. daytime work, weekend vs. weekday, lane closure vs. no closure, and full closure vs. partial closure. The availability and maturity of tools designed to produce quantitative estimates vary significantly when considering the range of work zone impacts. The broadest range of tools and analytical techniques available to an analyst focuses on work zone mobility impacts. Further, when the full range of mobility impacts can be quantitatively assessed, these impacts can be used in other analyses supporting safety, economic, environmental, and user cost.
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 12: Why Work Zone Impact Analyses?
To gain a clear understanding of the project’s mobility & safety issues
Constructability
Identify management strategies
May be required!
Image: ATSSA
Notes: Key Message: Discuss why analyze WZ
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Understanding the anticipated type, severity, and extent of work zone impacts associated with various project alternatives facilitates the incorporation of appropriate mitigation measures and strategies in project programming, design, and in the development of effective TMPs. Analysis of the work zone may include consideration of items such as the following:
Mobility and safety impacts of the project at both the corridor and network levels to include parallel corridors, alternate routes, the transportation network and other modes of transportation.
The combined impacts of concurrent projects that are located near each other or on the alternate route for another project.
Impacts on nearby intersections and interchanges, railroad crossings, and public transit and other junctions in the network.
Impacts on evacuation routes.
Impacts on affected public property (parks, recreational facilities, fire stations, etc.)
Impacts on affected businesses and residences.
Analysis may necessitate the use of analytical tools, depending on the degree of analysis required.
The analysis may also yield important information to address constructability issues, such as access requirements.
Suggested Questions: None
Additional Information: See FHWA website: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/wzta.htm
Possible Problems: Avoid getting too specific here.

## Slide 13: Why Work Zone Traffic Impact Analyses?
To systematically assess the work zone impacts of projects and take appropriate action to manage these impacts
Notes: Key Message: Introduce WZ issues and challenges
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: It is important to systematically assess the work zone impacts of projects and take appropriate action to manage these impacts. An analysis of mobility impacts can be helpful in supporting a safety analysis. The duration of congested conditions in the section of road affected by construction can be estimated when mobility impacts are projected. If the tool includes an estimate of diverted traffic volumes, these estimates can be key elements of an analysis of increased vehicle-miles traveled on alternative (possibly lower standard) roadways. The analysis of mobility impacts does not complete the safety analysis, but provides key estimates that support a robust safety analysis. In this case, crash rates on key facility types would have to be estimated and combined with the results of the mobility analysis.
Suggested Questions: Why is it important?
Additional Information: FHWA does not require the use of analytical tools on all projects, however an impacts assessment shall be done for all Federal-Aid projects. Minor or shorter duration projects may only warrant qualitative assessment. Major or longer duration project will require more extensive impacts assessment, likely including quantitative analysis through the use of sophisticated tools.
Possible Problems: None

## Slide 14: Fundamental Principles of TTC State:
“Road user movement (mobility) should be inhibited as little as practical”
  Ensure the impact to users is minimal
  Avoid congestion if possible
Notes: Key Message: Discuss one of the fundamental principles of TTC.
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Road user movement should be inhibited as little as practical, based on the following considerations:
A. TTC at work and incident sites should be designed on the assumption that drivers will only reduce their speeds if they clearly perceive a need to do so (see Section 6C.01).
B. Frequent and abrupt changes in geometrics such as lane narrowing, dropped lanes, or main roadway transitions that require rapid maneuvers, should be avoided.
C. Provisions should be made for the reasonably safe operation of work, particularly on high-speed, high volume roadways.
D. Road users should be encouraged to use alternative routes that do not include TTC zones.
E. Bicyclists and pedestrians, including those with disabilities, should be provided with access and reasonably safe passage through the TTC zone.
F. Roadway occupancy should be scheduled during off-peak hours and, if necessary, night work should be considered.
G. Early coordination with officials having jurisdiction over the affected cross streets and providing emergency services should occur before roadway or ramp closings.
Suggested Questions: Why do we want to avoid inhibiting mobility?
Additional Information: See MUTCD Page 6B-1.
Possible Problems: None

## Slide 15: Example
Analysis may discover that a queue may extend beyond the advance warning signs, so
  Other strategies may be deployed
  End-of-queue crashes may be avoided
Image: FHWA
Notes: Key Message: Example of the benefits of WZ analysis
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A careful analysis may discover that a queue may extend beyond the advance warning signs, so signs can be moved, their spacing changed or police may be deployed. It is not just meeting a standard, but making the work zone as safe as possible!
Suggested Questions: None
Additional Information: None
Possible Problems: None
Image Credit: https://www.fhwa.dot.gov/goshrp2/Solutions/Reliability/R11/WISE_Work_Zone_Impacts_and_Strategies_Estimator_Software

## Slide 16: When to Assess Work Zone Impacts?
During systems planning
Throughout the entire project’s lifecycle!
Image: ATSSA
Notes: Key Message: Discuss when to assess WZ impacts?
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: WZ impacts should be considered from the planning stages of a project. It is important to have the potential impacts of the WZ in mind since these impacts will affect the chosen strategy to control traffic, maintain mobility and optimize constructability. If work zone impacts of projects are not considered in systems planning, work zone impacts of projects may not be understood sufficiently enough to identify the work zone management strategies that are needed for a project. As a result, the project cost estimates (that are programmed into transportation plans) may not reflect the complete costs of work zone management. This could lead to expensive change orders during design, thereby delaying project implementation and increasing total cost. It may also lead to unavailability of funds for implementing appropriate work zone impacts management strategies, potentially resulting in undesirable safety and mobility issues. In addition impacts need to be reevaluated throughout the project, so adjustments can be made,
Suggested Questions: When to Assess Work Zone Impacts? At which stage?
Additional Information: Work zone impacts are not generally considered in systems planning. The primary reason cited for this is the lack of sufficient project-specific data during systems planning, such as how the project will be constructed, when exactly it will be built, how long it will last, etc. But many State Departments of Transportation (DOTs), Metropolitan Planning Organizations (MPOs), and other transportation agencies recognize the potential value of assessing work zone impacts during systems planning. There is general thinking in the industry that advancing work zone considerations as early as possible in the program delivery process will lead to overall benefits in terms of better planned, budgeted, and implemented projects that minimize work zone impacts. This section provides a potential approach and general guidance on advancing the consideration of work zone impacts to the systems planning stage.
Possible Problems: None

## Slide 17: In Summary..
We must analyze WZ traffic impacts to inhibit road user movement as little as practical and to improve safety and mobility!
Notes: Key Message: Summarize previous point
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: We must analyze WZ traffic impacts to inhibit road user movement as little as practical and to improve safety and mobility!
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 18: The Challenge
How to achieve constructability without compromising safety and mobility?
Notes: Key Message: Summarize the challenge
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As work zone impacts assessment is performed progressively through the various program delivery stages, the three basic issues of safety, mobility, and constructability are addressed in an iterative manner. Information from one stage feeds into the next, with the level of detail of the assessment progressively increasing from stage to stage. The objective is to achieve constructability without compromising safety and mobility.
Suggested Questions: How to achieve constructability without compromising safety and mobility?
Additional Information: Turn into a discussion.
Possible Problems: None

## Slide 19: Assessing and Managing Work Zone Impacts Lies in:
Maximizing the safety of users and workers
Optimizing Mobility (and accessibility)
Constructability
  Planning, designing and building projects efficiently
Image: ATSSA
Notes: Key Message: Discuss WZ Considerations
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Safety, mobility, and constructability are the three critical work zone related issues that need to be addressed while planning, designing, and building road projects. Constructability can be defined as the optimum use of construction knowledge and experience in planning, design, procurement, and field operations to achieve overall project objectives. The objective of constructability is to facilitate rational bids and minimize problems during construction. Benefits of constructability include cost reduction, schedule adherence, higher productivity, enhanced quality, and more safety and convenience for the traveling public. Constructability reviews are performed to facilitate the practicality of construction and minimize project delays, changes, and costs, while at the same time maximizing productivity, quality, safety, and convenience.
Suggested Questions: What is constructability? What is more important? All three are important. Out job is to optimize their relationship.
Additional Information: None
Possible Problems: Treat as an intro slide and to define these terms

## Slide 20: Impact Assessment is an Iterative Process
Impact Assessment
Safety
Mobility
Construct-ability
Image: FHWA
Notes: Key Message: Explain the iterative nature of impact assessment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The impacts assessment during design is an iterative process progressing through the various stages of design, and addressing the basic issues of safety, mobility, and constructability. Basic assumptions are re-examined and appropriate changes are made. Consensus of all involved parties is sought, and performance objectives for the work zone are developed. Information from one stage feeds into the next, with the level of detail of the assessment progressively increasing from stage to stage. The objective is to achieve constructability without compromising safety and mobility.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 21: Conflicting Goals?
Mobility
Keep costs down
Maximum levels
of safety
We want to maximize mobility while
maintaining safety & constructability!
Notes: Key Message: Discuss conflicting goals
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The more “safety” we provide, the more expensive the project may be.* Our job is to achieve the best balance between these 2. This is not easy since these are conflicting goals. You should pull more for safety, rather than to cut costs. Maintaining traffic flow and maintaining maximum levels of safety are not necessarily mutually exclusive. Some strategies can do both.
Suggested Questions: None.
Additional Information: None
Possible Problems: Turn into a discussion, if possible. *Total closures may be an exception, where we provide more safety at a lower cost.

## Slide 22: Who Does the WZ Impact Analysis?
The project owner?
  Planning
  Design
  Construction
  M&O (contractor?)
Others?
All of the above?
Notes: Key Message: Discuss who does the WZ impact analysis
Est. Presentation Time: Two minutes.
Explanation of Cues/Builds: None
Suggested Comments: The answer to this question is related to the point at which the analysis is done. Work zone impacts assessment is performed progressively through the various program delivery stages, the three basic issues of safety, mobility, and constructability are addressed in an iterative manner. Information from one stage feeds into the next, with the level of detail of the assessment progressively increasing from stage to stage. So, theoretically, it is all of the above. All stakeholders
Suggested Questions: Who does the WZ impact analysis?
Additional Information: M&O = maintenance and operations.
Possible Problems: Try to turn into a discussion.

## Slide 23: The Designer’s Role
To consider ALL factors and ALL users involved, the standards and guidelines, traffic impact analysis and apply engineering judgment to develop the BEST possible design
Notes: Key Message: Discuss the designer’s role
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Your job as a designer is to take all this information, standards and guidelines and APPLY them to a specific situation utilizing your best engineering judgment and CONSIDERING the needs of ALL users.
Suggested Questions: What is engineering judgment? See Definitions in MUTCD: Engineering Judgment—the evaluation of available pertinent information, and the application of appropriate principles, Standards, Guidance, and practices as contained in this Manual and other sources, for the purpose of deciding upon the applicability, design, operation, or installation of a traffic control device. Engineering judgment shall be exercised by an engineer, or by an individual working under the supervision of an engineer, through the application of procedures and criteria established by the engineer. Documentation of engineering judgment is not required.
Additional Information: Can you satisfy the needs of ALL users? No, but we should consider the needs of ALL.
Possible Problems: None.

## Slide 24: Types of Decisions
Scheduling
Application
Transportation Management Plan (TMP)
Notes: Key Message: Discuss the types of decisions that the analysis may facilitate
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: More specifically, however, are the types of decisions that must be made irrespective of where in the work zone analysis framework one is (Planning, PE/Design, Construction). These types of decisions are represented by three inter-related decision types that drive the overall work zone decision-making process as a three-part decision-making engine:
Scheduling Decisions—Decisions impacting when work zone activity will occur, ranging from the selection of time of day (e.g., the decision to perform work at night), to days of week (e.g., the decision to restrict work zone activity to weekends only), to time of year (e.g., a decision to work in summer only). For longer projects this includes how the work will be phased and staged along the roadway network, potentially over several years.
Application Decisions— Discussed earlier
Transportation Management Plan Decisions— Discussed earlier
Suggested Questions: Which decisions?
Additional Information: None
Possible Problems: None.

## Slide 25: Scheduling Decisions
Time of day
Day vs. night
Day of week
Time of year
  i.e., Summer only
Phasing and staging
Image: FHWA
Notes: Key Message: Discuss the types of decisions that the analysis may facilitate
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Scheduling Decisions—Decisions impacting when work zone activity will occur, ranging from the selection of time of day (e.g., the decision to perform work at night), to days of week (e.g., the decision to restrict work zone activity to weekends only), to time of year (e.g., a decision to work in summer only). For longer projects this includes how the work will be phased and staged along the roadway network, potentially over several years. Other considerations include availability of materials, peak volumes and the decision to work in phases.
Suggested Questions: How does scheduling impact your decision?
Additional Information: None
Possible Problems: None.

## Slide 26: Application Decisions
Construction techniques
  i.e., cast in place vs. precast
Image: FHWA
Notes: Key Message: Discuss the types of decisions that the analysis may facilitate
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Application Decisions—Decisions pertaining to the construction technique to be used within the work zone (e.g., a decision to use cast-in-place techniques rather than a pre-cast approach). There are numerous construction techniques that may be considered (see Online Resources, FHWA Office of Infrastructure available at the end of this report for links to more information). The selection of any one of these techniques will have different implications for work zone planning.
Suggested Questions: None
Additional Information: None
Possible Problems: This was discussed earlier so treat as a review. Use to reinforce the key point and gauge understanding.

## Slide 27: Transportation Management Plan (TMP) Decisions
How traffic will be managed while work zones are in place
Which strategies will be implemented to mitigate the impacts of the work zone
T
M
P
Notes: Key Message: Discuss the types of decisions that the analysis may facilitate
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Transportation Management Plan Decisions —Decisions that determine how traffic will be managed while work zones are in place. This includes issues of temporary traffic control (TTC—control strategies, traffic control devices), public information (PI—public awareness strategies, motorist information), and transportation operations (TO—demand management, work zone safety management). For example, developing a transportation management plan for a two-lane rural roadway may involve selecting between TTCs such as traffic signals or a flagging crew to support two-way, one lane operations; notifying the motoring public of possible delays through a PI campaign; and finally developing a TO enforcement plan to insure worker safety.
Suggested Questions: None
Additional Information: A more detailed discussion of developing transportation management plans is available in the publication Developing and Implementing Transportation Management Plans for Work Zones.
Possible Problems: None

## Slide 28: What is a TMP?
A set of coordinated transportation management strategies to manage the work zone impacts
  Required for ALL Federal Aid projects
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A TMP (an umbrella term) lays out a set of strategies for managing the work zone impacts of a project. Because work zone objectives, needs, and issues vary from project to project, the scope, content, and degree of detail in a TMP will also vary from project to project. It is ultimately up to the agency to establish and implement TMPs that best serve the mobility and safety needs of the motoring public, construction workers, businesses, and community.
Suggested Questions: Have you been involved with developing TMPs? If so, what was your role? Were they effective?
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm.
Possible Problems: Avoid getting too specific here.

## Slide 29: Work Zone Safety and Mobility Rule
All State and local governments that receive Federal-aid funding were required to comply by October 12, 07
Image: ATSSA
Notes: Key Message: Discuss Work Zone Safety and Mobility Rule
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Work Zone Safety and Mobility Rule was published on September 9, 2004 in the Federal Register. All state and local governments that receive federal-aid funding are required to comply with the provisions of the rule no later than October 12, 2007. The rule updates and broadens the former regulation at 23 CFR 630 Subpart J to address more of the current issues affecting work zone safety and mobility.
Possible Problems: None
Suggested Questions: None
Additional Information: None

## Slide 30: Work Zone Safety and Mobility Rule
Encourages broader consideration of the safety and mobility impacts of work zones across project development, and the implementation of strategies that help manage these impacts
Image: ATSSA
Notes: Key Message: Discuss Work Zone Safety and Mobility Rule
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The changes to the regulation encourage broader consideration of the safety and mobility impacts of work zones across project development, and the implementation of strategies that help manage these impacts during project delivery.
Possible Problems: None
Suggested Questions: None
Additional Information: None

## Slide 31: Work Zone Safety and Mobility Rule Provisions
States & local DOTs to implement an overall policy on WZ safety & mobility
Notes: Key Message: Discuss Work Zone Safety and Mobility Rule
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The rule has three primary components and goals. First, it calls for each State and local DOT to implement an overall policy on work zone safety and mobility to institutionalize the consideration and management of work zone impacts. Second, the rule requires establishment of agency-level processes to support policy implementation, including procedures for assessing the impacts of work zones, analyzing data, conducting training, and reviewing processes.
For a DOT, establishing an overall policy is the first step toward institutionalizing the planning, design, and operational strategies that reduce congestion and crashes due to work zones. Because of the high rates of retirement and turnover within DOTs and the increasing use of consultants, formalizing processes and practices will help ensure a consistent way of doing business across projects. Formalized processes also will lead to greater consistency and uniformity for highway users traveling through work zones.
Possible Problems: None.
Suggested Questions: None
Additional Information: None
Image Credit: https://www.countrylines.com/community/slow-down-go-around-roadside-utility-workers/

## Slide 32: Work Zone Safety and Mobility Rule Provisions
Establishment of agency-level processes to support policy implementation, including procedures for assessing WZ impacts, analyzing data, conducting training & reviewing processes
Image: ATSSA
Notes: Key Message: Discuss Work Zone Safety and Mobility Rule
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Rule also encouraged the establishment of agency-level processes to support policy implementation, including procedures for assessing WZ impacts, analyzing data, conducting training & reviewing processes.
Possible Problems: None.
Suggested Questions: None
Additional Information: None

## Slide 33: Work Zone Safety and Mobility Rule Provisions
Establishing project-level procedures to assess and manage the impacts of individual projects
  Identify “significant projects”
  Develop and implement a TMP for Federal-aid projects
Image: FHWA
Notes: Key Message: Discuss Work Zone Safety and Mobility Rule
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Third, the rule calls for establishing project-level procedures to assess and manage the impacts of individual projects.
Possible Problems: None.
Suggested Questions: None
Additional Information: None

## Slide 34: How Would TMPs Help?
Address the broader safety and mobility impacts of work zones at the corridor and network levels
Promote more efficient and effective construction phasing and staging, minimize contract duration and control costs
Improve work zone safety
Notes: Key Message: Discuss benefits of TMPs
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: Also, address needs of the traveling public and local businesses and communities.
Suggested Questions: Do you feel TMP’s would improve work zone safety? How?
Additional Information:
Possible Problems: Keep brief

## Slide 35: How Would TMPs Help?
Minimizing work zone impacts
Improving public relations
Minimizing complaints from the traveling public and local businesses and communities
Notes: Key Message: Discuss benefits of TMPs
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: Self explanatory
Suggested Questions: Do you feel TMP’s would improve work zone safety? How?
Additional Information:
Possible Problems: Keep brief

## Slide 36: How Much Detail?
  Based on the State or local transportation agency's work zone policy and the anticipated work zone impacts of the project
  Required components of a TMP depend on whether the project is “significant”
Image: FHWA
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The level of detail will vary by State and by project. The scope, content, and level of detail of a TMP will vary based on the agency's work zone policy, the anticipated work zone impacts of the project, and whether the project is determined to be a significant project.
Suggested Questions: How much detail?
Additional Information: http://ops.fhwa.dot.gov/wz/rule_guide/appc.htm
Possible Problems: Avoid getting too specific here.

## Slide 37: What is a “Significant Project”?
Projects that alone or in combination with other concurrent projects nearby, are anticipated to cause sustained work zone impacts that are greater than what is considered tolerable based on State policy and/or engineering judgment
Image: FHWA
Notes: Key Message: FHWA criteria for a significant project.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: Recognizing that not all road projects cause the same level of impact, the updated rule establishes a category for "significant" projects. A significant project is one that by itself or in combination with other nearby projects is anticipated to cause sustained impacts that are greater than considered tolerable according to State policy and/or engineering judgment. The rule contains both a general definition of significant project, which States could tailor in their policy, and a specific definition that is not changeable. This is the general definition. Many agencies have tailored this definition to establish either a set of criteria or a decision flowchart laying out how they determine if a project is a significant project.
Suggested Questions: How does your agency define "significant project?"
Additional Information: As defined in Section 630.1010 of the Rule, a significant project is one that, alone or in combination with other concurrent projects nearby is anticipated to cause sustained work zone impacts that are greater than what is considered tolerable based on State policy and/or engineering judgment.
Possible Problems: None

## Slide 38: What is a “Significant Project”?
All Interstate system projects within a designated Transportation Management Area (TMA) that occupy a location for more than three days with either intermittent or continuous lane closures
Notes: Key Message: FHWA criteria for a significant project.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: All Interstate projects that are within the boundaries of a designated Transportation Management Area (TMA) that occupy a location for more than three days with either intermittent or continuous lane closures shall be considered significant. States may request an exception to these provisions if they feel a project of this type does not have significant sustained impacts. Various agencies will have different judgments about what is a tolerable impact.
Suggested Questions: Do you feel this is an acceptable definition of significant project?
Additional Information: None
Possible Problems: This definition may vary by State.

## Slide 39: TMPs Shall Include:
Traffic Control Plan (TCP)
Public information (PI) and outreach
Transportation operation (TO) strategies
All 3 components are required for
“Significant Projects”
Notes: Key Message: Introduce the TMP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: The Work Zone Safety and Mobility Rule states that for significant projects the State shall develop a TMP that consists of a Temporary Traffic Control (TTC) plan and addresses both Transportation Operations (TO) and Public Information (PI) components. For individual projects or classes of projects that the State determines to have less than significant work zone impacts, the TMP may consist only of a TTC plan. However, states are encouraged to also consider TO and PI issues for these projects.
Suggested Questions: What is a TMP?
Additional Information: See FHWA website: http://ops.fhwa.dot.gov/wz/resources/final_rule/tmp_examples.htm
Possible Problems: Avoid getting too specific here.

## Slide 40: Traffic Control Plan (TCP) Component
A plan for maintenance and control of traffic during work
Addresses temporary traffic control
Consistent with the complexity of the project
Consistent with MUTCD, Roadside Design Guide and state standards
Adjusted to field conditions
Notes: Key Message: Introduce the TCP
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. A TCP is a set of drawings detailing how traffic will be controlled (or maintained).
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid getting too specific here.

## Slide 41: Public Information (PI) Component
Addresses communication with the public & concerned stakeholders
Seeks to inform affected users of the work zone and its conditions
Notes: Key Message: Introduce the PI component
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: The PI component addresses communication with the public & concerned stakeholders. It seeks to inform affected users of the work zone and its conditions
Suggested Questions: None
Additional Information: None
Possible Problems: Discuss in general terms here. More specific information is provided later in the course.
Image Credit: Microsoft online / creative commons

## Slide 42: Public Outreach Techniques
Highway advisory radio
Dedicated information phone number
Press kits
Variable message signs
emails
511
Websites
Other
Notes: Key Message: Additional outreach techniques.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: There are several PI outreach techniques available. Some are listed here. Dedicated phone numbers can be posted on the project to keep drivers informed about the project’s progress and mayor traffic events planned for the future. However the line must be manned and takes a large amount of staff time if manned 24/7. Variable or changeable message signs are one of the most immediate (provide instant information) techniques.
Suggested Questions: Which of these techniques has been most effective in your agency?
Additional Information: 511 is the USA’s Travel Information Number
Possible Problems: None

## Slide 43: Example of Project Outreach Website
Image: I95exitguide.com
Notes: Key Message: Provide PI example
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: This is an example of a website used to provide PI.
Suggested Questions: Which of these techniques has been most effective in your agency?
Additional Information: None
Possible Problems: None

## Slide 44: Transportation Operations (TO) Component
Addresses sustained operations and management strategies of the work zone impact area, such as:
  Demand management
  Corridor/network management
  Speed management & enforcement
  ITS
Notes: Key Message: These are the areas that must be considered in the traffic operations plan.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: TO strategies really refer to the traffic management goals we discussed above. Demand management would include shifting trips to other modes, routes or other times. Trip reductions of 20 to 25% of normal traffic have been achieved in some cases. Corridor/ network management may mean speeding up or delaying projects on alternate routes. Safety of road users on alternate routes must be assessed as well as the safety of workers and road users traversing the work zone. Speed management strategies, such as the use of enforcement, can be critical to maintaining safety in many areas. ITS can be useful for both improving safety (such as by alerting drivers to stopped traffic ahead) and improving mobility (such as by informing motorists of delays and alternate routes).
Suggested Questions:
Additional Information:
Possible Problems:

## Slide 45: Concepts of WZ Traffic Impact Analysis
Should be used throughout a project’s life
  From planning stages to construction
Should influence
  Selection of alternatives
  Design details
  Construction approach
  The TTC Plan
Image: FHWA
Notes: Key Message: Discuss when to use these concepts
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: These concepts and techniques should be used throughout a project, from planning stages to construction. They should influence the design of the work zone.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 46: Putting it all Together
TMP
Project characteristics
Travel/traffic characteristics
Work zone design
Procurement options
Constructability
Engineering judgment
TTC, TO, PI
Community issues
Traffic impact analysis
Notes: Key Message: Discuss considerations of the TMP
Est. Presentation Time: 1 minute
Explanation of Cues/Builds:
Suggested Comments: All these issues should be considered and be included in the project’s TMP. Safety, mobility, and constructability are affected by the following types of issues, including:
• Project characteristics.
• Travel and traffic characteristics.
• Corridor, network, and community issues.
• Design, procurement, and construction options.
• Work zone design and safety issues.
• TTC strategies.
• Transportation operations (TO) strategies.
• Public information (PI) strategies.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 47: Module Recap
Why do we need to analyze WZ traffic impacts?
Approximately, how many work zone fatalities are there in the USA?
What is the WZ designer’s role?
What is a TMP and its TO component?
What is a “Significant Project”?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.