## Slide 1: -MODULE 2- Work Zone Impact Analysis Fundamentals
Work Zone Traffic Impact Analysis
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Module 2 provides the basics of WZ impact analysis
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 2: Module Objectives
Define impacts assessment
Discuss components and steps of an impacts assessment
Discuss how to incorporate WZ impact assessment into program delivery
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Work Zone Impacts Assessment
An Approach to Assess and Manage Work Zone Safety and Mobility Impacts of Road Projects
Developed to provide guidance
Image: FHWA
Notes: Key Message: Introduce WZ Impacts Assessment Report
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The purpose of this document is to provide guidance to practitioners on developing and/or updating procedures to assess and manage the work zone impacts of their road projects. This document presents a general approach for conducting work zone impacts assessment and management. This approach is not the only way to perform work zone impacts assessment, and is not intended to advocate a “one-size-fits-all” approach. This module is based on this report.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 4: What is WZ Impacts Assessment?
The process of understanding the safety and mobility impacts of a road construction/ maintenance/ rehabilitation project
Notes: Key Message: Define WZ Impacts Assessment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Factors that will influence the level of impacts caused by a work zone include traffic conditions and characteristics, project characteristics, geographic/physical features, and aspects of the surrounding area (e.g., alternate routes, nearby businesses). The assessment process may involve a high-level, qualitative review of these factors for some projects, and a detailed quantitative analysis using modeling and/or simulation tools for other projects.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 5: WZ Impacts Assessment Constitutes:
Assessing the likely WZ impacts
Developing appropriate TMPs
Monitoring the actual impacts
Making adjustments to the TMP
Conducting performance assessments
Identifying trends towards overall improvement of work zone policies, procedures and practices
Notes: Key Message: Define WZ Impacts Assessment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Incorporating work zone impacts assessment in program delivery does not entail an entirely new process; rather, it involves the consideration of work zone impacts issues during pre-existing program delivery activities. Thus, the work zone impacts assessment process described in this Guide is structured to mirror the typical State DOT program delivery process. It constitutes:
Assessing the likely work zone impacts and developing appropriate work zone transportation management plans (TMPs) during project development and delivery.
• Monitoring the actual impacts of the project and making adjustments to the TMP (if necessary) during project implementation.
• Conducting performance assessment to track performance, document lessons learned, and identify trends towards overall improvement of work zone policies, procedures, and practices.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 6: Questions to Ask
Is extensive WZ impacts assessment needed for my project?
What project classification does my project fall under?
What are the corresponding WZ impacts assessment actions?
Notes: Key Message: Questions to ask
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Development and application of policy provisions for work zone impacts assessment may provide quick answers to questions such as:
• Do I need to perform an extensive work zone impacts assessment for my project?
• What project classification does my project fall under, and what are the corresponding work zone impacts assessment actions that I need to take?
• What management strategies should I consider in the Transportation Management Plan (TMP)?
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 7: Questions to Ask
What management strategies should I consider in the TMP?
Are there any policy provisions that require maintaining a certain number of lanes open during roadwork on a certain type of facility?
Notes: Key Message: Questions to ask
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Development and application of policy provisions for work zone impacts assessment may provide quick answers to questions such as:
• What management strategies should I consider in the Transportation Management Plan (TMP)?
• Are there any policy provisions that require maintenance of a certain number of lanes of traffic capacity during roadwork on a certain type of facility?
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 8: Questions to Ask
What is the agency’s policy guidance on how to account for road user costs in developing TMPs?
What are the agency’s policy provisions on incident management strategies for WZ?
Notes: Key Message: Questions to ask
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Development and application of policy provisions for work zone impacts assessment may provide quick answers to questions such as:
• What is the agency’s policy guidance on how to account for road user costs in developing TMPs?
• What are the agency’s policy provisions on traffic incident management strategies for work zones?
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 9: Questions to Ask
Does the agency’s policy allow performance-based contracting?
Are there any policy provisions that require monitoring of work zone performance for my project?
Notes: Key Message: Questions to ask
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Development and application of policy provisions for work zone impacts assessment may provide quick answers to questions such as:
• Does the agency’s policy allow performance-based contracting?
• Are there any policy provisions that require monitoring of work zone performance for my project?
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 10: Project Assessment Steps
Collect project information
Collect public perceptions/stakeholder inputs
Assess project-level performance
Synthesize & analyze data for program-level assessment
Evaluate/revise WZ impacts assessment
Management practices & procedures
Notes: Key Message: Project assessment steps
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
Suggested Questions: Most of the data needed for the project-level assessment should be available from each project’s monitoring efforts including field observations, crash data, and operational data. It is important that traffic and safety monitoring data collected during construction be documented and maintained in a consistent manner for each project.
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 11: Incorporating WZ Impact Analysis into Program Delivery
Policy level
Planning stages
Preliminary engineering
Design stages
Construction/ Implementation
Performance assessment
Maintenance & operation
Work zone impacts can be assessed and mitigated during all delivery phases of a project!
Notes: Key Message: Discuss the components of WZ impact assessment process
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Incorporating work zone impacts assessment in program delivery does not entail an entirely new process; rather, it involves the consideration of work zone impacts issues during pre-existing program delivery activities. Thus, the work zone impacts assessment process described in this Guide is structured to mirror the typical State DOT program delivery process. WZ impacts can be assessed and mitigated during all delivery phases of a project. The level of detail and type of work zone impacts assessment varies depending upon the program delivery stage. Let’s discuss these.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: Although the “tools” can be used at any point during this process, their main application is during the preliminary engineering and design phases. Avoid discussing these points here. This is an intro slide.

## Slide 12: 1. At the Policy Level…
To facilitate streamlined decision making and consistency
To help standardize WZ practices that are known to work
To serve as a guide for planning, designing, and constructing road projects
To obtain management buy-in & support
Notes: Key Message: Addressing WZ impacts at the policy level
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: At the policy-level, overall policies and program priorities are established and used for decision-making during the different program delivery stages. The policy is applied through policy provisions that address various aspects of transportation system planning, design, construction, maintenance, and operations. Policy provisions may be in the form of standard procedures, specific requirements, performance standards, and/ or policy guidance. Addressing work zone safety and mobility at the policy-level and applying the policy at the various stages of program delivery will facilitate streamlined decision-making and consistency. Policies can help standardize work zone practices that are known to work well, and serve as a guide for planning, designing, and constructing road projects. In addition, a policy-based approach to work zone safety and mobility facilitates buy-in and support from management for the effective assessment and management of work zone impacts. Such standardization and streamlining will in turn lead to good decision-making that results in safe and effective work zones, well-constructed projects, construction quality, improved agency operational and organizational efficiency, and cost effectiveness.
Suggested Questions: How can WZ impact assessment help at the policy level?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 13: 2. During Planning Stages…
Advancing work zone considerations as early as possible in the program delivery process
Will lead to overall benefits in terms of better planned, budgeted, and implemented projects that minimize work zone impacts
Notes: Key Message: WZ impacts assessment during systems planning
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Advancing work zone considerations as early as possible in the program delivery process will lead to overall benefits in terms of better planned, budgeted, and implemented projects that minimize work zone impacts.
Suggested Questions: How can WZ impact assessment help during planning stages?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Systems planning is the stage of program delivery where planning for the future is carried out by identifying transportation systems needs and deficiencies, developing and evaluating alternative improvement solutions, and compiling plans and programs for implementing the solutions. Systems planning is conducted at several levels including Statewide, regional, metropolitan, county, local, and corridor. The process is both interactive and iterative, with participation and feedback from concerned public and private organizations, other interested parties, and the general public. Work zone impacts are not generally considered in systems planning. The primary reason cited for this is the lack of sufficient project-specific data during systems planning, such as how the project will be constructed, when exactly it will be built, how long it will last, etc. But many State Departments of Transportation (DOTs), Metropolitan Planning Organizations (MPOs), and other transportation agencies recognize the potential value of assessing work zone impacts during systems planning.
Possible Problems: Quantitative analysis of work zone impacts may not be possible during systems planning due to inadequate project detail and lack of data. In such cases, the particular issue under investigation may be noted so that the staff that conduct assessments in subsequent phases are made aware of the issue.

## Slide 14: 3. During Preliminary Engineering…
At the project-level to identify and develop ways to implement the solution, identify potential issues/obstacles, and develop an implementation concept for the project
Image: ATSSA
Notes: Key Message: WZ impacts assessment during preliminary engineering
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In preliminary engineering, planning is done at the project-level to identify and develop ways to implement the solution, identify potential issues/obstacles, and develop an implementation concept for the project. The focus of preliminary engineering is to identify ways to implement projects.
Suggested Questions: How can WZ impact assessment help during preliminary engineering?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Preliminary engineering is the first stage in project development. This is the stage when designers and project planners conduct early project-level planning and develop an overall design concept of what the new facility would look like. At this stage, projects that are identified in systems planning are handed over to the respective project planners and designers to further develop the project. The main objective is to identify ways to implement the project, and develop appropriate plans and design concepts. Therefore, during preliminary engineering more project-specific information is collected and synthesized. The key difference between systems planning and preliminary engineering is that, in systems planning transportation improvement needs are identified, potential alternative solutions are developed and evaluated, and the best alternatives are chosen for further development and implementation. Therefore, the focus of systems planning is to identify projects.
Possible Problems: None

## Slide 15: 4. During Design Stages…
Will facilitate better decision-making
Will ultimately improve the operational performance of highways during construction and maintenance activities,
Will minimize the impacts on road users and businesses (such as back-of-queue crashes)
Image: FHWA
Notes: Key Message: WZ impacts assessment during design
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Through the course of these design stages, final decisions are made on the best options for all the aspects of the project. Based on these decisions the final plans, specifications, and estimates (PS&Es) and the bid package are developed, followed by bidding and contract award. The ability to estimate these work zone impacts at the early planning and design stages will facilitate better decision-making that will ultimately improve the operational performance of highways during construction and maintenance activities, and minimize the impacts on road users and businesses.
Suggested Questions: How can WZ impact assessment help during the design stages?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Design represents the stage in program delivery where the final design is conducted for the project and appropriate plan documents, specifications, and cost estimates are developed. These documents lay out exactly how the project will be built, what the issues are, and how the work zone will be implemented and managed. Design is an iterative process that consists of different stages, sometimes referred to by different percentages such as the 30% stage (preliminary engineering), the 60% and 90% stages, and then the final design for the project. Preliminary engineering and the subsequent design stages are generally performed by similar staff, i.e., project planners and designers belonging to the design/engineering departments of transportation agencies, either at the central office or the region/district level.
Possible Problems: None

## Slide 16: 5. During Construction…
To assess the impact of any proposed changes prior to the start of work
To implement the TMP
To monitor & manage WZ impacts during construction
To revise the TMP and, if necessary.
To document any findings
Image: ATSSA
Notes: Key Message: WZ impacts assessment during construction
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The objectives of work zone impacts assessment during construction are to:
• Address and resolve any pre-construction coordination issues.
• Assess the impact of any proposed changes prior to the start of work (e.g., contractor
proposed alternate construction staging and/or TMP).
• Implement the TMP.
• Actively monitor and manage work zone impacts during construction.
• Revise the TMP and implement appropriate revisions, if necessary.
• Document any findings or lessons for use in performance assessments.
Suggested Questions: How can WZ impact assessment help during construction?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Construction is the stage where the project is actually built in the field. The decisions made during the planning, preliminary engineering, and design stages are implemented during the construction stage. During construction, agencies focus on implementing the TCP, managing the construction project, facilitating safety for motorists and workers, and maintaining traffic through the work zone. Recordkeeping of day-to-day project activities and tracking of project progress is performed using field diaries and project logs. It is important to monitor the TMP in the field for effectiveness. The TMP should be adjusted to help manage the impacts.
Possible Problems: None

## Slide 17: Managing Impacts During Construction: Back-of-Queue Strategies
Image: ATSSA
Notes: 17
Key Message: Define the term queue
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A queue by definition is a line of people or vehicles waiting their turn. In the case of vehicles, each is waiting to get through a capacity restriction in a work zone. Queues can extend for miles upstream of the capacity restriction. Prior to a queue, flow can be very unstable. As queues dissipate, the flow is relatively stable.
Suggested Questions: What is the greatest safety risk from a queue? Speed variability, which creates greater rear-end crash risk.
Additional Information: None
Possible Problems: None

## Slide 18: Where are Queues Likely to Occur?
In the advance warning area for lane closures
Upstream of the advance warning area (more dangerous)
In the traffic space near the work area itself
Image: FHWA
Notes: 18
Key Message: Describe some common issues associated with queues
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: These areas can commonly experience queuing. The advance warning area provides information to motorists and can experience queues due to the downstream taper, for example. Queues may also extend upstream of the advance warning area, and the back-of-queue may extend past the first advance warning sign. Queues may also form adjacent to the work space as equipment moves in and out, causing temporary queuing.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 19: Back-of-Queue Issues
Increased crash risk, particularly rear-end crashes
Potentially large variability in speeds between approaching traffic and queued traffic
Impacts on driver expectations
  They may be accustomed to unencumbered travel and may have a slower perception-reaction time
Notes: 19
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: It is widely recognized that when congestion develops and queues form at the approach to a work zone, the risk of crashes increases, especially on highways where speeds are high and drivers are accustomed to unencumbered travel. These types of conditions may make queuing situations even more difficult for drivers to navigate safely. Queuing can lead to increased rear-end crash risk due to the higher speed of traffic approaching the back-of-queue. The higher the variability in speed, the higher the crash risk. Also, the crash may be more severe with injuries and possibly fatalities due to the high speed variability. According to a study conducted by the Liberty Mutual Research Center for Safety and Health, rear-end collisions account for 31% of crashes that occur at highway construction sites. The same study noted that 26% of crashes involved a stopped or slowing vehicle in the work zone.
Suggested Questions: None
Additional Information: Statistics source – “Motor vehicle crashes in roadway construction workzones”. Accident Analysis and Prevention, Volume 28, Issue 1, January 1996.
Possible Problems: None

## Slide 20: Back-of-Queue Issues
Geometry of roadway
  Limited sight distance to the back-of-queue due to curvature
Impacts from recurring congestion
Multiple public access points
Impacts near work vehicle access/egress points
Notes: 20
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: End-of-queue risks can be compounded by other site-specific conditions, such as limited sight distance and roadway curvature. Recurring congestion may also compound the problem. Roadway geometry may make it difficult for drivers to see a queue in enough time to be able to slow and stop. Access points near a traffic queue may make merge and diverge conditions less safe, and areas near work vehicle access points may also experience greater queue impacts.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 21: Why Should We Analyze Queues?
Analysis can provide valuable insights into the anticipated:
  Length of queue
  Time when queues may occur
  Location of queue
  Variability in traffic speeds
Analysis helps determine potential treatments for the problem
Notes: 21
Key Message: Describe some common issues associated with queues.
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Analysis of work zone impacts can help identify when and where queues are likely to occur. This helps to identify when mitigation strategies are needed and which strategies would be appropriate. We will discuss some treatments later. The more knowledge we have about the potential problems and issues, the better we can design treatments for the specific issues.
Suggested Questions: None
Additional Information: None
Possible Problems: We will hold off on discussing treatments until the analysis techniques have been described.

## Slide 22: Analyzing Potential Queues
When the volume to capacity ratio (V/C) exceeds one, a queue forms
Source: ATSSA
Notes: Key Message: Discuss demand as it relates to capacity
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Queues build as traffic demand increases above the capacity of the facility. A volume to capacity (v/c) ratio compares demand to capacity. A v/c ratio is less than one for undersaturated conditions, equal to one for saturated conditions, and greater than one for oversaturated conditions. Demand accurately represents the volume crossing a point on the roadway plus queued vehicles, while volume is simply a traffic count for a given time period. Queues can build rapidly once oversaturated conditions are present.
Suggested Questions: How can you have a v/c ratio greater than 1? It’s because of the stored vehicles in the queue that aren’t processed immediately, making the demand higher than the capacity. If you use traffic counts, do you typically get volume or demand? Typically volume, as the counts for a spot location do not represent the vehicles stored in the queue at the end of the count period. Additional methods or equipment would be needed to measure true demand that includes queued vehicles.
Additional Information: None
Possible Problems: None

## Slide 23: Example: V/C Estimate
This is a rough estimate of the potential for queuing if no other data are available
Source: ATSSA
Notes: 23
Key Message: Discuss how to calculate (roughly) a V/C ratio given planning level data
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is a high level analysis meant to illustrate how to calculate a rough estimate of a V/C ratio given only AADT. Begin with AADT, assume a directional split (60% for one direction is used in this example), use the factor 0.10 (commonly 10% of the total daily traffic occurs during the peak hour), estimate a capacity, and then calculate a V/C ratio. One can perform a sensitivity analysis to determine where the V/C break point lies (in this simplistic example, an AADT of 25,000 would reach capacity during the peak hour).
Suggested Questions: What might be an issue with the volumes used in a tool such as this? They may be counts and may not represent true demand. How would you measure demand? Count the vehicles in the queue at the end of the count period and add them to the volume.
Additional Information: AADT = average annual daily traffic (vpd), Capacity in vph.
Possible Problems: None

## Slide 24: Measured Average Work Zone Capacities for Freeways
Number of Lanes
Avg. Capacity
Normal | Open | vph | vphpl
3 | 1 | 1,170 | 1,170
2 | 1 | 1,550* | 1,550*
5 | 2 | 2,740 | 1,370
4 | 2 | 2,960 | 1,480
3 | 2 | 3,720* | 1,860*
4 | 3 | 4,560 | 1,520
Source: TRB, HCM Special Report 209
Notes: Key Message: Provide example of rough estimates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This table provides example capacities for lane closure scenarios. The columns on the left show how many lanes are open (“open”) from a given original number of lanes per direction (“normal”). The columns on the right show the average capacity for all lanes open (vph) and for each lane (vphpl).
Suggested Questions: How do we account for trucks? Convert them to passenger cars using passenger car equivalents (pce). Generally, a truck is equal to 2 passenger car equivalents. What is a truck (semi, delivery truck, etc.)? Anything with more than four tires touching the pavement (would include a six tire pick-up truck and count it the same in terms of impact as a an eighteen wheel semi!)
Additional Information: This report is from 1985 but the data is still applicable. Some newer values are shown with an asterisk from the 2000 HCM.
Possible Problems: Some may be familiar with numbers such as approximately 2,400 vphpl as capacity. The 2,400 number is an ideal capacity (no trucks, level terrain, shoulder, etc.). The numbers on this table are MEASURED capacities, so these numbers are more accurate (however some are based on limited observations). TRB Special Report 209 is the Highway Capacity Manual.
24

## Slide 25: Ohio-DOT Permitted Lane Closure Spreadsheet (PLCS)
Image: Ohio DOT
Notes: Key Message: Discuss, as an example, the Ohio Department of Transportation Permitted Lane Closure Spreadsheet (PLCS) Tool
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Some agencies have developed lane closure policies, lane closure analysis tools, or permitted lane closure maps that guide lane closure decisions.
This tool allows ODOT to determine if queues exceed their threshold. Unless the queue can be completely eliminated, they can estimate where it will end and determine the appropriate mitigation strategies. It is one example of how demand can be compared to capacity to determine whether or not queuing may occur. The capacity per lane is 1490 vphpl (a “spot” location) for this particular example. When the table shows a demand higher than 1490 vphpl and queues are expected to exceed the tolerance level, lane closures are not permitted during those time periods.
Suggested Questions: What might be an issue with the volumes used in a tool such as this? They may be counts and may not represent true demand. What would a queue estimate allow us to do differently than without it? It would let us place signs further upstream or add signs to the traffic control plan as an example of one specific treatment.
Additional Information: http://plcm.dot.state.oh.us//plcm/plcm_web.jsp.
Possible Problems: None

## Slide 26: Traffic Analysis Considerations
Seasonal variation
Demand fluctuation
Fluctuation within the peak hours or peak periods
Data accuracy
Image: FHWA
Notes: Key Message: Discuss considerations when performing an analysis
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Assess data as part of the planning process to determine the type of analysis that is feasible given the adequacy and coverage of the data. The analysis is only as good as the data used to predict impacts from lane closures, for example. Analysis using good data will help determine the extent of the impacts (such as whether or not queuing may exist for long periods of time). Additionally, understanding the limitations of the data can help determine the best analysis technique to use. Students may realize that data from congested time periods will underestimate demand and skew the analysis.
Suggested Questions: What might cause fluctuation during a peak hour? An example would be a plant shift letting out and flooding the network for a short time period. We account for this using the peak hour factor.
Additional Information: None
Possible Problems: None

## Slide 27: A Process-Oriented Approach
Comparison
of Alternatives
Design
Detailed
Analysis
Notes: 27
Key Message: Discuss the process for determining the best design
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Analysis of data will help understand potential issues for the project. The analysis produces specific metrics and measures for each alternative that can then feed into detailed design, staging, other requirements, and traffic control plan development.
Suggested Questions: Why is this a cycle? Due to the fact that there may be more than one alternative requiring more refined analysis at the design stage.
Additional Information: None
Possible Problems: None

## Slide 28: Choosing Mitigation Strategies
Once potential impacts are understood, appropriate strategies can be designed
Analyzing impacts can help determine the need for strategies
Design solutions that are tailored to solve a specific problem
Notes: Key Message: Introduce mitigation strategies
Est. Presentation Time: 1 minute
Explanation of Cues/Builds: None
Suggested Comments: Several different mitigation strategies can be considered to lessen impacts from road work. Planning-level analysis can help eliminate alternatives that would cause impacts above a tolerance threshold. Once impacts are known and quantified, mitigation techniques can be designed into the project. This occurs when the best alternative still has some potential issues that are unavoidable but can be treated.
Suggested Questions: Are there techniques used in your state to mitigate impacts?
Additional Information: None
Possible Problems: None

## Slide 29: Types of Strategies
Reducing/eliminating the end of queue
Strategies to treat the end of the queue
Communications techniques to improve awareness of impacts for enhanced trip planning
Image: FHWA
Notes: 29
Key Message: Discuss types of strategies to mitigate back-of-queue issues
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Ideally we eliminate the queue to the degree we can through good design, time of day restrictions, etc. For remaining queues, we provide treatment and motorist awareness to mitigate the impacts. We will go into these strategies more on the next slides.
Suggested Questions: What types of strategies have you used? How did they work?
Additional Information: None
Possible Problems: None

## Slide 30: Queue Reduction/Elimination - Nighttime Construction
May reduce or eliminate a queue that would normally occur during the day
Image: FHWA
Notes: 30
Key Message: Discuss the use of nighttime construction (may also be referred to as “off peak” work)
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Performing construction during nighttime hours, when traffic demand is lower, can reduce the frequency of queuing as compared with daytime work, when traffic demand is higher, and the potential for queuing is greater. It is becoming more and more common especially in urban areas. Analysis can help determine when nighttime work may alleviate back-of-queue issues that might occur if work were performed during daytime hours. Agencies may also reduce or eliminate queues by maintaining the same number of lanes during construction as prior to construction (by reducing lane widths, for example) or by increasing the length of taper or changing the location of the beginning of the taper.
Suggested Questions: What are some trade-offs to working at night compared with daytime? Noise issues, visibility, drowsy drivers, impaired drivers, limited work durations, and others. These considerations should be part of the decision-making process.
Additional Information: None
Possible Problems: None

## Slide 31: End of Queue Treatment: Proper TTC Setup
Important for alerting motorists of any potential hazards
Use appropriate devices and possibly law enforcement personnel for visibility
Image: ATSSA
Notes: 31
Key Message: Discuss the importance of proper setup of temporary traffic control devices
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Proper design and installation of devices is important. For example, sign spacing guidelines from the MUTCD may be exceeded to account for long queues. Drivers approaching the queue have the appropriate advanced warning of the potential hazard downstream. By analyzing impacts, designers can exceed the MUTCD sign spacing requirements and locate the advance warning signs upstream of the back-of-queue.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 32: End of Queue Treatment - Use of Law Enforcement Personnel
Image: ATSSA
Notes: 32
Key Message: Discuss the use of law enforcement personnel
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: Law enforcement vehicle appears on click.
Suggested Comments: Law enforcement personnel may provide presence as opposed to active enforcement. We focus on presence / visibility as a mitigation technique. For positioning, one state has a policy to have the officer between the 2nd and 3rd sign, on the shoulder, facing traffic, headlights off, emergency lights flashing. This is when motorists are about to make their maneuvers. If safe, the officer will move upstream with the queue as it builds to provide visibility in advance of the back-of-queue. Obviously this is situation specific and local agency policy should guide such a practice. We are emphasizing that this is one example, and not a requirement.
Suggested Questions: What is your policy? What do you think about this example?
Additional Information: There is little information on this. This is what one state (Louisiana) is doing. This is not required by the MUTCD or any standard that we are aware of.
For incidents, the MUTCD defines “Safe-Positioned” as the positioning of emergency vehicles at an incident in a manner that attempts to protect both the responders performing their duties and road users traveling through the incident scene, while minimizing, to the extent practical, disruption of the adjacent traffic flow. Possible Problems: This is a suggestion only and varies by location.

## Slide 33: End of Queue Treatment – Intelligent Transportation Systems
Image: FHWA
Notes: 33
Key Message: Discuss the use of Intelligent Transportation Systems in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: ITS can be used for mobile traffic monitoring and management. Some systems are active (physically control traffic such as the dynamic lane merge system) while others are passive (provide general information). Advance warning of slow or stopped traffic ahead may alleviate back-of-queue issues. Queues can be monitored by ITS technologies (sensors, cameras, etc.) that provide enhanced information to practitioners for decisions about the appropriate treatments to implement.
Suggested Questions: None
Additional Information: Examples include the CB Wizard system that alerts truck drivers to work zone issues, Dynamic Early Merge systems that create an enforceable “Do Not Pass When Flashing” zone, Late Merge systems that use both lanes but guide motorists to take turns at the merge point, real-time information systems that provide motorists with work zone congestion and delay information, and variable speed limit systems that can flatten the speed variability approaching the work zone by changing the posted speed in real-time.
Possible Problems: Researching some examples and spending a few minutes discussing issues and potential ITS solutions may be warranted.

## Slide 34: End of Queue Treatment – Dynamic Lane Merge System
Image: FHWA
Notes: 34
Key Message: Discuss the use of Dynamic Lane Merge Systems in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Dynamic Lane Merge Systems actively control traffic in advance of the taper. They have benefits such as reduced aggressive maneuvers at the merge point and supplemental advance warning information. Traffic is lined up into one lane so that smoother traffic flow occurs prior to the lane closure. It may also help draw extra attention to an area where queuing potential may occur.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 35: End of Queue Treatment – An Example From South Carolina
Some projects require truck-mounted PCMS to display queue warnings
Required when development of a lane closure-induced queue is evident
Truck/TMA with operator shall be placed on the shoulder; PCMS shall be 2,000 feet in advance of queue
Notes: 35
Key Message: Discuss truck mounted PCMS to display queue warnings in South Carolina
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: South Carolina DOT has a policy on use of truck mounted PCMS to display queue warnings. An excerpt from the policy is shown below:
1. The contractor shall provide a truck mounted changeable message sign for each lane closure when development of a traffic queue is evident. The contractor shall utilize the sign to provide advance notice to motorists that the motorists are approaching a traffic queue and should be prepared to stop.
2. The contractor shall place a truck mounted changeable message sign manned with an operator at all times on the shoulder of the roadway immediately upon the development of a traffic queue. The truck mounted changeable message sign shall remain no less than 2,000 feet in advance of the traffic queue at all times. Placement of the truck on the shoulder of the roadway without an operator is prohibited.
3. The contractor shall include a truck mounted attenuator only on vehicles over 5,000 lbs GVW.
4. The department requires the contractor to be prepared to stop work immediately and remove the lane closure if a TMA is unable to be provided in advance of a queue.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 36: End of Queue Monitoring – Portable or Permanent Cameras
Images: ASTI
Notes: 36
Key Message: Discuss the use of closed circuit television cameras in work zones
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Closed Circuit Television (CCTV) cameras can be used to monitor queues in and around work zones. As the queue grows, temporary traffic control personnel can monitor the camera images and implement strategies such as adjusting sign locations and spacing. Such CCTV devices can be portable or be part of a permanent ITS deployment. The ones shown here are portable, with a solar platform. Video, weather, and traffic sensors can also be combined on the same platform with wireless communications.
Suggested Questions: None
Additional Information: The pictures shown here are courtesy of Noah Jenkin of ASTI (an ITS vendor). The CCTV cameras are not required for the portable ITS system in operation in the location where these photos were taken, but they are an enhancement to the ITS deployment that allows for queue monitoring and manual adjustments to traffic control.
Possible Problems: None

## Slide 37: Public Information and Outreach
Project flyers
Websites
Marketing Materials
Signs
Alternate Route
Information
Traveler Information
Traffic Reports
Image: FHWA
Notes: 37
Key Message: Discuss types of public information and outreach strategies
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Many agencies provide advance information to motorists in the form of brochures, websites, and via other marketing materials. Agencies also use the media to provide information to motorists on upcoming construction projects and alternate routing, especially those with lane closures. Some additional information will likely have more of an effect on queue issues compared with general information sources such as brochures and flyers. Information may include travel times, delay, general messages on work zone conditions, and may warn motorists of potential hazards ahead. It may also include information on alternate routes or alternate means of transportation during the construction period. Sections 6I.02 and 6I.03 of the MUTCD recommend warning signs in advance of the end of queue for incidents.
Suggested Questions: What types of strategies have you used? How did they work?
Additional Information: None
Possible Problems: None

## Slide 38: Work Zone Inspection – An Example from Maryland
Includes multiple aspects of work zone operations (temporary traffic control devices as well as queuing)
Maryland SHA has a checklist that includes work zone impacts, ITS, traffic operations strategies, etc.
Notes: 38
Key Message: Discuss the role of inspection in queue identification and mitigation
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Queues may occur that were not anticipated prior to construction, or the queue may be longer than anticipated. Inspection plays an important role in queue verification and response. Inspectors can use a checklist, similar to the one described for Maryland, to note information about the queues and relay the information to the appropriate people for potential field modifications of temporary traffic control or other treatments and strategies.
Suggested Questions: None
Additional Information: Temporary Traffic Control Inspection Form (MD SHA): http://www.sha.maryland.gov/OOTS/14AppETTCInspectionFormmastercopyRev2.pdf
Possible Problems: None

## Slide 39: 6. During Performance Assessment
Quantitatively evaluate the;
  Safety
  Mobility
  Constructability
  Public perception and satisfaction
Image: FHWA
Notes: Key Message: Performance assessment
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are four key measures of work zone performance: Safety, Mobility, Constructability and public perception and satisfaction. Where feasible and appropriate, these performance measures should be evaluated quantitatively. In the absence of funding and/or data availability, measures of performance may be evaluated qualitatively.
Suggested Questions: How can WZ impact assessment help during performance assessment?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm. Periodic evaluation of work zone policies, processes, procedures, and work zone impacts aids in the process of addressing and managing the safety and mobility impacts of work zones. Performance assessments both at the project-level and program-level provide the required feedback to make policy, process, procedure, and program improvements and evaluate the effectiveness of work zone management strategies. There are four key measures of work zone performance: Safety, Mobility, Constructability and public perception and satisfaction. Where feasible and appropriate, these performance measures should be evaluated quantitatively. In the absence of funding and/or data availability, measures of performance may be evaluated qualitatively.
Possible Problems: Work zone performance assessment is not intended to require agencies to embark on a large data collection, storage, and analysis effort. The goal is to improve work zone safety and mobility by making effective use of the available data and information sources.

## Slide 40: 7. During Maintenance and Operations
To enhance procedures
To help plan and coordinate
To implement and manage for minimal impact
To incorporate features
Image: FHWA
Notes: Key Message: WZ impacts assessment in maintenance and operations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Assessing and managing the work zone impacts of M&O activities involves the following four key activities:
• Enhance agency procedures so that the direct safety and mobility impacts of M&O activities are minimized and better managed (e.g., improving TTC procedures, improving the visibility of maintenance workers/vehicles, better public information and advance warning systems, permitted lane-closure times, off-peak/nighttime work).
• Plan and coordinate M&O such that overall system-wide impacts are minimized (e.g., performing M&O activities as part of planned construction projects to minimize doing the M&O work as a separate activity – “don’t dig up the same road twice”).
• Implement and manage M&O activities such that they have minimal impacts on other construction projects and vice-versa (e.g., consider detour routes, diversions, adjacent highway sections).
• Incorporate features in construction projects that would facilitate future M&O with minimum disruption (e.g., wider shoulders, maintenance turn-abouts, designated pullouts).
Suggested Questions: How can WZ impact assessment help during M&O?
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 41: Impacts Assessment During M&O Activities
Need to be addressed from the overall system management perspective
Principles are the same
Image: FHWA
Notes: Key Message: WZ impacts assessment in maintenance and operations
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
Suggested Questions: The work zone impacts of M&O activities need to be addressed from the overall system management perspective in addition to the individual activity/corridor perspective. Work zone impacts assessment in M&O involves the same concepts and guidance presented in prior sections. The types of work zone safety and mobility issues and management strategies to consider are basically the same.
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/index.htm
Possible Problems: None

## Slide 42: Module Recap
What is a WZ impacts assessment?
When do we perform a WZ impacts assessment? Why?
What constitutes (key components) a work zone impact assessment?
How do we analyze back-of-queue issues?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.