## Slide 1: -MODULE 3- Analysis Approaches and Methodologies
Work Zone Traffic Impact Analysis
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Module 3 discusses WZ analysis approaches and methodologies
Suggested Questions: None
Additional Information: None
Possible Problems: None.

## Slide 2: Module Objectives
Discuss analysis (problem-solving) approaches and their application to WZ analysis
Discuss various tools available for work zone impact analysis: Strengths and weaknesses
Discuss their challenges and limitations
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Traffic Analysis Tools Can Help:
Improve the decision-making process
Evaluate & prioritize alternatives
Improve design and lower costs
Reduce disruptions to traffic
Present strategies to stakeholders
Operate & manage roadway capacity
Monitor performance
Notes: Key Message: Traffic Analysis Tools Applications
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Traffic analysis tools are designed to assist transportation professionals in evaluating the strategies that best address the transportation needs of their jurisdiction. Specifically, traffic analysis tools can help practitioners:
Improve the decision-making process. Traffic analysis tools help practitioners arrive at better planning/engineering decisions for complex transportation problems. They are used to estimate the impact of the deployment of traffic management and other strategies, and to help set priorities among competing projects. In addition, they can provide a consistent approach for comparing potential improvements or alternatives. Evaluate and prioritize planning/operational alternatives. This typically involves comparing “no build” conditions with alternatives, which include various types of potential improvements. The impacts are reported as performance measures and are defined as the difference between the no-build and alternative scenarios. The results can be used to select the best alternative or prioritize improvements, increasing the odds of having a successful deployment. Improve design and evaluation time and costs. Traffic analysis tools are relatively less costly when compared to pilot studies, field experiments, or full implementation costs. Furthermore, analytical tools can be used to assess multiple deployment combinations or other complex scenarios in a relatively short time. Reduce disruptions to traffic. Traffic management and control strategies come in many forms and options, and analytical tools provide a way to cheaply estimate the effects prior to full deployment of the management strategy. They may be used to initially test new transportation management systems concepts without the inconvenience of a field experiment. Present/market strategies to the public/stakeholders. Some traffic analysis tools have excellent graphical and animation displays, which could be used as tools to show “what if” scenarios to the public and/or stakeholders. Operate and manage existing roadway capacity. Some tools provide optimization capabilities, recommending the best design or control strategies to maximize the performance of a transportation facility. Monitor performance. Analytical tools can also be used to evaluate and monitor the performance of existing transportation facilities. In the future, it is hoped that monitoring systems can be directly linked to analytical tools for a more direct and real-time analysis process.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/trafficanalysistools/toolbox.htm
Possible Problems: Not all of these tools are specifically for work zones. The use of tools is not the only way to do impacts assessment and the use of tools is not required.

## Slide 4: Traffic Analysis Tools
Several, varying in level of complexity & capabilities, are available
Some designed specifically for WZ applications
Others, although not designed specifically for work zones, may be used
Image: ATSSA
Notes: Key Message: Traffic Analysis Tools
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: There are several tools available to perform impacts analysis. Some designed specifically for WZ applications Others, although not designed specifically for WZ, can be used.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/trafficanalysistools/toolbox.htm
Possible Problems: Not all of these tools are specifically for work zones. The use of tools is not the only way to do impacts assessment and the use of tools is not required.

## Slide 5: FHWA “Traffic Analysis Toolbox”
A collective term used to describe a variety of software-based analytical procedures and methodologies
Provides guidance, recommendations, and examples on the selection and use of traffic analysis tools
Notes: Key Message: Introduce FHWA’s traffic Analysis Toolbox
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: "Traffic analysis tools" is a collective term used to describe a variety of software-based analytical procedures and methodologies that support different aspects of traffic and transportation analyses. Traffic analysis tools include methodologies such as sketch-planning, travel demand modeling, traffic signal optimization, and traffic simulation. The purpose of the Traffic Analysis Toolbox is to provide guidance, recommendations, and examples on the selection and use of traffic analysis tools.
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/trafficanalysistools/toolbox.htm
Possible Problems: Not all of these tools are specifically for work zones.

## Slide 6: Tool Selection Principles
No single tool can do everything
No black box
Tool chosen depends on
  Accuracy needed
  Data available
  Resources available
Notes: Key Message: Introduce tool selection principles
Time: 2 min
Builds: None
Suggested Comments: There is no one analytical tool that can do everything or solve every problem. The method or tool selected for any analysis should be consistent with the analysis needs and fit within budget and resource requirements. Using too complex of a tool for the analysis needs, such as using a microsimulation tool for preliminary screening of scenarios, may result in a poor use of resources. At the same time, using too simplistic of a tool for the situation, for example using a travel demand model for detailed design of an operational strategy, may result in inaccurate or unreliable results. Some tools were not designed specifically for work zones but they can be used to analyze work zone situations.
Additional Information: None
Questions/Interactivity: None
Possible Problems: Will expand on these points in next module.

## Slide 7: Tool Selection Principles
Multiple tools may be necessary
Select the simplest tool (or approach!!) that best matches the needs of your project
FHWA does not require the use of tools at all!
Image: ATSSA
Notes: Key Message: Introduce tool selection principles
Time: 2 min
Builds: None
Suggested Comments: Although there are several tools are available, it is important to note that tools may not have to be used at all. FHWA does not require tools to be used to satisfy the TO requirement of the TMP. Sometimes it is best to keep it simple and use the simplest approach. In other words, choose the approach that best meets your needs.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 8: Three Levels of Detail
ESTIMATES
DETERMINISTIC TOOL
SIMULATION
MODEL
Increasing accuracy
Increasing complexity
Notes: Key Message: Explain the tradeoff between “complexity” (of modeling) and “accuracy” (of results).
Time: 1-2 minute(s)
Builds: None
Suggested Comments: Rough estimates are very simple to use, but perhaps not very accurate. If accuracy is needed then a more accurate tool will be required. As a rule of thumb, the simpler the tool, the less accuracy.
Deterministic, obviously a bit more complex, also gives better results; but has limitations, mainly the inability to study stochastic (random) events.
Simulation moves up both scales.
Additional Info: Use the pyramid to emphasize the tradeoff between complexity and accuracy.
Questions/Interactivity: Ask the class what is the main advantage of simulation. (You can’t field-study future or changed conditions, so simulation becomes a very powerful tool.)
Possible Problems: None

## Slide 9: Estimates
Simple analysis is better than nothing
Combine with historical data
Understand what will happen if you implement the TCP
Most common?
Image: ATSSA
Notes: Key Message: Discuss estimates
Time: 1-2 minute(s)
Builds: None
Suggested Comments: Sometimes, a simple estimate is all that is needed to give us a rough idea of the WZ impacts. Sometimes, a rough estimate is all we need to get an idea of the conditions that will be created when the TCP is implemented. Let’s look at an example.
Additional Info: Sketch-planning tools, HCM methodologies, travel demand models, macroscopic simulation models, and some traffic signal optimization tools will produce results that are often expressed as “maximum” or “average”. These tools do not analyze traffic at the individual vehicle level. Results are considered average for the time period and the network and give the analyst an idea of what traffic impact might be like during work zone implementation. These tools are usually less data intensive and may provide enough detail for many work zone analyses.
Questions/Interactivity: Is this commonly done? What are your thoughts? Try to generate discussion.
Possible Problems: FHWA does not require tools to be used at all, so rough estimates may be a satisfactory approach, depending on the situation.

## Slide 10: Measured Average Work Zone Capacities for Freeways
Normal | Open | vph | vphpl
3 | 1 | 1,170 | 1,170
2 | 1 | 1,340 | 1,340
5 | 2 | 2,740 | 1,370
4 | 2 | 2,960 | 1,480
3 | 2 | 2,980 | 1,490
4 | 3 | 4,560 | 1,520
Source: TRB, HCM, Special Report 209
Number of Lanes
Avg. Capacity
Notes: Key Message: Provide example of rough estimates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Another way is to use a table like this for estimation purposes. The columns on the left show how many lanes are open (“open”) from a given number (“normal”). The columns on the right show the average capacity for all lanes open (vph) and for the each lane (vphpl).
Suggested Questions: None
Additional Information: This report is from 1985 but the data is still applicable.
Possible Problems: Someone may be familiar with the number 2,000 vphpl as capacity. The 2,000 number is an ideal capacity (no trucks, rolling, shoulder, etc.). The numbers on this table at MEASURED capacities, so these numbers are more accurate.

## Slide 11: Estimates
0
200
400
600
800
1000
Cap.=1,000 vph
Cap.=500 vph
Congestion periods!
Congestion periods!
Time of Day
Image: ATSSA
Notes: Key Message: Provide example of rough estimates
Est. Presentation Time: 2-3 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In this example, capacity of the roadway was 1,000 vehicles per hour was before a closure, resulting in no congestion. With the closure, the capacity DECREASED to 500 vph, resulting in two congestion periods.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 12: Problem-Solving Methods
System
Experiment with
Actual System
Experiment with
Model of System
Physical
Model
Mathematical
Models
Deterministic
Simulation
Empirical
Notes: Key Message: Describe a logical problem-solving process.
Time: 2 min
Builds: <Click> to “X” out.
Suggested Comments:
Additional Info: Trace the serial “paths” for analysis. Briefly describe each path. Point out that in our context we don’t use physical models.
System = the traffic situation we wish to study.
Experiment with actual system = the “real world.”
Empirical = field studies.
Experiment with model… = using some model.
Mathematical models = a mathematical representation of the real world, using algorithms, equations, etc
Deterministic = derived formula (e.g., HCM).
Simulation = algorithm(s) as defined previously.
Physical = actual physical thing (e.g., a driving simulator).
Questions/Interactivity: None
Possible Problems: None

## Slide 13: Empirical Problem Solving
Highest credibility
Too expensive for most purposes
Notes: Key Message: Disadvantages of empirical studies
Time: 1 min
Builds: None
Suggested Comments: The word empirical denotes information gained by means of observation, experience, or experiment, as opposed to theoretical. It involved the collection of field data, which is expensive. Empirical is the most difficult in terms of resources, but if done right should yield the best results; however, as we’ve seen it isn’t always practical to do field studies.
Additional Info: Data collection techniques include:
Intersection counter board [turning movement counts (TMC)],
Radar gun (speed), and
Camera (volumes, turns, etc.).
Mention that empirical analysis does play an important role in model calibration.
Questions/Interactivity: Ask for examples of what these can collect (in parentheses above). Why the highest credibility? Based on actual field data.
Possible Problems: None

## Slide 14: Mathematical Models
If we cannot experiment with the real system, we may represent it mathematically though a model
May be
  Deterministic
  Simulation
Mathematical
Models
Deterministic
Simulation
Notes: Key Message: Discuss application of mathematical models
Time: 1 min
Builds: None
Suggested Comments: If we cannot experiment with the real system, we may represent it mathematically though a model. These models may be deterministic or simulation. Let’s explain.
Additional Info: None
Questions/Interactivity: None
Possible Problems: Treat as an intro slide.

## Slide 15: Deterministic Models
Same answer every time
Usually involves an equation or set of equations
Usually involves simple assumptions
Easy to use
Notes: Key Message: These are the advantages of deterministic models.
Time: 30 sec
Builds: None
Suggested Comments: These are the basic characteristics of deterministic models. Emphasize that the simplifying assumptions often make deterministic models inappropriate for some applications. For example, if my model says that the probability of getting tails when tossing a coin is .5, if I toss it 100 times, I will ALWAYS get 50 tails. Is that the way it is in real life? No.
Additional Info: None
Questions/Interactivity: Ask what is the best known example of deterministic models? (HCM)
Possible Problems: None

## Slide 16: Simulation Models
A representation of the real world by means of mathematical models
In this case, it is “traffic simulation”
The representation is the software implementation of a mathematical “model” to produces random (“stochastic”) results
Notes: Key Message: Define the term “simulation” in general.
Time: 1 min
Builds: None
Suggested Comments: Technically, a computer program is not a “model” per se, but rather it is the implementation of mathematical models. However, “model” is often (mistakenly) used in the context of software. With simulation, it is based on random (stochastic) processes so tossing the coin 100 times may result in multiple numbers of tails every time the model is run.
Additional Info: Explain what a model is: a mathematical representation of the real world, using algorithms, equations, etc.
Questions/Interactivity: None
Math: coin flips, lottery, etc.; and
Physical: model ships, cars, wind tunnel, etc.
Possible Problems: Simulation models also assume “100 percent safe driving,” so they will not be effective in predicting how changes in design might influence the probability of collisions. In addition, simulation models do not take into consideration how changes in the roadside environment (outside of the traveled way) affect driver behavior within the traveled way (e.g., obstruction of visibility, roadside distractions such as a stalled vehicle, etc.).
Image Credit: https://www.graphenea.com/blogs/graphene-news/on-chip-random-number-generation-with-graphene

## Slide 17: Stochastic Models
Use random numbers
Have random outcomes
Need rules of operation
Track queue accumulation and service
Provide measures of performance
Notes: Key Message: These are the most common characteristics of stochastic models.
Time: 1-2 min
Builds: None
Suggested Comments: Stochastic models try to represent the randomness and uncertainty of real world events through probabilistic expressions. Most simulation models are stochastic in nature.
Additional Info: Definition: A stochastic process is one whose behavior is non-deterministic in that a system's subsequent state is determined both by the process's predictable actions and by a random element. From Greek for “guess” or “random”.
Questions/Interactivity: Ask what a random number is. If there seems to be doubt, ask everyone to write down a number between 1 and 5. Record the participants’ selected numbers (1-5) on a flip chart. There should be a fairly uniform distribution of those choosing 1, 2, etc. Thus, the class randomly selected these five numbers, each number having an equal chance of being selected.
Possible Problems: None

## Slide 18: For the Same Input Conditions:
Deterministic
Models
Same
results
Stochastic
Models
Varying
results
Notes: Key Message: Summarize previous point
Time: Less than 1 min
Builds: Text boxes appear on click
Suggested Comments:
Additional Info: Summarizing..
Questions/Interactivity: None
Possible Problems: Treat as a summary slides, to summarize the points just discussed.

## Slide 19: Empirical Problem Solving vs. Simulation
Empirical
  Expensive
  Data intensive
  More credibility
  Usually not suitable to WZ
Simulation
  May be expensive
  Data intensive
  Requires calibration
  Garbage in = garbage out
Notes: Key Message: Compare empirical and simulation
Time: 2-3 min
Builds: None
Suggested Comments:
Additional Info: Self explanatory
Questions/Interactivity: None
Possible Problems: Treat as a summary slides, to summarize the points just discussed.

## Slide 20: Advantages/Features of Traffic Simulation
Randomness of traffic and driver behavior
Saturated conditions
Queue overflow
Car following and platoon propagation
More precision
Image: ATSSA
Notes: Key Message: Explains indirectly some of the advantages and features of simulation.
Time: 1 min
Builds: None
Additional Info:
The randomness of the modeling is consistent with “random” human behavior.
Permitted left turns are particularly complex random events (i.e., the order of arrivals, aggressiveness of drivers, etc.).
Queue overflows have very uncertain effects, again due to random responses.
Car following and the interactions of vehicles in moving platoons are also very complex issues.
None of these can possibly be handled well by deterministic models, so simulation is the only real answer.
Questions/Interactivity: Ask for any other examples.
Possible Problems: None

## Slide 21: Types of Traffic Analysis Tools
Sketch-planning tools
Travel demand models
Analytical/ Deterministic tools
Traffic signal optimization tools
Simulation models
Notes: Key Message: Introduce types of traffic analysis tools
Time: 1 min
Builds: None
Additional Info: "Traffic analysis tools" is a collective term used to describe a variety of software-based analytical procedures and methodologies that support different aspects of traffic and transportation analyses. Traffic analysis tools include methodologies such as sketch-planning, travel demand modeling, traffic signal optimization, and traffic simulation.
Questions/Interactivity: Ask for any other examples.
Possible Problems: Intro slide. Avoid giving details here.

## Slide 22: 1. Sketch-Planning Tools
Produce general order-of-magnitude estimates of travel demand & traffic operations in response to transportation improvements
Allow for evaluation of specific projects or alternatives without conducting an in-depth engineering analysis
Not a substitute for detailed engineering analysis
Notes: Key Message: Introduce sketch-planning tools
Time: 1-2 min
Builds: None
Additional Info: These tools produce general order-of-magnitude estimates of travel demand and traffic operations in response to transportation improvements. They allow for evaluation of specific projects or alternatives without conducting an in-depth engineering analysis. Sketch-planning tools perform some or all of the functions of other analysis tool types using simplified analyses techniques and highly aggregate data. Such techniques are primarily used to prepare preliminary materials and budgets and are not considered a substitute for the detailed engineering analysis often needed later in the project design and implementation process. Sketch-planning approaches are typically the simplest and least costly of traffic analysis techniques, and are usually limited in scope, analytical robustness, and presentation capabilities. Examples of sketch-planning tools include QuickZone, Surface Transportation Efficiency Analysis Model (STEAM), and ITS Deployment Analysis System (IDAS).
Questions/Interactivity: Ask for any other examples.
Possible Problems: None

## Slide 23: 1. Sketch-Planning Tools
Typically the simplest and least costly of traffic analysis techniques
Usually limited in scope, analytical robustness and presentation capabilities
Notes: Key Message: Introduce sketch-planning tools
Time: 1-2 min
Builds: None
Suggested Comments: Sketch-planning tools vary in complexity from analyzing only individual roadway segments to network-based analyses. Often, sketch-planning tools will be based upon simple queuing techniques or volume-to-capacity relationships from the Highway Capacity Manual. Although work zone specific sketch-planning tools have been available for many years, as a whole they continue to evolve and become more sophisticated in terms of features, use and outputs. The strength of sketch-planning tools rests upon their relative ease of use and ability to conduct a rapid analysis. Typically, a sketch-planning tool will require fewer resources and less staff training to deploy than a mesoscopic or microscopic simulation model since they are simpler in terms of data requirements, calibration, and interpretation of the results. Regarding work zones, an analysis using a sketch-planning tool is normally quite rapid including both the input of the data and the model run time. This is important in cases where a decision needs to be made quickly.
Questions/Interactivity: Ask for any other examples.
Possible Problems: May not want to mention specific examples here. Wait until the specific tools are discussed.
Examples of Sketch-Planning Planning Tools:
Better Decisions: http://mctrans.ce.ufl.edu/store/description.asp?itemID=165
HDM (Highway Design and Management): http://hdm4.piarc.org/
IDAS (ITS Deployment Analysis System): http://idas.camsys.com/
IMPACTS: http://www.fhwa.dot.gov/steam/impacts.htm
MicroBENCOST: http://mctrans.ce.ufl.edu/store/description.asp?itemID=166
QuickZone: http://www.tfhrc.gov/its/quickzon.htm
SCRITS (Screening for ITS): http://www.fhwa.dot.gov/steam/scrits.htm
Sketch Methods: http://plan2op.fhwa.dot.gov/toolbox/toolbox.htm
SMITE (Spreadsheet Model for Induced Travel Estimation): http://www.fhwa.dot.gov/steam/smite.htm
SPASM (Sketch-Planning Analysis Spreadsheet Model): http://www.fhwa.dot.gov/steam/spasm.htm
STEAM (Surface Transportation Efficiency Analysis Model): http://www.fhwa.dot.gov/steam/index.htm
TEAPAC (Traffic Engineering Applications Package)/SITE: http://www.strongconcepts.com/Products.htm
TrafikPlan: http://mctrans.ce.ufl.edu/store/description.asp?itemID=162
TransDec (Transportation Decision): http://tti.tamu.edu/researcher/v34n3/transdec.stm
Trip Generation: http://mctrans.ce.ufl.edu/store/description.asp?itemID=179
Turbo Architecture: http://itsarch.iteris.com/itsarch/html/turbo/turbooverview.htm

## Slide 24: 2. Travel Demand Models
Regional planning models
Operate at the regional level, and cover a large geographic area (multiple cities and counties)
Not part of this course
Notes: Key Message: Introduce travel demand models
Time: 1-2 min
Builds: None
Additional Info: Travel demand models – Travel demand models have specific analytical capabilities, such as the prediction of travel demand and the consideration of destination choice, mode choice, time-of-day travel choice, and route choice, as well as the representation of traffic flow in the highway network. These are mathematical models that forecast future travel demand based on current conditions, and future projections of household and employment characteristics. Travel demand models were originally developed to determine the benefits and impacts of major highway improvements in metropolitan areas. Travel demand models are suited for static analyses and are not capable of dynamic traffic analysis (i.e., time-varying analyses). Therefore, they have only limited capabilities to evaluate ITS/operational strategies and operational characteristics such as speed, delay, and queuing. Examples of travel demand models include TransCAD, Cube, Quick Response System (QRS) model, Équilibre Multimodal, Multimodal Equilibrium 2 (EMME2), IDAS, and VISUM. Travel demand models are traditionally thought of as the large regional planning models used by Regional Planning Commissions and Metropolitan Planning Organizations throughout the U.S. and were originally developed to determine the benefits and impact of major highway improvements in metropolitan areas. To this end, a distinguishing feature of travel demand models is their geographic coverage. Generally speaking, travel demand models include an entire metropolitan area: a city, its suburbs, and the adjacent counties as required by law or need. The basic goal of these models is to forecast long-term future travel demand based on current conditions and projections of future household and employment characteristics.
Questions/Interactivity: Ask for any other examples.
Possible Problems: Avoid discussing specific tools here.
Examples of Travel Demand Models:
b-Node Model: http://mctrans.ce.ufl.edu/store/description.asp?itemID=482, CUBE/MINUTP: http://www.citilabs.com/minutp/index.html, CUBE/TP+/Viper: http://www.citilabs.com/viper/index.html, CUBE/TRANPLAN (Transportation Planning): http://www.citilabs.com/tranplan/index.html
CUBE/TRIPS (Transport Improvement Planning System): http://citilabs.com/trips/index.html, EMME/2™: http://www.inro.ca/products/e2_products.html, IDAS: http://idas.camsys.com/, MicroTRIMS: http://mctrans.ce.ufl.edu/store/description.asp?itemID=483, QRS II (Quick Response System II): http://my.execpc.com/~ajh/index.html, SATURN (Simulation and Assignment of Traffic to Urban Road Network): http://mctrans.ce.ufl.edu/store/description.asp?itemID=157, TModel: http://www.tmodel.com, TransCAD®: http://www.caliper.com/tcovu.htm, TRANSIMS (Transportation Analysis Simulation System): http://tmip.tamu.edu/transims/

## Slide 25: Travel Demand Models
Forecast long-term future travel demands based on current conditions
VISIM, Emme/2, TransCAD
Image: INRO
Notes: Key Message: Introduce travel demand models
Time: 1-2 min
Builds: None
Suggested Comments: For work zone analysis, one strength offered by travel demand models is their ability to predict area-wide traffic redistribution. For example, if an agency is considering closing an important urban freeway-to-freeway interchange for several months while it is rebuilt, a travel demand model could help evaluate the overall changes in total daily traffic volumes on various roadways throughout the region. However, travel demand models have limited capabilities to accurately estimate changes in operational characteristics (such as speed, delay, and queuing) resulting from the implementation of operational strategies and changes (including the effects associated with roadwork construction). Because these models are prepared at a broad regional scale, they may lack accurate intersection turn volumes, so they may not be appropriate for detailed operational studies. They may model only one or two time periods (such as the AM peak hour or the daily average), which may not be sufficient for analyzing time-specific work zone traffic management strategies. Some travel demand models contain only the total traffic volume on each link (combining the traffic volume from both travel directions). If this is the case, it may be difficult to adapt the model for analyzing routes or time periods that have unequal directional flows. For example, if the modeled volumes represent the Annual Average Daily Traffic, extensive re-working of the model may be required if the work zone analysis requires determining the directional peak hour flows into and out of a city’s central business district. Other limitations include their relative complexity and expense to build and maintain. However, these limitations must be balanced with the fact that these types of models can handle larger networks more efficiently than mesoscopic and microscopic simulation models. Another consideration is that most major metropolitan areas already have a travel demand model constructed that could be used as a foundation for developing a transportation network for another model type.
Additional Info: http://www.inro.ca/en/index.php
Questions/Interactivity: Ask for any other examples.
Possible Problems: EMME 3 Beta is now available.

## Slide 26: 3. Analytical/Deterministic Models
Highway Capacity Manual (HCM)-based, or HCS
Same results for same conditions
Based upon the deterministic relationships of flow, speed and density
Not suitable for over-saturated conditions
Image: TRB
Notes: Key Message: Introduce analytical/deterministic models
Time: 1-2 min
Builds: None
Suggested Comments: Analytical/deterministic tools (HCM Based) – Most analytical/deterministic tools implement the procedures of the Highway Capacity Manual (HCM). HCM procedures are closed-form, macroscopic, deterministic, and static analytical procedures that estimate capacity and performance measures to determine the level of service (e.g., density, speed, and delay). They are closed-form because they are not iterative. The practitioner inputs the data and parameters and, after a sequence of analytical steps, the HCM procedures produce a single answer.
Additional Info: None
Questions/Interactivity: Ask for any other examples.
Possible Problems: None
Image Credit: https://onlinepubs.trb.org/onlinepubs/trnews/trnews273hcm2010.pdf

## Slide 27: HCM Procedures
Attributes:
  Macroscopic
  Deterministic
  Static
Advantages
  Quick!
  Good for small projects
Image: TRB
Notes: Key Message: Introduce analytical/deterministic models
Time: 1-2 min
Builds: None
Suggested Comments: Analytical/deterministic tools (HCM Based) –HCM procedures are macroscopic (inputs and outputs deal with average performance during a 15-minute or a one-hour analysis period), deterministic (any given set of inputs will always yield the same answer), and static (they predict average operating conditions over a fixed time period and do not deal with transitions in operations from one state to another). As such, these tools quickly predict capacity, density, speed, delay, and queuing on a variety of transportation facilities and are validated with field data, laboratory test beds, or small-scale experiments. Analytical/deterministic tools are good for analyzing the performance of isolated or small-scale transportation facilities, but are limited in their ability to analyze network or system effects. Examples of other analytical/deterministic tools include Synchro, and the TEAPAC suite of programs.
Additional Info: None
Questions/Interactivity: Ask for any other examples.
Possible Problems: None
Image Credit: https://onlinepubs.trb.org/onlinepubs/trnews/trnews273hcm2010.pdf

## Slide 28: 4. Traffic Signal Optimization Tools
Largely based on HCM procedures
Designed to develop optimal signal phasing and timing plans for isolated signal intersections, arterial streets or signal networks
Examples are PASSER, SYNCHRO & TRANSYT-7F
Notes: Key Message: Introduce traffic signal optimization tools
Time: 1-2 min
Builds: None
Suggested Comments: Traffic signal optimization tools are used to develop signal timing plans for isolated signal intersections, signalized arterial corridors and signal networks. The FHWA Traffic Analysis Toolbox indicates many of the available traffic signal optimization tools as including the ability to conduct capacity calculations, cycle length, splits optimizations, and coordination/offset plans (5). With respect to work zones, traffic signal optimization tools are useful when developing a signal plan for a temporary traffic signal or analyzing signal plans when a detour route is routed to an existing signalized arterial roadway. The primary limitation of these tools is their single focus. Traffic signal optimization tools are typically used to provide supplementary analysis when analyzing the overall mobility impacts of a work zone.
Traffic signal optimization tools are similar to analytical/deterministic tools, and are largely based on HCM procedures. However, traffic signal optimization tools are primarily designed to develop optimal signal phasings and timing plans for isolated signal intersections, arterial streets, or signal networks. Some optimization tools can also be used for optimizing ramp metering rates for freeway ramp control. The more advanced traffic signal optimization tools are capable of modeling actuated and semi-actuated traffic signals, with or without signal coordination. Examples of traffic signal optimization tools include Progression Analysis and Signal System Evaluation Routine (PASSER), Signal Operations Analysis Package (SOAP), Synchro, Traffic Network Study Tool (TRANSYT-7F), Time-Space Diagram for Windows (TSDWin), and the TEAPAC suite of programs.
Additional Info:
Questions/Interactivity: Ask for any other examples.
Possible Problems: None

## Slide 29: 5. Simulation Models
Detailed analysis
Time-varying
Stochastic
Human performance
System-wide analysis
Analysis of over-saturated conditions
Image: Caltrans
Notes: Key Message: Simulation is far more detailed and can do these better than deterministic, if the models are good.
Time: 1 min
Builds: None
Additional Info: This is a review:
Simulation is clearly time-varying, which is like the real world.
Simulation is stochastic, although we’ll see later how we must make sure the stochastic effect is done properly in CORSIM.
Human performance is better emulated by these processes.
Comprehensive models permit use to analyze a wide range of geographic, geometric, infrastructure, traffic, and human behavioral conditions.
Questions/Interactivity: None
Possible Problems:
Source: None
Reference: None
Image Credit: Caltrans/CA4PRS software tool

## Slide 30: Simulation Models
Based on random number seeds
Different results for same conditions
Three levels of detail:
  Macroscopic
  Microscopic
  Mesoscopic
Notes: Key Message: Discuss simulation models
Time: 1-2 min
Builds: None
Suggested Comments: Simulation tools are effective in evaluating the dynamic evolution of traffic congestion problems on transportation systems. By dividing the analytical period into time slices, a simulation model can evaluate the buildup, dissipation, and duration of traffic congestion. By evaluating systems of facilities, simulation models can evaluate the interference that occurs when congestion builds up at one location and impacts capacity at another location. Also, traffic simulators can model the variability in driver/vehicle characteristics. Simulation tools, however, require a plethora of input data, considerable error checking of the data, and manipulation of a large amount of potential calibration parameters. Simulation models cannot be applied to a specific facility without calibration of those parameters to actual conditions in the field. Calibration can be a complex and time-consuming process. The algorithms of simulation models are mostly developed independently and are not subject to peer review and acceptance in the professional community. There is no national consensus on the appropriateness of a simulation approach.
Additional Info: Mesoscopic and microscopic simulation models and some traffic signal optimization tools provide detailed results. Tools in these categories provide results that model individual vehicle movements and turning patterns. These tools are usually more resource intensive and require much more data. The results provided give a detailed assessment of existing conditions and multiple work zone alternatives and provide the agency with a good representation of what field conditions will be like during work zone implementation. Detailed assessments are often reserved for large, Type I work zones that will affect large numbers of travelers for a long duration.
Questions/Interactivity: Ask for any other examples.
Possible Problems: None
Image Credit: https://www.graphenea.com/blogs/graphene-news/on-chip-random-number-generation-with-graphene

## Slide 31: Simulation Methods (Level of Detail)
Simulation
Macroscopic
Microscopic
Mesoscopic
(Mixed)
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 1 min
Builds: None
Additional Info: Some model applications are somewhat in between. Mesoscopic models may be characterized by tracking vehicles at the individual level, yet their behavior is governed by higher level traffic relationships (e.g., flow, speed, density relationships).
Mesoscopic models may be partially deterministic and stochastic or all deterministic, but having some characteristics of microscopic.
Stochastic = having random effects
Questions/Interactivity: None
Possible Problems: None

## Slide 32: 5a. Macroscopic Models
Based upon the deterministic relationships of flow, speed and density
Section-by-section, rather than individual vehicles
Image: FHWA
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 1 min
Builds: None
Additional Info: Macroscopic simulation models are based on deterministic relationships of flow, speed, and density of the traffic stream. The simulation in a macroscopic model takes place on a section-by-section basis rather than tracking individual vehicles. Macroscopic simulation models were originally developed to model traffic in distinct transportation subnetworks, such as freeways, corridors (including freeways and parallel arterials), surface street grid networks, and rural highways. They consider platoons of vehicles and simulate traffic flow in small time increments. Macroscopic simulation models operate on the basis of aggregate speed/volume and demand/capacity relationships. Macroscopic models have considerably less demanding computer requirements than microscopic models. They do not, however, have the ability to analyze transportation improvements in as much detail as microscopic models, and do not consider trip generation, trip distribution, and mode choice in their evaluation of changes in transportation systems. Examples of macroscopic simulation models include Bottleneck Traffic Simulator (BTS), Freeway Corridor Simulation Model (FREQ), Corridor Flow Simulation Software (CORFLO), PASSER, and TRANSYT-7F.
Questions/Interactivity: None
Possible Problems: Graphic on left is for decoration. No need to explain it.
Examples of Macroscopic Models:
BTS (Bottleneck Traffic Simulator): http://mctrans.ce.ufl.edu/store/description.asp?itemID=287, FREQ12: http://www.its.berkeley.edu/computing/software/FREQ.html
KRONOS: http://www.its.umn.edu/labs/itslab.html, METACOR/METANET: http://www.inrets.fr/ur/gretia/METACOR-Ang-H-HajSalem.htm, NETCELL: http://www.its.berkeley.edu/computing/software/netcell.html, PASSER II-02: http://ttisoftware.tamu.edu/fraPasserII_02.htm, PASSER III-98: http://ttisoftware.tamu.edu/fraPasserIII_98.htm, PASSER IV-96: http://ttisoftware.tamu.edu/fraPasserIV_96.htm, SATURN: http://www.its.leeds.ac.uk/software/saturn/index.html, TRAF-CORFLO (Corridor Flow): http://mctrans.ce.ufl.edu/store/description.asp?itemID=441, TRANSYT-7F: http://mctrans.ce.ufl.edu/store/description.asp?itemID=437, VISTA (Visual Interactive System for Transport Algorithms): http://vista.civil.northwestern.edu/

## Slide 33: Macroscopic Simulation Tools
Generally broken into:
  Regional planning models
  Delay estimation tools
Image: TRB
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 1 min
Builds: None
Additional Info: Macroscopic simulation models – Macroscopic simulation models are based on deterministic relationships of flow, speed, and density of the traffic stream. The simulation in a macroscopic model takes place on a section-by-section basis rather than tracking individual vehicles. Macroscopic simulation models were originally developed to model traffic in distinct transportation subnetworks, such as freeways, corridors (including freeways and parallel arterials), surface street grid networks, and rural highways. They consider platoons of vehicles and simulate traffic flow in small time increments. Macroscopic simulation models operate on the basis of aggregate speed/volume and demand/capacity relationships. Macroscopic models have considerably less demanding computer requirements than microscopic models. They do not, however, have the ability to analyze transportation improvements in as much detail as microscopic models, and do not consider trip generation, trip distribution, and mode choice in their evaluation of changes in transportation systems. Examples of macroscopic simulation models include Bottleneck Traffic Simulator (BTS), Freeway Corridor Simulation Model (FREQ), Corridor Flow Simulation Software (CORFLO), PASSER, and TRANSYT-7F.
Questions/Interactivity: None
Possible Problems: None
Image Credit: National Academies/TRB

## Slide 34: 5b. Microscopic
Simulate the movement of individual vehicles based on car-following and lane-changing algorithms
Highest level of detail
Extensive data on roadway geometry & traffic control
Image: FHWA
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 2-3 min
Builds: None. Picture is a CORSIM screen capture.
Additional Info: Microscopic simulation models simulate the movement of individual vehicles, based on theories of car-following and lane-changing. Typically, vehicles enter a transportation network using a statistical distribution of arrivals (a stochastic process), and are tracked through the network over small time intervals (e.g., one second or fraction of a second). Typically, upon entry, each vehicle is assigned a destination, a vehicle type, and a driver type. In many microscopic simulation models, the traffic operational characteristics of each vehicle are influenced by vertical grade, horizontal curvature, and super-elevation, based on relationships developed in prior research. Computer time and storage requirements for microscopic models are large, usually limiting the network size and the number of simulation runs that can be completed.
Questions/Interactivity: None
Possible Problems: None
Image Credit: FHWA/CORSIM tool

## Slide 35: Some Microscopic Simulation Tools
Simulate the movement of individual vehicles based on car-following and lane-changing algorithms
Highest level of detail
Extensive data on roadway geometry & traffic control
Image: FHWA
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 2-3 min
Builds: None. Picture is a CORSIM screen capture.
Additional Info: Examples of microscopic simulation models include Traffic Software Integrated System/Corridor Simulation (TSIS/CORSIM), INTEGRATION, SimTraffic, Wide Area Traffic Simulation (WATSim), VISSIM, and Parallel Microscopic Traffic Simulator (PARAMICS). Microscopic simulation models were developed to accurately represent transportation systems at the individual vehicle level. They simulate the movement of individual vehicles based on car-following and lane-changing theories and other parameters. Microscopic simulation models update the positions and intentions of individual vehicles every second (or fraction of a second) as they move through a network. To account for the diversity of vehicles and driving styles that are encountered in real-world traffic, each vehicle is assigned a set of characteristics that influence the way it responds to the presence of other vehicles and to traffic control devices. In the past, available computing power tended to limit the size of networks that could be modeled with microscopic simulation models. Recent advances in processor speed have reduced this problem but the desire to model larger areas and more complex travel behavior still exists. Today, the primary limitation of microscopic simulation models is the substantial amount of roadway geometry, traffic control, and traffic pattern data they require. Many transportation agencies currently use microscopic models in conjunction with travel demand models to better understand the impact of roadway geometry modifications on level of service and carrying capacity. A limitation of microscopic simulation models includes the ability to model large geographic areas. The reason is not a function of computing power but the ability to calibrate a larger network which requires substantial data, resources and technical expertise.
Questions/Interactivity: None
Possible Problems: None
Examples of microscopic traffic simulation models:
AIMSUN2 (Advanced Interactive Microscopic Simulator for Urban and Non-Urban Networks): http://www.tss-bcn.com/aimsun.html, ANATOLL: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a4, CORSIM/TSIS (Traffic Software Integrated System): http://ops.fhwa.dot.gov/trafficanalysistools/corsim.htm, DRACULA (Dynamic Route Assignment Combining User Learning and Microsimulation): http://www.its.leeds.ac.uk/software/dracula, FLEXSYT-II: http://www.flexsyt.nl/informatieuk.htm, INTEGRATION: http://www.intgrat.com, MicroSim: http://www.its.leeds.ac.uk/projects/smartest/append3d.html, MICSTRAN (Microscopic Simulator Model for Traffic Networks): http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a16, MITSIM (Microscopic Traffic Simulator): http://mit.edu/its/mitsimlab.html, MIXIC: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a18, NEMIS: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a19, SIGSIM: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a26, SIMDAC: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a27, SIMNET: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a28, SimTraffic: http://www.trafficware.com, SISTM (Simulation of Strategies for Traffic on Motorways): http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a29
SITRA B+: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a30, SITRAS: http://www.its.leeds.ac.uk/projects/smartest/append3d.html#a31, SmartPATH: http://www.path.berkeley.edu/PATH/Research, TEXAS (Texas Model for Intersection Traffic): http://mctrans.ce.ufl.edu/store/description.asp?itemID=449, TRANSIMS: http://tmip.tamu.edu/transims/, TRARR: http://www.engr.umd.edu/~lovell/lovmay94.html, TWOPAS: http://www.tfhrc.gov/safety/ihsdm/tamweb.htm, WATSim© (Wide Area Traffic Simulation): http://www.kldassociates.com/unites.htm

## Slide 36: CORSIM
CORridor micro SIMulation model developed by FHWA
Part of the TSIS Suite
NETSIM + FRESIM
FRESIM component has WZ applications, programmed as “incidents”
Image: FHWA
Notes: Key Message: Introduce CORSIM
Time: 1 min
Builds: None
Suggested Comments: CORSIM is a comprehensive microscopic traffic simulation, applicable to surface streets, freeways, and integrated networks with a complete selection of control devices (i.e., stop/yield sign, traffic signals, and ramp metering). It simulates traffic and traffic control systems using commonly accepted vehicle and driver behavior models. CORSIM combines two of the most widely used traffic simulation models, NETSIM for surface streets, and FRESIM for freeways. CORSIM has been applied by thousands of practitioners and researchers worldwide over the past 30 years and embodies a wealth of experience and maturity. The Traffic Software Integrated System (TSIS) is a collection of software tools for use by traffic engineers and researchers. Originally built as a simple shell around CORSIM, TSIS has evolved into a sophisticated toolkit. Though used by the FHWA for conducting research, these tools are sold to the public.
Additional Info: TSIS = Traffic Software Integrated System
Questions/Interactivity: None
Possible Problems: CORSIM is not for work zone analysis specifically but it can be used for certain applications.

## Slide 37: CORSIM Screen
Closed lane
“Rubbernecking”
Image: FHWA
Notes: Key Message: Introduce CORSIM
Time: 1 min
Builds: None
Suggested Comments: This shows a screen capture of CORSIM, specifically its freeway model FRESIM. The area in red simulates a lane that has been closed, perhaps because a work zone. The area in yellow indicates rubbernecking, or a reduction of capacity on that lane. CORSIM would not show tapers, but it can simulate lane closures and report measures of effectiveness.
Additional Info: TSIS = Traffic Software Integrated System
Questions/Interactivity: None
Possible Problems: CORSIM is not for work zone analysis specifically but it can be used for certain applications.

## Slide 38: CORSIM Guidelines
Guidelines for Applying CORSIM available
NHI Course available
Image: FHWA
Notes: Key Message: Introduce CORSIM
Time: 1 min
Builds: None
Suggested Comments: FHWA has published a report with guidelines for applying CORSIM. An NHI course is also available.
Additional Info: Available from http://ops.fhwa.dot.gov/trafficanalysistools/tat_vol4/index.htm
Questions/Interactivity: None
Possible Problems: CORSIM is not for work zone analysis specifically but it can be used for certain applications. NHI = National Highway Institute

## Slide 39: TSIS Availability
Available from McTrans
Image: FHWA
Notes: Key Message: Introduce CORSIM
Time: 1 min
Builds: None
Suggested Comments: TSIS (pronounced “T”-sis”) can be ordered from http://mctrans.ce.ufl.edu/featured/TSIS/. McTrans is a full service software support center serving the transportation engineering and planning community. McTrans has a professional staff of faculty, programmers, technical support and administrative personnel to offer users a variety of services. Located at the University of Florida.
Additional Info: http://mctrans.ce.ufl.edu/
Questions/Interactivity: None
Possible Problems: CORSIM is not for work zone analysis specifically but it can be used for certain applications.

## Slide 40: 5c. Mesoscopic Models
Combine the properties of both macroscopic and microscopic models (“mixed”)
Not as data intensive
The prefix “meso” comes from the Greek word mesos, meaning middle
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 1 min
Builds: None
Additional Info: Mesoscopic simulation models – Mesoscopic models combine properties of both microscopic (discussed below) and macroscopic simulation models. As in microscopic models, the mesoscopic models' unit of traffic flow is the individual vehicle. Similar to microscopic simulation models, mesoscopic tools assign vehicle types and driver behavior, as well as their relationships with the roadway characteristics. Their movement, however, follows the approach of macroscopic models and is governed by the average speed on the travel link. Mesoscopic model travel prediction takes place at an aggregate level, and does not consider dynamic speed/volume relationships. As such, mesoscopic models provide less accuracy than microsimulation tools, but are superior to typical planning analysis techniques. Examples of mesoscopic models include Continuous Traffic Assignment Model (CONTRAM), and Dynamic Network Assignment Simulation Model for Advanced Road Telematics for Planning (DYNASMART-P).
Questions/Interactivity: None
Possible Problems: None
Examples of mesoscopic simulation tools:
CONTRAM (Continuous Traffic Assignment Model): http://www.contram.com
DYNAMIT-P, DYNAMIT-X, DYNASMART-P, DYNASMART-X: http://www.dynamictrafficassignment.org
MesoTS: http://plan2op.fhwa.dot.gov/pdfs/Pdf2/mesoscopic.pdf

## Slide 41: Mesoscopic Models
Macro level with the ability to “zoom” areas to a micro level
Represent the flow of vehicles on a link, but not individually
Notes: Key Message: Continuing the discussion of simulation methods.
Time: 1 min
Builds: None
Additional Info: Mesoscopic simulation models are the newest generation of traffic simulation modeling tools. These tools evolved from a need for an intermediate level of analysis. They provide more detail than both the travel demand models and macroscopic simulation models discussed previously, but not as much fidelity as the microscopic simulation tools discussed in the next section. Mesoscopic models tend to represent the relative flow of vehicles on a network link, but do not represent individual lanes on the link. The strength of mesoscopic simulation models when analyzing work zones includes the ability to model both large geographic areas and corridors. In addition, diversion routes and signalized intersections can be modeled. In the case of a corridor with an interstate and signalized arterial road running through it, the diversion route onto the arterial could be more readily modeled using a mesoscopic simulation model. This type of analysis would not be easy to conduct using travel demand models or macroscopic simulation models, and can only be represented in a more limited fashion in some sketch-planning tools. Commonly used mesoscopic simulation tools for work zone analysis include the family of DYNASMART and DYNAMIT models as well as newly introduced hybrid/multi-scale models including Cube’s Avenue and Caliper’s TransModeler.
Questions/Interactivity: None
Possible Problems: None

## Slide 42: Work Zone – Specific Analysis Tools
QuickZone
QUEWZ-98
Construction Analysis for Pavement Rehabilitation Strategies (CA4PRS)
Dynasmart-P
Image: ATSSA
Notes: Key Message: Introduce WZ-specific tools
Time: 1 min
Builds: None
Suggested Comments: There are work zone-specific analysis tools. They are listed on the screen. Let’s look at them.
Additional Info: None
Questions/Interactivity: None
Possible Problems: Some tools, such as DYNASMART-P, were not designed specifically for work zones but they can be used to analyze work zone situations.

## Slide 43: 1. QuickZone
Delay-estimation model developed by FHWA
Analyzes work zone impacts of alternate work zone design and mitigation strategies.
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: QuickZone is a work zone delay estimation model developed by the Federal Highway Administration (FHWA) Research, Development, and Technology (RD&T) program. QuickZone was developed to help State and local transportation agencies better understand and consider the impacts of work zones as they plan, design, and implement their highway projects. QuickZone can help enable the consideration of the work zone impacts of alternate work zone design and mitigation strategies. QuickZone provides this capability to project planners and engineers, whereby they can obtain an estimate of delay, queuing, and user costs associated with alternate work zone design and mitigation strategies. QuickZone provides analysis options to estimate work zone delays and user costs for different demand patterns and for temporal (seasonal, weekly, daily) and spatial variations of work zone configurations. It can quantify corridor delay resulting from capacity decreases in work zones; identify the impact on delay of alternative construction phasing plans; and support tradeoff analyses between construction costs and delay costs. Work zone impacts and costs are estimated for an average day of work, which can then be amortized to get an estimate of average annual costs based on a user-specified life-cycle for the improvement. It can assess the impact of delay-mitigation strategies, such as alternate routing, signal re-timing, lane widening, and ramp metering. In addition to estimating work zone delays and user costs, QuickZone also provides a sketch-planning analysis of travel behavioral changes in response to work zones. QuickZone also supports the calculation of work-completion incentives. The software will therefore help highway agencies better phase and stage their construction and maintenance activities. For example, QuickZone enables road owners and contractors to compare the effects of doing highway work at night instead of during the day, or that of diverting traffic to one road versus another road at various stages of construction.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: None
Possible Problems: None

## Slide 44: QuickZone’s Primary Functions
Quantification of corridor delay resulting from capacity decreases in work zones
Identification of delay impacts of alternative project phasing plans
Supporting tradeoff analyses between construction costs and delay costs
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: The primary functions of QuickZone are:
Quantification of corridor delay resulting from capacity decreases in work zones.
Identification of delay impacts of alternative project phasing plans.
Supporting tradeoff analyses between construction costs and delay costs.
Examination of impacts of construction staging, by: - location along mainline - time-of-day (peak vs. off-peak) - season (summer vs. winter)
Assessment of travel demand measures and other delay mitigation strategies.
Allowing the establishment of work completion incentives.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: None
Possible Problems: None

## Slide 45: QuickZone’s Primary Functions (cont.)
Examination of impacts of construction staging, by:
Location along mainline
Time-of-day (peak vs. off-peak)
Season (summer vs. winter)
Assessment of travel demand measures and other delay mitigation strategies
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: The primary functions of QuickZone are:
Quantification of corridor delay resulting from capacity decreases in work zones.
Identification of delay impacts of alternative project phasing plans.
Supporting tradeoff analyses between construction costs and delay costs.
Examination of impacts of construction staging, by: - location along mainline - time-of-day (peak vs. off-peak) - season (summer vs. winter)
Assessment of travel demand measures and other delay mitigation strategies.
Allowing the establishment of work completion incentives.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: None
Possible Problems: None

## Slide 46: QuickZone’s Primary Functions (cont.)
Provides information to support the establishment of appropriate work completion incentives
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: The primary functions of QuickZone are:
Quantification of corridor delay resulting from capacity decreases in work zones.
Identification of delay impacts of alternative project phasing plans.
Supporting tradeoff analyses between construction costs and delay costs.
Examination of impacts of construction staging, by: - location along mainline - time-of-day (peak vs. off-peak) - season (summer vs. winter)
Assessment of travel demand measures and other delay mitigation strategies.
Allowing the establishment of work completion incentives.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: None
Possible Problems: None

## Slide 47: QuickZone
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: A prototype Project Delay Summary from QuickZone, featuring: (1) A graph depicting the projected average delay (in vehicle-hours) by time of day. Each line represents the profile for a particular phase of the project. This graph will be helpful in identifying which phases are likely to be the primary generators of delay during the life of the construction project. (2) In the upper right-hand corner, a table showing total average daily delay (vehicle-hours) for each phase. (3) In the lower right-hand corner, a table showing the maximum length (in vehicles) of the mainline queue for each graph. This figure can be used to compute maximum user delay or to determine if the mainline queue grows beyond some key position.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: None
Possible Problems: None

## Slide 48: QuickZone Data Needs
To use QuickZone, a user would input data such as:
Work zone location
Projected detour routes, if any
Anticipated volumes of traffic
Construction dates and times
Image: FHWA
Notes: Key Message: Introduce QuickZone
Time: 2 min
Builds: None
Suggested Comments: To use QuickZone, a user would input data such as:
Work zone location.
Projected detour routes, if any.
Anticipated volumes of traffic.
Construction dates and times.
The program is designed so that the setup of a typical work-zone network should take less than an hour. Once the data is entered, results should be available in graphic form in about three minutes. The graphic will display the amount of delay in vehicle-hours as well as the maximum length of the queue that can be expected.
Additional Info: For additional information, contact Debbie Curtis in Operations/ITS at: deborah.curtis@fhwa.dot.gov.
Questions/Interactivity: Haw many of you have used QuickZone? How was your experience?
Possible Problems: None

## Slide 49: 2. QUEWZ-98
Queue and User Cost Evaluation of Work Zones
For planning and scheduling freeway work zone lane closures
Analyzes traffic conditions on a freeway segment with and without a lane closure in place
Image: TXDOT
Notes: Key Message: Introduce QUEWZ-98
Time: 2 min
Builds: None
Suggested Comments: Texas Transportation Institute (TTI), in cooperation with the Texas Department of Transportation (TxDOT), has developed a microcomputer analysis tool, QUEWZ-98, that estimates traffic impacts, emissions and additional road user costs resulting from short-term lane closures in work zones. The program and manual provide critical information to personnel responsible for planning and scheduling freeway work zone activities. QUEWZ-98 is a microcomputer analysis tool for planning and scheduling freeway work zone lane closures. It analyzes traffic conditions on a freeway segment with and without a lane closure in place and provides estimates of the additional road user costs and of the queuing resulting from a work zone lane closure. The road user costs calculated include travel time, vehicle operating costs, and excess emissions. A user's manual for QUEWZ-98 is available. After describing the capabilities and input data requirements of QUEWZ-98, it provides instructions on using Q98MENU, a menu-driven user interface, to run QUEWZ-98. It also includes three examples to illustrate the various input and output options that are available.
Additional Info: QUEWZ-98 can be obtained from McTrans at http://mctrans.ce.ufl.edu/
Questions/Interactivity: None
Possible Problems: None

## Slide 50: QUEWZ-98
Developed by TTI and TXDOT
Simulates traffic flows through freeway segments (both with and without a work zone lane closure)
Estimate changes in traffic flow characteristics and added costs
Provides estimates of queues and costs
Notes: Key Message: Introduce QUEWZ-98
Time: 2 min
Builds: None
Suggested Comments: QUEWZ-98 is the latest version of QUEWZ (Queue and User Cost Evaluation of Work Zones), a mainframe program developed for TxDOT to simulate traffic flows through freeway segments (both with and without a work zone lane closure) and estimate changes in traffic flow characteristics and added costs due to closures. The model can be applied to freeway facilities or multilane divided highways with as many as six lanes in each direction and can analyze 24 consecutive hours of operation. Output comes in two different forms: (1) road user cost output and (2) lane closure schedule output. The road user cost output is the estimate of traffic conditions (volumes, capacities, speeds, queue length, etc.) and the additional road user costs for each hour that traffic conditions are affected by the lane closure. Estimates of excess emissions due to the closure are also available as part of the road user cost output. The lane closure schedule output summarizes the hours of the day during which a given number of lanes can be closed without causing excessive congestion. With these projections, transportation personnel can create more efficient, cost-effective plans for lane closures on roadway work zones.
Additional Info: QUEWZ-98 can be obtained from McTrans at http://mctrans.ce.ufl.edu/ . TTI = Texas Transportation Institute
Questions/Interactivity: None
Possible Problems: None

## Slide 51: 3. Construction Analysis for Pavement Rehab Strategies
CA4PRS:
  Estimates the distance a highway can be rehabilitated for various closure timeframes
  Integrates pavement, construction, and traffic related decision-making
  Can optimize rehab strategies
Image: Caltrans
Notes: Key Message: Introduce CA4PRS
Time: 2 min
Builds: None
Suggested Comments: Construction Analysis for Pavement Rehabilitation Strategies (CA4PRS) is a computer model intended to estimate the maximum amount (distance) of highway that can be rehabilitated or reconstructed within various closure timeframes. This model integrates pavement, construction, and traffic related decision-making by balancing numerous constraints such as scheduling interfaces, pavement materials and design, contractor logistics and resources, and traffic operations. When combined with a traffic model, the CA4PRS software can help determine which pavement structures and rehabilitation strategies maximize on-schedule construction production without creating unacceptable traffic delays. CA4PRS yields additional benefits when its results are integrated with various traffic simulation modeling tools in quantifying the impact of work zone lane closures to the whole highway network, including local arterials and neighboring freeways.
Additional Info: More information on CA4PRS is available at http://www.dot.ca.gov/newtech/roadway/ca4prs/ca4prs.htm
Questions/Interactivity: None
Possible Problems: None

## Slide 52: CA4PRS
Developed/supported by Caltrans
Helps balance pavement design, construction constraints, traffic operations and budgets
Images: Caltrans
Notes: Key Message: Introduce CA4PRS
Time: 2 min
Builds: None
Suggested Comments: CA4PRS was developed by Caltrans under a pooled-fund consortium. Demonstrations have shown that CA4PRS is user-friendly, easy to learn, and valuable in any project phase. Its greatest value lies in its capability to provide information to the planner/designer to optimally balance pavement design, construction constraints, traffic operations, and agency budget for transportation agencies — especially during the planning and design of rehabilitation projects.
CA4PRS helps agencies, contractors, and consultants prepare strategies (including the PS&E package) for highway projects by:
  Estimating working days and CPM schedules,
  Developing construction staging plans,
  Supplementing traffic management plans, and
  Outlining incentives and cost (A) + schedule (B) contracts
Additional Info: More information on CA4PRS is available at http://www.dot.ca.gov/newtech/roadway/ca4prs/ca4prs.htm
Questions/Interactivity: None
Possible Problems: None

## Slide 53
Image: Caltrans
Notes: Key Message: Introduce CA4PRS
Time: 2 min
Builds: None
Suggested Comments: For State transportation departments that did not participate in the original pooled-fund consortium, the software is available for a licensing fee of $1,000 ($3,000 for industry users and $750 for academia). Two-day training workshops are also available. For more information on licensing the software or holding training workshops, contact E.B. Lee at the University of California at Berkeley's Institute of Transportation Studies, 510-665-3637 (email: eblee@berkeley.edu), or Michael Samadian at Caltrans, 916-324-2048 (email: michael_samadian@dot.ca.gov). Information on the software is also available online at www.dot.ca.gov/research/roadway/ca4prs/index.htm.
Additional Info: More information on CA4PRS is available at http://www.dot.ca.gov/newtech/roadway/ca4prs/ca4prs.htm
Questions/Interactivity: None
Possible Problems: FHWA pooled fund study (CA, MN, TX, WA)

## Slide 54: 4. Dynasmart-P
Mesoscopic simulation model with dynamic traffic assignment
Has been used for analyzing regional work zone impacts
Image: FHWA
Notes: Key Message: Introduce Dynasmart-P
Time: 2 min
Builds: None
Suggested Comments: Dynamic Network Assignment-Simulation Model for Advanced Roadway Telematics (DYNASMART-P) supports transportation network planning and traffic operations decisions, including evaluation of ITS deployment options, through the use of simulation-based dynamic traffic assignment. This tool combines (1) dynamic network assignment models, used primarily in conjunction with demand forecasting procedures for planning applications, and (2) traffic simulation models, used primarily for traffic operational studies. DYNASMART-P provides the capability to model the evolution of traffic flows in a traffic network, which result from the decisions of individual travelers seeking for the best paths en-route over a given planning horizon. It overcomes many of the known limitations of static tools used in current planning practice. These limitations pertain to the types of alternative measures that may be represented and evaluated, and the policy questions that planning agencies are increasingly asked to address. DYNASMART-P defines a new generation of transportation planning methodologies, which can interface readily with existing four step procedures, yet provides a meaningful jump in the range and type of measures that can be evaluated.
Additional Info: http://mctrans.ce.ufl.edu/featured/dynasmart/
Questions/Interactivity: None
Possible Problems: None

## Slide 55: Dynasmart-P
Supports:
  Network planning & traffic operations decisions
  Evaluation of ITS deployment options
Image: FHWA
Notes: Key Message: Introduce Dynasmart-P
Time: 2 min
Builds: None
Suggested Comments: Because it considers the time-varying nature of traffic flows, it is expected to produce more useful estimates of state variables such as speeds, queue lengths, delays, and congestion effects to better assess the functional and environmental impacts of a variety of traditional and emerging transportation planning measures, including the deployment of ITS and non-ITS technologies. DYNASMART-P requires input data commonly used by the traditional traffic assignment and simulation models, particularly with regard to network representation and spatial demand loading patterns. The input data vary with the network being analyzed and the level of detail required by the user. Complexity of the network could range from a linear freeway network to an integrated network with High-Occupancy Vehicle (HOV) lanes, High-Occupancy Toll (HOT) lanes, ramp metering, transit services, possibly incidents and signal controlled intersections on surface streets. Applications to date have included metropolitan and regional networks with up to 35,000 nodes and 100,000 links, with nearly one million vehicles simulated over horizons of several hours.
Additional Info: http://mctrans.ce.ufl.edu/featured/dynasmart/
Questions/Interactivity: None
Possible Problems: None

## Slide 56: Dynasmart-P Applications
Providing dynamic traffic assignment methods for traditional transportation planning analyses
Assessing the impacts of ITS technologies, such as dynamic message signs, ramp meters and in-vehicle guidance systems on the transportation network
Image: FHWA
Notes: Key Message: Introduce Dynasmart-P
Time: 2 min
Builds: None
Suggested Comments: Potential applications of DYNASMART-P include:
Providing dynamic traffic assignment methods for traditional transportation planning analyses.
Assessing the impacts of ITS technologies, such as dynamic message signs, ramp meters, and in-vehicle guidance systems, on the transportation network.
Additional Info: http://mctrans.ce.ufl.edu/featured/dynasmart/
Questions/Interactivity: None
Possible Problems: None

## Slide 57: Dynasmart-P Applications (cont.)
Assessing the impacts of different traffic operations and control strategies
Supporting decision-making for regional work zone management
Evaluating incident management and special event management strategies
Image: FHWA
Notes: Key Message: Introduce Dynasmart-P
Time: 2 min
Builds: None
Suggested Comments: Potential applications of DYNASMART-P include:
Assessing the impacts of different traffic operations and control strategies.
Supporting decision-making for regional work zone management.
Evaluating incident management and special event management strategies.
Additional Info: http://mctrans.ce.ufl.edu/featured/dynasmart/
Questions/Interactivity: None
Possible Problems: None

## Slide 58: Dynasmart-P Applications (cont.)
Evaluating congestion- pricing schemes
Providing information to support integrated transportation corridor investment decisions
Helping to improve estimates of mobile source emissions
Image: FHWA
Notes: Key Message: Introduce Dynasmart-P
Time: 2 min
Builds: None
Suggested Comments: Potential applications of DYNASMART-P include:
Evaluating congestion-pricing schemes.
Providing information to support integrated transportation corridor investment decisions.
Helping to improve estimates of mobile source emissions
Additional Info: http://mctrans.ce.ufl.edu/featured/dynasmart. More information is available at the DYNASMART-P Web site at http://www.dynasmart.com.
For More Information Contact: John Halkias, FHWA Office of Operations, john.halkias@fhwa.dot.gov, 202-366-2183
Questions/Interactivity: None
Possible Problems: None

## Slide 59: Three Methodologies
Screening
Mono-Scale
Multi-Scale
Each with strengths and weaknesses!
Notes: Key Message: Introduce modeling methodologies
Time: 1 min
Builds: Text box appears on click
Suggested Comments: There are three methodologies, each with strengths and weaknesses, that can be applied to modeling. They are listed on the screen. Let’s discuss them.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 60: 1. Screening
The use of simpler tools with limited data to screen WZ projects for more in-depth analysis
Tells you:
  Where to spend your money
  Which projects are critical
ADVANTAGE: Fewer resources needed
DISADVANTAGE: Results not definite
Notes: Key Message: Introduce screening
Time: 1 min
Builds: None
Suggested Comments: This methodology is characterized by the use of simpler tools using archived data to screen work zone projects to determine which may warrant more in-depth analysis. This concept has been used to allocate resources for work zone analysis when looking across a number of projects to identify potential mobility impacts. For single projects this includes the use of simpler transportation modeling approaches such as sketch-planning and HCM in early project phases and the use of a more complex transportation modeling approaches (if warranted) later in the project.
Additional Information: The advantages of this methodology include the focusing of agency resources (institutional, financial, and technical) on projects or issues that have the most potential mobility impact. It can be difficult early in project development or when looking across many projects to accurately identify where significant congestion is likely to be induced by work zone activity. The disadvantage of this methodology is that the high-level screening transportation analysis tools used in earlier stages may not produce consistent predictions of impacts with more detailed tools used in later stages.
Questions/Interactivity: None
Possible Problems: None

## Slide 61: 2. Mono-Scale
A single analytical tool applied consistently throughout the project
Attractive if a calibrated, well-maintained, reliable model available
ADVANTAGE: Model consistency guaranteed
DISADVANTAGE: A single tool may not be well-suited for everything
Notes: Key Message: Introduce the mono-scale approach
Time: 2 min
Builds: None
Suggested Comments: The mono-scale methodology features a single transportation analysis tool applied consistently throughout the project life-cycle. The advantage of this methodology is that model consistency is essentially guaranteed throughout the project life-cycle. Resources invested in developing the tool and its supporting data are passed along as the project proceeds. The disadvantage of this methodology is that a single tool may be well-suited to support some types of decisions but not well-suited to others. A mono-scale methodology may be an attractive option if a calibrated, well-maintained model of the work zone impact area is already in hand. If there is not a good match between the transportation modeling approach and model type in-hand, and there are some resources in hand to extend or enhance the analysis, a multi-scale methodology can be considered.
Additional Information: For example, a mono-scale methodology using microscopic simulation of the immediate work zone area may capture detailed elements of traffic control (work zone geometry and traffic signal operations) but have only limited capability to predict impacts from diversion on parallel routes.
Questions/Interactivity: None
Possible Problems: None

## Slide 62: 3. Multi-Scale
Several tools used throughout the project
Use only on large projects with a large WZ impact area
ADVANTAGE: Checks and balances
DISADVANTAGE: Staff, data, time resources are significant
Notes: Key Message: Introduce the multi-scale approach
Time: 1 min
Builds: None
Suggested Comments: This methodology deploys several tools in combination from project planning through construction, and any inconsistencies between models are identified and resolved throughout the process. This type of methodology is effective for looking at a complete range of issues using the most appropriate tool with the added value of cross-validation among tools and data types. The disadvantage of this methodology is that the agency resources (the technical staff, funding, and scheduling) are significant as well as the required data (specifically its quality and availability). This type of methodology is likely to be deployed only on the largest projects with a large work zone impact area, longer duration, and significant resources devoted to mobility impacts mitigation.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 63: DISCUSSION
Which approach is better for you and why?
Which one would you use? Why?
Notes: Key Message: Discussion on modeling approaches
Time: 1 min
Builds: None
Suggested Comments: Which approach is better for you and why? Which one would you use? Why?
Additional Information: Generate discussion about the advantages and disadvantages of each.
Questions/Interactivity: None
Possible Problems: None
Image Credit: https://www.slideshare.net/rmulyaningsih/ict2-28587397

## Slide 64: Identifying a Methodology: Questions to Ask:
Does it make sense to move forward with work zone analysis for a given project?
What criteria should be used to select an actual modeling approach for a project?
Which challenges and imitations exist?
Notes: Key Message: Discussion on modeling identification
Time: 2-3 min
Builds: None
Suggested Comments: Once an analyst has a better understanding of the factors influencing an overall work zone analysis, the next step is to consider some critical questions: Does it make sense to move forward with work zone analysis for a given project? What criteria should be used to select an actual modeling approach for a project? Which limitations exist? The decision about what transportation modeling approach to select for a work zone analysis is secondary to the decision to deploy a transportation modeling approach at all. However, once the decision is made to use a transportation analysis tool, the question turns to which tool is best suited given my circumstances? The difficult part is balancing the available resources (time, money, data, etc.) with the desired level of detail (e.g., ability to model one-lane/two way operations using historic traffic counts for a Type I project).
Additional Information: When resources are limited, however, the analyst must consider whether a less detailed analysis using a simpler tool is adequate to the requirements of the analysis. If the mismatch between the necessary level of detail and resource availability is high enough, the corresponding technical risk may be so high that a drastic re-consideration of modeling approach may be appropriate.
Questions/Interactivity: None
Possible Problems: Try to generate discussion

## Slide 65: Challenges and Limitations
Lack of quality data
Limited empirical data
Limited funding
Availability of training
Limited resources
Image: FHWA
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: As long as they are used correctly, traffic analysis tools are useful and effective in helping transportation professionals best address their transportation needs. Each tool and tool category is designed to perform different traffic analysis functions, and there is no one analytical tool that can do everything or solve every problem. This section addresses some of the challenges and limitations of available traffic analysis tools that should be considered when selecting a tool:
Additional Information: There are many factors associated with selecting a specific methodology or tool which include functionality, results, time, training and cost. Choosing a tool is generally a tradeoff among these five criteria. Functionality (the capability to represent specific work zone attributes) and level of detail (capability to quantitatively differentiate between alternatives) are two critical criteria because if the tool cannot analyze a specific situation or provide the necessary results to the precision or accuracy required, it would not be useful regardless of the cost, training or development time applied. In some instances, such as a project currently in the construction phase, it may be critical that results are provided in a timely manner. The time required to assemble the required data and calibrate a simulation tool is generally much longer than the time and resources required to utilize a sketch-planning (delay estimation) tool. The need for timeliness must be balanced against the ability of the sketch-planning tool to provide a meaningful solution accurately reflecting the problem under study. Finally, the training and cost associated with a particular tool should be considered. Simulation tools often require a high level of expertise and training, skills which are possessed by relatively fewer individuals and can be costly to hire and retain. On the other hand, many of the sketch-planning and HCM tools are more accessible, can be mastered by a broad range of staff within a short time and are inexpensive to purchase.
Questions/Interactivity: None
Possible Problems: This is an intro slide. Avoid getting into detail here.
Image Credits: http://innovativemobility.org/wp-content/uploads/2015/02/Robert-Sheehan-Mobility-on-Demand.pdf

## Slide 66: Challenges and Limitations (cont.)
Lack of understanding of the limitations of the tool
Tools may not be specifically designed for work zones
Lack of features
Tendency to use simpler analytical tools
Image: FHWA
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: As long as they are used correctly, traffic analysis tools are useful and effective in helping transportation professionals best address their transportation needs. Each tool and tool category is designed to perform different traffic analysis functions, and there is no one analytical tool that can do everything or solve every problem. This section addresses some of the challenges and limitations of available traffic analysis tools that should be considered when selecting a tool:
Additional Information: None
Questions/Interactivity: None
Possible Problems: This is an intro slide. Avoid getting into detail here.

## Slide 67: Challenges and Limitations (cont.)
Biases against models and traffic analysis tools
Let’s discuss these challenges and how to overcome them!
Image: FHWA
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: Text box appears on click
Suggested Comments: As long as they are used correctly, traffic analysis tools are useful and effective in helping transportation professionals best address their transportation needs. Each tool and tool category is designed to perform different traffic analysis functions, and there is no one analytical tool that can do everything or solve every problem. This section addresses some of the challenges and limitations of available traffic analysis tools that should be considered when selecting a tool:
Additional Information: None
Questions/Interactivity: None
Possible Problems: This is an intro slide. Avoid getting into detail here.
Image Credits: http://blog.astutesolutions.com/Portals/2021/images/ChallengesAhead.jpg

## Slide 68: 1. Lack of Quality Data
If good data are not available:
  Get better data, or
  Use a simpler non data-intensive model
The user should balance the needs for a detailed analysis with the available data
Images: FHWA
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: Text box appears on click
Suggested Comments: If good data are not available, the user should consider a less data-intensive tool category, such as a sketch-planning tool rather than micro simulation. However, the results of the simpler tool categories are usually more generalized, so the user should carefully balance the needs of a more detailed analysis with the amount of data required. Each tool uses unique analytical methodologies, so the data requirements for analysis can vary greatly from tool to tool and by tool category. In many cases, data from previous projects contribute very little to a new analytical effort. Adequate resources must be budgeted for data collection.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 69: 2. Limited Empirical Data
Data collection is often the most expensive part of the assessment
Approach: Look at the project objective and limit the data collection to the data that are critical to the study
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: Text box appears on click
Suggested Comments: Data collection can often be the most costly component of a study. The best approach is to look at the ultimate goals and objectives of the task and focus data collection on the data that are crucial to the study.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 70: 3. Limited Funding
Tools can require a significant capital investment
More scenarios = more money
Focus on the project’s goals & objectives
Identify the point of diminishing returns
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: Text box appears on click
Suggested Comments: Limited funding for conducting the study, purchasing tools, running analytical scenarios, and training users is often a consideration in transportation studies. Traffic analysis tools can require a significant capital investment. Software licensing and training fees can make up a large portion of the budget. Also, the analysis of more scenarios costs money. When faced with funding limitations, focus on the project’s goals and objectives, and try to identify the point of diminishing returns for the investment.
Additional Information: None
Questions/Interactivity: None
Possible Problems: None

## Slide 71: Funding Needs
Data collection and evaluation
Purchasing tools
Running analytical scenarios
Calibration
Training/Consulting
Software licensing
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Funds will be required. These items need to be considered:
Data collection and evaluation
Purchasing tools
Running analytical scenarios
Calibration
Training
Software licensing
Additional Information: None
Questions/Interactivity: Any experiences in this room?
Possible Problems: None

## Slide 72: 4. Availability of Training
Tools may have steep learning curves
Some transportation professionals do not have adequate modeling and simulation training
Consider outsourcing
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Tools may have steep learning curves and some transportation professionals do not have adequate modeling and simulation training. Consider out-sourcing the work if in-house expertise is not available.
Additional Information: None
Questions/Interactivity: Any experiences in this room?
Possible Problems: None

## Slide 73: 5. Limited Resources
Limitations in staffing, capabilities, and funding for building the network and conducting the analysis should be considered
Model coding and calibration is a resource intensive process
Difficult to keep project on target
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Limitations in staffing, capabilities, and funding for building the network and conducting the analysis should be considered. The implementation of most traffic analysis tools is a resource-intensive process, especially in the model coding and calibration (front-end) phases for simulation analyses. Careful scheduling and pre-agreed upon acceptance criteria are necessary to keep the project focused and on target.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None
Image Credit: https://www.dreamstime.com/photos-images/private-office.html

## Slide 74: 6. Lack of Understanding of the Limitations of the Tool
Important to assess them up-front
Communication (with previous users) is key
Research the experiences of others
Do your best to really know the tool’s inner works (algorithms)
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Often, limitations and “bugs” are not discovered until the project is underway. It is important to learn from experiences with past projects or to communicate with fellow users of a particular tool or tool category in order to assess the tool’s capabilities and limitations. By researching the experiences of others, users can gain a better understanding of what they may encounter as the project progresses.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None

## Slide 75: 7. Tools May Not Be Specifically Designed For WZ
Do you have confidence in the tool?
Do you trust the output?
Does the tool give you the information you need to make decisions?
Match the project’s desired performance measures with the tool’s output
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: The output measures produced by each tool vary, so the process of matching the project’s desired performance measures with the tool’s output is important. In addition, there are very few tools that directly analyze WZ strategies and the impacts associated with them.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None

## Slide 76: 8. Lack of Features
“Tricking” the tool into mimicking a certain strategy is a short-term solution and may yield bad results
If the model doesn’t do what you need, don’t use it!
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Some analytical tools are not designed to evaluate the specific strategies that users would like to implement. Often, “tricking” the tool into mimicking a certain strategy is a short-term solution; however, there should be flexibility so that advanced users may customize the tools.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None

## Slide 77: 9. Tendency To Use Simpler Analytical Tools
Avoid using an inappropriate tool for the project because of:
  Ease of use
  Lack of resources
  Past experiences
  Lack of familiarity with other available tools
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: Because of lack of resources, past experience, or lack of familiarity with other available tools, many agencies prefer to use a tool currently in their possession, even if it is not the most appropriate tool for the project.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None
Image Credit: http://mantzm17.weebly.com/math.html

## Slide 78: 10. Biases Against Models And Traffic Analysis Tools
Some prefer traditional methods
Some say models are unreliable and “black boxes”
More complex projects require more advanced tools
Notes: Key Message: Discussion the challenges and limitations of modeling
Time: 1 min
Builds: None
Suggested Comments: These biases are not only because of the challenges listed above, but also because models are not always reliable and are often considered “black boxes.” Some transportation professionals prefer to use “back-of- the-envelope” calculations, charts, or nomographs to estimate the results. This may be adequate for simpler tasks; however, more complex projects require more advanced tools.
Possible Problems: None
Additional Information: None
Questions/Interactivity: None

## Slide 79: Key Points to Ponder
Work zone decision-making is an evolutionary process which supports a number of key questions to be answered
Data requirements are a driving force behind developing a transportation modeling approach
Notes: Key Message: Ponder key points
Time: 2 min
Builds: None
Suggested Comments: Volume IX highlighted four key points that are important to consider when an analyst is deciding upon which transportation modeling approach to ultimately develop and use. This slide shows the first 2:
1. Work zone decision-making is an evolutionary process which supports a number of key questions to be answered.— Work zone analysis evolves over time as the roadway construction project moves forward from Planning to PE/Design to Construction and key decisions need to be supported. As the overall project moves forward it is always evolving and the use of a transportation modeling approach is always predicated on certain key decisions that have to be made
2. Data requirements are a driving force behind developing a transportation modeling approach—Different factors need to be considered when selecting a transportation modeling approach. It is a complex issue to unravel. However, what each of these examples shows is that data requirements are an important factor to consider.
Possible Problems: None
Additional Information: None
Questions/Interactivity: Treat as a summary and keep brief.

## Slide 80: Key Points to Ponder (cont.)
Identifying a Strategic Methodology early in the project life-cycle can mitigate future work zone analysis problems
Developing a transportation modeling approach is unique to each work zone analysis
Notes: Key Message: Ponder key points (3-4)
Time: 2 min
Builds: None
Suggested Comments: The other 2 are:
3. Identifying a Strategic Methodology early in the project life-cycle can mitigate future work zone analysis problems—As discussed in Section 3.0, three strategic methodologies were presented representing various modeling opportunities for work zone analysis: mono-scale, screening, and multi-scale. These methodologies serve as a foundation on which transportation modeling approaches could be incorporated into the overall work zone decision-making framework.
4. Developing a transportation modeling approach is unique to each work zone analysis—While many people desire a prescriptive “cookbook” method to direct them in determining which transportation modeling approach to use, making that determination based solely upon one particular factor is problematic.
Possible Problems: None
Additional Information: None
Questions/Interactivity: Treat as a summary and keep brief.

## Slide 81: Module Recap
What’s the difference between deterministic and stochastic models?
What’s the difference between microscopic and macroscopic models?
Name the three modeling methodologies
Name three challenges and limitations in the use of traffic analysis tools
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.

## Slide 82: Workshop 1: Analysis of Traffic Count Data and Calculation of V/C Ratios
Refer to the scenario provided
Problem: Traffic counts are needed to perform a macroscopic analysis of the impacts of a work zone on this network.
Refer to diagram provided:

## Slide 83: Network

## Slide 84: Team Assignments
Calculate the total demand for links 2, 4, and 5
If the one-way capacity of link 5 is reduced to 1,000 vph during construction, will link 5 have any operational issues during construction?
Is further analysis needed?

## Slide 85: Assumptions
Link 2 demand is 10,000 vph.
60/40 D-factor (directional distribution)
10% K-factor (hourly distribution)
Capacity of 1,000 vph for each link

## Slide 86
Link | Iteration 1 | Iteration 2 | Iteration 3 | Iteration 4 | Iteration 5 | V/C Ratio
1 | 15,000 |  |  |  |  | 
2 | 10,000 |  |  |  |  | 
3 | 26,000 |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 | 28,000 |  |  |  |  | 
Result |  |  |  |  |  |