## Slide 1: -MODULE 4- Tool Selection Considerations
Work Zone Traffic Impact Analysis
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s discuss tool selection considerations
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 2: Module Objectives
Discuss factors that must be considered when deploying analytical tools
Discuss questions to ask when choosing an analytical tool
Present a methodology for selecting an analytical tool
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Deployment of Analytical Tools
Best accomplished when the analytical capability is well-matched to the context for analysis
The tool must match the needs
Tools should never be used to make key decisions,
but to understand the potential impacts
and inform key decisions!
Notes: Key Message: Deployment of Analytical Tools
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Let’s discuss the importance of selecting and applying the proper tool. This is best accomplished when the analytical capability is well-matched to the context for analysis. The tool must match the needs.
Suggested Questions: What is the criteria to select and deploy an analytical tool?
Additional Information: None
Possible Problems: None
Image Credt: https://www.palomar.edu/testwritingstrategies/2015/10/30/make-me-a-match/2-pattern-matching/

## Slide 4: Factors to Consider
  Data availability and quality
  Work zone impact area geography
  Agency resources
Notes: Key Message: Factors to Consider
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at the various factors to consider. These are listed on the screen.
Suggested Questions: None
Additional Information: None
Possible Problems: This is an intro slide. Avoid getting into details here.

## Slide 5: 1. Data Availability & Quality
Possibly the most important factor when considering the application of “tools”
Data include both:
  Roadway characteristics
  Traffic data
Notes: Key Message: Discuss Data Availability & Quality
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: This is possibly the most important factor when considering the application of “tools”. The availability of data and the quality of the data may determine the tool to choose. In all cases, it is important that the data available be of high quality such that the outputs of the model are useful in supporting the decisions being made.
Suggested Questions: Which data do these tools need?
Additional Information: An important component to using data is the quality of the data. The purpose of using data (be it primary or archived) is to prepare models that best represent actual field conditions resulting in an analysis producing the most accurate results possible. Primary data can often provide the most valuable data for modeling; however, collecting this data is resource intensive and costly. Many analyses for work zone planning purposes are conducted without this type of resource intensive primary data collection.
Possible Problems: Some may disagree with this point. Try to generate discussion.

## Slide 6: Roadway Characteristics
Physical attributes
  Lane configuration
  Intersections
  Alternate routes
  Lane widths
  Etc.
Anything necessary to
build the “network”
Image: ATSSA
Notes: Key Message: Discuss Roadway Characteristics
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: Text box appears on click.
Suggested Comments: These are possible data needs.
Suggested Questions: How do we find these data? If not available, it may need to be collected.
Additional Information: None
Possible Problems: None

## Slide 7: Traffic Data
Describes how the roadway network is utilized by the user:
  Traffic counts
  Hourly volumes
  Speeds
  Etc.
Image: FHWA
Notes: Key Message: Discuss Traffic Data
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are possible traffic data needs.
Suggested Questions: How do we find these data? If not available, it may need to be collected. Ask: Is this critical to the model? How much accuracy is needed? Can the data be estimated? Would that estimate impact the results?
Additional Information: Good references is ITE’s Manual of Transportation Engineering Studies (www.ite.org)
Possible Problems: None

## Slide 8: Obtaining Traffic Data
  Traffic counts
    Count stations
    Road tube counts
  Hourly volumes
    Peak hour volumes
  Speeds
    Posted speed
    85th percentile
Image: FHWA
Notes: Key Message: Discuss Traffic Data
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are possible traffic data needs.
Suggested Questions: How do we find these data? If not available, it may need to be collected. Ask: Is this critical to the model? How much accuracy is needed? Can the data be estimated? Would that estimate impact the results?
Additional Information: Good references is ITE’s Manual of Transportation Engineering Studies (www.ite.org)
Possible Problems: None

## Slide 9: The Key to Work Zone Impact Analysis
A balance between the desired precision of the results & the quality of the available data
Garbage in = garbage out
Notes: Key Message: Discuss The key to work zone impact analysis
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: At the end, we need a balance between the desired precision of the results & the quality of the available data. The results will be as good as the data we provide: Garbage in = garbage out
Suggested Questions: None
Additional Information: None
Possible Problems: None
Image Credit: https://pixabay.com/images/search/trash%20can/

## Slide 10: The Key to Work Zone Impact Analysis
If the available data are poor, a micro analysis may not be prudent
More precision = better data!
Notes: Key Message: Discuss The key to work zone impact analysis
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For example, if the available data is poor, a micro analysis, such as CORSIM, may not be prudent. This is key if a consultant is hired. We cannot expect a lot of accuracy and level of confidence in the results is the data was poor.
Suggested Questions: Who can tell me an example of a microscopic tool? CORSIM!
Additional Information: None
Possible Problems: None
Image Credit: Wikipedia.com/calipers

## Slide 11: 2. Work Zone Impact Area Geography
The type of work
The network typology
The geographic scale of the work zone
Image: Caltrans
Notes: Key Message: Discuss Work Zone Impact Area Geography
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The second issue we need to discuss is the work area impact area geography. Let’s look at three factors:
a. The type of work
b. The network typology
c. The geographic scale of the work zone
Suggested Questions: How would the area geography impact tool selection?
Additional Information: None
Possible Problems: None

## Slide 12: a. Work Zones Types
One example is given in FHWA’s Work Zone Assessment Guide
Classified based on expected work zone impacts
Image: FHWA
Notes: Key Message: Discuss Work Zone Impact Area Geography
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The first important factor is the type of work zone. One example is given in FHWA’s Work Zone Assessment Guide. WZ types are classified based on expected work zone impacts
Suggested Questions: None
Additional Information: http://ops.fhwa.dot.gov/wz/resources/final_rule/wzi_guide/wzi_guide.pdf
Possible Problems: None

## Slide 13: Project Classification
The example categorizes work zones into four types based on their expected impact levels
  Type I
  Type II
  Type III
  Type IV
Image: FHWA
Notes: Key Message: Discuss Project Classification
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The example categorizes work zones into four types based on their expected impact levels: Types I, II, III, and IV. A project classification system separates road projects into different types based on the severity of expected work zone impacts. Such classification enables agencies to apply policies and practices that are best suited to each type of project. It also helps address specific aspects of work zone related decision-making for different project types. For example, a project classification system may be used to identify the needed level of work zone impacts assessment for a project (i.e., high-level qualitative assessment or detailed quantitative analysis); preferred construction approaches; work zone design options and TMP strategies; and work zone monitoring and performance assessment requirements. Classification systems will vary based on an agency’s needs. They can range from a simple scheme (e.g., high, medium, and low work zone impact projects) to a multidimensional matrix of projects that recommends appropriate work zone management strategies for different project types. In general, a simple classification system that is practical and easy to adopt and apply is recommended.
Suggested Questions: None
Additional Information: None
Possible Problems: Emphasize that this is an EXAMPLE.

## Slide 14: Type I
Metro/Regional/Intra-state level impact
Very high level of public interest
Significant user cost impacts
Very long duration
Example: Central Artery, Boston
Image: FHWA
Notes: Key Message: Discuss Type I Projects
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Refer to page 3-9 of Work Zone Impacts Assessment Guide
Suggested Questions: Page 3-9
Additional Information: None
Possible Problems: None

## Slide 15: Type II
Predominantly metro/regional impact
Moderate to high public interest
Affects a moderate to high number of travelers
Moderate to high user cost impacts
Moderate to long duration
Example: Major bridge repair
Notes: Key Message: Discuss Type II Projects
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Refer to page 3-9 of Work Zone Impacts Assessment Guide
Suggested Questions: Page 3-9
Additional Information: None
Possible Problems: None

## Slide 16: Type III
Metro/regional level impact
Low to moderate level of interest
Affects a low/moderate level of travelers
Low to moderate user cost impacts
May include lane closures for moderate duration
Example: Minor interchange repair
Notes: Key Message: Discuss Type III Projects
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Refer to page 3-9 of Work Zone Impacts Assessment Guide
Suggested Questions: Page 3-9
Additional Information: None
Possible Problems: None

## Slide 17: Type IV
Affects the traveling public to a small degree
Low public interest
Duration is short to moderate
Work zones are usually mobile and typically recurring
Example: Guardrail repair
Image: FHWA
Notes: Key Message: Discuss Type IV Projects
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory. Refer to page 3-9 of Work Zone Impacts Assessment Guide
Suggested Questions: Page 3-9
Additional Information: None
Possible Problems: None

## Slide 18: b. Network Typology
The form of the network
Will impact the type of modeling approach to use
Three categories
  Isolated
  Pipe
  Network
Images: FHWA
Notes: Key Message: Discuss Network Typology
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: For work zone analysis, network typology is composed of three general categories:
-Isolated
-Pipe
-Network
Suggested Questions: What is typology? A systematic classification or study of types.
Additional Information: None
Possible Problems: Treat as an intro slide.

## Slide 19: Isolated Typology
A single work zone with limited interaction with surrounding infrastructure and facilities
Example: A rural lane closure or an interstate bridge deck replacement
Images: FHWA
Notes: Key Message: Discuss Network Typology
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
-Isolated. A single work zone with limited interaction with surrounding infrastructure and facilities. Examples include a rural lane closure or an interstate bridge deck replacement.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 20: Pipe Typology
A roadway segment with multiple work zones interacting with each other
Work zones typically do not include any type of viable alternate or detour route
Image: FHWA
Notes: Key Message: Discuss Network Typology
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: -Pipe. A roadway segment with multiple work zones interacting with each other. These work zones typically do not include any type of viable alternate or detour route.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 21: Network Typology
A connected, inter-dependent network structure with multiple access points and one or more viable alternate routes
Images: FHWA
Notes: Key Message: Discuss Network Typology
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Network. A connected, inter-dependent network structure with multiple access points and one or more viable alternate routes.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 22: c. The Geographic Scale Of The Work Zone
Physical size of the work zone
Dimensions of the analysis area
The larger the WZ, the more difficult the use of microscopic simulation becomes
Notes: Key Message: Discuss The Geographic Scale Of The Work Zone
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Scale refers to the physical size of the work zone, the dimensions of the analysis area. The larger the WZ, the more difficult the use of microscopic simulation becomes. Why? More data!
Suggested Questions: Why? More data!
Additional Information: None
Possible Problems: None

## Slide 23: Rule of Thumb
As the need to examine the impact to more users (motorists, pedestrians, bicyclists, motorcyclists) increases, the ability to use certain types of modeling approaches decreases
Notes: Key Message: Discuss a Rule of Thumb
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: As the need to examine the impact to more motorists, users and travelers increase, the ability to use certain types of modeling approaches decreases. Why? More data!
Suggested Questions: Why? More data! More assumptions!
Additional Information: Treat as a summary slide. Try to generate discussion.
Possible Problems: This is not ALWAYS true. It is a rule of thumb!

## Slide 24: 3. Agency Resources
In-house technical staff
Availability of consultants
Funding resources
The model itself!
Will impact
model selection
Notes: Key Message: Discuss Agency Resources
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Developing an analytical approach will be strongly dependent upon the resources the transportation agency has available to these analyses. No question, use of certain models can get expensive. Funding availability may limit the extent to which a work zone analysis can be conducted because money is not available for acquiring the necessary modeling tool or issuing a contract for the analysis to be conducted by a consultant. Regardless, any type of work zone analysis will require at least a minimum amount of funding and the accuracy and results of the analysis will depend to a certain degree on the amount of money available. These costs must be considered in model selection. Issues such as the ones on the screen must be considered.
Suggested Questions: None
Additional Information: These resources can be categorized as institutional arrangements within the organization that enable or hinder the flow of information; technical staff that are able to conduct the required analysis and/or data collection; funding to acquire the technical expertise or models; and scheduling requirements. All four of these agency resource categories play an important role when making a determination to deploy a transportation modeling approach.
Possible Problems: None

## Slide 25: In-House vs. Outsourcing
Consider
  In-house expertise & time commitments
  Long-term implications
  Cost
Notes: Key Message: Discuss In-House vs. Outsourcing
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: A critical component to the successful use and deployment of work zone modeling tools is the technical expertise to use them. Often, transportation agencies will have either in-house expertise regarding the use of a specific model or access to a consultant with the expertise through a contractual arrangement. In this situation, an agency may be limited to a specific model based upon the technical capability at hand. For example, many transportation agencies make a decision to use modeling products from a specific vendor. In this case, if an agency/analyst wanted to use a different modeling tool that is not available from the vendor, additional time and resources would need to be made available in order to acquire and run the model. Even if an outside contractor is used to conduct the analysis, the transportation agency will still need to have enough expertise on-hand in order to oversee and validate the work zone analysis findings.
Application of the tools (with a degree of confidence) will take time. Do we want the analysis done in-house (by staff) or outsource to consultants? Consider the long term implications. For example, the exclusive use of consultants may not generate in-house expertise.
Suggested Questions: What are the advantages and disadvantages?
Additional Information: None
Possible Problems: None

## Slide 26: Methodology for Selecting a Traffic Analysis Tool
FHWA has developed detailed guidance/tools for selecting a traffic analysis tool
Traffic Analysis Toolbox Volume II
Image: FHWA
Notes: Key Message: Present a Methodology for Selecting a Traffic Analysis Tool
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The selection of any traffic analysis tool should align the purpose and objective of the analysis with the capabilities and limitation of the tool. From a project administrative perspective, there are several technical, time requirements and budget factors which come into play, as does the availability of the associated data. FHWA has developed detailed guidance/tools for selecting a traffic analysis tool
Suggested Questions: None
Additional Information: An automated tool has been developed to implement these steps. This tool can be found on the FHWA Traffic Analysis Tools Web site at: http://ops.fhwa.dot.gov/Travel/Traffic_Analysis_Tools/traffic_analysis_tools.htm
Possible Problems: The guide DOES NOT recommend specific tools.

## Slide 27: Model Selection Considerations
An important step in the process
Ask yourself the following questions:
Notes: Key Message: Discuss Model Selection Considerations
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Resource requirements, whether they are financial, personnel, or skill-related, can be a major consideration in selecting an analytical tool. In addition, using a more advanced and data-intensive tool may provide a greater understanding of the alternatives; however, accurate and detailed data are still needed to produce representative results. We need to ask the following questions:
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 28: Questions to Ask:
What is the average capital cost to acquire the traffic analysis tool?
Is the tool methodology type easy to learn?
Does it require expensive and/or lengthy training sessions?
Is the tool generally user-friendly
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Tool Capital Cost: What is the average capital cost to acquire the traffic analysis tool? In this category, tools that cost, on average, less than $1,000 are considered to be inexpensive, while tools that cost from $1,000 to $5,000 are considered to be mid-range. Any tools that cost more than $5,000 are considered to be expensive.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 29: Questions to Ask (cont.)
Is the tool popular and well regarded by current users?
How much computer power is necessary to adequately run the analysis?
Has the model been validated?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: What is validation? Have the equations and algorithms build into the model been confirmed as valid? Is the model tested? Validation is done by the developer, as opposed to calibration, which is done by the user. Definition: to make valid; substantiate; confirm.
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 30: Questions to Ask (cont.)
What is the typical amount of input data required to perform the analysis?
How long does the tool take to perform the analysis?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Hardware Requirements: How much computer power is necessary to adequately run the analysis?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 31: Questions to Ask (cont.)
Does the tool generally produce output in formats that require no further post-processing or reformatting?
Does the tool have a detailed and well-written user’s manual?
Are there articles and reports on past projects evaluated using this type of tool?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any experiences with these issues in this group?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 32: Questions to Ask (cont.)
Is technical support generally available for this tool?
Are there mailing lists, chat rooms or newsgroups dedicated to this tool where users can communicate with each other?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any experiences with these issues in this group?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 33: Questions to Ask (cont.)
Does the tool allow for customization of the key analytical parameters?
Is the tool flexible enough to allow for customization?
How much calibration will be needed?
Does the tool generally provide default values for its parameters, rates or impact values?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any experiences with these issues in this group?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 34: Questions to Ask (cont.)
Does the tool generally have export/import features to/from other software (e.g., integration with Microsoft® Excel, Geographic Information Systems (GIS) tools, other traffic analysis tools, etc.)?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any experiences with these issues in this group?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 35: Questions to Ask (cont.)
Does the tool have animation/presentation features such as:
  3Dl views
  Zoom-in/-out
  Detailed link views
  Ability to produce charts and tables
  Etc.?
Notes: Key Message: Discuss Questions to Ask
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Self explanatory
Suggested Questions: Any experiences with these issues in this group?
Additional Information: Treat as a checklist.
Possible Problems: None

## Slide 36: Tool Selection Principles
No single tool can do everything
Multiple tools may be necessary
FHWA does not require tools be used
Select the simplest tool that best matches the needs of your project
Notes: Key Message: Present a Tool Selection Checklist
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: Tool selection principles include:
No single tool can do everything
Multiple tools may be necessary at different levels of project development
FHWA does not require a tools be used
Select the simplest tool that best matches the needs of your project
Suggested Questions: How do we select the best tool for our project?
Additional Information: None
Possible Problems: No need to go through each of the bullets in detail. Consider the bullets a checklist for future reference.

## Slide 37: Tool Selection Checklist
Describes the various conditions under which five of the more common class of tools is likely to be most helpful in supporting work zone planning and management
Not all conditions in an individual list need be present for the specific class of tools to be appropriate:
SEE HANDOUT!
Notes: Key Message: Present a Tool Selection Checklist
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: Text box appears on click
Suggested Comments: This section describes the various conditions under which five of the more common class of tools is likely to be most helpful in supporting work zone planning and management: Sketch-Planning or Analytical/Deterministic Tools, Travel Demand/Macro Models, Mesoscopic Simulation Models, and Microscopic Simulation Models. A more detailed assessment is provided in the report Traffic Analysis Tools IX: Work Zone Analysis: A Guide for Analysts which includes concepts such as problem complexity, availability of resources and time, individual tool selection, fidelity of results and multi-scale analysis approaches.
Suggested Questions: None
Additional Information: None
Possible Problems: No need to go through each of the bullets in detail. Consider the bullets a checklist for future reference.

## Slide 38: Summary: Results Will:
Improve decision-making
Help understand the mobility, financial, environmental and safety aspects of the WZ
Help support key decisions
Ultimately improve safety and mobility!
Notes: Key Message: Summarize course
Est. Presentation Time: 1-2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The results from transportation analytical can serve to improve decision-making as well as improve overall understanding of relationships between the many forces affecting work zone decision-making: mobility, financial, environmental and safety. Work zone analysis should never be used to make key decisions but instead developed as a trusted resource for understanding the potential mobility impacts and using this information to inform key decisions. The informative value of analysis used by decision-makes will be directly related to how well the analyst has considered both the context for analysis (decisions to be supported and relevant performance measures) and the context for validation (data and staff resources). The job of the work zone analyst extends beyond merely conducting an analysis and reporting results; but to provide decision-makers with a broader understanding that connects the findings of the analysis within the decision-making context. Placed in context, a well-summarized level of understanding can be provided to decision-makers and other staff working on the project, even if decision-makers do not have first-hand experience with the analytical approach.
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 39: Module Recap
Name the 4 factors to consider when considering WZ impact analysis tools
How do data needs affect model selection?
Name the three network typologies
Which are some of the questions to ask when selecting a tool?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.