## Slide 1: -MODULE 6- Case Study Snapshots
Work Zone Traffic Impact Analysis
Image: ATSSA
Notes: Key Message: Introduce module
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In Module 6 we will present case study snapshots.
Suggested Questions: None
Additional Information: Goal: The goal of this module is to enable learners to discuss successful case studies that have used the analytical tools discussed in this course.
Possible Problems: None.

## Slide 2: Module Objectives
Provide snapshots of successful case studies that utilized the tools we have discussed
Notes: Key Message: State the module objectives
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: None

## Slide 3: Case Studies Available
Traffic Analysis Toolbox Volume IX includes 17 case study examples
Two will be discussed here
Image: FHWA
Notes: Key Message: Introduce Case Studies
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Traffic Analysis Toolbox Volume IX: Work Zone Modeling and Simulation—A Guide for Analysts includes numerous case study examples, discussion and analysis designed to provide the prospective work zone analyst with information pertaining to the selection of a transportation modeling approach (including the identification of opportunities for use, managing technical risk and examples) as well as specific project applications (including constructability, scheduling and transportation management plan design and evaluation).
Suggested Questions: Where do these case studies come from?
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
A total of 17 case studies are included in this volume (13 project applications and 4 strategic modeling approaches) The 17 case studies are categorized as either Project Applications or Strategic Modeling Approaches. The case studies included in this document were selected based upon access to the analysts and/or decision makers, availability of reports and data regarding the work zone application, geographic diversity, and project application (uniqueness).
Possible Problems: None

## Slide 4: Sample Case Studies
Caltrans I-15 Pavement Reconstruction Project
Glacier National Park: Going to the Sun Road Rehabilitation Project
Maryland SHA Lane Closure Analysis Program
Michigan DOT: Southeastern Michigan Simulation Network
Notes: Key Message: List Case Studies
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are some of the case studies included in Traffic Analysis Toolbox Volume IX: Work Zone Modeling and Simulation—A Guide for Analysts
Suggested Questions: None
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
Possible Problems: No need to go through this list one by one. It is intended to let students know which case studies are available, for their reference.

## Slide 5: Sample Case Studies (cont.)
New Jersey Turnpike Authority: Lane Closure Application
Nova Scotia, Canada: Reeves Street
Utah DOT I-15 Reconstruction Design-Build Evaluation
Wisconsin DOT Work Zone Signal Optimization
Notes: Key Message: List Case Studies (cont.)
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are additional case studies included in the Guide.
Suggested Questions: None
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
Possible Problems: No need to go through this list one by one. It is intended to let students know which case studies are available, for their reference.

## Slide 6: Sample Case Studies (cont.)
Wisconsin DOT: Transportation Management Plan Development Process
Woodrow Wilson Bridge Reconstruction
Yosemite National Park: Yosemite Village Roadway Reconstruction
Zion National Park: Entrance Booth Reconstruction
Notes: Key Message: List Case Studies (cont.)
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: These are additional case studies included in the Guide. Let’s look a one of them!
Suggested Questions: None
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
Possible Problems: No need to go through this list one by one. It is intended to let students know which case studies are available, for their reference.

## Slide 7: MD SHA Lane Closure Analysis Program
Transportation Analysis:
Approach | Sketch-Planning
Modeling tool | Lane closure analysis program built w/ Excel
Work Zones:
Type | Type II – IV
Network Configuration | Isolated
Work Zones:
Work zone size | Small
Analysis area | Local
Notes: Key Message: Discuss one case study: MD SHA Lane Closure Analysis Program
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Let’s look at one case study from the Guide, MD SHA Lane Closure Analysis Program. Here are the work zone characteristics.
Suggested Questions: None
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
Possible Problems: MD SHA = Maryland State Highway Administration

## Slide 8: Lane Closure Analysis Program (LCAP)
Developed by MD SHA to analyze wz impacts
Presents allowable thresholds for decreasing mobility measured in terms of queues and delays in work zones
Part of a tiered approach
Notes: Key Message: Discuss MD SHA Lane Closure Analysis Program
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The Maryland State Highway Administration (SHA) has developed the Lane Closure Analysis Program (LCAP) to support state traffic engineers with a structured method to analyze work zone impacts. The LCAP tool was developed based upon the guidance written in the Work Zone Lane Closure Analysis Guidelines which present allowable thresholds for decreasing mobility measured in terms of queues and delays in work zones. LCAP is part of a tiered approach to work zone analysis that SHA has developed. Depending on the complexity of a project, SHA recommends starting with LCAP for simple cases, QuickZone for simple cases with network impacts, and then simulation tools such as CORSIM, VISSIM, and SimTraffic for relatively complex scenarios requiring detailed analysis.
Suggested Questions: None
Additional Information: http://www.sha.maryland.gov/OOTS/WorkZoneAnalysisGuide_Sept08.pdf
Possible Problems: None

## Slide 9: LCAP Description
Quantifies queues and delays resulting from capacity decreases in freeway work zones
MS Excel program
Compare expected travel demand against work zone capacity on an hour-by-hour basis to estimate delay and mainline queue growth
Notes: Key Message: Describe the Lane Closure Analysis Program
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: LCAP is an analytical tool designed to quantify queues and delays resulting from capacity decreases in freeway work zones. LCAP is written as a program within Microsoft Excel and compares expected travel demand against work zone capacity on an hour-by-hour basis to estimate delay and mainline queue growth.
Suggested Questions: None
Additional Information: http://www.sha.maryland.gov/OOTS/WorkZoneAnalysisGuide_Sept08.pdf: Spreadsheets can be used to compare demand and capacity during each time interval to determine the residual queues. This tool can be implemented either using spreadsheet software (such as Microsoft Excel) or the Lane Closure
Analysis Program (LCAP), a program recently developed by the University of Maryland for the SHA, that extracted the lane closure functions from the QuickZone software. These spreadsheet methods can take as inputs: hourly traffic volumes, truck percentages, work zone length, number of existing and work zone lanes, location of closed lanes, lateral clearance, work zone intensity, work zone grade, existing capacity, and type of terrain. These inputs are used to implement any of the aforementioned capacity approximations in order to determine the estimated work zone capacity. Once the work zone capacity has been determined, the roadway capacity is compared to the demand volume during each analysis interval and the difference between them will be the change in queue length of the analysis interval. These applications will report the estimated queue length at the end of each analysis interval. Queue duration is determined by counting the number of intervals where a particular queue length exists. Using trial and error, the user can select desired lane closure hours and view the anticipated resulting queue. Based on the allowable queue length, lane closure schedules can be determined for each day of the week. This type of analysis should be performed for work zones that involve lane closures and are not influenced by ramps.
Possible Problems: None
Image Credit: https://iconape.com/microsoft-excel-2010-logo-logo-icon-svg-png.html

## Slide 10: LCAP Steps
Enter project information
Input demand
Describe the work zone
  Lane closure information
  Capacity information
  Output type
Obtain results
Notes: Key Message: Describe LCAP steps
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments:
STEP 1: Open existing file or Start new file. The user has the choice of opening an existing LCAP file or starting a new case for analysis.
Enter project information. The Project Information screen allows the user to input data that defines the project. The project description, analyst’s name and date of analysis should be input here. The project description should contain information to identify the project, such as roadway name, direction of travel, segment of road, and work being performed.
STEP 2: Input demand. The demand is an essential part of the LCAP program. Users may enter their own data or access SHA’s traffic data from the Traffic Monitoring website (http://www.marylandroads.com/tmsreports/).
STEP 3: Describe the work zone. The closure analysis screen is used to determine the hours during the day when lanes can be closed without causing excessive queuing or delays. The user is prompted to select input options in terms of maximum allowable queue length or maximum allowable delay (to be highlighted in red or yellow when exceeded) and proposed lane closure hours. Using trial and error in the start and finish times of the work zone, lane closure schedules can be determined based on allowable queues or delays.
 Lane Closure Information—The user enters the total number of freeway lanes and the number of open lanes with the lane closure in effect.
 Capacity Information—The user enters the roadway capacity without and with the work zone in vehicles per hour per lane. The work zone capacity can be determined in four ways:
1. engineering judgment,
2. 1997 Highway Capacity Manual,
3. University of Maryland Capacity Estimation equation, or
4. 2000 Highway Capacity Manual equation.
 Output Type—The user selects queue length or delay as the measure of the work zones mobility impact. The user has the option of highlighting the output in red or yellow if the queue exceeds a specified length (miles) or the delay exceeds a specified period of time (minutes).
STEP 4
Save File. LCAP has the ability to save all of the data associated with the project.
Suggested Questions: None
Additional Information: http://www.ops.fhwa.dot.gov/wz/traffic_analysis/tatv9_wz/tatvol_9.pdf, PUBLICATION NO. FHWA-HOP-09-001, March 2009
Possible Problems: This case study was adapted from the LCAP User Guide available at http://marylandroads.com/safety/workzone.asp.

## Slide 11: Sample LCAP Output
Notes: Key Message: Show LCAP sample output
Est. Presentation Time: Less than 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Here is a sample output from LCAP analysis. Notice the queue reported.
Suggested Questions: Is this an acceptable queue?
Additional Information: http://www.sha.maryland.gov/OOTS/WorkZoneAnalysisGuide_Sept08.pdf, Page 25.
Possible Problems: Text may not be legible.

## Slide 12: QuickZone Case Study Snapshots
FHWA Website includes eight
Three will be highlighted here
For others:
  www.tfhrc.gov/its/pubs/ quickzone.htm
Image: FHWA
Notes: Key Message: Introduce QuickZone Case Study Snapshots
Est. Presentation Time: Less than 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The FHWA website also includes eight QuickZone case study snapshots. We will highlight three of them to illustrate the benefits of quick, simple impact analysis. The overall goal in terms of ease-of-use for QuickZone is less than one hour to input and check a QuickZone network, and less than three minutes to analyze the data and produce delay profiles over the project duration. Target users of QuickZone include state and local traffic construction, operations, and planning staff as well as construction contractors. QuickZone allows these users to:
-Quantify corridor delay resulting from capacity decreases in work zones;
-Identify delay impacts of alternative project phasing plans; and
-Support tradeoff analyses between construction costs and delay costs.
Suggested Questions: None
Additional Information: Download a demo version of QuickZone at www.tfhrc.gov/its/quickzon.htm
Possible Problems: None

## Slide 13: Snapshot #1: I-40 Full Closure Feasibility Assessment
Rehabilitation project on I-40 east of downtown Knoxville, TN
Image: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Tennessee Department of Transportation (TDOT) identified a section of I-40 east of downtown Knoxville as a candidate for major rehabilitation, and in 2004, considered various strategies to perform the needed roadwork, keeping in mind construction costs, project duration, and potential impact to road users.
Suggested Questions: None
Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm. In this case study, two networks were constructed in QuickZone to model the I-40 closure. The first included both I-40 and I-640 and was used for the initial delay screening activity. A second more detailed model was constructed just of the I-640 detour including key bottlenecks at interchanges along its length in both east and west directions (Figure 2.1.2). For example, capacity of the off-ramp from westbound I-40 onto I-640 was estimated with consideration features of the proposed travel movement, e.g., number of lanes, grade, ramp curvature and merge area length. Likewise, a capacity reduction was modeled at the intersection of I-640 and I-275 because of a narrowing of the I-640 as it passes beneath I-275. Modeling the details of the bottleneck areas was important in identifying the capability of I-640 to effectively absorb diverted travel volume from I-40 during the proposed full closure period.
Possible Problems: None

## Slide 14: Snapshot #1: I-40 Full Closure Feasibility Assessment
TDOT considered the use of a full closure
Image: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In particular, TDOT considered the use of a full closure to complete complex work on freeway interchanges without the maintenance of through traffic on I-40.
Suggested Questions: Who remembers the benefits of full closures?
Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm.
Given the potential disruption a full closure might have on the distribution of travel demand throughout the Knoxville area, TNDOT commissioned a traffic study to identify likely travel demand for I-640 given a full closure on I-40. Vehicle-matching technology was utilized to identify the current volume of through traffic traversing the length of I-40 in the Knoxville area in both eastbound and westbound directions. This characterization of current traffic patterns was combined with projected demand increases over the period 2004-2008 to arrive at average daily travel demand for I-640 given the full closure condition on I-40. QuickZone analysts utilized these average travel demand figures to determine likely hour-by-hour travel demand taking into consideration current prevailing distributions of travel demand on I-640 by time-of-day, day-of-week and month of the year (obtained from TNDOT permanent count stations as well as periodic count activities). These refined travel demand estimates were then applied with the detailed model of the I-640 diversion route in QuickZone to predict queue length and delay throughout the proposed full closure period.
Possible Problems: None

## Slide 15: Full Closure Advantages
Reduced project duration
Improved worker safety
Potential cost savings over more traditional approaches
Image: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The advantages of this option over more traditional approaches include reduced project duration, improved worker safety, and potential cost savings over more traditional approaches. However, the impact on road users throughout the closure period was poorly understood. From the road network geometry in the metropolitan area, it was clear that the brunt of the diverted traffic demand would have to be borne by I-640. TDOT commissioned a traffic study to predict traffic volumes on I-640 for a prospective 2008 full closure on I-40. The study used vehicle-matching technologies to identify through and local traffic volumes by collecting field data in the first half of 2004. The results of this study were used by analysts to better predict travel demands on I-640 during the construction period.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 16: Why QuickZone? It Eliminated the Guess Work!
Images: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The advantages of this option over more traditional approaches include reduced project duration, improved worker safety, and potential cost savings over more traditional approaches. However, the impact on road users throughout the closure period was poorly understood. From the road network geometry in the metropolitan area, it was clear that the brunt of the diverted traffic demand would have to be borne by I-640.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 17: Scope of TDOT Study
Predict traffic volumes on I-640 for a prospective 2008 full closure on I-40
Use vehicle-matching technologies to identify through and local traffic volumes by collecting field data
Use results to better predict travel demands on I-640 during the construction period
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: TDOT commissioned a traffic study to predict traffic volumes on I-640 for a prospective 2008 full closure on I-40. The study used vehicle-matching technologies to identify through and local traffic volumes by collecting field data in the first half of 2004. The results of this study were used by analysts to better predict travel demands on I-640 during the construction period.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 18: QuickZone Study
To identify the likelihood of significant congestion under the proposed full closure option
When it became clear that congestion was likely to be significant, more refined traffic demand data and more detailed network geometry were applied in QuickZone
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The study used QuickZone to identify the likelihood of significant congestion under the proposed full closure option by presenting a quick prediction based on current traffic volumes. When it became clear that congestion was likely to be significant, more refined traffic demand data and more detailed network geometry was applied in QuickZone. The increased scope identified the likely delay impacts and targets to assist the management of local and interstate traffic demand in preventing lengthy delays on I-640 and at the I-40/I-640 interchanges.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 19: Key Observations
QuickZone can be utilized to predict likely delay impacts from a proposed full closure on a major interstate
Image: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The study used QuickZone to identify the likelihood of significant congestion under the proposed full closure option by presenting a quick prediction based on current traffic volumes.
Results:
In the initial screening analysis performed with QuickZone, it became clear that I-640 would be unlikely to absorb a significant share of I-40 volume given expected 2008 travel demand conditions without serious congestion conditions developing during peak periods and on high-volume weekend conditions associated with the summer travel season. The predicted severity of congestion prompted TNDOT to consider a more detailed model of the I-640 detour route in QuickZone along with bringing into QuickZone the results of the more detailed I-40 closure traffic study completed in mid-2004. The analysis of the more detailed detour model in QuickZone indicated that several key bottlenecks along the proposed diversion route would not support the combination of current travel demand and diverted travel demand from I-40. Queuing at these bottlenecks are predicted to generate significant congestion during morning and afternoon peak travel demand periods that would persist without dissipation in the mid-day period for most weekdays. In addition, heavy travel demand on the weekends in the summer would generate backups at some of the same bottlenecks with significant delays that would build and dissipate over a period of 6-8 hours.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 20: Key Observations
Predicted delays highlighted the potential for extensive delays and helped TDOT mobilize resources for demand management and public outreach prior to construction
Image: FHWA
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: When it became clear that congestion was likely to be significant, more refined traffic demand data and more detailed network geometry was applied in QuickZone. The increased scope identified the likely delay impacts and targets to assist the management of local and interstate traffic demand in preventing lengthy delays on I-640 and at the I-40/I-640 interchanges.
Results:
Because of the severity and duration of the predicted delays, the QuickZone analysis was extended to consider the improvement of I-640 to reduce bottleneck effects at key intersections (like the one with I-275). Even with these improvements, it was clear that significant and potentially unacceptable delays would be likely unless travel demand management strategies could shift local and interstate road users away from weekday peak periods and summer weekend afternoons. Using QuickZone, the effectiveness of strategies aimed at reducing through truck travel as well as local and interstate passenger car values were analyzed. A range of target values for demand management were explored to realize some of the reductions in travel demand required to reduce delay to minimal levels. TNDOT is considering these targets as well as potential public outreach on the project as a result of the QuickZone analysis.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 21: Key Observations (cont.)
A tiered modeling approach is a cost effective strategy for using QuickZone
  1. Less detailed data are used to scope potential delays
  2. If deemed necessary, enhanced travel demand and more detailed network models are employed
Notes: Key Message: Introduce Snapshot #1: I-40 Full Closure Feasibility Assessment
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The study used QuickZone to identify the likelihood of significant congestion under the proposed full closure option by presenting a quick prediction based on current traffic volumes. When it became clear that congestion was likely to be significant, more refined traffic demand data and more detailed network geometry was applied in QuickZone. The increased scope identified the likely delay impacts and targets to assist the management of local and interstate traffic demand in preventing lengthy delays on I-640 and at the I-40/I-640 interchanges.
Suggested Questions: None
Additional Information:
Brian Fouch, P.E. Region Three Area Engineer FHWA–Tennessee Division 615–781–5765 brian.fouch@fhwa.dot.gov
Steve Allen Transportation Manager 2 TDOT 615–741–2208 steve.allen@state.tn.us
Possible Problems: None

## Slide 22: Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Woodrow Wilson Bridge replacement project in the Washington, DC metropolitan area
Image: Maryland SHA
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Maintaining roadway capacity is an important aspect in the ongoing Woodrow Wilson Bridge replacement project in the Washington, DC metropolitan area. Lane closures are conducted only at night to minimize impact on road users. In the fall of 2001, a contractor for the Maryland State Highway Administration was in the process of constructing one of many new bridges as part of the project at the MD 210/ I-295/I-95 interchange just east of the Potomac River shoreline. The plan included closing lanes during the overnight hours (12 a.m. to 4 a.m.) and was scheduled to take from 4 to 6 months to complete. When this phase of the roadwork began, it was clear the limited hours of lane closures were incompatible with required setup and takedown time.
Suggested Questions: None
Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm. Overview:
The replacement of the Woodrow Wilson Bridge, along Interstate 95 in the Metropolitan Washington, DC area, is an extremely large and complex construction project requiring the close coordination of numerous contractors and various state and local government agencies. The Woodrow Wilson Bridge carries upwards of 100,000 vehicles per day along Interstate 95 which spans the Potomac River. The current 6-lane bridge is being replaced with a dual-span bridge that will more than double the number of traffic lanes. The management of the construction project primarily involves the Maryland State Highway Administration and the Virginia Department of Transportation who are responsible for overseeing daily operations of the construction site including scheduled lane closures. An important aspect to the replacement of the Woodrow Wilson Bridge is to maintain current roadway capacity during peak periods while construction takes place. This requires limited, if any, lane closures during peak periods and daylight hours. In general, any necessary lane closures were conducted at night to minimize the impact on drivers. In Fall 2001, a contractor for the Maryland State Highway Administration was in the process of constructing one of many new bridges as part of the replacement and refurbishment of the Woodrow Wilson Bridge at the MD 210/I-295/I-95 interchange just east of the Potomac River shoreline (see Figure 2.2.1 below). The construction involved the demolition of existing bridges and the construction of new bridges. The plan included closing lanes during the overnight hours (12:00pm to 4:00am) and two temporary openings in the median barrier in order to divert traffic safely around the construction area while construction was taking place. This work zone plan configuration was scheduled to take between 4 and 6 months to complete. The need for QuickZone arose when the contractor determined that to more efficiently utilize available resources, a four-hour window of construction would not be sufficient. The original work zone plan had lane closures occurring between 12:00pm and 4:00pm and the contractor estimated it would take 1.5 hours for work zone set up and take down, leaving 2.5 hours of actual production time. The contractor went to the Woodrow Wilson Bridge management team requesting more hours of production time to better utilize available resources. The request for more production time essentially meant that lane closure durations would have to increase. The request was sent to the Maryland State Highway Administration to analyze and make/provide feedback to the Woodrow Wilson Bridge management team.
Possible Problems: None

## Slide 23: The Problem
Original plan included closing lanes during the overnight hours (12 a.m. to 4 a.m.) for 4 -6 months
The limited hours of lane closures were incompatible with required setup and takedown time
Image: Maryland SHA
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Project engineers responded with a QuickZone analysis that included multiple scenarios for extending the lane closure duration time and the number of lanes closed. The results showed an insignificant difference for motorists if the lane closures began at 9 p.m. instead of the proposed 12 a.m. Opening all lanes by 5 a.m. would be sufficient to maintain traffic flow. As a result of this information the lanes were closed at 9 p.m. and reopened by 5 a.m. Consequently, total duration of the construction project was reduced from an estimated 6 months to 2 months, hence reducing the impact on motorists. Moreover, the increase in the contractor’s productive time (from 2.5 hours to 6 hours) resulted in better utilization of available resources and ultimately saved money on the overall construction project. QuickZone allowed the management team to easily test various work zone plan scenarios and determine the best compromise between the interests of the construction project and the public.
The analysis required a quick analysis of multiple scenarios of when lane closures could take place without severely impacting motorists. The consultant chosen to conduct the analysis utilized MD-QuickZone for a number of reasons:
-QuickZone had the ability to analyze multiple scenarios very quickly.
-Maryland State Highway Administration had a customized version of QuickZone available that they were encouraging traffic engineers across to use for analyze work zone impacts.
-Results , namely delay and queue, were exactly the measures they needed to make a decision regarding the extension of the lane closure duration.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None
Contacts:
Andrew Lessner
QuickZone Analyst
Maryland State Highway
Administration
410–787–5864
alessner@sha.state.md.us
Jawad Paracha
Transportation Engineer
Maryland State Highway
Administration
410–787–5891
jparacha@sha.state.md.us

## Slide 24: The Solution
QuickZone analysis for extending the lane closure duration time and the number of lanes closed showed an insignificant difference for motorists if the lane closures began at 9 p.m. instead of the proposed 12 a.m.
Opening all lanes by 5 a.m. would be sufficient to maintain traffic flow
Image: FHWA
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Project engineers responded with a QuickZone analysis that included multiple scenarios for extending the lane closure duration time and the number of lanes closed. The results showed an insignificant difference for motorists if the lane closures began at 9 p.m. instead of the proposed 12 a.m. Opening all lanes by 5 a.m. would be sufficient to maintain traffic flow. As a result of this information the lanes were closed at 9 p.m. and reopened by 5 a.m. Consequently, total duration of the construction project was reduced from an estimated 6 months to 2 months, hence reducing the impact on motorists. Moreover, the increase in the contractor’s productive time (from 2.5 hours to 6 hours) resulted in better utilization of available resources and ultimately saved money on the overall construction project. QuickZone allowed the management team to easily test various work zone plan scenarios and determine the best compromise between the interests of the construction project and the public.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None
Contacts:
Andrew Lessner
QuickZone Analyst
Maryland State Highway
Administration
410–787–5864
alessner@sha.state.md.us
Jawad Paracha
Transportation Engineer
Maryland State Highway
Administration
410–787–5891
jparacha@sha.state.md.us

## Slide 25: Woodrow Wilson Bridge QuickZone Network
Image: FHWA
Image: Maryland SHA
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: The QuickZone network for the Woodrow Wilson Bridge was complex in design due to the complex nature of the roadway geometry. The location of the construction included multiple roads coming together to form a complex interchange. In order to account for the total demand on the roads, the Woodrow Wilson Bridge QuickZone network includes 35 nodes and 53 links. Many of the links were the individual entrance and exit ramps along with the primary travel lanes of the outer and inner loops of the capital beltway. The network is shown in this bottom figure.
Traffic volumes and demand data were available from both the Maryland State Highway Administration and the Virginia Department of Transportation. Demand data for the inner-loop was acquired from the various MD-SHA permanent traffic count stations set up prior to the construction site. The data is available to anyone interested via the Maryland Roads web site (www.marylandroads.com). Demand data for the outer-loop was made available through special traffic counts conducted by the VDOT on the Virginia approach to the Woodrow Wilson Bridge. Lane capacities, lengths, and free-flow speeds were gathered from historical data.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 26: Key Observations:
QuickZone can be used to estimate delay and queuing on large construction projects with high volumes
Impacts on the motorist were reduced since total duration of the construction project was reduced from an estimated 6 months to 2 months
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Maintaining roadway capacity is an important aspect in the ongoing Woodrow Wilson Bridge replacement project in the Washington, DC metropolitan area. Lane closures are conducted only at night to minimize impact on road users. In the fall of 2001, a contractor for the Maryland State Highway Administration was in the process of constructing one of many new bridges as part of the project at the MD 210/ I-295/I-95 interchange just east of the Potomac River shoreline. The plan included closing lanes during the overnight hours (12 a.m. to 4 a.m.) and was scheduled to take from 4 to 6 months to complete. When this phase of the roadwork began, it was clear the limited hours of lane closures were incompatible with required setup and takedown time.
QuickZone can be used to estimate delay and queuing on large construction projects with high volumes.
Impacts on the motorist were reduced since total duration of the construction project was reduced from an estimated 6 months to 2 months.
Efficient dialog was created between the construction contractor and the Woodrow Wilson Bridge management team.
Results:
The QuickZone analysis included multiple scenarios for extending the lane closure duration time and the number of lanes closed. These scenarios included beginning lane closures at 9:00pm, 10:00pm, 11:00pm and 12:00am and removing the work zone at 4:00am and 5:00am. The results of the analysis showed that there was very little impact to drivers if the lane closures began at 9:00pm or 12:00am and that opening all lanes up by 5:00am would be sufficient. These results were presented to the Woodrow Wilson Bridge management team, Federal Highway Administration and MD-SHA. As a result of this analysis, the contractor was given permission to begin lane closures at 9:00pm and remove the lane closures by 5:00am.
At the time of the analysis, MD-QuickZone was a fairly new software program and had not been extensively used. An important aspect of trusting the results of QuickZone was to insure that the actual queue and delay that developed in the field were similar to the results generated by QuickZone. The Woodrow Wilson Bridge management team made the decision to monitor the queue and delay for the first week of construction. The results generated by QuickZone were very similar to those seen in the field.
The impact of the change in the work zone plan had very positive results. Overall, the impact to the traveling public was reduced since total duration of the construction project was reduced from an estimated 6 months to 2 months. The increase in production time to the contractor more than doubled (2.5 hours to 6 hours) resulting in better utilization of available resources and ultimately saving money on the overall construction project. Another important impact of using QuickZone was the creation of a dialog between the construction contractor and the Woodrow Wilson Bridge management team. The management team was in the position of weighing the interests of the construction contractor, who needed more production time, against that of the traveling public, who did not want unnecessary queuing and delay. QuickZone was a tool the management team could easily utilize to test out various work zone plan scenarios and determine the best compromise between the interests of the construction contractor and the public.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 27: Key Observations:
Efficient dialog was created between the construction contractor and the Woodrow Wilson Bridge management team
Image: Maryland SHA
Notes: Key Message: Introduce Snapshot #2: I-95 Operational Analysis for Lane Closures at Night
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: Maintaining roadway capacity is an important aspect in the ongoing Woodrow Wilson Bridge replacement project in the Washington, DC metropolitan area. Lane closures are conducted only at night to minimize impact on road users. In the fall of 2001, a contractor for the Maryland State Highway Administration was in the process of constructing one of many new bridges as part of the project at the MD 210/ I-295/I-95 interchange just east of the Potomac River shoreline. The plan included closing lanes during the overnight hours (12 a.m. to 4 a.m.) and was scheduled to take from 4 to 6 months to complete. When this phase of the roadwork began, it was clear the limited hours of lane closures were incompatible with required setup and takedown time.
QuickZone can be used to estimate delay and queuing on large construction projects with high volumes.
Impacts on the motorist were reduced since total duration of the construction project was reduced from an estimated 6 months to 2 months.
Efficient dialog was created between the construction contractor and the Woodrow Wilson Bridge management team.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 28: Case Study Snapshot #3: Justifying the Additional Cost of Night Work in Nova Scotia
Image: FHWA
Notes: Key Message: Introduce Case Study Snapshot #3: Justifying the Additional Cost of Night Work in Nova Scotia
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In 2001, the intersection of Reeves Street and Trunk 4 in Port Hawkesbury, Nova Scotia— along a key access route to the Trans Canada Highway—was slated to be upgraded. Both roads are generally two-lane roads with certain sections upgraded to include designated turn lanes. Average annual daily traffic (AADT) through the intersection is roughly 8,000 vehicles per day with approximately 10 percent truck volume. Truck traffic is concentrated during the daytime on weekdays. Most of the traffic volume at this location in Port Hawkesbury is through-traffic continuing on to some of the industrial centers near the town or to points further north. The reconstruction involved a major upgrade of the intersection including additional dedicated turn lanes to accommodate higher traffic volumes and to improve safety. Construction was slated to take place only during daylight hours because of cost and safety concerns. However, it was also evident that any construction during the day would have an impact on motorists. The reconstruction involved a major upgrade of the intersection including additional dedicated turn lanes to accommodate higher traffic volumes and to improve safety. Construction was slated to take place only during daylight hours because of cost and safety concerns. However, it was also evident that any construction during the day would have an impact on motorists. QuickZone Version 1.0 was used to test alternate strategies, including the possibility of a detour route through a residential district.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 29: The Problem
In 2001, the intersection of Reeves Street and Trunk 4 in Port Hawkesbury, Nova Scotia— along a key access route to the Trans Canada Highway—was slated to be upgraded
Construction was slated to take place only during daylight hours with significant cost & safety concerns
Notes: Key Message: Introduce Case Study Snapshot #3: Justifying the Additional Cost of Night Work in Nova Scotia
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: In 2001, the intersection of Reeves Street and Trunk 4 in Port Hawkesbury, Nova Scotia— along a key access route to the Trans Canada Highway—was slated to be upgraded. Both roads are generally two-lane roads with certain sections upgraded to include designated turn lanes. Average annual daily traffic (AADT) through the intersection is roughly 8,000 vehicles per day with approximately 10 percent truck volume. Truck traffic is concentrated during the daytime on weekdays. Most of the traffic volume at this location in Port Hawkesbury is through-traffic continuing on to some of the industrial centers near the town or to points further north. The reconstruction involved a major upgrade of the intersection including additional dedicated turn lanes to accommodate higher traffic volumes and to improve safety. Construction was slated to take place only during daylight hours because of cost and safety concerns. However, it was also evident that any construction during the day would have an impact on motorists. The reconstruction involved a major upgrade of the intersection including additional dedicated turn lanes to accommodate higher traffic volumes and to improve safety. Construction was slated to take place only during daylight hours because of cost and safety concerns. However, it was also evident that any construction during the day would have an impact on motorists. QuickZone Version 1.0 was used to test alternate strategies, including the possibility of a detour route through a residential district.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 30: The Solution
QuickZone was used to test alternate strategies
For daytime work, QuickZone predicted up to a 4.1-mile queue and 70 minutes of delay
Eliminating daylight work Fri-Sat cut in half the queuing and the delays associated with the construction
Image: FHWA
Notes: Key Message: Introduce Case Study Snapshot #3: Justifying the Additional Cost of Night Work in Nova Scotia
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: QuickZone Version 1.0 was used to test alternate strategies, including the possibility of a detour route through a residential district. Under the original traffic control plan, the intersection operated 24 hours a day, 7 days a week. Under these conditions, QuickZone predicted up to a 6.5-kilometer (4.1-mile) queue and 70 minutes of delay. Project engineers noted that queues and delays did not form during the overnight hours on any day, especially Friday. They also tested a scenario that eliminated construction during daylight hours on Fridays and Saturdays. Using this information, construction was planned for mornings and evenings during weekdays. This approach cut in half the queuing and the delays associated with the construction. In addition, the number of vehicles on the detour route was reduced to 6,000 vehicles per week, a 40 percent reduction. The QuickZone analysis allowed project engineers to better plan the construction schedule and make the decision to perform some of the most disruptive phases of construction at night.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None

## Slide 31: Key Observations: QuickZone:
Can identify potential queuing and delays through simple intersection analysis
Provided the analytical backup to effectively demonstrate the advantages of nighttime construction
Estimates of queue length and delays were consistent with field observations
Notes: Key Message: Introduce Case Study Snapshot #3: Justifying the Additional Cost of Night Work in Nova Scotia
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: KEY OBSERVATIONS
QuickZone can identify potential queuing and delays through simple intersection analysis.
QuickZone provided the analytical backup to effectively demonstrate the advantages of nighttime construction.
QuickZone estimates of queue length and delays were consistent with field observations.
Suggested Questions: None
  Additional Information: www.tfhrc.gov/its/pubs/ quickzone.htm
Possible Problems: None
Contact:
Gerard Kennedy, P. E. Project Engineer Nova Scotia Department of Transportation and Public Works 902–563–2518 kennedge@gov.ns.ca

## Slide 32: More Case Studies and Successful Applications
www.dot.ca.gov/newtech/roadway/ca4prs/cwz_workshop.htm
Image: Caltrans
Notes: Key Message: Introduce More (other) case studies
Est. Presentation Time: 2 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: KEY OBSERVATIONS:
QuickZone can identify potential queuing and delays through simple intersection analysis.
QuickZone provided the analytical backup to effectively demonstrate the advantages of nighttime construction.
QuickZone estimates of queue length and delays were consistent with field observations.
Suggested Questions: None
  Additional Information: www.dot.ca.gov/newtech/roadway/ca4prs/cwz_workshop.htm
Possible Problems: None

## Slide 33: Module Recap
What have these case studies demonstrated re: work zone analytical tools?
Notes: Key Message: Recap module
Est. Presentation Time: 1 minute(s)
Explanation of Cues/Builds: None
Suggested Comments: None
Suggested Questions: None
Additional Information: None
Possible Problems: Avoid telling the audience the answers to these questions. Their purpose is to gauge understanding. You may add other questions.